3GPP TSG-CT WG1 Meeting #130-e	C1-21xxxx was C1-213210

# Electronic meeting; 20-28 May 2021

Source:	Nokia, Nokia Shanghai Bell

Title:	Introducing the UE-to-network relay reselection procedure

Spec:	3GPP TS 24.554 V0.2.0

Agenda item:	17.2.18

Document for:	Agreement

1. Introduction

Stage-2 ProSe spec TS 23.304 has defined the procedures for UE-to-Network Relay Discovery. For the Relay Discovery to complete successfully, the procedure to enable a remote UE to reselect a suitable ProSe UE-to-network relay UE needs to be specified.

2. Reason for Change

Introducing the UE-to-network relay reselection procedure.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TS 24.554 V0.2.0.

* * * First Change * * * *

### 8.2.Y	UE-to-network relay reselection procedure

#### 8.2.Y.1	General

The purpose of the UE-to-network relay reselection procedure is to enable a remote UE to reselect a ProSe UE-to-network relay UE to obtain a connectivity service to 5GC when the serving ProSe UE-to-network relay UE is no longer suitable.

#### 8.2.Y.2	UE-to-network relay reselection procedure initiation

The remote UE shall trigger the UE-to-network relay reselection procedure if one of the following conditions is met:

a)	the UE has received a lower layers indication that the serving ProSe UE-to-network relay UE no longer fulfills the lower layers criteria as specified in 3GPP TS 38.331 [TBD];

b)	the parameters related to ProSe UE-to-network relay in the ProSe direct discovery service authorisation (e.g., Relay Service Code, User Info ID, etc.) have been updated and the serving ProSe UE-to-network relay UE no longer fulfills the conditions specified in subclause XYZ;

c)	the UE has received a PROSE DIRECT LINK ESTABLISHMENT REJECT message from the ProSe UE-to-network relay UE with the cause value "direct communication to the target UE not allowed";

d)	the UE has received a PROSE DIRECT LINK RELEASE REQUEST message from the ProSe UE-to-network relay UE with the cause value "direct communication to the target UE not allowed";

e)	the UE has received a PROSE DIRECT LINK RELEASE REQUEST message from the ProSe UE-to-network relay UE with the cause value "direct connection is not available anymore";

f)	the UE has not received any response from the ProSe UE-to-network relay UE after M consecutive retransmissions of PROSE DIRECT LINK ESTABLISHMENT REQUEST or PROSE DIRECT LINK KEEPALIVE REQUEST messages; or

g)	the UE has not received any response from the ProSe UE-to-network relay UE after M consecutive retransmissions of PROSE PC5 DISCOVERY message for UE-to-Network Relay Discovery Solicitation used to trigger the PROSE PC5 DISCOVERY message signal strength measurement between the UE and the ProSe UE-to-network relay UE with which the UE has a link established.

NOTE:	The value of M is implementation specific and is less than or equal to the maximum number of retransmissions allowed for PC5 Signalling protocol.

In cases c) and d), the remote UE shall exclude the ProSe UE-to-network relay UE which sent the message specified in cases c) or d) from the UE-to-network relay reselection process described below.

To conduct UE-to-network relay reselection process, the UE shall first initiate one of the following procedures or both depending on UE's service authorisation for ProSe direct discovery:

-	monitoring procedure for UE-to-network relay discovery as specified in subclause AAA; or

-	discoverer procedure for UE-to-network relay discovery as specified in subclause BBB.

After the execution of the above discovery procedure(s), the remote UE performs the UE-to-network relay selection procedure as specified in subclause CCC.

* * * End of Changes * * * *