# 3GPP TSG CT WG1 Meeting 130-e	C1-213248

# Electronic meeting, 20-28 May 2021

Title:	LS on reconfiguring a subscription parameter in the UE

Release:	Rel-17

Work Item:	TEI17

To:	3GPP SA2

Contact person:	Kundan Tiwari

Kundan.tiwari@india.nec.com

+919650954544

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

# 1	Overall description

CT1 has discussed the following scenario, in which the UDM/AMF cannot determine the requirement to configure the UE with UE’s subscription information.

1) A first USIM (SUPI 1) is inserted in the ME. The UE is registered to a PLMN. The 5GMM parameters (e.g. CAG information and other UE subscription information) are stored in the ME’s memory for the first USIM.

2) The UE is switched off and the UE performs the deregistration procedure. The UDM also maintain PEI-SUPI 1 association.

3) The user removes the first USIM from the ME and insert a second USIM (SUPI 2).

4) The UE deletes the 5GMM parameters of the first USIM. The UE is registered to a PLMN for the second USIM.

5) The user re-inserts the first USIM in the same ME and the UE performs the registration procedure. The PEI-SUPI 1 association does not change in the AMF. If the AMF hasn’t purged the UE’s context, the AMF does not send Nudm_UECM_Registration message to the UDM. If the AMF has purged the UE’s context, the AMF indicates the PEI and SUPI 1 association to the UDM during the registration procedure in the message Nudm_UECM_Registration when the AMF is registering itself to the UDM.

6) For the UDM, the PEI-SUPI 1 association remains same, therefore the UDM will not push the 5GMM parameters (e.g. CAG information or other subscription information) to the UE.

7) The UE will not have 5GMM parameters (e.g. CAG Information or other subscription information). The absence of the 5GMM parameters may affect the UE’s operation, for instance due to the lack of CAG Information a CAG-only UE may attempt to register on a non-CAG cell and the network will have to reject the UE’s registration and send an updated CAG information list in the registration reject message, which will require additional OTA resources.

# 2	Actions

To 3GPP SA2

ACTION: 	 CT1 kindly requesting SA2 to provide guidance how to ensure the UE has up-to-date UE subscription parameter(s) in the above scenario.

# 3	Dates of next TSG CT WG1 meetings

TBD