# 3GPP TSG CT WG1 Meeting 130-e	C1-213248

# Electronic meeting, 20-28 May 2021

Title:	LS on reconfiguring a subscription parameter in the UE

Release:	Rel-17

Work Item:	TEI17

To:	3GPP SA2

Contact person:	Kundan Tiwari

Kundan.tiwari@india.nec.com

+919650954544

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

# 1	Overall description

CT1 has discussed following scenario, in which the UDM/AMF cannot determine the requirement to configure the UE with UE’s subscription information.

1) A first USIM (SUPI 1) is inserted in the ME. The UE is registered to a PLMN. The 5GMM parameters (e.g. CAG information and other UE subscription information) is stored in the ME memory for the first USIM.

2) The UE is switched off and the UE performs deregistration procedure. The UDM also maintain PEI-SUPI 1 association.

3) The user removes the first USIM from the ME and insert a second USIM (SUPI 2).

4) The UE deletes the 5GMM parameters of the first USIM. The UE is registered to a PLMN for the second USIM.

5) The user re-insert the first USIM in the same ME, the UE performs registration procedure. The PEI-SUPI 1 association does not change in the AMF. If the AMF haven’t purged the UE, The AMF does not send Nudm_UECM_Registration message to the UDM.

In case the AMF purged the UE context, the AMF indicates the PEI and SUPI 1 association to the UDM during the registration procedure in the message Nudm_UECM_Registration when the AMF is registering itself to the UDM.

6) For the UDM the PEI-SUPI 1 association remains same, therefore it will not push the 5GMM parameters (e.g. CAG information or other subscription information) to the UE.

7) The UE will not have 5GMM parameters (e.g. CAG Information or other subscription information). In absence of the 5GMM parameters the UE is not able to perform the NAS or AS procedure as expected. In some case may lead to the no service.

# 2	Actions

To 3GPP SA2

ACTION: 	 CT1 kindly requesting SA2 to provide guidance how to configure the UE with UE subscription parameter(s) in the above scenario.

# 3	Dates of next TSG CT WG1 meetings

TBD