3GPP TSG-CT WG1 Meeting #131-e	C1-21xxxx

# E-meeting, 19-27 August 2021

Title:	LS on backoff timer handling when NSSAA is not completed

Work Item:	eNS, 5GProtoc17

Source:	CT1

To:	CT4

Cc:	SA2

Contact person:	Sunhee Kim

Sunhee.kim@lge.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

TS 29.526 says that

5.2.2.2.1 General If the slice-specific authentication and authorization cannot be completed, then: If it is due to receiving a response with HTTP status code "504 Gateway Timeout" or due to lack of response from the NSSAAF during an NSSAA procedure, the AMF may re-initiate slice-specific authentication and authorization procedure based on its policy or set a back-off timer value in order to prevent UE from sending REGISTRATION REQUEST message. The AMF should wait for a configured period before re-initiating slice-specific authentication and authorization procedure. If the retry attempts are exhausted, the AMF stops the slice-specific authentication and authorization procedure.

From the CT1's perspective, it is not clear what does the description of “AMF may set a back-off timer value in order to prevent UE from sending REGISTRATION REQUEST message” exactly means.

CT1 believes that the description we quoted above is related to NAS and is CT1 responsibility. CT1 does not specify such mechanism in R16. So, CT1 would like to know the reason why CT4 introduced such mechanism and hope that CT4 can update their specifications based on CT1 conclusion.

# 2	Actions

To CT4

ACTION: 	CT1 kindly asks CT4 to provide answers to the questions above.

# 3	Dates of next TSG CT WG1 meetings

CT1#132e	11th-15th October 2021	electronic meeting

CT1#133e	11th-19th November 2021	electronic meeting