3GPP TSG-CT WG1 Meeting #132-e	C1-21xxxx

# E-meeting, 11-15 October 2021

Title:	Reply LS on UAC enhancements for minimization of service interruption when disaster condition applies

Response to:	Reply LS R2-2109173 on UAC enhancements for minimization of service interruption when disaster condition applies from RAN2

Release:	Rel-17

Work Item:	FS_MINT-CT

Source:	CT1

To:	RAN2

Cc:	SA1

Contact person:	Sung Hwan WON

sung.won@nokia.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	-

# 1	Overall description

CT1 appreciates RAN2’s analyses on Solutions #38 and #40 in 3GPP TR 24.811. About the questions in R2-2109173, CT1 would like to provide answers as below.

Q1: whether MINT UE should be independently configured for Access Identity 3 for each Access Category (compared to Access Identity 0)?

Both solutions allow independent “configuration for Access Identity 3” for each access category. The access category of an access attempt by a UE configured for Access Identity 3 is determined based on the existing mechanism.

Q2: whether access control for Access Identity 3 applies both: barring factor and barring time?

Both solutions use barring factor only. Since both solutions do not impact barring time, the existing IE uac-BarringTime for an access category will govern the barring time if an access attempt of a UE configured for Access Identity 3 is barred for the access category.

# 2	Actions

To RAN2

ACTION: 	CT1 respectfully requests RAN2 to take the above answers into account.

# 3	Dates of next TSG CT WG1 meetings

CT1#132e	11th-15th October 2021	electronic meeting

CT1#133e	11th-19th November 2021	electronic meeting