# 3GPP TSG CT WG1 Meeting 131-e	TDoc C1-214942

# E-meeting, 19-27 August 2021

Title:	LS on Scope of 5GMM reject cause “PLMN not allowed to operate at the present UE location”

Response to:	-

Release:	Rel-17

Work Item:	5GSAT_ARCH-CT

Source:	CT1

To:	SA2

Cc:	SA1

Contact person:	Roland Gruber

rgruber at apple dot com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	C1-213155

# 1	Overall description

With 23.502 CR 2482 r1 (S2-2101667) SA2 agreed that the network will reject the 5G registration request with a new 5GMM reject cause #78 “PLMN not allowed to operate at the present UE location” if the UE attempts registration in a geographical position in which the network is not allowed to provide services. However, SA2 has not defined the geographical scope of this registration reject. If no other allowable PLMN+RAT is available, the UE could again select the PLMN which has sent the reject cause #78 and trigger a new registration attempt once it has moved a little further, even it is still in a location, where the PLMN is not allowed to operate.

# 2	Actions

To SA2

ACTION: 	3GPP TSG CT WG1 kindly asks SA1 and SA2 group to discuss the issue outlined above and provide guidance to CT1 under which conditions the UE may select the satellite NG-RAN based PLMN again and initiate a new registration attempt after it has received cause #78 from this PLMN over satellite NG-RAN.

# 3	Dates of next TSG CT WG1 meetings

CT1#132e	11th-15th October 2021	electronic meeting

CT1#133e	11th-19th November 2021	electronic meeting