3GPP TSG-CT WG1 Meeting #133-e	C1-216696

# E-meeting, 11-19 November 2021

Title:	[draft] LS on network supporting ePCO IE for ID_UAS

Response to:

Release:	Release 17

Work Item:	ID_UAS

Source:	CT1

To:	SA2

Cc:

Contact person:	Sunghoon Kim

sunghoon@qti.qualcomm.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

CT1 has discussed to support ID_UAS feature in EPS and identified a protocol issue with the UE providing the parameters for UUAA-SM or for C2 authorization or for both, due to the size limit to 255 octets based on current specs (TS 24.301) for IP based PDN connection in WB-S1 mode. Therefore, CT1 would like to ask questions to SA2 as followings:

Question 1): Whether UUAA-SM or C2 authorization needs to be supported by MME/S-GW of previous release (from rel-13 to rel-16)?

Question 2): If the answer to the Question 1 is No, whether it needs to support the UAV UE which changing serving MME, or the serving S-GW or both (e.g., due to the UE mobility) to be served by a target MME, or the target S-GW or both, of previous release (from rel-13 to rel-16)?

# 2	Actions

To SA2

ACTION: 	CT1 kindly asks SA2 to answer above questions.

# 3	Dates of next TSG CT WG1 meetings

CT1#133-bis-e	17th-21th January 2022	electronic meeting

CT1#134-e	17th-25th February 2022	electronic meeting