3GPP TSG-CT WG1 Meeting #133-e	C1-21xxxx

# E-meeting, 11-19 November 2021

Source:	Nokia, Nokia Shanghai Bell

Title:	Clarifications for the Relay Discovery Additional Information procedure

Spec:	3GPP TS 24.554 V0.5.0

Agenda item:	17.2.18

Document for:	Agreement

1. Reason for Change

It is proposed to clarify that the relation between the Relay Discovery Additional Information procedure and the Cell ID announcement procedure, by clarifying that, after sending the PROSE CELL ID ANNOUNCEMENT RESPONSE message, the 5G ProSe layer-3 UE-to-network relay UE shall start nnouncing the NCGI of the serving cell by triggering the announcing UE procedure for relay discovery additional information

2. Proposal

It is proposed to agree the following changes to 3GPP TS 24.554 V0.5.0.

* * * First Change * * * *

#### 8.2.8.3	5G ProSe Cell ID announcement procedure accepted by the 5G ProSe layer-3 UE-to-network relay UE

Upon receiving a PROSE CELL ID ANNOUNCEMENT REQUEST message, the 5G ProSe layer-3 UE-to-network relay UE shall allocate a NCGI announcement request refresh timer T5106 to the remote UE, and start a timer T5107. The timer T5107 shall be longer than the NCGI announcement request refresh timer T5106.

Then the 5G ProSe layer-3 UE-to-network relay UE shall respond a PROSE CELL ID ANNOUNCEMENT RESPONSE message with a NCGI announcement request refresh timer T5106 IE set to the T5106 timer value assigned by the 5G ProSe layer-3 UE-to-network relay UE. The 5G ProSe layer-3 UE-to-network relay UE shall start announcing the NCGI of the serving cell by triggering the announcing UE procedure for relay discovery additional information as described in clause 8.2.1.2.3.

* * * End of Changes * * * *