3GPP TSG-CT WG1 Meeting #133-e	C1-217152

# E-meeting, 11-19 November 2021

Title:	LS on validity of cause code 78

Response to:	-

Release:	Rel-17

Work Item:	5GSAT_ARCH-CT

Source:	CT1

To:	SA2

Cc:	-

Contact person:	Mikael Wass

mikael dot wass at ericsson dot com

-

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

CT1 has discussed the validity of cause code 78, indicating that the PLMN is not allowed to operate at the present UE location. This results in a limitation to reattempt access to a PLMN via satellite access after receiving a reject or deregistration from that PLMN with cause code 78.

CT1 considers a mechanism where the UE may retry access to the same PLMN based on expiry of a minimum time or the UE moved to a position at a minimum distance away from the location where the cause code 78 was received. In the mechanism under consideration, the values for time and distance would be selected by the UE based on implementation, but the network can optionally provide time and distance values as lower bounds of the UE selected values.

CT1 would like to ask SA2 whether the optional network signalling of lower bound values to support the mechanism described above is acceptable from an SA2 perspective, and if stage 2 specification can be updated accordingly.

# 2	Actions

To SA2

ACTION: 	CT1 asks SA2 group to answer the question on stage 2 aspects of a mechanism for validity of cause code 78.

# 3	Dates of next TSG CT WG1 meetings

CT1#133-bis-e	17th-21st January 2022	electronic meeting

CT1#134-e	17th-25th February 2022	electronic meeting