## Slide 1: Ranging_SL UE-LMF interactions
Tingfang Tang(Rapportuer)

## Slide 2: Background & Proposed way fwd
UE-LMF interactions include the following as shown in Annex1 ：
  SL-MO-LR request/response
  SL-MT-LR request/response
  RSPP Capability Transfer as shown in Annex2(NOTE1)
  RSPP Assistance Data Transfer as shown in Annex3(NOTE1)
  RSPP Location Information Transfer as shown in Annex4 (NOTE1)
  NOTE1: Both 1) Only SLPP messages for UE1 and/or UEx(s) in one NAS message, and 2) Other information, plus SLPP messages for UE1 and/or UEx(s) in one NAS message are supported

## Slide 3: Background & Proposed way fwd
Proposals for stage 3 implementation of the UE-LMF interactions
  NOTE2: the embedded SLPP message is included in the similar way to that for embedded LPP message (multiplePositioningProtocolPDUs)
  NOTE3: LCS-SS payload container for RSPP signaling transfer can be a general one uesed for Capability Transfer/Assistance Data Transfer/Location Information Transfer
  NOTE4: Extending 5.2.1.6 of 24.571 for DL, and extending 5.2.2.10 of 24.571 for UL.
 | Only SLPP messages for UE1 and/or UEx | Other information, plus SLPP messages for UE1 and/or UEx
SL-MO-LR |  | LCS-SS payload container for SL-MO-LR with embedded SLPP message(s)(NOTE2)
SL-MT-LR |  | LCS-SS payload container for SL-MT-LR with embedded SLPP message(s)(NOTE2)
Capability Transfer | SLPP payload container(NOTE4) | LCS-SS payload container for RSPP signaling transfer(NOTE3)
Assistance Data Transfer | SLPP payload container(NOTE4) | LCS-SS payload container for RSPP signaling transfer(NOTE3)
Location Information Transfer | SLPP payload container(NOTE4) | LCS-SS payload container for RSPP signaling transfer(NOTE3)

## Slide 4: Proposed way fwd for SLPP payload container
Proposals for stage 3 implementation of SLPP payload container (if no concern on extending 5.2.1.6 of 24.571 for DL, and extending 5.2.2.10 of 24.571 for UL to transfer SLPP message(s) for other UEs described in previous):
  Option1: Application layer ID visible to the AMF, correlated UE ID included outside of the payload container content.
  Option2: Application layer ID not visible to the AMF, correlated UE ID included as part of the payload container content

## Slide 5: Annex1: UE-LMF interactions

## Slide 6: Annex2: Capabilities exchange for UE-LMF

## Slide 7: Annex3: Assistance data exchange for UE-LMF

## Slide 8: Annex4: Location information exchange for UE-LMF