3GPP TSG-CT1 Meeting #39bis	Tdoc C1-051279

Cannes, France, 12-14 October 2005

| CR-Form-v7.1 |
| --- |
| CHANGE REQUEST |
| ( | Tr 24879 | CR | CRNum | ( rev | - | ( Current version: | 0.1.1 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Use of User Agent Header to transport Personal ME identifier |
| --- | --- |
| Source: ( | LM Ericsson |
| Work item code: ( | CSI |  | Date: ( | dd/mm/yyyy |
| Category: ( |  |  | Release: ( |  |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Ph2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) |
| Reason for change: ( | In 23.279 requirements have been stated regarding Personal ME identifier - Minimal impact on SIP signalling and no impact on the IM CN subsystem; - The identifier should fit into UUS-1 signalling, also allowing for other services to be run over UUS-1; - The Personal ME Identifier is not to be used for routing purposes within the network; The Personal ME Identifier uniquely identifies an ME of the user. Based on these requiremnets we propose to use User-Agent header to transport the Personal ME identifier. We also propose to use the format CSIXXX where X is a digit. |
| Summary of change: ( | User Agent header is added to UE capability exchange procedure and IMS session set up procedure. |
| Consequences if ( not approved: |  |
| Clauses affected: ( |  |
|  | Y | N |  |  |
| Other specs ( |  |  | Other core specifications ( |  |
| Affected: |  |  | Test specifications |  |
|  |  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at http://www.3gpp.org/specs/CR.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word ““revision marks””  feature (also known as ““track changes””) when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With ““track changes”” disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

#### 5.3.1.2	Exchange of UE Capability Information – IM Session First Scenario

The OPTIONS request shall be in accordance with 3GPP TS 24.229 [5] with the following clarifications:

a)	The Request URI shall:

-	include the URI received in the P-Asserted Identity header from the remote user; or if that is not available:

-	include a tel URI corresponding to the MSISDN intended for the CS call set up; or

-	include a SIP URI associated with the remote user available in the UE.

Note 1:Note 2:	If no SIP URI or TEL URI in accordance with above is available the UE cannot initiate the OPTIONS request.

b)	The P-Preferred Identity header shall either include:

-	preferably the MSISDN of the CUA as an assumed registered Tel-URI; or

-	SIP URI associated with the CUA.

c)	The Accept-Contact header may include a feature tag with the value “+g.3gpp.cs-voice” or “+g.3gpp.cs-video” or both marked as explicit.

d)	The User-Agent header may include the personal ME identifier.

The 200 (OK) response to the OPTIONS request shall be in accordance with 3GPP TS 24.229 [5] with the following clarifications:

a)	The Contact header indicating the supported capabilities of the UE as  “+g.3gpp.cs-voice” or “+g.3gpp.cs-video” or both.

b) 	The Server header may include the personal ME identifier.

pon the receipt of the 200  response the UE acts in accordance with 3GPP TS 24.229 [5]. In addition, the UE may update the UE capability information for the remote user.

#### 5.3.1.3	Session set-up – originating case

When the originating CUA wishes to establish an IM session in combination with a CS call, the CUA shall use the call initiation procedure specified in 3GPP TS 24.229 [5].

The CUA shall:

a)	include the MSISDN intended for the CS call set-up or a SIP-URI available in the CUA; and

Note:	The MSISDN can only be included as a Tel-URI if it in international format.

b)	include the s MSISDN as a tel-URI;

c)	include  “+g.3gpp.cs-voice”, “+g.3gpp.cs-video”, or both values marked as explicit; and

d)	 include the personal ME identifier the User-Agent header.

#### 5.3.1.4	Session set-up – terminating case

When the terminating CUA receives an initial request, the terminating CUA shall apply the procedures as specified in 3GPP TS 24.229 [5].

The UE may include in the Server header in the responses the personal ME identifier.

#### 6.3.1.2	Exchange of UE Capability Information – CS First Scenario

The OPTIONS request shall be in accordance with 3GPP TS 24.229 [5] with the following clarifications:

a)	The Request URI shall include one of the following:

-	the URI, as received in P-Asserted Identity header from the terminating CUA during the terminal capability information exchange procedure; or, if this is not available;

-	the connected number information element as a Tel-URI that was received during establishment of the existing CS call. If this is not available, the MSISDN used for the CS call set-up as a Tel-URI ( the used Called Party BCD Number); or

- the Calling Party BCD number information element as a Tel-URI, received during establishment of the existing CS call; or

- A SIP URI associated with the remote user stored in the UE.

Note 1:	If no SIP URI or TEL URI in accordance with above is available the UE cannot initiate the OPTIONS request.

b)	The P-Preferred Identity header shall either include:

-	the MSISDN of the UE as a Tel-URI; or

-	a SIP URI associated with the UE.

Note 2:	It is possible that these identities are not registered.

- The Accept-Contact header may include either a +g.3gpp.cs-voice or a  +g.3gpp.cs-video feature tag marked as explicit. The Accept-Contact header may also include both feature tags.

d)	The User-Agent header may include the personal ME identifier.

The 200 response to the OPTIONS request shall be in accordance with 3GPP TS 24.229 [5] with the following clarifications:

a)	the Contact header indicating  the supported capabilities of the UE as either CS Video, CS Voice or both.

b) 	The Server header may include personal ME identifier.

.

Upon the receipt of the 200 response, the UE acts in accordance with 3GPP TS 24.229 [5]. In addition, the UE may update the UE capability information for the remote user.

#### 6.3.1.3	Session set-up – originating case

When the originating CUA wishes to add an IMS part of a CSICS call it shall use the call initiation procedure specified in 3GPP TS 24.229 [5] with the following clarifications:

a)	The Request URI in the initial request shall either include:

1)	the URI, as received in P-Asserted ID header from the terminating CUA during the terminal capability information exchange procedure; or if this is not available

2)	a Tel-URI that either is:

-	derived from connected number information element, received during establishment of the existing CS call, and if this is not available derived from the MSISDN used for the CS call set-up ( the used Called Party BCD Number); or

-	derived from the Calling Party BCD number information element, received during establishment of the existing CS call.

b)	The P-Preferred Identity Header in the initial request should include a Tel URI corresponding the MSISDN of the UE;

c)	The Accept-Contact header in the initial request shall include either a +g.3gpp.cs-voice or a +g.3gpp.cs-video feature tag marked as explicit; and

d)	The User-Agent header may include personal ME identifier.

Note 1:	If privacy is indicated it is not possible to correlate the CS call and the IMS session.

#### 6.3.1.4	Session set-up – terminating case

When the terminating CUA receives an initial request for an IMS session, the terminating CUA shall apply the procedures as specified in 3GPP TS 24.229 [5] with the following additions:

a)	If the Accept-Contact header includes in an entry either a +g.3gpp.cs-voice or a +g.3gpp.cs-video feature tag, the CUA shall check if one of the identities in the P-Asserted-Identity header matches the received Calling Party BCD number information element or Connected number information element received for an ongoing CS call. If there is a match, a CSICS call is established.

b)	If the Accept-Contact header does not include either a +g.3gpp.cs-voice or a +g.3gpp.cs-video feature tag, or the Accept-Contact header is  not included in request, the CUA shall not consider this a CSI call/session.

´c)	The UE may include in the Server header in the 200 response the personal ME identifier.

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .
The list is also included in a MS Excel file included in the zip file containing the CR cover sheet template.

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.