3GPP TSG-CT1 Meeting #41	Tdoc C1-060605

Denver, USA, 13-17 February 2006

| CR-Form-v7.1 |
| --- |
| CHANGE REQUEST |
| ( | 24.229 | CR | 1138 | ( rev | 2 | ( Current version: | 7.2.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Session termination by P-CSCF |
| --- | --- |
| Source: ( | Lucent Technologies |
| Work item code: ( | IMSProtoc |  | Date: ( | 6/2/2006 |
| Category: ( | F |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Ph2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) |
| Reason for change: ( | If the UE sends an SDP offer containing the media parameters that are not allowed by local policy, the session may be established and immediately terminated by a BYE request. i.e.: "When the P-CSCF receives a 200 (OK) response containing SDP offer, the P-CSCF shall examine the media parameters in the received SDP. If the P-CSCF finds any media parameters which are not allowed on the network by local policy, the P-CSCF shall forward the SDP offer and on the receipt of the ACK request containing the SDP answer, it shall immediately terminate the session as described in subclause 5.2.8.1.2." Subsequently, the UE cannot try to re-establish a session with permissible media parameters, since it doesn't know why the session was terminated. |
| Summary of change: ( | Include in the BYE request the Reason header the 488 (Not Acceptable Here) response code that will enable the UE to re-establish the failed session. |
| Consequences if ( not approved: | The user - upon initiating or modifying a call - will not know the reason why is the network cleared the call. |

| Clauses affected: ( | 5.2.8.1.2 |
| --- | --- |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at http://www.3gpp.org/specs/CR.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

##### 5.2.8.1.2	Release of an existing session

Upon receipt of an indication that the radio/bearer interface resources are no longer available for a session (e.g. abort session request from PDF) or upon detecting that the SDP offer conveyed in a SIP response contained parameters which are not allowed according to the local policy (as specified in the subclause 6.2), the P-CSCF shall release the respective  dialog by applying the following steps:

1)	if the P-CSCF serves the calling user of the session it shall generate a BYE request based on the information saved for the related dialog, including:

-	a Request-URI, set to the stored Contact header provided by the called user;

-	a To header, set to the To header value as received in the 200 (OK) response for the initial INVITE request;

-	a From header, set to the From header value as received in the initial INVITE request;

-	a Call-ID header, set to the Call-Id header value as received in the initial INVITE request;

-	a CSeq header, set to the current CSeq value stored for the direction from the calling to the called user, incremented by one;

-	a Route header, set to the routeing information towards the called user as stored for the dialog;

-	a Reason header that contains:

-	a 503 (Service Unavailable) response code, if radio/bearer interface resources are no longer available; or

-	a 488 (Not Acceptable Here) response code, if a SDP offer conveyed in a SIP response contained parameters which are not allowed according to the local policy; and

-	further headers, based on local policy.

2)	If the P-CSCF serves the called user of the session it shall generate a BYE request based on the information saved for the related dialog, including:

-	a Request-URI, set to the stored Contact header provided by the calling user;

-	a To header, set to the From header value as received in the initial INVITE request;

-	a From header, set to the To header value as received in the 200 (OK) response for the initial INVITE request;

-	a Call-ID header, set to the Call-Id header value as received in the initial INVITE request;

-	a CSeq header, set to the current CSeq value stored for the direction from the called to the calling user, incremented by one;

-	a Route header, set to the routeing information towards the calling user as stored for the dialog;

-	a Reason header that contains:

-	a 503 (Service Unavailable) response code, if radio/bearer interface resources are no longer available; or

-	a 488 (Not Acceptable Here) response code, if SDP payload contained parameters which are not allowed according to the local policy; and

-	further headers, based on local policy.

3)	send the so generated BYE request towards the indicated user.

4)	upon receipt of the 2xx responses for the BYE request, shall delete all information related to the dialog and the related multimedia session.

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .
The list is also included in a MS Excel file included in the zip file containing the CR cover sheet template.

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.