TSG-CT WG3 Meeting #108-e	C3-201409

E-Meeting, 19th – 28th February 2020											(Revision of C3-201287)

Source:	Huawei

Title:	Pseudo-CR on API enhancement to support I-NEF Event Exposure

Spec:	3GPP TS 29.591 0.3.0

Agenda item:	16.14

Document for:	Agreement

1. Introduction

<Introduction part (optional)>

2. Reason for Change

The API definition to support I-NEF Event Exposure is still incompleted.

3. Conclusions

Enhancement the API definition to support I-NEF event exposure by adding the events, i.e.  Loss of connectivity, UE reachability, Location Reporting, Communication failure, Availability after Downlink Data Notification failure; and Downlink data delivery status.

4. Proposal

It is proposed to agree the following changes to 3GPP TS 29.591 0.3.0.

*** 1st Change ***

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 23.501: "System Architecture for the 5G System; Stage 2".

[3]	3GPP TS 23.502: "Procedures for the 5G System; Stage 2".

[4]	3GPP TS 29.500: "5G System; Technical Realization of Service Based Architecture; Stage 3".

[5]	3GPP TS 29.501: "5G System; Principles and Guidelines for Services Definition; Stage 3".

[6]	OpenAPI: "OpenAPI 3.0.0 Specification", https://github.com/OAI/OpenAPI-Specification/blob/master/versions/3.0.0.md.

[7]	3GPP TR 21.900: "Technical Specification Group working methods".

[8]	3GPP TS 33.501: "Security architecture and procedures for 5G system".

[9]	IETF RFC 6749: "The OAuth 2.0 Authorization Framework".

[10]	3GPP TS 29.510: "5G System; Network Function Repository Services; Stage 3".

[11]	IETF RFC 7540: "Hypertext Transfer Protocol Version 2 (HTTP/2)".

[12]	IETF RFC 8259: "The JavaScript Object Notation (JSON) Data Interchange Format".

[13]	IETF RFC 7807: "Problem Details for HTTP APIs".

[14]	3GPP TS 23.288: "Architecture enhancements for 5G System (5GS) to support network data analytics services".

[15]	3GPP TS 29.522: "5G System; Network Exposure Function Northbound APIs; Stage 3".

[16]	3GPP TS 29.571: "5G System; Common Data Types for Service Based Interfaces; Stage 3".

[17]	3GPP TS 29.520: "5G System; Network Data Analytics Services; Stage 3".

[18]	3GPP TS 29.517: "Application Function Event Exposure Service".

[19]	3GPP TS 29.551: "5G System; Packet Flow Description Management Service; Stage 3".

[20]	3GPP TS 29.541: "5G System; Network Exposure Function Services for Non-IP Data Delivery (NIDD); Stage 3".

[TS29518]	3GPP TS 29.518: "5G System; Access and Mobility Management Services; Stage 3".*** Next Change ***

#### 5.1.6.1	General

This clause specifies the application data model supported by the API.

Table 5.1.6.1-1 specifies the data types defined for the Nnef_EventExposure service based interface protocol.

Table 5.1.6.1-1: Nnef_EventExposure specific Data Types

| Data type | Section defined | Description | Applicability |
| --- | --- | --- | --- |
| NefEvent | 5.1.6.3.3 |  |  |
| NefEventExposureNotif | 5.1.6.2.3 |  |  |
| NefEventExposureSubsc | 5.1.6.2.2 |  |  |
| NefEventNotification | 5.1.6.2.4 |  |  |
| NefEventSubs | 5.1.6.2.5 |  |  |
| UeCommunicationInfo | 5.1.6.2.6 |  |  |
| DddStatusInfo | 5.1.6.2.x |  |  |

Table 5.1.6.1-2 specifies data types re-used by the Nnef_EventExposure service based interface protocol from other specifications, including a reference to their respective specifications and when needed, a short description of their use within the Nnef_EventExposure service based interface.

Table 5.1.6.1-2: Nnef_EventExposure re-used Data Types

| Data type | Reference | Comments | Applicability |
| --- | --- | --- | --- |
| ApplicationId | 3GPP TS 29.571 [13] |  |  |
| AnalyticsReportingRequirement | 3GPP TS 29.520 [17] |  |  |
| CommunicationCollection | 3GPP TS 29.517 [18] |  |  |
| ExceptionInfo | 3GPP TS 29.520 [17] |  |  |
| Supi | 3GPP TS 29.571 [16] |  |  |
| SupportedFeatures | 3GPP TS 29.571 [16] |  |  |
| Uri | 3GPP TS 29.571 [16] |  |  |
| DataTime | 3GPP TS 29.571 [16] |  |  |
| DddTrafficDescriptor | 3GPP TS 29.571 [16] |  |  |
| Gpsi | 3GPP TS 29.571 [16] |  |  |
| PresenceInfo | 3GPP TS 29.571 [16] |  |  |
| UeReachability | 3GPP TS 29.518 [TS29518] |  |  |
| DlDataDeliveryStatus | 3GPP TS 29.571 [16] | Downlink data delivery status |  |
| CommunicationFailure | 3GPP TS 29.518 [TS29518] |  |  |

*** Next Change ***

##### 5.1.6.2.4	Type: NefEventNotification

Table 5.1.6.2.4-1: Definition of type NefEventNotification

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| event | NefEvent | M | 1 | Reported application related event. |  |
| timeStamp | DateTime | M | 1 | Time at which the event is observed. |  |
| svcExprcInfo | ServiceExperienceInfo(FFS) | C | 0..1 | Contains the service experience information. Shall be present if the "event" attribute sets to "SVC_EXPERIENCE" | ServiceExperience |
| ueMobilityInfo | UeMobilityInfo(FFS) | C | 0..1 | Contains the UE mobility information. Shall be present if the "event" attribute sets to "UE_MOBILITY" | UeMobility |
| ueCommInfos | array(UeCommunicationInfo) | C | 1..N | Contains the application communication information. Shall be present if the "event" attribute sets to "UE_COMM" | UeCommunication |
| excepInfos | array(ExceptionInfo) | C | 1..N | Each element represents the exception information for a service flow. Shall be present if the "event" attribute sets to "EXCEPTIONS". | Exceptions |
| supi | Supi | C | 0..1 | Represents a SUPI of the UE. Shall be present if the "event" sets to "LOSS_OF_CONNECTIVITY", "DDD_STATUS", "LOCATION_REPORT", "UE_REACHABILITY", "AVAILABILITY_AFTER_DDN_FAILURE" or "COMM_FAILURE". (NOTE) | LossOfConnectivity DownlinkDataDeliveryStatus AvailabilityAfterDDNFailure CommunicationFailure LocationReport UeReachability |
| gpsi | Gpsi | O | 0..1 | Represents a GPSI of the UE. May be present if available when the "event" sets to "LOSS_OF_CONNECTIVITY", "DDD_STATUS", "LOCATION_REPORT", "UE_REACHABILITY", "AVAILABILITY_AFTER_DDN_FAILURE" or "COMM_FAILURE". (NOTE) | LossOfConnectivity DownlinkDataDeliveryStatus AvailabilityAfterDDNFailure CommunicationFailure LocationReport UeReachability |
| dddTraDescriptor | DddTrafficDescriptor | C | 0..1 | Represents the downlink data descriptor impact by downlink data delivery status change. Shall be present if "event" sets to "DDD_STATUS". | DownlinkDataDeliveryStatus |
| loc | PresenceInfo | C | 0..1 | Represents the location of UE. Shall be present if "event" sets to "LOCATION_REPORT". | LocationReport |
| reachability | UeReachability | C | 0..1 | Represents the reachability of UE. Shall be present if "event" sets to "UE_REACHABILITY". | UeReachability |
| dddStatusInfo | DddStatusInfo | C | 0..1 | Represents the downlink data delivery status information. Shall be present if the "event" sets to "DDD_STATUS". | DownlinkDataDeliveryStatus |
| commFailure | CommunicationFailure | C | 0..1 | Represents the communication failure information for the UE. | CommunicationFailure |
| NOTE: If the event report corresponds to an event subscription of a single UE, then the same UE identifier (i.e. the SUPI and if available the GPSI) received during subscription creation shall be included in the report. If the event report corresponds to an event subscription for group of UEs or any UE, then the SUPI and if available the GPSI shall be included in the event report. |

*** Next Change ***

##### 5.1.6.2.x	Type DddStatusInfo

Table 5.1.6.2.x-1: Definition of type DddStatusInfo

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| dddStatus | DlDataDeliveryStatus | M | 1 | Downlink data delivery status (discarded, transmitted, buffered). |  |
| maxWaitTime | DateTime | C | 0..1 | The estimated maximum waiting time for downlink data delivery, Shall be included for event "downlink data delivery status" with status "BUFFERED". |  |

*** Next Change ***

##### 5.1.6.3.3	Enumeration: NefEvent

The enumeration NefEvent represents the observed event requested by the NF service consumer to be monitored. It shall comply with the provisions defined in table 5.1.6.3.3-1.

Table 5.1.6.3.3-1: Enumeration NefEvent

| Enumeration value | Description | Applicability |
| --- | --- | --- |
| SVC_EXPERIENCE | Indicates that the observed event is service experience. | ServiceExperience |
| UE_COMM | Indicates that the observed event is UE communication. | UeMobility |
| UE_MOBILITY | Indicates that the observed event is UE mobility. | UeCommunication |
| EXCEPTIONS | Indicates that the observed event is exceptions information. | Exceptions |
| LOCATION_REPORT | Indicates that the observed event is the last know location of a UE or a group of UEs in roaming status. | LocationReport |
| UE_REACHABILITY | Indicates that the observed event is the current reachability of a UE or a group of UEs in roaming status. | UeReachability |
| LOSS_OF_CONNECTIVITY | Indicates that the observed event is that a target UE is no longer reachable in roaming status. | LossOfConnectivity |
| COMM_FAILURE | Indicates that the observed event is communication failure in roaming status. | CommunicationFailure |
| DDD_STATUS | Indicates that the observed event is downlink data delivery status in roaming status. | DownlinkDataDeliveryStutus |
| AVAILABILITY_AFTER_DDN_FAILURE | Indicates that the observed event is availability after downlink data notification failure. | AvailabilityAfterDDNFailure |

*** Next Change ***

### 5.1.8	Feature negotiation

The optional features in table 5.1.8-1 are defined for the Nnef_EventExposure API. They shall be negotiated using the extensibility mechanism defined in clause 6.6 of 3GPP TS 29.500 [4].

Table 5.1.8-1: Supported Features

| Feature number | Feature Name | Description |
| --- | --- | --- |
| 1 | ServiceExperience |  |
| 2 | UeMobility |  |
| 3 | UeCommunication |  |
| 4 | Exceptions |  |
| x | LocationReport | This feature indicates support for the "LOCATION_REPORT" event in roaming status. |
| y | UeReachability | This feature indicates support for the "UE_REACHABILITY" event in roaming status. |
| z | LossOfConnectivity | This feature indicates support for the "LOSS_OF_CONNECTIVITY" event in roaming status. |
| a | CommunicationFailure | This feature indicates support for the "COMM_FAILURE" event in roaming status. |
| b | DownlinkDataDeliveryStaus | This feature indicates support for the "DDD_STATUS" event in roaming status. |
| c | AvaiabilityAfterDDNFailure | This feature indicates support for the "AVAILABILITY_AFTER_DDN_FAILURE" event in roaming status. |

*** End of Changes ***