Third Generation Partnership Project (3GPP™)

DRAFT Meeting Report
for
TSG CT WG3
meeting: 61

Ljubljana, Slovenia, 24/01/2011 to 28/01/2011

this draft:  Monday, (2011-02-14) 05:22  [date/time according to secretary's PC time zone setting]

1	Opening of the meeting	4

2	Agenda/schedule	4

2.1	Approval of the agenda.	4

2.2	Proposed schedule	4

3	Registration of documents	4

4	Reports	5

4.1	Report from previous CT3 meeting	5

4.2	Report from previous CT plenary	5

4.3	Reports from other groups	6

5	Items for immediate consideration	6

5.1	IPR disclosures	6

5.2	Other items for immediate consideration	6

6	Received Liaison Statements	6

7	Release 7 and earlier releases (incl. mirror CRs to later releases)	9

7.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	9

7.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	9

7.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]	17

7.4	Multimedia Broadcast and Multicast Service  [MBMS]	17

7.5	Policy and Charging Control [PCC]	17

7.6	Diameter for Gi interface [DIAMGi]	17

7.7	Diameter for Wi interface [DIAMWi]	17

7.8	Multimedia interworking between IMS and CS networks [MIW-IMS]	17

7.9	Protocol impact from providing IMS services via fixed broadband [FBI]	17

7.10	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]	17

7.11	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	17

7.12	Technical Enhancements and Improvements [TEIx]	17

7.13	Other Work Items	17

8	Release 8 (incl. mirror CRs to later releases)	17

8.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	17

8.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	17

8.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]	19

8.4	Multimedia Broadcast and Multicast Service  [MBMS]	19

8.5	Policy and Charging Control (non-SAE) [PCC]	19

8.6	Void	19

8.7	Diameter for Gi interface [DIAMGi]	19

8.8	Diameter for Wi interface [DIAMWi]	19

8.9	Multimedia interworking between IMS and CS networks (incl. MONA extensions) [MIW-IMS]	19

8.10	Protocol impact from providing IMS services via fixed broadband [FBI]	19

8.11	Void	19

8.12	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]	19

8.13	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	19

8.14	PCC aspects of SAE [SAES-St3-PCC]	19

8.14.1	Signalling flows (29.213)	21

8.14.2	Gx and Gxx interfaces (29.212)	21

8.14.3	Rx interface (29.214)	23

8.14.4	S9 interface (29.215)	23

8.15	Interworking between EPC and external PDNs [SAES-St3-intwk]	24

8.16	IMS inter-operator service interconnection interface [FBI2-IOPSI]	24

8.17	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	27

8.18	Interworking between User-to-User Signaling (UUS) and SIP [UUSIW]	27

8.19	Work Items related to TISPAN transfer	27

8.19.1	Maintenance of TISPAN R1 [MAINT_R1]	27

8.19.2	Maintenance of TISPAN R2 [MAINT_R2]	27

8.19.3	Documentation of TISPAN R1 and R2  in CT3 [REDOC_TIS-C3]	27

8.19.4	Support of Overlap signalling [Overlap]	27

8.19.5	Stage 3 (CT3) of CWonIMS [CW_IMS]	27

8.19.6	Stage 3 (CT3) of [CCBS_CCNR]	27

8.20	Contributions on Common IMS related to 3GPP2 [REDOC_3GPP2]	29

8.21	Support of Service-Level Interworking for Messaging Services [MESSIW]	29

8.22	Enhancement of interworking between MTSI and Circuit Switched networks  [MTSI_eMHI]	29

8.23	Core Network Impacts for A-Interface Over IP [AoIP-CN]	29

8.24	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]	30

8.25	CAT solution for voice and video call in CS domain [CAT_SS]	30

8.26	Technical Enhancements and Improvements [TEI8]	30

8.27	Rel-8 contributions on other Work Items	30

9	Release 9 (incl. mirror CRs to later releases)	30

9.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	30

9.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	30

9.3	Protocol impact from providing IMS services via fixed broadband [FBI]	30

9.4	MBMS [MBMS]	30

9.5	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	30

9.6	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	30

9.7	CS-IBCF and CS-TrGW definition in 3GPP specifications [CS-IBCF]	30

9.8	Interconnection Border Control Function (IBCF) – Transition Gateway (TrGW); Ix interface, Stage 3 [IMS_IBCF]	31

9.9	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	31

9.10	Operational Description of the Inter-IMS NNI   [II-NNI]	31

9.11	Support for IMS Emergency Calls over GPRS and EPS [IMS_EMER_GPRS_EPS]	38

9.12	PCC Enhancements [PCC-Enh]	38

9.13	Completion of IMS Restoration Procedures [eIMS_RP]	46

9.14	CT1 aspects of SRVCC support for IMS Emergency Calls [IMS_EMER_GPRS_EPS-SRVCC]	46

9.15	IMS Media Plane Security [MEDIASEC_CORE]	46

9.16	PCC aspects of SAE [SAES-St3-PCC]	46

9.17	Technical Enhancements and Improvements [TEI9]	46

9.18	Rel-9 contributions on other work items	46

10	Release 10	46

10.1	Study on PCRF Failure and Restoration [FS_PCRF-FR]	46

10.2	CPM-SMS Interworking [CPM-SMS]	46

10.3	Optimal Media Routeing [OMR]	46

10.4	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]	53

10.5	Void	58

10.6	Call Completion Not Logged in [CCNL]	58

10.7	IP Flow Mobility and WLAN offload (Stage 3) [IFOM-CT]	58

10.8	Enabling Coder Selection and Rate Adaption for UTRAN and E-UTRAN for Load Adaptive Applications, CN impacts [ECSRA_LAA-CN]	61

10.8.1	Packet Core impacts	62

10.8.2	IMS/CS impacts	62

10.9	S2b Mobility based on GTP [SMOG-St3]	62

10.10	CT aspects of Enhancements for Multimedia Priority Service [eMPS-CN]	63

10.11	PCRF failure and restoration [PCRF-FR]	65

10.12	CT aspects of Multi Access PDN Connectivity  [MAPCON-St3]	65

10.13	CT3 Aspects of Policy Enhancements for Sponsored Connectivity and Coherent Access to Policy related Data Bases [PEST-CT3]	67

10.14	Dynamic View of Headers in Messages for II-NNI [NNI_DV]	76

10.15	Technical Enhancements and Improvements [TEI10]	83

10.16	Other Work Items for Rel-10	87

10.16.1	Void	90

10.16.2	CS and IMS Interworking for CAT service [CIIC]	90

10.16.3	PCC Enhancements [PCC-Enh]	90

10.16.4	PCC aspects of SAE [SAES-St3-PCC]	90

10.16.5	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	90

11	Release 11	90

11.1	Technical Enhancements and Improvements [TEI11]	90

11.2	Other Rel-11 Work Items	90

12	Work Organisation	90

12.1	Work Plan Review	90

13	Summary of results	91

14	Any other business	91

15	Closing of the meeting	91

15.1                TR/TS	91

15.2                Work Item	91

15.3                Liaison Statements	91

15.3.1                  Incoming liaison statements	91

15.3.2                  Outgoing liaison statements	91

15.4	Agreed Change Requests	92

Annex A : List of contribution documents	97

Annex B : List of participants	111

Note: Hyperlinks to tdocs will work only if the present report is in a subdirectory named "report" and the tdocs themselves are in a parallel subdirectory names "docs".

## 1	Opening of the meeting

CT3 Chairman, Dr.Ragnar Huslende welcomed CT3 delegates to CT3#61 meeting in Ljubljana, Slovenia. And this meeting is the debut of Mr.Jiwan Han, the new MCC of CT3. Dr.Ragnar had a welcome speech of CT3#61.

## 2	Agenda/schedule

### 2.1	Approval of the agenda.

C3-110001	Draft Agenda for CT3#61
					Source: CT3 Chairman

Decision: 		The document was agreed.

### 2.2	Proposed schedule

C3-110044	Proposed Schedule for CT3#61
					Source: 	CT3 Chairman

Decision: 		The document was revised to C3-110188.

C3-110188	Proposed Schedule for CT3#61
					Source: CT3 Chairman

(Replaces C3-110044)

Decision: 		The document was revised to C3-110295.

C3-110295	Proposed Schedule for CT3#61
					Source: CT3 Chairman

(Replaces C3-110188)

Decision: 		The document was noted.

## 3	Registration of documents

C3-110002	Allocation of documents to agenda items (start of Day1)
					Source: CT3 Chairman

Decision: 		The document was noted.

C3-110003	Allocation of documents to agenda items (start of Day2)
					Source: CT3 Chairman

Decision: 		The document was noted.

C3-110004	Allocation of documents to agenda items (start of Day3)
					Source: CT3 Chairman

Decision: 		The document was noted.

C3-110005	Allocation of documents to agenda items (start of Day4)
					Source: CT3 Chairman

Decision: 		The document was noted.

C3-110006	Allocation of documents to agenda items (start of Day5)
					Source: CT3 Chairman

Decision: 		The document was noted.

C3-110007	Allocation of documents to agenda items (end of Day5)
					Source: CT3 Chairman

Discussion:

400 document numbers allocated at the end of the meeting

Decision: 		The document was noted.

C3-110180	Allocation of documents to agenda items (at Deadline)
					Source: CT3 Chairman

Discussion:

180 documents numbers allocated at deadline.

Decision: 		The document was noted.

## 4	Reports

### 4.1	Report from previous CT3 meeting

C3-110008	Draft Report from CT3#60
					Source: MCC

Decision: 		The document was approved.

### 4.2	Report from previous CT plenary

C3-110045	Brief Notes from CT#50 relevant to CT3
					Source: CT3 Chairman

Decision: 		The document was noted.

### 4.3	Reports from other groups

## 5	Items for immediate consideration

### 5.1	IPR disclosures

The chairman reminded the delegates of their obligations relating to Intellectual Propoerty Rights using the following wording:

The attention of the members of this Working Group is drawn to the fact that 3GPP Individual Members have the obligation under the IPR Policies of their respective Organizational Partners to inform their respective Organizational Partners of Essential IPRs they become aware of.

The members take note that they are hereby invited:

•  to investigate in their company whether their company does own IPRs which are, or are likely to become Essential in respect of the work of the Technical Specification Group.

•  to notify the Director-General, or the Chairman of their respective Organizational Partners, of all potential IPRs that their company may own, by means of the IPR Statement and the Licensing declaration forms.

### 5.2	Other items for immediate consideration

## 6	Received Liaison Statements

C3-110012	Reply LS to 3GPP TSG CT4 on support of ECN
					Source: Q3/16

Abstract:

Q3/16 thanks 3GPP TSG CT4 for its liaison on ECN (explicit congestion notification) (our TD 330/Gen, yours C4-103381). Q3/16 has noted that 3GPP TS26.114 is based on the IETF work in this area. We do note however that the features described in 3GPP TS26.114 are based on an early private IETF draft (draft westerlund avt-ecn-for-rtp-02) whereas the latest IETF working group supported draft is draft-ietf-avt-ecn-for-rtp-03. We recommend for compatibility that 3GPP TS26.114 be modified to take into account the latest work. For example: 3GPP TS26.114 specifies the use of "nonce" however this is removed in the current IETF draft. Specification 3GPP TS26.114 also does not appear to consider the relationship with RTCP reporting introduced in later drafts.

Q3/16 has analysed (draft-ietf-avt-ecn-for-rtp-03) and sees the general use of ECN functionality in various IP based networks, not only in 3GPP specified networks.

As such Q3/16 has started a work item: H.248.ECN "Explicit Congestion Notification Support". This item will consider the support of ECN in MGs and the interaction with the various RTP/RTCP configurations. The scope of H.248.ECN covers RTP/UDP but would not be limited to that particular bearer type. Likewise it will also focus on supporting any media format which may benefit from ECN indication not just the "AMR" family of codecs. Also in addition to describing the use of ECN related SDP in H.248, Q3/16 sees the need for the definition of statistics for logging purposes and procedures for handling ECN failure and re-negotiation. These functions appear not to be considered by 3GPP TS 26.114.

As per previous work: e.g. H.248.77 "SRTP package and procedures", H.248.72 "H.248 support for MONA", we look forward to receiving your input so that we can provide a solution that may be used by your various H.248 profiles.

Discussion:

Use the latest version of the IETF draft. It is necessary that we have any input requirements to their H.248 ECN work. Related discussion paper: tdoc 123.

Decision: 		The document was noted.

C3-110013	Reply LS to R2-105299 on Handling of UTRAN Mobility Information
					Source: RAN WG2

Abstract:

RAN2 thanks SA2 for the LS on Handling of UTRAN Mobility Information (S2-104449/R2-105299) in the context of CSFB and PS handover, and would like to provide the following responses to the questions raised by SA2.

Question 1: Will the RNC during PS handover always (regardless whether the LAI is changed or not) deliver the LAI as part of the UTRAN Mobility Information to the UE?

Answer: Detailed RNC behaviour is not specified, but RAN2 assumes the indicated behaviour can be expected.

Question 2: Will the RNCs always provide the UTRAN Mobility Information to the UE as soon as possible?

Answer: As indicated above, detailed RNC behaviour is not specified, but RAN2 assumes the indicated behaviour can be expected. From a RAN2 point of view, “as soon as possible” should be as soon as the security operations on the Uu interface are completed, i.e. UTRAN receives the Security Mode Complete from the UE.

Question 3: SA2 would also like to ask whether the RNC would be able to handle and forward to CN a NAS message sent by the UE before the UE receiving the UTRAN Mobility Information.

Answer: After a (PS) handover to UTRAN, and integrity protection has been activated, RAN2 assumes an RNC should be able to handle and forward a NAS message to the appropriate CN domain, but (again) this is up to RNC implementation.

Question 4: In such a case, would sending the NAS message immediately without waiting for the UTRAN Mobility Information be faster than if the UE would wait for the UTRAN Mobility Information?

Answer:

On the network side, sending UMI message after sending the RLC ACK for the Security Mode Complete can take as little as 100 ms, depending on RNC implementation.

Given the above, whether it will be faster to send a NAS message in uplink or to wait for the UMI message can depend on other factors, e.g. the LAI match or mismatch, that are hard to predict and outside the scope of RAN2 expertise.

Discussion:

No impact on CT3 identified.

Decision: 		The document was noted.

C3-110014	LS response on Passing Restart Counter to External Network
					Source: 3GPP TSG SA2

Abstract:

SA2 thanks CT4 for the LS (C4-101562) on Passing Restart Counter to External Network.

With respect to CT4 request to consider the proposed optimization for removing Gx diameter sessions when the SGSN or A-GW restarts as part of the Study on Policy Solutions and Enhancements. SA2 understands that stage 2 requirements for restoration is under CT4 responsibility, so SA2 would assume that CT4 takes care of the stage 2 work for the functionality described.

SA2 does not foresee any need for undertaking any SA2 activity under the study on Policy Solutions and Enhancements.

Discussion:

Cc: CT3

Decision: 		The document was noted.

C3-110015	LS on NIMTC impacts on PMIP
					Source: SA2

Abstract:

As defined in TS23.401, the indicator(s) defined within the NIMTC Work Item is sent to P-GW to apply P-GW control of overload function upon PDN connectivity establishment.

When P-GW control of overload function is applied, P-GW may reject the PDN connectivity request message with an indication of congestion with a back-off timer.

For PMIP based EPC, SA2 agreed that the indicator, congestion indication and back-off timer are exchanged over on-path signalling i.e. PMIP is used rather than Gxc/Gx interfaces.

Discussion:

Mr.Weihua represented this LS. No impact on CT3?

Decision: 		The document was noted.

C3-110016	LS on User CSG Information reporting
					Source: SA2

Abstract:

SA2 thanks CT3 for the LS on User CSG Information reporting.

How to subscribe to User CSG Information changes

The current description in 23.203 defines 3 credit reauthorization triggers over Gy in clause A.1.3.1.3 for GPRS access and in the corresponding clauses for both EPC based and PMIP access and 3 CSG Information reporting triggers over Gx in clause A.1.3.4 for GPRS access and in the corresponding clauses for EPC both GTP and PMIP access that directly correspond to the events of the UE entering/leaving/accessing a CSG cell, the UE entering/leaving/accessing a hybrid cell in which the subscriber is a CSG member or the UE entering/leaving/accessing a hybrid call in which the subscribed is not a CSG member. Separate triggers are defined in order to enable control over what User CSG information are needed so that unnecessary signalling in the network can be avoided and only the needed User CSG information are reported to the OCS and to the OFCS.

How to request the access network to report to the User CSG Information changes

The current description in 23.203 defines that for GPRS and EPC based GTP accesses in clauses A.1.3.4 and A.4.3.4 the GGSN/PDN GW sets the MS Info Change Reporting Action IE based on the information provided by the OCS and the PCRF For EPC based PMIP access the S-GW sets the MS Info Change Reporting Action IE based on the event triggers received from the PCRF as stated in Annex A.5.3.1.3.

Answer #1, item 1: For PMIP, the PCEF subscribes to the event triggers to the BBERF via PCRF based on the information received from both PCEF and OCS and the BBERF will use the event triggers to indicate the access network the required User CSG Reporting,

Answer #1, item 2: For GTP, the PCEF requests the access network to report on User CSG Information Change based on both the information received by the PCRF and the OCS. If different values are provided, the PCEF aggregates the information provided by the PCRF and the OCS.

Answer #2: SA2 confirms that both the OCS and the PCRF can request different User CSG information change reporting levels separately:

•	For online charging the OCS subscribes to the credit reauthorization triggers for User CSG reporting changes to the PCEF.

•	For offline charging the PCRF provisions the User CSG reporting triggers to the PCEF.

Discussion:

Miss. Susanna represented this LS. Mr.Weihua has a question regarding the relations of PCRF,OCS, and PCEF and Miss.Susanna answered for this. Mr.Zhou joined the discussion and all agreeds. (Related CRs in  tdocs 20 & 21)

Decision: 		The document was noted.

## 7	Release 7 and earlier releases (incl. mirror CRs to later releases)

### 7.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 7.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-110072	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-443  (Rel-7) v7.21.0
					Source: Ericsson

Abstract:

Clause 2:

The obsolete RFC 2327 for SDP is replaced with RFC 4566 to be aligned with 3GPP TS 24.229.

Sub-clauses 7.2.3.1.1 and 7.3.3.1.1:

When SIP preconditions are used the I-MGCF should request confirmation for the resource reservation if the received INVITE indicates preconditions as not met.

Sub-clause 7.2.3.1.3:

Conditions when the I-MGCF should send the COT message indicating successful continuity check are clarified since it is unclear if the statement "requested preconditions (if any) in the IMS network have been met" means that both remote and local preconditions must be fulfilled.

Added condition that the offered media streams should be set to active mode.

Sub-clause 7.3.3.1.3:

Conditions when the I-MGCF should send the COT message indicating successful continuity check are clarified since it is unclear if the statement "requested preconditions (if any) in the IMS network have been met" means that both remote and local preconditions must be fulfilled.

Decision: 		The document was revised to C3-110250.

C3-110250	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-443  rev 1 (-) v7.21.0
					Source: Ericsson

(Replaces C3-110072)

Discussion:

MS.Nevenka (from Ericsson) represented this CR. Removed parts will be re-discussed in SLC. (for CT1 or CT3?)

Decision: 		The document was revised to C3-110393.

C3-110393	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-443  rev 2 (-) v7.21.0
					Source: Ericsson

(Replaces C3-110250)

Decision: 		The document was agreed.

C3-110073	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-444  (Rel-8) v8.13.0
					Source: Ericsson

Decision: 		The document was revised to C3-110251.

C3-110251	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-444  rev 1 (-) v8.13.0
					Source: Ericsson

(Replaces C3-110073)

Decision: 		The document was revised to C3-110394.

C3-110394	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-444  rev 2 (-) v8.13.0
					Source: Ericsson

(Replaces C3-110251)

Decision: 		The document was agreed.

C3-110074	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-445  (Rel-9) v9.4.0
					Source: Ericsson

Decision: 		The document was revised to C3-110252.

C3-110252	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-445  rev 1 (-) v9.4.0
					Source: Ericsson

(Replaces C3-110074)

Decision: 		The document was revised to C3-110395.

C3-110395	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-445  rev 2 (-) v9.4.0
					Source: Ericsson

(Replaces C3-110252)

Decision: 		The document was agreed.

C3-110075	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-446  (Rel-10) v10.0.0
					Source: Ericsson

Decision: 		The document was revised to C3-110253.

C3-110253	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-446  rev 1 (-) v10.0.0
					Source: Ericsson

(Replaces C3-110075)

Decision: 		The document was revised to C3-110396.

C3-110396	Clarification of I-MGCF behaviour when SIP preconditions are used
					29.163	  CR-446  rev 2 (-) v10.0.0
					Source: Ericsson

(Replaces C3-110253)

Decision: 		The document was agreed.

C3-110076	Clarification of O-MGCF behaviour when SIP preconditions are used
					29.163	  CR-447  (Rel-7) v7.21.0
					Source: Ericsson

Abstract:

7.2.3.2.2.2 and 7.3.3.2.2.2:

O-MGCF should not set the media stream to inactive mode in the initial SDP offer indicates local preconditions are fulfilled.

7.2.3.2.3 and 7.3.3.2.3:

When O-MGCF indicates local preconditions met in the subsequent SDP offer it should set related media streams to active mode. Preconditions met indication should be sent for each created early SIP dialog for which the received provisional response indicated support for preconditions.

Decision: 		The document was revised to C3-110254.

C3-110254	Clarification of O-MGCF behaviour when SIP preconditions are used
					29.163	  CR-447  rev 1 (-) v7.21.0
					Source: Ericsson

(Replaces C3-110076)

Decision: 		The document was agreed.

C3-110077	Clarification of O-MGCF behaviour when SIP preconditions are used
					29.163	  CR-448  (Rel-8) v8.13.0
					Source: Ericsson

Decision: 		The document was revised to C3-110255.

C3-110255	Clarification of O-MGCF behaviour when SIP preconditions are used
					29.163	  CR-448  rev 1 (-) v8.13.0
					Source: Ericsson

(Replaces C3-110077)

Decision: 		The document was agreed.

C3-110078	Clarification of O-MGCF behaviour when SIP preconditions are used
					29.163	  CR-449  (Rel-9) v9.4.0
					Source: Ericsson

Decision: 		The document was revised to C3-110256.

C3-110256	Clarification of O-MGCF behaviour when SIP preconditions are used
					29.163	  CR-449  rev 1 (-) v9.4.0
					Source: Ericsson

(Replaces C3-110078)

Decision: 		The document was agreed.

C3-110079	Clarification of O-MGCF behaviour when SIP preconditions are used
					29.163	  CR-450  (Rel-10) v10.0.0
					Source: Ericsson

Decision: 		The document was revised to C3-110257.

C3-110257	Clarification of O-MGCF behaviour when SIP preconditions are used
					29.163	  CR-450  rev 1 (-) v10.0.0
					Source: Ericsson

(Replaces C3-110079)

Decision: 		The document was agreed.

C3-110106	New Cause Code mappings of CV 23,38- 47and 65-79
					29.163	  CR-457  (Rel-7) v7.21.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Abstract:

Addition of SIP –ISUP cause Code/Response mappings

Discussion:

The comments were below.

Add NOTE3 to 503

Editorial: Add cause value number, Check font size, Clauses Affected, Update mappings to agreements.

Indicate that 47 is class default.

Accepted in principle:  23, 38, 41-47, 79, 103

65: Ericsson has concerns and asks how to populate Accept header that must be added to cause 415. AT-T has concerns that existing mapping does not give any indication for troubleshooting. Offline discussion

69: Ericsson asks how to populate the Allow header in 405. Oki suggested 501 instead. Agreement to use 501

70: Ericsson asks how to populate the Allow header in 405. Oki suggested 488 instead. Ericson and T-COM propose 501. Agreement to use 501

98: Ericsson asks how to populate the Allow header in 405. Ericsson suggest 501. Agreement to use 501

Decision: 		The document was revised to C3-110258.

C3-110258	New Cause Code mappings of CV 23,38- 47and 65-79
					29.163	  CR-457  rev 1 (-) v7.21.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110106)

Decision: 		The document was agreed.

C3-110107	New Cause Code mappings of CV 23,38- 47and 65-79
					29.163	  CR-458  (Rel-8) v8.13.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110259.

C3-110259	New Cause Code mappings of CV 23,38- 47and 65-79
					29.163	  CR-458  rev 1 (-) v8.13.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110107)

Decision: 		The document was agreed.

C3-110108	New Cause Code mappings of CV 23,38- 47and 65-79
					29.163	  CR-459  (Rel-9) v9.4.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110260.

C3-110260	New Cause Code mappings of CV 23,38- 47and 65-79
					29.163	  CR-459  rev 1 (-) v9.4.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110108)

Decision: 		The document was agreed.

C3-110109	New Cause Code mappings of CV 23,38- 47and 65-79
					29.163	  CR-460  (Rel-10) v10.0.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110261.

C3-110261	New Cause Code mappings of CV 23,38- 47and 65-79
					29.163	  CR-460  rev 1 (-) v10.0.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110109)

Decision: 		The document was agreed.

C3-110110	Change of Cause code mapping
					29.163	  CR-461  (Rel-7) v7.21.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Abstract:

Change of SIP –ISUP-SIP cause Code/Response mapping.

Decision: 		The document was revised to C3-110262.

C3-110262	Change of Cause code mapping
					29.163	  CR-461  rev 1 (-) v7.21.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110110)

Decision: 		The document was agreed.

C3-110111	Change of Cause code mapping
					29.163	  CR-462  (Rel-8) v8.13.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110263.

C3-110263	Change of Cause code mapping
					29.163	  CR-462  rev 1 (-) v8.13.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110111)

Decision: 		The document was agreed.

C3-110112	Change of Cause code mapping
					29.163	  CR-463  (Rel-9) v9.4.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110264.

C3-110264	Change of Cause code mapping
					29.163	  CR-463  rev 1 (-) v9.4.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110112)

Decision: 		The document was agreed.

C3-110113	Change of Cause code mapping
					29.163	  CR-464  (Rel-10) v10.0.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110265.

C3-110265	Change of Cause code mapping
					29.163	  CR-464  rev 1 (-) v10.0.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110113)

Decision: 		The document was agreed.

C3-110117	Mapping of ISUP Cause Value 88 to Response 606 and vice versa
					29.163	  CR-468  (Rel-7) v7.21.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Abstract:

Change mapping in Table 9 and 18. Mapping CV88 to Response 606 and vice

Discussion:

The comment was "Editorials: Remove unaffected Clause etc".

Decision: 		The document was revised to C3-110266.

C3-110266	Mapping of ISUP Cause Value 88 to Response 606 and vice versa
					29.163	  CR-468  rev 1 (-) v7.21.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110117)

Decision: 		The document was agreed.

C3-110118	Mapping of ISUP Cause Value 88 to Response 606 and vice versa
					29.163	  CR-469  (Rel-8) v8.13.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110267.

C3-110267	Mapping of ISUP Cause Value 88 to Response 606 and vice versa
					29.163	  CR-469  rev 1 (-) v8.13.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110118)

Decision: 		The document was agreed.

C3-110119	Mapping of ISUP Cause Value 88 to Response 606 and vice versa
					29.163	  CR-470  (Rel-9) v9.4.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110268.

C3-110268	Mapping of ISUP Cause Value 88 to Response 606 and vice versa
					29.163	  CR-470  rev 1 (-) v9.4.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110119)

Decision: 		The document was agreed.

C3-110120	Mapping of ISUP Cause Value 88 to Response 606 and vice versa
					29.163	  CR-471  (Rel-10) v10.0.0
					Source: Deutsche Telekom, ATT, Telecom Italia

Decision: 		The document was revised to C3-110269.

C3-110269	Mapping of ISUP Cause Value 88 to Response 606 and vice versa
					29.163	  CR-471  rev 1 (-) v10.0.0
					Source: Deutsche Telekom, ATT, Telecom Italia

(Replaces C3-110120)

Decision: 		The document was agreed.

C3-110127	ISUP Cause/SIP Status Code Mapping and SIP Forking
					Source: AT&T

Abstract:

If an ISUP cause code is mapped to a 6xx SIP status code at a PSTN gateway, a forking AS will only terminate that leg.

Furthermore proxy forking at a S-CSCF will not be affected, because it will not fork toward a PSTN gateway.

Discussion:

Ericsson believes that AS can register PSTN user and forking to MGCF can then occur. This should be documented in GSMA specs that Mr.Jan (from Ericsson) will distribute.

AS case will not cause any problems

Decision: 		The document was noted.

### 7.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]

### 7.4	Multimedia Broadcast and Multicast Service  [MBMS]

### 7.5	Policy and Charging Control [PCC]

### 7.6	Diameter for Gi interface [DIAMGi]

### 7.7	Diameter for Wi interface [DIAMWi]

### 7.8	Multimedia interworking between IMS and CS networks [MIW-IMS]

### 7.9	Protocol impact from providing IMS services via fixed broadband [FBI]

### 7.10	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]

### 7.11	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 7.12	Technical Enhancements and Improvements [TEIx]

### 7.13	Other Work Items

## 8	Release 8 (incl. mirror CRs to later releases)

### 8.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 8.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-110114	Missing Timer definition for TIR
					29.163	  CR-465  (Rel-8) v8.13.0
					Source: Deutsche Telekom

Abstract:

Adding of TTIR1 Timer.

Decision: 		The document was revised to C3-110270.

C3-110270	Missing Timer definition for TIR
					29.163	  CR-465  rev 1 (-) v8.13.0
					Source: Deutsche Telekom

(Replaces C3-110114)

Decision: 		The document was revised to C3-110345.

C3-110345	Missing Timer definition for TIR
					29.163	  CR-465  rev 2 (-) v8.13.0
					Source: Deutsche Telekom

(Replaces C3-110270)

Decision: 		The document was agreed.

C3-110115	Missing Timer definition for TIR
					29.163	  CR-466  (Rel-9) v9.4.0
					Source: Deutsche Telekom

Decision: 		The document was revised to C3-110271.

C3-110271	Missing Timer definition for TIR
					29.163	  CR-466  rev 1 (-) v9.4.0
					Source: Deutsche Telekom

(Replaces C3-110115)

Decision: 		The document was revised to C3-110346.

C3-110346	Missing Timer definition for TIR
					29.163	  CR-466  rev 2 (-) v9.4.0
					Source: Deutsche Telekom

(Replaces C3-110271)

Decision: 		The document was agreed.

C3-110116	Missing Timer definition for TIR
					29.163	  CR-467  (Rel-10) v10.0.0
					Source: Deutsche Telekom

Decision: 		The document was revised to C3-110272.

C3-110347	Missing Timer definition for TIR
					29.163	  CR-467  rev 2 (-) v10.0.0
					Source: Deutsche Telekom

(Replaces C3-110272)

Decision: 		The document was agreed.

### 8.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]

### 8.4	Multimedia Broadcast and Multicast Service  [MBMS]

### 8.5	Policy and Charging Control (non-SAE) [PCC]

### 8.6	Void

### 8.7	Diameter for Gi interface [DIAMGi]

### 8.8	Diameter for Wi interface [DIAMWi]

### 8.9	Multimedia interworking between IMS and CS networks (incl. MONA extensions) [MIW-IMS]

### 8.10	Protocol impact from providing IMS services via fixed broadband [FBI]

### 8.11	Void

### 8.12	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]

### 8.13	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 8.14	PCC aspects of SAE [SAES-St3-PCC]

C3-110093	LS on QoS-Negotiation and QoS-Upgrade on the Gx for GnGp SGSN
					Source: Huawei

Abstract:

During CT3#60 meeting, whether the PCEF report the QoS-Negotiation AVP and QoS-Upgrade AVP to the PCRF was discussed.

In TS 29.060, the No QoS negotiation bit field is relevant for an Update PDP Context procedure and is used by SGSN to indicate to GGSN whether QoS re-negotiation may be done during the Update procedure; the Upgrade QoS Supported bit field is relevant for an Create PDP Context or Update PDP Context procedure and is used by SGSN to indicate to GGSN whether QoS upgrade in Response message functionality is supported.

On one hand, if the PCEF does not inform the PCRF that SGSN does not support QoS upgrade, the PCRF may provision an authorized QoS which is higher than the requested QoS for this PDP context, this may cause the termination of the PDP context.

On the other hand, SA2 has the decision that when the Gn/Gp SGSN accesses to the PGW, the IP-CAN type should be set to 3GPP-EPS, and it has specified in TS 23.203 that: “The PDN GW shall mediate Gn/Gp procedures so that PCRF experiences no difference compared to S5/S8 procedures”.

Further, for 3GPP-EPS access type, as the PCEF perform the bearer binding, when the PCRF authorize the PCC rule, it does not know which bearer will be bound to, the PCRF has nothing to do with the bearer level parameters of QoS-Negotiation AVP and QoS-Upgrade AVP.

S4-SGSN has no such problems, as S4-SGSN supports the upgraded QoS, and the S4-SGSN will reject the PDP Context Activation and terminates the procedure if the QoS is negotiated.

The proposed solutions are:

(1)	 For QoS-Negotiation AVP

The PCEF does not report the QoS-Negotiation AVP over Gx interface, taking the same procedure as S4-SGSN to reject the the PDP Context Activation and terminates the procedure if the QoS is negotiated by the PCRF, this has no impact to current SA2 and CT3 specifications.

(2)	For QoS-Upgrade AVP

Solution A:

The PCEF does not report the QoS-Upgrade AVP, and reject the the PDP Context Activation and terminates the procedure if the QoS is upgraded by the PCRF; this has no impact to current SA2 and CT3 specifications;

Solution B:

The PCEF reports the QoS-Upgrade AVP to the PCRF. This has the impact to SA2 and CT3, SA2 need change the IP-CAN type to 3GPP-GPRS if the Gn/Gp SGSN accesses to the PGW, and modify related clauses in TS 23.203.

Discussion:

The comments were below.

WID in CP-080575

The following questions should be asked:

1.	What kind of information can be negotiated? If the QCI and ARP can be changed?

2.	Does the PGW mediate Gn/Gp procedures so that PCRF experiences no difference compared to S5/S8 procedures?

What the PGW action if received QoS-Negotiation AVP and QoS-Upgrade AVP? Terminate the PDP context or not

Decision: 		The document was revised to C3-110201.

C3-110201	LS on QoS-Negotiation and QoS-Upgrade on the Gx for GnGp SGSN
					Source: Huawei

(Replaces C3-110093)

Decision: 		The document was approved.

C3-110174	Reference to 3GPP2 updated
					29.212	  CR-577  (Rel-8) v8.10.0
					Source: Nokia Siemens Networks

Abstract:

Editor’s Note for temporary reference removed.

Discussion:

The reference should be changed to “PCC for cdma2000 1x and HRPD Networks”.

Decision: 		The document was revised to C3-110205.

C3-110205	Reference to 3GPP2 updated
					29.212	  CR-577  rev 1 (-) v8.10.0
					Source: Nokia Siemens Networks

(Replaces C3-110174)

Decision: 		The document was agreed.

C3-110175	Reference to 3GPP2 updated
					29.212	  CR-578  (Rel-9) v9.5.0
					Source: Nokia Siemens Networks

Decision: 		The document was revised.

C3-110206	Reference to 3GPP2 updated
					29.212	  CR-578  rev 1 (-) v9.5.0
					Source: Nokia Siemens Networks

(Replaces C3-110175)

Decision: 		The document was agreed.

C3-110176	Reference to 3GPP2 updated
					29.212	  CR-579  (Rel-10) v10.1.0
					Source: Nokia Siemens Networks

Decision: 		The document was revised to C3-110207.

C3-110207	Reference to 3GPP2 updated
					29.212	  CR-579  rev 1 (-) v10.1.0
					Source: Nokia Siemens Networks

(Replaces C3-110176)

Decision: 		The document was agreed.

#### 8.14.1	Signalling flows (29.213)

#### 8.14.2	Gx and Gxx interfaces (29.212)

C3-110145	Modification failure of APN-AMBR and Default EPS Bearer QoS
					29.212	  CR-566  (Rel-8) v8.10.0
					Source: ZTE

Abstract:

1.	In clause 4.5.5.7, If the modification of the QoS per APN fails, the PCEF shall retain the existing QoS per APN without any modification and send to the PCRF a new CCR command with the Event Trigger set to APN-AMBR _MODIFICATION_FAILURE.

2.	In clause 4.5.5.9, If the modification of the default EPS bearer QoS information fails, the PCEF shall retain the existing default EPS bearer QoS without any modification and send to the PCRF a new CCR command with the Event Trigger set to DEFAULT-EPS-BEARER-QOS _MODIFICATION_FAILURE.

3.	In clause 5.3.7, define the separate event trigger value for the modification failure of APN-AMBR and Default EPS Bearer QoS.

4.	Some event trigger values are corrected so that they would be alignment in the different version for the same event trigger.

Decision: 		The document was revised to C3-110202.

C3-110202	Modification failure of APN-AMBR and Default EPS Bearer QoS
					29.212	  CR-566  rev 1 (-) v8.10.0
					Source: ZTE

(Replaces C3-110145)

Decision: 		The document was agreed.

C3-110146	Modification failure of APN-AMBR and Default EPS Bearer QoS
					29.212	  CR-567  (Rel-9) v9.5.0
					Source: ZTE

Decision: 		The document was revised to C3-110203.

C3-110203	Modification failure of APN-AMBR and Default EPS Bearer QoS
					29.212	  CR-567  rev 1 (-) v9.5.0
					Source: ZTE

(Replaces C3-110146)

Decision: 		The document was agreed.

C3-110147	Modification failure of APN-AMBR and Default EPS Bearer QoS
					29.212	  CR-568  (Rel-10) v10.1.0
					Source: ZTE

Decision: 		The document was revised to C3-110204.

C3-110204	Modification failure of APN-AMBR and Default EPS Bearer QoS
					29.212	  CR-568  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110147)

Decision: 		The document was agreed.

C3-110214	Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R8 29.212)
					29.212	  CR-581  (Rel-8) v8.10.0
					Source: Huawei

Abstract:

For QOS_CHANGE:

Adding the description that “When applicable to 3GPP-GPRS and the PCRF perform bearer binding, the Bearer-Identifier AVP shall be provided to indicate the affected bearer.”

2.	   For QOS_CHANGE_EXCEEDING_AUTHORIZATION:

Adding the description that this is only applied for GPRS access type;

Discussion:

It was the new tdoc for Rel-8.

Decision: 		The document was revised to C3-110333.

C3-110333	CR 581 29.212 Rel-8 Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R8 29.212)
					29.212	  CR-581  rev 1 (-) v..
					Source: Huawei

(Replaces C3-110214)

Decision: 		The document was agreed.

#### 8.14.3	Rx interface (29.214)

#### 8.14.4	S9 interface (29.215)

C3-110148	Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case
					29.215	  CR-129  (Rel-8) v8.8.0
					Source: ZTE

Abstract:

1.	In clause 4.5.1.5, the V-PCRF shall validate the Default-EPS-Bearer-QoS AVP in case it is received in the CCA or RAR command. If the QoS validation fails, the V-PCRF shall retain the existing default EPS bearer QoS without any modification and reject the request using a CCR/RAA command respectively to the H-PCRF. The CCR/RAA shall include the Subsession-Enforcement-Info AVP for the affected S9 subsession that includes the S9 subsession identifier within the Subsession-Id AVP, the QoS-Information AVP to indicate the acceptable QoS, and the Event Trigger set to DEFAULT-EPS-BEARER-QOS_MODIFICATION_FAILURE.

2.	The V-PCRF shall validate the APN-AMBR in case it is received in the CCA or RAR command. If the QoS validation fails, the V-PCRF shall retain the existing APN-AMBR without any modification and reject the request using a CCR/RAA command respectively to the H-PCRF. The CCR/RAA shall include the Subsession-Enforcement-Info AVP for the affected S9 subsession that includes the S9 subsession identifier within the Subsession-Id AVP, the QoS-Information AVP to indicate the acceptable QoS, and the Event Trigger set to APN-AMBR_MODIFICATION_FAILURE.

Decision: 		The document was agreed.

C3-110149	Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case
					29.215	  CR-130  (Rel-9) v9.5.0
					Source: ZTE

Decision: 		The document was agreed.

C3-110150	Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case
					29.215	  CR-131  (Rel-10) v10.0.0
					Source: ZTE

Decision: 		The document was agreed.

C3-110340	Correction to the descriptions of multiple BBERF scenario
					29.215	  CR-139  (Rel-9) v9.5.0
					Source: ZTE

Abstract:

In clause 4.5.1.4, correcting that the H-PCRF and the V-PCRF needs to handle more than one BBERF related with the same IP-CAN session in the multiple BBERF scenarios.

Discussion:

In the meeting, WI and Cat were changed like this "WI = SAES-St3-PCC, Cat = F"

Decision: 		The document was agreed.

C3-110339	Correction to the descriptions of multiple BBERF scenario
					29.215	  CR-138  (Rel-8) v8.8.0
					Source: ZTE

Discussion:

In the meeting, WI and Cat were changed like this "WI = SAES-St3-PCC, Cat = F"

Decision: 		The document was agreed.

### 8.15	Interworking between EPC and external PDNs [SAES-St3-intwk]

### 8.16	IMS inter-operator service interconnection interface [FBI2-IOPSI]

C3-110060	Correcting header table in annex A
					29.165	  CR-170  (Rel-8) v8.7.0
					Source: Ericsson

Abstract:

-Retry-After and Info-Package is added to the table

- NNI is changed to II-NNI

- Table is changed to table

- … between home and visited IMS" is removed

Discussion:

Mr.Jan (from Ericsson) represented this CR. Dr.Thomas , Mr.Naoki and Ms.Beata had an opinion regarding II-NNI and roaming. It was revised to 244.

Decision: 		The document was revised to C3-110244.

C3-110244	Correcting header table in annex A
					29.165	  CR-170  rev 1 (-) v8.7.0
					Source: Ericsson

(Replaces C3-110060)

Decision: 		The document was agreed.

C3-110061	Correcting header table in annex A
					29.165	  CR-171  (Rel-9) v9.5.0
					Source: Ericsson

Discussion:

Mr.Jan (from Ericsson) represented this CR. The  same changes of C3-110060 are needed in document. It was revised to 245.

Decision: 		The document was revised to C3-110245.

C3-110245	Correcting header table in annex A
					29.165	  CR-171  rev 1 (-) v9.5.0
					Source: Ericsson

(Replaces C3-110061)

Decision: 		The document was agreed.

C3-110062	Correcting header table in annex A
					29.165	  CR-172  (Rel-10) v10.2.0
					Source: Ericsson

Discussion:

Mr.Jan (from Ericsson) represented this CR. The minor miss-typing is in document. It was revised to 246.

Decision: 		The document was revised to C3-110246.

C3-110246	Correcting header table in annex A
					29.165	  CR-172  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110062)

Decision: 		The document was agreed.

C3-110066	Adding MMTel feature tag in clause 12
					29.165	  CR-176  (Rel-8) v8.7.0
					Source: Ericsson

Abstract:

Added the MMTel feature tag (+g.3gpp.icsi-ref set to "urn:urn-7:3gpp-service.ims.icsi.mmtel") in the general subclause.

The text is aligned with release 10 text.

Discussion:

Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110067	Adding MMTel feature tag in clause 12
					29.165	  CR-177  (Rel-9) v9.5.0
					Source: Ericsson

Discussion:

Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110068	Adding MMTel feature tag in clause 12
					29.165	  CR-178  (Rel-10) v10.2.0
					Source: Ericsson

Discussion:

Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

### 8.17	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

### 8.18	Interworking between User-to-User Signaling (UUS) and SIP [UUSIW]

### 8.19	Work Items related to TISPAN transfer

#### 8.19.1	Maintenance of TISPAN R1 [MAINT_R1]

#### 8.19.2	Maintenance of TISPAN R2 [MAINT_R2]

#### 8.19.3	Documentation of TISPAN R1 and R2  in CT3 [REDOC_TIS-C3]

#### 8.19.4	Support of Overlap signalling [Overlap]

#### 8.19.5	Stage 3 (CT3) of CWonIMS [CW_IMS]

#### 8.19.6	Stage 3 (CT3) of [CCBS_CCNR]

C3-110083	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-454  (Rel-8) v8.13.0
					Source: Ericsson

Abstract:

Add a mapping between CgPN and P-Asserted-Identity. In addition a formatting error in the implementation of C3-101367 and some minor formatting errors have been corrected.

Discussion:

Mr.Jan (from Ericsson) represented this CR. The delegates found some miss-typing in the document. It was revised to 241.

Decision: 		The document was revised to C3-110241.

C3-110241	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-454  rev 1 (-) v8.13.0
					Source: Ericsson

(Replaces C3-110083)

Decision: 		The document was revised to C3-110348.

C3-110348	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-454  rev 2 (-) v8.13.0
					Source: Ericsson

(Replaces C3-110241)

Decision: 		The document was agreed.

C3-110084	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-455  (Rel-9) v9.4.0
					Source: Ericsson

Discussion:

Mr.Jan (from Ericsson) represented this CR. The same miss-typing of C3-110083 found, so it was revised to 242.

Decision: 		The document was revised to C3-110242.

C3-110242	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-455  rev 1 (-) v9.4.0
					Source: Ericsson

(Replaces C3-110084)

Decision: 		The document was revised to C3-110349.

C3-110349	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-455  rev 2 (-) v9.4.0
					Source: Ericsson

(Replaces C3-110242)

Decision: 		The document was agreed.

C3-110085	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-456  (Rel-10) v10.0.0
					Source: Ericsson

Discussion:

Mr.Jan (from Ericsson) represented this CR. The same miss-typing of C3-110083 found, so it was revised to 243.

Decision: 		The document was revised to C3-110243.

C3-110243	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-456  rev 1 (-) v10.0.0
					Source: Ericsson

(Replaces C3-110085)

Decision: 		The document was revised to C3-110350.

C3-110350	CCBS/CCNR correction of SUBSCRIBE request
					29.163	  CR-456  rev 2 (-) v10.0.0
					Source: Ericsson

(Replaces C3-110243)

Decision: 		The document was agreed.

### 8.20	Contributions on Common IMS related to 3GPP2 [REDOC_3GPP2]

### 8.21	Support of Service-Level Interworking for Messaging Services [MESSIW]

### 8.22	Enhancement of interworking between MTSI and Circuit Switched networks  [MTSI_eMHI]

### 8.23	Core Network Impacts for A-Interface Over IP [AoIP-CN]

C3-110080	IETF Reference Update: RFC 5993
					29.163	  CR-451  (Rel-8) v8.13.0
					Source: Ericsson

Abstract:

IETF draft-ietf-avt-rtp-gsm-hr is changed throughout the document to RFC 5993.

Discussion:

Ms.Nevenka (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110081	IETF Reference Update: RFC 5993
					29.163	  CR-452  (Rel-9) v9.4.0
					Source: Ericsson

Discussion:

Ms.Nevenka (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110082	IETF Reference Update: RFC 5993
					29.163	  CR-453  (Rel-10) v10.0.0
					Source: Ericsson

Discussion:

Mr.Nevenka (from Ericsson) represented this CR.

Decision: 		The document was agreed.

### 8.24	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]

### 8.25	CAT solution for voice and video call in CS domain [CAT_SS]

### 8.26	Technical Enhancements and Improvements [TEI8]

### 8.27	Rel-8 contributions on other Work Items

## 9	Release 9 (incl. mirror CRs to later releases)

### 9.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 9.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 9.3	Protocol impact from providing IMS services via fixed broadband [FBI]

### 9.4	MBMS [MBMS]

### 9.5	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 9.6	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

### 9.7	CS-IBCF and CS-TrGW definition in 3GPP specifications [CS-IBCF]

C3-110289	Adding CS-Ix functionalities to Mc-profile
					29.235	  CR-84  (Rel-9) v9.6.0
					Source: Nokia Siemens Networks

Abstract:

Adding of border control functions to the Mc profile

Discussion:

If Rel-9 version is agreed in CT4.Dependent on 23.205 CR 0240

Decision: 		The document was agreed.

### 9.8	Interconnection Border Control Function (IBCF) – Transition Gateway (TrGW); Ix interface, Stage 3 [IMS_IBCF]

### 9.9	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 9.10	Operational Description of the Inter-IMS NNI   [II-NNI]

C3-110038	Correction on Major Capabilities over II-NNI
					29.165	  CR-155  (Rel-9) v9.5.0
					Source: OKI

Abstract:

Revised description is inserted in 6.1.3 Table 6.1.3.1 of 3GPP TS 29.165.

Decision: 		The document was agreed.

C3-110039	Correction on Major Capabilities over II-NNI
					29.165	  CR-156  (Rel-10) v10.2.0
					Source: OKI

Decision: 		The document was agreed.

C3-110040	Addition of the Target-Dialog header field to the table of major capabilities and Annex A
					29.165	  CR-157  (Rel-9) v9.5.0
					Source: Fujitsu Limited

Abstract:

The following items are corrected.

- Adding RFC 4538 in Section 2 as a reference.

- Adding the Target-Dialog header field to “Table 6.1.3.1: Major capabilities over II-NNI” in Section 6.1.3.

- Adding the Target-Dialog header field to “Table A.1: Supported header fields” in Annex A.

Decision: 		The document was revised to C3-110273.

C3-110273	Addition of the Target-Dialog header field to the table of major capabilities and Annex A
					29.165	  CR-157  rev 1 (-) v9.5.0
					Source: Fujitsu Limited

(Replaces C3-110040)

Decision: 		The document was agreed.

C3-110041	Addition of the Target-Dialog header field to the table of major capabilities and Annex A
					29.165	  CR-158  (Rel-10) v10.2.0
					Source: Fujitsu Limited

Decision: 		The document was revised to C3-110274.

C3-110274	Addition of the Target-Dialog header field to the table of major capabilities and Annex A
					29.165	  CR-158  rev 1 (-) v10.2.0
					Source: Fujitsu Limited

(Replaces C3-110041)

Decision: 		The document was agreed.

C3-110042	Correcting major capabilities related to trust domain
					29.165	  CR-159  (Rel-9) v9.5.0
					Source: NEC, NTT

Abstract:

1) “History-Info”, “P-Asserted-Service” and “Resource-Priority” are applied by a trust domain, according to TS 24.229 (4.4 Trust domain). Hence, their II-NNI status is  “m in case of a trust relationship between the interconnected networks, else n/a” in Table A.1.

Corresponding major capabilities were corrected.

2) “P-Early-Media” is applied by a trust domain, according to TS 24.229 (4.4 Trust domain).

Corresponding major capability and Table A.1 were corrected.

3) “P-Charging-Vector” described in Table 6.2 (Management of SIP header fields over II-NNI in presence or not of a trust relationship) has inconsistent II-NNI status between the major capabilities table and the Table A.1.

Corresponding major capability was corrected.

Decision: 		The document was revised to C3-110275.

C3-110275	Correcting major capabilities related to trust domain
					29.165	  CR-159  rev 1 (-) v9.5.0
					Source: NEC, NTT

(Replaces C3-110042)

Decision: 		The document was revised to C3-110351.

C3-110351	Correcting major capabilities related to trust domain
					29.165	  CR-159  rev 2 (-) v9.5.0
					Source: NEC, NTT

(Replaces C3-110275)

Discussion:

Mr.Naoki (from NEC) represented this CR. Mr.Jan and Dr.Thomas discussed about this. It seems to need the offline discussion.

Decision: 		The document was agreed.

C3-110043	Correcting major capabilities related to trust domain
					29.165	  CR-160  (Rel-10) v10.2.0
					Source: NEC, NTT

Decision: 		The document was revised to C3-110276.

C3-110276	Correcting major capabilities related to trust domain
					29.165	  CR-160  rev 1 (-) v10.2.0
					Source: NEC, NTT

(Replaces C3-110043)

Decision: 		The document was revised to C3-110352.

C3-110352	Correcting major capabilities related to trust domain
					29.165	  CR-160  rev 2 (-) v10.2.0
					Source: NEC, NTT

(Replaces C3-110276)

Decision: 		The document was agreed.

C3-110053	Reference clause updates
					29.165	  CR-163  (Rel-9) v9.5.0
					Source: Ericsson

Abstract:

- draft-drage-sipping-service-identification-04 (July 2010) is replaced by an RFC

- version of draft-ietf-sipcore-keep is updated

- draft-ietf-sip-ipv6-abnf-fix-05 (April 2010) is now replaced with an RFC

- Wrong title on [125] corrected

Decision: 		The document was agreed.

C3-110054	Reference clause updates
					29.165	  CR-164  (Rel-10) v10.2.0
					Source: Ericsson

Decision: 		The document was revised to C3-110277.

C3-110277	Reference clause updates
					29.165	  CR-164  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110054)

Decision: 		The document was agreed.

C3-110057	Updates of the Major capability table
					29.165	  CR-167  (Rel-9) v9.5.0
					Source: Ericsson

Abstract:

- references to new rows 97,99 (Ua role) and 107,109 (Proxy role) are added to the table.

- references to 70C, 70D, 70E, 70F, 70G  (UA role) and 80C, 80D, 80E, 80F, 80G (Proxy role) are removed from the table since the rows are deleted in 3GPP TS 24.229.

Decision: 		The document was revised to C3-110278.

C3-110278	Updates of the Major capability table
					29.165	  CR-167  rev 1 (-) v9.5.0
					Source: Ericsson

(Replaces C3-110057)

Decision: 		The document was revised to C3-110354.

C3-110354	Updates of the Major capability table
					29.165	  CR-167  rev 2 (-) v9.5.0
					Source: Ericsson

(Replaces C3-110278)

Discussion:

Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110058	Updates of the Major capability table
					29.165	  CR-168  (Rel-10) v10.2.0
					Source: Ericsson

Decision: 		The document was revised to C3-110279.

C3-110279	Updates of the Major capability table
					29.165	  CR-168  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110058)

Decision: 		The document was revised to C3-110355.

C3-110355	Updates of the Major capability table
					29.165	  CR-168  rev 2 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110279)

Decision: 		The document was agreed.

C3-110063	Reference update: RFC 6086
					29.165	  CR-173  (Rel-9) v9.5.0
					Source: Ericsson

Abstract:

The reference to the INFO specification is updated. The draft name is replaced with the RFC number.

The new version does not contain any technical changes.

Decision: 		The document was revised to C3-110280.

C3-110280	Reference update: RFC 6086
					29.165	  CR-173  rev 1 (-) v9.5.0
					Source: Ericsson

(Replaces C3-110063)

Decision: 		The document was agreed.

C3-110064	Reference update: RFC 6086
					29.165	  CR-174  (Rel-10) v10.2.0
					Source: Ericsson

Decision: 		The document was agreed.

C3-110139	Alignment of INFO support for DTMF transport with TS 24.182
					29.165	  CR-193  (Rel-9) v9.5.0
					Source: NTT, NTT DOCOMO

Abstract:

The description of SIP INFO mechanism for DTMF transport within CAT is changed in order to align with 3GPP TS 24.182.

Decision: 		The document was revised to C3-110281.

C3-110281	Alignment of INFO support for DTMF transport with TS 24.182
					29.165	  CR-193  rev 1 (-) v9.5.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110139)

Decision: 		The document was agreed.

C3-110140	Alignment of INFO support for DTMF transport with TS 24.182
					29.165	  CR-194  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO

Decision: 		The document was revised to C3-110282.

C3-110282	Alignment of INFO support for DTMF transport with TS 24.182
					29.165	  CR-194  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110140)

Decision: 		The document was revised to C3-110368.

C3-110368	Alignment of INFO support for DTMF transport with TS 24.182
					29.165	  CR-194  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110282)

Decision: 		The document was revised to C3-110397.

C3-110397	Alignment of INFO support for DTMF transport with TS 24.182
					29.165	  CR-194  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110368)

Decision: 		The document was revised to C3-110399.

C3-110399	Alignment of INFO support for DTMF transport with TS 24.182
					29.165	  CR-194  rev 4 (-) v10.2.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110397)

Decision: 		The document was agreed.

C3-110141	The descriptions of values within the Privacy header field
					29.165	  CR-195  (Rel-9) v9.5.0
					Source: NTT, NTT DOCOMO

Abstract:

The descriptions for the clarifications on the support of values within Privacy header field are added in 3GPP TS 29.165 subclause 12.3, 12.4 and 12.6.

Discussion:

It was questioned if this CR is required

Decision: 		The document was revised to C3-110283.

C3-110283	The descriptions of values within the Privacy header field
					29.165	  CR-195  rev 1 (-) v9.5.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110141)

Decision: 		The document was revised to C3-110369.

C3-110369	The descriptions of values within the Privacy header field
					29.165	  CR-195  rev 2 (-) v9.5.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110283)

Decision: 		The document was revised to C3-110372.

C3-110372	The descriptions of values within the Privacy header field
					29.165	  CR-195  rev 3 (-) v9.5.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110369)

Discussion:

It seems to need the offline discussion, and  suspected that this CR is required.

Decision: 		The document was postponed till the next meeting.

C3-110142	The descriptions of values within the Privacy header field
					29.165	  CR-196  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO

Decision: 		The document was revised to C3-110284.

C3-110284	The descriptions of values within the Privacy header field
					29.165	  CR-196  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110142)

Decision: 		The document was revised to C3-110370.

C3-110370	The descriptions of values within the Privacy header field
					29.165	  CR-196  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110284)

Decision: 		The document was revised to C3-110373.

C3-110373	The descriptions of values within the Privacy header field
					29.165	  CR-196  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO

(Replaces C3-110370)

Decision: 		The document was postponed till the next meeting.

### 9.11	Support for IMS Emergency Calls over GPRS and EPS [IMS_EMER_GPRS_EPS]

### 9.12	PCC Enhancements [PCC-Enh]

C3-110020	Completion of CSG information reporting
					29.212	  CR-552  (Rel-9) v9.5.0
					Source: Ericsson

Abstract:

The CSG information reporting with PMIP S5/S8 is enabled.

The CSG-Information-Reporting AVP controls the reporting to the charging domain, including the offline charging system.

Decision: 		The document was revised to C3-110208.

C3-110208	Completion of CSG information reporting
					29.212	  CR-552  rev 1 (-) v9.5.0
					Source: Ericsson

(Replaces C3-110020)

Decision: 		The document was revised to C3-110298.

C3-110298	Completion of CSG information reporting
					29.212	  CR-552  rev 2 (-) v9.5.0
					Source: Ericsson

(Replaces C3-110208)

Decision: 		The document was agreed.

C3-110021	Completion of CSG information reporting
					29.212	  CR-553  (Rel-10) v10.1.0
					Source: Ericsson

Decision: 		The document was revised to C3-110209.

C3-110209	Completion of CSG information reporting
					29.212	  CR-553  rev 1 (-) v10.1.0
					Source: Ericsson

(Replaces C3-110021)

Decision: 		The document was agreed.

C3-110086	Correction of the Event-Trigger AVP enumeration
					29.212	  CR-554  (Rel-9) v9.5.0
					Source: Ericsson

Abstract:

Enumerated values renumbered to align with Release 8 version

Decision: 		The document was revised to C3-110210.

C3-110210	Correction of the Event-Trigger AVP enumeration
					29.212	  CR-554  rev 1 (-) v9.5.0
					Source: Ericsson

(Replaces C3-110086)

Decision: 		The document was agreed.

C3-110087	Correction of the Event-Trigger AVP enumeration
					29.212	  CR-555  (Rel-10) v10.1.0
					Source: Ericsson

Decision: 		The document was revised to C3-110211.

C3-110211	Correction of the Event-Trigger AVP enumeration
					29.212	  CR-555  rev 1 (-) v10.1.0
					Source: Ericsson

(Replaces C3-110087)

Decision: 		The document was agreed.

C3-110090	Bearer binding function in PCEF
					29.212	  CR-556  (Rel-9) v9.5.0
					Source: Ericsson, Huawei

Abstract:

Making normative the description that if the evolved ARP is not supported by the SGSN, the bearer binding function in GGSN/PDN GW shall not combine PCC rules with different ARPs value onto the same PDP context. Including the mapping tables fo the derivation of the Evolved ARP to Rel 99 ARP parameter value as specified in Annex E of TS 23.401.

Decision: 		The document was revised to C3-110212.

C3-110212	Bearer binding function in PCEF
					29.212	  CR-556  rev 1 (-) v9.5.0
					Source: Ericsson, Huawei

(Replaces C3-110090)

Discussion:

Dependent on CR#300 TS29.213

Decision: 		The document was agreed.

C3-110091	Bearer binding function in PCEF
					29.212	  CR-557  (Rel-10) v10.1.0
					Source: Ericsson, Huawei

Decision: 		The document was revised to C3-110213.

C3-110213	Bearer binding function in PCEF
					29.212	  CR-557  rev 1 (-) v10.1.0
					Source: Ericsson, Huawei

(Replaces C3-110091)

Discussion:

Dependent on CR#301 TS 29.213

Decision: 		The document was agreed.

C3-110094	Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212)
					29.212	  CR-558  (Rel-9) v9.5.0
					Source: Huawei

Abstract:

Adding the description that QOS_CHANGE QOS_CHANGE_EXCEEDING_AUTHORIZATION are only applied for GPRS access type; moving the APN QoS change to the DEFAULT_EPS_BEARER_QOS_CHANGE.

Discussion:

QOS_CHANGE can also be applied for APN and keeping DEFAULT_EPS_BEARER_QOS_CHANGE unchanged.

Moved from PCC-Enh Rel-9.

Decision: 		The document was revised to C3-110215.

C3-110215	Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212)
					29.212	  CR-558  rev 1 (-) v9.5.0
					Source: Huawei

(Replaces C3-110094)

Decision: 		The document was revised to C3-110334.

C3-110334	Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212)
					29.212	  CR-558  rev 2 (-) v9.5.0
					Source: Huawei

(Replaces C3-110215)

Decision: 		The document was agreed.

C3-110095	Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212)
					29.212	  CR-559  (Rel-10) v10.1.0
					Source: Huawei

Decision: 		The document was revised to C3-110216.

C3-110216	Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212)
					29.212	  CR-559  rev 1 (-) v10.1.0
					Source: Huawei

(Replaces C3-110095)

Decision: 		The document was revised to C3-110335.

C3-110335	Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212)
					29.212	  CR-559  rev 2 (-) v10.1.0
					Source: Huawei

(Replaces C3-110216)

Decision: 		The document was agreed.

C3-110096	Bearer binding function in GGSN (R9 29.213)
					29.213	  CR-300  (Rel-9) v9.5.0
					Source: Huawei, Ericsson

Abstract:

Adding the description that if the evolved ARP is not supported by the SGSN, the bearer binding function in GGSN shall not combine PCC rules with different ARPs value onto the same PDP context, and the GGSN shall map the Evolved ARP to Rel 99 ARP parameter value as specified in TS 29.212.

Decision: 		The document was revised to C3-110217.

C3-110217	Bearer binding function in GGSN (R9 29.213)
					29.213	  CR-300  rev 1 (-) v9.5.0
					Source: Huawei, Ericsson

(Replaces C3-110096)

Decision: 		The document was revised to C3-110336.

C3-110336	Bearer binding function in GGSN (R9 29.213)
					29.213	  CR-300  rev 2 (-) v9.5.0
					Source: Huawei, Ericsson

(Replaces C3-110217)

Discussion:

Dependent on CR#556 3GPP TS 29.212

Decision: 		The document was revised to C3-110299.

C3-110299	Bearer binding function in GGSN (R9 29.213)
					29.213	  CR-300  rev 3 (-) v9.5.0
					Source: Huawei, Ericsson

(Replaces C3-110336)

Decision: 		The document was agreed.

C3-110097	Bearer binding function in GGSN (R9 29.213)
					29.213	  CR-301  (Rel-10) v10.0.0
					Source: Huawei, Ericsson

Decision: 		The document was revised to C3-110218.

C3-110218	Bearer binding function in GGSN (R9 29.213)
					29.213	  CR-301  rev 1 (-) v10.0.0
					Source: Huawei, Ericsson

(Replaces C3-110097)

Decision: 		The document was revised to C3-110337.

C3-110337	Bearer binding function in GGSN (R9 29.213)
					29.213	  CR-301  rev 2 (-) v10.0.0
					Source: Huawei, Ericsson

(Replaces C3-110218)

Discussion:

Dependent on CR#557 3GPP TS 29.212

Decision: 		The document was revised to C3-110300.

C3-110300	Bearer binding function in GGSN (R9 29.213)
					29.213	  CR-301  rev 3 (-) v10.0.0
					Source: Huawei, Ericsson

(Replaces C3-110337)

Decision: 		The document was agreed.

C3-110151	Fixing Supported-Feature feature bit definitions
					29.214	  CR-164  (Rel-9) v9.5.0
					Source: ZTE

Abstract:

Table 5.3.1 has been updated to indicate which AVPs are applicable to the ProvAFsignalFlow feature bit.

Decision: 		The document was revised to C3-110219.

C3-110219	Fixing Supported-Feature feature bit definitions
					29.214	  CR-164  rev 1 (-) v9.5.0
					Source: ZTE

(Replaces C3-110151)

Decision: 		The document was agreed.

C3-110152	Fixing Supported-Feature feature bit definitions
					29.214	  CR-165  (Rel-10) v10.1.0
					Source: ZTE

Decision: 		The document was revised to C3-110220.

C3-110220	Fixing Supported-Feature feature bit definitions
					29.214	  CR-165  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110152)

Decision: 		The document was agreed.

C3-110172	Bearer control mode when using MUPSAP
					29.212	  CR-575  (Rel-9) v9.5.0
					Source: Qualcomm Incorporated

Abstract:

It is clarified that the PCRF chooses the same bearer control mode for all bearers to the same APN from a UE.

Discussion:

Modify the new text that this is only for MUPSAP, and also add the change to Gxx.

Decision: 		The document was revised to C3-110221.

C3-110221	Bearer control mode when using MUPSAP
					29.212	  CR-575  rev 1 (-) v9.5.0
					Source: Qualcomm Incorporated

(Replaces C3-110172)

Decision: 		The document was revised to C3-110361.

C3-110361	Bearer control mode for multiple PDN connections
					29.212	  CR-575  rev 2 (-) v9.5.0
					Source: Qualcomm Incorporated

(Replaces C3-110221)

Discussion:

Remove MUPSAP from title. Can only be conditionally agreed.(LS) Discuss in SLC whether we want this for Rel-8 also.

Decision: 		The document was conditionally agreed.

C3-110173	Bearer control mode when using MUPSAP
					29.212	  CR-576  (Rel-10) v10.1.0
					Source: Qualcomm Incorporated

Decision: 		The document was revised to C3-110222.

C3-110222	Bearer control mode when using MUPSAP
					29.212	  CR-576  rev 1 (-) v10.1.0
					Source: Qualcomm Incorporated

(Replaces C3-110173)

Decision: 		The document was revised to C3-110362.

C3-110362	Bearer control mode for multiple PDN connections
					29.212	  CR-576  rev 2 (-) v10.1.0
					Source: Qualcomm Incorporated

(Replaces C3-110222)

Discussion:

The title was changed.

Decision: 		The document was Conditionally agreed.

C3-110177	LS on Updating codes in TS 29.230
					Source: Nokia Siemens Networks

Abstract:

CT3 has updated AVP codes and fixed related clashes in TS 29.212. CT3 kindly asks CT4 to update TS 29.230 accrodingly. The following changes are required in TS 29.230:

Decision: 		The document was revised to C3-110223.

C3-110223	LS on Updating codes in TS 29.230
					Source: Nokia Siemens Networks

(Replaces C3-110177)

Discussion:

Will come back to this in Salt Lake C. More new AVPs?  Send the LS to CT4 after the plenary?

Decision: 		The document was postponed till the next meeting.

C3-110314	LS out Bearer control mode and multiple PDN connectivity
					Source: Qualcomm Incorporated

Abstract:

CT3 discussed and conditionally agreed to the enclosed CR on associating the same bearer control mode across simultaneous PDN connections established between a UE and an APN over the same IP-CAN type. CT3 could not see any use case for associating different bearer control mode values for different PDN

Discussion:

Mr.Subramanian (from Qualcomm Incorporated) represented this Outgoing LS.

Decision: 		The document was revised to C3-110363.

C3-110363	LS out Bearer control mode and multiple PDN connectivity
					Source: Qualcomm Incorporated

(Replaces C3-110314)

Decision: 		The document was revised to C3-110367.

C3-110367	LS out Bearer control mode and multiple PDN connectivity
					Source: Qualcomm Incorporated

(Replaces C3-110363)

Decision: 		The document was approved.

### 9.13	Completion of IMS Restoration Procedures [eIMS_RP]

### 9.14	CT1 aspects of SRVCC support for IMS Emergency Calls [IMS_EMER_GPRS_EPS-SRVCC]

### 9.15	IMS Media Plane Security [MEDIASEC_CORE]

### 9.16	PCC aspects of SAE [SAES-St3-PCC]

### 9.17	Technical Enhancements and Improvements [TEI9]

### 9.18	Rel-9 contributions on other work items

## 10	Release 10

### 10.1	Study on PCRF Failure and Restoration [FS_PCRF-FR]

### 10.2	CPM-SMS Interworking [CPM-SMS]

C3-110051	Minor corrections
					29.311	  CR-022  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

Editorial corrections (spelling, unnecessar/missing spaces, content of tables are justified to left, etc.) and some terminology related errors corrected.

Discussion:

Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110052	Remove unexplained NOTEs
					29.311	  CR-023  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

The 2 NOTEs are removed.

Discussion:

Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

### 10.3	Optimal Media Routeing [OMR]

C3-110022	Revised WID on Optimal Media Routeing
					Source: Alcatel-Lucent

Abstract:

International communications and terminal roaming introduce a number of scenarios where sessions may traverse multiple IMS networks. The use of Border Control Functions makes both the signalling and bearer path traverse through the same networks and this could result in a non-optimal media path with a higher than optimal number of transition gateways inserted.

To ensure Quality of Service (QoS), minimal delay, and, in certain cases, minimal transport costs, there is a need to enable the routeing of media traffic via an optimal path between those networks without including unnecessary parts of the path that the signalling flow needs to take.

As a result of this, SA2 have developed a feature called OMR which addresses this and other use cases.

The OMR algorithm also has the potential to reduce the number of calls where transcoding is applied and to reach a more optimal allocation of transcoding points.

Stage 3 text is needed to realize the stage 2 requirements provided by 3GPP TS 23.228.

Discussion:

Regarding OMR, Mr. Jim suggested that this item is moved to CT4.  It was postpone after CT4 discussion.

After the lunch break, Mr.Jan had an opinion that it possibly impect to CT3. It will be endorsed by CT4.

Decision: 		The document was agreed.

C3-110023	Restructuring and completion of OMR SDP offer procedures
					29.079 v-
					Source: Alcatel-Lucent, Nokia Siemens Networks, Ericsson

Abstract:

The text is restructured to avoid duplicated text and bring the order of the procedures closer to the anticipated order in real implementations.

Procedures for proactive transcoding without resouce reservation are added.

Arbitrary restrictions on when a secondary realm can be added are removed.

Discussion:

Alcatel-Lucent represented this PCR.Dr.Thomas had an opinion and Alcatel-Lucent agreed with him. It was revised to 233.

Decision: 		The document was revised to C3-110233.

C3-110233	Restructuring and completion of OMR SDP offer procedures
					29.079 v-
					Source: Alcatel-Lucent, Nokia Siemens Networks, Ericsson

(Replaces C3-110023)

Decision: 		The document was agreed.

C3-110024	Restructuring and completion of OMR SDP answer procedures
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

The OMR SDP answer procedures have been reorganized to be easier to understand and to remove duplication of procedure text.

Some logic errors have been corrected.

Discussion:

Alcatel-Lucent represented this PCR. Dr.Thomas had an opinion and Mr.Jan joined the discussion. It seems to need the offline discussion. It was revised to 234.

Decision: 		The document was revised to C3-110234.

C3-110234	Restructuring and completion of OMR SDP answer procedures
					29.079 v-
					Source: Alcatel-Lucent

(Replaces C3-110024)

Decision: 		The document was agreed.

C3-110025	Restructuring and completion of OMR UA procedures
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

The OMR SDP answer procedures have been reorganized to be easier to understand and remove duplication of procedure text.

Some logic errors have been corrected.

Discussion:

Mr.Richard represented this PCR. Mr.Jan had a comment that some words are missing and there is some miss-typing. It was revised to 235

Decision: 		The document was revised to C3-110235.

C3-110235	Restructuring and completion of OMR UA procedures
					29.079 v-
					Source: Alcatel-Lucent

(Replaces C3-110025)

Decision: 		The document was agreed.

C3-110026	OMR check sum procedures
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

The existing OMR text assumes that a OMR checksum will be calculated that cover both the session level and media level information. This would have be calculated independently for each media line. This means it would be possible to determine if the SDP has been changed, but not if just the session level information or just the media level information was modified.

To address this shortcoming two separate checksums are proposed, one for the session level information and one for the media level information. Both check-sum attributes will be proposed as new media level attributes

Discussion:

Mr.Jim (Alcatel-Lucent) represented this PCR. Dr.Thomas had a question and Mr.Jim answered for it. Mr.Jan joined the discussion for checksum and the others. It seems to need the offline discussion. It was revised to 231.

Decision: 		The document was revised to C3-110231.

C3-110231	OMR check sum procedures
					29.079 v-
					Source: Alcatel-Lucent

(Replaces C3-110026)

Decision: 		The document was revised to C3-110374.

C3-110374	OMR check sum procedures
					29.079 v-
					Source: Alcatel-Lucent

(Replaces C3-110231)

Decision: 		The document was agreed.

C3-110027	Updated OMR CapNeg procedures
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

Multiple editor’s notes related to capneg are removed and the capneg procedures are updated to require an IMS-ALG to use the same configuration number when making backward compatible changes to preferred configurations.

Discussion:

Mr.Richard (Alcatel-Lucent) represented this PCR. Mr.Jan had a suggestion regarding some definition and Mr.Richard agreed with him. C3-110027 and C3-110122 were merged into 236.

Decision: 		The document was merged with C3-110122  into C3-110236.

C3-110028	Encapsulation of session level information during OMR procedures
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

The session level encapsulation procedures are modified to encapsulate session level information whenever there is a change at the media level.

Discussion:

Mr.Richard represented this PCR. Mr.Jan had a comment regarding reconstruction of sentence.

Decision: 		The document was agreed.

C3-110029	Handling of SDP o-line during OMR
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

A statement is made the SDP session level lines not addressed are handled per standard IMS-ALG procedures.

Discussion:

Mr.Jim represented this PCR. Mr.Jan,  Mr.Richard, Dr.Thomas had an opinion that some text need to be changed. It was revised to 237.

Decision: 		The document was revised to C3-110237.

C3-110237	Handling of SDP o-line during OMR
					29.079 v-
					Source: Alcatel-Lucent

(Replaces C3-110029)

Decision: 		The document was revised to C3-110375.

C3-110375	Handling of SDP o-line during OMR
					29.079 v-
					Source: Alcatel-Lucent

(Replaces C3-110237)

Decision: 		The document was agreed.

C3-110030	Deletion of OMR editor's note regarding 24.229 profile table
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

The existing editor's note is removed.

Discussion:

Mr.Jim represented this PCR. It will be agreed after CT1's decision. Ms.Nevenka suggested that the decision should be 'pre-agreed'. Related CR is agreed in CT1

Decision: 		The document was agreed.

C3-110031	Remove OMR trust domain editor's note
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

The existing editor's note is removed.

Discussion:

Mr.Jim represented this PCR.

Decision: 		The document was agreed.

C3-110032	Remove editor's note for "codec" and "codec list" definitions
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

Remove the editor's note.

Discussion:

Mr.Jim represented this PCR. Dr.Thomas had an opinion regarding sentence.

Decision: 		The document was agreed.

C3-110033	Remove editor's note for placement of realm definition in TS 24.229
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

The editor's note is removed.

Discussion:

Mr.Jim represented this PCR.

Decision: 		The document was agreed.

C3-110034	Deletion of OMR Annex A of 29.079
					29.079 v-
					Source: Alcatel-Lucent

Abstract:

Annex A deleted

Discussion:

Mr.Jim represented this PCR.

Decision: 		The document was agreed.

C3-110035	OMR SDP attribute syntax definition (for information)
					Source: Alcatel-Lucent

Abstract:

Refernces updated.

Abbreviations updates.

Working Annex A of TS 29.079 is moved to clause 7 of 24.229 with minor modifications to align to 24.229 reference numbers and removal of editor's note indicating that this action is to occur.

Discussion:

Mr.Jim represented this information. The attached document introduces the OMR SDP syntax into 3GPP TS 24.229 – owned by CT1. It is provided here for consideration and approval prior to being presented in CT1. Dr.Thomas and Mr.Jan joined the discussion. It was revised to 232

Decision: 		The document was revised to C3-110232.

C3-110232	OMR SDP attribute syntax definition (for information)
					Source: Alcatel-Lucent

(Replaces C3-110035)

Discussion:

This version is the output from CT1. CT3 needs to know at least the technically changes and that the CR has been accepted by CT1 so that we can remove the corresponding text in 29.079. (ref tdoc 34)

Decision: 		The document was noted.

C3-110048	Annex X with simple message flows introduced
					Source: Ericsson

Abstract:

One very simple example flow added. (More complex scenarios to be added later)

Discussion:

Mr.Jan (from Ericsson) represented this PCR.  Mr.Richard, Mr.Roland and Dr.Thomas had a comment that some corrections are needed for clear understanding. It was revised to 238.

Decision: 		The document was revised to C3-110238.

C3-110238	Annex X with simple message flows introduced
					Source: Ericsson

(Replaces C3-110048)

Decision: 		The document was agreed.

C3-110122	Handling of capability negotiation
					29.079 v1.0.0
					Source: Nokia Siemens Networks

Abstract:

An IMS-ALGs shall not compare codec information in received visited realm instances with the codec information in an SDP answer with capneg attributes, and will thus not initiate a second offer answer exchange.

As a consequence, a decision to establish an optimised path can only be reached as part of the SDP offer procedures for the IMS ALG.

To aid the establishment of an optimised path in this phase, an IMS ALG that uses SDP capneg and added codecs available via transcoding shall initiate a second offer-answer exchange.

Discussion:

Dr.Thomas (from Nokia Siemens Networks) represent this PCR. Mr.Richard and Mr.Jan had an opinion. It seems to need the offline discussion.it was revised to 236. tdoc 122 and 27 are merged into 236.

Decision: 		The document was merged with C3-110027 into C3-110236.

C3-110236	Updated OMR CapNeg procedures
					29.079 v1.0.0
					Source: Nokia Siemens Networks, Alcatel-Lucent

(Replaces C3-110122)

Abstract:

The capneg procedures are updated to require an IMS-ALG to use the same configuration number when making backward compatible changes to preferred configurations.

Decision: 		The document was revised to C3-110376.

C3-110376	Updated OMR CapNeg procedures
					29.079 v1.0.0
					Source: Nokia Siemens Networks, Alcatel-Lucent

(Replaces C3-110236)

Decision: 		The document was agreed.

C3-110377	TR 29.079 v1.1.0
					Source: Alcatel-Lucent

Discussion:

To be made available by Jim February 7th.

Decision: 		The document was postponed.

### 10.4	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]

C3-110036	Add missing E-CSCF to II-NNI network diagram
					29.165	  CR-154  (Rel-10) v10.2.0
					Source: Alcatel-Lucent

Decision: 		The document was withdrawn.

C3-110049	RFC 5318 in the Major capability table
					29.165	  CR-161  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

RFC 5318 added in the major capability table

Discussion:

Mr.Jan (from Ericsson) represented this CR. Dr.Thomas had an opinion regarding numbering. It was revised to 248.

Decision: 		The document was revised to C3-110248.

C3-110248	RFC 5318 in the Major capability table
					29.165	  CR-161  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110049)

Decision: 		The document was agreed.

C3-110050	Updating OMA presence requirements
					29.165	  CR-162  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

- The editor's note is removed and replaced with a subclause per presence service function.

- The OMA presence 2.0 is updated with more detail requirements and aligned with OMA 1.1.

Discussion:

Mr.Jan (from Ericsson) represented this CR. Dr.Thomas  and Mr.Roland had an opinion. It was revised to 249.

Decision: 		The document was revised to C3-110249.

C3-110249	Updating OMA presence requirements
					29.165	  CR-162  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110050)

Decision: 		The document was revised to C3-110378.

C3-110378	Updating OMA presence requirements
					29.165	  CR-162  rev 2 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110249)

Decision: 		The document was agreed.

C3-110055	Introduction of ATCF
					29.165	  CR-165  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

ATCF is introduced in the architecture

Discussion:

Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110056	Interoperability of IMS Service Continuity over II-NNI updates
					29.165	  CR-166  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

- Included stable procedure changes

- Added Editor's notes as reminders so we don't forget rel-10 updates that are not ready yet

Discussion:

Mr.Jan (from Ericsson) represented this CR. There were some missing-typing & part and it was revised to 315.

Decision: 		The document was revised to C3-110315.

C3-110315	Interoperability of IMS Service Continuity over II-NNI updates
					29.165	  CR-166  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110056)

Decision: 		The document was revised to C3-110286.

C3-110286	Interoperability of IMS Service Continuity over II-NNI updates
					29.165	  CR-166  rev 2 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110315)

Decision: 		The document was agreed.

C3-110059	Adding new header fields Annex A
					29.165	  CR-169  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

P-Refused-URI-List, Policy-Contact, Suppress-If-Match, Target-Dialog header fields are added to the table in Annex A

Discussion:

Mr.Jan (from Ericsson) represented this CR. Mr.Naoki, Dr.Thomas had a comment regarding Annex A and References and Ms.Beata, Mr.Kenjiro joined the discussion. It was revised to 316

Decision: 		The document was revised to C3-110316.

C3-110316	Adding new header fields Annex A
					29.165	  CR-169  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110059)

Decision: 		The document was revised to C3-110287.

C3-110287	Adding new header fields Annex A
					29.165	  CR-169  rev 2 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110316)

Decision: 		The document was revised to C3-110379.

C3-110379	Adding new header fields Annex A
					29.165	  CR-169  rev 3 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110287)

Decision: 		The document was agreed.

C3-110065	Reference points Mi, Mm, Mw and I2
					29.165	  CR-175  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

- I2 added to the list of symbols.

- A NOTE added

Discussion:

Mr.Jan (from Ericsson) represented this CR. Dr.Thomas had a question and Mr.Jan answered for it. Mr.Naoki joined the discussion. It was revised to 317.

Decision: 		The document was revised to C3-110317.

C3-110317	Reference points Mi, Mm, Mw and I2
					29.165	  CR-175  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110065)

Decision: 		The document was agreed.

C3-110069	Minor corrections to 3GPP TS 29.165
					29.165	  CR-179  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

Editorial errors corrected

Discussion:

Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110070	Alignment with 23.228 Ici reference point
					29.165	  CR-180  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

Removed I-CSCF from the Ici reference point description.

Discussion:

It was postponed from Jacksonville meeting. Mr.Jan (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110071	Miscellaneous error corrections to 3GPP TS 29.165
					29.165	  CR-181  (Rel-10) v10.2.0
					Source: Ericsson

Abstract:

Miscellaneous errors corrected

Discussion:

Mr.Jan (from Ericsson) represented this CR. Dr.Thomas had a question regarding 3rd change. It was revised to 318.

Decision: 		The document was revised to C3-110318.

C3-110318	Miscellaneous error corrections to 3GPP TS 29.165
					29.165	  CR-181  rev 1 (-) v10.2.0
					Source: Ericsson

(Replaces C3-110071)

Decision: 		The document was agreed.

C3-110179	Addition of normative references for in band DTMF and SDP messages
					29.165	  CR-197  (Rel-10) v10.2.0
					Source: Orange

Abstract:

Normative references have been added in:

-	§ 7.1 (Media and Codec) for the SIP/DP codec negotiation procedure and for in-band DTMF (with RTP);

-	§ 6.1.2.1 (SDP protocol; general) for the encoding of SDP bodies.

-	References section was updated accordingly.

Discussion:

Ms.Beata (from Orange) represented this CR. Mr.Roland had a question regarding NOTE 3, and Dr.Thomas gave a suggestion of SDP protocol. It seems to need the offline discussion and was revised to 319.

Decision: 		The document was revised to C3-110319.

C3-110319	Addition of normative references for in band DTMF and SDP messages
					29.165	  CR-197  rev 1 (-) v10.2.0
					Source: Orange

(Replaces C3-110179)

Decision: 		The document was revised to C3-110380.

C3-110380	Addition of normative references for in band DTMF and SDP messages
					29.165	  CR-197  rev 2 (-) v10.2.0
					Source: Orange

(Replaces C3-110319)

Decision: 		The document was agreed.

### 10.5	Void

### 10.6	Call Completion Not Logged in [CCNL]

### 10.7	IP Flow Mobility and WLAN offload (Stage 3) [IFOM-CT]

C3-110098	Event triggers for multiple BBERFs in IP flow mobility case (R10 29.212)
					29.212	  CR-560  (Rel-10) v10.1.0
					Source: Huawei

Abstract:

Adding the AN-GW-Address AVP in the Event-Report-Indication AVP

Discussion:

Mr.Weihua (from Huawei) represented this CR. Mr.Patrick had a question rearding it and Mr.Weihua answered for Mr.Patrick's question.  Mr.Zhou and Miss Susanna joined this discussion and commented about missing part of this CR. It was revised to 190 and need offline discussion.

Decision: 		The document was revised to C3-110190.

C3-110190	Event triggers for multiple BBERFs in IP flow mobility case (R10 29.212)
					29.212	  CR-560  rev 1 (-) v10.1.0
					Source: Huawei

(Replaces C3-110098)

Decision: 		The document was agreed.

C3-110143	IFOM message flow
					29.213	  CR-307  (Rel-10) v10.0.0
					Source: Qualcomm Incorporated

Abstract:

Addition of text describing usage of IP flow mobility routing rules in case of IP-CAN session establishment

Addition of 2 message flows describing the case of IP flow mobility when multiple accesses are used

Discussion:

Mr.Patrick (From Qualcomm) represented this CR. Mr.Weihua,  Mr.Zhou, Miss. Susanna,and  Mr.Chairman commented about this CR and it was revised to 191.

Decision: 		The document was revised to C3-110191.

C3-110191	IFOM message flow
					29.213	  CR-307  rev 1 (-) v10.0.0
					Source: Qualcomm Incorporated

(Replaces C3-110143)

Discussion:

Mr.Patrick (from Qualcomm Incorporated) represented this CR. Mr.Norbert had a comment regarding cover page and  Mr.Zhou joined the discussion about PCRF and PCEF. It was revised to 296.

Decision: 		The document was revised to C3-110296.

C3-110296	IFOM message flow
					29.213	  CR-307  rev 2 (-) v10.0.0
					Source: Qualcomm Incorporated

(Replaces C3-110191)

Decision: 		The document was agreed.

C3-110144	Identification of BBF against IP flow mobility routing rule
					29.212	  CR-574  (Rel-10) v10.1.0
					Source: Qualcomm Incorporated

Abstract:

Removal of editor’s notes of 4a.5.7.3. Provisioning of solution for the case of gw-control session with no IP frame AVP

Discussion:

Mr.Patrick (from Qualcomm Incorporated) ) represented this CR. Mr.Weihua had a question and Miss Susana joined the discussion.it was revised to 192.

Decision: 		The document was revised to C3-110192.

C3-110192	Identification of BBF against IP flow mobility routing rule
					29.212	  CR-574  rev 1 (-) v10.1.0
					Source: Qualcomm Incorporated

(Replaces C3-110144)

Discussion:

It was revised to 297 for the same reason of C3-110191.

Decision: 		The document was revised to C3-110297.

C3-110297	Identification of BBF against IP flow mobility routing rule
					29.212	  CR-574  rev 2 (-) v10.1.0
					Source: Qualcomm Incorporated

(Replaces C3-110192)

Decision: 		The document was revised to C3-110302.

C3-110302	Identification of BBF against IP flow mobility routing rule
					29.212	  CR-574  rev 3 (-) v10.1.0
					Source: Qualcomm Incorporated

(Replaces C3-110297)

Decision: 		The document was agreed.

C3-110153	RAT based charging for IFOM
					29.212	  CR-569  (Rel-10) v10.1.0
					Source: ZTE

Abstract:

If the IP flow mobility is supported and the tariff depends on what access network is in use for the sevice data flow, then a separate Charging key is allocated for each access network, and the PCRF sets the Charging key in accordance with the access network in use

Discussion:

Mr.Zhou represented this CR. Miss.Susanna and Mr.Simmon had an opinion for it and  Mr.Fernando joined the discussion.  It seems to need the offline discussion. It was revised to 194.

Decision: 		The document was revised to C3-110194.

C3-110194	RAT based charging for IFOM
					29.212	  CR-569  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110153)

Decision: 		The document was revised to C3-110353.

C3-110353	RAT based charging for IFOM
					29.212	  CR-569  rev 2 (-) v10.1.0
					Source: ZTE

(Replaces C3-110194)

Decision: 		The document was agreed.

C3-110154	Usage of the IFOM related AVPs in Subsession-Enforcement-Info
					29.215	  CR-132  (Rel-10) v10.0.0
					Source: ZTE

Abstract:

Routing-Rule-Install and Routing-Rule-Remove AVPs are only applicable when the Subsession-Enforcement-Info AVP is provided within a CCR

Discussion:

Mr.Zhou represented this CR. Mr.Weihua had a comment regarding AVP. It was revised to 195.

Decision: 		The document was revised to C3-110195.

C3-110195	Usage of the IFOM related AVPs in Subsession-Enforcement-Info
					29.215	  CR-132  rev 1 (-) v10.0.0
					Source: ZTE

(Replaces C3-110154)

Decision: 		The document was agreed.

### 10.8	Enabling Coder Selection and Rate Adaption for UTRAN and E-UTRAN for Load Adaptive Applications, CN impacts [ECSRA_LAA-CN]

C3-110092	Clarifying the use of MBR>GBR
					29.213	  CR-299  (Rel-10) v10.0.0
					Source: Ericsson

Abstract:

It is stated that the PCRF may be configured with operator specific policies that may enable or prevent the use of MBR>GBR.

Discussion:

Miss. Susana represented this CR. Mr.Weihua had a question and Mr.Susana answered for it.Dr.Thomas  and Mr.Zhou joined the discussion. It was revised to 193

Decision: 		The document was revised to C3-110193.

C3-110193	Clarifying the use of MBR>GBR
					29.213	  CR-299  rev 1 (-) v10.0.0
					Source: Ericsson

(Replaces C3-110092)

Discussion:

It seems to need the offline discussion.

Decision: 		The document was postponed till the next meeting.

C3-110123	Status of ECN discussions in SA4 and anticipated impacts to CT3
					Source: Nokia Siemens Networks

Abstract:

This contribution aims to trigger some discussion in CT3 about a number of issues related to ECN support, and update CT3 about the status of related discussions in SA4 and IETF AVT.

Discussion:

Dr.Thomas represented this discussion paper. Mr.Phil and Dr.Thomas discussed about status of discussions of SA4. It seems to need more offline discussion. It was revised to 239.

Decision: 		The document was revised to C3-110239.

C3-110239	Status of ECN discussions in SA4 and anticipated impacts to CT3
					Source: Nokia Siemens Networks

(Replaces C3-110123)

Discussion:

LS Out Questions to SA4 on ECN.

Decision: 		The document was postponed till the next meeting.

#### 10.8.1	Packet Core impacts

#### 10.8.2	IMS/CS impacts

### 10.9	S2b Mobility based on GTP [SMOG-St3]

C3-110124	S2b GTP addition to Annex D.1
					29.212	  CR-564  (Rel-10) v10.1.0
					Source: alcatel-lucent

Abstract:

Paragraph reworded to remove ambiguity as not all non-3GPP accesses require Gxx

Decision: 		The document was revised to C3-110224.

C3-110224	S2b GTP addition to Annex D.1
					29.212	  CR-564  rev 1 (-) v10.1.0
					Source: alcatel-lucent

(Replaces C3-110124)

Decision: 		The document was revised to C3-110338.

C3-110338	S2b GTP addition to Annex D.1
					29.212	  CR-564  rev 2 (-) v10.1.0
					Source: alcatel-lucent

(Replaces C3-110224)

Decision: 		The document was agreed.

C3-110125	S2b RAT Type
					29.212	  CR-565  (Rel-10) v10.1.0
					Source: alcatel-lucent

Abstract:

A new RAT is defined and the specification is updated in accordance with 29.274

Decision: 		The document was revised to C3-110225.

C3-110225	S2b RAT Type
					29.212	  CR-565  rev 1 (-) v10.1.0
					Source: alcatel-lucent

(Replaces C3-110125)

Decision: 		The document was agreed.

C3-110126	S2b HO
					29.213	  CR-302  (Rel-10) v10.0.0
					Source: alcatel-lucent

Decision: 		The document was withdrawn.

### 10.10	CT aspects of Enhancements for Multimedia Priority Service [eMPS-CN]

C3-110017	Bearer priority handling for EMPS.
					29.212	  CR-551  (Rel-10) v10.1.0
					Source: Ericsson

Abstract:

Clause 4.5.x.1.3 is updated so that only the ARP is updated upon IMS priority service invocation/revokation.

Discussion:

Miss.Susana (from Ericsson) represented this CR.

Decision: 		The document was agreed.

C3-110018	Bearer priority handling for EMPS.
					29.213	  CR-297  (Rel-10) v10.0.0
					Source: Ericsson

Discussion:

Miss.Susana represented this CR.

Decision: 		The document was agreed.

C3-110019	MPS Support over Rx
					29.214	  CR-158  (Rel-10) v10.1.0
					Source: Ericsson

Abstract:

New AVPs are defined to identify an MPS session and namespace to be prioritized.

Procedures have been defined for the PCRF to identify the MPS session and take specific actions in the main body and in the IMS annex.

Discussion:

Miss.Susana represented this CR. This CR is related to tdoc 99. Mr.Fernando and Mr.Weihua had an opinion regarding the priority of MPS and MPS session and Miss.Susana answered for it. Dr.Thomas joined the discussion. It was revised to 197.

Decision: 		The document was revised to C3-110197.

C3-110197	MPS Support over Rx
					29.214	  CR-158  rev 1 (-) v10.1.0
					Source: Ericsson

(Replaces C3-110019)

Discussion:

This CR postponed till the next meeting. Mr.Martin will set up a conference call Thursday 10th Feb.15:00~17:00 CET. CRs to be provided asap on the CT3 mailing list.

Decision: 		The document was postponed till the next meeting.

C3-110099	Supporting MPS over Rx (R10 29.214)
					29.214	  CR-160  (Rel-10) v10.1.0
					Source: Huawei

Abstract:

Adding the definition of MPS-Session-Indication AVP and related procedure.

Discussion:

Mr.Weihua represented this CR. Miss.Susanna had a comment. It needs offline discussion. It was merged with 19 into 197.

Decision: 		The document was merged with C3-110019 into C3-110197.

C3-110155	Update of the gateway control session establishment procedure for eMPS
					29.213	  CR-303  (Rel-10) v10.0.0
					Source: ZTE, Ericsson

Abstract:

(1)	In step 5, SPR may include MPS EPS Priority, MPS Priority Level and IMS Signalling Priority of establishment a PS session with priority

In step 6, for case 2b and IP-CAN session establishment, if MPS EPS Priority, MPS Priority Level, and IMS Signalling Priority are present for the user, the PCRF takes the information into account.

Discussion:

Mr.Zhou represented this CR.

Decision: 		The document was agreed.

C3-110322	Discussion: Example eMPS Call Scenarios
					Source: A&T

Discussion:

Mr.Martin (from AT&T) represented this discussion paper. Mr.Weihua and Miss Susana ask a question to Mr.Martin, He answered for it. See comments at C3-110197

Decision: 		The document was noted.

### 10.11	PCRF failure and restoration [PCRF-FR]

### 10.12	CT aspects of Multi Access PDN Connectivity  [MAPCON-St3]

C3-110156	Applicability of the access network information related AVPs in Subsession-Enforcement-Info
					29.215	  CR-133  (Rel-10) v10.0.0
					Source: ZTE

Abstract:

Clarify that IP-CAN-Type, RAT-Type, 3GPP-SGSN-MCC-MNC, 3GPP-SGSN-Address, 3GPP-SGSN-IPv6-Address, RAI, 3GPP-User-Location-Info, 3GPP2-BSID and User-CSG-Information are only applicable to functionality introduced with the MAPCON feature as described in clause 5.4.1.

Discussion:

Mr.Zhou (from ZTE) represented this CR. Miss.Susanna had an opinion regarding some sentences and Dr.Zhou agreed with her. It was revised to 198.

Decision: 		The document was revised to C3-110198.

C3-110198	Applicability of the access network information related AVPs in Subsession-Enforcement-Info
					29.215	  CR-133  rev 1 (-) v10.0.0
					Source: ZTE

(Replaces C3-110156)

Decision: 		The document was agreed.

C3-110157	Correction to the descriptions of multiple BBERF scenario
					29.215	  CR-134  (Rel-10) v10.0.0
					Source: ZTE

Abstract:

(1)	In clause 4.5.1.4, correcting that the H-PCRF and the V-PCRF needs to handle more than one BBERF related with the same IP-CAN session in the multiple BBERF scenarios

In clause 4.5.1.8, adding a NOTE to clarify that scenario that there are two BBERFs related with the same UE when the multi access PDN connectivity is supported is separate from the multiple BBERF scenarios as described in clause 4.5.1.4

Discussion:

Mr.Zhou represented this CR. Miss.Susanna had an opinion and Mr.Zhou agreed with her. It was revised to 199.

Decision: 		The document was revised to C3-110199.

C3-110199	Correction to the descriptions of multiple BBERF scenario
					29.215	  CR-134  rev 1 (-) v10.0.0
					Source: ZTE

(Replaces C3-110157)

Decision: 		The document was revised to C3-110341.

C3-110341	Correction to the descriptions of multiple BBERF scenario
					29.215	  CR-134  rev 2 (Rel-10) v10.0.0
					Source: ZTE

(Replaces C3-110199)

Discussion:

Moved from Rel-10 (WI MAPCON), WI : SAES-St3-PCC

,Cat B->A

Decision: 		The document was agreed.

C3-110158	Resolve the conflict of the access network information at the command level and the subsession level for the MAPCON scenario
					29.215	  CR-135  (Rel-10) v10.0.0
					Source: ZTE

Abstract:

(1)	For clause 4.5.1.8, add a sentence to clarify that the access network informaiton reported at the command level is only applicable for the IP-CAN session which no access network information reported in the corresponding S9 subsession.

For clause 5.3.2, Delete the related editor’s note.

Discussion:

Mr.Zhou represented this CR. Mr.Weihua had a question regarding 1st change and Mr.Zhou answered for it.Miss Susanna and Dr.Thomas joined the discussion regarding adding paragraph and changing sentence.  It seems to need the offline discussion. It was revised to 200.

Decision: 		The document was revised to C3-110200.

C3-110200	Resolve the conflict of the access network information at the command level and the subsession level for the MAPCON scenario
					29.215	  CR-135  rev 1 (-) v10.0.0
					Source: ZTE

(Replaces C3-110158)

Decision: 		The document was agreed.

### 10.13	CT3 Aspects of Policy Enhancements for Sponsored Connectivity and Coherent Access to Policy related Data Bases [PEST-CT3]

C3-110088	SPR data usage optional for sponsored data connectivity
					29.213	  CR-298  (Rel-10) v10.0.0
					Source: Ericsson

Abstract:

Implementing the stage 2 requirement that the PCRF may authorize a sponsored connectivity without requiring explicit authorizing data from the SPR to do so.

Discussion:

Miss.Susana (from Ericsson) represented this CR. Mr.Weihua had  a question regarding 29.212. Mr.zhou joined the discussion about V-PCRF. It was revised to 226.

Decision: 		The document was revised to C3-110226.

C3-110226	SPR data usage optional for sponsored data connectivity
					29.213	  CR-298  rev 1 (-) v10.0.0
					Source: Ericsson

(Replaces C3-110088)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was postponed till the next meeting.

C3-110089	The support for sponsored connectivity declared initially and maintained througout IP-CAN session
					29.214	  CR-159  (Rel-10) v10.1.0
					Source: Ericsson

Abstract:

The Editor's note is removed without any further action.

Discussion:

Miss Susana (from Ericsson) represented this CR. Mr.Weihua had a question regarding PCRF, PCEF and Miss.Susana answered for it. Mr.Zhou joined the discussion about PCRF,PCEF. It was revised to 227.

Decision: 		The document was revised to C3-110227.

C3-110227	Authorization of the sponsored data connectivity(29.214)
					29.214	  CR-159  rev 1 (-) v10.1.0
					Source: Ericsson, ZTE

(Replaces C3-110089)

Discussion:

Mr.Zhou (from ZTE) had a question regarding 1st change and Mr.Subramanian joined the discussion. It seems to need the offline discussion and was revised to 364.The title was changed.

Decision: 		The document was revised to C3-110364.

C3-110364	Authorization of the sponsored data connectivity(29.214)
					29.214	  CR-159  rev 2 (-) v10.1.0
					Source: Ericsson, ZTE

(Replaces C3-110227)

Decision: 		The document was revised to C3-110381.

C3-110381	Authorization of the sponsored data connectivity(29.214)
					29.214	  CR-159  rev 3 (-) v10.1.0
					Source: Ericsson, ZTE

(Replaces C3-110364)

Discussion:

Dependent on  TS 29.212 #561

Decision: 		The document was agreed.

C3-110100	Reporting for sponsored connectivity (R10 29.212)
					29.212	  CR-561  (Rel-10) v10.1.0
					Source: Huawei

Abstract:

Adding the definition of SPONSOR_ IDENTIFIER _LEVEL and related description in the Reporting-Level AVP.

Decision: 		The document was agreed.

C3-110101	ASP operators information for sponsored data connectivity (R10 29.214)
					29.214	  CR-161  (Rel-10) v10.1.0
					Source: Huawei

Abstract:

Adding the descrition to support the sponsored data connectivity of the application service provider to align with SA2 requirement.

Decision: 		The document was revised to C3-110185.

C3-110102	Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212)
					29.212	  CR-562  (Rel-10) v10.1.0
					Source: Huawei

Discussion:

Before the meeting, it was revised to 186.

Decision: 		The document was revised to C3-110186.

C3-110103	Usage for sponsored connectivity (R10 29.214)
					29.214	  CR-162  (Rel-10) v10.1.0
					Source: Huawei

Discussion:

Before the meeting, it was revised to 187

Decision: 		The document was revised to C3-110187.

C3-110159	Clarification of the sponsored data connectivity support (29.212)
					29.212	  CR-570  (Rel-10) v10.1.0
					Source: ZTE

Abstract:

1.	Descriptions of authorization is specifies in  clause 4.5.2.6

2.	Sponsor Identity and Application Service Provider Identity may be provided within the PCC rule for the offline charging

Other minor correction

Discussion:

Mr.Zhou represented this CR. Miss.Susana had a comment in 1st change and Mr.Weihua joined the discussion about PCRF. It was merged with 186  into 229.

Decision: 		The document was merged with C3-110186 into C3-110229.

C3-110160	Correction to feature bit for sponsored data connectivity (29.212)
					29.212	  CR-571  (Rel-10) v10.1.0
					Source: ZTE

Discussion:

Mr.Zhou (from ZTE) represented this CR. Miss.Susana had a comment regarding 'SponsoredConnectivity'. It was revised to 291.

Decision: 		The document was revised to C3-110291.

C3-110291	Correction to feature bit for sponsored data connectivity (29.212)
					29.212	  CR-571  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110160)

Decision: 		The document was agreed.

C3-110161	Correction to Sponsor-Identity AVP and Application-Service-Provider-Identity AVP(29.212)
					29.212	  CR-572  (Rel-10) v10.1.0
					Source: ZTE

Abstract:

(1)	Sponsor-Identity and Application-Service-Provider-Identity may be included in  in Charging-Rule-Definition AVP for the offline charging

Application-Service-Provider-Identity is added into Charging-Rule-Definition AVP

Discussion:

Mr.Zhou (from ZTE) represented this CR. Miss.Susana had a comment. It was revised to 292

Decision: 		The document was revised to C3-110292.

C3-110292	Correction to Sponsor-Identity AVP and Application-Service-Provider-Identity AVP(29.212)
					29.212	  CR-572  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110161)

Decision: 		The document was revised to C3-110343.

C3-110343	Correction to Sponsor-Identity AVP and Application-Service-Provider-Identity AVP(29.212)
					29.212	  CR-572  rev 2 (-) v10.1.0
					Source: ZTE

(Replaces C3-110292)

Discussion:

Dependent on 29.212 CR#561

Decision: 		The document was agreed.

C3-110162	Clarify the usage reporting during the IP-CAN session modification(29.213)
					29.213	  CR-304  (Rel-10) v10.0.0
					Source: ZTE

Abstract:

If the session modifcation affected a sponsored data flow and the H-PCRF detects that the usage threshold provided by the AF has been reached, this message includes the accumulated usage in the Used-Service-Unit AVP within the Sponsored-Connectivity-Data AVP and the Specific-Action AVP set to the value USAGE_REPORT.

Discussion:

Mr.Zhou (from ZTE) represented this CR.

Decision: 		The document was agreed.

C3-110163	Offline charging for sponsored data connectivity(29.213)
					29.213	  CR-305  (Rel-10) v10.0.0
					Source: ZTE

Abstract:

If the provided PCC rules are related to an AF session associated with a sponsor, the H-PCRF includes the Usage-Monitoring-Information AVP in the Charging-Rule-Definition AVP if AF provided the application usage thresholds and may also include the Sponsor-Identity AVP and the Application-Service-Provider-Identity AVP that it received from the AF in the Charging-Rule-Definition AVP if the offline charging is applicable for the PCC rules.

Discussion:

Mr.Zhou (from ZTE) represented this CR. Miss.Susana had an opinion and it was revised to 293.

Decision: 		The document was revised to C3-110293.

C3-110293	Offline charging for sponsored data connectivity(29.213)
					29.213	  CR-305  rev 1 (-) v10.0.0
					Source: ZTE

(Replaces C3-110163)

Decision: 		The document was revised to C3-110344.

C3-110344	Offline charging for sponsored data connectivity(29.213)
					29.213	  CR-305  rev 2 (-) v10.0.0
					Source: ZTE

(Replaces C3-110293)

Discussion:

Dependent  on 29.212 CR# 561

Decision: 		The document was agreed.

C3-110164	Authorization of the sponsored data connectivity(29.214)
					29.214	  CR-166  (Rel-10) v10.1.0
					Source: ZTE

Abstract:

1.	The PCRF peoforms the authorizations of sponsored data connectivity in the initial provisioning of session informatin and modification of session information procedure. If the authoriztion is failure, the PCRF responds to the AF with an AA-Answer including the Experrimental-Result-Code AVP set to the value UNAUTHORIZED_SPONSORED_DATA_CONNECTIVITY.

2.	The new Experrimental-Result-Code AVP, “UNAUTHORIZED_SPONSORED_DATA_CONNECTIVITY”, is defined.

Other minor corrections

Discussion:

Mr.Zhou (from ZTE) represented this CR. Miss.Susana and Mr.Weihua had a comment regarding 1st change and the last change. It was revised to 294.

Decision: 		The document was revised to C3-110294.

C3-110294	Authorization of the sponsored data connectivity(29.214)
					29.214	  CR-166  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110164)

Decision: 		The document was revised to C3-110330.

C3-110330	Authorization of the sponsored data connectivity(29.214)
					29.214	  CR-166  rev 2 (-) v10.1.0
					Source: ZTE

(Replaces C3-110294)

Discussion:

Miss Susana (from Ericsson) had a comment regarding sentence in 1st change. It was merged into 227.

Decision: 		The document was merged into C3-110227.

C3-110165	Correction to feature bit for sponsored data connectivity (29.214)
					29.214	  CR-167  (Rel-10) v10.1.0
					Source: ZTE

Abstract:

(1)	Delete the unnecessary sentence in the description of feature bit “SponsoredConnectivity” (i.e. this feature is described in subclause 4.4.5b).

(2)	 Add the NOTE to clarify that the feature bit “SponsoredConnectivity” excludes the capability that PCRF supports the usage monitoring.

(3)	Define a new feature bit (i.e. SponsoredConnectivity-UsageMonitoring) that indicates that PCRF support for usage monitoring for sponsored data connectivity

(4)	 Change the applicability of Granted-Service-Unit and Used-Service-Unit to SponsoredConnectivity-UsageMonitoring

Change the applicability of value Usage_Report of Specific-Action to SponsoredConnectivity-UsageMonitoring

Discussion:

Mr.Zhou (from ZTE) represented this CR. Miss Susana and Mr.Subramanian had a comment and Mr.Zhou agreed with her. It was revised to 307.

Decision: 		The document was revised to C3-110307.

C3-110307	Correction to feature bit for sponsored data connectivity (29.214)
					29.214	  CR-167  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110165)

Decision: 		The document was agreed.

C3-110166	Correction to the Reporting Usage for Sponsored Data Connectivity(29.214)
					29.214	  CR-168  (Rel-10) v10.1.0
					Source: ZTE

Abstract:

1.	Clarify the accumulated usage reporting procedure. When the PCRF detects that the usage threshold has been reached, the PCRF shall report the accumulated usage since the last report to the AF in a RA-Request (RAR) command with the Specific-Action AVP set to the value USAGE_REPORT. Otherwise, when the AF session is terminated (e.g. due to the IP-CAN session termination or AF initiated AF session termination), the PCRF shall report the accumulated usage since the last report to the AF in ST-Answer (STA) command

Other minor corrections

Discussion:

Mr.Zhou (from ZTE) represented this CR. Mr.Subramanian and Mr.Norbert had a commint regarding missing word in 1st change. Miss Susana and Mr.Fernando had a comment regrarding AF session. It was revised to 308.

Decision: 		The document was revised to C3-110308.

C3-110308	Correction to the Reporting Usage for Sponsored Data Connectivity(29.214)
					29.214	  CR-168  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110166)

Decision: 		The document was agreed.

C3-110171	Support sponsored data connectivity in roaming case
					29.215	  CR-137  (Rel-10) v10.0.0
					Source: ZTE

Abstract:

(1)	For the case that AF located the in the HPLMN, the H-PCRF performs the authorizations based on sponsored data connectivity profiles stored in the SPR located in the HPLMN. The provisioning of sponsored data connectivity per PCC rule shall be performed using the PCC and QoS rule provisioning procedure from the H-PCRF to the V-PCRF.

(2)	For the case that AF located the in the VPLMN, the V-PCRF performs the authorizations based on sponsored data connectivity profiles stored in the SPR located in the VPLMN. In this case, the V-PCRF handles the sponsored data connectivity locally as described in 3GPP TS29.212[3].

(3)	Feature fit for SponsoredConnectivity is set as SponsoredConnectivity-OfflineCharging which indicates support for offline charging with Sponsor Identity and Application Service Provider Identity of sponsored data connectivity feature.

Discussion:

Mr.Zhou (from ZTE) represented this CR. Mr.Suburamanian, Miss Susana, Mr.Fernando discussed this CR, but it seems to need offline discussion. It was revised to 309

Decision: 		The document was revised to C3-110309.

C3-110309	Support sponsored data connectivity in roaming case
					29.215	  CR-137  rev 1 (-) v10.0.0
					Source: ZTE

(Replaces C3-110171)

Discussion:

Wait for reply LS from SA2

Decision: 		The document was postponed till the next meeting.

C3-110184	Reporting for sponsored connectivity (R10 29.212)
					29.212	  CR-561r1  rev 1 (Rel-10) v10.1.0
					Source: Huawei, Orange

Abstract:

Adding the definition of SPONSOR_ IDENTIFIER _LEVEL and related description in the Reporting-Level AVP.

Discussion:

Mr.Weihua (from Huawei) represented this CR. Miss.Susana had a comment regarding 'SPONSOR_ IDENTIFIER'. Mr.Zhou joined the discussion about this. It was revised to 228.

Decision: 		The document was revised to C3-110228.

C3-110228	Reporting for sponsored connectivity (R10 29.212)
					29.212	  CR-561r1  rev 2 (-) v10.1.0
					Source: Huawei, Orange

(Replaces C3-110184)

Decision: 		The document was agreed.

C3-110185	ASP operators information for sponsored data connectivity (R10 29.214)
					29.214	  CR-161r1  rev 1 (Rel-10) v10.1.0
					Source: Huawei, Orange

(Replaces C3-110101)

Abstract:

Adding the descrition to support the sponsored data connectivity of the application service provider to align with SA2 requirement.

Discussion:

Mr.Weihua (from Huawei) represented this CR. There is an opinion regarding IMS. Miss.Susana had a general comment about this CR and Mr.Weihua answered for it. It seems to need offline discussion.

Decision: 		The document was revised to C3-110342.

C3-110342	ASP operators information for sponsored data connectivity (R10 29.214)
					29.214	  CR-161r1  rev 2 (-) v10.1.0
					Source: Huawei, Orange

(Replaces C3-110185)

Discussion:

New input from SA2. The CR may not be needed?

Decision: 		The document was postponed till the next meeting.

C3-110186	Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212)
					29.212	  CR-562r1  rev 1 (Rel-10) v10.1.0
					Source: Huawei, Orange

Abstract:

Adding the definition of SPONSOR_ IDENTIFIER _LEVEL and related description in the Reporting-Level AVP.

Discussion:

Mr.Weihua (from Huawei) represented this CR. Mr.Zhou  and Miss.Susana discussed about PCRF. The delegate found some miss-typing in cover sheet. It was revised to 229.

Decision: 		The document was revised to C3-110229.

C3-110229	Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212)
					29.212	  CR-562r1  rev 2 (-) v10.1.0
					Source: Huawei, Orange

(Replaces C3-110186)

Decision: 		The document was revised to C3-110301.

C3-110301	Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212)
					29.212	  CR-562r1  rev 3 (-) v10.1.0
					Source: Huawei, Orange

(Replaces C3-110229)

Discussion:

Mr.Weihua,Miss Susana, Mr.Zhou and Mr.Fernando discussed about Sponsored Data Connectivity. It was revised to 365.

Decision: 		The document was revised to C3-110365.

C3-110365	Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212)
					29.212	  CR-562r1  rev 4 (-) v10.1.0
					Source: Huawei, Orange

(Replaces C3-110301)

Decision: 		The document was agreed.

C3-110187	Usage for sponsored connectivity (R10 29.214)
					29.214	  CR-162r1  rev 1 (Rel-10) v10.1.0
					Source: Huawei, Orange

Abstract:

Modify the descrition in clause 4.4.1 and 4.4.2 to align with SA2 requirement.

Discussion:

Mr.Weihua (from Huawei) represented this CR. Mr.Robert, Miss.Susana had a comment regarding AF. It was revised to 230.

Decision: 		The document was revised to C3-110230.

C3-110230	Usage for sponsored connectivity (R10 29.214)
					29.214	  CR-162r1  rev 2 (-) v10.1.0
					Source: Huawei, Orange

(Replaces C3-110187)

Decision: 		The document was agreed.

C3-110313	LS out Sponsored data connectivity in the roaming case
					Source: ZTE

Discussion:

Mr.Zhou (from ZTE) represented this outgoing LS. It was revised to 303.

Decision: 		The document was revised to C3-110303.

C3-110303	LS out Sponsored data connectivity in the roaming case
					Source: ZTE

(Replaces C3-110313)

Discussion:

Mr.Nobert (from Nokia Siemens Network) had a commnet regarding Action 2. It was revised to 366.

Decision: 		The document was revised to C3-110366.

C3-110366	LS out Sponsored data connectivity in the roaming case
					Source: ZTE

(Replaces C3-110303)

Decision: 		The document was approved.

### 10.14	Dynamic View of Headers in Messages for II-NNI [NNI_DV]

C3-110128	New annex for dynamic view of SIP messages
					29.165	  CR-182  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

1. The title of the annex is added.

2. The general explanation of the new Annex is added in subclause X.1.

3. The subclause titles and editor's notes for each SIP methods are added.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. Mr.Jan had a comment regarding dynamic view and Dr.Thomas and Ms.Beata joined this discussion and It seems to need the offline discussion. It was revised to 320.

Decision: 		The document was revised to C3-110320.

C3-110320	New annex for dynamic view of SIP messages
					29.165	  CR-182  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110128)

Decision: 		The document was revised to C3-110383.

C3-110383	New annex for dynamic view of SIP messages
					29.165	  CR-182  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110320)

Decision: 		The document was agreed.

C3-110129	Summary of notation codes in dynamic view (ACK method)
					29.165	  CR-183  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within ACK request in dynamic view is added.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. Mr.Jan had a comment regarding ACK method and Dr.Thomas, Mr. Jim joined the discussion. It seems to need the offline discussion. It was revised to 321.

Decision: 		The document was revised to C3-110321.

C3-110321	Summary of notation codes in dynamic view (ACK method)
					29.165	  CR-183  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110129)

Discussion:

The CRs in this series are agreed as a basis for further work. They are subject to possible further revisions at the next meeting.  The final decision on whether to submit the CRs to the plenary will be made at the next meeting.

Companies should ask for revision of the existing CR numbers, and keep changes-on-changes in the versions submitted to the next meeting.

In SLC we need to keep track of the revision numbers and remove changes-on-changes.

Decision: 		The document was agreed.

C3-110130	Summary of notation codes in dynamic view (BYE method)
					29.165	  CR-184  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

It is not possible to know the conditons of SIP header fields sent over the II-NNI between operators and result in inter-operability problems.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. There are the same comment of C3-110129 and Dr.Thomas had an another comment regarding extra explanation for understading and 'Geolocation-Error'. Ms.Beata, Mr.Jan, Dr.Thomas  joined the discussion about 'WWW-Authenticate'. It was revised to 323.

Decision: 		The document was revised to C3-110323.

C3-110323	Summary of notation codes in dynamic view (BYE method)
					29.165	  CR-184  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110130)

Decision: 		The document was revised to C3-110305.

C3-110305	Summary of notation codes in dynamic view (BYE method)
					29.165	  CR-184  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110323)

Decision: 		The document was revised to C3-110385.

C3-110385	Summary of notation codes in dynamic view (BYE method)
					29.165	  CR-184  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110305)

Decision: 		The document was agreed.

C3-110131	Summary of notation codes in dynamic view (CANCEL method)
					29.165	  CR-185  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within CANCEL request and response in dynamic view is added.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. There are the same comment of C3-110130 and Dr.Thomas had an another comment regarding table x.4.2. Ms.Beata joined the discussion about this.It was revised to 324.

Decision: 		The document was revised to C3-110324.

C3-110324	Summary of notation codes in dynamic view (CANCEL method)
					29.165	  CR-185  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110131)

Decision: 		The document was agreed.

C3-110132	Summary of notation codes in dynamic view (INVITE method)
					29.165	  CR-186  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within INVITE request and response in dynamic view is added.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. Ms.Beata had a question and Mr.Jim answered for it. Dr.Thomas had a comment regarding 'History-Info', 'P-Asserted-Service' and 'P-Preferred-Service', 'P-Called-Party-ID'. Mr.Jan, Mr.Jim, Ms.Beata  joined the discussion and it seems to need offline discussion. It was revised to 325.

Decision: 		The document was revised to C3-110325.

C3-110325	Summary of notation codes in dynamic view (INVITE method)
					29.165	  CR-186  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110132)

Decision: 		The document was revised to C3-110306.

C3-110306	Summary of notation codes in dynamic view (INVITE method)
					29.165	  CR-186  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110325)

Decision: 		The document was revised to C3-110386.

C3-110386	Summary of notation codes in dynamic view (INVITE method)
					29.165	  CR-186  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110306)

Decision: 		The document was agreed.

C3-110133	Summary of notation codes in dynamic view (MESSAGE method)
					29.165	  CR-187  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within MESSAGE request and response in dynamic view is added.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. This CR was  the same condition of C3-110132. Dr.Thomas, Ms.Beata joined this discussion about table x.7.1. It was revised to 326.

Decision: 		The document was revised to C3-110326.

C3-110326	Summary of notation codes in dynamic view (MESSAGE method)
					29.165	  CR-187  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110133)

Decision: 		The document was revised to C3-110356.

C3-110356	Summary of notation codes in dynamic view (MESSAGE method)
					29.165	  CR-187  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110326)

Decision: 		The document was revised to C3-110387.

C3-110387	Summary of notation codes in dynamic view (MESSAGE method)
					29.165	  CR-187  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110356)

Decision: 		The document was agreed.

C3-110134	Summary of notation codes in dynamic view (OPTIONS method)
					29.165	  CR-188  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within OPTIONS request and response in dynamic view is added.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. There was the same discussion of C3-110133. It was revised to 324.

Decision: 		The document was revised to C3-110327.

C3-110327	Summary of notation codes in dynamic view (OPTIONS method)
					29.165	  CR-188  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110134)

Decision: 		The document was revised to C3-110357.

C3-110357	Summary of notation codes in dynamic view (OPTIONS method)
					29.165	  CR-188  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110327)

Decision: 		The document was revised to C3-110388.

C3-110388	Summary of notation codes in dynamic view (OPTIONS method)
					29.165	  CR-188  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110357)

Decision: 		The document was agreed.

C3-110135	Summary of notation codes in dynamic view (PRACK method)
					29.165	  CR-189  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within PRACK request and response in dynamic view is added.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. Dr.Thomas had a opinion regarding 'WWW-Authenticate'.  It was revised to 328.

Decision: 		The document was revised to C3-110328.

C3-110328	Summary of notation codes in dynamic view (PRACK method)
					29.165	  CR-189  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110135)

Decision: 		The document was revised to C3-110358.

C3-110358	Summary of notation codes in dynamic view (PRACK method)
					29.165	  CR-189  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110328)

Decision: 		The document was revised to C3-110389.

C3-110389	Summary of notation codes in dynamic view (PRACK method)
					29.165	  CR-189  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110358)

Decision: 		The document was agreed.

C3-110136	Summary of notation codes in dynamic view (PUBLISH method)
					29.165	  CR-190  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within PUBLISH request and response in dynamic view is added.

Discussion:

Mr.Kenjiro (from NTT) represented this CR. There was the same discusssion and it was revised to 329.

Decision: 		The document was revised to C3-110329.

C3-110329	Summary of notation codes in dynamic view (PUBLISH method)
					29.165	  CR-190  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110136)

Decision: 		The document was revised to C3-110360.

C3-110360	Summary of notation codes in dynamic view (PUBLISH method)
					29.165	  CR-190  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110329)

Decision: 		The document was revised to C3-110390.

C3-110390	Summary of notation codes in dynamic view (PUBLISH method)
					29.165	  CR-190  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110360)

Decision: 		The document was agreed.

C3-110137	Summary of notation codes in dynamic view (REGISTER method)
					29.165	  CR-191  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within REGISTER request and response in dynamic view is added.

Discussion:

NTT represented this CR. Dr.Thomas had a comment regarding table x.13.1. Mr.Naoki, Mr.Roland and Ms.Beata  joined the discussion about this. It was revised to 331

Decision: 		The document was revised to C3-110331.

C3-110331	Summary of notation codes in dynamic view (REGISTER method)
					29.165	  CR-191  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110137)

Decision: 		The document was agreed.

C3-110138	Summary of notation codes in dynamic view (UPDATE method)
					29.165	  CR-192  (Rel-10) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

Abstract:

Summary of notation codes within UPDATE request and response in dynamic view is added.

Discussion:

NTT represented this CR. It was revised to 332.

Decision: 		The document was revised to C3-110332.

C3-110332	Summary of notation codes in dynamic view (UPDATE method)
					29.165	  CR-192  rev 1 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110138)

Decision: 		The document was revised to C3-110359.

C3-110359	Summary of notation codes in dynamic view (UPDATE method)
					29.165	  CR-192  rev 2 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110332)

Decision: 		The document was revised to C3-110391.

C3-110391	Summary of notation codes in dynamic view (UPDATE method)
					29.165	  CR-192  rev 3 (-) v10.2.0
					Source: NTT, NTT DOCOMO, AT&T

(Replaces C3-110359)

Decision: 		The document was agreed.

### 10.15	Technical Enhancements and Improvements [TEI10]

C3-110037	Add missing E-CSCF to interworking network diagram
					29.162	  CR-071  (Rel-10) v10.0.0
					Source: Alcatel-Lucent

Abstract:

The interworking network figure is modified to include the E-CSCF.

The border control figure is modified to include the E-CSCF.

Mm is added to border control figure to align with reference below figure.

Mb interface labels added to border control figure .

Discussion:

Mr.Jim (from Alcatel-Lucent) represented this CR. There are missing tdoc and CR number in cover page. Dr.Thomas and Mr.Jan joined the discussion about figure 1 and 2. It was revised to 247.

Decision: 		The document was revised.

C3-110247	Add missing E-CSCF to interworking network diagram
					29.162	  CR-071  rev 1 (-) v10.0.0
					Source: Alcatel-Lucent

(Replaces C3-110037)

Discussion:

It was moved from II-NNI2.

Decision: 		The document was revised to C3-110290.

C3-110290	Add missing E-CSCF to interworking network diagram
					29.162	  CR-071  rev 2 (-) v10.0.0
					Source: Alcatel-Lucent

(Replaces C3-110247)

Discussion:

WI was changed to "IMS-CCR-IWIP".

Decision: 		The document was revised to C3-110392.

C3-110392	Add missing E-CSCF to interworking network diagram
					29.162	  CR-071  rev 3 (-) v10.0.0
					Source: Alcatel-Lucent

(Replaces C3-110290)

Decision: 		The document was agreed.

C3-110104	Gx request handling (R10 29.212)
					29.212	  CR-563  (Rel-10) v10.1.0
					Source: Huawei

Discussion:

Before the meeting, it was revised to 183. WI : SAES-St3-PCC

Decision: 		The document was revised to C3-110183.

C3-110167	Correction to the AVPs to support xDSL line identification on the Gx
					29.212	  CR-573  (Rel-10) v10.1.0
					Source: ZTE

Abstract:

1.	In the Table 5.4, the applicability of Logical-Access-ID and Physical-Access-ID is marked as Rel-10.

2.	Logical-Access-ID and Physical-Access-ID AVP is  added into CCR command of Gx and remove from CCR command of the Gxx.

Discussion:

Mr.Zhou (from ZTE) represented this CR. There is some miss-typing in 3rd change.Miss Susana, Mr.Norbert had a comment and it seems to need the offline discussion. It was revised to 310.

Decision: 		The document was revised to C3-110310.

C3-110310	Correction to the AVPs to support xDSL line identification on the Gx
					29.212	  CR-573  rev 1 (-) v10.1.0
					Source: ZTE

(Replaces C3-110167)

Decision: 		The document was agreed.

C3-110168	Usage of the AVPs to support xDSL line identification on the S9 interface
					29.215	  CR-136  (Rel-10) v10.0.0
					Source: ZTE

Abstract:

Logical-Access-ID and Physical-Access-ID AVPs are not applicable for the S9 reference point.

Discussion:

Mr.Zhou (from ZTE) represented this CR. Mr.Simon and Miss Susana had a comment regarding AVP. It was revised to 311.

Decision: 		The document was revised to C3-110311.

C3-110311	Usage of the AVPs to support xDSL line identification on the S9 interface
					29.215	  CR-136  rev 1 (-) v10.0.0
					Source: ZTE

(Replaces C3-110168)

Decision: 		The document was revised to C3-110304.

C3-110304	Usage of the AVPs to support xDSL line identification on the S9 interface
					29.215	  CR-136  rev 2 (-) v10.0.0
					Source: ZTE

(Replaces C3-110311)

Decision: 		The document was agreed.

C3-110178	Overlapping AVP code values
					29.212	  CR-580  (Rel-10) v10.1.0
					Source: Nokia Siemens Networks

Discussion:

WI:  IFOM-CT, It was revised to 181 before the meeting

Decision: 		The document was revised to CP-110181.

C3-110181	Overlapping AVP code values
					29.212	  CR-580r1  rev 1 (Rel-10) v10.1.0
					Source: Nokia Siemens Networks

Abstract:

A new code value is allocated to the Routing-Rule-Install AVP.

Discussion:

Dr.Thomas represented this CR. It was revised to 196.

Decision: 		The document was revised to C3-110196.

C3-110196	Overlapping AVP code values
					29.212	  CR-580r1  rev 2 (-) v10.1.0
					Source: Nokia Siemens Networks

(Replaces C3-110181)

Decision: 		The document was agreed.

C3-110183	Gx request handling (R10 29.212)
					29.212	  CR-563r1  rev 1 (Rel-10) v10.1.0
					Source: Huawei

Abstract:

Adding the description that the PCRF shall send an RA-Request command to the PCEF/BBERF, only after the previous RA-Request has been acknowledged for the same IP-CAN/gateway control session.

Discussion:

Mr.Weihua (from Huawei) represented this CR. Miss Susana had a comment regarding PCRF and Mr.Fernando, Mr.Zhou joined the discussion about numbering. It seems to need the offline discussion and revised to 312.

Decision: 		The document was revised to C3-110312.

C3-110312	Gx request handling (R10 29.212)
					29.212	  CR-563r1  rev 2 (-) v10.1.0
					Source: Huawei

(Replaces C3-110183)

Decision: 		The document was agreed.

### 10.16	Other Work Items for Rel-10

C3-110105	Request Type in Rx AAR
					29.214	  CR-163  (Rel-10) v10.1.0
					Source: Tekelec

Abstract:

The AAR message in Rx is updated with a new optional AVP called Rx-Request-Type.

Discussion:

Tekelec represented this CR. Miss Susana, Mr.Fernando,and Mr.Zhou discussed about this CR, but it seems to need the offline discussion. It was postponedd tilll the next meeting.Possibly a discussion paper will be provided to the next meeting so that companies can analyse the impact/need for this AVP.

Decision: 		The document was postponed till the next meeting.

C3-110121	Adding CS-Ix functionalities to Mc-profile
					29.235	  CR-083  (Rel-10) v9.6.0
					Source: Nokia Siemens Networks

Abstract:

Adding of border control functions to the Mc profile

Discussion:

Nokia Siemans Networks represented this CR. Ms.Nevenka had an opinion regarding the release, and the delegates found some miss-typing in the document. It was revised to 240.

Decision: 		The document was revised to C3-110240.

C3-110240	Adding CS-Ix functionalities to Mc-profile
					29.235	  CR-083  rev 1 (-) v9.6.0
					Source: Nokia Siemens Networks

(Replaces C3-110121)

Decision: 		The document was revised to C3-110288.

C3-110288	Adding CS-Ix functionalities to Mc-profile
					29.235	  CR-083  rev 2 (-) v9.6.0
					Source: Nokia Siemens Networks

(Replaces C3-110240)

Decision: 		The document was withdrawn.

C3-110169	CS and IMS Interworking for Early Session Disposition SDP
					Source: ZTE

Abstract:

In stage 1 specification for CAT service, it has the requirement that the CAT service can be interworked between CS network and IMS network.

As specified in stage 3 specification 3GPP TS 24.182, it defined three models to implement the CAT service, the gateway model, forking model and early session model. And 3GPP TS 29.163 defines the mechanism for interworking between IMS network and CS network, but it only consider the case when CAT provided using P-Early-Media header field, which cover the gateway model and forking model. Since early session method is one option to deploy CAT service and other services, e.g. CRS, the interworking for early session between CS network and IMS network need to be specified.

Based on the stage 1 requirements, the relevant stage 3 specification work is needed

Discussion:

Mr.Li shitao (from ZTE) represented this item. Dr.Thomas had a opinion regarding it.  Ms.Nevenka and Mr.Jim joined this dicussion. This item seems to need more discussion. Additional implications were brought up, possibly rel-11 a more realistic timeframe if we go forward with the WID. It was revised to 189.

Decision: 		The document was revised to C3-110189.

C3-110189	CS and IMS Interworking for Early Session Disposition SDP
					Source: ZTE

(Replaces C3-110169)

Discussion:

Mr.Li shitao (from ZTE) represented this item. Dr.Thomas, Mr.Itsuma, Ms.Nevenka and Mr.Weihua  discussed about  the interworking for CAT service between CS network and IMS network. It was revised to 285.

Decision: 		The document was revised to C3-110285.

C3-110285	CS and IMS Interworking for Early Session Disposition SDP
					Source: ZTE

(Replaces C3-110189)

Decision: 		The document was revised to C3-110371.

C3-110371	CS and IMS Interworking for Early Session Disposition SDP
					Source: ZTE

(Replaces C3-110285)

Discussion:

NTT used this tdoc number by mistake.

Decision: 		The document was revised to C3-110382.

C3-110382	CS and IMS Interworking for Early Session Disposition SDP
					Source: ZTE

(Replaces C3-110371)

Discussion:

In the objectives the two additional paragraphs marked in blue needs further work, e.g discussion paper(s) at the Salt Lake City meeting.

It was agreed to include any CAT interworking related issues found necessary at the next meeting into a revision of the WID.

Decision: 		The document was revised.

C3-110384	CS and IMS Interworking for Early Session Disposition SDP
					Source: ZTE

(Replaces C3-110382)

Discussion:

Technically agreed, but has rev. marks.

Decision: 		The document was revised to C3-110398.

C3-110398	CS and IMS Interworking for Early Session Disposition SDP
					Source: ZTE

(Replaces C3-110384)

Discussion:

It was Clean version.

Decision: 		The document was agreed.

C3-110170	Adding function for supporting early session
					29.163	  CR-472  (Rel-10) v10.0.0
					Source: ZTE

Discussion:

Its Comments collected. Revision expected in Salt Lake City.Do we want to cover MONA?

Decision: 		The document was postponed till the next meeting.

#### 10.16.1	Void

#### 10.16.2	CS and IMS Interworking for CAT service [CIIC]

#### 10.16.3	PCC Enhancements [PCC-Enh]

#### 10.16.4	PCC aspects of SAE [SAES-St3-PCC]

#### 10.16.5	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

## 11	Release 11

### 11.1	Technical Enhancements and Improvements [TEI11]

### 11.2	Other Rel-11 Work Items

## 12	Work Organisation

### 12.1	Work Plan Review

C3-110009	Latest Version of 3GPP Workplan
					Source: MCC

Decision: 		The document was noted.

C3-110046	Status of CT3 Work Items
					Source: CT3 Chairman

Decision: 		The document was revised to C3-110400.

C3-110400	Status of CT3 Work Items
					Source: CT3 Chairman

(Replaces C3-110046)

Decision: 		The document was agreed.

12.2	Specification Review

C3-110010	Status of CT3 specifications following CT#50 meeting
					Source: MCC

Decision: 		The document was noted.

12.3	Next meetings, allocation of hosts

C3-110011	Meeting Calendar for 2011
					Source: MCC

Decision: 		The document was noted.

C3-110047	CT3 Meetings for Rel-11
					Source: CT3 Chairman

Decision: 		The document was noted.

C3-110182	CT WG Meetings proposal 2012
					Source: CT Chairs

Decision: 		The document was noted.

## 13	Summary of results

## 14	Any other business

## 15	Closing of the meeting

### 15.1        TR/TS

### 15.2         Work Item

| Document | Title | Source | new/revised |
| --- | --- | --- | --- |
| C3-110022 | Revised WID on Optimal Media Routeing | Alcatel-Lucent | WID |
| C3-110398 | CS and IMS Interworking for Early Session Disposition SDP | ZTE | WID |

### 15.3         Liaison Statements

#### 15.3.1      Incoming liaison statements

| Document | Title | From | Decision | Reply in |
| --- | --- | --- | --- | --- |
| C3-110012 | Reply LS to 3GPP TSG CT4 on support of ECN | Q3/16 | noted |  |
| C3-110013 | Reply LS to R2-105299 on Handling of UTRAN Mobility Information | RAN WG2 | noted |  |
| C3-110014 | LS response on Passing Restart Counter to External Network | 3GPP TSG SA2 | noted |  |
| C3-110015 | LS on NIMTC impacts on PMIP | SA2 | noted |  |
| C3-110016 | LS on User CSG Information reporting | SA2 | noted |  |

#### 15.3.2     Outgoing liaison statements

| Document | Title | To | Cc | reply to i/c LS |
| --- | --- | --- | --- | --- |
| C3-110201 | LS on QoS-Negotiation and QoS-Upgrade on the Gx for GnGp SGSN | SA2 | CT4 | - |
| C3-110366 | LS out Sponsored data connectivity in the roaming case | SA2 | - | - |
| C3-110367 | LS out Bearer control mode and multiple PDN connectivity | SA2 | - | - |

### Agreed Change Requests

| Document | Title | Source | Spec | CR | Rev | Cat | WI | Release | Decision |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C3-110017 | Bearer priority handling for EMPS. | Ericsson | 29.212 | 551 | - | F | eMPS-CN | Rel-10 | agreed |
| C3-110018 | Bearer priority handling for EMPS. | Ericsson | 29.213 | 297 | - | F | eMPS-CN | Rel-10 | agreed |
| C3-110038 | Correction on Major Capabilities over II-NNI | OKI | 29.165 | 155 | - | F | II-NNI | Rel-9 | agreed |
| C3-110039 | Correction on Major Capabilities over II-NNI | OKI | 29.165 | 156 | - | A | II-NNI | Rel-10 | agreed |
| C3-110051 | Minor corrections | Ericsson | 29.311 | 022 | - | F | CPM-SMS | Rel-10 | agreed |
| C3-110052 | Remove unexplained NOTEs | Ericsson | 29.311 | 023 | - | F | CPM-SMS | Rel-10 | agreed |
| C3-110053 | Reference clause updates | Ericsson | 29.165 | 163 | - | F | II-NNI | Rel-9 | agreed |
| C3-110055 | Introduction of ATCF | Ericsson | 29.165 | 165 | - | B | II-NNI2 | Rel-10 | agreed |
| C3-110064 | Reference update: RFC 6086 | Ericsson | 29.165 | 174 | - | A | II-NNI | Rel-10 | agreed |
| C3-110066 | Adding MMTel feature tag in clause 12 | Ericsson | 29.165 | 176 | - | F | FBI2-IOPSI | Rel-8 | agreed |
| C3-110067 | Adding MMTel feature tag in clause 12 | Ericsson | 29.165 | 177 | - | A | FBI2-IOPSI | Rel-9 | agreed |
| C3-110068 | Adding MMTel feature tag in clause 12 | Ericsson | 29.165 | 178 | - | A | FBI2-IOPSI | Rel-10 | agreed |
| C3-110069 | Minor corrections to 3GPP TS 29.165 | Ericsson | 29.165 | 179 | - | F | II-NNI2 | Rel-10 | agreed |
| C3-110070 | Alignment with 23.228 Ici reference point | Ericsson | 29.165 | 180 | - | F | II-NNI2 | Rel-10 | agreed |
| C3-110080 | IETF Reference Update: RFC 5993 | Ericsson | 29.163 | 451 | - | F | AoIP-CN | Rel-8 | agreed |
| C3-110081 | IETF Reference Update: RFC 5993 | Ericsson | 29.163 | 452 | - | A | AoIP-CN | Rel-9 | agreed |
| C3-110082 | IETF Reference Update: RFC 5993 | Ericsson | 29.163 | 453 | - | A | AoIP-CN | Rel-10 | agreed |
| C3-110100 | Reporting for sponsored connectivity (R10 29.212) | Huawei | 29.212 | 561 | - | B | PEST-CT3 | Rel-10 | agreed |
| C3-110148 | Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case | ZTE | 29.215 | 129 | - | F | SAES-St3-PCC | Rel-8 | agreed |
| C3-110149 | Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case | ZTE | 29.215 | 130 | - | A | SAES-St3-PCC | Rel-9 | agreed |
| C3-110150 | Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case | ZTE | 29.215 | 131 | - | A | SAES-St3-PCC | Rel-10 | agreed |
| C3-110155 | Update of the gateway control session establishment procedure for eMPS | ZTE, Ericsson | 29.213 | 303 | - | B | eMPS-CN | Rel-10 | agreed |
| C3-110162 | Clarify the usage reporting during the IP-CAN session modification(29.213) | ZTE | 29.213 | 304 | - | B | PEST-CT3 | Rel-10 | agreed |
| C3-110190 | Event triggers for multiple BBERFs in IP flow mobility case (R10 29.212) | Huawei | 29.212 | 560 | 1 | F | IFOM-CT | - | agreed |
| C3-110195 | Usage of the IFOM related AVPs in Subsession-Enforcement-Info | ZTE | 29.215 | 132 | 1 | B | IFOM-CT | - | agreed |
| C3-110196 | Overlapping AVP code values | Nokia Siemens Networks | 29.212 | 580r1 | 2 | F | IFOM-CT | - | agreed |
| C3-110198 | Applicability of the access network information related AVPs in Subsession-Enforcement-Info | ZTE | 29.215 | 133 | 1 | B | MAPCON-St3 | - | agreed |
| C3-110200 | Resolve the conflict of the access network information at the command level and the subsession level for the MAPCON scenario | ZTE | 29.215 | 135 | 1 | B | MAPCON-St3 | - | agreed |
| C3-110202 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | 29.212 | 566 | 1 | F | SAES-St3-PCC | - | agreed |
| C3-110203 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | 29.212 | 567 | 1 | A | SAES-St3-PCC | - | agreed |
| C3-110204 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | 29.212 | 568 | 1 | A | SAES-St3-PCC | - | agreed |
| C3-110205 | Reference to 3GPP2 updated | Nokia Siemens Networks | 29.212 | 577 | 1 | F | SAES-St3-PCC | - | agreed |
| C3-110206 | Reference to 3GPP2 updated | Nokia Siemens Networks | 29.212 | 578 | 1 | A | SAES-St3-PCC | - | agreed |
| C3-110207 | Reference to 3GPP2 updated | Nokia Siemens Networks | 29.212 | 579 | 1 | A | SAES-St3-PCC | - | agreed |
| C3-110209 | Completion of CSG information reporting | Ericsson | 29.212 | 553 | 1 | A | PCC-Enh | - | agreed |
| C3-110210 | Correction of the Event-Trigger AVP enumeration | Ericsson | 29.212 | 554 | 1 | F | PCC-Enh | - | agreed |
| C3-110211 | Correction of the Event-Trigger AVP enumeration | Ericsson | 29.212 | 555 | 1 | A | PCC-Enh | - | agreed |
| C3-110212 | Bearer binding function in PCEF | Ericsson, Huawei | 29.212 | 556 | 1 | F | PCC-Enh | - | agreed |
| C3-110213 | Bearer binding function in PCEF | Ericsson, Huawei | 29.212 | 557 | 1 | A | PCC-Enh | - | agreed |
| C3-110219 | Fixing Supported-Feature feature bit definitions | ZTE | 29.214 | 164 | 1 | F | PCC-Enh | - | agreed |
| C3-110220 | Fixing Supported-Feature feature bit definitions | ZTE | 29.214 | 165 | 1 | A | PCC-Enh | - | agreed |
| C3-110225 | S2b RAT Type | alcatel-lucent | 29.212 | 565 | 1 | B | SMOG-ST3 | - | agreed |
| C3-110228 | Reporting for sponsored connectivity (R10 29.212) | Huawei, Orange | 29.212 | 561r1 | 2 | B | PEST-CT3 | - | agreed |
| C3-110230 | Usage for sponsored connectivity (R10 29.214) | Huawei, Orange | 29.214 | 162r1 | 2 | F | PEST-CT3 | - | agreed |
| C3-110244 | Correcting header table in annex A | Ericsson | 29.165 | 170 | 1 | F | FBI2-IOPSI | - | agreed |
| C3-110245 | Correcting header table in annex A | Ericsson | 29.165 | 171 | 1 | A | FBI2-IOPSI | - | agreed |
| C3-110246 | Correcting header table in annex A | Ericsson | 29.165 | 172 | 1 | A | FBI2-IOPSI | - | agreed |
| C3-110248 | RFC 5318 in the Major capability table | Ericsson | 29.165 | 161 | 1 | B | II-NNI2 | - | agreed |
| C3-110254 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | 29.163 | 447 | 1 | F | IMS-CCR-IWCS | - | agreed |
| C3-110255 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | 29.163 | 448 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110256 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | 29.163 | 449 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110257 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | 29.163 | 450 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110258 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 457 | 1 | F | IMS-CCR-IWCS | - | agreed |
| C3-110259 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 458 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110260 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 459 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110261 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 460 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110262 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 461 | 1 | F | IMS-CCR-IWCS | - | agreed |
| C3-110263 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 462 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110264 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 463 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110265 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 464 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110266 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 468 | 1 | F | IMS-CCR-IWCS | - | agreed |
| C3-110267 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 469 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110268 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 470 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110269 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | 29.163 | 471 | 1 | A | IMS-CCR-IWCS | - | agreed |
| C3-110273 | Addition of the Target-Dialog header field to the table of major capabilities and Annex A | Fujitsu Limited | 29.165 | 157 | 1 | F | II-NNI | - | agreed |
| C3-110274 | Addition of the Target-Dialog header field to the table of major capabilities and Annex A | Fujitsu Limited | 29.165 | 158 | 1 | A | II-NNI | - | agreed |
| C3-110277 | Reference clause updates | Ericsson | 29.165 | 164 | 1 | A | II-NNI | - | agreed |
| C3-110280 | Reference update: RFC 6086 | Ericsson | 29.165 | 173 | 1 | F | II-NNI | - | agreed |
| C3-110281 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | 29.165 | 193 | 1 | F | II-NNI | - | agreed |
| C3-110286 | Interoperability of IMS Service Continuity over II-NNI updates | Ericsson | 29.165 | 166 | 2 | B | II-NNI2 | - | agreed |
| C3-110289 | Adding CS-Ix functionalities to Mc-profile | Nokia Siemens Networks | 29.235 | 84 | - | - | CS-IBCF | Rel-9 | agreed |
| C3-110291 | Correction to feature bit for sponsored data connectivity (29.212) | ZTE | 29.212 | 571 | 1 | B | PEST-CT3 | - | agreed |
| C3-110296 | IFOM message flow | Qualcomm Incorporated | 29.213 | 307 | 2 | B | IFOM-CT | - | agreed |
| C3-110298 | Completion of CSG information reporting | Ericsson | 29.212 | 552 | 2 | F | PCC-Enh | - | agreed |
| C3-110299 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | 29.213 | 300 | 3 | F | PCC-Enh | - | agreed |
| C3-110300 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | 29.213 | 301 | 3 | A | PCC-Enh | - | agreed |
| C3-110302 | Identification of BBF against IP flow mobility routing rule | Qualcomm Incorporated | 29.212 | 574 | 3 | B | IFOM-CT | - | agreed |
| C3-110304 | Usage of the AVPs to support xDSL line identification on the S9 interface | ZTE | 29.215 | 136 | 2 | B | TEI10 | - | agreed |
| C3-110307 | Correction to feature bit for sponsored data connectivity (29.214) | ZTE | 29.214 | 167 | 1 | B | PEST-CT3 | - | agreed |
| C3-110308 | Correction to the Reporting Usage for Sponsored Data Connectivity(29.214) | ZTE | 29.214 | 168 | 1 | B | PEST-CT3 | - | agreed |
| C3-110310 | Correction to the AVPs to support xDSL line identification on the Gx | ZTE | 29.212 | 573 | 1 | B | TEI10 | - | agreed |
| C3-110312 | Gx request handling (R10 29.212) | Huawei | 29.212 | 563r1 | 2 | F | SAES-St3-PCC | - | agreed |
| C3-110317 | Reference points Mi, Mm, Mw and I2 | Ericsson | 29.165 | 175 | 1 | F | II-NNI2 | - | agreed |
| C3-110318 | Miscellaneous error corrections to 3GPP TS 29.165 | Ericsson | 29.165 | 181 | 1 | - | II-NNI2 | - | agreed |
| C3-110321 | Summary of notation codes in dynamic view (ACK method) | NTT, NTT DOCOMO, AT&T | 29.165 | 183 | 1 | B | NNI_DV | - | agreed |
| C3-110324 | Summary of notation codes in dynamic view (CANCEL method) | NTT, NTT DOCOMO, AT&T | 29.165 | 185 | 1 | B | NNI_DV | - | agreed |
| C3-110331 | Summary of notation codes in dynamic view (REGISTER method) | NTT, NTT DOCOMO, AT&T | 29.165 | 191 | 1 | B | NNI_DV | - | agreed |
| C3-110333 | CR 581 29.212 Rel-8 Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R8 29.212) | Huawei | 29.212 | 581 | 1 | - | SAES-St3-PCC | - | agreed |
| C3-110334 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212) | Huawei | 29.212 | 558 | 2 | F | PCC-Enh | - | agreed |
| C3-110335 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212) | Huawei | 29.212 | 559 | 2 | A | PCC-Enh | - | agreed |
| C3-110338 | S2b GTP addition to Annex D.1 | alcatel-lucent | 29.212 | 564 | 2 | B | SMOG-ST3 | - | agreed |
| C3-110339 | Correction to the descriptions of multiple BBERF scenario | ZTE | 29.215 | 138 | - | F | SAES-St3-PCC | Rel-8 | agreed |
| C3-110340 | Correction to the descriptions of multiple BBERF scenario | ZTE | 29.215 | 139 | - | F | SAES-St3-PCC | Rel-9 | agreed |
| C3-110341 | Correction to the descriptions of multiple BBERF scenario | ZTE | 29.215 | 134 | 2 | A | SAES-St3-PCC | Rel-10 | agreed |
| C3-110343 | Correction to Sponsor-Identity AVP and Application-Service-Provider-Identity AVP(29.212) | ZTE | 29.212 | 572 | 2 | B | PEST-CT3 | - | agreed |
| C3-110344 | Offline charging for sponsored data connectivity(29.213) | ZTE | 29.213 | 305 | 2 | B | PEST-CT3 | - | agreed |
| C3-110345 | Missing Timer definition for TIR | Deutsche Telekom | 29.163 | 465 | 2 | F | IMS-CCR-IWCS | - | agreed |
| C3-110346 | Missing Timer definition for TIR | Deutsche Telekom | 29.163 | 466 | 2 | A | IMS-CCR-IWCS | - | agreed |
| C3-110347 | Missing Timer definition for TIR | Deutsche Telekom | 29.163 | 467 | 2 | A | IMS-CCR-IWCS | - | agreed |
| C3-110348 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | 29.163 | 454 | 2 | F | CCBS_CCNR | - | agreed |
| C3-110349 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | 29.163 | 455 | 2 | A | CCBS_CCNR | - | agreed |
| C3-110350 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | 29.163 | 456 | 2 | A | CCBS_CCNR | - | agreed |
| C3-110351 | Correcting major capabilities related to trust domain | NEC, NTT | 29.165 | 159 | 2 | F | II-NNI | - | agreed |
| C3-110352 | Correcting major capabilities related to trust domain | NEC, NTT | 29.165 | 160 | 2 | A | II-NNI | - | agreed |
| C3-110353 | RAT based charging for IFOM | ZTE | 29.212 | 569 | 2 | B | IFOM-CT | - | agreed |
| C3-110354 | Updates of the Major capability table | Ericsson | 29.165 | 167 | 2 | F | II-NNI | - | agreed |
| C3-110355 | Updates of the Major capability table | Ericsson | 29.165 | 168 | 2 | A | II-NNI | - | agreed |
| C3-110365 | Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212) | Huawei, Orange | 29.212 | 562r1 | 4 | F | PEST-CT3 | - | agreed |
| C3-110378 | Updating OMA presence requirements | Ericsson | 29.165 | 162 | 2 | B | II-NNI2 | - | agreed |
| C3-110379 | Adding new header fields Annex A | Ericsson | 29.165 | 169 | 3 | F | II-NNI2 | - | agreed |
| C3-110380 | Addition of normative references for in band DTMF and SDP messages | Orange | 29.165 | 197 | 2 | F | II-NNI2 | - | agreed |
| C3-110381 | Authorization of the sponsored data connectivity(29.214) | Ericsson, ZTE | 29.214 | 159 | 3 | F | PEST-CT3 | - | agreed |
| C3-110383 | New annex for dynamic view of SIP messages | NTT, NTT DOCOMO, AT&T | 29.165 | 182 | 2 | B | NNI_DV | - | agreed |
| C3-110385 | Summary of notation codes in dynamic view (BYE method) | NTT, NTT DOCOMO, AT&T | 29.165 | 184 | 3 | B | NNI_DV | - | agreed |
| C3-110386 | Summary of notation codes in dynamic view (INVITE method) | NTT, NTT DOCOMO, AT&T | 29.165 | 186 | 3 | B | NNI_DV | - | agreed |
| C3-110387 | Summary of notation codes in dynamic view (MESSAGE method) | NTT, NTT DOCOMO, AT&T | 29.165 | 187 | 3 | B | NNI_DV | - | agreed |
| C3-110388 | Summary of notation codes in dynamic view (OPTIONS method) | NTT, NTT DOCOMO, AT&T | 29.165 | 188 | 3 | B | NNI_DV | - | agreed |
| C3-110389 | Summary of notation codes in dynamic view (PRACK method) | NTT, NTT DOCOMO, AT&T | 29.165 | 189 | 3 | B | NNI_DV | - | agreed |
| C3-110390 | Summary of notation codes in dynamic view (PUBLISH method) | NTT, NTT DOCOMO, AT&T | 29.165 | 190 | 3 | B | NNI_DV | - | agreed |
| C3-110391 | Summary of notation codes in dynamic view (UPDATE method) | NTT, NTT DOCOMO, AT&T | 29.165 | 192 | 3 | B | NNI_DV | - | agreed |
| C3-110392 | Add missing E-CSCF to interworking network diagram | Alcatel-Lucent | 29.162 | 071 | 3 | F | TEI10 | - | agreed |
| C3-110393 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | 29.163 | 443 | 2 | F | IMS-CCR-IWCS | - | agreed |
| C3-110394 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | 29.163 | 444 | 2 | A | IMS-CCR-IWCS | - | agreed |
| C3-110395 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | 29.163 | 445 | 2 | A | IMS-CCR-IWCS | - | agreed |
| C3-110396 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | 29.163 | 446 | 2 | A | IMS-CCR-IWCS | - | agreed |
| C3-110399 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | 29.165 | 194 | 4 | A | II-NNI | - | agreed |
| C3-110361 | Bearer control mode for multiple PDN connections | Qualcomm Incorporated | 29.212 | 575 | 2 | F | PCC-Enh | - | conditionally agreed |
| C3-110362 | Bearer control mode for multiple PDN connections | Qualcomm Incorporated | 29.212 | 576 | 2 | A | PCC-Enh | - | Conditionally agreed |
| C3-110028 | Encapsulation of session level information during OMR procedures | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110030 | Deletion of OMR editor's note regarding 24.229 profile table | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110031 | Remove OMR trust domain editor's note | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110032 | Remove editor's note for "codec" and "codec list" definitions | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110033 | Remove editor's note for placement of realm definition in TS 24.229 | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110034 | Deletion of OMR Annex A of 29.079 | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110233 | Restructuring and completion of OMR SDP offer procedures | Alcatel-Lucent, Nokia Siemens Networks, Ericsson | 29.079 | - | - | - | OMR | - | agreed |
| C3-110234 | Restructuring and completion of OMR SDP answer procedures | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110235 | Restructuring and completion of OMR UA procedures | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110238 | Annex X with simple message flows introduced | Ericsson | - | - | - | - | OMR | - | agreed |
| C3-110374 | OMR check sum procedures | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110375 | Handling of SDP o-line during OMR | Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |
| C3-110376 | Updated OMR CapNeg procedures | Nokia Siemens Networks, Alcatel-Lucent | 29.079 | - | - | - | OMR | - | agreed |

## Annex A : List of contribution documents

| Document | Title | Source | Decision | Replaces | Replaced by |
| --- | --- | --- | --- | --- | --- |
| C3-110001 | Draft Agenda for CT3#61 | CT3 Chairman | agreed | - | - |
| C3-110002 | Allocation of documents to agenda items (start of Day1) | CT3 Chairman | noted | - | - |
| C3-110003 | Allocation of documents to agenda items (start of Day2) | CT3 Chairman | noted | - | - |
| C3-110004 | Allocation of documents to agenda items (start of Day3) | CT3 Chairman | noted | - | - |
| C3-110005 | Allocation of documents to agenda items (start of Day4) | CT3 Chairman | noted | - | - |
| C3-110006 | Allocation of documents to agenda items (start of Day5) | CT3 Chairman | noted | - | - |
| C3-110007 | Allocation of documents to agenda items (end of Day5) | CT3 Chairman | noted | - | - |
| C3-110008 | Draft Report from CT3#60 | MCC | approved | - | - |
| C3-110009 | Latest Version of 3GPP Workplan | MCC | noted | - | - |
| C3-110010 | Status of CT3 specifications following CT#50 meeting | MCC | noted | - | - |
| C3-110011 | Meeting Calendar for 2011 | MCC | noted | - | - |
| C3-110012 | Reply LS to 3GPP TSG CT4 on support of ECN | Q3/16 | noted | - | - |
| C3-110013 | Reply LS to R2-105299 on Handling of UTRAN Mobility Information | RAN WG2 | noted | - | - |
| C3-110014 | LS response on Passing Restart Counter to External Network | 3GPP TSG SA2 | noted | - | - |
| C3-110015 | LS on NIMTC impacts on PMIP | SA2 | noted | - | - |
| C3-110016 | LS on User CSG Information reporting | SA2 | noted | - | - |
| C3-110017 | Bearer priority handling for EMPS. | Ericsson | agreed | - | - |
| C3-110018 | Bearer priority handling for EMPS. | Ericsson | agreed | - | - |
| C3-110019 | MPS Support over Rx | Ericsson | revised | - | C3-110197 |
| C3-110020 | Completion of CSG information reporting | Ericsson | revised | - | C3-110208 |
| C3-110021 | Completion of CSG information reporting | Ericsson | revised | - | C3-110209 |
| C3-110022 | Revised WID on Optimal Media Routeing | Alcatel-Lucent | agreed | - | - |
| C3-110023 | Restructuring and completion of OMR SDP offer procedures | Alcatel-Lucent, Nokia Siemens Networks, Ericsson | revised | - | C3-110233 |
| C3-110024 | Restructuring and completion of OMR SDP answer procedures | Alcatel-Lucent | revised | - | C3-110234 |
| C3-110025 | Restructuring and completion of OMR UA procedures | Alcatel-Lucent | revised | - | C3-110235 |
| C3-110026 | OMR check sum procedures | Alcatel-Lucent | revised | - | C3-110231 |
| C3-110027 | Updated OMR CapNeg procedures | Alcatel-Lucent | merged with C3-110122 into C3-110236 | - | C3-110236 |
| C3-110028 | Encapsulation of session level information during OMR procedures | Alcatel-Lucent | agreed | - | - |
| C3-110029 | Handling of SDP o-line during OMR | Alcatel-Lucent | revised | - | C3-110237 |
| C3-110030 | Deletion of OMR editor's note regarding 24.229 profile table | Alcatel-Lucent | agreed | - | - |
| C3-110031 | Remove OMR trust domain editor's note | Alcatel-Lucent | agreed | - | - |
| C3-110032 | Remove editor's note for "codec" and "codec list" definitions | Alcatel-Lucent | agreed | - | - |
| C3-110033 | Remove editor's note for placement of realm definition in TS 24.229 | Alcatel-Lucent | agreed | - | - |
| C3-110034 | Deletion of OMR Annex A of 29.079 | Alcatel-Lucent | agreed | - | - |
| C3-110035 | OMR SDP attribute syntax definition (for information) | Alcatel-Lucent | revised | - | C3-110232 |
| C3-110036 | Add missing E-CSCF to II-NNI network diagram | Alcatel-Lucent | withdrawn | - | - |
| C3-110037 | Add missing E-CSCF to interworking network diagram | Alcatel-Lucent | revised | - | - |
| C3-110038 | Correction on Major Capabilities over II-NNI | OKI | agreed | - | - |
| C3-110039 | Correction on Major Capabilities over II-NNI | OKI | agreed | - | - |
| C3-110040 | Addition of the Target-Dialog header field to the table of major capabilities and Annex A | Fujitsu Limited | revised | - | C3-110273 |
| C3-110041 | Addition of the Target-Dialog header field to the table of major capabilities and Annex A | Fujitsu Limited | revised | - | C3-110274 |
| C3-110042 | Correcting major capabilities related to trust domain | NEC, NTT | revised | - | C3-110275 |
| C3-110043 | Correcting major capabilities related to trust domain | NEC, NTT | revised | - | C3-110276 |
| C3-110044 | Proposed Schedule for CT3#61 | CT3 Chairman | revised | - | C3-110188 |
| C3-110045 | Brief Notes from CT#50 relevant to CT3 | CT3 Chairman | noted | - | - |
| C3-110046 | Status of CT3 Work Items | CT3 Chairman | revised | - | C3-110400 |
| C3-110047 | CT3 Meetings for Rel-11 | CT3 Chairman | noted | - | - |
| C3-110048 | Annex X with simple message flows introduced | Ericsson | revised | - | C3-110238 |
| C3-110049 | RFC 5318 in the Major capability table | Ericsson | revised | - | C3-110248 |
| C3-110050 | Updating OMA presence requirements | Ericsson | revised | - | C3-110249 |
| C3-110051 | Minor corrections | Ericsson | agreed | - | - |
| C3-110052 | Remove unexplained NOTEs | Ericsson | agreed | - | - |
| C3-110053 | Reference clause updates | Ericsson | agreed | - | - |
| C3-110054 | Reference clause updates | Ericsson | revised | - | C3-110277 |
| C3-110055 | Introduction of ATCF | Ericsson | agreed | - | - |
| C3-110056 | Interoperability of IMS Service Continuity over II-NNI updates | Ericsson | revised | - | C3-110315 |
| C3-110057 | Updates of the Major capability table | Ericsson | revised | - | C3-110278 |
| C3-110058 | Updates of the Major capability table | Ericsson | revised | - | C3-110279 |
| C3-110059 | Adding new header fields Annex A | Ericsson | revised | - | C3-110316 |
| C3-110060 | Correcting header table in annex A | Ericsson | revised | - | C3-110244 |
| C3-110061 | Correcting header table in annex A | Ericsson | revised | - | C3-110245 |
| C3-110062 | Correcting header table in annex A | Ericsson | revised | - | C3-110246 |
| C3-110063 | Reference update: RFC 6086 | Ericsson | revised | - | C3-110280 |
| C3-110064 | Reference update: RFC 6086 | Ericsson | agreed | - | - |
| C3-110065 | Reference points Mi, Mm, Mw and I2 | Ericsson | revised | - | C3-110317 |
| C3-110066 | Adding MMTel feature tag in clause 12 | Ericsson | agreed | - | - |
| C3-110067 | Adding MMTel feature tag in clause 12 | Ericsson | agreed | - | - |
| C3-110068 | Adding MMTel feature tag in clause 12 | Ericsson | agreed | - | - |
| C3-110069 | Minor corrections to 3GPP TS 29.165 | Ericsson | agreed | - | - |
| C3-110070 | Alignment with 23.228 Ici reference point | Ericsson | agreed | - | - |
| C3-110071 | Miscellaneous error corrections to 3GPP TS 29.165 | Ericsson | revised | - | C3-110318 |
| C3-110072 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | revised | - | C3-110250 |
| C3-110073 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | revised | - | C3-110251 |
| C3-110074 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | revised | - | C3-110252 |
| C3-110075 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | revised | - | C3-110253 |
| C3-110076 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | revised | - | C3-110254 |
| C3-110077 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | revised | - | C3-110255 |
| C3-110078 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | revised | - | C3-110256 |
| C3-110079 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | revised | - | C3-110257 |
| C3-110080 | IETF Reference Update: RFC 5993 | Ericsson | agreed | - | - |
| C3-110081 | IETF Reference Update: RFC 5993 | Ericsson | agreed | - | - |
| C3-110082 | IETF Reference Update: RFC 5993 | Ericsson | agreed | - | - |
| C3-110083 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | revised | - | C3-110241 |
| C3-110084 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | revised | - | C3-110242 |
| C3-110085 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | revised | - | C3-110243 |
| C3-110086 | Correction of the Event-Trigger AVP enumeration | Ericsson | revised | - | C3-110210 |
| C3-110087 | Correction of the Event-Trigger AVP enumeration | Ericsson | revised | - | C3-110211 |
| C3-110088 | SPR data usage optional for sponsored data connectivity | Ericsson | revised | - | C3-110226 |
| C3-110089 | The support for sponsored connectivity declared initially and maintained througout IP-CAN session | Ericsson | revised | - | C3-110227 |
| C3-110090 | Bearer binding function in PCEF | Ericsson, Huawei | revised | - | C3-110212 |
| C3-110091 | Bearer binding function in PCEF | Ericsson, Huawei | revised | - | C3-110213 |
| C3-110092 | Clarifying the use of MBR>GBR | Ericsson | revised | - | C3-110193 |
| C3-110093 | LS on QoS-Negotiation and QoS-Upgrade on the Gx for GnGp SGSN | Huawei | revised | - | C3-110201 |
| C3-110094 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212) | Huawei | revised | - | C3-110215 |
| C3-110095 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212) | Huawei | revised | - | C3-110216 |
| C3-110096 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | revised | - | C3-110217 |
| C3-110097 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | revised | - | C3-110218 |
| C3-110098 | Event triggers for multiple BBERFs in IP flow mobility case (R10 29.212) | Huawei | revised | - | C3-110190 |
| C3-110099 | Supporting MPS over Rx (R10 29.214) | Huawei | merged with C3-110019 into C3-110197 | - | C3-110197 |
| C3-110100 | Reporting for sponsored connectivity (R10 29.212) | Huawei | agreed | - | - |
| C3-110101 | ASP operators information for sponsored data connectivity (R10 29.214) | Huawei | revised | - | C3-110185 |
| C3-110102 | Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212) | Huawei | revised | - | C3-110186 |
| C3-110103 | Usage for sponsored connectivity (R10 29.214) | Huawei | revised | - | C3-110187 |
| C3-110104 | Gx request handling (R10 29.212) | Huawei | revised | - | C3-110183 |
| C3-110105 | Request Type in Rx AAR | Tekelec | postponed till the next meeting | - | - |
| C3-110106 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110258 |
| C3-110107 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110259 |
| C3-110108 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110260 |
| C3-110109 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110261 |
| C3-110110 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110262 |
| C3-110111 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110263 |
| C3-110112 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110264 |
| C3-110113 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110265 |
| C3-110114 | Missing Timer definition for TIR | Deutsche Telekom | revised | - | C3-110270 |
| C3-110115 | Missing Timer definition for TIR | Deutsche Telekom | revised | - | C3-110271 |
| C3-110116 | Missing Timer definition for TIR | Deutsche Telekom | revised | - | C3-110272 |
| C3-110117 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110266 |
| C3-110118 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110267 |
| C3-110119 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110268 |
| C3-110120 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | revised | - | C3-110269 |
| C3-110121 | Adding CS-Ix functionalities to Mc-profile | Nokia Siemens Networks | revised | - | C3-110240 |
| C3-110122 | Handling of capability negotiation | Nokia Siemens Networks | merged with C3-110027 into C3-110236 | - | C3-110236 |
| C3-110123 | Status of ECN discussions in SA4 and anticipated impacts to CT3 | Nokia Siemens Networks | revised | - | C3-110239 |
| C3-110124 | S2b GTP addition to Annex D.1 | alcatel-lucent | revised | - | C3-110224 |
| C3-110125 | S2b RAT Type | alcatel-lucent | revised | - | C3-110225 |
| C3-110126 | S2b HO | alcatel-lucent | withdrawn | - | - |
| C3-110127 | ISUP Cause/SIP Status Code Mapping and SIP Forking | AT&T | noted | - | - |
| C3-110128 | New annex for dynamic view of SIP messages | NTT, NTT DOCOMO, AT&T | revised | - | C3-110320 |
| C3-110129 | Summary of notation codes in dynamic view (ACK method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110321 |
| C3-110130 | Summary of notation codes in dynamic view (BYE method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110323 |
| C3-110131 | Summary of notation codes in dynamic view (CANCEL method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110324 |
| C3-110132 | Summary of notation codes in dynamic view (INVITE method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110325 |
| C3-110133 | Summary of notation codes in dynamic view (MESSAGE method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110326 |
| C3-110134 | Summary of notation codes in dynamic view (OPTIONS method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110327 |
| C3-110135 | Summary of notation codes in dynamic view (PRACK method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110328 |
| C3-110136 | Summary of notation codes in dynamic view (PUBLISH method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110329 |
| C3-110137 | Summary of notation codes in dynamic view (REGISTER method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110331 |
| C3-110138 | Summary of notation codes in dynamic view (UPDATE method) | NTT, NTT DOCOMO, AT&T | revised | - | C3-110332 |
| C3-110139 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | revised | - | C3-110281 |
| C3-110140 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | revised | - | C3-110282 |
| C3-110141 | The descriptions of values within the Privacy header field | NTT, NTT DOCOMO | revised | - | C3-110283 |
| C3-110142 | The descriptions of values within the Privacy header field | NTT, NTT DOCOMO | revised | - | C3-110284 |
| C3-110143 | IFOM message flow | Qualcomm Incorporated | revised | - | C3-110191 |
| C3-110144 | Identification of BBF against IP flow mobility routing rule | Qualcomm Incorporated | revised | - | C3-110192 |
| C3-110145 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | revised | - | C3-110202 |
| C3-110146 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | revised | - | C3-110203 |
| C3-110147 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | revised | - | C3-110204 |
| C3-110148 | Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case | ZTE | agreed | - | - |
| C3-110149 | Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case | ZTE | agreed | - | - |
| C3-110150 | Modification failure of APN-AMBR and Default EPS Bearer QoS in romaing case | ZTE | agreed | - | - |
| C3-110151 | Fixing Supported-Feature feature bit definitions | ZTE | revised | - | C3-110219 |
| C3-110152 | Fixing Supported-Feature feature bit definitions | ZTE | revised | - | C3-110220 |
| C3-110153 | RAT based charging for IFOM | ZTE | revised | - | C3-110194 |
| C3-110154 | Usage of the IFOM related AVPs in Subsession-Enforcement-Info | ZTE | revised | - | C3-110195 |
| C3-110155 | Update of the gateway control session establishment procedure for eMPS | ZTE, Ericsson | agreed | - | - |
| C3-110156 | Applicability of the access network information related AVPs in Subsession-Enforcement-Info | ZTE | revised | - | C3-110198 |
| C3-110157 | Correction to the descriptions of multiple BBERF scenario | ZTE | revised | - | C3-110199 |
| C3-110158 | Resolve the conflict of the access network information at the command level and the subsession level for the MAPCON scenario | ZTE | revised | - | C3-110200 |
| C3-110159 | Clarification of the sponsored data connectivity support (29.212) | ZTE | merged with C3-110186 into C3-110229 | - | C3-110229 |
| C3-110160 | Correction to feature bit for sponsored data connectivity (29.212) | ZTE | revised | - | C3-110291 |
| C3-110161 | Correction to Sponsor-Identity AVP and Application-Service-Provider-Identity AVP(29.212) | ZTE | revised | - | C3-110292 |
| C3-110162 | Clarify the usage reporting during the IP-CAN session modification(29.213) | ZTE | agreed | - | - |
| C3-110163 | Offline charging for sponsored data connectivity(29.213) | ZTE | revised | - | C3-110293 |
| C3-110164 | Authorization of the sponsored data connectivity(29.214) | ZTE | revised | - | C3-110294 |
| C3-110165 | Correction to feature bit for sponsored data connectivity (29.214) | ZTE | revised | - | C3-110307 |
| C3-110166 | Correction to the Reporting Usage for Sponsored Data Connectivity(29.214) | ZTE | revised | - | C3-110308 |
| C3-110167 | Correction to the AVPs to support xDSL line identification on the Gx | ZTE | revised | - | C3-110310 |
| C3-110168 | Usage of the AVPs to support xDSL line identification on the S9 interface | ZTE | revised | - | C3-110311 |
| C3-110169 | CS and IMS Interworking for Early Session Disposition SDP | ZTE | revised | - | C3-110189 |
| C3-110170 | Adding function for supporting early session | ZTE | postponed till the next meeting | - | - |
| C3-110171 | Support sponsored data connectivity in roaming case | ZTE | revised | - | C3-110309 |
| C3-110172 | Bearer control mode when using MUPSAP | Qualcomm Incorporated | revised | - | C3-110221 |
| C3-110173 | Bearer control mode when using MUPSAP | Qualcomm Incorporated | revised | - | C3-110222 |
| C3-110174 | Reference to 3GPP2 updated | Nokia Siemens Networks | revised | - | C3-110205 |
| C3-110175 | Reference to 3GPP2 updated | Nokia Siemens Networks | revised | - | - |
| C3-110176 | Reference to 3GPP2 updated | Nokia Siemens Networks | revised | - | C3-110207 |
| C3-110177 | LS on Updating codes in TS 29.230 | Nokia Siemens Networks | revised | - | C3-110223 |
| C3-110178 | Overlapping AVP code values | Nokia Siemens Networks | revised | - | CP-110181 |
| C3-110179 | Addition of normative references for in band DTMF and SDP messages | Orange | revised | - | C3-110319 |
| C3-110180 | Allocation of documents to agenda items (at Deadline) | CT3 Chairman | noted | - | - |
| C3-110181 | Overlapping AVP code values | Nokia Siemens Networks | revised | - | C3-110196 |
| C3-110182 | CT WG Meetings proposal 2012 | CT Chairs | noted | - | - |
| C3-110183 | Gx request handling (R10 29.212) | Huawei | revised | - | C3-110312 |
| C3-110184 | Reporting for sponsored connectivity (R10 29.212) | Huawei, Orange | revised | - | C3-110228 |
| C3-110185 | ASP operators information for sponsored data connectivity (R10 29.214) | Huawei, Orange | revised | C3-110101 | C3-110342 |
| C3-110186 | Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212) | Huawei, Orange | revised | - | C3-110229 |
| C3-110187 | Usage for sponsored connectivity (R10 29.214) | Huawei, Orange | revised | - | C3-110230 |
| C3-110188 | Proposed Schedule for CT3#61 | CT3 Chairman | revised | C3-110044 | C3-110295 |
| C3-110189 | CS and IMS Interworking for Early Session Disposition SDP | ZTE | revised | C3-110169 | C3-110285 |
| C3-110190 | Event triggers for multiple BBERFs in IP flow mobility case (R10 29.212) | Huawei | agreed | C3-110098 | - |
| C3-110191 | IFOM message flow | Qualcomm Incorporated | revised | C3-110143 | C3-110296 |
| C3-110192 | Identification of BBF against IP flow mobility routing rule | Qualcomm Incorporated | revised | C3-110144 | C3-110297 |
| C3-110193 | Clarifying the use of MBR>GBR | Ericsson | postponed till the next meeting | C3-110092 | - |
| C3-110194 | RAT based charging for IFOM | ZTE | revised | C3-110153 | C3-110353 |
| C3-110195 | Usage of the IFOM related AVPs in Subsession-Enforcement-Info | ZTE | agreed | C3-110154 | - |
| C3-110196 | Overlapping AVP code values | Nokia Siemens Networks | agreed | C3-110181 | - |
| C3-110197 | MPS Support over Rx | Ericsson | postponed till the next meeting | C3-110019 | - |
| C3-110198 | Applicability of the access network information related AVPs in Subsession-Enforcement-Info | ZTE | agreed | C3-110156 | - |
| C3-110199 | Correction to the descriptions of multiple BBERF scenario | ZTE | revised | C3-110157 | C3-110341 |
| C3-110200 | Resolve the conflict of the access network information at the command level and the subsession level for the MAPCON scenario | ZTE | agreed | C3-110158 | - |
| C3-110201 | LS on QoS-Negotiation and QoS-Upgrade on the Gx for GnGp SGSN | Huawei | approved | C3-110093 | - |
| C3-110202 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | agreed | C3-110145 | - |
| C3-110203 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | agreed | C3-110146 | - |
| C3-110204 | Modification failure of APN-AMBR and Default EPS Bearer QoS | ZTE | agreed | C3-110147 | - |
| C3-110205 | Reference to 3GPP2 updated | Nokia Siemens Networks | agreed | C3-110174 | - |
| C3-110206 | Reference to 3GPP2 updated | Nokia Siemens Networks | agreed | C3-110175 | - |
| C3-110207 | Reference to 3GPP2 updated | Nokia Siemens Networks | agreed | C3-110176 | - |
| C3-110208 | Completion of CSG information reporting | Ericsson | revised | C3-110020 | C3-110298 |
| C3-110209 | Completion of CSG information reporting | Ericsson | agreed | C3-110021 | - |
| C3-110210 | Correction of the Event-Trigger AVP enumeration | Ericsson | agreed | C3-110086 | - |
| C3-110211 | Correction of the Event-Trigger AVP enumeration | Ericsson | agreed | C3-110087 | - |
| C3-110212 | Bearer binding function in PCEF | Ericsson, Huawei | agreed | C3-110090 | - |
| C3-110213 | Bearer binding function in PCEF | Ericsson, Huawei | agreed | C3-110091 | - |
| C3-110214 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R8 29.212) | Huawei | revised | - | C3-110333 |
| C3-110215 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212) | Huawei | revised | C3-110094 | C3-110334 |
| C3-110216 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212) | Huawei | revised | C3-110095 | C3-110335 |
| C3-110217 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | revised | C3-110096 | C3-110336 |
| C3-110218 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | revised | C3-110097 | C3-110337 |
| C3-110219 | Fixing Supported-Feature feature bit definitions | ZTE | agreed | C3-110151 | - |
| C3-110220 | Fixing Supported-Feature feature bit definitions | ZTE | agreed | C3-110152 | - |
| C3-110221 | Bearer control mode when using MUPSAP | Qualcomm Incorporated | revised | C3-110172 | C3-110361 |
| C3-110222 | Bearer control mode when using MUPSAP | Qualcomm Incorporated | revised | C3-110173 | C3-110362 |
| C3-110223 | LS on Updating codes in TS 29.230 | Nokia Siemens Networks | postponed till the next meeting | C3-110177 | - |
| C3-110224 | S2b GTP addition to Annex D.1 | alcatel-lucent | revised | C3-110124 | C3-110338 |
| C3-110225 | S2b RAT Type | alcatel-lucent | agreed | C3-110125 | - |
| C3-110226 | SPR data usage optional for sponsored data connectivity | Ericsson | postponed till the next meeting | C3-110088 | - |
| C3-110227 | Authorization of the sponsored data connectivity(29.214) | Ericsson, ZTE | revised | C3-110089 | C3-110364 |
| C3-110228 | Reporting for sponsored connectivity (R10 29.212) | Huawei, Orange | agreed | C3-110184 | - |
| C3-110229 | Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212) | Huawei, Orange | revised | C3-110186 | C3-110301 |
| C3-110230 | Usage for sponsored connectivity (R10 29.214) | Huawei, Orange | agreed | C3-110187 | - |
| C3-110231 | OMR check sum procedures | Alcatel-Lucent | revised | C3-110026 | C3-110374 |
| C3-110232 | OMR SDP attribute syntax definition (for information) | Alcatel-Lucent | noted | C3-110035 | - |
| C3-110233 | Restructuring and completion of OMR SDP offer procedures | Alcatel-Lucent, Nokia Siemens Networks, Ericsson | agreed | C3-110023 | - |
| C3-110234 | Restructuring and completion of OMR SDP answer procedures | Alcatel-Lucent | agreed | C3-110024 | - |
| C3-110235 | Restructuring and completion of OMR UA procedures | Alcatel-Lucent | agreed | C3-110025 | - |
| C3-110236 | Updated OMR CapNeg procedures | Nokia Siemens Networks, Alcatel-Lucent | revised | C3-110122 | C3-110376 |
| C3-110237 | Handling of SDP o-line during OMR | Alcatel-Lucent | revised | C3-110029 | C3-110375 |
| C3-110238 | Annex X with simple message flows introduced | Ericsson | agreed | C3-110048 | - |
| C3-110239 | Status of ECN discussions in SA4 and anticipated impacts to CT3 | Nokia Siemens Networks | postponed till the next meeting | C3-110123 | - |
| C3-110240 | Adding CS-Ix functionalities to Mc-profile | Nokia Siemens Networks | revised | C3-110121 | C3-110288 |
| C3-110241 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | revised | C3-110083 | C3-110348 |
| C3-110242 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | revised | C3-110084 | C3-110349 |
| C3-110243 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | revised | C3-110085 | C3-110350 |
| C3-110244 | Correcting header table in annex A | Ericsson | agreed | C3-110060 | - |
| C3-110245 | Correcting header table in annex A | Ericsson | agreed | C3-110061 | - |
| C3-110246 | Correcting header table in annex A | Ericsson | agreed | C3-110062 | - |
| C3-110247 | Add missing E-CSCF to interworking network diagram | Alcatel-Lucent | revised | C3-110037 | C3-110290 |
| C3-110248 | RFC 5318 in the Major capability table | Ericsson | agreed | C3-110049 | - |
| C3-110249 | Updating OMA presence requirements | Ericsson | revised | C3-110050 | C3-110378 |
| C3-110250 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | revised | C3-110072 | C3-110393 |
| C3-110251 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | revised | C3-110073 | C3-110394 |
| C3-110252 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | revised | C3-110074 | C3-110395 |
| C3-110253 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | revised | C3-110075 | C3-110396 |
| C3-110254 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | agreed | C3-110076 | - |
| C3-110255 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | agreed | C3-110077 | - |
| C3-110256 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | agreed | C3-110078 | - |
| C3-110257 | Clarification of O-MGCF behaviour when SIP preconditions are used | Ericsson | agreed | C3-110079 | - |
| C3-110258 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110106 | - |
| C3-110259 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110107 | - |
| C3-110260 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110108 | - |
| C3-110261 | New Cause Code mappings of CV 23,38- 47and 65-79 | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110109 | - |
| C3-110262 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110110 | - |
| C3-110263 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110111 | - |
| C3-110264 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110112 | - |
| C3-110265 | Change of Cause code mapping | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110113 | - |
| C3-110266 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110117 | - |
| C3-110267 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110118 | - |
| C3-110268 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110119 | - |
| C3-110269 | Mapping of ISUP Cause Value 88 to Response 606 and vice versa | Deutsche Telekom, ATT, Telecom Italia | agreed | C3-110120 | - |
| C3-110270 | Missing Timer definition for TIR | Deutsche Telekom | revised | C3-110114 | C3-110345 |
| C3-110271 | Missing Timer definition for TIR | Deutsche Telekom | revised | C3-110115 | C3-110346 |
| C3-110272 | Missing Timer definition for TIR | Deutsche Telekom | revised | C3-110116 | C3-110347 |
| C3-110273 | Addition of the Target-Dialog header field to the table of major capabilities and Annex A | Fujitsu Limited | agreed | C3-110040 | - |
| C3-110274 | Addition of the Target-Dialog header field to the table of major capabilities and Annex A | Fujitsu Limited | agreed | C3-110041 | - |
| C3-110275 | Correcting major capabilities related to trust domain | NEC, NTT | revised | C3-110042 | C3-110351 |
| C3-110276 | Correcting major capabilities related to trust domain | NEC, NTT | revised | C3-110043 | C3-110352 |
| C3-110277 | Reference clause updates | Ericsson | agreed | C3-110054 | - |
| C3-110278 | Updates of the Major capability table | Ericsson | revised | C3-110057 | C3-110354 |
| C3-110279 | Updates of the Major capability table | Ericsson | revised | C3-110058 | C3-110355 |
| C3-110280 | Reference update: RFC 6086 | Ericsson | agreed | C3-110063 | - |
| C3-110281 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | agreed | C3-110139 | - |
| C3-110282 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | revised | C3-110140 | C3-110368 |
| C3-110283 | The descriptions of values within the Privacy header field | NTT, NTT DOCOMO | revised | C3-110141 | C3-110369 |
| C3-110284 | The descriptions of values within the Privacy header field | NTT, NTT DOCOMO | revised | C3-110142 | C3-110370 |
| C3-110285 | CS and IMS Interworking for Early Session Disposition SDP | ZTE | revised | C3-110189 | C3-110371 |
| C3-110286 | Interoperability of IMS Service Continuity over II-NNI updates | Ericsson | agreed | C3-110315 | - |
| C3-110287 | Adding new header fields Annex A | Ericsson | revised | C3-110316 | C3-110379 |
| C3-110288 | Adding CS-Ix functionalities to Mc-profile | Nokia Siemens Networks | withdrawn | C3-110240 | - |
| C3-110289 | Adding CS-Ix functionalities to Mc-profile | Nokia Siemens Networks | agreed | - | - |
| C3-110290 | Add missing E-CSCF to interworking network diagram | Alcatel-Lucent | revised | C3-110247 | C3-110392 |
| C3-110291 | Correction to feature bit for sponsored data connectivity (29.212) | ZTE | agreed | C3-110160 | - |
| C3-110292 | Correction to Sponsor-Identity AVP and Application-Service-Provider-Identity AVP(29.212) | ZTE | revised | C3-110161 | C3-110343 |
| C3-110293 | Offline charging for sponsored data connectivity(29.213) | ZTE | revised | C3-110163 | C3-110344 |
| C3-110294 | Authorization of the sponsored data connectivity(29.214) | ZTE | revised | C3-110164 | C3-110330 |
| C3-110295 | Proposed Schedule for CT3#61 | CT3 Chairman | noted | C3-110188 | - |
| C3-110296 | IFOM message flow | Qualcomm Incorporated | agreed | C3-110191 | - |
| C3-110297 | Identification of BBF against IP flow mobility routing rule | Qualcomm Incorporated | revised | C3-110192 | C3-110302 |
| C3-110298 | Completion of CSG information reporting | Ericsson | agreed | C3-110208 | - |
| C3-110299 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | agreed | C3-110336 | - |
| C3-110300 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | agreed | C3-110337 | - |
| C3-110301 | Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212) | Huawei, Orange | revised | C3-110229 | C3-110365 |
| C3-110302 | Identification of BBF against IP flow mobility routing rule | Qualcomm Incorporated | agreed | C3-110297 | - |
| C3-110303 | LS out Sponsored data connectivity in the roaming case | ZTE | revised | C3-110313 | C3-110366 |
| C3-110304 | Usage of the AVPs to support xDSL line identification on the S9 interface | ZTE | agreed | C3-110311 | - |
| C3-110305 | Summary of notation codes in dynamic view (BYE method) | NTT, NTT DOCOMO, AT&T | revised | C3-110323 | C3-110385 |
| C3-110306 | Summary of notation codes in dynamic view (INVITE method) | NTT, NTT DOCOMO, AT&T | revised | C3-110325 | C3-110386 |
| C3-110307 | Correction to feature bit for sponsored data connectivity (29.214) | ZTE | agreed | C3-110165 | - |
| C3-110308 | Correction to the Reporting Usage for Sponsored Data Connectivity(29.214) | ZTE | agreed | C3-110166 | - |
| C3-110309 | Support sponsored data connectivity in roaming case | ZTE | postponed till the next meeting | C3-110171 | - |
| C3-110310 | Correction to the AVPs to support xDSL line identification on the Gx | ZTE | agreed | C3-110167 | - |
| C3-110311 | Usage of the AVPs to support xDSL line identification on the S9 interface | ZTE | revised | C3-110168 | C3-110304 |
| C3-110312 | Gx request handling (R10 29.212) | Huawei | agreed | C3-110183 | - |
| C3-110313 | LS out Sponsored data connectivity in the roaming case | ZTE | revised | - | C3-110303 |
| C3-110314 | LS out Bearer control mode and multiple PDN connectivity | Qualcomm Incorporated | revised | - | C3-110363 |
| C3-110315 | Interoperability of IMS Service Continuity over II-NNI updates | Ericsson | revised | C3-110056 | C3-110286 |
| C3-110316 | Adding new header fields Annex A | Ericsson | revised | C3-110059 | C3-110287 |
| C3-110317 | Reference points Mi, Mm, Mw and I2 | Ericsson | agreed | C3-110065 | - |
| C3-110318 | Miscellaneous error corrections to 3GPP TS 29.165 | Ericsson | agreed | C3-110071 | - |
| C3-110319 | Addition of normative references for in band DTMF and SDP messages | Orange | revised | C3-110179 | C3-110380 |
| C3-110320 | New annex for dynamic view of SIP messages | NTT, NTT DOCOMO, AT&T | revised | C3-110128 | C3-110383 |
| C3-110321 | Summary of notation codes in dynamic view (ACK method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110129 | - |
| C3-110322 | Discussion: Example eMPS Call Scenarios | A&T | noted | - | - |
| C3-110323 | Summary of notation codes in dynamic view (BYE method) | NTT, NTT DOCOMO, AT&T | revised | C3-110130 | C3-110305 |
| C3-110324 | Summary of notation codes in dynamic view (CANCEL method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110131 | - |
| C3-110325 | Summary of notation codes in dynamic view (INVITE method) | NTT, NTT DOCOMO, AT&T | revised | C3-110132 | C3-110306 |
| C3-110326 | Summary of notation codes in dynamic view (MESSAGE method) | NTT, NTT DOCOMO, AT&T | revised | C3-110133 | C3-110356 |
| C3-110327 | Summary of notation codes in dynamic view (OPTIONS method) | NTT, NTT DOCOMO, AT&T | revised | C3-110134 | C3-110357 |
| C3-110328 | Summary of notation codes in dynamic view (PRACK method) | NTT, NTT DOCOMO, AT&T | revised | C3-110135 | C3-110358 |
| C3-110329 | Summary of notation codes in dynamic view (PUBLISH method) | NTT, NTT DOCOMO, AT&T | revised | C3-110136 | C3-110360 |
| C3-110330 | Authorization of the sponsored data connectivity(29.214) | ZTE | merged into C3-110227 | C3-110294 | - |
| C3-110331 | Summary of notation codes in dynamic view (REGISTER method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110137 | - |
| C3-110332 | Summary of notation codes in dynamic view (UPDATE method) | NTT, NTT DOCOMO, AT&T | revised | C3-110138 | C3-110359 |
| C3-110333 | CR 581 29.212 Rel-8 Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R8 29.212) | Huawei | agreed | C3-110214 | - |
| C3-110334 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212) | Huawei | agreed | C3-110215 | - |
| C3-110335 | Access type for QOS_CHANGE and QOS_CHANGE_EXCEEDING_AUTHORIZATION (R9 29.212) | Huawei | agreed | C3-110216 | - |
| C3-110336 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | revised | C3-110217 | C3-110299 |
| C3-110337 | Bearer binding function in GGSN (R9 29.213) | Huawei, Ericsson | revised | C3-110218 | C3-110300 |
| C3-110338 | S2b GTP addition to Annex D.1 | alcatel-lucent | agreed | C3-110224 | - |
| C3-110339 | Correction to the descriptions of multiple BBERF scenario | ZTE | agreed | - | - |
| C3-110340 | Correction to the descriptions of multiple BBERF scenario | ZTE | agreed | - | - |
| C3-110341 | Correction to the descriptions of multiple BBERF scenario | ZTE | agreed | C3-110199 | - |
| C3-110342 | ASP operators information for sponsored data connectivity (R10 29.214) | Huawei, Orange | postponed till the next meeting | C3-110185 | - |
| C3-110343 | Correction to Sponsor-Identity AVP and Application-Service-Provider-Identity AVP(29.212) | ZTE | agreed | C3-110292 | - |
| C3-110344 | Offline charging for sponsored data connectivity(29.213) | ZTE | agreed | C3-110293 | - |
| C3-110345 | Missing Timer definition for TIR | Deutsche Telekom | agreed | C3-110270 | - |
| C3-110346 | Missing Timer definition for TIR | Deutsche Telekom | agreed | C3-110271 | - |
| C3-110347 | Missing Timer definition for TIR | Deutsche Telekom | agreed | C3-110272 | - |
| C3-110348 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | agreed | C3-110241 | - |
| C3-110349 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | agreed | C3-110242 | - |
| C3-110350 | CCBS/CCNR correction of SUBSCRIBE request | Ericsson | agreed | C3-110243 | - |
| C3-110351 | Correcting major capabilities related to trust domain | NEC, NTT | agreed | C3-110275 | - |
| C3-110352 | Correcting major capabilities related to trust domain | NEC, NTT | agreed | C3-110276 | - |
| C3-110353 | RAT based charging for IFOM | ZTE | agreed | C3-110194 | - |
| C3-110354 | Updates of the Major capability table | Ericsson | agreed | C3-110278 | - |
| C3-110355 | Updates of the Major capability table | Ericsson | agreed | C3-110279 | - |
| C3-110356 | Summary of notation codes in dynamic view (MESSAGE method) | NTT, NTT DOCOMO, AT&T | revised | C3-110326 | C3-110387 |
| C3-110357 | Summary of notation codes in dynamic view (OPTIONS method) | NTT, NTT DOCOMO, AT&T | revised | C3-110327 | C3-110388 |
| C3-110358 | Summary of notation codes in dynamic view (PRACK method) | NTT, NTT DOCOMO, AT&T | revised | C3-110328 | C3-110389 |
| C3-110359 | Summary of notation codes in dynamic view (UPDATE method) | NTT, NTT DOCOMO, AT&T | revised | C3-110332 | C3-110391 |
| C3-110360 | Summary of notation codes in dynamic view (PUBLISH method) | NTT, NTT DOCOMO, AT&T | revised | C3-110329 | C3-110390 |
| C3-110361 | Bearer control mode for multiple PDN connections | Qualcomm Incorporated | conditionally agreed | C3-110221 | - |
| C3-110362 | Bearer control mode for multiple PDN connections | Qualcomm Incorporated | Conditionally agreed | C3-110222 | - |
| C3-110363 | LS out Bearer control mode and multiple PDN connectivity | Qualcomm Incorporated | revised | C3-110314 | C3-110367 |
| C3-110364 | Authorization of the sponsored data connectivity(29.214) | Ericsson, ZTE | revised | C3-110227 | C3-110381 |
| C3-110365 | Requesting Usage Monitoring Control for sponsored connectivity (R10 29.212) | Huawei, Orange | agreed | C3-110301 | - |
| C3-110366 | LS out Sponsored data connectivity in the roaming case | ZTE | approved | C3-110303 | - |
| C3-110367 | LS out Bearer control mode and multiple PDN connectivity | Qualcomm Incorporated | approved | C3-110363 | - |
| C3-110368 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | revised | C3-110282 | C3-110397 |
| C3-110369 | The descriptions of values within the Privacy header field | NTT, NTT DOCOMO | revised | C3-110283 | C3-110372 |
| C3-110370 | The descriptions of values within the Privacy header field | NTT, NTT DOCOMO | revised | C3-110284 | C3-110373 |
| C3-110371 | CS and IMS Interworking for Early Session Disposition SDP | ZTE | revised | C3-110285 | C3-110382 |
| C3-110372 | The descriptions of values within the Privacy header field | NTT, NTT DOCOMO | postponed till the next meeting | C3-110369 | - |
| C3-110373 | The descriptions of values within the Privacy header field | NTT, NTT DOCOMO | postponed till the next meeting | C3-110370 | - |
| C3-110374 | OMR check sum procedures | Alcatel-Lucent | agreed | C3-110231 | - |
| C3-110375 | Handling of SDP o-line during OMR | Alcatel-Lucent | agreed | C3-110237 | - |
| C3-110376 | Updated OMR CapNeg procedures | Nokia Siemens Networks, Alcatel-Lucent | agreed | C3-110236 | - |
| C3-110377 | TR 29.079 v1.1.0 | Alcatel-Lucent | postponed | - | - |
| C3-110378 | Updating OMA presence requirements | Ericsson | agreed | C3-110249 | - |
| C3-110379 | Adding new header fields Annex A | Ericsson | agreed | C3-110287 | - |
| C3-110380 | Addition of normative references for in band DTMF and SDP messages | Orange | agreed | C3-110319 | - |
| C3-110381 | Authorization of the sponsored data connectivity(29.214) | Ericsson, ZTE | agreed | C3-110364 | - |
| C3-110382 | CS and IMS Interworking for Early Session Disposition SDP | ZTE | revised | C3-110371 | - |
| C3-110383 | New annex for dynamic view of SIP messages | NTT, NTT DOCOMO, AT&T | agreed | C3-110320 | - |
| C3-110384 | CS and IMS Interworking for Early Session Disposition SDP | ZTE | revised | C3-110382 | C3-110398 |
| C3-110385 | Summary of notation codes in dynamic view (BYE method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110305 | - |
| C3-110386 | Summary of notation codes in dynamic view (INVITE method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110306 | - |
| C3-110387 | Summary of notation codes in dynamic view (MESSAGE method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110356 | - |
| C3-110388 | Summary of notation codes in dynamic view (OPTIONS method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110357 | - |
| C3-110389 | Summary of notation codes in dynamic view (PRACK method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110358 | - |
| C3-110390 | Summary of notation codes in dynamic view (PUBLISH method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110360 | - |
| C3-110391 | Summary of notation codes in dynamic view (UPDATE method) | NTT, NTT DOCOMO, AT&T | agreed | C3-110359 | - |
| C3-110392 | Add missing E-CSCF to interworking network diagram | Alcatel-Lucent | agreed | C3-110290 | - |
| C3-110393 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | agreed | C3-110250 | - |
| C3-110394 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | agreed | C3-110251 | - |
| C3-110395 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | agreed | C3-110252 | - |
| C3-110396 | Clarification of I-MGCF behaviour when SIP preconditions are used | Ericsson | agreed | C3-110253 | - |
| C3-110397 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | revised | C3-110368 | C3-110399 |
| C3-110398 | CS and IMS Interworking for Early Session Disposition SDP | ZTE | agreed | C3-110384 | - |
| C3-110399 | Alignment of INFO support for DTMF transport with TS 24.182 | NTT, NTT DOCOMO | agreed | C3-110397 | - |
| C3-110400 | Status of CT3 Work Items | CT3 Chairman | agreed | C3-110046 | - |

## Annex B : List of participants

| Name | Representing | Status-Partner | Ctry | Ph | Mob Ph | Email |
| --- | --- | --- | --- | --- | --- | --- |
| Allen, Andrew (Mr.) | Research in Motion Japan Ltd. | 3GPPMEMBER (ARIB) | US | +18478098636 |  | aallen@rim.com |
| Arai, Kenjiro (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81422593518 |  | arai.kenjiro@lab.ntt.co.jp |
| Bakker, John-Luc (Mr.) | Research in Motion UK Limited | 3GPPMEMBER (ETSI) | GB | +1-972-373-1761 | +1-908-463-7321 | jbakker@rim.com |
| Belling, Thomas (Dr.) | Nokia Siemens Networks | 3GPPMEMBER (ETSI) | DE | +49 89 5159 75207 | +49 172 2974678 | Thomas.Belling@nsn.com |
| Berry, Nigel. H (Mr.) | Alcatel-Lucent Telecom Ltd | 3GPPMEMBER (ETSI) | GB | +44 1793775019 |  | Nigel.Berry@alcatel-lucent.com |
| BERTRAND, Simon (Mr.) | ORANGE SA | 3GPPMEMBER (ETSI) | FR | +33145294200 |  | simon.bertrand@orange-ftgroup.com |
| Biondic, Nevenka (Mrs.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | HR | +385 1 365 3824 |  | nevenka.biondic@ericsson.com |
| Calme, Jim (Mr.) | Alcatel-Lucent | 3GPPMEMBER (ATIS) | US | +1 630 979 4385 |  | jim.calme@alcatel-lucent.com |
| Dobrowolska, Béata (Ms.) | France Telecom | 3GPPMEMBER (ETSI) | FR | +33145295759 |  | beata.dobrowolska@orange-ftgroup.com |
| Dolly, Martin (Mr.) | AT&T | 3GPPMEMBER (ATIS) | US | +1 609 903 3360 |  | md3135@att.com |
| Drage, Keith (Mr.) | Alcatel-Lucent Deutschland AG | 3GPPMEMBER (ETSI) | GB | +44 1793 897312 | +44 7799 658151 | Keith.Drage@alcatel-lucent.com |
| Ejzak, Richard (Mr.) | Alcatel-Lucent | 3GPPMEMBER (ATIS) | US | +1 630 979 7036 |  | richard.ejzak@alcatel-lucent.com |
| Fernandez, Susana (Miss) | Nanjing Ericsson Panda Com Ltd | 3GPPMEMBER (CCSA) | ES | +34646006865 |  | susana.fernandez@ericsson.com |
| Han, Jiwan (Mr.) | ETSI | 3GPPORG_REP (ETSI) | FR | +33 (0)4 92 94 42 31 | +33 4 74 40 83 69 | jiwan.han@etsi.org |
| Hodges, Phil (Mr.) | Ericsson Inc. | 3GPPMEMBER (ATIS) | AU | +61 404069546 |  | philip.hodges@ericsson.com |
| Holm, Jan (Mr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | SE | +46 8 719 7378 | + 46705197378 | Jan.Holm@ericsson.com |
| Holmberg, Christer (Mr.) | Nippon Ericsson K.K. | 3GPPMEMBER (ARIB) | SE | +35892992943 | +358405604412 | christer.holmberg@ericsson.com |
| Huslende, Ragnar (Dr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | NO | +47 911 10828 | +47 911 10828 | ragnar.huslende@ericsson.com |
| Jesske, Roland (Mr.) | Deutsche Telekom AG | 3GPPMEMBER (ETSI) | DE | +49 6151 628 2766 | +49 171 861 8445 | r.jesske@telekom.de |
| Jones, Mark (Mr.) | Bridgewater Systems | 3GPPMEMBER (ETSI) | CA | +1 613 301 7758 | +1-613-301-7758 | mark.jones@bridgewatersystems.com |
| Kato, Kei (Mr.) | Oki Electric Industry Co. Ltd. | 3GPPMEMBER (TTC) | JP | +81 3 5445 6350 |  | katou235@oki.com |
| Klehn, Norbert (Mr.) | Nokia Siemens Networks Oy | 3GPPMEMBER (ETSI) | DE | +49 89 5159 29090 | +49 171 3340782 | norbert.klehn@nsn.com |
| Lavasani, Shahab (Mr.) | Huawei Technologies Sweden AB | 3GPPMEMBER (ETSI) | SE | +46 70 6360204 | +46 70 6360204 | shahab.lavasani@huawei.com |
| Lu, Fei (Mr.) | ZTE Corporation | 3GPPMEMBER (ETSI) | CN | +86-25-52871114 | +86-13951628123 | lu.fei1@zte.com.cn |
| Lu, Feng (Mr.) | HuaWei Technologies Co., Ltd | 3GPPMEMBER (CCSA) | CN | +86 13482431645 |  | morpheus.lufeng@huawei.com |
| Matsuura, Takaaki (Mr.) | NTT DOCOMO INC. | 3GPPMEMBER (TTC) | JP | +81 468 40 3333 |  | takaaki.matsuura.sp@s1.nttdocomo.com |
| Mizukami, Takashi (Mr.) | Oki Electric Industry Co. Ltd. | 3GPPMEMBER (TTC) | JP | +81 80 5960 0444 |  | mizukami653@oki.com |
| Morishige, Yoshihito (Mr.) | Fujitsu Limited | 3GPPMEMBER (ARIB) | JP | + |  | y-morishige@jp.fujitsu.com |
| Muto, Yuta (Mr.) | Hitachi Ltd. | 3GPPMEMBER (ARIB) | JP | +81-42-323-1111 |  | yuta.muto.nc@hitachi.com |
| Pandit, Krishna (Dr.) | QUALCOMM CDMA Technologies | 3GPPMEMBER (ETSI) | DE | +49-911-54013750 |  | kpandit@qualcomm.com |
| Punz, Gottfried (Mr.) | NEC Technologies (UK) LTD | 3GPPMEMBER (ETSI) | GB | +49 6221 4342 119 |  | gottfried.punz@nw.neclab.eu |
| Qiao, Weihua (Mr.) | HuaWei Technologies Co., Ltd | 3GPPMEMBER (CCSA) | CN | +86 10 82882310 |  | qiaoweihua@huawei.com |
| Renzullo, Jared (Mr.) | Tekelec | 3GPPMEMBER (ATIS) | US | +15088047069 |  | jared.renzullo@tekelec.com |
| Sasaki, Tetsuo (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81 43 211 3532 |  | t-sasaki@lab.ntt.co.jp |
| Shi, Shufeng (Mrs.) | HUAWEI TECHNOLOGIES Co. Ltd. | 3GPPMEMBER (ETSI) | CN | +86-29-87674036 |  | shishf@huawei.com |
| Shu, Lin (Mr.) | HiSilicon Technologies Co., Lt | 3GPPMEMBER (CCSA) | CN | +86-15216618582 |  | shulin@huawei.com |
| Stupar, Patrick (Mr.) | QUALCOMM UK Ltd | 3GPPMEMBER (ETSI) | DE | +4991154013120 |  | pstupar@qualcomm.com |
| Subramanian, Ramachandran (Mr.) | Qualcomm Incorporated | 3GPPMEMBER (ATIS) | US | +1 858 651 2350 |  | rsubrama@qualcomm.com |
| Suzuki, Naoaki (Mr.) | NEC Corporation | 3GPPMEMBER (ARIB) | JP | +81-4-7185-6722 |  | n-suzuki@en.jp.nec.com |
| Tamura, Toshiyuki (Mr.) | NEC Corporation | 3GPPMEMBER (ETSI) | JP | +81 44 455 8496 |  | tamurato@aj.jp.nec.com |
| Tanaka, Itsuma (Mr.) | DOCOMO Communications Lab. | 3GPPMEMBER (ETSI) | JP | +81 46 840 3545 |  | tanakai@nttdocomo.co.jp |
| Tian, Tian (Miss) | ZTE Corporation | 3GPPMEMBER (ETSI) | CN | +86-025-52877867 |  | tian.tian1@zte.com.cn |
| Varma, Vijay (Dr.) | Telcordia Technologies | 3GPPMEMBER (ATIS) | US | +1 732 758-2811 |  | vvarma@telcordia.com |
| Yamashita, Hideyuki (Mr.) | NTT DOCOMO INC. | 3GPPMEMBER (ARIB) | JP | +81 422515618 |  | yamashitahi@s1.nttdocomo.co.jp |
| YANG, Weiwei (Mr.) | Huawei Technologies (UK) | 3GPPMEMBER (ETSI) | CN | +86-755-28421525 |  | tommy@huawei.com |
| Zheng, Yali (Miss) | HUAWEI TECHNOLOGIES Co. Ltd. | 3GPPMEMBER (ETSI) | CN | +86-21-68644808 |  | yali.zheng@huawei.com |
| Zhou, Xiaoyun (Mr.) | ZTE Corporation | 3GPPMEMBER (CCSA) | CN | +8613813823840 |  | zhou.xiaoyun@zte.com.cn |

Report prepared by: Jiwan Han