Third Generation Partnership Project (3GPP™)

DRAFT Meeting Report
for
TSG CT WG3
meeting: 70

Chicago, USA, 06/08/2012 to 10/08/2012

1	Opening of the meeting	6

2	Agenda/schedule	6

2.1	Approval of the agenda.	6

2.2	Proposed schedule	6

3	Registration of documents	7

4	Reports	8

4.1	Report from previous CT3 meeting	8

4.2	Report from previous CT plenary	8

4.3	Reports from other groups	8

5	Items for immediate consideration	8

5.1	IPR disclosures	8

5.2	Other items for immediate consideration	8

6	Received Liaison Statements	10

7	Release 7 and earlier releases	15

7.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	15

7.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	15

7.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]	17

7.4	Multimedia Broadcast and Multicast Service  [MBMS]	17

7.5	Policy and Charging Control [PCC]	17

7.6	Diameter for Gi interface [DIAMGi]	20

7.7	Diameter for Wi interface [DIAMWi]	20

7.8	Multimedia interworking between IMS and CS networks [MIW-IMS]	20

7.9	Protocol impact from providing IMS services via fixed broadband [FBI]	20

7.10	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]	22

7.11	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	22

7.12	Technical Enhancements and Improvements [TEIx]	22

7.13	Other Work Items	22

8	Release 8	22

8.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	22

8.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	22

8.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]	25

8.4	Multimedia Broadcast and Multicast Service  [MBMS]	25

8.5	Policy and Charging Control (non-SAE) [PCC]	25

8.6	Void	25

8.7	Diameter for Gi interface [DIAMGi]	25

8.8	Diameter for Wi interface [DIAMWi]	25

8.9	Multimedia interworking between IMS and CS networks (incl. MONA extensions) [MIW-IMS]	25

8.10	Protocol impact from providing IMS services via fixed broadband [FBI]	25

8.11	IMS Interworking Protocol Aspects in Support of Cable Rebulatory Requirements [PktCbl-Intw]	25

8.12	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]	25

8.13	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	25

8.14	PCC aspects of SAE [SAES-St3-PCC]	25

8.14.1	- Signalling flows (29.213)	26

8.14.2	- Gx and Gxx interfaces (29.212)	27

8.14.3	- Rx interface (29.214)	29

8.14.4	- S9 interface (29.215)	31

8.15	Interworking between EPC and external PDNs [SAES-St3-intwk]	31

8.16	IMS inter-operator service interconnection interface [FBI2-IOPSI]	32

8.17	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	32

8.18	Interworking between User-to-User Signaling (UUS) and SIP [UUSIW]	32

8.19	Work Items related to TISPAN transfer	32

8.19.1	- Maintenance of TISPAN R1 [MAINT_R1]	32

8.19.2	- Maintenance of TISPAN R2 [MAINT_R2]	32

8.19.3	- Documentation of TISPAN R1 and R2  in CT3 [REDOC_TIS-C3]	32

8.19.4	- Support of Overlap signalling [Overlap]	41

8.19.5	- Stage 3 (CT3) of CWonIMS [CW_IMS]	41

8.19.6	- Stage 3 (CT3) of [CCBS_CCNR]	41

8.20	Contributions on Common IMS related to 3GPP2 [REDOC_3GPP2]	41

8.21	Support of Service-Level Interworking for Messaging Services [MESSIW]	41

8.22	Enhancement of interworking between MTSI and Circuit Switched networks  [MTSI_eMHI]	41

8.23	Core Network Impacts for A-Interface Over IP [AoIP-CN]	41

8.24	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]	41

8.25	CAT solution for voice and video call in CS domain [CAT_SS]	41

8.26	Technical Enhancements and Improvements [TEI8]	41

8.27	Rel-8 contributions on other Work Items	41

9	Release 9	41

9.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	41

9.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	41

9.3	Protocol impact from providing IMS services via fixed broadband [FBI]	45

9.4	MBMS [MBMS]	45

9.5	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	45

9.6	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	45

9.7	PCC aspects of SAE [SAES-St3-PCC]	45

9.8	Reserved	45

9.9	Reserved	45

9.10	Reserved	45

9.11	Reserved	45

9.12	Reserved	45

9.13	Reserved	45

9.14	Reserved	45

9.15	Reserved	45

9.16	CS-IBCF and CS-TrGW definition in 3GPP specifications [CS-IBCF]	45

9.17	Interconnection Border Control Function (IBCF) – Transition Gateway (TrGW); Ix interface, Stage 3 [IMS_IBCF]	45

9.18	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	45

9.19	Operational Description of the Inter-IMS NNI   [II-NNI]	45

9.20	Support for IMS Emergency Calls over GPRS and EPS [IMS_EMER_GPRS_EPS]	48

9.21	PCC Enhancements [PCC-Enh]	48

9.22	Completion of IMS Restoration Procedures [eIMS_RP]	48

9.23	CT1 aspects of SRVCC support for IMS Emergency Calls [IMS_EMER_GPRS_EPS-SRVCC]	48

9.24	IMS Media Plane Security [MEDIASEC_CORE]	48

9.25	Technical Enhancements and Improvements [TEI9]	48

9.26	Rel-9 contributions on other work items	48

10	Release 10	48

10.1	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	48

10.2	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	48

10.3	PCC aspects of SAE [SAES-St3-PCC]	48

10.4	Interworking between EPC and external PDNs [SAES-St3-intwk]	48

10.5	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	48

10.6	PCC Enhancements [PCC-Enh]	48

10.7	Reserved	49

10.8	Reserved	49

10.9	Reserved	49

10.10	Reserved	49

10.11	Reserved	49

10.12	Reserved	49

10.13	Reserved	49

10.14	Reserved	49

10.15	Reserved	49

10.16	CPM-SMS Interworking [CPM-SMS]	49

10.17	Optimal Media Routeing [OMR]	49

10.18	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]	49

10.19	Call Completion Not Logged in [CCNL]	55

10.20	IP Flow Mobility and WLAN offload (Stage 3) [IFOM-CT]	55

10.21	Enabling Coder Selection and Rate Adaption for UTRAN and E-UTRAN for Load Adaptive Applications, CN impacts [ECSRA_LAA-CN]	55

10.21.1	-  Packet Core impacts	55

10.21.2	-  IMS/CS impacts	55

10.22	S2b Mobility based on GTP [SMOG-St3]	55

10.23	CT aspects of Enhancements for Multimedia Priority Service [eMPS-CN]	55

10.24	PCRF failure and restoration [PCRF-FR]	55

10.25	CT aspects of Multi Access PDN Connectivity  [MAPCON-St3]	55

10.26	CT3 Aspects of Policy Enhancements for Sponsored Connectivity and Coherent Access to Policy related Data Bases [PEST-CT3]	55

10.27	Dynamic View of Headers in Messages for II-NNI [NNI_DV]	55

10.28	CS and IMS Interworking for CAT early session model [CIIC_ES]	55

10.29	Stage 3 for Network Improvements for Machine Type Communications [NIMTC]	55

10.30	Technical Enhancements and Improvements [TEI10]	55

10.31	Rel-10 contributions on other Work Items	55

11	Release 11	55

11.1	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	55

11.2	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	56

11.3	Policy Control and Charging [PCC]	56

11.4	Interworking between EPC and external PDNs [SAES-St3-intwk]	56

11.5	PCC aspects of SAE [SAES-St3-PCC]	56

11.6	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	58

11.7	PCC Enhancements [PCC-Enh]	59

11.8	Optimal Media Routeing [OMR]	59

11.9	Dynamic View of Headers in Messages for II-NNI [NNI_DV]	59

11.10	Reserved	59

11.11	Reserved	59

11.12	Reserved	59

11.13	Reserved	59

11.14	Reserved	59

11.15	Reserved	59

11.16	Reserved	59

11.17	CT3 aspects of QoS Control Based on Subscriber Spending Limits  [QoS_SSL-CT3]	62

11.18	USSD Simulation Service in IMS-stage 3 [USSI]	62

11.19	Single Radio Video Call Continuity       [vSRVCC-CT]	63

11.19.1	IMS-related	63

11.19.2	PCC-related	63

11.20	Further improvement of usability of II-NNI specification for inter-connection [NNI_OI]	63

11.21	IMS Stage-3 IETF Protocol Alignment          [IMSProtoc5]	64

11.22	CT aspects of Single Radio Voice Call Continuity from UTRAN/GERAN to E-UTRAN/HSPA [rSRVCC-CT]	64

11.22.1	IMS/CS related docs	64

11.22.2	Packet Core related docs	65

11.23	Stage 3 for System Improvements to Machine-Type Communications [SIMTC-Reach]	66

11.24	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block I [BBAI_BBI-CT]	71

11.25	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block II [BBAI_BBII-CT]	76

11.26	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block III [BBAI_BBIII-CT]	79

11.27	CN aspects of Anonymous Call Rejection in the CS domain [ACR_CS-CN]	79

11.28	IMS Emergency PSAP Callback [EMC_PC]	79

11.29	Advanced Interconnection of Services [IPXS]	79

11.30	Enhancements for Multimedia Priority Service (MPS)  Gateway Control Priority [eMPS_Gateway]	80

11.31	CN aspects of Mobility based On GTP & PMIPv6 for WLAN access to EPC [SaMOG_WLAN-CN]	80

11.32	CN aspects of Service Identification for RRC Improvements in GERAN [SIRIG]	80

11.33	CT aspect on Network Provided Location Information for IMS [NWK-PL2IMS-CT]	80

11.34	II-NNI enhancements: SIP timers applicability [NNI_timers]	81

11.35	Roaming Architecture for Voice over IMS with Local Breakout – CT aspects [RAVEL-CT]	81

11.36	Inclusion of Media Resource Broker [MRB]	84

11.37	Technical Enhancements and Improvements [TEI11]	85

11.37.0	Usage momitoring congestion handling	85

11.37.1	IMS/CS related docs	86

11.37.2	Misc. Packet Core related docs	86

11.37.3	29.212 title correction	86

11.38	Rel-11 contributions on other Work Items	87

11.38.1	Enhanced T.38 FAX support	87

11.38.2	Void	89

11.38.3	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]	89

11.38.4	Enhancement for EPC Nodes Restoration [eNR_EPC]	90

11.38.5	IMS overload control	90

12	Release 12	91

12.1	Interworking between a PLMN with WLAN to access the EPC and a PDN	91

13	Joint sessions	92

14	Work Organisation	92

14.1	Work Plan Review	92

14.2	Specification Review	93

14.3	Next meetings, allocation of hosts	93

15	Summary of results	93

16	Any other business	93

17	Closing of the meeting	93

Annex A. TS/TR	93

Annex B. Work Item	93

Annex C. Liaison Statements	94

Annex C.1 Incoming Liaison Statements	94

Annex C.2 Outgoing Liaison Statements	94

Annex D. Agreed Change Requests	95

Annex E. List of Participants	100

Note: Hyperlinks to tdocs will work only if the present report is in a subdirectory named "report" and the tdocs themselves are in a parallel subdirectory names "docs".

## 1	Opening of the meeting

CT3 Chairman, Dr.Ragnar Huslende, opened and welcomed the delegates to CT3#70 in Chicago USA on 9:00 Monday 6th August 2012.

CT3 Chairman reminded the delegates to register with personal signature, no post-meeting registration, to wear the badge and to be prudent for using the internet connection.

## 2	Agenda/schedule

### 2.1	Approval of the agenda.

C3-121284	Draft agenda for CT3#70
					Source: CT3 Chairman

Discussion:

251 tdoc numbers allocated at the deadline.

Decision: 		The document was Noted.

### 2.2	Proposed schedule

C3-121330	Proposed schedule for CT3#70
					Source: CT3 Chairman

Discussion:

Few comments for schedule were issued and the revision was produced.

Decision: 		The document was Revised to C3-121557.

C3-121557	Proposed schedule for CT3#70
					Source: CT3 Chairman

(Replaces C3-121330)

Decision: 		The document was Revised to C3-121585.

C3-121585	Proposed schedule for CT3#70
					Source: CT3 Chairman

(Replaces C3-121557)

Decision: 		The document was Revised to C3-121704.

C3-121704	Proposed schedule for CT3#70
					Source: CT3 Chairman

(Replaces C3-121585)

Discussion:

483 tdoc numbers allocated at the end of the meeting.

Decision: 		The document was Noted.

## 3	Registration of documents

C3-121453	Allocation of documents to agenda items (at Deadline)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121454	Allocation of documents to agenda items (Start of Day 1)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121455	Allocation of documents to agenda items (Start of Day 2)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121456	Allocation of documents to agenda items (Start of Day 3)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121457	Allocation of documents to agenda items (Start of Day 4)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121458	Allocation of documents to agenda items (Start of Day 5)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121459	Allocation of documents to agenda items (End of Day 5)
					Source: CT3 Chairman

Decision: 		The document was Noted.

## 4	Reports

### 4.1	Report from previous CT3 meeting

C3-121460	Draft Meeting Report from CT3#69
					Source: MCC

Decision: 		The document was Approved.

### 4.2	Report from previous CT plenary

C3-121331	Brief Notes from CP#56 relevant to CT3
					Source: CT3 Chairman

Decision: 		The document was Noted.

### 4.3	Reports from other groups

## 5	Items for immediate consideration

### 5.1	IPR disclosures

### 5.2	Other items for immediate consideration

C3-121332	Draft References in CT3 Specifications
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121333	Proposed updates to CT3 ToR
					Source: CT3 Chairman

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121535	LS on Title for 3GPP TS 29.212
					Source: Allot Communications

Abstract:

1. Overall Description:

During CT#56 it was agreed not to change the title of approved TS/TR. It means that changes in title of TS 29.212 introduced in Rel-11, while Sd interface was introduced into the document ("Policy and Charging Control over Gx/.Sd reference Point"), are to be reverted back to the previous title, which covers only Gx Reference point ("Policy and Charging Control over Gx reference Point").

CT3 has identified the following problems with such an approach:

TS 29.212 scope covers Gx (and Gxx which is a functional subset of Gx in a specific case) AND Sd (whose scope is substantially different than Gx up to e.g. different session establishment messages and procedures, unsolicited application reporting etc.). Nevertheless, many procedures/AVPs are re-used therefore it makes sense to keep Gx and Sd in the same document.

In case of Sd interface, such a title without "Sd" would not reflect the contents of the document correctly.

It will be very difficult to find where Sd interface is defined in our documents without having it mentioned explicitly in the document title.

Change to the header by including Sd interface was introduced a year ago. Reverting back to the previous title (without Sd) is misleading for the people following our 3GPP activities, as to why such a reversion was made and the rationale behind.

2. Actions:

To CT group.

ACTION: 	CT3 kindly asks CT to re-consider their decision about reverting to the original title of 3GPP TS 29.212 in this particular case only as an exception, keep the title as exists today "Policy and Charging Control (PCC) over Gx/Sd reference point" and allow for the CRs with references change to accommodate this name.

Discussion:

It was recommanded to keep the current which is new tile and updating references in the related specifications. This LS was withdrawn by request from source company before the meeting.

Decision: 		The document was Withdrawn.

C3-121537	LS on Title for 3GPP TS 29.212
					Source: Allot Communication

Abstract:

1. Overall Description:

During CT#56 it was agreed not to change the title of approved TS/TR. It means that changes in title of TS 29.212 introduced in Rel-11, while Sd interface was introduced into the document ("Policy and Charging Control over Gx/.Sd reference Point"), are to be reverted back to the previous title, which covers only Gx Reference point ("Policy and Charging Control over Gx reference Point").

CT3 has identified the following problems with such an approach:

TS 29.212 scope covers Gx (and Gxx which is a functional subset of Gx in a specific case) AND Sd (whose scope is substantially different than Gx up to e.g. different session establishment messages and procedures, unsolicited application reporting etc.). Nevertheless, many procedures/AVPs are re-used therefore it makes sense to keep Gx and Sd in the same document.

In case of Sd interface, such a title without "Sd" would not reflect the contents of the document correctly.

It will be very difficult to find where Sd interface is defined in our documents without having it mentioned explicitly in the document title.

Change to the header by including Sd interface was introduced a year ago. Reverting back to the previous title (without Sd) is misleading for the people following our 3GPP activities, as to why such a reversion was made and the rationale behind.

Additionally, not only Sd interface, but also Gxx and S15 descriptions are included in the TS 29.212. This make title including "Gx" only even more incorrect.

Such a method also prevent us from extending TS 29.212 in the future to include new interfaces, similar to Gx/Gxx/Sd/S15 descriptions, as the title is interface specific.

2. Actions:

To CT group.

ACTION: 	CT3 kindly asks CT to agree on the following way forward in this case:

Write a new TS (new number - possibly 29.212-1) with a generic title "Reference points for Policy and Charging Control (PCC) of core network entities" which will be infinitely extensible to other interfaces in the future.  Its contents (apart from title page and history table) would be identical to the current 29.212 Rel-11.

Create a CR to 29.212 Rel-11 which deletes all of its normative contents and creates a new clause 4 which reads "The technical provisions formerly in the present TS can now be found in 3GPP TS 29.212-1 [x]."

Discussion:

This outgoing LS was produced after deadline for adding content of action section. (same title to C3-121535). And new title TS 29.212-1 was offered. The related CR is C3-121538. The revision was produced for adding John Meredith's comments.

Decision: 		The document was Revised to C3-121539.

C3-121539	LS on Title for 3GPP TS 29.212
					Source: Allot Communication

(Replaces C3-121537)

Decision: 		The document was Noted.

C3-121541	LS on Title of TS 29.212
					Source: tbd

Decision: 		The document was Withdrawn.

## 6	Received Liaison Statements

C3-121464	Reply LS on CT3 LS on Questions regarding BBAI procedures
					Source: TSG SA WG2

Discussion:

It is reply LS to C3-120827.

Decision: 		The document was Noted.

C3-121465	Reply LS on OSCAR conclusions 
					Source: TSG SA WG2

Discussion:

It is reply LS to C3-120867

Decision: 		The document was Noted.

C3-121466	Reply LS on assignment of 3 digit MNC
					Source: TSG CT WG1

Decision: 		The document was Noted.

C3-121467	Reply LS on H(e)NB local IP address for Fixed Broadband Access network interworking
					Source: TSG CT WG4

Discussion:

CT3 decided to leave the decision to SA2.

Decision: 		The document was Noted.

C3-121468	Reply LS on OSCAR conclusions
					Source: TSG CT WG1

Decision: 		The document was Noted.

C3-121469	LS on Absolute Time of MBMS Data Transfer
					Source: TSG RAN WG3

Decision: 		The document was Noted.

C3-121470	Reply LS on H(e)NB local IP address for Fixed Broadband Access network interworking 
					Source: TSG SA WG3

Decision: 		The document was Noted.

C3-121471	NGN studies
					Source: ITU-T Study Group 3 Rapporteur on NGN

Discussion:

There is no impact to CT3.

Decision: 		The document was Noted.

C3-121472	Liaison Regarding MSF/ETSI/GSMA RCS VoLTE Interoperability Event
					Source: ETSI TC INT (IMS Network Testing)

Discussion:

Any issues with specifications owned by CT3 should be feed back.

Decision: 		The document was Noted.

C3-121473	Reply LS on Assignment of 3 digit MNC
					Source: TSG CT

Decision: 		The document was Noted.

C3-121474	Reply LS on Assignment of 3 digit MNC
					Source: TSG SA

Decision: 		The document was Noted.

C3-121475	LS on GSMA Application Network Efficiency Task Force – whitepaper and actions
					Source: TSG SA

Discussion:

The proposed reply LS is C3-121536.

Decision: 		The document was Noted.

C3-121476	LS on security for the Tsp interface
					Source: TSG SA WG3

Discussion:

Related PCR is C3-121325.

Decision: 		The document was Noted.

C3-121477	LS on GSMA Application Network Efficiency Task Force “whitepaper and actions” 
					Source: TSG SA WG2

Decision: 		The document was Noted.

C3-121478	LS response on V-PCRF-Indicated IP-CAN Session Modification for NSWO traffic 
					Source: TSG SA WG2

Discussion:

Related CR is C3-121443.

Decision: 		The document was Noted.

C3-121479	Reply LS on TFT usage for the primary PDP context when access to the PGW
					Source: TSG SA WG2

Discussion:

Related CR is from C3-121412 to C3-121415.

Decision: 		The document was Noted.

C3-121480	LS on Tsp
					Source: TSG SA WG2

Discussion:

Related PCR is C3-121534.

Decision: 		The document was Noted.

C3-121481	Triggering functionality and relation to 3GPP CT WG3 working assumption
					Source: ETSI TC M2M

Decision: 		The document was Noted.

C3-121536	Reply LS on GSMA Application Network Efficiency Task Force – whitepaper and actions
					Source: Alcatal-Lucent

Discussion:

This outgoing LS was produced by request after deadline. Response to LS, C3-121475. Offline exercise offered for co-work with interested companies.

Decision: 		The document was Revised to C3-121669.

C3-121542	Reply LS on security for the Tsp interface
					Source: Nokia Siemens Networks

Discussion:

It is the reply LS on C3-121476.

Decision: 		The document was Revised to C3-121724.

C3-121669	Reply LS on GSMA Application Network Efficiency Task Force – whitepaper and actions
					Source: Alcatal-Lucent

(Replaces C3-121536)

Abstract:

1. Overall Description:

3GPP CT WG3 has received the LS (SP-120423) for TSG SA to take the GSMA white paper into account for further work/study on network optimization techniques that mitigate 3GPP network issues due to penetration of smart phones.

3GPP CT WG3 has performed an early review of the solutions from the GSMA Whitepaper and has identified in the 3GPP-CT3-Actions.xls file (attached):

solutions that are outside the scope of 3GPP CT3;

solutions already covered in 3GPP CT3;

items that are in Rel-12 SA2 and for which CT3 will investigate further on potential CT3 actions dependent on stage 2 requirements (note that 3GPP CT3 has not started the Rel-12 work).

The SA2 actions received from 3GPP SA WG2 are copied in the CT3 file to provide additional background to the CT3 answers.

2. Actions:

To CT group.

ACTION: 	CT3 asks TSG CT to take this information into account for a reply to TSG SA.

Discussion:

This outgoing LS was produced by request after deadline. Response to LS, C3-121475. Offline exercise offered for co-work with interested companies.

Decision: 		The document was Approved.

C3-121724	Reply LS on security for the Tsp interface
					Source: Nokia Siemens Networks

(Replaces C3-121542)

Decision: 		The document was Revised to C3-121736.

C3-121728	LS out Reply LS on Questions regarding BBAI procedures
					Source: Orange

Decision: 		The document was Revised to C3-121735.

C3-121735	LS out Reply LS on Questions regarding BBAI procedures
					Source: Orange

(Replaces C3-121728)

Abstract:

1. Overall Description:

CT3 would like to thank SA2 for the reply LS regarding BBAI procedures.

During CT3#70 some concerns were raised regarding the PCRF determining whether or not the UE connects via a Fixed Broadband Access based on the UE local IP address or H(e)NB local IP address received over Gx/Gxx.

CT3 understands that this mechanism is “re-use” of the configuration described in “BPCF discovery and selection” clause of TS 23.203 – Annex P:

“The PCRF (for non-roaming) and the V-PCRF (for roaming cases) selects the correct BBF network entry point based on UE Local IP address for WLAN access and based on H(e)NB Local IP address and/or FQDN of BBF access network, if available, received from the PCEF/BBERF for H(e)NB case”.

Section P.6.1.1 of TS 23.203 also states that;

The PCRF functionality defined in clause 6.2.1.0 shall apply. In addition, to support interworking with Fixed Broadband networks, the PCRF shall:

….

-     Be able to be configured with the relation of IP address ranges to Fixed Broadband Access, to allow BPCF discovery.

The main concern is that it forces a 3GPP operator to get knowledge of all the IP ranges that can be allocated to a UE in the BBF network. It has been mentioned that a 3GPP operator could have potentially a lot BBF operator roaming partners. As a consequence, this approach does not seem scalable.

This is seen as a real drawback for the deployment of the interworking with BBF network mainly because:

- The 3GPP operator must configure and maintain this database (IP@ ranges – BBF network). This kind of database is prone to error and misconfiguration and this would imply that the 3GPP operator has to be aware of a BBF network renumbering.

- Every BBF network (with whom roaming agreement are established) has to provide this information (all possible IP@ ranges used in the BBF network for IP allocation).

Thus it has been pointed out by some operators during CT3#70 meeting that deploying such configuration mechanisms leads to management and provisioning constraints.

2. Actions:

To SA2 group.

ACTION: 	SA2 is kindly asked to confirm whether a solution requiring configuration and maintenance of many IP address ranges in the PCRF is the most efficient, or whether a more elegant alternative can be found.

Decision: 		The document was Approved.

C3-121736	Reply LS on security for the Tsp interface
					Source: Nokia Siemens Networks

(Replaces C3-121724)

Decision: 		The document was Revised to C3-121754.

C3-121754	Reply LS on security for the Tsp interface
					Source: Nokia Siemens Networks

(Replaces C3-121736)

Abstract:

1. Overall Description:

CT3 thanks SA3 for their LS on security for the Tsp interface.

Within the LS, SA3 had requested CT3 to "respond to SA3 whether RFC 3588 is still preferred over the upcoming RFC 3588bis". CT3 has decided to continue using RFC 3588 rather than the RFC 3588bis IETF draft as baseline for the Tsp interface Diameter procedures in Rel-11.

CT3 has also agreed to incorporate the PCR attached to the received LS into draft TS 29.368 without any significant changes apart from the removal of RFC3588bis related editor's notes suggested by SA3.

2. Actions: NONE

Decision: 		The document was Approved.

## 7	Release 7 and earlier releases

### 7.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 7.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-121692	Mapping of CANCEL request
					29.163	  CR-0686  (Rel-7) v7.25.0
					Source: Orange, AT&T

Discussion:

The category is "F" and moved from Rel-9

Decision: 		The document was Agreed.

C3-121693	Mapping of CANCEL request
					29.163	  CR-0687  (Rel-8) v8.19.0
					Source: Orange, AT&T

Decision: 		The document was Agreed.

C3-121523	Mapping of CANCEL request 
					29.163	  CR-0612  rev 1 (Rel-9) v9.10.0
					Source: Orange

Decision: 		The document was Revised to C3-121627.

C3-121627	Mapping of CANCEL request 
					29.163	  CR-0612  rev 2 (Rel-9) v9.10.0
					Source: Orange

(Replaces C3-121523)

Discussion:

Category should be "A".

Decision: 		The document was Revised to C3-121694.

C3-121694	Mapping of CANCEL request 
					29.163	  CR-0612  rev 3 (Rel-9) v9.10.0
					Source: Orange, AT&T

(Replaces C3-121627)

Discussion:

The category is "A"

Decision: 		The document was Agreed.

C3-121524	Mapping of CANCEL request 
					29.163	  CR-0613  rev 1 (Rel-10) v10.6.0
					Source: Orange

Decision: 		The document was Revised to C3-121628.

C3-121628	Mapping of CANCEL request 
					29.163	  CR-0613  rev 2 (Rel-10) v10.6.0
					Source: Orange, AT&T

(Replaces C3-121524)

Decision: 		The document was Agreed.

C3-121525	Mapping of CANCEL request 
					29.163	  CR-0614  rev 1 (Rel-11) v11.3.0
					Source: Orange

Decision: 		The document was Revised to C3-121629.

C3-121629	Mapping of CANCEL request 
					29.163	  CR-0614  rev 2 (Rel-11) v11.3.0
					Source: Orange, AT&T

(Replaces C3-121525)

Decision: 		The document was Agreed.

### 7.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]

### 7.4	Multimedia Broadcast and Multicast Service  [MBMS]

### 7.5	Policy and Charging Control [PCC]

C3-121389	Correction of assigned internet protocol number (29.214 R7)
					29.214	  CR-0229  (Rel-7) v7.11.0
					Source: Alcatel-Lucent

Decision: 		The document was Revised to C3-121647.

C3-121390	Correction of assigned internet protocol number (29.214 R8)
					29.214	  CR-0230  (Rel-8) v8.12.0
					Source: Alcatel-Lucent

Decision: 		The document was Revised to C3-121648.

C3-121391	Correction of assigned internet protocol number (29.214 R9)
					29.214	  CR-0231  (Rel-9) v9.9.0
					Source: Alcatel-Lucent

Decision: 		The document was Revised to C3-121649.

C3-121392	Correction of assigned internet protocol number (29.214 R10)
					29.214	  CR-0232  (Rel-10) v10.6.0
					Source: Alcatel-Lucent

Decision: 		The document was Revised to C3-121650.

C3-121393	Correction of assigned internet protocol number (29.214 R11)
					29.214	  CR-0233  (Rel-11) v11.5.0
					Source: Alcatel-Lucent

Decision: 		The document was Revised to C3-121651.

C3-121486	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0894  (Rel-7) v7.14.0
					Source: ZTE

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121487	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0895  (Rel-8) v8.16.0
					Source: ZTE

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121488	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0896  (Rel-9) v9.11.0
					Source: ZTE

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121489	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0897  (Rel-10) v10.7.0
					Source: ZTE

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121490	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0898  (Rel-11) v11.5.0
					Source: ZTE

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121647	Correction of assigned internet protocol number (29.214 R7)
					29.214	  CR-0229  rev 1 (Rel-7) v7.11.0
					Source: Alcatel-Lucent

(Replaces C3-121389)

Decision: 		The document was Agreed.

C3-121648	Correction of assigned internet protocol number (29.214 R8)
					29.214	  CR-0230  rev 1 (Rel-8) v8.12.0
					Source: Alcatel-Lucent

(Replaces C3-121390)

Decision: 		The document was Agreed.

C3-121649	Correction of assigned internet protocol number (29.214 R9)
					29.214	  CR-0231  rev 1 (Rel-9) v9.9.0
					Source: Alcatel-Lucent

(Replaces C3-121391)

Decision: 		The document was Agreed.

C3-121650	Correction of assigned internet protocol number (29.214 R10)
					29.214	  CR-0232  rev 1 (Rel-10) v10.6.0
					Source: Alcatel-Lucent

(Replaces C3-121392)

Decision: 		The document was Agreed.

C3-121651	Correction of assigned internet protocol number (29.214 R11)
					29.214	  CR-0233  rev 1 (Rel-11) v11.5.0
					Source: Alcatel-Lucent

(Replaces C3-121393)

Decision: 		The document was Agreed.

C3-121668	LS out LS on QoS parameters can be upgraded and downgraded
					Source: ZTE

Decision: 		The document was Approved.

### 7.6	Diameter for Gi interface [DIAMGi]

### 7.7	Diameter for Wi interface [DIAMWi]

### 7.8	Multimedia interworking between IMS and CS networks [MIW-IMS]

### 7.9	Protocol impact from providing IMS services via fixed broadband [FBI]

C3-121315	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0633  rev 5 (Rel-7) v7.25.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121600.

C3-121316	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0634  rev 5 (Rel-8) v8.19.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121601.

C3-121317	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0635  rev 5 (Rel-9) v9.10.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121602.

C3-121318	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0636  rev 5 (Rel-10) v10.6.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121603.

C3-121319	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0637  rev 5 (Rel-11) v11.3.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121604.

C3-121600	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0633  rev 6 (Rel-7) v7.25.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121315)

Decision: 		The document was Agreed.

C3-121601	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0634  rev 6 (Rel-8) v8.19.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121316)

Decision: 		The document was Agreed.

C3-121602	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0635  rev 6 (Rel-9) v9.10.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121317)

Decision: 		The document was Agreed.

C3-121603	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0636  rev 6 (Rel-10) v10.6.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121318)

Decision: 		The document was Agreed.

C3-121604	P-Early-Media Header is Mandatory for MGCF
					29.163	  CR-0637  rev 6 (Rel-11) v11.3.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121319)

Decision: 		The document was Agreed.

### 7.10	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]

### 7.11	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 7.12	Technical Enhancements and Improvements [TEIx]

### 7.13	Other Work Items

## 8	Release 8

### 8.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 8.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-121336	Reference alignment for RTP Payload Format for AMR and AMR-WB Audio Codecs
					29.163	  CR-0670  (Rel-8) v8.19.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121337	Reference alignment for RTP Payload Format for AMR and AMR-WB Audio Codecs
					29.163	  CR-0671  (Rel-9) v9.10.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121338	Reference alignment for RTP Payload Format for AMR and AMR-WB Audio Codecs
					29.163	  CR-0672  (Rel-10) v10.6.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121339	Reference alignment for RTP Payload Format for AMR and AMR-WB Audio Codecs
					29.163	  CR-0673  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121346	Request "Connected Line Identity" for TIP
					29.163	  CR-0674  (Rel-8) v8.19.0
					Source: Ericsson

Discussion:

This CR was withdrawn before meeting by request from source company.

Decision: 		The document was Withdrawn.

C3-121347	Request "Connected Line Identity" for TIP
					29.163	  CR-0675  (Rel-9) v9.10.0
					Source: Ericsson

Discussion:

This CR was withdrawn before meeting by request from source company.

Decision: 		The document was Withdrawn.

C3-121348	Request "Connected Line Identity" for TIP
					29.163	  CR-0676  (Rel-10) v10.6.0
					Source: Ericsson

Discussion:

This CR was withdrawn before meeting by request from source company. This CR was proposed only for Rel-11 (C3-121349).

Decision: 		The document was Withdrawn.

C3-121450	XML schema defintion correction
					29.163	  CR-0685  (Rel-8) v8.19.0
					Source: Belgacom

Decision: 		The document was Revised to C3-121704.

C3-121516	TIP TIR interworking 29.163r8
					29.163	  CR-0618  rev 1 (Rel-8) v8.19.0
					Source: Orange

Decision: 		The document was Revised to C3-121617.

C3-121517	TIP TIR interworking 29.163r9
					29.163	  CR-0606  rev 2 (Rel-9) v9.10.0
					Source: Orange

Decision: 		The document was Revised to C3-121618.

C3-121518	TIP TIR interworking 29.163r10
					29.163	  CR-0607  rev 2 (Rel-10) v10.6.0
					Source: Orange

Decision: 		The document was Revised to C3-121619.

C3-121519	TIP TIR interworking 29.163r11
					29.163	  CR-0608  rev 2 (Rel-11) v11.3.0
					Source: Orange

Decision: 		The document was Revised to C3-121620.

C3-121617	TIP TIR interworking 29.163r8
					29.163	  CR-0618  rev 2 (Rel-8) v8.19.0
					Source: Orange

(Replaces C3-121516)

Decision: 		The document was Revised to C3-121710.

C3-121618	TIP TIR interworking 29.163r9
					29.163	  CR-0606  rev 3 (Rel-9) v9.10.0
					Source: Orange

(Replaces C3-121517)

Decision: 		The document was Revised to C3-121711.

C3-121619	TIP TIR interworking 29.163r10
					29.163	  CR-0607  rev 3 (Rel-10) v10.6.0
					Source: Orange

(Replaces C3-121518)

Decision: 		The document was Revised to C3-121712.

C3-121620	TIP TIR interworking 29.163r11
					29.163	  CR-0608  rev 3 (Rel-11) v11.3.0
					Source: Orange

(Replaces C3-121519)

Decision: 		The document was Revised to C3-121713.

C3-121710	TIP TIR interworking 29.163r8
					29.163	  CR-0618  rev 3 (Rel-8) v8.19.0
					Source: Orange

(Replaces C3-121617)

Decision: 		The document was Agreed.

C3-121711	TIP TIR interworking 29.163r9
					29.163	  CR-0606  rev 4 (Rel-9) v9.10.0
					Source: Orange

(Replaces C3-121618)

Decision: 		The document was Agreed.

C3-121712	TIP TIR interworking 29.163r10
					29.163	  CR-0607  rev 4 (Rel-10) v10.6.0
					Source: Orange

(Replaces C3-121619)

Decision: 		The document was Agreed.

C3-121713	TIP TIR interworking 29.163r11
					29.163	  CR-0608  rev 4 (Rel-11) v11.3.0
					Source: Orange

(Replaces C3-121620)

Decision: 		The document was Agreed.

### 8.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]

### 8.4	Multimedia Broadcast and Multicast Service  [MBMS]

### 8.5	Policy and Charging Control (non-SAE) [PCC]

### 8.6	Void

### 8.7	Diameter for Gi interface [DIAMGi]

### 8.8	Diameter for Wi interface [DIAMWi]

### 8.9	Multimedia interworking between IMS and CS networks (incl. MONA extensions) [MIW-IMS]

### 8.10	Protocol impact from providing IMS services via fixed broadband [FBI]

### 8.11	IMS Interworking Protocol Aspects in Support of Cable Rebulatory Requirements [PktCbl-Intw]

### 8.12	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]

### 8.13	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 8.14	PCC aspects of SAE [SAES-St3-PCC]

Changes affecting only one  PCC TS should be put under the respective sub-items  8.14.1/2/3/4 below.

Related CRs affecting several  PCC TSs  may be grouped together directly under agenda item 8.14

#### 8.14.1	- Signalling flows (29.213)

C3-121482	Store session information and identify IP-CAN Session (R8 29.213)
					29.213	  CR-0431  (Rel-8) v8.14.0
					Source: Huawei, Nokia Siemens Networks

Decision: 		The document was Revised to C3-121652.

C3-121483	Store session information and identify IP-CAN Session (R9 29.213)
					29.213	  CR-0432  (Rel-9) v9.9.0
					Source: Huawei, Nokia Siemens Networks

Decision: 		The document was Revised to C3-121653.

C3-121484	Store session information and identify IP-CAN Session (R10 29.213)
					29.213	  CR-0433  (Rel-10) v10.6.0
					Source: Huawei, Nokia Siemens Networks

Decision: 		The document was Revised to C3-121654.

C3-121485	Store session information and identify IP-CAN Session (R11 29.213)
					29.213	  CR-0434  (Rel-11) v11.3.0
					Source: Huawei, Nokia Siemens Networks

Decision: 		The document was Revised to C3-121655.

C3-121652	Store session information and identify IP-CAN Session (R8 29.213)
					29.213	  CR-0431  rev 1 (Rel-8) v8.14.0
					Source: Huawei, Nokia Siemens Networks

(Replaces C3-121482)

Decision: 		The document was Agreed.

C3-121653	Store session information and identify IP-CAN Session (R9 29.213)
					29.213	  CR-0432  rev 1 (Rel-9) v9.9.0
					Source: Huawei, Nokia Siemens Networks

(Replaces C3-121483)

Decision: 		The document was Agreed.

C3-121654	Store session information and identify IP-CAN Session (R10 29.213)
					29.213	  CR-0433  rev 1 (Rel-10) v10.6.0
					Source: Huawei, Nokia Siemens Networks

(Replaces C3-121484)

Decision: 		The document was Agreed.

C3-121655	Store session information and identify IP-CAN Session (R11 29.213)
					29.213	  CR-0434  rev 1 (Rel-11) v11.3.0
					Source: Huawei, Nokia Siemens Networks

(Replaces C3-121485)

Decision: 		The document was Agreed.

#### 8.14.2	- Gx and Gxx interfaces (29.212)

C3-121404	Store session information and identify IP-CAN Session (R8 29.212)
					29.212	  CR-0876  (Rel-8) v8.16.0
					Source: Huawei, Nokia Siemens Networks

Discussion:

This CR was withdrawn by request from source company.

Decision: 		The document was Withdrawn.

C3-121405	Store session information and identify IP-CAN Session (R9 29.212)
					29.212	  CR-0877  (Rel-9) v9.11.0
					Source: Huawei, Nokia Siemens Networks

Discussion:

This CR was withdrawn by request from source company.

Decision: 		The document was Withdrawn.

C3-121406	Store session information and identify IP-CAN Session (R10 29.212)
					29.212	  CR-0878  (Rel-10) v10.7.0
					Source: Huawei, Nokia Siemens Networks

Discussion:

This CR was withdrawn by request from source company.

Decision: 		The document was Withdrawn.

C3-121407	Store session information and identify IP-CAN Session (R11 29.212)
					29.212	  CR-0879  (Rel-11) v11.5.0
					Source: Huawei, Nokia Siemens Networks

Discussion:

This CR was withdrawn by request from source company.

Decision: 		The document was Withdrawn.

C3-121412	TFT usage for the primary PDP context when using PGW (R8 29.212)
					29.212	  CR-0880  (Rel-8) v8.16.0
					Source: Huawei

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121413	TFT usage for the primary PDP context when using PGW (R9 29.212)
					29.212	  CR-0881  (Rel-9) v9.11.0
					Source: Huawei

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121414	TFT usage for the primary PDP context when using PGW (R10 29.212)
					29.212	  CR-0882  (Rel-10) v10.7.0
					Source: Huawei

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121415	TFT usage for the primary PDP context when using PGW (R11 29.212)
					29.212	  CR-0883  (Rel-11) v11.5.0
					Source: Huawei

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121656	Reply LS LS on TFT usage for the primary PDP context when using PGW
					Source: Ericsson

Decision: 		The document was Revised to C3-121737.

C3-121737	Reply LS LS on TFT usage for the primary PDP context when using PGW
					Source: Ericsson

(Replaces C3-121656)

Decision: 		The document was Revised to C3-121755.

C3-121755	Reply LS LS on TFT usage for the primary PDP context when using PGW
					Source: Ericsson

(Replaces C3-121737)

Decision: 		The document was Approved.

#### 8.14.3	- Rx interface (29.214)

C3-121394	Clarification of Supported-Features AVP (29.214 R8)
					29.214	  CR-0234  (Rel-8) v8.12.0
					Source: Alcatel-Lucent

Decision: 		The document was Withdrawn.

C3-121395	Clarification of Supported-Features AVP (29.214 R9)
					29.214	  CR-0235  (Rel-9) v9.9.0
					Source: Alcatel-Lucent

Decision: 		The document was Withdrawn.

C3-121396	Clarification of Supported-Features AVP (29.214 R10)
					29.214	  CR-0236  (Rel-10) v10.6.0
					Source: Alcatel-Lucent

Decision: 		The document was Withdrawn.

C3-121397	Clarification of Supported-Features AVP (29.214 R11)
					29.214	  CR-0237  (Rel-11) v11.5.0
					Source: Alcatel-Lucent

Decision: 		The document was Withdrawn.

C3-121408	Applicable IP-CAN Type (R8 29.214)
					29.214	  CR-0239  (Rel-8) v8.12.0
					Source: Huawei

Decision: 		The document was Revised to C3-121684.

C3-121409	Applicable IP-CAN Type (R9 29.214)
					29.214	  CR-0240  (Rel-9) v9.9.0
					Source: Huawei

Decision: 		The document was Revised to C3-121685.

C3-121410	Applicable IP-CAN Type (R10 29.214)
					29.214	  CR-0241  (Rel-10) v10.6.0
					Source: Huawei

Decision: 		The document was Revised to C3-121686.

C3-121411	Applicable IP-CAN Type (R11 29.214)
					29.214	  CR-0242  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Revised to C3-121687.

C3-121684	Applicable IP-CAN Type (R8 29.214)
					29.214	  CR-0239  rev 1 (Rel-8) v8.12.0
					Source: Huawei

(Replaces C3-121408)

Decision: 		The document was Agreed.

C3-121685	Applicable IP-CAN Type (R9 29.214)
					29.214	  CR-0240  rev 1 (Rel-9) v9.9.0
					Source: Huawei

(Replaces C3-121409)

Decision: 		The document was Agreed.

C3-121686	Applicable IP-CAN Type (R10 29.214)
					29.214	  CR-0241  rev 1 (Rel-10) v10.6.0
					Source: Huawei

(Replaces C3-121410)

Decision: 		The document was Revised to C3-121717.

C3-121687	Applicable IP-CAN Type (R11 29.214)
					29.214	  CR-0242  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121411)

Decision: 		The document was Revised to C3-121718.

C3-121717	Applicable IP-CAN Type (R10 29.214)
					29.214	  CR-0241  rev 2 (Rel-10) v10.6.0
					Source: Huawei

(Replaces C3-121686)

Decision: 		The document was Agreed.

C3-121718	Applicable IP-CAN Type (R11 29.214)
					29.214	  CR-0242  rev 2 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121687)

Decision: 		The document was Agreed.

#### 8.14.4	- S9 interface (29.215)

### 8.15	Interworking between EPC and external PDNs [SAES-St3-intwk]

C3-121416	SGSN address when GnGp SGSN accesses to PGW (R8 29.061)
					29.061	  CR-0380  (Rel-8) v8.9.0
					Source: Huawei

Decision: 		The document was Revised to C3-121657.

C3-121417	SGSN address when GnGp SGSN accesses to PGW (R9 29.061)
					29.061	  CR-0381  (Rel-9) v9.9.0
					Source: Huawei

Decision: 		The document was Revised to C3-121658.

C3-121418	SGSN address when GnGp SGSN accesses to PGW (R10 29.061)
					29.061	  CR-0382  (Rel-10) v10.6.0
					Source: Huawei

Decision: 		The document was Revised to C3-121659.

C3-121419	SGSN address when GnGp SGSN accesses to PGW (R11 29.061)
					29.061	  CR-0383  (Rel-11) v11.1.0
					Source: Huawei

Decision: 		The document was Revised to C3-121660.

C3-121657	SGSN address when GnGp SGSN accesses to PGW (R8 29.061)
					29.061	  CR-0380  rev 1 (Rel-8) v8.9.0
					Source: Huawei

(Replaces C3-121416)

Decision: 		The document was Agreed.

C3-121658	SGSN address when GnGp SGSN accesses to PGW (R9 29.061)
					29.061	  CR-0381  rev 1 (Rel-9) v9.9.0
					Source: Huawei

(Replaces C3-121417)

Decision: 		The document was Agreed.

C3-121659	SGSN address when GnGp SGSN accesses to PGW (R10 29.061)
					29.061	  CR-0382  rev 1 (Rel-10) v10.6.0
					Source: Huawei

(Replaces C3-121418)

Decision: 		The document was Agreed.

C3-121660	SGSN address when GnGp SGSN accesses to PGW (R11 29.061)
					29.061	  CR-0383  rev 1 (Rel-11) v11.1.0
					Source: Huawei

(Replaces C3-121419)

Decision: 		The document was Agreed.

### 8.16	IMS inter-operator service interconnection interface [FBI2-IOPSI]

### 8.17	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

### 8.18	Interworking between User-to-User Signaling (UUS) and SIP [UUSIW]

### 8.19	Work Items related to TISPAN transfer

#### 8.19.1	- Maintenance of TISPAN R1 [MAINT_R1]

#### 8.19.2	- Maintenance of TISPAN R2 [MAINT_R2]

#### 8.19.3	- Documentation of TISPAN R1 and R2  in CT3 [REDOC_TIS-C3]

C3-121287	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0661  (Rel-8) v8.19.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121609.

C3-121288	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0662  (Rel-9) v9.10.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121610.

C3-121289	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0663  (Rel-10) v10.6.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121611.

C3-121290	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0664  (Rel-11) v11.3.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121612.

C3-121291	Correction of mapping MICD IDR
					29.163	  CR-0665  (Rel-8) v8.19.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121613.

C3-121292	Correction of mapping MICD IDR
					29.163	  CR-0666  (Rel-9) v9.10.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121614.

C3-121293	Correction of mapping MICD IDR
					29.163	  CR-0667  (Rel-10) v10.6.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121615.

C3-121294	Correction of mapping MICD IDR
					29.163	  CR-0668  (Rel-11) v11.3.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-121616.

C3-121398	PSTN XML schema Bearer Capability correction
					29.163	  CR-0678  (Rel-8) v8.19.0
					Source: Nokia Siemens Networks, Deutsche Telefom

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121643.

C3-121399	PSTN XML schema Bearer Capability correction
					29.163	  CR-0679  (Rel-9) v9.10.0
					Source: Nokia Siemens Networks, Deutsche Telefom

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121644.

C3-121400	PSTN XML schema Bearer Capability correction
					29.163	  CR-0680  (Rel-10) v10.6.0
					Source: Nokia Siemens Networks, Deutsche Telefom

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121645.

C3-121401	PSTN XML schema Bearer Capability correction
					29.163	  CR-0681  (Rel-11) v11.3.0
					Source: Nokia Siemens Networks, Deutsche Telefom

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121646.

C3-121447	XML schema defintion correction
					29.163	  CR-0682  (Rel-11) v11.3.0
					Source: Belgacom

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121608

C3-121448	XML schema defintion correction
					29.163	  CR-0683  (Rel-10) v10.6.0
					Source: Belgacom

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121607

C3-121449	XML schema defintion correction
					29.163	  CR-0684  (Rel-9) v9.10.0
					Source: Belgacom

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121606.

C3-121529	RTTI 29.658r8
					29.658	  CR-0016  (Rel-8) v8.5.0
					Source: Orange

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121621.

C3-121530	RTTI 29.658r9
					29.658	  CR-0017  (Rel-9) v9.1.0
					Source: Orange

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121622.

C3-121531	RTTI 29.658r10
					29.658	  CR-0018  (Rel-10) v10.1.0
					Source: Orange

Discussion:

The WI was changed to "REDOC_TIS-C3".

Decision: 		The document was Revised to C3-121623.

C3-121605	XML schema defintion correction
					29.163	  CR-0685  rev 1 (Rel-8) v8.19.0
					Source: Belgacom

(Replaces C3-121450)

Decision: 		The document was Revised to C3-121680.

C3-121606	XML schema defintion correction
					29.163	  CR-0684  rev 1 (Rel-9) v9.10.0
					Source: Belgacom

(Replaces C3-121449)

Discussion:

The category was changed to "A".

Decision: 		The document was Revised to C3-121681.

C3-121607	XML schema defintion correction
					29.163	  CR-0683  rev 1 (Rel-10) v10.6.0
					Source: Belgacom

(Replaces C3-121448)

Decision: 		The document was Revised to C3-121682.

C3-121608	XML schema defintion correction
					29.163	  CR-0682  rev 1 (Rel-11) v11.3.0
					Source: Belgacom

(Replaces C3-121447)

Decision: 		The document was Revised to C3-121683.

C3-121609	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0661  rev 1 (Rel-8) v8.19.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121287)

Decision: 		The document was Revised to C3-121676.

C3-121610	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0662  rev 1 (Rel-9) v9.10.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121288)

Decision: 		The document was Revised to C3-121677.

C3-121611	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0663  rev 1 (Rel-10) v10.6.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121289)

Decision: 		The document was Revised to C3-121678.

C3-121612	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0664  rev 1 (Rel-11) v11.3.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121290)

Decision: 		The document was Revised to C3-121679.

C3-121613	Correction of mapping MICD IDR
					29.163	  CR-0665  rev 1 (Rel-8) v8.19.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121291)

Discussion:

CT3 were waiting for CT1's decision and It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121614	Correction of mapping MICD IDR
					29.163	  CR-0666  rev 1 (Rel-9) v9.10.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121292)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121615	Correction of mapping MICD IDR
					29.163	  CR-0667  rev 1 (Rel-10) v10.6.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121293)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121616	Correction of mapping MICD IDR
					29.163	  CR-0668  rev 1 (Rel-11) v11.3.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121294)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121621	RTTI 29.658r8
					29.658	  CR-0016  rev 1 (Rel-8) v8.5.0
					Source: Orange

(Replaces C3-121529)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121622	RTTI 29.658r9
					29.658	  CR-0017  rev 1 (Rel-9) v9.1.0
					Source: Orange

(Replaces C3-121530)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121623	RTTI 29.658r10
					29.658	  CR-0018  rev 1 (Rel-10) v10.1.0
					Source: Orange

(Replaces C3-121531)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121643	PSTN XML schema Bearer Capability correction
					29.163	  CR-0678  rev 1 (Rel-8) v8.19.0
					Source: Nokia Siemens Networks, Deutsche Telefom

(Replaces C3-121398)

Decision: 		The document was Agreed.

C3-121644	PSTN XML schema Bearer Capability correction
					29.163	  CR-0679  rev 1 (Rel-9) v9.10.0
					Source: Nokia Siemens Networks, Deutsche Telefom

(Replaces C3-121399)

Decision: 		The document was Agreed.

C3-121645	PSTN XML schema Bearer Capability correction
					29.163	  CR-0680  rev 1 (Rel-10) v10.6.0
					Source: Nokia Siemens Networks, Deutsche Telefom

(Replaces C3-121400)

Decision: 		The document was Agreed.

C3-121646	PSTN XML schema Bearer Capability correction
					29.163	  CR-0681  rev 1 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks, Deutsche Telefom

(Replaces C3-121401)

Decision: 		The document was Agreed.

C3-121676	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0661  rev 2 (Rel-8) v8.19.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121609)

Decision: 		The document was Revised to C3-121738.

C3-121677	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0662  rev 2 (Rel-9) v9.10.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121610)

Decision: 		The document was Revised to C3-121739.

C3-121678	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0663  rev 2 (Rel-10) v10.6.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121611)

Decision: 		The document was Revised to C3-121740.

C3-121679	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0664  rev 2 (Rel-11) v11.3.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121612)

Decision: 		The document was Revised to C3-121741.

C3-121680	XML schema defintion correction
					29.163	  CR-0685  rev 2 (Rel-8) v8.19.0
					Source: Belgacom

(Replaces C3-121605)

Decision: 		The document was Agreed.

C3-121681	XML schema defintion correction
					29.163	  CR-0684  rev 2 (Rel-9) v9.10.0
					Source: Belgacom

(Replaces C3-121606)

Discussion:

Category was changed to "A".

Decision: 		The document was Agreed.

C3-121682	XML schema defintion correction
					29.163	  CR-0683  rev 2 (Rel-10) v10.6.0
					Source: Belgacom

(Replaces C3-121607)

Discussion:

Category was changed to "A".

Decision: 		The document was Agreed.

C3-121683	XML schema defintion correction
					29.163	  CR-0682  rev 2 (Rel-11) v11.3.0
					Source: Belgacom

(Replaces C3-121608)

Discussion:

Category was changed to "A".

Decision: 		The document was Agreed.

C3-121738	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0661  rev 3 (Rel-8) v8.19.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121676)

Decision: 		The document was Agreed.

C3-121739	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0662  rev 3 (Rel-9) v9.10.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121677)

Decision: 		The document was Agreed.

C3-121740	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0663  rev 3 (Rel-10) v10.6.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121678)

Decision: 		The document was Agreed.

C3-121741	Correction of mapping for COLP-TIP second-first identity
					29.163	  CR-0664  rev 3 (Rel-11) v11.3.0
					Source: Deutsche Telekom (Roland)

(Replaces C3-121679)

Decision: 		The document was Agreed.

#### 8.19.4	- Support of Overlap signalling [Overlap]

#### 8.19.5	- Stage 3 (CT3) of CWonIMS [CW_IMS]

#### 8.19.6	- Stage 3 (CT3) of [CCBS_CCNR]

### 8.20	Contributions on Common IMS related to 3GPP2 [REDOC_3GPP2]

### 8.21	Support of Service-Level Interworking for Messaging Services [MESSIW]

### 8.22	Enhancement of interworking between MTSI and Circuit Switched networks  [MTSI_eMHI]

### 8.23	Core Network Impacts for A-Interface Over IP [AoIP-CN]

### 8.24	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]

### 8.25	CAT solution for voice and video call in CS domain [CAT_SS]

### 8.26	Technical Enhancements and Improvements [TEI8]

### 8.27	Rel-8 contributions on other Work Items

## 9	Release 9

### 9.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 9.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-121520	Mapping between SIP Responses and ISUP Cause Values
					29.163	  CR-0609  rev 1 (Rel-9) v9.10.0
					Source: Orange

Decision: 		The document was Revised to C3-121624.

C3-121521	Mapping between SIP Responses and ISUP Cause Values
					29.163	  CR-0610  rev 1 (Rel-10) v10.6.0
					Source: Orange

Decision: 		The document was Revised to C3-121625.

C3-121522	Mapping between SIP Responses and ISUP Cause Values
					29.163	  CR-0611  rev 1 (Rel-11) v11.3.0
					Source: Orange

Decision: 		The document was Revised to C3-121626.

C3-121526	Privacy 29.163r9
					29.163	  CR-0655  rev 2 (Rel-9) v9.10.0
					Source: Orange

Decision: 		The document was Revised to C3-121640.

C3-121527	Privacy 29.163r10
					29.163	  CR-0656  rev 2 (Rel-10) v10.6.0
					Source: Orange

Decision: 		The document was Revised to C3-121641.

C3-121528	Privacy 29.163r11
					29.163	  CR-0657  rev 2 (Rel-11) v11.3.0
					Source: Orange

Decision: 		The document was Revised to C3-121642.

C3-121624	Mapping between SIP Responses and ISUP Cause Values
					29.163	  CR-0609  rev 2 (Rel-9) v9.10.0
					Source: Orange

(Replaces C3-121520)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121625	Mapping between SIP Responses and ISUP Cause Values
					29.163	  CR-0610  rev 2 (Rel-10) v10.6.0
					Source: Orange

(Replaces C3-121521)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121626	Mapping between SIP Responses and ISUP Cause Values
					29.163	  CR-0611  rev 2 (Rel-11) v11.3.0
					Source: Orange

(Replaces C3-121522)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121640	Privacy 29.163r9
					29.163	  CR-0655  rev 3 (Rel-9) v9.10.0
					Source: Orange

(Replaces C3-121526)

Discussion:

it was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121641	Privacy 29.163r10
					29.163	  CR-0656  rev 3 (Rel-10) v10.6.0
					Source: Orange

(Replaces C3-121527)

Discussion:

it was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121642	Privacy 29.163r11
					29.163	  CR-0657  rev 3 (Rel-11) v11.3.0
					Source: Orange

(Replaces C3-121528)

Discussion:

it was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121688	LS out LS on Mapping between SIP Responses and ISUP Cause Values
					Source: Orange

Decision: 		The document was Revised to C3-121714.

C3-121714	LS on Mapping between SIP Responses and ISUP Cause Values
					Source: Orange

(Replaces C3-121688)

Abstract:

1. Overall Description:

In the past 3GPP TSG CT WG3 (CT3) had a fruitful cooperation with i3Forum to enhance the mapping between SIP Responses and ISUP Cause Values in 3GPP TS 29.163.

During recent meetings CT3 has discussed the technical aspects of mapping between SIP Responses and ISUP Cause Values. CT3 has considered but not yet agreed the attached CR.

Before agreeing this document CT3 would welcome feedback of i3Forum.

2. Actions:

To i3Forum group.

ACTION: 	I3Forum is invited to kindly provide feedback on the proposed changes.

Decision: 		The document was Approved.

### 9.3	Protocol impact from providing IMS services via fixed broadband [FBI]

### 9.4	MBMS [MBMS]

### 9.5	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 9.6	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

### 9.7	PCC aspects of SAE [SAES-St3-PCC]

### 9.8	Reserved

### 9.9	Reserved

### 9.10	Reserved

### 9.11	Reserved

### 9.12	Reserved

### 9.13	Reserved

### 9.14	Reserved

### 9.15	Reserved

### 9.16	CS-IBCF and CS-TrGW definition in 3GPP specifications [CS-IBCF]

### 9.17	Interconnection Border Control Function (IBCF) – Transition Gateway (TrGW); Ix interface, Stage 3 [IMS_IBCF]

### 9.18	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 9.19	Operational Description of the Inter-IMS NNI   [II-NNI]

C3-121299	Correction on the description of "g.3gpp.crs"
					29.165	  CR-0428  (Rel-9) v9.11.0
					Source: NTT

Decision: 		The document was Agreed.

C3-121300	Correction on the description of "g.3gpp.crs"
					29.165	  CR-0429  (Rel-10) v10.8.0
					Source: NTT

Decision: 		The document was Agreed.

C3-121301	Correction on the description of "g.3gpp.crs"
					29.165	  CR-0430  (Rel-11) v11.3.0
					Source: NTT

Decision: 		The document was Agreed.

C3-121302	Correction on the description of "application/vnd.etsi.mcid+xml" MIME body
					29.165	  CR-0431  (Rel-9) v9.11.0
					Source: NTT

Decision: 		The document was Agreed.

C3-121303	Correction on the description of "application/vnd.etsi.mcid+xml" MIME body
					29.165	  CR-0432  (Rel-10) v10.8.0
					Source: NTT

Decision: 		The document was Agreed.

C3-121304	Correction on the description of "application/vnd.etsi.mcid+xml" MIME body
					29.165	  CR-0433  (Rel-11) v11.3.0
					Source: NTT

Decision: 		The document was Agreed.

C3-121312	Correcting reference
					29.165	  CR-0438  (Rel-9) v9.11.0
					Source: NTT

Decision: 		The document was Revised to C3-121587.

C3-121313	Correcting reference
					29.165	  CR-0439  (Rel-10) v10.8.0
					Source: NTT

Decision: 		The document was Revised to C3-121588.

C3-121314	Correcting reference
					29.165	  CR-0440  (Rel-11) v11.3.0
					Source: NTT

Decision: 		The document was Revised to C3-121589.

C3-121340	Reference update: draft-kaplan-dispatch-session-id
					29.165	  CR-0446  (Rel-9) v9.11.0
					Source: Ericsson

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121341	Reference update: draft-kaplan-dispatch-session-id
					29.165	  CR-0447  (Rel-10) v10.8.0
					Source: Ericsson

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121342	Reference update: draft-kaplan-dispatch-session-id
					29.165	  CR-0448  (Rel-11) v11.3.0
					Source: Ericsson

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121587	Correcting reference
					29.165	  CR-0438  rev 1 (Rel-9) v9.11.0
					Source: NTT

(Replaces C3-121312)

Decision: 		The document was Agreed.

C3-121588	Correcting reference
					29.165	  CR-0439  rev 1 (Rel-10) v10.8.0
					Source: NTT

(Replaces C3-121313)

Decision: 		The document was Agreed.

C3-121589	Correcting reference
					29.165	  CR-0440  rev 1 (Rel-11) v11.3.0
					Source: NTT

(Replaces C3-121314)

Decision: 		The document was Agreed.

### 9.20	Support for IMS Emergency Calls over GPRS and EPS [IMS_EMER_GPRS_EPS]

### 9.21	PCC Enhancements [PCC-Enh]

### 9.22	Completion of IMS Restoration Procedures [eIMS_RP]

### 9.23	CT1 aspects of SRVCC support for IMS Emergency Calls [IMS_EMER_GPRS_EPS-SRVCC]

### 9.24	IMS Media Plane Security [MEDIASEC_CORE]

### 9.25	Technical Enhancements and Improvements [TEI9]

### 9.26	Rel-9 contributions on other work items

## 10	Release 10

### 10.1	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 10.2	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 10.3	PCC aspects of SAE [SAES-St3-PCC]

### 10.4	Interworking between EPC and external PDNs [SAES-St3-intwk]

### 10.5	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 10.6	PCC Enhancements [PCC-Enh]

C3-121420	Removal of Maximum MBR APN-AMBR (R10 29.212)
					29.212	  CR-0884  (Rel-10) v10.7.0
					Source: Huawei

Discussion:

Technically agreed, but it has dependancy on SA2's CR.

Decision: 		The document was Revised to C3-121723.

C3-121421	Removal of Maximum MBR APN-AMBR (R11 29.212)
					29.212	  CR-0885  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Revised to C3-121719.

C3-121719	Removal of Maximum MBR APN-AMBR (R11 29.212)
					29.212	  CR-0885  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121421)

Decision: 		The document was Agreed.

C3-121723	Removal of Maximum MBR APN-AMBR (R10 29.212)
					29.212	  CR-0884  rev 1 (Rel-10) v10.7.0
					Source: Huawei

(Replaces C3-121420)

Discussion:

WI was changed to "PCC-Enh".

Decision: 		The document was Agreed.

### 10.7	Reserved

### 10.8	Reserved

### 10.9	Reserved

### 10.10	Reserved

### 10.11	Reserved

### 10.12	Reserved

### 10.13	Reserved

### 10.14	Reserved

### 10.15	Reserved

### 10.16	CPM-SMS Interworking [CPM-SMS]

### 10.17	Optimal Media Routeing [OMR]

### 10.18	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]

C3-121297	P-Refused-URI-List header field
					29.165	  CR-0426  (Rel-10) v10.8.0
					Source: NTT

Decision: 		The document was Agreed.

C3-121298	P-Refused-URI-List header field
					29.165	  CR-0427  (Rel-11) v11.3.0
					Source: NTT

Decision: 		The document was Revised to C3-121630.

C3-121305	Correcting minor errors
					29.165	  CR-0434  (Rel-11) v11.3.0
					Source: NTT

Discussion:

The WI was changed to "II-NNI2" and category to "A"

Decision: 		The document was Revised to C3-121594.

C3-121307	Clarification on the SDP rules for transporting media streams with TCP
					29.165	  CR-0436  (Rel-10) v10.8.0
					Source: OKI, NTT

Decision: 		The document was Revised to C3-121631.

C3-121308	Clarification on the SDP rules for transporting media streams with TCP
					29.165	  CR-0437  (Rel-11) v11.3.0
					Source: OKI, NTT

Decision: 		The document was Revised to C3-121632.

C3-121343	draft-ietf-sipcore-proxy-feature: reference update and technical changes
					29.165	  CR-0449  (Rel-10) v10.8.0
					Source: Ericsson

Discussion:

This CR was technically agreed, however it needed to be check with CT1's CR for terminology.

Decision: 		The document was Revised to C3-121633.

C3-121344	draft-ietf-sipcore-proxy-feature: reference update and technical changes
					29.165	  CR-0450  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121634.

C3-121351	Feature-Caps added to trust domain - CT CR CORRELATION NEEDED
					29.165	  CR-0452  (Rel-10) v10.8.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121352	Feature-Caps added to trust domain - CT CR CORRELATION NEEDED
					29.165	  CR-0453  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121357	IUT reference update
					29.165	  CR-0458  (Rel-10) v10.8.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121358	IUT reference update
					29.165	  CR-0459  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121637.

C3-121359	MIME body name update
					29.165	  CR-0460  (Rel-10) v10.8.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121360	MIME body name update
					29.165	  CR-0461  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121635.

C3-121361	CDIV corrections
					29.165	  CR-0462  (Rel-10) v10.8.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121362	CDIV corrections
					29.165	  CR-0463  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121363	Missing the Event header in MWI
					29.165	  CR-0464  (Rel-10) v10.8.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121364	Missing the Event header in MWI
					29.165	  CR-0465  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121636.

C3-121365	Event header field missing in CC services
					29.165	  CR-0466  (Rel-10) v10.8.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121366	Event header field missing in CC services
					29.165	  CR-0467  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121367	Correcting error in basic PS to CS SRVCC
					29.165	  CR-0468  (Rel-10) v10.8.0
					Source: Ericsson

Discussion:

CR was withdrawn before meeting by request from source company.

Decision: 		The document was Withdrawn.

C3-121368	Correcting error in basic PS to CS SRVCC
					29.165	  CR-0469  (Rel-11) v11.3.0
					Source: Ericsson

Discussion:

CR was withdrawn before meeting by request from source company.

Decision: 		The document was Withdrawn.

C3-121594	Correcting minor errors
					29.165	  CR-0434  rev 1 (Rel-11) v11.3.0
					Source: NTT

(Replaces C3-121305)

Discussion:

Category changed to "A", WI changed to "II-NNI2".

Decision: 		The document was Agreed.

C3-121596	Correcting minor errors
					29.165	  CR-0471  (Rel-10) v10.8.0
					Source: NTT

Discussion:

The WI was changed to "II-NNI2" and category to "F".

Decision: 		The document was Agreed.

C3-121630	P-Refused-URI-List header field
					29.165	  CR-0427  rev 1 (Rel-11) v11.3.0
					Source: NTT

(Replaces C3-121298)

Discussion:

This CR was technically agreed.

Decision: 		The document was Agreed.

C3-121631	Clarification on the SDP rules for transporting media streams with TCP
					29.165	  CR-0436  rev 1 (Rel-10) v10.8.0
					Source: OKI, NTT

(Replaces C3-121307)

Decision: 		The document was Agreed.

C3-121632	Clarification on the SDP rules for transporting media streams with TCP
					29.165	  CR-0437  rev 1 (Rel-11) v11.3.0
					Source: OKI, NTT

(Replaces C3-121308)

Decision: 		The document was Agreed.

C3-121633	draft-ietf-sipcore-proxy-feature: reference update and technical changes
					29.165	  CR-0449  rev 1 (Rel-10) v10.8.0
					Source: Ericsson

(Replaces C3-121343)

Decision: 		The document was Agreed.

C3-121634	draft-ietf-sipcore-proxy-feature: reference update and technical changes
					29.165	  CR-0450  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121344)

Discussion:

MCC need to identify CT4 CR to complete the implementation.

Decision: 		The document was Agreed.

C3-121635	MIME body name update
					29.165	  CR-0461  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121360)

Decision: 		The document was Agreed.

C3-121636	Missing the Event header in MWI
					29.165	  CR-0465  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121364)

Decision: 		The document was Agreed.

C3-121637	IUT reference update
					29.165	  CR-0459  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121358)

Decision: 		The document was Agreed.

### 10.19	Call Completion Not Logged in [CCNL]

### 10.20	IP Flow Mobility and WLAN offload (Stage 3) [IFOM-CT]

### 10.21	Enabling Coder Selection and Rate Adaption for UTRAN and E-UTRAN for Load Adaptive Applications, CN impacts [ECSRA_LAA-CN]

#### 10.21.1	-  Packet Core impacts

#### 10.21.2	-  IMS/CS impacts

### 10.22	S2b Mobility based on GTP [SMOG-St3]

### 10.23	CT aspects of Enhancements for Multimedia Priority Service [eMPS-CN]

### 10.24	PCRF failure and restoration [PCRF-FR]

### 10.25	CT aspects of Multi Access PDN Connectivity  [MAPCON-St3]

### 10.26	CT3 Aspects of Policy Enhancements for Sponsored Connectivity and Coherent Access to Policy related Data Bases [PEST-CT3]

### 10.27	Dynamic View of Headers in Messages for II-NNI [NNI_DV]

### 10.28	CS and IMS Interworking for CAT early session model [CIIC_ES]

### 10.29	Stage 3 for Network Improvements for Machine Type Communications [NIMTC]

### 10.30	Technical Enhancements and Improvements [TEI10]

### 10.31	Rel-10 contributions on other Work Items

## 11	Release 11

### 11.1	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-121349	Request "Connected Line Identity" for TIP
					29.163	  CR-0677  (Rel-11) v11.3.0
					Source: Ericsson

Discussion:

The category (A to F) and agenda (to 11.2) was changed because 1346~1348 were withdrawn before meeting.

Decision: 		The document was Merged into C3-121620.

### 11.2	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 11.3	Policy Control and Charging [PCC]

C3-121434	Reporting multiple events to AF (R11 29.214)
					29.214	  CR-0245  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Revised to C3-121665.

C3-121665	Reporting multiple events to AF (R11 29.214)
					29.214	  CR-0245  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121434)

Decision: 		The document was Revised to C3-121721.

C3-121721	Reporting multiple events to AF (R11 29.214)
					29.214	  CR-0245  rev 2 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121665)

Discussion:

WI was changed to "PCC".

Decision: 		The document was Agreed.

### 11.4	Interworking between EPC and external PDNs [SAES-St3-intwk]

### 11.5	PCC aspects of SAE [SAES-St3-PCC]

C3-121369	Incorrect references
					29.215	  CR-0255  (Rel-11) v11.5.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121661.

C3-121370	Additional input to obtain GBR values
					29.213	  CR-0425  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Merged with C3-121428 into C3-121670.

C3-121427	Serving network limitation for PCC Rule Authorization (R11 29.212)
					29.212	  CR-0888  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Revised to C3-121671.

C3-121428	Serving network limitation for PCC Rule Authorization (R11 29.213)
					29.213	  CR-0428  (Rel-11) v11.3.0
					Source: Huawei

Decision: 		The document was Merged with C3-121370 into C3-121670.

C3-121429	Supported feature for R11 (R11 29.212)
					29.212	  CR-0889  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Merged with C3-121509 into C3-121662.

C3-121430	Supported feature for R11 (R11 29.215)
					29.215	  CR-0261  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Merged with C3-121510 into C3-121663.

C3-121661	Incorrect references
					29.215	  CR-0255  rev 1 (Rel-11) v11.5.0
					Source: Ericsson

(Replaces C3-121369)

Decision: 		The document was Agreed.

C3-121662	Supported feature for R11 (R11 29.212)
					29.212	  CR-0889  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121429)

Decision: 		The document was Agreed.

C3-121663	Supported feature for R11 (R11 29.215)
					29.215	  CR-0261  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121430)

Decision: 		The document was Agreed.

C3-121670	Additional input to obtain GBR values
					29.213	  CR-0425  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121370)

Decision: 		The document was Agreed.

C3-121671	Serving network limitation for PCC Rule Authorization (R11 29.212)
					29.212	  CR-0888  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121427)

Decision: 		The document was Revised to C3-121720.

C3-121720	Serving network limitation for PCC Rule Authorization (R11 29.212)
					29.212	  CR-0888  rev 2 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121671)

Decision: 		The document was Agreed.

### 11.6	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

C3-121386	Encoding of Absolute Time of MBMS Data Transfer
					29.061	  CR-0379  (Rel-11) v11.1.0
					Source: Alcatel-Lucent, Ericsson, Verizon Wireless

Decision: 		The document was Agreed.

### 11.7	PCC Enhancements [PCC-Enh]

### 11.8	Optimal Media Routeing [OMR]

### 11.9	Dynamic View of Headers in Messages for II-NNI [NNI_DV]

### 11.10	Reserved

### 11.11	Reserved

### 11.12	Reserved

### 11.13	Reserved

### 11.14	Reserved

### 11.15	Reserved

### 11.16	Reserved

C3-121285	29.212 header correction to remove Sd
					29.212	  CR-0870  (Rel-11) v11.5.0
					Source: Allot Communications

Discussion:

It needed to roll back to previous title and was agreed internally. The related CR will be provided only if the new proposed generic title is not approved in the plenary.

Decision: 		The document was Agreed internally.

C3-121286	TS 29.212 header change considerations
					Source: Allot Communications

Discussion:

Conclusion of NM saga is near! :)

Decision: 		The document was Noted.

C3-121295	ADC Rule mapping
					29.212	  CR-0871  (Rel-11) v11.5.0
					Source: Deutsche Telekom (Roland)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121431	Correction of redirection functionality (R11 29.212)
					29.212	  CR-0890  (Rel-11) v11.5.0
					Source: Huawei, Allot Communications

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121491	Clarification of the redirection function
					29.212	  CR-0899  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Revised to C3-121583.

C3-121540	Info on TS 29.212 title change
					Source: CT3 Chairman

Discussion:

This Information sheet was produced before the meeting by the request of CT3 Chairman. CT3 agreed to have a generic tiltle for TS 29.212 from Rel-11 onwards. The Updating references in the related specifications have to be completed in this plenary cycle.

CT3 actions (Allot Communications / Juniper Networks)

- Agree CR to introduce a generic title for Rel-11

- Agree CRs to align the reference lists in CT3 specs.

Company action (Alla has volunteered to do this):

- Submit CR pack to CT plenary to align the references in all the other CT WG  specs

- Submit CR pack to SA plenary to align the references in all the SA WG specs

And no reply LS to CT needed.

Possible new titles are :

Possible new titles:

- “Policy and Charging Control (PCC)”

- “Reference Points for Policy and Charging Control (PCC) of  Core Network Entities”

- “Reference Points for Policy and Charging Control (PCC)”

- "Policy and Charging Control (PCC) Reference Points"

Option 4 was agreed, e.g. since it excludes contents of 29.213.

Dr. Adrian Neal (from VODAFONE) will trigger discussion on the mailing list for having guidelines to tell which reference points shoud be added to the same specification in the future.

Decision: 		The document was Noted.

C3-121581	LS out LS on the redirection of functionality of SAPP
					Source: Huawei

Abstarct:

1. Overall Description:

To implement the SA2 requirement in S2-122408, CT3 has discussed the redirection functionality of SAPP and has the following questions to ask SA2:

In the absence of redirect destination information in an ADC rule with redirection enabled, whether redirection destination address can be locally configured in the PCEF/TDF?

If redirection destination address cannot be locally configured in the PCEF/TDF and the PCRF does not provide the redirection destination address in the ADC rule with redirection enabled, should the PCEF/TDF report an error to the PCRF that the redirection ADC rule cannot be enforced?

c)	How the redirection address is obtained for the predefined ADC rules?

2. Actions:

To SA2 group.

ACTION:

CT3 kindly ask SA2 to provide the answer to clarify the above questions.

Decision: 		The document was Approved.

C3-121582	LS out LS on Charging Issues regading PCC and ADC rules
					Source: Deutsche Telekom

Abstarct:

1. Overall Description:

3GPP TS 23.203 Specification section 6.2.2.1 indicates that “For PCEF enhanced with ADC, PCEF shall first enforce the PCC rules and then the ADC rules in the uplink direction. In the downlink direction, the ADC rules shall be enforced on the traffic before the PCC rules are applied.”

CT3 has noticed that there are concerns over charging accuracy that, as a result of this requirement, policy enforcement with an ADC rule may cause the uplink packets to be charged wrongly, e.g. when an ADC rule causes the uplink packets to be dropped.

On the other hand, in the same clause, it is stated “A PCEF shall ensure that an IP packet, which is discarded at the PCEF as a result from policy enforcement or flow based charging is neither reported for offline charging nor cause credit consumption for online charging”.  CT3 interprets that to state that an IP packet that is discarded at the PCEF due to policy enforcement with an ADC rule falls under the same requirement, also for the uplink direction.

CT3 has also identified that the same situation may occur for the use of a TDF and that CT3 cannot identify any method to fulfill the requirement derived in the previous paragraph for that case.

2. Actions:

To SA2 group.

ACTION: 	CT3 asks SA2 kindly to clarify whether the exemption from charging for packets that the PCEF discards is also valid for the case the ADC rule causes the packet to be discarded. In that case it is appreciated if SA2 could, provide clarifications and possibly corrections in the aforementioned specification to ensure the interactions between ADC and PCC allow consistent charging.

CT3 kindly asks SA2 to clarify whether the same requirement applies for the case of a TDF performing ADC rule enforcement and, if so, define how to fulfill the requirement.

Decision: 		The document was Approved.

C3-121583	Clarification of the redirection function
					29.212	  CR-0899  rev 1 (Rel-11) v11.5.0
					Source: ZTE

(Replaces C3-121491)

Decision: 		The document was Agreed.

### 11.17	CT3 aspects of QoS Control Based on Subscriber Spending Limits  [QoS_SSL-CT3]

C3-121311	Time Based Sy Controls
					29.219	  CR-0006  (Rel-11) v11.1.0
					Source: Openet

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121433	Clean-up for spending limit description (R11 29.219)
					29.219	  CR-0007  (Rel-11) v11.1.0
					Source: Huawei

Decision: 		The document was Agreed.

### 11.18	USSD Simulation Service in IMS-stage 3 [USSI]

C3-121353	Unstructured Supplementary Service Data (USSD)
					29.165	  CR-0454  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121593.

C3-121593	Unstructured Supplementary Service Data (USSD)
					29.165	  CR-0454  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121353)

Decision: 		The document was Revised to C3-121695.

C3-121695	Unstructured Supplementary Service Data (USSD)
					29.165	  CR-0454  rev 2 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121593)

Decision: 		The document was Revised to C3-121742.

C3-121742	Unstructured Supplementary Service Data (USSD)
					29.165	  CR-0454  rev 3 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121695)

Decision: 		The document was Agreed.

### 11.19	Single Radio Video Call Continuity       [vSRVCC-CT]

#### 11.19.1	IMS-related

#### 11.19.2	PCC-related

### 11.20	Further improvement of usability of II-NNI specification for inter-connection [NNI_OI]

C3-121296	Removal of editor's note in Annex C
					29.165	  CR-0425  (Rel-11) v11.3.0
					Source: NTT

Decision: 		The document was Revised to C3-121590.

C3-121306	Managing the maximum length of a SIP message body
					29.165	  CR-0435  (Rel-11) v11.3.0
					Source: Fujitsu, NTT

Decision: 		The document was Revised to C3-121591.

C3-121590	Removal of editor's note in Annex C
					29.165	  CR-0425  rev 1 (Rel-11) v11.3.0
					Source: NTT, Ericsson

(Replaces C3-121296)

Decision: 		The document was Agreed.

C3-121591	Managing the maximum length of a SIP message body
					29.165	  CR-0435  rev 1 (Rel-11) v11.3.0
					Source: Fujitsu, NTT

(Replaces C3-121306)

Decision: 		The document was Revised to C3-121690.

C3-121690	Managing the maximum length of a SIP message body
					29.165	  CR-0435  rev 2 (Rel-11) v11.3.0
					Source: Fujitsu, NTT

(Replaces C3-121591)

Decision: 		The document was Agreed.

### 11.21	IMS Stage-3 IETF Protocol Alignment          [IMSProtoc5]

C3-121356	Editorial corrections
					29.165	  CR-0457  (Rel-11) v11.3.0
					Source: Ericsson

Discussion:

The category was changed F to D by request from source company.

Decision: 		The document was Revised to C3-121595.

C3-121595	Editorial corrections
					29.165	  CR-0457  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121356)

Decision: 		The document was Agreed.

### 11.22	CT aspects of Single Radio Voice Call Continuity from UTRAN/GERAN to E-UTRAN/HSPA [rSRVCC-CT]

C3-121492	Support of rSRVCC in Gx
					29.212	  CR-0900  (Rel-11) v11.5.0
					Source: ZTE

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

#### 11.22.1	IMS/CS related docs

C3-121355	CS to PS access transfer
					29.165	  CR-0456  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121597.

C3-121597	CS to PS access transfer
					29.165	  CR-0456  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121355)

Decision: 		The document was Revised to C3-121696.

C3-121696	CS to PS access transfer
					29.165	  CR-0456  rev 2 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121597)

Decision: 		The document was Revised to C3-121743.

C3-121743	CS to PS access transfer
					29.165	  CR-0456  rev 3 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121696)

Decision: 		The document was Revised to C3-121757.

C3-121757	CS to PS access transfer
					29.165	  CR-0456  rev 4 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121743)

Decision: 		The document was Agreed.

#### 11.22.2	Packet Core related docs

C3-121422	Discussion on PCC support for rSRVCC
					Source: Huawei

Decision: 		The document was Noted.

C3-121423	PCC support for rSRVCC (R11 29.212)
					29.212	  CR-0886  (Rel-11) v11.5.0
					Source: Huawei

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121424	PCC support for rSRVCC (R11 29.214)
					29.214	  CR-0243  (Rel-11) v11.5.0
					Source: Huawei

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121584	LS out LS on PCC support for rSRVCC
					Source: Huawei

Decision: 		The document was Approved.

### 11.23	Stage 3 for System Improvements to Machine-Type Communications [SIMTC-Reach]

C3-121309	MTC-IWF Load Control
					Source: Juniper Networks

Decision: 		The document was Revised to C3-121558.

C3-121310	MTC-IWF Discovery
					Source: Juniper Networks

Decision: 		The document was Revised to C3-121559.

C3-121325	Tsp interface security procedures
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121560.

C3-121329	Tsp Reference numbrt
					Source: Nokia Siemens Networks

Decision: 		The document was Merged with C3-121436 into C3-121561.

C3-121334	Revised WID for Stage 3 for System Improvements to Machine-Type Communications
					Source: Ericsson

Discussion:

No impact on PCC identified for Rel-11 so it needed to be removed.

Decision: 		The document was Revised to C3-121562.

C3-121379	Alignment of Diameter AVPs between CT3 and CT4
					Source: Ericsson, Acision

Decision: 		The document was Revised to C3-121563.

C3-121380	Correction to subclause references
					Source: Ericsson, Acision

Decision: 		The document was Agreed.

C3-121381	Removal of Editor's Note: External-Id is defined by 3GPP TSG CT WG4 and will be referenced when TS on S6a is available to be referenced.
					Source: Ericsson, Acision

Discussion:

C3-121438 was merged into this.

Decision: 		The document was Revised to C3-121564.

C3-121382	Removal of Report AVP.
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121383	Tsp interface security
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-121384	Removal of editors note, It is for further study if the structure of the procedures is reasonably future proof.
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121385	Removal of editors note, It is for further study if Diameter Base Protocol AVPs, Redirect-Host, Redirect-Host-Usage, Redirect-Max-Cache-Time and Origin-State-Id are needed.
					Source: Ericsson, Acision

Decision: 		The document was Agreed.

C3-121435	Clarification of Tsp routing (29.368)
					Source: Huawei, HiSilicon

Decision: 		The document was Merged with C3-121559 into C3-121565.

C3-121436	Reference number (29.368)
					Source: Huawei, HiSilicon

Decision: 		The document was Merged with C3-121329 into C3-121561.

C3-121437	External identifier (29.368)
					Source: Huawei, HiSilicon

Decision: 		The document was Merged into C3-121381.

C3-121515	External ID for SIMTC
					29.061	  CR-0384  (Rel-11) v11.1.0
					Source: Nokia Siemens Networks

Discussion:

The lucky number winner! Mr.Juha Rasanen will receive some prize from MCC in the next meeting.

Decision: 		The document was Revised to C3-121567.

C3-121533	Tsp Error Scenarios
					Source: Acision

Decision: 		The document was Revised to C3-121573.

C3-121534	Tsp Explicit SCS-ID
					Source: Acision

Decision: 		The document was Revised to C3-121574.

C3-121558	MTC-IWF Load Control
					Source: Juniper Networks

(Replaces C3-121309)

Decision: 		The document was Revised to C3-121566.

C3-121559	MTC-IWF Discovery
					Source: Juniper Networks

(Replaces C3-121310)

Decision: 		The document was Merged with C3-121435 into C3-121565.

C3-121560	Tsp interface security procedures
					Source: Nokia Siemens Networks

(Replaces C3-121325)

Decision: 		The document was Agreed.

C3-121561	Tsp Reference numbrt
					Source: Nokia Siemens Networks

(Replaces C3-121329)

Decision: 		The document was Agreed.

C3-121562	Revised WID for Stage 3 for System Improvements to Machine-Type Communications
					Source: Ericsson

(Replaces C3-121334)

Decision: 		The document was Endorsed.

C3-121563	Alignment of Diameter AVPs between CT3 and CT4
					Source: Ericsson, Acision

(Replaces C3-121379)

Decision: 		The document was Agreed.

C3-121564	Removal of Editor's Note: External-Id is defined by 3GPP TSG CT WG4 and will be referenced when TS on S6a is available to be referenced.
					Source: Ericsson, Acision, Huawei, HiSilicon

(Replaces C3-121381)

Discussion:

Huawei, HiSilicon were added to source company.

Decision: 		The document was Agreed.

C3-121565	Clarification of Tsp routing (29.368)
					Source: Huawei, HiSilicon, Juniper Networks

(Replaces C3-121435)

Decision: 		The document was Revised to C3-121725.

C3-121566	MTC-IWF Load Control
					Source: Juniper Networks

(Replaces C3-121558)

Decision: 		The document was Revised to C3-121598.

C3-121567	External ID for SIMTC
					29.061	  CR-0384  rev 1 (Rel-11) v11.1.0
					Source: Nokia Siemens Networks

(Replaces C3-121515)

Decision: 		The document was Revised to C3-121576.

C3-121573	Tsp Error Scenarios
					Source: Acision

(Replaces C3-121533)

Decision: 		The document was Agreed.

C3-121574	Tsp Explicit SCS-ID
					Source: Acision

(Replaces C3-121534)

Decision: 		The document was Agreed.

C3-121576	External ID for SIMTC
					29.061	  CR-0384  rev 2 (Rel-11) v11.1.0
					Source: Nokia Siemens Networks

(Replaces C3-121567)

Decision: 		The document was Revised to C3-121726.

C3-121598	MTC-IWF Load Control
					Source: Juniper Networks, Openet, Ericsson

(Replaces C3-121566)

Decision: 		The document was Agreed.

C3-121725	Clarification of Tsp routing (29.368)
					Source: Huawei, HiSilicon, Juniper Networks

(Replaces C3-121565)

Decision: 		The document was Agreed.

C3-121726	External ID for SIMTC
					29.061	  CR-0384  rev 3 (Rel-11) v11.1.0
					Source: Nokia Siemens Networks

(Replaces C3-121576)

Decision: 		The document was Agreed.

C3-121763	TS 29.368 v 1.1.0
					Source: Ericsson

Discussion:

It will be provided by Mr.Sven-ove Emanuelsson (from Ericsson) at the lease Friday 17th August and submitted to the plenary for approval after MCC's checking and updating for editorial improvements.

Decision: 		The document was [not addressed].

C3-121764	Presentation sheet for TS 29.368 v 1.1.0
					Source: Ericsson

Discussion:

It will be provided by Mr.Sven-ove Emanuelsson (from Ericsson) at the lease Friday 17th August.

Decision: 		The document was [not addressed].

### 11.24	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block I [BBAI_BBI-CT]

C3-121371	BBAI related Event Triggers completion
					29.212	  CR-0872  (Rel-11) v11.5.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121372	APN support in S9 and S9a
					29.215	  CR-0256  (Rel-11) v11.5.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121373	PCRF selection by BPCF
					29.213	  CR-0426  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121546.

C3-121374	Completion of S9 and S9a procedures
					29.215	  CR-0257  (Rel-11) v11.5.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121547.

C3-121376	Inclusion of ePDG/PGW IP Address in Gx/Gxx procedures
					29.212	  CR-0873  (Rel-11) v11.5.0
					Source: Ericsson

Decision: 		The document was Merged with C3-121438 into C3-121549.

C3-121378	QoS info in S9a session establishment response 
					29.215	  CR-0258  (Rel-11) v11.5.0
					Source: Ericsson

Discussion:

The category should be changed to "F".

Decision: 		The document was Revised to C3-121548.

C3-121388	Correction of AVPs for BBAI in case of EPC routed scenario
					29.215	  CR-0260  (Rel-11) v11.5.0
					Source: Alcatel-Lucent, Ericsson, ZTE

Decision: 		The document was Agreed.

C3-121438	Available APN for Gateway Control Session Establishment (R11 29.212)
					29.212	  CR-0892  (Rel-11) v11.5.0
					Source: Huawei

Discussion:

This CR was merged with C3-121376(merger) into C3-121549.

Decision: 		The document was Merged with C3-121376 into C3-121549.

C3-121439	Definition of case 1, case 2a and case 2b (R11 29.212)
					29.212	  CR-0893  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Revised to C3-121550.

C3-121440	Definition of case 1, case 2a and case 2b (R11 29.215)
					29.215	  CR-0262  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Revised to C3-121551.

C3-121441	Transport of ePDG or PGW IP address over S9 (R11 29.215)
					29.215	  CR-0263  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Revised to C3-121552.

C3-121442	V-PCRF-Initiated IP-CAN Session Modification for EPC routed traffic (R11 29.213)
					29.213	  CR-0429  (Rel-11) v11.3.0
					Source: Huawei

Decision: 		The document was Agreed.

C3-121493	Correction to the scope of BBAI annex
					29.212	  CR-0901  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Agreed.

C3-121494	Including the ePDG address and P-GW address on Gx and Gxx
					29.212	  CR-0902  (Rel-11) v11.5.0
					Source: ZTE

Discussion:

Offline discussion offered.

Decision: 		The document was Revised to C3-121672.

C3-121495	Including the UDP-Source-Port in the Qos-Rule-Install
					29.212	  CR-0903  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Agreed.

C3-121496	Unsolicited application reporting for BBAI
					29.212	  CR-0904  (Rel-11) v11.5.0
					Source: ZTE, Ericsson

Decision: 		The document was Agreed.

C3-121497	Remove the IP-CAN type and RAT Type from the Gx/Gxx protocol
					29.212	  CR-0905  (Rel-11) v11.5.0
					Source: ZTE, Alcatel-Lucent,Ericsson

Decision: 		The document was Revised to C3-121554.

C3-121498	Correction to the IP-CAN session establishment and termination procedures for S2c case
					29.213	  CR-0435  (Rel-11) v11.3.0
					Source: ZTE

Decision: 		The document was Revised to C3-121673.

C3-121499	Including the UDP-Source-Port in the QoS-Rule-Install
					29.215	  CR-0264  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Agreed.

C3-121500	Functionality of the PCRF for EPC-routed in 29.215
					29.215	  CR-0265  (Rel-11) v11.5.0
					Source: ZTE

Discussion:

MCC should be check the intruction from CR author.

Decision: 		The document was Revised to C3-121555.

C3-121514	Correction to S9a session establishment procedure for S2c case
					29.215	  CR-0270  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Revised to C3-121556.

C3-121546	PCRF selection by BPCF
					29.213	  CR-0426  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121373)

Decision: 		The document was Agreed.

C3-121547	Completion of S9 and S9a procedures
					29.215	  CR-0257  rev 1 (Rel-11) v11.5.0
					Source: Ericsson

(Replaces C3-121374)

Decision: 		The document was Agreed.

C3-121548	QoS info in S9a session establishment response 
					29.215	  CR-0258  rev 1 (Rel-11) v11.5.0
					Source: Ericsson

(Replaces C3-121378)

Decision: 		The document was Agreed.

C3-121549	Inclusion of ePDG/PGW IP Address in Gx/Gxx procedures
					29.212	  CR-0873  rev 1 (Rel-11) v11.5.0
					Source: Ericsson, Huawei

(Replaces C3-121376)

Decision: 		The document was Agreed.

C3-121550	Definition of case 1, case 2a and case 2b (R11 29.212)
					29.212	  CR-0893  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121439)

Decision: 		The document was Agreed.

C3-121551	Definition of case 1, case 2a and case 2b (R11 29.215)
					29.215	  CR-0262  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121440)

Decision: 		The document was Agreed.

C3-121552	Transport of ePDG or PGW IP address over S9 (R11 29.215)
					29.215	  CR-0263  rev 1 (Rel-11) v11.5.0
					Source: Huawei

(Replaces C3-121441)

Decision: 		The document was Agreed.

C3-121554	Remove the IP-CAN type and RAT Type from the Gx/Gxx protocol
					29.212	  CR-0905  rev 1 (Rel-11) v11.5.0
					Source: ZTE, Alcatel-Lucent,Ericsson

(Replaces C3-121497)

Decision: 		The document was Revised to C3-121727.

C3-121555	Functionality of the PCRF for EPC-routed in 29.215
					29.215	  CR-0265  rev 1 (Rel-11) v11.5.0
					Source: ZTE

(Replaces C3-121500)

Decision: 		The document was Revised to C3-121729.

C3-121556	Correction to S9a session establishment procedure for S2c case
					29.215	  CR-0270  rev 1 (Rel-11) v11.5.0
					Source: ZTE

(Replaces C3-121514)

Decision: 		The document was Agreed.

C3-121672	Including the ePDG address and P-GW address on Gx and Gxx
					29.212	  CR-0902  rev 1 (Rel-11) v11.5.0
					Source: ZTE

(Replaces C3-121494)

Discussion:

Offline discussion offered.

Decision: 		The document was Agreed.

C3-121673	Correction to the IP-CAN session establishment and termination procedures for S2c case
					29.213	  CR-0435  rev 1 (Rel-11) v11.3.0
					Source: ZTE

(Replaces C3-121498)

Decision: 		The document was Agreed.

C3-121727	Removal of RAT-Type BBF-WLAN from the Gx/Gxx protocol
					29.212	  CR-0905  rev 2 (Rel-11) v11.5.0
					Source: ZTE, Alcatel-Lucent,Ericsson

(Replaces C3-121554)

Discussion:

Title was changed to "Removal of RAT-Type BBF-WLAN from the Gx/Gxx protocol".

Decision: 		The document was Agreed.

C3-121729	Functionality of the PCRF for EPC-routed in 29.215
					29.215	  CR-0265  rev 2 (Rel-11) v11.5.0
					Source: ZTE

(Replaces C3-121555)

Decision: 		The document was Agreed.

### 11.25	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block II [BBAI_BBII-CT]

C3-121375	Removal of data list provided over S9a reference point
					29.213	  CR-0427  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121377	Completion of Sd procedures for BBAI II
					29.212	  CR-0874  (Rel-11) v11.5.0
					Source: Ericsson, Huawei

Decision: 		The document was Revised to C3-121575.

C3-121387	Transport Access Type AVP for BBAI in case of NSWO scenario
					29.215	  CR-0259  (Rel-11) v11.5.0
					Source: Alcatel-Lucent, Ericsson

Decision: 		The document was Withdrawn.

C3-121443	V-PCRF-Initiated IP-CAN Session Modification for NSWO traffic (R11 29.213)
					29.213	  CR-0430  (Rel-11) v11.3.0
					Source: Huawei

Decision: 		The document was Revised to C3-121553.

C3-121501	Remove the editors note regarding the supported feature for NSWO
					29.212	  CR-0906  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Agreed.

C3-121502	Define the new IP-CAN type value BBF for the NSWO case
					29.212	  CR-0907  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Withdrawn.

C3-121503	Clarification of session binding for NSWO
					29.213	  CR-0436  (Rel-11) v11.3.0
					Source: ZTE

Decision: 		The document was Revised to C3-121578.

C3-121504	PCRF-initiated IP-CAN session termination for NSWO traffic
					29.213	  CR-0437  (Rel-11) v11.3.0
					Source: ZTE,

Decision: 		The document was Revised to C3-121579.

C3-121505	Add UE-Local-IPv6-Prefix to carry the UE Local IP address
					29.215	  CR-0266  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Agreed.

C3-121506	Correct the applicability of AVPs to the specific access over S9a*
					29.215	  CR-0267  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Revised to C3-121674.

C3-121507	Functionality fo the PCRF for NSWO in 29.215
					29.215	  CR-0268  (Rel-11) v11.5.0
					Source: ZTE

Discussion:

MCC will check the instruction from CR author which was related with C3-121555.

Decision: 		The document was Revised to C3-121580.

C3-121553	V-PCRF-Initiated IP-CAN Session Modification for NSWO traffic (R11 29.213)
					29.213	  CR-0430  rev 1 (Rel-11) v11.3.0
					Source: Huawei

(Replaces C3-121443)

Decision: 		The document was Agreed.

C3-121575	Completion of Sd procedures for BBAI II
					29.212	  CR-0874  rev 1 (Rel-11) v11.5.0
					Source: Ericsson, Huawei

(Replaces C3-121377)

Decision: 		The document was Agreed.

C3-121578	Clarification of session binding for NSWO
					29.213	  CR-0436  rev 1 (Rel-11) v11.3.0
					Source: ZTE

(Replaces C3-121503)

Decision: 		The document was Agreed.

C3-121579	PCRF-initiated IP-CAN session termination for NSWO traffic
					29.213	  CR-0437  rev 1 (Rel-11) v11.3.0
					Source: ZTE,

(Replaces C3-121504)

Decision: 		The document was Revised to C3-121730.

C3-121580	Functionality fo the PCRF for NSWO in 29.215
					29.215	  CR-0268  rev 1 (Rel-11) v11.5.0
					Source: ZTE

(Replaces C3-121507)

Decision: 		The document was Revised to C3-121731.

C3-121674	Remove IP-CAN type and RAT type
					29.215	  CR-0267  rev 1 (Rel-11) v11.5.0
					Source: ZTE

(Replaces C3-121506)

Discussion:

Title was changed to "Remove IP-CAN type and RAT type".

Decision: 		The document was Agreed.

C3-121730	PCRF-initiated IP-CAN session termination for NSWO traffic
					29.213	  CR-0437  rev 2 (Rel-11) v11.3.0
					Source: ZTE,

(Replaces C3-121579)

Discussion:

MCC needs to fix the figure number in the figure.

Decision: 		The document was Agreed.

C3-121731	Functionality fo the PCRF for NSWO in 29.215
					29.215	  CR-0268  rev 2 (Rel-11) v11.5.0
					Source: ZTE

(Replaces C3-121580)

Decision: 		The document was Agreed.

### 11.26	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block III [BBAI_BBIII-CT]

### 11.27	CN aspects of Anonymous Call Rejection in the CS domain [ACR_CS-CN]

### 11.28	IMS Emergency PSAP Callback [EMC_PC]

C3-121766	Exception sheet for IMS Emergency PSAP Callback
					Source: Ericsson

Discussion:

It will be provided on the CT3 mailing list by Mr.Jan Holm (from Ericsson) within Friday 17th August.

Decision: 		The document was [not addressed].

### 11.29	Advanced Interconnection of Services [IPXS]

C3-121350	IPXS impact in 3GPP TS 29.165
					Source: Ericsson

Discussion:

No impacts identified on SIP major capabilities, headers etc, however clarification that interfaces of both sides of IPXS are in scope is desirable.

Decision: 		The document was Noted.

C3-121638	Add IPXS to architecture
					29.165	  CR-0472  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121705.

C3-121705	Add IPXS to architecture
					29.165	  CR-0472  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121638)

Decision: 		The document was Revised to C3-121746.

C3-121746	Add IPXS to architecture
					29.165	  CR-0472  rev 2 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121705)

Decision: 		The document was Agreed.

### 11.30	Enhancements for Multimedia Priority Service (MPS)  Gateway Control Priority [eMPS_Gateway]

C3-121328	eMPs
					29.292	  CR-0053  (Rel-11) v11.2.0
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121592.

C3-121592	eMPs
					29.292	  CR-0053  rev 1 (Rel-11) v11.2.0
					Source: Nokia Siemens Networks

(Replaces C3-121328)

Decision: 		The document was Agreed.

### 11.31	CN aspects of Mobility based On GTP & PMIPv6 for WLAN access to EPC [SaMOG_WLAN-CN]

### 11.32	CN aspects of Service Identification for RRC Improvements in GERAN [SIRIG]

### 11.33	CT aspect on Network Provided Location Information for IMS [NWK-PL2IMS-CT]

C3-121402	Addition of PLMN ID for NETLOC in TS 29.214
					29.214	  CR-0238  (Rel-11) v11.5.0
					Source: Ericsson

Decision: 		The document was Merged with C3-121426 into C3-121666.

C3-121403	Addition of PLMN ID for NETLOC in TS 29.212
					29.212	  CR-0875  (Rel-11) v11.5.0
					Source: Ericsson

Decision: 		The document was Merged with C3-121425 into C3-121667.

C3-121425	Addition of PLMN ID for NETLOC (R11 29.212)
					29.212	  CR-0887  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Merged with C3-121403 into C3-121667.

C3-121426	Addition of PLMN ID for NETLOC (R11 29.214)
					29.214	  CR-0244  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Merged with C3-121402 into C3-121666.

C3-121666	Addition of PLMN ID for NETLOC in TS 29.214
					29.214	  CR-0238  rev 1 (Rel-11) v11.5.0
					Source: Ericsson

(Replaces C3-121402)

Decision: 		The document was Agreed.

C3-121667	Addition of PLMN ID for NETLOC in TS 29.212
					29.212	  CR-0875  rev 1 (Rel-11) v11.5.0
					Source: Ericsson

(Replaces C3-121403)

Decision: 		The document was Agreed.

### 11.34	II-NNI enhancements: SIP timers applicability [NNI_timers]

### 11.35	Roaming Architecture for Voice over IMS with Local Breakout – CT aspects [RAVEL-CT]

C3-121320	Loopback NNI
					29.165	  CR-0441  (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121697.

C3-121321	Roaming Option Item
					29.165	  CR-0442  (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121698.

C3-121322	Adding TRF into reference architecture
					29.165	  CR-0443  (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121699.

C3-121444	OMR modification
					29.079	  CR-0013  (Rel-11) v11.0.0
					Source: Huawei

Decision: 		The document was Agreed.

C3-121451	Discussion on usage of the rn parameter for interconnection routeing
					Source: Deutsche Telekom (Reihard,, Roland)

Decision: 		The document was Noted.

C3-121452	Naming of transit network
					29.079	  CR-0014  (Rel-11) v11.0.0
					Source: Deutsche Telekom (Reihard,, Roland)

Decision: 		The document was Revised to C3-121701.

C3-121697	Loopback NNI
					29.165	  CR-0441  rev 1 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121320)

Decision: 		The document was Revised to C3-121747.

C3-121698	Roaming Option Item
					29.165	  CR-0442  rev 1 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121321)

Decision: 		The document was Revised to C3-121706.

C3-121699	Adding TRF into reference architecture
					29.165	  CR-0443  rev 1 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121322)

Decision: 		The document was Revised to C3-121750.

C3-121700	LS out IMS interconnection routing
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121751.

C3-121701	Naming of transit network
					29.079	  CR-0014  rev 1 (Rel-11) v11.0.0
					Source: Deutsche Telekom (Reihard,, Roland)

(Replaces C3-121452)

Decision: 		The document was Agreed.

C3-121706	Roaming Option Item
					29.165	  CR-0442  rev 2 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121698)

Decision: 		The document was Revised to C3-121749.

C3-121747	Loopback NNI
					29.165	  CR-0441  rev 2 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121697)

Decision: 		The document was Agreed.

C3-121748	Exception sheet on Roaming Architecture for Voice over IMS with Local Breakout - CT aspects
					Source: Deutsche Telekom

Discussion:

It will be provided by Mr. Reinhard Lauster (from T-Mobile) on the CT3 mailing list within Moday 13rd August.

Decision: 		The document was [not addressed].

C3-121749	Roaming Option Item
					29.165	  CR-0442  rev 3 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121706)

Decision: 		The document was Agreed.

C3-121750	Adding TRF into reference architecture
					29.165	  CR-0443  rev 2 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121699)

Decision: 		The document was Revised to C3-121758.

C3-121751	LS out IMS interconnection routing
					Source: Nokia Siemens Networks

(Replaces C3-121700)

Decision: 		The document was Revised to C3-121756.

C3-121756	LS out IMS interconnection routing
					Source: Nokia Siemens Networks

(Replaces C3-121751)

Abstract:

1. Overall Description:

3GPP TSG CT WG3 (CT3) is documenting the Inter-IMS Network to Network Interface (II-NNI) in 3GPP TS 29.165.

CT3 has become aware that some SIP interconnection networks still use the routing mechanisms defined in the obsoleted SIP IETF RFC 2543, rather than the routeing mechanisms according to the newer SIP IETF RFC 3261 based on the SIP "Route" header field.

CT3 would like to draw the attention of GSMA and i3Forum to the fact that according to 3GPP TS 29.165 and 3GPP TS 24.229, an interconnection between two IMS networks requires the mandatory support of the IETF RFC 3261 routing mechanism including the SIP "Route" header and by the interconnecting network.

2. Actions: NONE

Decision: 		The document was Approved.

C3-121758	Adding TRF into reference architecture
					29.165	  CR-0443  rev 3 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121750)

Decision: 		The document was Agreed.

### 11.36	Inclusion of Media Resource Broker [MRB]

C3-121345	Optimised allocation of media resources
					29.165	  CR-0451  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121702.

C3-121702	Optimised allocation of media resources
					29.165	  CR-0451  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121345)

Decision: 		The document was Agreed.

C3-121323	Media control related SIP signalling traversing the II- NNI is not considered
					29.165	  CR-0444  (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

Discussion:

The WI was chnged to "MRB".

Decision: 		The document was Revised to C3-121703.

C3-121703	Media control related SIP signalling traversing the II- NNI is not considered
					29.165	  CR-0444  rev 1 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121323)

Decision: 		The document was Revised to C3-121707.

C3-121707	Media control related SIP signalling traversing the II- NNI is not considered
					29.165	  CR-0444  rev 2 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121703)

Discussion:

The WI was chnged to "MRB".

Decision: 		The document was Agreed.

### 11.37	Technical Enhancements and Improvements [TEI11]

#### 11.37.0	Usage momitoring congestion handling

C3-121432	Usage monitoring congestion handling (R11 29.212)
					29.212	  CR-0891  (Rel-11) v11.5.0
					Source: Huawei

Decision: 		The document was Merged with C3-121508 into C3-121664.

C3-121508	Clarification of the usage monitoring congestion handling
					29.212	  CR-0908  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Merged with C3-121432 into C3-121664.

C3-121664	Clarification of the usage monitoring congestion handling
					29.212	  CR-0908  rev 1 (Rel-11) v11.5.0
					Source: ZTE, Huawei

(Replaces C3-121508)

Discussion:

Huawei was added to source company.

Decision: 		The document was Revised to C3-121722.

C3-121722	Clarification of the usage monitoring congestion handling
					29.212	  CR-0908  rev 2 (Rel-11) v11.5.0
					Source: ZTE, Huawie

(Replaces C3-121664)

Decision: 		The document was Agreed.

#### 11.37.1	IMS/CS related docs

C3-121324	Minor Corrections
					29.165	  CR-0445  (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

Decision: 		The document was Agreed.

C3-121532	CLIP 29.292r11
					29.292	  CR-0054  (Rel-11) v11.2.0
					Source: Orange

Decision: 		The document was Withdrawn.

#### 11.37.2	Misc. Packet Core related docs

C3-121509	Remove the FFS regarding the mandatory feature in Rel11 
					29.212	  CR-0909  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Merged with C3-121429 into C3-121662.

C3-121510	Remove the FFS regarding the mandatory feature in Rel11 
					29.215	  CR-0269  (Rel-11) v11.5.0
					Source: ZTE

Decision: 		The document was Merged with C3-121430 into C3-121663.

#### 11.37.3	29.212 title correction

C3-121538	Clean-up of TS 29.212 to align with the new specification number
					29.212	  CR-0910  (Rel-11) v11.5.0
					Source: Allot Communications

Discussion:

This CR was produced after deadline for supporting o/g LS (C3-121535, C3-121537).

Decision: 		The document was Withdrawn.

C3-121568	Title correction
					29.212	  CR-0911  (Rel-11) v11.5.0
					Source: Allot Communications, Juniper Networks

Decision: 		The document was Agreed.

C3-121569	Reference list correction to align with the corrected TS 29.212 title
					29.061	  CR-0385  (Rel-11) v11.1.0
					Source: Allot Communications,  Juniper Networks

Decision: 		The document was Revised to C3-121732.

C3-121732	Reference list correction to align with the corrected TS 29.212 title
					29.061	  CR-0385  rev 1 (Rel-11) v11.1.0
					Source: Allot Communications

(Replaces C3-121569)

Decision: 		The document was Agreed.

C3-121570	Reference list correction to align with the corrected TS 29.212 title
					29.213	  CR-0438  (Rel-11) v11.3.0
					Source: Allot Communications, Juniper Networks

Decision: 		The document was Agreed.

C3-121571	Reference list correction to align with the corrected TS 29.212 title
					29.214	  CR-0246  (Rel-11) v11.5.0
					Source: Allot Communications, Juniper Networks

Decision: 		The document was Agreed.

C3-121572	Reference list correction to align with the corrected TS 29.212 title
					29.215	  CR-0271  (Rel-11) v11.5.0
					Source: Allot Communications, Juniper Networks

Decision: 		The document was Agreed.

### 11.38	Rel-11 contributions on other Work Items

#### 11.38.1	Enhanced T.38 FAX support

C3-121326	Support of T.38 related SDP attributes
					Source: Nokia Siemens Networks

Discussion:

Adding supporting IM and the changes according to the email from Mr.Adrian Zoica, ETSI WID Manager will be provided, and Mr.Naoaki Suzuki (from NEC) is the rapporteur for this WID. So the revision is produced.

Decision: 		The document was Revised to C3-121543.

C3-121327	Support of T.38 related SDP attributes
					29.163	  CR-0669  (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121586.

C3-121513	Clarify CT1 position in T.38 interworking related work
					Source: NEC, NTT

Decision: 		The document was Noted.

C3-121543	Support of T.38 related SDP attributes
					Source: NEC, Nokia Siemens Networks

(Replaces C3-121326)

Decision: 		The document was Revised to C3-121675.

C3-121586	Support of T.38 related SDP attributes
					29.163	  CR-0669  rev 1 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121327)

Decision: 		The document was Revised to C3-121709.

C3-121675	Support of T.38 related SDP attributes
					Source: NEC, Nokia Siemens Networks

(Replaces C3-121543)

Decision: 		The document was Revised to C3-121689.

C3-121689	Support of T.38 related SDP attributes
					Source: NEC, Nokia Siemens Networks, NTT

(Replaces C3-121675)

Decision: 		The document was Agreed.

C3-121708	Exception sheet for Enhanced T.38 FAX support
					Source: NEC, NTT

Decision: 		The document was Revised to C3-121759.

C3-121709	Support of T.38 related SDP attributes
					29.163	  CR-0669  rev 2 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121586)

Decision: 		The document was Revised to C3-121760.

C3-121716	LS out LS on T.38 related work in CT WGs
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121753.

C3-121753	LS out LS on T.38 related work in CT WGs
					Source: Nokia Siemens Networks

(Replaces C3-121716)

Decision: 		The document was Approved.

C3-121759	Exception sheet for Enhanced T.38 FAX support
					Source: NEC, NTT

(Replaces C3-121708)

Decision: 		The document was Agreed.

C3-121760	Support of T.38 related SDP attributes
					29.163	  CR-0669  rev 3 (Rel-11) v11.3.0
					Source: Nokia Siemens Networks

(Replaces C3-121709)

Decision: 		The document was Agreed.

#### 11.38.2	Void

#### 11.38.3	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]

C3-121354	Adding MIME body table and removing an EN - CT CR CORRELATION NEEDED
					29.165	  CR-0455  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121639.
F

C3-121639	Adding MIME body table and removing an EN - CT CR CORRELATION NEEDED
					29.165	  CR-0455  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121354)

Decision: 		The document was Revised to C3-121715.

C3-121715	Adding MIME body table and removing an EN - CT CR CORRELATION NEEDED
					29.165	  CR-0455  rev 2 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121639)

Decision: 		The document was Revised to C3-121761.

C3-121761	Adding MIME body table and removing an EN - CT CR CORRELATION NEEDED
					29.165	  CR-0455  rev 3 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121715)

Decision: 		The document was Agreed.

#### 11.38.4	Enhancement for EPC Nodes Restoration [eNR_EPC]

C3-121577	Updated WID on the enhancement for EPC Nodes Restoration
					Source: ZTE

Decision: 		The document was Endorsed.

C3-121733	Exception sheet for Enhancement for EPC Nodes Restoration
					Source: ZTE

Decision: 		The document was Revised to C3-121762.

C3-121762	Exception sheet for Enhancement for EPC Nodes Restoration
					Source: ZTE

(Replaces C3-121733)

Decision: 		The document was Agreed.

#### 11.38.5	IMS overload control

C3-121511	Inclusion of SIP overload control
					Source: Alcatel-Lucent, AT&T / Keith Drage

Discussion:

The new WID was needed.

Decision: 		The document was Noted.

C3-121512	Support of overload control
					29.165	  CR-0470  (Rel-11) v11.3.0
					Source: Alcatel-Lucent, AT&T / Keith Drage

Discussion:

The WID was moved from IMSProto5 to ''IOC" (new WI).

Decision: 		The document was Revised to C3-121599.

C3-121599	Support of overload control
					29.165	  CR-0470  rev 1 (Rel-11) v11.3.0
					Source: Alcatel-Lucent, AT&T / Keith Drage

(Replaces C3-121512)

Decision: 		The document was Revised to C3-121744.

C3-121691	New WID on IMS overload control
					Source: Alcatel-Lucent

Decision: 		The document was Endorsed.

C3-121744	Support of overload control
					29.165	  CR-0470  rev 2 (Rel-11) v11.3.0
					Source: Alcatel-Lucent, AT&T / Keith Drage

(Replaces C3-121599)

Decision: 		The document was Revised to C3-121752.

C3-121745	Exception sheet on IMS overload control
					Source: Alcatal-Lucent

Discussion:

It will be provided by Mr.Keith Drage (from Alcatel-Lucent)  on the CT3 mailing list within 17th August.

Decision: 		The document was [not addressed].

C3-121752	Support of overload control
					29.165	  CR-0470  rev 3 (Rel-11) v11.3.0
					Source: Alcatel-Lucent, AT&T / Keith Drage

(Replaces C3-121744)

Decision: 		The document was Agreed.

## 12	Release 12

### 12.1	Interworking between a PLMN with WLAN to access the EPC and a PDN

C3-121445	Interworking between a PLMN with WLAN to access the EPC and a PDN
					Source: Huawei, HiSilicon

Discussion:

Acording to advice from Mr.Adrian Zoicas, ETSI WID Mangaer, and the comments from Ericsson, Juniper Networks and ZTE, the changes were suggested. Supporting IM will be welcomed.  The revision was produced.

Decision: 		The document was Revised to C3-121544.

C3-121446	Interworking between a PLMN with WLAN to access the EPC and a PDN
					Source: Huawei, HiSilicon

Decision: 		The document was Noted.

C3-121544	Interworking between a PLMN with WLAN to access the EPC and a PDN
					Source: Huawei, HiSilicon

(Replaces C3-121445)

Discussion:

TS 29.061 will be used and needed the completion date.

Decision: 		The document was Revised to C3-121734.

C3-121545	Exception sheet for Interworking between PLMN with WLAN to access the EPC and a PDN
					Source: Huawei, HiSilicon

Decision: 		The document was Withdrawn.

C3-121734	Interworking between a PLMN with WLAN to access the EPC and a PDN
					Source: Huawei, HiSilicon

(Replaces C3-121544)

Decision: 		The document was Agreed.

## 13	Joint sessions

## 14	Work Organisation

### 14.1	Work Plan Review

C3-121335	Status of CT3 Work Items
					Source: CT3 Chairman

Decision: 		The document was Revised to C3-121765.

C3-121461	Lastest Version of 3GPP Workplan
					Source: MCC

Decision: 		The document was Noted.

C3-121765	Status of CT3 Work Items
					Source: CT3 Chairman

(Replaces C3-121335)

Decision: 		The document was Noted.

### 14.2	Specification Review

C3-121462	Status of CT3 Specifications following CT#56 meeting
					Source: MCC

Decision: 		The document was Noted.

### 14.3	Next meetings, allocation of hosts

C3-121463	Meeting Calendar for 2012 - 2013
					Source: MCC

Discussion:

CT3 agreed that the meeting in April 2013 (CT3#72-BIS) is not needed. The host will be informed accordingly and CT3 meeting calendar will be updated.

Decision: 		The document was Noted.

## 15	Summary of results

## 16	Any other business

## 17	Closing of the meeting

## Annex A. TS/TR

| Tdoc | Type | Title | Source |
| --- | --- | --- | --- |
| C3-121763 | 3GPP TS | TS 29.368 v 1.1.0 | Ericsson |
| C3-121764 | 3GPP TS | Presentation sheet for TS 29.368 v 1.1.0 | Ericsson |

## Annex B. Work Item

| Tdoc | Type | Title | Source |
| --- | --- | --- | --- |
| C3-121689 | WID | Support of T.38 related SDP attributes | NEC, Nokia Siemens Networks, NTT |
| C3-121734 | WID | Interworking between a PLMN with WLAN to access the EPC and a PDN | Huawei, HiSilicon |
| C3-121562 | WID | Revised WID for Stage 3 for System Improvements to Machine-Type Communications | Ericsson |
| C3-121577 | WID | Updated WID on the enhancement for EPC Nodes Restoration | ZTE |
| C3-121691 | WID | New WID on IMS overload control | Alcatel-Lucent |

## Annex C. Liaison Statements

### Annex C.1 Incoming Liaison Statements

| Tdoc | Title | Source | Source File | Response | Decision |
| --- | --- | --- | --- | --- | --- |
| C3-121464 | Reply LS on CT3 LS on Questions regarding BBAI procedures | TSG SA WG2 | S2-122435 | C3-121735 | Noted |
| C3-121465 | Reply LS on OSCAR conclusions | TSG SA WG2 | S2-122578 |  | Noted |
| C3-121466 | Reply LS on assignment of 3 digit MNC | TSG CT WG1 | C1-122166 |  | Noted |
| C3-121467 | Reply LS on H(e)NB local IP address for Fixed Broadband Access network interworking | TSG CT WG4 | C4-121308 |  | Noted |
| C3-121468 | Reply LS on OSCAR conclusions | TSG CT WG1 | C1-122400 |  | Noted |
| C3-121469 | LS on Absolute Time of MBMS Data Transfer | TSG RAN WG3 | R3-121343 |  | Noted |
| C3-121470 | Reply LS on H(e)NB local IP address for Fixed Broadband Access network interworking | TSG SA WG3 | S3-120513 |  | Noted |
| C3-121471 | NGN studies | ITU-T Study Group 3 Rapporteur on NGN | COM 3-LS023 |  | Noted |
| C3-121472 | Liaison Regarding MSF/ETSI/GSMA RCS VoLTE Interoperability Event | ETSI TC INT (IMS Network Testing) | INT(12)000101 |  | Noted |
| C3-121473 | Reply LS on Assignment of 3 digit MNC | TSG CT | CP-120424 |  | Noted |
| C3-121474 | Reply LS on Assignment of 3 digit MNC | TSG SA | SP-120429 |  | Noted |
| C3-121475 | LS on GSMA Application Network Efficiency Task Force – whitepaper and actions | TSG SA | SP-120423 | C3-121669 | Noted |
| C3-121476 | LS on security for the Tsp interface | TSG SA WG3 | S3-120778 | C3-121754 | Noted |
| C3-121477 | LS on GSMA Application Network Efficiency Task Force “whitepaper and actions” | TSG SA WG2 | S2-123424 |  | Noted |
| C3-121478 | LS response on V-PCRF-Indicated IP-CAN Session Modification for NSWO traffic | TSG SA WG2 | S2-123323 |  | Noted |
| C3-121479 | Reply LS on TFT usage for the primary PDP context when access to the PGW | TSG SA WG2 | S2-123345 | C3-121755 | Noted |
| C3-121480 | LS on Tsp | TSG SA WG2 | S2-123392 |  | Noted |
| C3-121481 | Triggering functionality and relation to 3GPP CT WG3 working assumption | ETSI TC M2M | M2M(12)21_116r1 |  | Noted |

### Annex C.2 Outgoing Liaison Statements

| Tdoc | Title | LS To | LS Cc | Attachment |
| --- | --- | --- | --- | --- |
| C3-121581 | LS out LS on the redirection of functionality of SAPP | SA2 |  |  |
| C3-121582 | LS out LS on Charging Issues regading PCC and ADC rules | SA2 |  |  |
| C3-121584 | LS out LS on PCC support for rSRVCC | SA2 |  | C3-121422, C3-121423, C3-121424, C3-121492 |
| C3-121668 | LS out LS on QoS parameters can be upgraded and downgraded | SA2 |  |  |
| C3-121669 | Reply LS on GSMA Application Network Efficiency Task Force – whitepaper and actions | 3GPP TSG CT | CT1, CT4 | 3GPP-CT3-Actions |
| C3-121714 | LS on Mapping between SIP Responses and ISUP Cause Values | i3Forum |  | C3-121624 |
| C3-121735 | LS out Reply LS on Questions regarding BBAI procedures | SA2 | CT4 |  |
| C3-121753 | LS out LS on T.38 related work in CT WGs | SA4 | CT1, CT4 | C3-121689, C3-121760 |
| C3-121754 | Reply LS on security for the Tsp interface | SA3 |  |  |
| C3-121755 | Reply LS LS on TFT usage for the primary PDP context when using PGW | SA2 | CT4 |  |
| C3-121756 | LS out IMS interconnection routing | GSMA, i3Forum | CT1 |  |

## Annex D. Agreed Change Requests

| Tdoc | Type | Title | Source | Spec | CR | CR_revision | Release | 'Decision' | Version_old | Work_item | Category |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C3-121297 | CR | P-Refused-URI-List header field | NTT | 29.165 | 0426 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121299 | CR | Correction on the description of "g.3gpp.crs" | NTT | 29.165 | 0428 | 0 | Rel-9 | Agreed | 9.11.0 | II-NNI | F |
| C3-121300 | CR | Correction on the description of "g.3gpp.crs" | NTT | 29.165 | 0429 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI | A |
| C3-121301 | CR | Correction on the description of "g.3gpp.crs" | NTT | 29.165 | 0430 | 0 | Rel-11 | Agreed | 11.3.0 | II-NNI | A |
| C3-121302 | CR | Correction on the description of "application/vnd.etsi.mcid+xml" MIME body | NTT | 29.165 | 0431 | 0 | Rel-9 | Agreed | 9.11.0 | II-NNI | F |
| C3-121303 | CR | Correction on the description of "application/vnd.etsi.mcid+xml" MIME body | NTT | 29.165 | 0432 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI | A |
| C3-121304 | CR | Correction on the description of "application/vnd.etsi.mcid+xml" MIME body | NTT | 29.165 | 0433 | 0 | Rel-11 | Agreed | 11.3.0 | II-NNI | A |
| C3-121324 | CR | Minor Corrections | Nokia Siemens Networks | 29.165 | 0445 | 0 | Rel-11 | Agreed | 11.3.0 | TEI11 | F |
| C3-121336 | CR | Reference alignment for RTP Payload Format for AMR and AMR-WB Audio Codecs | Ericsson | 29.163 | 0670 | 0 | Rel-8 | Agreed | 8.19.0 | IMS-CCR-IWCS | F |
| C3-121337 | CR | Reference alignment for RTP Payload Format for AMR and AMR-WB Audio Codecs | Ericsson | 29.163 | 0671 | 0 | Rel-9 | Agreed | 9.10.0 | IMS-CCR-IWCS | A |
| C3-121338 | CR | Reference alignment for RTP Payload Format for AMR and AMR-WB Audio Codecs | Ericsson | 29.163 | 0672 | 0 | Rel-10 | Agreed | 10.6.0 | IMS-CCR-IWCS | A |
| C3-121339 | CR | Reference alignment for RTP Payload Format for AMR and AMR-WB Audio Codecs | Ericsson | 29.163 | 0673 | 0 | Rel-11 | Agreed | 11.3.0 | IMS-CCR-IWCS | A |
| C3-121351 | CR | Feature-Caps added to trust domain - CT CR CORRELATION NEEDED | Ericsson | 29.165 | 0452 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121352 | CR | Feature-Caps added to trust domain - CT CR CORRELATION NEEDED | Ericsson | 29.165 | 0453 | 0 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121357 | CR | IUT reference update | Ericsson | 29.165 | 0458 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121359 | CR | MIME body name update | Ericsson | 29.165 | 0460 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121361 | CR | CDIV corrections | Ericsson | 29.165 | 0462 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121362 | CR | CDIV corrections | Ericsson | 29.165 | 0463 | 0 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121363 | CR | Missing the Event header in MWI | Ericsson | 29.165 | 0464 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121365 | CR | Event header field missing in CC services | Ericsson | 29.165 | 0466 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121366 | CR | Event header field missing in CC services | Ericsson | 29.165 | 0467 | 0 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121371 | CR | BBAI related Event Triggers completion | Ericsson | 29.212 | 0872 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121372 | CR | APN support in S9 and S9a | Ericsson | 29.215 | 0256 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121375 | CR | Removal of data list provided over S9a reference point | Ericsson | 29.213 | 0427 | 0 | Rel-11 | Agreed | 11.3.0 | BBAI_BBII-CT | B |
| C3-121386 | CR | Encoding of Absolute Time of MBMS Data Transfer | Alcatel-Lucent, Ericsson, Verizon Wireless | 29.061 | 0379 | 0 | Rel-11 | Agreed | 11.1.0 | MBMS_EPS | F |
| C3-121388 | CR | Correction of AVPs for BBAI in case of EPC routed scenario | Alcatel-Lucent, Ericsson, ZTE | 29.215 | 0260 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | F |
| C3-121433 | CR | Clean-up for spending limit description (R11 29.219) | Huawei | 29.219 | 0007 | 0 | Rel-11 | Agreed | 11.1.0 | QoS_SSL-CT3 | F |
| C3-121442 | CR | V-PCRF-Initiated IP-CAN Session Modification for EPC routed traffic (R11 29.213) | Huawei | 29.213 | 0429 | 0 | Rel-11 | Agreed | 11.3.0 | BBAI_BBI-CT | F |
| C3-121444 | CR | OMR modification | Huawei | 29.079 | 0013 | 0 | Rel-11 | Agreed | 11.0.0 | RAVEL-CT | F |
| C3-121493 | CR | Correction to the scope of BBAI annex | ZTE | 29.212 | 0901 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | F |
| C3-121495 | CR | Including the UDP-Source-Port in the Qos-Rule-Install | ZTE | 29.212 | 0903 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121496 | CR | Unsolicited application reporting for BBAI | ZTE, Ericsson | 29.212 | 0904 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121499 | CR | Including the UDP-Source-Port in the QoS-Rule-Install | ZTE | 29.215 | 0264 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | F |
| C3-121501 | CR | Remove the editors note regarding the supported feature for NSWO | ZTE | 29.212 | 0906 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBII-CT | B |
| C3-121505 | CR | Add UE-Local-IPv6-Prefix to carry the UE Local IP address | ZTE | 29.215 | 0266 | 0 | Rel-11 | Agreed | 11.5.0 | BBAI_BBII-CT | B |
| C3-121546 | CR | PCRF selection by BPCF | Ericsson | 29.213 | 0426r1 | 1 | Rel-11 | Agreed | 11.3.0 | BBAI_BBI-CT | B |
| C3-121547 | CR | Completion of S9 and S9a procedures | Ericsson | 29.215 | 0257r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121548 | CR | QoS info in S9a session establishment response | Ericsson | 29.215 | 0258r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | F |
| C3-121549 | CR | Inclusion of ePDG/PGW IP Address in Gx/Gxx procedures | Ericsson, Huawei | 29.212 | 0873r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121550 | CR | Definition of case 1, case 2a and case 2b (R11 29.212) | Huawei | 29.212 | 0893r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | F |
| C3-121551 | CR | Definition of case 1, case 2a and case 2b (R11 29.215) | Huawei | 29.215 | 0262r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | F |
| C3-121552 | CR | Transport of ePDG or PGW IP address over S9 (R11 29.215) | Huawei | 29.215 | 0263r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | F |
| C3-121553 | CR | V-PCRF-Initiated IP-CAN Session Modification for NSWO traffic (R11 29.213) | Huawei | 29.213 | 0430r1 | 1 | Rel-11 | Agreed | 11.3.0 | BBAI_BBII-CT | F |
| C3-121556 | CR | Correction to S9a session establishment procedure for S2c case | ZTE | 29.215 | 0270r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | F |
| C3-121568 | CR | Title correction | Allot Communications, Juniper Networks | 29.212 | 0911 | 0 | Rel-11 | Agreed | 11.5.0 | TEI11 | F |
| C3-121570 | CR | Reference list correction to align with the corrected TS 29.212 title | Allot Communications, Juniper Networks | 29.213 | 0438 | 0 | Rel-11 | Agreed | 11.3.0 | TEI11 | F |
| C3-121571 | CR | Reference list correction to align with the corrected TS 29.212 title | Allot Communications, Juniper Networks | 29.214 | 0246 | 0 | Rel-11 | Agreed | 11.5.0 | TEI11 | F |
| C3-121572 | CR | Reference list correction to align with the corrected TS 29.212 title | Allot Communications, Juniper Networks | 29.215 | 0271 | 0 | Rel-11 | Agreed | 11.5.0 | TEI11 | F |
| C3-121575 | CR | Completion of Sd procedures for BBAI II | Ericsson, Huawei | 29.212 | 0874r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBII-CT | B |
| C3-121578 | CR | Clarification of session binding for NSWO | ZTE | 29.213 | 0436r1 | 1 | Rel-11 | Agreed | 11.3.0 | BBAI_BBII-CT | F |
| C3-121583 | CR | Clarification of the redirection function | ZTE | 29.212 | 0899r1 | 1 | Rel-11 | Agreed | 11.5.0 | SAPP-CT3 | F |
| C3-121587 | CR | Correcting reference | NTT | 29.165 | 0438r1 | 1 | Rel-9 | Agreed | 9.11.0 | II-NNI | F |
| C3-121588 | CR | Correcting reference | NTT | 29.165 | 0439r1 | 1 | Rel-10 | Agreed | 10.8.0 | II-NNI | A |
| C3-121589 | CR | Correcting reference | NTT | 29.165 | 0440r1 | 1 | Rel-11 | Agreed | 11.3.0 | II-NNI | A |
| C3-121590 | CR | Removal of editor's note in Annex C | NTT, Ericsson | 29.165 | 0425r1 | 1 | Rel-11 | Agreed | 11.3.0 | NNI_OI | D |
| C3-121592 | CR | eMPs | Nokia Siemens Networks | 29.292 | 0053r1 | 1 | Rel-11 | Agreed | 11.2.0 | eMPS_Gateway | B |
| C3-121594 | CR | Correcting minor errors | NTT | 29.165 | 0434r1 | 1 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121595 | CR | Editorial corrections | Ericsson | 29.165 | 0457r1 | 1 | Rel-11 | Agreed | 11.3.0 | IMSprotoc5 | D |
| C3-121596 | CR | Correcting minor errors | NTT | 29.165 | 0471 | 0 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121600 | CR | P-Early-Media Header is Mandatory for MGCF | Deutsche Telekom (Roland) | 29.163 | 0633r6 | 6 | Rel-7 | Agreed | 7.25.0 | FBI | F |
| C3-121601 | CR | P-Early-Media Header is Mandatory for MGCF | Deutsche Telekom (Roland) | 29.163 | 0634r6 | 6 | Rel-8 | Agreed | 8.19.0 | FBI | A |
| C3-121602 | CR | P-Early-Media Header is Mandatory for MGCF | Deutsche Telekom (Roland) | 29.163 | 0635r6 | 6 | Rel-9 | Agreed | 9.10.0 | FBI | A |
| C3-121603 | CR | P-Early-Media Header is Mandatory for MGCF | Deutsche Telekom (Roland) | 29.163 | 0636r6 | 6 | Rel-10 | Agreed | 10.6.0 | FBI | A |
| C3-121604 | CR | P-Early-Media Header is Mandatory for MGCF | Deutsche Telekom (Roland) | 29.163 | 0637r6 | 6 | Rel-11 | Agreed | 11.3.0 | FBI | A |
| C3-121628 | CR | Mapping of CANCEL request | Orange, AT&T | 29.163 | 0613r2 | 2 | Rel-10 | Agreed | 10.6.0 | IMS-CCR-IWCS | A |
| C3-121629 | CR | Mapping of CANCEL request | Orange, AT&T | 29.163 | 0614r2 | 2 | Rel-11 | Agreed | 11.3.0 | IMS-CCR-IWCS | A |
| C3-121630 | CR | P-Refused-URI-List header field | NTT | 29.165 | 0427r1 | 1 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121631 | CR | Clarification on the SDP rules for transporting media streams with TCP | OKI, NTT | 29.165 | 0436r1 | 1 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121632 | CR | Clarification on the SDP rules for transporting media streams with TCP | OKI, NTT | 29.165 | 0437r1 | 1 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121633 | CR | draft-ietf-sipcore-proxy-feature: reference update and technical changes | Ericsson | 29.165 | 0449r1 | 1 | Rel-10 | Agreed | 10.8.0 | II-NNI2 | F |
| C3-121634 | CR | draft-ietf-sipcore-proxy-feature: reference update and technical changes | Ericsson | 29.165 | 0450r1 | 1 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121635 | CR | MIME body name update | Ericsson | 29.165 | 0461r1 | 1 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121636 | CR | Missing the Event header in MWI | Ericsson | 29.165 | 0465r1 | 1 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121637 | CR | IUT reference update | Ericsson | 29.165 | 0459r1 | 1 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | A |
| C3-121643 | CR | PSTN XML schema Bearer Capability correction | Nokia Siemens Networks, Deutsche Telefom | 29.163 | 0678r1 | 1 | Rel-8 | Agreed | 8.19.0 | REDOC_TIS-C3 | F |
| C3-121644 | CR | PSTN XML schema Bearer Capability correction | Nokia Siemens Networks, Deutsche Telefom | 29.163 | 0679r1 | 1 | Rel-9 | Agreed | 9.10.0 | REDOC_TIS-C3 | A |
| C3-121645 | CR | PSTN XML schema Bearer Capability correction | Nokia Siemens Networks, Deutsche Telefom | 29.163 | 0680r1 | 1 | Rel-10 | Agreed | 10.6.0 | REDOC_TIS-C3 | A |
| C3-121646 | CR | PSTN XML schema Bearer Capability correction | Nokia Siemens Networks, Deutsche Telefom | 29.163 | 0681r1 | 1 | Rel-11 | Agreed | 11.3.0 | REDOC_TIS-C3 | A |
| C3-121647 | CR | Correction of assigned internet protocol number (29.214 R7) | Alcatel-Lucent | 29.214 | 0229r1 | 1 | Rel-7 | Agreed | 7.11.0 | PCC | F |
| C3-121648 | CR | Correction of assigned internet protocol number (29.214 R8) | Alcatel-Lucent | 29.214 | 0230r1 | 1 | Rel-8 | Agreed | 8.12.0 | PCC | A |
| C3-121649 | CR | Correction of assigned internet protocol number (29.214 R9) | Alcatel-Lucent | 29.214 | 0231r1 | 1 | Rel-9 | Agreed | 9.9.0 | PCC | A |
| C3-121650 | CR | Correction of assigned internet protocol number (29.214 R10) | Alcatel-Lucent | 29.214 | 0232r1 | 1 | Rel-10 | Agreed | 10.6.0 | PCC | A |
| C3-121651 | CR | Correction of assigned internet protocol number (29.214 R11) | Alcatel-Lucent | 29.214 | 0233r1 | 1 | Rel-11 | Agreed | 11.5.0 | PCC | A |
| C3-121652 | CR | Store session information and identify IP-CAN Session (R8 29.213) | Huawei, Nokia Siemens Networks | 29.213 | 0431r1 | 1 | Rel-8 | Agreed | 8.14.0 | SAES-St3-PCC | F |
| C3-121653 | CR | Store session information and identify IP-CAN Session (R9 29.213) | Huawei, Nokia Siemens Networks | 29.213 | 0432r1 | 1 | Rel-9 | Agreed | 9.9.0 | SAES-St3-PCC | A |
| C3-121654 | CR | Store session information and identify IP-CAN Session (R10 29.213) | Huawei, Nokia Siemens Networks | 29.213 | 0433r1 | 1 | Rel-10 | Agreed | 10.6.0 | SAES-St3-PCC | A |
| C3-121655 | CR | Store session information and identify IP-CAN Session (R11 29.213) | Huawei, Nokia Siemens Networks | 29.213 | 0434r1 | 1 | Rel-11 | Agreed | 11.3.0 | SAES-St3-PCC | A |
| C3-121657 | CR | SGSN address when GnGp SGSN accesses to PGW (R8 29.061) | Huawei | 29.061 | 0380r1 | 1 | Rel-8 | Agreed | 8.9.0 | SAES-St3-intwk | F |
| C3-121658 | CR | SGSN address when GnGp SGSN accesses to PGW (R9 29.061) | Huawei | 29.061 | 0381r1 | 1 | Rel-9 | Agreed | 9.9.0 | SAES-St3-intwk | A |
| C3-121659 | CR | SGSN address when GnGp SGSN accesses to PGW (R10 29.061) | Huawei | 29.061 | 0382r1 | 1 | Rel-10 | Agreed | 10.6.0 | SAES-St3-intwk | A |
| C3-121660 | CR | SGSN address when GnGp SGSN accesses to PGW (R11 29.061) | Huawei | 29.061 | 0383r1 | 1 | Rel-11 | Agreed | 11.1.0 | SAES-St3-intwk | A |
| C3-121661 | CR | Incorrect references | Ericsson | 29.215 | 0255r1 | 1 | Rel-11 | Agreed | 11.5.0 | SAES-St3-PCC | D |
| C3-121662 | CR | Supported feature for R11 (R11 29.212) | Huawei | 29.212 | 0889r1 | 1 | Rel-11 | Agreed | 11.5.0 | SAES-St3-PCC | F |
| C3-121663 | CR | Supported feature for R11 (R11 29.215) | Huawei | 29.215 | 0261r1 | 1 | Rel-11 | Agreed | 11.5.0 | SAES-St3-PCC | F |
| C3-121666 | CR | Addition of PLMN ID for NETLOC in TS 29.214 | Ericsson | 29.214 | 0238r1 | 1 | Rel-11 | Agreed | 11.5.0 | NWK-PC2IMS-CT | B |
| C3-121667 | CR | Addition of PLMN ID for NETLOC in TS 29.212 | Ericsson | 29.212 | 0875r1 | 1 | Rel-11 | Agreed | 11.5.0 | NWK-PC2IMS-CT | B |
| C3-121670 | CR | Additional input to obtain GBR values | Ericsson | 29.213 | 0425r1 | 1 | Rel-11 | Agreed | 11.3.0 | SAES-St3-PCC | F |
| C3-121672 | CR | Including the ePDG address and P-GW address on Gx and Gxx | ZTE | 29.212 | 0902r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121673 | CR | Correction to the IP-CAN session establishment and termination procedures for S2c case | ZTE | 29.213 | 0435r1 | 1 | Rel-11 | Agreed | 11.3.0 | BBAI_BBI-CT | F |
| C3-121674 | CR | Remove IP-CAN type and RAT type | ZTE | 29.215 | 0267r1 | 1 | Rel-11 | Agreed | 11.5.0 | BBAI_BBII-CT | B |
| C3-121680 | CR | XML schema defintion correction | Belgacom | 29.163 | 0685r2 | 2 | Rel-8 | Agreed | 8.19.0 | REDOC_TIS-C3 | F |
| C3-121681 | CR | XML schema defintion correction | Belgacom | 29.163 | 0684r2 | 2 | Rel-9 | Agreed | 9.10.0 | REDOC_TIS-C3 | A |
| C3-121682 | CR | XML schema defintion correction | Belgacom | 29.163 | 0683r2 | 2 | Rel-10 | Agreed | 10.6.0 | REDOC_TIS-C3 | A |
| C3-121683 | CR | XML schema defintion correction | Belgacom | 29.163 | 0682r2 | 2 | Rel-11 | Agreed | 11.3.0 | REDOC_TIS-C3 | A |
| C3-121684 | CR | Applicable IP-CAN Type (R8 29.214) | Huawei | 29.214 | 0239r1 | 1 | Rel-8 | Agreed | 8.12.0 | SAES-St3-PCC | F |
| C3-121685 | CR | Applicable IP-CAN Type (R9 29.214) | Huawei | 29.214 | 0240r1 | 1 | Rel-9 | Agreed | 9.9.0 | SAES-St3-PCC | A |
| C3-121690 | CR | Managing the maximum length of a SIP message body | Fujitsu, NTT | 29.165 | 0435r2 | 2 | Rel-11 | Agreed | 11.3.0 | NNI_OI | B |
| C3-121692 | CR | Mapping of CANCEL request | Orange, AT&T | 29.163 | 0686 | 0 | Rel-7 | Agreed | 7.25.0 | IMS-CCR-IWCS | F |
| C3-121693 | CR | Mapping of CANCEL request | Orange, AT&T | 29.163 | 0687 | 0 | Rel-8 | Agreed | 8.19.0 | IMS-CCR-IWCS | A |
| C3-121694 | CR | Mapping of CANCEL request | Orange, AT&T | 29.163 | 0612r3 | 3 | Rel-9 | Agreed | 9.10.0 | IMS-CCR-IWCS | A |
| C3-121701 | CR | Naming of transit network | Deutsche Telekom (Reihard,, Roland) | 29.079 | 0014r1 | 1 | Rel-11 | Agreed | 11.0.0 | RAVEL-CT | F |
| C3-121702 | CR | Optimised allocation of media resources | Ericsson | 29.165 | 0451r1 | 1 | Rel-11 | Agreed | 11.3.0 | MRB | B |
| C3-121707 | CR | Media control related SIP signalling traversing the II- NNI is not considered | Nokia Siemens Networks | 29.165 | 0444r2 | 2 | Rel-11 | Agreed | 11.3.0 | MRB | F |
| C3-121710 | CR | TIP TIR interworking 29.163r8 | Orange | 29.163 | 0618r3 | 3 | Rel-8 | Agreed | 8.19.0 | IMS-CCR-IWCS | F |
| C3-121711 | CR | TIP TIR interworking 29.163r9 | Orange | 29.163 | 0606r4 | 4 | Rel-9 | Agreed | 9.10.0 | IMS-CCR-IWCS | A |
| C3-121712 | CR | TIP TIR interworking 29.163r10 | Orange | 29.163 | 0607r4 | 4 | Rel-10 | Agreed | 10.6.0 | IMS-CCR-IWCS | A |
| C3-121713 | CR | TIP TIR interworking 29.163r11 | Orange | 29.163 | 0608r4 | 4 | Rel-11 | Agreed | 11.3.0 | IMS-CCR-IWCS | A |
| C3-121717 | CR | Applicable IP-CAN Type (R10 29.214) | Huawei | 29.214 | 0241r2 | 2 | Rel-10 | Agreed | 10.6.0 | SAES-St3-PCC | A |
| C3-121718 | CR | Applicable IP-CAN Type (R11 29.214) | Huawei | 29.214 | 0242r2 | 2 | Rel-11 | Agreed | 11.5.0 | SAES-St3-PCC | A |
| C3-121719 | CR | Removal of Maximum MBR APN-AMBR (R11 29.212) | Huawei | 29.212 | 0885r1 | 1 | Rel-11 | Agreed | 11.5.0 | PCC-Enh | A |
| C3-121720 | CR | Serving network limitation for PCC Rule Authorization (R11 29.212) | Huawei | 29.212 | 0888r2 | 2 | Rel-11 | Agreed | 11.5.0 | SAES-St3-PCC | F |
| C3-121721 | CR | Reporting multiple events to AF (R11 29.214) | Huawei | 29.214 | 0245r2 | 2 | Rel-11 | Agreed | 11.5.0 | PCC | F |
| C3-121722 | CR | Clarification of the usage monitoring congestion handling | ZTE, Huawie | 29.212 | 0908r2 | 2 | Rel-11 | agreed | 11.5.0 | TEI11 | F |
| C3-121723 | CR | Removal of Maximum MBR APN-AMBR (R10 29.212) | Huawei | 29.212 | 0884r1 | 1 | Rel-10 | Agreed | 10.7.0 | PCC-Enh | F |
| C3-121726 | CR | External ID for SIMTC | Nokia Siemens Networks | 29.061 | 0384r3 | 3 | Rel-11 | Agreed | 11.1.0 | SIMTC-Reach | B |
| C3-121727 | CR | Removal of RAT-Type BBF-WLAN from the Gx/Gxx protocol | ZTE, Alcatel-Lucent,Ericsson | 29.212 | 0905r2 | 2 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121729 | CR | Functionality of the PCRF for EPC-routed in 29.215 | ZTE | 29.215 | 0265r2 | 2 | Rel-11 | Agreed | 11.5.0 | BBAI_BBI-CT | B |
| C3-121730 | CR | PCRF-initiated IP-CAN session termination for NSWO traffic | ZTE, | 29.213 | 0437r2 | 2 | Rel-11 | Agreed | 11.3.0 | BBAI_BBII-CT | B |
| C3-121731 | CR | Functionality fo the PCRF for NSWO in 29.215 | ZTE | 29.215 | 0268r2 | 2 | Rel-11 | Agreed | 11.5.0 | BBAI_BBII-CT | B |
| C3-121732 | CR | Reference list correction to align with the corrected TS 29.212 title | Allot Communications | 29.061 | 0385r1 | 1 | Rel-11 | Agreed | 11.1.0 | TEI11 | F |
| C3-121738 | CR | Correction of mapping for COLP-TIP second-first identity | Deutsche Telekom (Roland) | 29.163 | 0661r3 | 3 | Rel-8 | Agreed | 8.19.0 | REDOC_TIS-C3 | F |
| C3-121739 | CR | Correction of mapping for COLP-TIP second-first identity | Deutsche Telekom (Roland) | 29.163 | 0662r3 | 3 | Rel-9 | Agreed | 9.10.0 | REDOC_TIS-C3 | A |
| C3-121740 | CR | Correction of mapping for COLP-TIP second-first identity | Deutsche Telekom (Roland) | 29.163 | 0663r3 | 3 | Rel-10 | Agreed | 10.6.0 | REDOC_TIS-C3 | A |
| C3-121741 | CR | Correction of mapping for COLP-TIP second-first identity | Deutsche Telekom (Roland) | 29.163 | 0664r3 | 3 | Rel-11 | Agreed | 11.3.0 | REDOC_TIS-C3 | A |
| C3-121742 | CR | Unstructured Supplementary Service Data (USSD) | Ericsson | 29.165 | 0454r3 | 3 | Rel-11 | Agreed | 11.3.0 | USSI | B |
| C3-121746 | CR | Add IPXS to architecture | Ericsson | 29.165 | 0472r2 | 2 | Rel-11 | Agreed | 11.3.0 | IPXS | F |
| C3-121747 | CR | Loopback NNI | Nokia Siemens Networks | 29.165 | 0441r2 | 2 | Rel-11 | Agreed | 11.3.0 | RAVEL-CT | B |
| C3-121749 | CR | Roaming Option Item | Nokia Siemens Networks | 29.165 | 0442r3 | 3 | Rel-11 | Agreed | 11.3.0 | RAVEL-CT | B |
| C3-121752 | CR | Support of overload control | Alcatel-Lucent, AT&T / Keith Drage | 29.165 | 0470r3 | 3 | Rel-11 | Agreed | 11.3.0 | IOC | B |
| C3-121757 | CR | CS to PS access transfer | Ericsson | 29.165 | 0456r4 | 4 | Rel-11 | Agreed | 11.3.0 | rSRVCC-CT | B |
| C3-121758 | CR | Adding TRF into reference architecture | Nokia Siemens Networks | 29.165 | 0443r3 | 3 | Rel-11 | Agreed | 11.3.0 | RAVEL-CT | B |
| C3-121760 | CR | Support of T.38 related SDP attributes | Nokia Siemens Networks | 29.163 | 0669r3 | 3 | Rel-11 | Agreed | 11.3.0 | MMTel_T.38_FAX | B |
| C3-121761 | CR | Adding MIME body table and removing an EN - CT CR CORRELATION NEEDED | Ericsson | 29.165 | 0455r3 | 3 | Rel-11 | Agreed | 11.3.0 | II-NNI2 | F |

## Annex E. List of Participants

| Name | Representing | Status-Partner | Ctry | Ph | Mob Ph | Email |
| --- | --- | --- | --- | --- | --- | --- |
| Alberth, Bill (Mr.) | Motorola Mobility Germany GmbH | 3GPPMEMBER (ETSI) | GB | +44 780 2361 664 |  | bill.alberth@motorola.com |
| Allen, Andrew (Mr.) | Research in Motion Japan Ltd. | 3GPPMEMBER (ARIB) | US | +18478098636 |  | aallen@rim.com |
| Arai, Kenjiro (Mr.) | NTT | 3GPPMEMBER (TTC) |  | +81422593518 |  | arai.kenjiro@lab.ntt.cojp |
| Arreaga, Arturo (Mr.) | Rogers Wireless Inc. | 3GPPMEMBER (ATIS) | CA | +1 (647) 747 4223 |  | arturo.arreaga@rci.rogers.com |
| Axell, J?rgen (Dr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | SE | +46 10 719 4450 | +46 70 519 4450 | Jorgen.Axell@ericsson.com |
| Bakker, John-Luc (Mr.) | Research in Motion UK Limited | 3GPPMEMBER (ETSI) | GB | +1-972-373-1761 | +1-908-463-7321 | jbakker@rim.com |
| Belling, Thomas (Dr.) | Nokia Siemens Networks GmbH | 3GPPMEMBER (ETSI) | DE | +49 89 5159 75207 | +49 172 2974678 | Thomas.Belling@nsn.com |
| Berry, Nigel. H (Mr.) | Alcatel-Lucent Telecom Ltd | 3GPPMEMBER (ETSI) | GB | +44 1793775019 |  | Nigel.Berry@alcatel-lucent.com |
| BERTRAND, Simon (Mr.) | ORANGE SA | 3GPPMEMBER (ETSI) | FR | +33145294200 |  | simon.bertrand@orange.com |
| Biondic, Nevenka (Mrs.) | Ericsson Inc. | 3GPPMEMBER (ATIS) | HR | +385 1 365 3824 |  | nevenka.biondic@ericsson.com |
| Brinkmann, Horst (Mr.) | Alcatel-Lucent Deutschland AG | 3GPPMEMBER (ETSI) | DE | +49 711 821 37207 |  | horst.brinkmann@alcatel-lucent.com |
| Chowdhury, Sayan (Mr.) | Tekelec | 3GPPMEMBER (ATIS) | US | +1-508-804-7078 |  | sayan.chowdhury@tekelec.com |
| Dobrowolska, Beata (Ms.) | France Telecom | 3GPPMEMBER (ETSI) | FR | +33145295759 |  | beata.dobrowolska@orange.com |
| Dolly, Martin (Mr.) | AT&T | 3GPPMEMBER (ATIS) | US | +1 609 903 3360 |  | md3135@att.com |
| Drage, Keith (Mr.) | Alcatel-Lucent Telecom Ltd | 3GPPMEMBER (ETSI) | GB | +44 1793 897312 | +44 7799 658151 | Keith.Drage@alcatel-lucent.com |
| Emanuelsson, Sven-ove (Mr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | SE | +46107121548 |  | sven-ove.emanuelsson@ericsson.com |
| Farhoumand, Rouzbeh (Mr.) | HuaWei Technologies Co., Ltd | 3GPPMEMBER (ATIS) | US |  | +1-469-682-9924 | rouzbeh.farhoumand@huawei.com |
| Fernandez, Susana (Miss) | Nanjing Ericsson Panda Com Ltd | 3GPPMEMBER (CCSA) | ES | +34646006865 |  | susana.fernandez@ericsson.com |
| Gebler, Erik (Mr.) | Acision UK Ltd | 3GPPMEMBER (ETSI) | NL | +31 30 210 3173 | +31 624 241 655 | erik.gebler@acision.com |
| Gellert, Dorothy (Ms.) | INTERDIGITAL COMMUNICATIONS | 3GPPMEMBER (ETSI) | US | +1-650-796-9470 |  | dorothy.gellert@interdigital.com |
| Goldner, Alla (Mrs.) | Allot Communications Ltd. | 3GPPMEMBER (ETSI) | IL | +97297619251 |  | agoldner@allot.com |
| Han, Jiwan (Mr.) | ETSI | MCC | FR | +33 (4) 92 94 42 31 | +33 (0)6 74 40 83 69 | jiwan.han@etsi.org |
| Herrero-Veron, Christian (Mr.) | Huawei Technologies Japan Co., | 3GPPMEMBER (ARIB) | SE | +46739200806 |  | christian.herrero@huawei.com |
| Hodges, Phil (Mr.) | Ericsson Japan K.K. | 3GPPMEMBER (ARIB) | AU | +61 404069546 |  | philip.hodges@ericsson.com |
| Holm, Jan (Mr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | SE | +46 8 719 7378 | + 46705197378 | Jan.Holm@ericsson.com |
| Holmberg, Christer (Mr.) | Ericsson Japan K.K. | 3GPPMEMBER (ARIB) | SE | +35892992943 | +358405604412 | christer.holmberg@ericsson.com |
| Huelsemann, Martin (Mr.) | Telekom Deutschland GmbH | 3GPPMEMBER (ETSI) | DE | +49 6151 58 12765 |  | Martin.Huelsemann@telekom.de |
| Huslende, Ragnar (Dr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | NO | +47 911 10828 | +47 911 10828 | ragnar.huslende@ericsson.com |
| Inoue, Yoshihiro (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81 422 36 7502 |  | yoshihiro.inoue@ntt-at.co.jp |
| Itsuma, Tanaka (Mr.) | DOCOMO Communications Lab. | 3GPPMEMBER (ETSI) | DE | +81 90 3100 7242 |  | tanakai@nttdocomo.co.jp |
| Jesske, Roland (Mr.) | Deutsche Telekom AG | 3GPPMEMBER (ETSI) | DE | +49 6151 5812766 | +49 171 861 8445 | r.jesske@telekom.de |
| Jones, Mark (Mr.) | Amdocs Software Systems Ltd | 3GPPMEMBER (ETSI) | CA | +1-613-301-7758 |  | mark.jones@amdocs.com |
| Kanegae, Shunsuke (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81422596689 |  | kanegae.shunsuke@lab.ntt.co.jp |
| Lair, Yannick (Mr.) | NEC Technologies (UK) LTD | 3GPPMEMBER (ETSI) | GB | +33 1 55688227 |  | yannick.lair@nectech.fr |
| Landais, Bruno (Mr.) | Alcatel-Lucent | 3GPPMEMBER (ETSI) | FR | +33 2 96 04 82 61 |  | bruno.landais@alcatel-lucent.com |
| Lauster, Reinhard (Mr.) | T-Mobile Austria GmbH | 3GPPMEMBER (ETSI) | AT | +43 1 79585 7173 | +43 676 8200 7173 | reinhard.lauster@t-mobile.at |
| Lavasani, Shahab (Mr.) | Huawei Technologies Sweden AB | 3GPPMEMBER (ETSI) | SE | +46 70 6360204 | +46 70 6360204 | shahab.lavasani@huawei.com |
| Lee, Jay (Mr.) | Verizon Communications, Inc. | 3GPPMEMBER (ATIS) | US | +1-925-952-6747 |  | jay.lee@verizon.com |
| Lehane, Bart (Mr.) | Openet Telecom | 3GPPMEMBER (ETSI) | IE | +353 01 620 46 00 |  | bartlehane@openet.com |
| Liu, Jennifer (Ms.) | Alcatel-Lucent | 3GPPMEMBER (ATIS) | US | +1-972-477-8532 | +1-214-536-3185 | jennifer.liu@alcatel-lucent.com |
| Lu, Fei (Mr.) | ZTE Corporation | 3GPPMEMBER (ETSI) | CN | +86-25-88014634 | +86-13951628123 | lu.fei1@zte.com.cn |
| Lukacs, Donald (Mr.) | Applied Communication Sciences | 3GPPMEMBER (ATIS) |  | +17327585293 |  | dlukacs@appcomsci.com |
| Mase, Asami (Miss) | Oki Electric Industry Co. Ltd. | 3GPPMEMBER (TTC) | JP | + |  | mase622@oki.com |
| Matsuura, Takaaki (Mr.) | NTT DOCOMO INC. | 3GPPMEMBER (TTC) | JP | +81 468 40 3333 |  | takaaki.matsuura.sp@s1.nttdocomo.com |
| Mizukami, Takashi (Mr.) | Oki Electric Industry Co. Ltd. | 3GPPMEMBER (TTC) | JP | +81 80 5960 0444 |  | mizukami653@oki.com |
| Monrad, Atle (Mr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | NO | +47 45410665 | +47 454 10 665 | atle.monrad@ericsson.com |
| Morishige, Yoshihito (Mr.) | Fujitsu Limited | 3GPPMEMBER (ARIB) | JP | + |  | y-morishige@jp.fujitsu.com |
| Muto, Yuta (Mr.) | Hitachi Ltd. | 3GPPMEMBER (ARIB) | JP | +81-42-323-1111 |  | yuta.muto.nc@hitachi.com |
| Neal, Adrian (Dr.) | VODAFONE Group Plc | 3GPPMEMBER (ETSI) | GB | +44 7919555744 | +447919555744 | adrian.neal@vodafone.com |
| Oprescu, Val (Mr.) | Motorola Solutions Germany | 3GPPMEMBER (ETSI) | US | +1 847 576 3465 |  | voprescu@motorolasolutions.com |
| Pham, Quang truong (Mr.) | NEC Corporation | 3GPPMEMBER (ETSI) | JP | +81 3 3798 9259 |  | q-pham@az.jp.nec.com |
| Pianigiani, Jacopo (Ms.) | Juniper Networks | 3GPPMEMBER (ETSI) | US | +393357350536 |  | JPIANIGIANI@JUNIPER.NET |
| Procopio, Roberto (Mr.) | TELECOM ITALIA S.p.A. | 3GPPMEMBER (ETSI) | IT | +39 011 228 5061 |  | roberto.procopio@telecomitalia.it |
| Punz, Gottfried (Mr.) | NEC Telecom MODUS Ltd. | 3GPPMEMBER (ETSI) | GB | +49 6221 4342 119 |  | gottfried.punz@nw.neclab.eu |
| Qiao, Weihua (Mr.) | HuaWei Technologies Co., Ltd | 3GPPMEMBER (CCSA) | CN | +86 10 82882310 |  | qiaoweihua@huawei.com |
| Ramachandran, Shyamal (Mr.) | Qualcomm Korea | 3GPPMEMBER (TTA) | GB | +1 858 8453197 |  | shyamalr@qualcomm.com |
| Räsänen, Juha (Mr.) | Nokia Siemens Networks Oy | 3GPPMEMBER (ETSI) | FI | +358 7180 08000 | +358 40 543 9058 | juha.rasanen@nsn.com |
| Salot, Nirav (Mr.) | Cisco Systems Belgium | 3GPPMEMBER (ETSI) |  |  | +919326737733 | nsalot@cisco.com |
| Sasaki, Tetsuo (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81 43 211 3532 |  | t-sasaki@lab.ntt.co.jp |
| Schmitt, Peter (Mr.) | Huawei Technologies France | 3GPPMEMBER (ETSI) | CN |  | +49 171 7450251 | peter.schmitt@huawei.com |
| Shaikh, Viqar (Mr.) | Applied Communication Sciences | 3GPPMEMBER (ATIS) |  |  |  | vshaikh@appcomsci.com |
| Shi, Shufeng (Mrs.) | Huawei Technologies (UK) | 3GPPMEMBER (ETSI) |  | +862981775094 | +8613571984613 | susan.shishufeng@huawei.com |
| Shrader, David (Mr.) | Ericsson Inc. | 3GPPMEMBER (ATIS) | US | +9172130314 |  | david.shrader@ericsson.com |
| Shu, Lin (Mr.) | HiSilicon Technologies Co., Lt | 3GPPMEMBER (CCSA) | CN | +86-15216618582 |  | shulin@huawei.com |
| Subramanian, Ramachandran (Mr.) | Qualcomm Japan Inc | 3GPPMEMBER (ARIB) | US | +1 858 651 2350 |  | rsubrama@qualcomm.com |
| Suzuki, Naoaki (Mr.) | NEC Corporation | 3GPPMEMBER (ARIB) | JP | +81-4-7185-6722 |  | n-suzuki@en.jp.nec.com |
| Suzuki, Tomohiro (Mr.) | Fujitsu Limited | 3GPPMEMBER (TTC) | JP | +81 44 754 4160 |  | suzuki.tomohiro@jp.fujitsu.com |
| Takakura, Tsuyoshi (Mr.) | NTT DOCOMO INC. | 3GPPMEMBER (TTC) | JP | +81 468 40 3370 |  | takakurat@s1.nttdocomo.co.jp |
| Takeda, Shinya (Mr.) | NTT DOCOMO INC. | 3GPPMEMBER (ARIB) | JP | +046-840-3530 |  | takedash@nttdocomo.co.jp |
| Tamura, Toshiyuki (Mr.) | NEC Corporation | 3GPPMEMBER (TTC) | JP | +81 44 455 8496 |  | tamurato@aj.jp.nec.com |
| Vaidya, Rahul (Mr.) | Juniper Networks | 3GPPMEMBER (ETSI) | IN | +91-9886759942 |  | rahulv@juniper.net |
| Van Geel, Jan (Mr.) | BELGACOM | 3GPPMEMBER (ETSI) | BE | +32 2 202 10 35 | +32 477 841830 | jan.van.geel@belgacom.be |
| Wild, Peter A. (Mr.) | Vodafone Teknoloji Hizmetleri | 3GPPMEMBER (ETSI) | DE | +49 211 533 3798 | +49 172 7211170 | peter.wild@vodafone.com |
| Xia, Xu (Mr.) | ETSI | 3GPPORG_REP (ETSI) | CN | +861059722026 |  | xiatony@huawei.com |
| Yang, Xiangying (Dr.) | Apple France | 3GPPMEMBER (ETSI) | US | +1 408-862-0419 |  | xiangying_yang@apple.com |
| Yu, James (Dr.) | NeuStar Inc. | 3GPPMEMBER (ETSI) | US | +1 571-434-5572 | +1 703-622-5187 | james.yu@neustar.biz |
| Yu, Youyang (Miss) | Huawei Technologies Japan Co., | 3GPPMEMBER (ARIB) | CN | +13661409703 |  | yuyouyang@huawei.com |
| Zhou, Xiaoyun (Mr.) | ZTE Corporation | 3GPPMEMBER (CCSA) | CN | +8613813823840 |  | zhou.xiaoyun@zte.com.cn |
| Biondic, Nevenka (Mrs.) | Ericsson Inc. | 3GPPMEMBER (ATIS) | HR | +385 1 365 3824 |  | nevenka.biondic@ericsson.com |
| Han, Jiwan (Mr.) | KT Corp. | 3GPPMEMBER (TTA) | FR | +33 (4) 92 94 42 31 | +33 (0)6 74 40 83 69 | jiwan.han@etsi.org |
| Jones, Mark (Mr.) | Amdocs Software Systems Ltd | 3GPPMEMBER (ETSI) | CA | +1-613-301-7758 |  | mark.jones@amdocs.com |
| Lauster, Reinhard (Mr.) | T-Mobile Austria GmbH | 3GPPMEMBER (ETSI) | AT | +43 1 79585 7173 | +43 676 8200 7173 | reinhard.lauster@t-mobile.at |
| Liu, Jennifer (Ms.) | Alcatel-Lucent | 3GPPMEMBER (ATIS) | US | +1-972-477-8532 | +1-214-536-3185 | jennifer.liu@alcatel-lucent.com |
| Lu, Fei (Mr.) | ZTE Corporation | 3GPPMEMBER (ETSI) | CN | +86-25-88014634 | +86-13951628123 | lu.fei1@zte.com.cn |

Report prepared by: Jiwan HAN