Third Generation Partnership Project (3GPP™)

DRAFT Meeting Report
for
TSG CT WG3
meeting: 71

New Orleans, USA, 12/11/2012 to 16/11/2012

1	Opening of the meeting	6

2	Agenda/schedule	6

2.1	Approval of the agenda.	6

2.2	Proposed schedule	6

3	Registration of documents	6

4	Reports	7

4.1	Report from previous CT3 meeting	7

4.2	Report from previous CT plenary	7

4.3	Reports from other groups	8

5	Items for immediate consideration	8

5.1	IPR disclosures	8

5.2	Other items for immediate consideration	8

6	Received Liaison Statements	8

7	Release 7 and earlier releases	10

7.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	10

7.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	10

7.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]	10

7.4	Multimedia Broadcast and Multicast Service  [MBMS]	10

7.5	Policy and Charging Control [PCC]	10

7.6	Diameter for Gi interface [DIAMGi]	14

7.7	Diameter for Wi interface [DIAMWi]	14

7.8	Multimedia interworking between IMS and CS networks [MIW-IMS]	14

7.9	Protocol impact from providing IMS services via fixed broadband [FBI]	14

7.10	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]	14

7.11	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	14

7.12	Technical Enhancements and Improvements [TEIx]	14

7.13	Other Work Items	14

8	Release 8	14

8.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	14

8.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	14

8.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]	15

8.4	Multimedia Broadcast and Multicast Service  [MBMS]	15

8.5	Policy and Charging Control (non-SAE) [PCC]	15

8.6	Void	17

8.7	Diameter for Gi interface [DIAMGi]	17

8.8	Diameter for Wi interface [DIAMWi]	17

8.9	Multimedia interworking between IMS and CS networks (incl. MONA extensions) [MIW-IMS]	17

8.10	Protocol impact from providing IMS services via fixed broadband [FBI]	17

8.11	IMS Interworking Protocol Aspects in Support of Cable Rebulatory Requirements [PktCbl-Intw]	17

8.12	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]	17

8.13	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	17

8.14	PCC aspects of SAE [SAES-St3-PCC]	17

8.14.1	- Signalling flows (29.213)	17

8.14.2	- Gx and Gxx interfaces (29.212)	17

8.14.3	- Rx interface (29.214)	20

8.14.4	- S9 interface (29.215)	22

8.15	Interworking between EPC and external PDNs [SAES-St3-intwk]	22

8.16	IMS inter-operator service interconnection interface [FBI2-IOPSI]	23

8.17	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	24

8.18	Interworking between User-to-User Signaling (UUS) and SIP [UUSIW]	24

8.19	Work Items related to TISPAN transfer	24

8.19.1	- Maintenance of TISPAN R1 [MAINT_R1]	24

8.19.2	- Maintenance of TISPAN R2 [MAINT_R2]	24

8.19.3	- Documentation of TISPAN R1 and R2  in CT3 [REDOC_TIS-C3]	24

8.19.4	- Support of Overlap signalling [Overlap]	25

8.19.5	- Stage 3 (CT3) of CWonIMS [CW_IMS]	25

8.19.6	- Stage 3 (CT3) of [CCBS_CCNR]	25

8.20	Contributions on Common IMS related to 3GPP2 [REDOC_3GPP2]	25

8.21	Support of Service-Level Interworking for Messaging Services [MESSIW]	25

8.22	Enhancement of interworking between MTSI and Circuit Switched networks  [MTSI_eMHI]	25

8.23	Core Network Impacts for A-Interface Over IP [AoIP-CN]	25

8.24	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]	25

8.25	CAT solution for voice and video call in CS domain [CAT_SS]	26

8.26	Technical Enhancements and Improvements [TEI8]	26

8.27	Rel-8 contributions on other Work Items	26

9	Release 9	26

9.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	27

9.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	27

9.3	Protocol impact from providing IMS services via fixed broadband [FBI]	27

9.4	MBMS [MBMS]	27

9.5	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	27

9.6	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	27

9.7	PCC aspects of SAE [SAES-St3-PCC]	27

9.8	Reserved	27

9.9	Reserved	27

9.10	Reserved	27

9.11	Reserved	27

9.12	Reserved	27

9.13	Reserved	27

9.14	Reserved	27

9.15	Reserved	27

9.16	CS-IBCF and CS-TrGW definition in 3GPP specifications [CS-IBCF]	27

9.17	Interconnection Border Control Function (IBCF) – Transition Gateway (TrGW); Ix interface, Stage 3 [IMS_IBCF]	27

9.18	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	27

9.19	Operational Description of the Inter-IMS NNI [II-NNI]	27

9.20	Support for IMS Emergency Calls over GPRS and EPS [IMS_EMER_GPRS_EPS]	30

9.21	PCC Enhancements [PCC-Enh]	30

9.22	Completion of IMS Restoration Procedures [eIMS_RP]	30

9.23	CT1 aspects of SRVCC support for IMS Emergency Calls [IMS_EMER_GPRS_EPS-SRVCC]	30

9.24	IMS Media Plane Security [MEDIASEC_CORE]	31

9.25	Technical Enhancements and Improvements [TEI9]	31

9.26	Rel-9 contributions on other work items	31

10	Release 10	31

10.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	31

10.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	31

10.3	PCC aspects of SAE [SAES-St3-PCC]	31

10.4	Interworking between EPC and external PDNs [SAES-St3-intwk]	31

10.5	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	31

10.6	PCC Enhancements [PCC-Enh]	31

10.7	Reserved	32

10.8	Reserved	32

10.9	Reserved	32

10.10	Reserved	32

10.11	Reserved	32

10.12	Reserved	32

10.13	Reserved	32

10.14	Reserved	32

10.15	Reserved	32

10.16	CPM-SMS Interworking [CPM-SMS]	32

10.17	Optimal Media Routeing [OMR]	32

10.18	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]	33

10.19	Call Completion Not Logged in [CCNL]	38

10.20	IP Flow Mobility and WLAN offload (Stage 3) [IFOM-CT]	38

10.21	Enabling Coder Selection and Rate Adaption for UTRAN and E-UTRAN for Load Adaptive Applications, CN impacts [ECSRA_LAA-CN]	38

10.21.1	-  Packet Core impacts	38

10.21.2	-  IMS/CS impacts	38

10.22	S2b Mobility based on GTP [SMOG-St3]	39

10.23	CT aspects of Enhancements for Multimedia Priority Service [eMPS-CN]	39

10.24	PCRF failure and restoration [PCRF-FR]	39

10.25	CT aspects of Multi Access PDN Connectivity  [MAPCON-St3]	39

10.26	CT3 Aspects of Policy Enhancements for Sponsored Connectivity and Coherent Access to Policy related Data Bases [PEST-CT3]	39

10.27	Dynamic View of Headers in Messages for II-NNI [NNI_DV]	39

10.28	CS and IMS Interworking for CAT early session model [CIIC_ES]	40

10.29	Stage 3 for Network Improvements for Machine Type Communications [NIMTC]	40

10.30	Technical Enhancements and Improvements [TEI10]	40

10.31	Rel-10 contributions on other Work Items	40

11	Release 11	40

11.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	40

11.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	40

11.3	Policy Control and Charging [PCC]	40

11.4	Interworking between EPC and external PDNs [SAES-St3-intwk]	42

11.5	PCC aspects of SAE [SAES-St3-PCC]	42

11.6	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	44

11.7	PCC Enhancements [PCC-Enh]	44

11.8	Optimal Media Routeing [OMR]	45

11.9	Dynamic View of Headers in Messages for II-NNI [NNI_DV]	45

11.10	Reserved	45

11.11	Reserved	45

11.12	Reserved	45

11.13	Reserved	45

11.14	Reserved	45

11.15	Reserved	45

11.16	CT3 aspects of Service Awareness and Privacy Policies [SAPP-CT3]	45

11.17	CT3 aspects of QoS Control Based on Subscriber Spending Limits  [QoS_SSL-CT3]	47

11.18	USSD Simulation Service in IMS-stage 3 [USSI]	48

11.19	Single Radio Video Call Continuity       [vSRVCC-CT]	48

11.19.1	IMS-related	48

11.19.2	PCC-related	48

11.20	Further improvement of usability of II-NNI specification for inter-connection [NNI_OI]	48

11.21	IMS Stage-3 IETF Protocol Alignment          [IMSProtoc5]	49

11.22	CT aspects of Single Radio Voice Call Continuity from UTRAN/GERAN to E-UTRAN/HSPA [rSRVCC-CT]	50

11.22.1	IMS/CS related docs	51

11.22.2	Packet Core related docs	51

11.23	Stage 3 for System Improvements to Machine-Type Communications [SIMTC-Reach]	51

11.24	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block I [BBAI_BBI-CT]	53

11.25	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block II [BBAI_BBII-CT]	57

11.26	Void	58

11.27	CN aspects of Anonymous Call Rejection in the CS domain [ACR_CS-CN]	58

11.28	IMS Emergency PSAP Callback [EMC_PC]	58

11.29	Advanced Interconnection of Services [IPXS]	58

11.30	Enhancements for Multimedia Priority Service (MPS)  Gateway Control Priority [eMPS_Gateway]	58

11.31	CN aspects of Mobility based On GTP & PMIPv6 for WLAN access to EPC [SaMOG_WLAN-CN]	60

11.32	CN aspects of Service Identification for RRC Improvements in GERAN [SIRIG]	60

11.33	CT aspect on Network Provided Location Information for IMS [NWK-PL2IMS-CT]	60

11.34	II-NNI enhancements: SIP timers applicability [NNI_timers]	61

11.35	Roaming Architecture for Voice over IMS with Local Breakout – CT aspects [RAVEL-CT]	61

11.36	Inclusion of Media Resource Broker [MRB]	62

11.37	Enhanced T.38 FAX support [MMTel_T.38_FAX]	62

11.38	Enhanced Nodes Restoration for EPC [eNR_EPC]	63

11.39	IMS overload control [IOC]	63

11.40	Technical Enhancements and Improvements [TEI11]	64

11.41	Rel-11 contributions on other Work Items	64

11.41.1	Stage 3 for Support for 3GPP Voice Interworking with Enterprise IP-PBX [VINE-CT1]	65

11.41.2	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	65

11.41.3	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]	65

12	Release 12	65

12.1	Interworking between a PLMN with WLAN to access the EPC and a PDN [SAES_WLAN_EPC_intwk]	65

12.2	Technical Enhancements and Improvements [TEI12]	66

12.3	Rel-12 contributions on other Work Items	66

12.3.1	CT aspects of Extended IMS media plane security [eMEDIASEC_CT]	66

12.3.2	Indicating Use Case [IUC-CT]	66

12.3.3	DRVCC enhancements [eDRVCC]	66

12.3.4	IMS based Telepresence (Stage 3) [IMS_TELEP]	67

12.3.5	IMS Stage-3 IETF Protocol Alignment  [IMSProtoc6]	67

12.3.6	Synchronization between A Pair of  DRAs for PCRF addressing  [DRAs_Sync]	67

12.3.7	Other documents	68

13	Joint sessions	68

14	Work Organisation	68

14.1	Work Plan Review	68

14.2	Specification Review	68

14.3	Next meetings, allocation of hosts	69

15	Summary of results	69

16	Any other business	69

17	Closing of the meeting	69

Annex A. TS/TR	69

Annex B. Work Item	69

Annex C. Liaison Statements	70

Annex C.1 Incoming Liaison Statements	70

Annex C.2 Outgoing Liaison Statements	71

Annex D. Agreed Change Requests	71

Annex E. List of Participants	75

this draft:  Tuesday, (2012-11-27) 11:21  [date/time according to secretary's PC time zone setting]

Note: Hyperlinks to tdocs will work only if the present report is in a subdirectory named "report" and the tdocs themselves are in a parallel subdirectory names "docs".

## 1	Opening of the meeting

Dr. Ragnar Huslende, CT3 Chairman, opened CT3#71 in New Orleans, USA and warmly welcomed the delegates to the meeting on 09:00 Monday 12nd November 2012.

CT3 Chairman reminded the delegates the register with personal signature, no post-meeing registration, to wear the badge and to be prudent for using internet connection.

## 2	Agenda/schedule

### 2.1	Approval of the agenda.

C3-121767	Draft Agenda for the CT3#71 Meeting
					Source: CT3 Chairman

Decision: 		The document was Approved.

### 2.2	Proposed schedule

C3-121960	Proposed Schedule for CT3#71
					Source: CT3 Chairman

Decision: 		The document was Revised to C3-122055.

C3-122055	Proposed Schedule for CT3#71
					Source: CT3 Chairman

(Replaces C3-121960)

Decision: 		The document was Revised to C3-122111.

C3-122111	Proposed Schedule for CT3#71
					Source: CT3 Chairman

(Replaces C3-122055)

Decision: 		The document was Noted.

## 3	Registration of documents

C3-121769	Allocation of documents to agenda items (at Deadline)
					Source: CT3 Chairman

Discussion:

195 tdoc numbers were allocated at the deadline.

Decision: 		The document was Noted.

C3-121770	Allocation of documents to agenda items (Start of Day 1)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121771	Allocation of documents to agenda items (Start of Day 2)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121772	Allocation of documents to agenda items (Start of Day 3)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121773	Allocation of documents to agenda items (Start of Day 4)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121774	Allocation of documents to agenda items (Start of Day 5)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-121775	Allocation of documents to agenda items (End of Day 5)
					Source: CT3 Chairman

Discussion:

362 tdocs were produced at the end of  the meeting  (105 agreed CRs).

Decision: 		The document was Noted.

## 4	Reports

### 4.1	Report from previous CT3 meeting

C3-121776	Draft Meeting Report from CT3#70
					Source: MCC

Decision: 		The document was Approved.

### 4.2	Report from previous CT plenary

C3-121798	Brief Notes from CT#57 relevant to CT3
					Source: CT3 Chairman

Decision: 		The document was Noted.

### 4.3	Reports from other groups

## 5	Items for immediate consideration

### 5.1	IPR disclosures

CT3 Chairman reminded IPR policy of 3GPP to delegates.

### 5.2	Other items for immediate consideration

C3-121796	Proposed Revision of CT3 ToR
					Source: CT3 Chairman

Decision: 		The document was Agreed.

C3-121797	Draft References in CT3 Specifications
					Source: CT3 Chairman

Decision: 		The document was Noted.

## 6	Received Liaison Statements

C3-121780	Reply LS on GSMA Application Network Efficiency Task Force "whitepaper and actions"
					Source: TSG CT WG4

Decision: 		The document was Noted.

C3-121781	LS on GSMA Application Network Efficiency Task Force “whitepaper and actions”
					Source: TSG RAN WG2

Decision: 		The document was Noted.

C3-121782	LS on GSMA Application Network Efficiency Task Force “whitepaper and actions” 
					Source: TSG SA WG4

Decision: 		The document was Noted.

C3-121783	Reply LS on T.38 related work in CT WGs
					Source: TSG SA WG4

Decision: 		The document was Noted.

C3-121784	LS on GSMA Application Network Efficiency Task Force “whitepaper and actions” 
					Source: TSG SA WG5

Decision: 		The document was Noted.

C3-121785	LS on TS 32.299 AVPs for update in TS 29.230
					Source: TSG SA WG5

Discussion:

There is no impact to CT3.

Decision: 		The document was Noted.

C3-121786	LS on GSMA Application Network Efficiency Task Force "whitepaper and actions"
					Source: TSG CT

Decision: 		The document was Noted.

C3-121787	LS on GSMA Application Network Efficiency Task Force “whitepaper and actions”
					Source: TSG RAN

Decision: 		The document was Noted.

C3-121788	Reply to 3GPP Liaison Statement on RC Mapping
					Source: i3 Forum WG "Technical Aspects"

Discussion:

There was no consensus for CR in i3Forum.

Decision: 		The document was Noted.

C3-121789	LS on Charging issue regarding PCC and ADC Rules
					Source: TSG SA WG2

Discussion:

Related CRs are C3-121873, and C3-121920.

Decision: 		The document was Noted.

C3-121790	Reply LS on QoS parameters that can be upgraded and downgraded
					Source: TSG SA WG2

Discussion:

Related CRs are C3-121857 ~ C3-121861 (Rel-7 ~ Rel-11), C3-121897 ~ C3-121901 (Rel-7 ~ Rel-11), and C3-1804 ~ C3-121870 (Rel-8 ~ Rel-11).

Decision: 		The document was Noted.

C3-121791	Reply LS on PCC support for rSRVCC
					Source: TSG SA WG2

Discussion:

Related CRs are C3-121819, C3-121877 and C3-121906.

Decision: 		The document was Noted.

C3-121792	LS on Device Triggering Identification
					Source: TSG SA WG2

Discussion:

Reply LS is C3-121818 and the related reference is C3-121921.

Decision: 		The document was Noted.

C3-121963	Reply LS on Device Triggering Identification
					Source: TSG SA WG3

Decision: 		The document was Noted.

C3-121964	LS on SDP offer-answer negotiation of AVPF and CCM feedback messages
					Source: TSG SA WG4

Discussion:

Needing time for considering, temporary postponed till this week. CT3 will come back to check this LS after CT4's discussion. And finally it was postponed till the next meeting.

Decision: 		The document was Postponed.

## 7	Release 7 and earlier releases

Release 7 and earlier releases are frozen. Only essential category F and category A CRs are allowed.

### 7.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 7.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 7.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]

### 7.4	Multimedia Broadcast and Multicast Service  [MBMS]

### 7.5	Policy and Charging Control [PCC]

C3-121857	QoS parameters which can be upgraded or downgraded (R7 29.212)
					29.212	  CR-0920  (Rel-7) v7.14.0
					Source: Huawei

Decision: 		The document was Merged with C3-121897 into C3-122001.

C3-121858	QoS parameters which can be upgraded or downgraded (R8 29.212)
					29.212	  CR-0921  (Rel-8) v8.16.0
					Source: Huawei

Decision: 		The document was Merged with C3-121898 into C3-122002.

C3-121859	QoS parameters which can be upgraded or downgraded (R9 29.212)
					29.212	  CR-0922  (Rel-9) v9.11.0
					Source: Huawei

Decision: 		The document was Merged with C3-121899 into C3-122003.

C3-121860	QoS parameters which can be upgraded or downgraded (R10 29.212)
					29.212	  CR-0923  (Rel-10) v10.8.0
					Source: Huawei

Decision: 		The document was Merged with C3-121900 into C3-122004.

C3-121861	QoS parameters which can be upgraded or downgraded (R11 29.212)
					29.212	  CR-0924  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Merged with C3-121901 into C3-122005.

C3-121897	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0932  (Rel-7) v7.14.0
					Source: ZTE

Decision: 		The document was Merged with C3-121857 into C3-122001.

C3-121898	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0933  (Rel-8) v8.16.0
					Source: ZTE

Decision: 		The document was Merged with C3-121858 into C3-122002.

C3-121899	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0934  (Rel-9) v9.11.0
					Source: ZTE

Decision: 		The document was Merged with C3-121859 into C3-122003.

C3-121900	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0935  (Rel-10) v10.8.0
					Source: ZTE

Decision: 		The document was Merged with C3-121860 into C3-122004.

C3-121901	Clarification of QoS authorization in the case that QoS upgrated is not supported
					29.212	  CR-0936  (Rel-11) v11.6.0
					Source: ZTE

Decision: 		The document was Merged with C3-121861 into C3-122005.

C3-122001	QoS parameters which can be upgraded or downgraded (R7 29.212)
					29.212	  CR-0920  rev 1 (Rel-7) v7.14.0
					Source: Huawei

(Replaces C3-121857)

Decision: 		The document was Revised to C3-122074.

C3-122002	QoS parameters which can be upgraded or downgraded (R8 29.212)
					29.212	  CR-0921  rev 1 (Rel-8) v8.16.0
					Source: Huawei

(Replaces C3-121858)

Decision: 		The document was Revised to C3-122075.

C3-122003	QoS parameters which can be upgraded or downgraded (R9 29.212)
					29.212	  CR-0922  rev 1 (Rel-9) v9.11.0
					Source: Huawei

(Replaces C3-121859)

Decision: 		The document was Revised to C3-122076.

C3-122004	QoS parameters which can be upgraded or downgraded (R10 29.212)
					29.212	  CR-0923  rev 1 (Rel-10) v10.8.0
					Source: Huawei

(Replaces C3-121860)

Decision: 		The document was Revised to C3-122077.

C3-122005	QoS parameters which can be upgraded or downgraded (R11 29.212)
					29.212	  CR-0924  rev 1 (Rel-11) v11.6.0
					Source: Huawei

(Replaces C3-121861)

Decision: 		The document was Revised to C3-122078.

C3-122074	QoS parameters which can be upgraded or downgraded (R7 29.212)
					29.212	  CR-0920  rev 2 (Rel-7) v7.14.0
					Source: Huawei

(Replaces C3-122001)

Decision: 		The document was Agreed.

C3-122075	QoS parameters which can be upgraded or downgraded (R8 29.212)
					29.212	  CR-0921  rev 2 (Rel-8) v8.16.0
					Source: Huawei

(Replaces C3-122002)

Decision: 		The document was Revised to C3-122113.

C3-122076	QoS parameters which can be upgraded or downgraded (R9 29.212)
					29.212	  CR-0922  rev 2 (Rel-9) v9.11.0
					Source: Huawei

(Replaces C3-122003)

Decision: 		The document was Agreed.

C3-122077	QoS parameters which can be upgraded or downgraded (R10 29.212)
					29.212	  CR-0923  rev 2 (Rel-10) v10.8.0
					Source: Huawei

(Replaces C3-122004)

Decision: 		The document was Agreed.

C3-122078	QoS parameters which can be upgraded or downgraded (R11 29.212)
					29.212	  CR-0924  rev 2 (Rel-11) v11.6.0
					Source: Huawei

(Replaces C3-122005)

Decision: 		The document was Agreed.

C3-122113	QoS parameters which can be upgraded or downgraded (R8 29.212)
					29.212	  CR-0921  rev 3 (Rel-8) v8.16.0
					Source: Huawei, ZTE

(Replaces C3-122075)

Decision: 		The document was Agreed.

### 7.6	Diameter for Gi interface [DIAMGi]

### 7.7	Diameter for Wi interface [DIAMWi]

### 7.8	Multimedia interworking between IMS and CS networks [MIW-IMS]

### 7.9	Protocol impact from providing IMS services via fixed broadband [FBI]

### 7.10	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]

### 7.11	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 7.12	Technical Enhancements and Improvements [TEIx]

### 7.13	Other Work Items

## 8	Release 8

Release 8 is frozen. Only essential category F and category A CRs are allowed.

### 8.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 8.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-121949	cpc in PAI 29.163r8
					29.163	  CR-0695  (Rel-8) v8.20.0
					Source: Orange

Discussion:

Postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121950	cpc in PAI 29.163r9
					29.163	  CR-0696  (Rel-9) v9.11.0
					Source: Orange

Discussion:

Postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121951	cpc in PAI 29.163r10
					29.163	  CR-0697  (Rel-10) v10.7.0
					Source: Orange

Discussion:

Postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121952	cpc in PAI 29.163r11
					29.163	  CR-0698  (Rel-11) v11.4.0
					Source: Orange

Discussion:

Postponed till the next meeting.

Decision: 		The document was Postponed.

### 8.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]

### 8.4	Multimedia Broadcast and Multicast Service  [MBMS]

### 8.5	Policy and Charging Control (non-SAE) [PCC]

C3-121902	Bearer binding mechenism for GPRS
					29.212	  CR-0937  (Rel-8) v8.16.0
					Source: ZTE

Decision: 		The document was Revised to C3-122006.

C3-121903	Bearer binding mechenism for GPRS
					29.212	  CR-0938  (Rel-9) v9.11.0
					Source: ZTE

Decision: 		The document was Revised to C3-122007.

C3-121904	Bearer binding mechenism for GPRS
					29.212	  CR-0939  (Rel-10) v10.8.0
					Source: ZTE

Decision: 		The document was Revised to C3-122008.

C3-121905	Bearer binding mechenism for GPRS
					29.212	  CR-0940  (Rel-11) v11.6.0
					Source: ZTE

Decision: 		The document was Revised to C3-122009.

C3-122006	Bearer binding mechenism for GPRS
					29.212	  CR-0937  rev 1 (Rel-8) v8.16.0
					Source: ZTE

(Replaces C3-121902)

Decision: 		The document was Agreed.

C3-122007	Bearer binding mechenism for GPRS
					29.212	  CR-0938  rev 1 (Rel-9) v9.11.0
					Source: ZTE

(Replaces C3-121903)

Decision: 		The document was Agreed.

C3-122008	Bearer binding mechenism for GPRS
					29.212	  CR-0939  rev 1 (Rel-10) v10.8.0
					Source: ZTE

(Replaces C3-121904)

Decision: 		The document was Agreed.

C3-122009	Bearer binding mechenism for GPRS
					29.212	  CR-0940  rev 1 (Rel-11) v11.6.0
					Source: ZTE

(Replaces C3-121905)

Decision: 		The document was Agreed.

### 8.6	Void

### 8.7	Diameter for Gi interface [DIAMGi]

### 8.8	Diameter for Wi interface [DIAMWi]

### 8.9	Multimedia interworking between IMS and CS networks (incl. MONA extensions) [MIW-IMS]

### 8.10	Protocol impact from providing IMS services via fixed broadband [FBI]

### 8.11	IMS Interworking Protocol Aspects in Support of Cable Rebulatory Requirements [PktCbl-Intw]

### 8.12	Bandwidth Saving at Nb Interface with IP transport [BSNbIP]

### 8.13	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 8.14	PCC aspects of SAE [SAES-St3-PCC]

Related CRs affecting several  PCC TSs  may be grouped together directly under agenda item 8.14. Changes affecting only one  PCC TS should be put under the respective sub-items  8.14.1/2/3/4 below.

#### 8.14.1	- Signalling flows (29.213)

#### 8.14.2	- Gx and Gxx interfaces (29.212)

C3-121804	QCI and ARP handling, Gn connected P-GW
					29.212	  CR-0913  (Rel-8) v8.16.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122010.

C3-121805	QCI and ARP handling, Gn connected P-GW
					29.212	  CR-0914  (Rel-9) v9.11.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122011.

C3-121806	QCI and ARP handling, Gn connected P-GW
					29.212	  CR-0915  (Rel-10) v10.8.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122012.

C3-121807	QCI and ARP handling, Gn connected P-GW
					29.212	  CR-0916  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122013.

C3-121932	TFT usage for the primary PDP context when using PGW (R8 29.212)
					29.212	  CR-0945  (Rel-8) v8.16.0
					Source: Huawei

Decision: 		The document was Revised to C3-122079.

C3-121933	TFT usage for the primary PDP context when using PGW (R9 29.212)
					29.212	  CR-0946  (Rel-9) v9.11.0
					Source: Huawei

Decision: 		The document was Revised to C3-122080.

C3-121934	TFT usage for the primary PDP context when using PGW (R10 29.212)
					29.212	  CR-0947  (Rel-10) v10.8.0
					Source: Huawei

Decision: 		The document was Revised to C3-122081.

C3-121935	TFT usage for the primary PDP context when using PGW (R11 29.212)
					29.212	  CR-0948  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Revised to C3-122082.

C3-122010	QCI and ARP handling, Gn connected P-GW
					29.212	  CR-0913  rev 1 (Rel-8) v8.16.0
					Source: Ericsson

(Replaces C3-121804)

Decision: 		The document was Agreed.

C3-122011	QCI and ARP handling, Gn connected P-GW
					29.212	  CR-0914  rev 1 (Rel-9) v9.11.0
					Source: Ericsson

(Replaces C3-121805)

Decision: 		The document was Agreed.

C3-122012	QCI and ARP handling, Gn connected P-GW
					29.212	  CR-0915  rev 1 (Rel-10) v10.8.0
					Source: Ericsson

(Replaces C3-121806)

Decision: 		The document was Agreed.

C3-122013	QCI and ARP handling, Gn connected P-GW
					29.212	  CR-0916  rev 1 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-121807)

Discussion:

Congratulations! Mr.Sven-ove Emanuelsson is the lucky number winner! Sven-ove will receive the prize from MCC in the next meeting!

Decision: 		The document was Agreed.

C3-122079	TFT usage for the primary PDP context when using PGW (R8 29.212)
					29.212	  CR-0945  rev 1 (Rel-8) v8.16.0
					Source: Huawei

(Replaces C3-121932)

Decision: 		The document was Revised to C3-122109.

C3-122080	TFT usage for the primary PDP context when using PGW (R9 29.212)
					29.212	  CR-0946  rev 1 (Rel-9) v9.11.0
					Source: Huawei

(Replaces C3-121933)

Decision: 		The document was Revised to C3-122115.

C3-122081	TFT usage for the primary PDP context when using PGW (R10 29.212)
					29.212	  CR-0947  rev 1 (Rel-10) v10.8.0
					Source: Huawei

(Replaces C3-121934)

Decision: 		The document was Revised to C3-122116.

C3-122082	TFT usage for the primary PDP context when using PGW (R11 29.212)
					29.212	  CR-0948  rev 1 (Rel-11) v11.6.0
					Source: Huawei

(Replaces C3-121935)

Decision: 		The document was Revised to C3-122117.

C3-122109	TFT usage for the primary PDP context when using PGW (R8 29.212)
					29.212	  CR-0945  rev 2 (Rel-8) v8.16.0
					Source: Huawei

(Replaces C3-122079)

Decision: 		The document was Revised to C3-122114.

C3-122114	TFT usage for the primary PDP context when using PGW (R8 29.212)
					29.212	  CR-0945  rev 3 (Rel-8) v8.16.0
					Source: Huawei

(Replaces C3-122109)

Decision: 		The document was Agreed.

C3-122115	TFT usage for the primary PDP context when using PGW (R9 29.212)
					29.212	  CR-0946  rev 2 (Rel-9) v9.11.0
					Source: Huawei

(Replaces C3-122080)

Decision: 		The document was Agreed.

C3-122116	TFT usage for the primary PDP context when using PGW (R10 29.212)
					29.212	  CR-0947  rev 2 (Rel-10) v10.8.0
					Source: Huawei

(Replaces C3-122081)

Decision: 		The document was Agreed.

C3-122117	TFT usage for the primary PDP context when using PGW (R11 29.212)
					29.212	  CR-0948  rev 2 (Rel-11) v11.6.0
					Source: Huawei

(Replaces C3-122082)

Decision: 		The document was Agreed.

#### 8.14.3	- Rx interface (29.214)

C3-121808	PCC procedures for Rx sessions with no service information
					29.214	  CR-0248  (Rel-8) v8.13.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122070.

C3-121809	PCC procedures for Rx sessions with no service information
					29.214	  CR-0249  (Rel-9) v9.10.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122071.

C3-121810	PCC procedures for Rx sessions with no service information
					29.214	  CR-0250  (Rel-10) v10.7.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122072.

C3-121811	PCC procedures for Rx sessions with no service information
					29.214	  CR-0251  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122073.

C3-121944	Clarification of Supported-Features AVP (29.214 R8)
					29.214	  CR-0256  (Rel-8) v8.13.0
					Source: Alcatel-Lucent

Discussion:

C3-121799 and related CRs had provided a better solution. It was withdrawn by request.

Decision: 		The document was Withdrawn.

C3-121945	Clarification of Supported-Features AVP (29.214 R9)
					29.214	  CR-0257  (Rel-9) v9.10.0
					Source: Alcatel-Lucent

Decision: 		The document was Withdrawn.

C3-121946	Clarification of Supported-Features AVP (29.214 R10)
					29.214	  CR-0258  (Rel-10) v10.7.0
					Source: Alcatel-Lucent

Decision: 		The document was Withdrawn.

C3-121947	Clarification of Supported-Features AVP (29.214 R11)
					29.214	  CR-0259  (Rel-11) v11.6.0
					Source: Alcatel-Lucent

Decision: 		The document was Withdrawn.

C3-122070	PCC procedures for Rx sessions with no service information
					29.214	  CR-0248  rev 1 (Rel-8) v8.13.0
					Source: Ericsson

(Replaces C3-121808)

Decision: 		The document was Agreed.

C3-122092	PCC procedures for Rx sessions with no service information
					29.214	  CR-0249  rev 1 (Rel-9) v9.10.0
					Source: Ericsson

(Replaces C3-121809)

Decision: 		The document was Agreed.

C3-122093	PCC procedures for Rx sessions with no service information
					29.214	  CR-0250  rev 1 (Rel-10) v10.7.0
					Source: Ericsson

(Replaces C3-121810)

Decision: 		The document was Agreed.

C3-122094	PCC procedures for Rx sessions with no service information
					29.214	  CR-0251  rev 1 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-121811)

Decision: 		The document was Agreed.

#### 8.14.4	- S9 interface (29.215)

### 8.15	Interworking between EPC and external PDNs [SAES-St3-intwk]

C3-121862	Preconfigured packet filters and PCC rules for dedicated signalling bearer (R8 29.061)
					29.061	  CR-0386  (Rel-8) v8.10.0
					Source: Huawei

Decision: 		The document was Agreed.

C3-121863	Preconfigured packet filters and PCC rules for dedicated signalling bearer (R9 29.061)
					29.061	  CR-0387  (Rel-9) v9.10.0
					Source: Huawei

Decision: 		The document was Agreed.

C3-121864	Preconfigured packet filters and PCC rules for dedicated signalling bearer (R10 29.061)
					29.061	  CR-0388  (Rel-10) v10.7.0
					Source: Huawei

Decision: 		The document was Agreed.

C3-121865	Preconfigured packet filters and PCC rules for dedicated signalling bearer (R11 29.061)
					29.061	  CR-0389  (Rel-11) v11.2.0
					Source: Huawei

Decision: 		The document was Agreed.

### 8.16	IMS inter-operator service interconnection interface [FBI2-IOPSI]

C3-121886	Correcting a reference for trust relationship
					29.165	  CR-0494  (Rel-8) v8.11.0
					Source: NTT

Decision: 		The document was Withdrawn.

C3-121887	Correcting a reference for trust relationship
					29.165	  CR-0495  (Rel-9) v9.12.0
					Source: NTT

Decision: 		The document was Withdrawn.

C3-121888	Correcting a reference for trust relationship
					29.165	  CR-0496  (Rel-10) v10.9.0
					Source: NTT

Decision: 		The document was Withdrawn.

C3-121889	Correcting a reference for trust relationship
					29.165	  CR-0497  (Rel-11) v11.4.0
					Source: NTT

Decision: 		The document was Revised to C3-122053.

C3-122053	Correcting a reference for trust relationship
					29.165	  CR-0497  rev 1 (Rel-11) v11.4.0
					Source: NTT

(Replaces C3-121889)

Discussion:

Category was changed to "F". It was postponed till the next meeting.

Decision: 		The document was Postponed.

### 8.17	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

### 8.18	Interworking between User-to-User Signaling (UUS) and SIP [UUSIW]

### 8.19	Work Items related to TISPAN transfer

#### 8.19.1	- Maintenance of TISPAN R1 [MAINT_R1]

#### 8.19.2	- Maintenance of TISPAN R2 [MAINT_R2]

#### 8.19.3	- Documentation of TISPAN R1 and R2  in CT3 [REDOC_TIS-C3]

C3-121955	RTTI 29.658r8
					29.658	  CR-0016  rev 2 (Rel-8) v8.5.0
					Source: Orange

Decision: 		The document was Postponed.

C3-121956	RTTI 29.658r9
					29.658	  CR-0017  rev 2 (Rel-9) v9.1.0
					Source: Orange

Decision: 		The document was Postponed.

C3-121957	RTTI 29.658r10
					29.658	  CR-0018  rev 2 (Rel-10) v10.1.0
					Source: Orange

Decision: 		The document was Postponed.

C3-121958	RTTI 29.658r11
					29.658	  CR-0019  (Rel-11) v10.1.0
					Source: Orange

Decision: 		The document was Postponed.

#### 8.19.4	- Support of Overlap signalling [Overlap]

#### 8.19.5	- Stage 3 (CT3) of CWonIMS [CW_IMS]

#### 8.19.6	- Stage 3 (CT3) of [CCBS_CCNR]

### 8.20	Contributions on Common IMS related to 3GPP2 [REDOC_3GPP2]

### 8.21	Support of Service-Level Interworking for Messaging Services [MESSIW]

### 8.22	Enhancement of interworking between MTSI and Circuit Switched networks  [MTSI_eMHI]

### 8.23	Core Network Impacts for A-Interface Over IP [AoIP-CN]

### 8.24	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]

C3-121841	IMSI detach in MSC Server
					29.292	  CR-0055  (Rel-8) v8.6.0
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-121842	IMSI detach in MSC Server
					29.292	  CR-0056  (Rel-9) v9.2.0
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-121843	IMSI detach in MSC Server
					29.292	  CR-0057  (Rel-10) v10.3.0
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-121844	IMSI detach in MSC Server
					29.292	  CR-0058  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122054.

C3-122054	IMSI detach in MSC Server
					29.292	  CR-0058  rev 1 (Rel-11) v11.3.0
					Source: Ericsson

(Replaces C3-121844)

Discussion:

Category is changed to "F".

Decision: 		The document was Agreed.

### 8.25	CAT solution for voice and video call in CS domain [CAT_SS]

### 8.26	Technical Enhancements and Improvements [TEI8]

### 8.27	Rel-8 contributions on other Work Items

## 9	Release 9

Release 9 is frozen. Only essential categoy F and category A CRs are allowed.

### 9.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 9.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 9.3	Protocol impact from providing IMS services via fixed broadband [FBI]

### 9.4	MBMS [MBMS]

### 9.5	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 9.6	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

### 9.7	PCC aspects of SAE [SAES-St3-PCC]

### 9.8	Reserved

### 9.9	Reserved

### 9.10	Reserved

### 9.11	Reserved

### 9.12	Reserved

### 9.13	Reserved

### 9.14	Reserved

### 9.15	Reserved

### 9.16	CS-IBCF and CS-TrGW definition in 3GPP specifications [CS-IBCF]

### 9.17	Interconnection Border Control Function (IBCF) – Transition Gateway (TrGW); Ix interface, Stage 3 [IMS_IBCF]

### 9.18	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 9.19	Operational Description of the Inter-IMS NNI [II-NNI]

C3-121827	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0476  (Rel-9) v9.12.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121970.

C3-121828	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0477  (Rel-10) v10.9.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121971.

C3-121829	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0478  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121972.

C3-121833	Trust domain error corrections
					29.165	  CR-0480  (Rel-9) v9.12.0
					Source: Ericsson

Discussion:

WI should be changed to II-NNI in coverpage.

Decision: 		The document was Revised to C3-121933.

C3-121834	Trust domain error corrections
					29.165	  CR-0481  (Rel-10) v10.9.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121974.

C3-121835	Trust domain error corrections
					29.165	  CR-0482  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121975.

C3-121970	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0476  rev 1 (Rel-9) v9.12.0
					Source: Ericsson

(Replaces C3-121827)

Decision: 		The document was Agreed.

C3-121971	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0477  rev 1 (Rel-10) v10.9.0
					Source: Ericsson

(Replaces C3-121828)

Decision: 		The document was Revised to C3-122022.

C3-121972	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0478  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121829)

Decision: 		The document was Agreed.

C3-121973	Trust domain error corrections
					29.165	  CR-0480  rev 1 (Rel-9) v9.12.0
					Source: Ericsson

(Replaces C3-121833)

Decision: 		The document was Agreed.

C3-121974	Trust domain error corrections
					29.165	  CR-0481  rev 1 (Rel-10) v10.9.0
					Source: Ericsson

(Replaces C3-121834)

Decision: 		The document was Agreed.

C3-121975	Trust domain error corrections
					29.165	  CR-0482  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121835)

Decision: 		The document was Agreed.

C3-122022	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0477  rev 2 (Rel-10) v10.9.0
					Source: Ericsson

(Replaces C3-121971)

Decision: 		The document was Revised to C3-122025.

C3-122025	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0477  rev 3 (Rel-10) v10.9.0
					Source: Ericsson

(Replaces C3-122022)

Decision: 		The document was Revised to C3-122101.

C3-122101	Removal of draft-dawes-dispatch-mediasec-parameter draft
					29.165	  CR-0477  rev 4 (Rel-10) v10.9.0
					Source: Ericsson

(Replaces C3-122025)

Decision: 		The document was Agreed.

### 9.20	Support for IMS Emergency Calls over GPRS and EPS [IMS_EMER_GPRS_EPS]

### 9.21	PCC Enhancements [PCC-Enh]

### 9.22	Completion of IMS Restoration Procedures [eIMS_RP]

### 9.23	CT1 aspects of SRVCC support for IMS Emergency Calls [IMS_EMER_GPRS_EPS-SRVCC]

C3-121893	Updating IMEI URN draft reference
					29.163	  CR-0690  (Rel-9) v9.11.0
					Source: Research in Motion

Decision: 		The document was Revised to C3-121976.

C3-121894	Updating IMEI URN draft reference
					29.163	  CR-0691  (Rel-10) v10.7.0
					Source: Research in Motion

Decision: 		The document was Revised to C3-121977.

C3-121895	Updating IMEI URN draft reference
					29.163	  CR-0692  (Rel-11) v11.4.0
					Source: Research in Motion

Decision: 		The document was Revised to C3-121978.

C3-121976	Updating IMEI URN draft reference
					29.163	  CR-0690  rev 1 (Rel-9) v9.11.0
					Source: Research in Motion

(Replaces C3-121893)

Decision: 		The document was Agreed.

C3-121977	Updating IMEI URN draft reference
					29.163	  CR-0691  rev 1 (Rel-10) v10.7.0
					Source: Research in Motion

(Replaces C3-121894)

Decision: 		The document was Agreed.

C3-121978	Updating IMEI URN draft reference
					29.163	  CR-0692  rev 1 (Rel-11) v11.4.0
					Source: Research in Motion

(Replaces C3-121895)

Decision: 		The document was Agreed.

### 9.24	IMS Media Plane Security [MEDIASEC_CORE]

### 9.25	Technical Enhancements and Improvements [TEI9]

### 9.26	Rel-9 contributions on other work items

## 10	Release 10

Release 10 is frozen. Only essential category F and category A CRs are allowed.

### 10.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 10.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 10.3	PCC aspects of SAE [SAES-St3-PCC]

### 10.4	Interworking between EPC and external PDNs [SAES-St3-intwk]

### 10.5	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 10.6	PCC Enhancements [PCC-Enh]

C3-121812	Correction on sponsored connectivity procedures
					29.213	  CR-0439  (Rel-10) v10.7.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121813	Correction on sponsored connectivity procedures
					29.213	  CR-0440  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Agreed.

### 10.7	Reserved

### 10.8	Reserved

### 10.9	Reserved

### 10.10	Reserved

### 10.11	Reserved

### 10.12	Reserved

### 10.13	Reserved

### 10.14	Reserved

### 10.15	Reserved

### 10.16	CPM-SMS Interworking [CPM-SMS]

### 10.17	Optimal Media Routeing [OMR]

C3-121824	Reference update of draft-ietf-mediactrl-mixer-control-package
					29.079	  CR-0017  (Rel-10) v10.3.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121825	Reference update of draft-ietf-mediactrl-mixer-control-package
					29.079	  CR-0018  (Rel-11) v11.1.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121883	OMR Signalling Flows
					29.079	  CR-0019  (Rel-10) v10.3.0
					Source: Huawei

Decision: 		The document was Revised to C3-121979.

C3-121884	OMR Signalling Flows
					29.079	  CR-0020  (Rel-11) v11.1.0
					Source: Huawei

Decision: 		The document was Revised to C3-121980.

C3-121979	OMR Signalling Flows
					29.079	  CR-0019  rev 1 (Rel-10) v10.3.0
					Source: Huawei

(Replaces C3-121883)

Decision: 		The document was Revised to C3-122023.

C3-121980	OMR Signalling Flows
					29.079	  CR-0020  rev 1 (Rel-11) v11.1.0
					Source: Huawei

(Replaces C3-121884)

Decision: 		The document was Revised to C3-122024.

C3-122023	OMR Signalling Flows
					29.079	  CR-0019  rev 2 (Rel-10) v10.3.0
					Source: Huawei

(Replaces C3-121979)

Decision: 		The document was Agreed.

C3-122024	OMR Signalling Flows
					29.079	  CR-0020  rev 2 (Rel-11) v11.1.0
					Source: Huawei

(Replaces C3-121980)

Decision: 		The document was Agreed.

### 10.18	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]

C3-121793	Clarification of SDP setting condition over the II-NNI
					29.165	  CR-0473  (Rel-10) v10.9.0
					Source: Fujitsu, NTT

Decision: 		The document was Revised to C3-122043.

C3-121794	Clarification of SDP setting condition over the II-NNI
					29.165	  CR-0474  (Rel-11) v11.4.0
					Source: Fujitsu, NTT

Decision: 		The document was Revised to C3-122044.

C3-121845	Reference update: draft-ietf-sipcore-proxy-feature
					29.165	  CR-0488  (Rel-10) v10.9.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121846	Reference update: draft-ietf-sipcore-proxy-feature
					29.165	  CR-0489  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121854	Clarification for call release due to user plane transport related errors
					29.165	  CR-0491  (Rel-10) v10.9.0
					Source: NEC, NTT

Decision: 		The document was Revised to C3-122045.

C3-121855	Clarification for call release due to user plane transport related errors
					29.165	  CR-0492  (Rel-11) v11.4.0
					Source: NEC, NTT

Decision: 		The document was Revised to C3-122046.

C3-121890	Description of charging correlation over II-NNI
					29.165	  CR-0498  (Rel-10) v10.9.0
					Source: NTT

Decision: 		The document was Revised to C3-122047.

C3-121891	Description of charging correlation over II-NNI
					29.165	  CR-0499  (Rel-11) v11.4.0
					Source: NTT

Decision: 		The document was Revised to C3-122048.

C3-121953	Policy-Contact in OMA 29.165r10
					29.165	  CR-0502  (Rel-10) v10.9.0
					Source: Orange

Decision: 		The document was Revised to C3-122049.

C3-121954	Policy-Contact in OMA 29.165r11
					29.165	  CR-0503  (Rel-11) v11.4.0
					Source: Orange

Decision: 		The document was Revised to C3-122050.

C3-122026	Clarification of SDP setting condition over the II-NNI
					29.165	  CR-0473  rev 2 (Rel-10) v10.9.0
					Source: Fujitsu, NTT

(Replaces C3-122043)

Decision: 		The document was Agreed.

C3-122027	Clarification of SDP setting condition over the II-NNI
					29.165	  CR-0474  rev 2 (Rel-11) v11.4.0
					Source: Fujitsu, NTT

(Replaces C3-122044)

Decision: 		The document was Agreed.

C3-122028	Description of charging correlation over II-NNI
					29.165	  CR-0498  rev 2 (Rel-10) v10.9.0
					Source: NTT

(Replaces C3-122047)

Decision: 		The document was Revised to C3-122118.

C3-122029	Description of charging correlation over II-NNI
					29.165	  CR-0499  rev 2 (Rel-11) v11.4.0
					Source: NTT

(Replaces C3-122048)

Decision: 		The document was Revised to C3-122119.

C3-122030	Policy-Contact in OMA 29.165r10
					29.165	  CR-0502  rev 2 (Rel-10) v10.9.0
					Source: Orange

(Replaces C3-122049)

Decision: 		The document was Revised to C3-122102.

C3-122043	Clarification of SDP setting condition over the II-NNI
					29.165	  CR-0473  rev 1 (Rel-10) v10.9.0
					Source: Fujitsu, NTT

(Replaces C3-121793)

Decision: 		The document was Revised to C3-122026.

C3-122044	Clarification of SDP setting condition over the II-NNI
					29.165	  CR-0474  rev 1 (Rel-11) v11.4.0
					Source: Fujitsu, NTT

(Replaces C3-121794)

Decision: 		The document was Revised to C3-122027.

C3-122045	Clarification for call release due to user plane transport related errors
					29.165	  CR-0491  rev 1 (Rel-10) v10.9.0
					Source: NEC, NTT

(Replaces C3-121854)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-122046	Clarification for call release due to user plane transport related errors
					29.165	  CR-0492  rev 1 (Rel-11) v11.4.0
					Source: NEC, NTT

(Replaces C3-121855)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-122047	Description of charging correlation over II-NNI
					29.165	  CR-0498  rev 1 (Rel-10) v10.9.0
					Source: NTT

(Replaces C3-121890)

Decision: 		The document was Revised to C3-122028.

C3-122048	Description of charging correlation over II-NNI
					29.165	  CR-0499  rev 1 (Rel-11) v11.4.0
					Source: NTT

(Replaces C3-121891)

Decision: 		The document was Revised to C3-122029.

C3-122049	Policy-Contact in OMA 29.165r10
					29.165	  CR-0502  rev 1 (Rel-10) v10.9.0
					Source: Orange

(Replaces C3-121953)

Decision: 		The document was Revised to C3-122101.

C3-122050	Policy-Contact in OMA 29.165r11
					29.165	  CR-0503  rev 1 (Rel-11) v11.4.0
					Source: Orange

(Replaces C3-121954)

Decision: 		The document was Revised to C3-122102.

C3-122071	Policy-Contact in OMA 29.165r11
					29.165	  CR-0503  rev 2 (Rel-11) v11.4.0
					Source: Orange

(Replaces C3-122050)

Decision: 		The document was Agreed.

C3-122102	Policy-Contact in OMA 29.165r10
					29.165	  CR-0502  rev 3 (Rel-10) v10.9.0
					Source: Orange

(Replaces C3-122030)

Decision: 		The document was Agreed.

C3-122118	Description of charging correlation over II-NNI
					29.165	  CR-0498  rev 3 (Rel-10) v10.9.0
					Source: NTT

(Replaces C3-122028)

Decision: 		The document was Agreed.

C3-122119	Description of charging correlation over II-NNI
					29.165	  CR-0499  rev 3 (Rel-11) v11.4.0
					Source: NTT

(Replaces C3-122029)

Decision: 		The document was Revised to C3-122122.

C3-122122	Description of charging correlation over II-NNI
					29.165	  CR-0499  rev 4 (Rel-11) v11.4.0
					Source: NTT

(Replaces C3-122119)

Decision: 		The document was Agreed.

### 10.19	Call Completion Not Logged in [CCNL]

### 10.20	IP Flow Mobility and WLAN offload (Stage 3) [IFOM-CT]

### 10.21	Enabling Coder Selection and Rate Adaption for UTRAN and E-UTRAN for Load Adaptive Applications, CN impacts [ECSRA_LAA-CN]

#### 10.21.1	-  Packet Core impacts

#### 10.21.2	-  IMS/CS impacts

C3-121848	Reference update: RFC 6679
					29.162	  CR-0113  (Rel-10) v10.6.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122051.

C3-121849	Reference update: RFC 6679
					29.162	  CR-0114  (Rel-11) v11.0.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122052.

C3-121850	Reference update: RFC 6679
					29.163	  CR-0688  (Rel-10) v10.7.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121851	Reference update: RFC 6679
					29.163	  CR-0689  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121852	Reference update: RFC 6679
					29.292	  CR-0059  (Rel-10) v10.3.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121853	Reference update: RFC 6679
					29.292	  CR-0060  (Rel-11) v11.3.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-122051	Reference update: RFC 6679
					29.162	  CR-0113  rev 1 (Rel-10) v10.6.0
					Source: Ericsson

(Replaces C3-121848)

Decision: 		The document was Agreed.

C3-122052	Reference update: RFC 6679
					29.162	  CR-0114  rev 1 (Rel-11) v11.0.0
					Source: Ericsson

(Replaces C3-121849)

Decision: 		The document was Agreed.

### 10.22	S2b Mobility based on GTP [SMOG-St3]

### 10.23	CT aspects of Enhancements for Multimedia Priority Service [eMPS-CN]

### 10.24	PCRF failure and restoration [PCRF-FR]

### 10.25	CT aspects of Multi Access PDN Connectivity  [MAPCON-St3]

### 10.26	CT3 Aspects of Policy Enhancements for Sponsored Connectivity and Coherent Access to Policy related Data Bases [PEST-CT3]

### 10.27	Dynamic View of Headers in Messages for II-NNI [NNI_DV]

C3-121982	The deletion of Security-Server header from dynamic view tables
					29.165	  CR-0504  (Rel-10) v10.9.0
					Source: OKI, NTT

Decision: 		The document was Agreed.

C3-121856	The deletion of Security-Server header from dynamic view tables
					29.165	  CR-0493  (Rel-11) v11.4.0
					Source: OKI, NTT

Discussion:

Category should be changed to "A" and needed Rel-10, Category "F" CR, so the revision, C3-121981 and New CR, C3-121982 (Rel-10) were produced.

Decision: 		The document was Revised to C3-121981.

C3-121981	The deletion of Security-Server header from dynamic view tables
					29.165	  CR-0493  rev 1 (Rel-11) v11.4.0
					Source: OKI, NTT

(Replaces C3-121856)

Decision: 		The document was Agreed.

### 10.28	CS and IMS Interworking for CAT early session model [CIIC_ES]

### 10.29	Stage 3 for Network Improvements for Machine Type Communications [NIMTC]

### 10.30	Technical Enhancements and Improvements [TEI10]

### 10.31	Rel-10 contributions on other Work Items

## 11	Release 11

### 11.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 11.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 11.3	Policy Control and Charging [PCC]

C3-121924	PCC CPE traversal support 
					29.213	  CR-0450  (Rel-11) v11.4.0
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-121969.

C3-121939	Correction of PCRF addressing in the presence of NAT devices and overlapping address space
					29.213	  CR-0451  (Rel-11) v11.4.0
					Source: China MobileHuawei, ZTE

Decision: 		The document was Revised to C3-121986.

C3-121940	Correction of Rx reference point for PCRF addressing
					29.214	  CR-0255  (Rel-11) v11.6.0
					Source: China MobileHuawei, ZTE

Decision: 		The document was Revised to C3-121987.

C3-121941	Discussion of policy control in the presence of NAT devices and overlapping address space
					Source: China MobileHuawei, ZTE

Decision: 		The document was Noted.

C3-121969	PCC CPE traversal support 
					29.213	  CR-0450  rev 1 (Rel-11) v11.4.0
					Source: Nokia Siemens Networks

(Replaces C3-121924)

Decision: 		The document was Agreed.

C3-121986	Correction of PCRF addressing in the presence of NAT devices and overlapping address space
					29.213	  CR-0451  rev 1 (Rel-11) v11.4.0
					Source: China MobileHuawei, ZTE

(Replaces C3-121939)

Discussion:

Orange suggested this CR should be moved to Rel-12.

Decision: 		The document was Revised to C3-122104.

C3-121987	Correction of Rx reference point for PCRF addressing
					29.214	  CR-0255  rev 1 (Rel-11) v11.6.0
					Source: China MobileHuawei, ZTE

(Replaces C3-121940)

Decision: 		The document was Revised to C3-122105.

C3-122104	Correction of PCRF addressing in the presence of NAT devices and overlapping address space
					29.213	  CR-0451  rev 2 (Rel-11) v11.4.0
					Source: China Mobile, Huawei, ZTE

(Replaces C3-121986)

Discussion:

This 2 CRs (C3-122104, C3-122105)  are technically correct according to CT3's point of view however Orange expressed sustained objection against this CR. Orange belived that this solution can not cover all of scenario. CT3 agreed that this 2 CRs are going to plenary meeting for decision. Orange will provide discussion paper to plenary meeting for this subject.

Decision: 		The document was Agreed.

C3-122105	Correction of Rx reference point for PCRF addressing
					29.214	  CR-0255  rev 2 (Rel-11) v11.6.0
					Source: China Mobile, Huawei, ZTE

(Replaces C3-121987)

Decision: 		The document was Agreed.

### 11.4	Interworking between EPC and external PDNs [SAES-St3-intwk]

### 11.5	PCC aspects of SAE [SAES-St3-PCC]

C3-121799	Handling of optional and mandatory features with Supported-Features AVP
					Source: Ericsson

Decision: 		The document was Noted.

C3-121800	Clarification of Supported-Features AVP (29.212 R11)
					29.212	  CR-0912  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122014.

C3-121801	Clarification of Supported-Features AVP (29.214 R11)
					29.214	  CR-0247  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122015.

C3-121802	Clarification of Supported-Features AVP (29.215 R11)
					29.215	  CR-0272  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122016.

C3-121866	Clean up of Editor's Notes (R11 29.212)
					29.212	  CR-0925  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Revised to C3-122021.

C3-121867	Clean up of Editor's Notes (R11 29.213)
					29.213	  CR-0442  (Rel-11) v11.4.0
					Source: Huawei

Decision: 		The document was Revised to C3-122017.

C3-121868	Clean up of Editor's Notes (R11 29.214)
					29.214	  CR-0253  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Revised to C3-122018.

C3-121869	Clean up of Editor's Notes (R11 29.215)
					29.215	  CR-0273  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Revised to C3-122019.

C3-122014	Clarification of Supported-Features AVP (29.212 R11)
					29.212	  CR-0912  rev 1 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-121800)

Decision: 		The document was Revised to C3-122095.

C3-122015	Clarification of Supported-Features AVP (29.214 R11)
					29.214	  CR-0247  rev 1 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-121801)

Decision: 		The document was Revised to C3-122096.

C3-122016	Clarification of Supported-Features AVP (29.215 R11)
					29.215	  CR-0272  rev 1 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-121802)

Decision: 		The document was Revised to C3-122097.

C3-122017	Clean up of Editor's Notes (R11 29.213)
					29.213	  CR-0442  rev 1 (Rel-11) v11.4.0
					Source: Huawei

(Replaces C3-121867)

Decision: 		The document was Revised to C3-122084.

C3-122018	Clean up of Editor's Notes (R11 29.214)
					29.214	  CR-0253  rev 1 (Rel-11) v11.6.0
					Source: Huawei

(Replaces C3-121868)

Decision: 		The document was Agreed.

C3-122019	Clean up of Editor's Notes (R11 29.215)
					29.215	  CR-0273  rev 1 (Rel-11) v11.6.0
					Source: Huawei

(Replaces C3-121869)

Decision: 		The document was Agreed.

C3-122021	Clean up of Editor's Notes (R11 29.212)
					29.212	  CR-0925  rev 1 (Rel-11) v11.6.0
					Source: Huawei

(Replaces C3-121866)

Decision: 		The document was Agreed.

C3-122084	Clean up of Editor's Notes (R11 29.213)
					29.213	  CR-0442  rev 2 (Rel-11) v11.4.0
					Source: Huawei

(Replaces C3-122017)

Decision: 		The document was Agreed.

C3-122095	Clarification of Supported-Features AVP (29.212 R11)
					29.212	  CR-0912  rev 2 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-122014)

Decision: 		The document was Agreed.

C3-122096	Clarification of Supported-Features AVP (29.214 R11)
					29.214	  CR-0247  rev 2 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-122015)

Decision: 		The document was Agreed.

C3-122097	Clarification of Supported-Features AVP (29.215 R11)
					29.215	  CR-0272  rev 2 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-122016)

Decision: 		The document was Agreed.

### 11.6	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 11.7	PCC Enhancements [PCC-Enh]

C3-121870	IP-CAN session termination when usage quota reached (R11 29.212)
					29.212	  CR-0926  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Withdrawn.

### 11.8	Optimal Media Routeing [OMR]

### 11.9	Dynamic View of Headers in Messages for II-NNI [NNI_DV]

### 11.10	Reserved

### 11.11	Reserved

### 11.12	Reserved

### 11.13	Reserved

### 11.14	Reserved

### 11.15	Reserved

### 11.16	CT3 aspects of Service Awareness and Privacy Policies [SAPP-CT3]

C3-121814	Correction of redirection functionality
					29.212	  CR-0917  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Merged with C3-121874 into C3-121988.

C3-121871	Correction on ADC functionality description (R11 29.212)
					29.212	  CR-0927  (Rel-11) v11.6.0
					Source: Huawei, Hisilicon, Allot Communications

Decision: 		The document was Revised to C3-121989.

C3-121872	Correction on ADC functionality description (R11 29.213)
					29.213	  CR-0443  (Rel-11) v11.4.0
					Source: Huawei, Hisilicon, Allot Communications

Decision: 		The document was Revised to C3-121992.

C3-121873	Enforcement order of PCC and ADC rules for PCEF enhanced with ADC (R11 29.212)
					29.212	  CR-0928  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Revised to C3-121993.

C3-121874	Redirect address for ADC rule (R11 29.212)
					29.212	  CR-0929  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Merged with C3-121814 into C3-121988.

C3-121920	ADC Rule mapping
					29.212	  CR-0944  (Rel-11) v11.6.0
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Merged with C3-121873 into C3-121993.

C3-121938	Clarification to connection establishment procedure on Sd interface
					29.212	  CR-0950  (Rel-11) v11.6.0
					Source: Tekelec

Discussion:

WI should be changed to "SAPP-CT3".

Decision: 		The document was Withdrawn.

C3-121988	Redirect address for ADC rule (R11 29.212)
					29.212	  CR-0929  rev 1 (Rel-11) v11.6.0
					Source: Huawei, Ericsson

(Replaces C3-121874)

Decision: 		The document was Revised to C3-122101.

C3-121989	Correction on ADC functionality description (R11 29.212)
					29.212	  CR-0927  rev 1 (Rel-11) v11.6.0
					Source: Huawei, Hisilicon, Allot Communications

(Replaces C3-121871)

Decision: 		The document was Agreed.

C3-121992	Correction on ADC functionality description (R11 29.213)
					29.213	  CR-0443  rev 1 (Rel-11) v11.4.0
					Source: Huawei, Hisilicon, Allot Communications

(Replaces C3-121872)

Decision: 		The document was Agreed.

C3-121993	Enforcement order of PCC and ADC rules for PCEF enhanced with ADC (R11 29.212)
					29.212	  CR-0928  rev 1 (Rel-11) v11.6.0
					Source: Huawei,  Deutsche Telekom, Allot Communications

(Replaces C3-121873)

Discussion:

Deutsche Telekom and Allot Communications were added to source companies.

Decision: 		The document was Agreed.

C3-122085	Redirect address for ADC rule (R11 29.212)
					29.212	  CR-0929  rev 2 (Rel-11) v11.6.0
					Source: Huawei, Ericsson

(Replaces C3-121988)

Decision: 		The document was Agreed.

### 11.17	CT3 aspects of QoS Control Based on Subscriber Spending Limits  [QoS_SSL-CT3]

C3-121803	Clarification of Supported-Features AVP (29.219 R11)
					29.219	  CR-0008  (Rel-11) v11.2.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122062.

C3-121875	Update of Sy specific Experimental-Result-Code (R11 29.219)
					29.219	  CR-0009  (Rel-11) v11.2.0
					Source: Huawei

Decision: 		The document was Merged into C3-122087.

C3-121876	LS on Diameter code allocation for TS 29.219
					Source: Huawei

Decision: 		The document was Revised to C3-122063.

C3-121937	Addition of values to the Experimental-Result-Code AVP
					29.219	  CR-0010  (Rel-11) v11.2.0
					Source: Tekelec, Verizon

Decision: 		The document was Withdrawn.

C3-121961	Addition of values to the Experimental-Result-Code AVP
					29.219	  CR-0010  rev 1 (Rel-11) v11.2.0
					Source: Tekelec, Verizon

Decision: 		The document was Revised to C3-122056.

C3-122056	Addition of values to the Experimental-Result-Code AVP
					29.219	  CR-0010  rev 2 (Rel-11) v11.2.0
					Source: Tekelec, Verizon

(Replaces C3-121961)

Decision: 		The document was Revised to C3-122086.

C3-122062	Clarification of Supported-Features AVP (29.219 R11)
					29.219	  CR-0008  rev 1 (Rel-11) v11.2.0
					Source: Ericsson

(Replaces C3-121803)

Decision: 		The document was Agreed.

C3-122063	LS on Diameter code allocation for TS 29.219
					Source: Huawei

(Replaces C3-121876)

Decision: 		The document was Approved.

C3-122086	Addition of values to the Experimental-Result-Code AVP
					29.219	  CR-0010  rev 3 (Rel-11) v11.2.0
					Source: Tekelec, Verizon, Alcatel-Lucent, Huawei

(Replaces C3-122056)

Decision: 		The document was Revised to C3-122087.

C3-122087	Addition of values to the Experimental-Result-Code AVP
					29.219	  CR-0010  rev 4 (Rel-11) v11.2.0
					Source: Tekelec, Verizon, Alcatel-Lucent, Huawei

(Replaces C3-122086)

Decision: 		The document was Agreed.

### 11.18	USSD Simulation Service in IMS-stage 3 [USSI]

### 11.19	Single Radio Video Call Continuity       [vSRVCC-CT]

#### 11.19.1	IMS-related

#### 11.19.2	PCC-related

### 11.20	Further improvement of usability of II-NNI specification for inter-connection [NNI_OI]

C3-121837	Transcoding option item
					29.165	  CR-0484  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121983.

C3-121838	Bulk registration option item
					29.165	  CR-0485  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121983	Transcoding option item
					29.165	  CR-0484  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121837)

Decision: 		The document was Withdrawn.

C3-122034	Feature capability g.3gpp.trf error corrections
					29.165	  CR-0483  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121836)

Discussion:

WI was changed to "NNI_OI".

Decision: 		The document was Agreed.

### 11.21	IMS Stage-3 IETF Protocol Alignment          [IMSProtoc5]

C3-121830	S-CSCF restoration procedures
					29.165	  CR-0479  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121984.

C3-121847	Reference column in MIME body table
					29.165	  CR-0490  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Revised to C3-121985.

C3-121892	Correcting minor errors
					29.165	  CR-0500  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-121984	S-CSCF restoration procedures
					29.165	  CR-0479  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121830)

Decision: 		The document was Agreed.

C3-121985	Reference column in MIME body table
					29.165	  CR-0490  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121847)

Decision: 		The document was Agreed.

C3-122037	Interface between the ISC gateway and an AS in an enterprise network
					29.165	  CR-0475  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121826)

Discussion:

WI should be changed to "IMSProtoc5".

Decision: 		The document was Agreed.

### 11.22	CT aspects of Single Radio Voice Call Continuity from UTRAN/GERAN to E-UTRAN/HSPA [rSRVCC-CT]

C3-121819	End of CS to PS handover procedure
					29.212	  CR-0919  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Merged with C3-121877 and C3-121906 into C3-122020.

C3-121877	PCC support for rSRVCC (R11 29.212)
					29.212	  CR-0930  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Merged with C3-121819 and C3-121906 into C3-122020.

C3-121906	Support of rSRVCC in Gx
					29.212	  CR-0941  (Rel-11) v11.6.0
					Source: ZTE

Decision: 		The document was Merged with C3-121819 and C3-121877 into C3-122020.

C3-122020	End of CS to PS handover procedure
					29.212	  CR-0919  rev 1 (Rel-11) v11.6.0
					Source: Ericsson, Huawei, ZTE

(Replaces C3-121819)

Decision: 		The document was Revised to C3-122098.

C3-122098	End of CS to PS handover procedure
					29.212	  CR-0919  rev 2 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-122020)

Decision: 		The document was Agreed.

#### 11.22.1	IMS/CS related docs

#### 11.22.2	Packet Core related docs

### 11.23	Stage 3 for System Improvements to Machine-Type Communications [SIMTC-Reach]

C3-121816	Assignment of allocated Diameter code values
					29.368	  CR-0001  (Rel-11) v11.0.0
					Source: Ericsson, Juniper

Decision: 		The document was Revised to C3-121990.

C3-121817	LS on Diameter AVP code value allocation in TS 29.368
					Source: Ericsson

Decision: 		The document was Revised to C3-121991.

C3-121818	Reply LS on Device Triggering Identification
					Source: Ericsson

Decision: 		The document was Revised to C3-122057.

C3-121878	Clarification of MTC-IWF load control (R11 29.368)
					29.368	  CR-0002  (Rel-11) v11.0.0
					Source: Huawei, Hisilicon

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-121921	Device triggering identification
					Source: Ericsson

Decision: 		The document was Noted.

C3-121930	Correction of MTC-IWF checks on quota and rate of device triggers from SCS
					29.368	  CR-0003  (Rel-11) v11.0.0
					Source: Intel, Chen-Ho

Decision: 		The document was Revised to C3-122059.

C3-121990	Assignment of allocated Diameter code values
					29.368	  CR-0001  rev 1 (Rel-11) v11.0.0
					Source: Ericsson, Juniper

(Replaces C3-121816)

Decision: 		The document was Agreed.

C3-121991	LS on Diameter AVP code value allocation in TS 29.368
					Source: Ericsson

(Replaces C3-121817)

Discussion:

It has to be checked wehether additional values need to be added.

Decision: 		The document was Approved.

C3-122057	Reply LS on Device Triggering Identification
					Source: Ericsson

(Replaces C3-121818)

Decision: 		The document was Revised to C3-122069.

C3-122058	Removal of empty clauses
					29.368	  CR-0004  (Rel-11) v11.0.0
					Source: Nokia Siemens Networks

Decision: 		The document was Agreed.

C3-122059	Correction of MTC-IWF checks on quota and rate of device triggers from SCS
					29.368	  CR-0003  rev 1 (Rel-11) v11.0.0
					Source: Intel, Chen-Ho

(Replaces C3-121930)

Decision: 		The document was Revised to C3-122108.

C3-122069	Reply LS on Device Triggering Identification
					Source: Ericsson

(Replaces C3-122057)

Decision: 		The document was Revised to C3-122083.

C3-122083	Reply LS on Device Triggering Identification
					Source: Ericsson

(Replaces C3-122069)

Decision: 		The document was Revised to C3-122107.

C3-122107	Reply LS on Device Triggering Identification
					Source: Ericsson

(Replaces C3-122083)

Decision: 		The document was Approved.

C3-122108	Correction of MTC-IWF checks on quota and rate of device triggers from SCS
					29.368	  CR-0003  rev 2 (Rel-11) v11.0.0
					Source: Intel, Chen-Ho

(Replaces C3-122059)

Decision: 		The document was Revised to C3-122110.

C3-122110	Correction of MTC-IWF checks on quota and rate of device triggers from SCS
					29.368	  CR-0003  rev 3 (Rel-11) v11.0.0
					Source: Intel, Chen-Ho

(Replaces C3-122108)

Decision: 		The document was Agreed.

### 11.24	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block I [BBAI_BBI-CT]

C3-121907	AVP of PCRF address in session establishment trigger
					29.215	  CR-0274  (Rel-11) v11.6.0
					Source: ZTE

Decision: 		The document was Revised to C3-121994.

C3-121908	AVP of PCRF address in session establishment trigger
					29.213	  CR-0444  (Rel-11) v11.4.0
					Source: ZTE

Decision: 		The document was Revised to C3-121995.

C3-121909	Correction to the BPCF Addressing
					29.213	  CR-0445  (Rel-11) v11.4.0
					Source: ZTE

Decision: 		The document was Revised to C3-121996.

C3-121910	Corrections to the call flows for EPC-routed
					29.213	  CR-0446  (Rel-11) v11.4.0
					Source: ZTE

Discussion:

The related CR is C3-121997.

Decision: 		The document was Revised to C3-122068.

C3-121911	AN-GW-Address over Gx for EPC-routed
					29.212	  CR-0942  (Rel-11) v11.6.0
					Source: ZTE

Decision: 		The document was Merged with C3-121936 into C3-121998.

C3-121912	AVP for S9 session termination notification
					29.213	  CR-0447  (Rel-11) v11.4.0
					Source: ZTE, Ericsson

Decision: 		The document was Revised to C3-121999.

C3-121913	AVP for S9 session termination notification
					29.215	  CR-0275  (Rel-11) v11.6.0
					Source: ZTE, Ericsson

Decision: 		The document was Revised to C3-122000.

C3-121914	Clarification of the S9 session procedure for EPC-routed traffic
					29.215	  CR-0276  (Rel-11) v11.6.0
					Source: ZTE

Decision: 		The document was Revised to C3-121997.

C3-121915	Correction to the DRA functionality for NSWO Addressing
					29.213	  CR-0448  (Rel-11) v11.4.0
					Source: ZTE

Decision: 		The document was Revised to C3-122060.

C3-121936	Transport of ePDG IP address over Gx
					29.212	  CR-0949  (Rel-11) v11.6.0
					Source: CATT

Decision: 		The document was Merged with C3-121911 into C3-121998.

C3-121994	AVP of PCRF address in session establishment trigger
					29.215	  CR-0274  rev 1 (Rel-11) v11.6.0
					Source: ZTE

(Replaces C3-121907)

Decision: 		The document was Revised to C3-122099.

C3-121995	AVP of PCRF address in session establishment trigger
					29.213	  CR-0444  rev 1 (Rel-11) v11.4.0
					Source: ZTE

(Replaces C3-121908)

Decision: 		The document was Agreed.

C3-121996	Correction to the BPCF Addressing
					29.213	  CR-0445  rev 1 (Rel-11) v11.4.0
					Source: ZTE

(Replaces C3-121909)

Decision: 		The document was Agreed.

C3-121997	Clarification of the S9 session procedure for EPC-routed traffic
					29.215	  CR-0276  rev 1 (Rel-11) v11.6.0
					Source: ZTE

(Replaces C3-121914)

Decision: 		The document was Revised to C3-122067.

C3-121998	AN-GW-Address over Gx for EPC-routed
					29.212	  CR-0942  rev 1 (Rel-11) v11.6.0
					Source: ZTE, CATT

(Replaces C3-121911)

Decision: 		The document was Agreed.

C3-121999	AVP for S9 session termination notification
					29.213	  CR-0447  rev 1 (Rel-11) v11.4.0
					Source: ZTE, Ericsson, Huawei

(Replaces C3-121912)

Decision: 		The document was Revised to C3-122100.

C3-122000	AVP for S9 session termination notification
					29.215	  CR-0275  rev 1 (Rel-11) v11.6.0
					Source: ZTE, Ericsson, Huawei

(Replaces C3-121913)

Decision: 		The document was Agreed.

C3-122060	Correction to the DRA functionality for NSWO Addressing
					29.213	  CR-0448  rev 1 (Rel-11) v11.4.0
					Source: ZTE

(Replaces C3-121915)

Decision: 		The document was Agreed.

C3-122067	Clarification of the S9 session procedure for EPC-routed traffic
					29.215	  CR-0276  rev 2 (Rel-11) v11.6.0
					Source: ZTE

(Replaces C3-121997)

Decision: 		The document was Revised to C3-122101.

C3-122068	Corrections to the call flows for EPC-routed
					29.213	  CR-0446  rev 1 (Rel-11) v11.4.0
					Source: ZTE

(Replaces C3-121910)

Decision: 		The document was Agreed.

C3-122089	Clarification of the S9 session procedure for EPC-routed traffic
					29.215	  CR-0276  rev 3 (Rel-11) v11.6.0
					Source: ZTE

(Replaces C3-122067)

Decision: 		The document was Agreed.

C3-122099	AVP of PCRF address in session establishment trigger
					29.215	  CR-0274  rev 2 (Rel-11) v11.6.0
					Source: ZTE

(Replaces C3-121994)

Decision: 		The document was Revised to C3-122120.

C3-122100	AVP for S9 session termination notification
					29.213	  CR-0447  rev 2 (Rel-11) v11.4.0
					Source: ZTE, Ericsson

(Replaces C3-121999)

Decision: 		The document was Agreed.

C3-122120	AVP of PCRF address in session establishment trigger
					29.215	  CR-0274  rev 3 (Rel-11) v11.6.0
					Source: ZTE

(Replaces C3-122099)

Decision: 		The document was Agreed.

### 11.25	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block II [BBAI_BBII-CT]

C3-121916	Corrections to the call flows for NSWO
					29.213	  CR-0449  (Rel-11) v11.4.0
					Source: ZTE

Discussion:

It was agreed however agenda item was changed to "11.25" (BBII)

Decision: 		The document was Agreed.

C3-121917	Editorial corrections to the BBAI BB2 architecture
					29.215	  CR-0277  (Rel-11) v11.6.0
					Source: ZTE, Ericsson

Decision: 		The document was Agreed.

C3-121918	Clarification of S9 session procedure for NSWO traffic
					29.215	  CR-0278  (Rel-11) v11.6.0
					Source: ZTE

Decision: 		The document was Revised to C3-122061.

C3-122061	Clarification of S9 session procedure for NSWO traffic
					29.215	  CR-0278  rev 1 (Rel-11) v11.6.0
					Source: ZTE

(Replaces C3-121918)

Decision: 		The document was Agreed.

### 11.26	Void

### 11.27	CN aspects of Anonymous Call Rejection in the CS domain [ACR_CS-CN]

### 11.28	IMS Emergency PSAP Callback [EMC_PC]

C3-121840	Callback for emergency call
					29.165	  CR-0487  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122031.

C3-121896	PSAP Callback Indicator
					29.214	  CR-0254  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-122031	Callback for emergency call
					29.165	  CR-0487  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121840)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

### 11.29	Advanced Interconnection of Services [IPXS]

### 11.30	Enhancements for Multimedia Priority Service (MPS)  Gateway Control Priority [eMPS_Gateway]

C3-121927	Support of Multimedia Priority Service (MPS) in Modify over Ix Interface
					29.162	  CR-0115  (Rel-11) v11.0.0
					Source: Applied Communication Sciences, National Communica

Decision: 		The document was Revised to C3-122040.

C3-121928	Additional Text for Support of Multimedia Priority Service (MPS) in over Mn Interface
					29.163	  CR-0694  (Rel-11) v11.4.0
					Source: Applied Communication Sciences, National Communica

Decision: 		The document was Revised to C3-122041.

C3-121929	Example use case illustrating inclusion of priority information in H.248 Modify command
					Source: Applied Communication Sciences, National Communica

Decision: 		The document was Revised to C3-122042.

C3-122040	Support of Multimedia Priority Service (MPS) in Modify over Ix Interface
					29.162	  CR-0115  rev 1 (Rel-11) v11.0.0
					Source: Applied Communication Sciences, National Communica

(Replaces C3-121927)

Decision: 		The document was Revised to C3-122090.

C3-122041	Additional Text for Support of Multimedia Priority Service (MPS) in over Mn Interface
					29.163	  CR-0694  rev 1 (Rel-11) v11.4.0
					Source: Applied Communication Sciences, National Communica

(Replaces C3-121928)

Decision: 		The document was Revised to C3-122091.

C3-122042	Example use case illustrating inclusion of priority information in H.248 Modify command
					Source: Applied Communication Sciences, National Communica

(Replaces C3-121929)

Decision: 		The document was Noted.

C3-122090	Support of Multimedia Priority Service (MPS) in Modify over Ix Interface
					29.162	  CR-0115  rev 2 (Rel-11) v11.0.0
					Source: Applied Communication Sciences, National Communica

(Replaces C3-122040)

Decision: 		The document was Revised to C3-122127.

C3-122091	Additional Text for Support of Multimedia Priority Service (MPS) in over Mn Interface
					29.163	  CR-0694  rev 2 (Rel-11) v11.4.0
					Source: Applied Communication Sciences, NCS, AT&T, Alcatel-Lucent

(Replaces C3-122041)

Decision: 		The document was Agreed.

C3-122127	Support of Multimedia Priority Service (MPS) in Modify over Ix Interface
					29.162	  CR-0115  rev 3 (Rel-11) v11.0.0
					Source: Applied Communication Sciences, National Communica

(Replaces C3-122090)

Decision: 		The document was Revised to C3-122128.

C3-122128	Support of Multimedia Priority Service (MPS) in Modify over Ix Interface
					29.162	  CR-0115  rev 4 (Rel-11) v11.0.0
					Source: Applied Communication Sciences, National Communica

(Replaces C3-122127)

Discussion:

This CR was aligned with the related CT4 CR.

Decision: 		The document was Agreed.

### 11.31	CN aspects of Mobility based On GTP & PMIPv6 for WLAN access to EPC [SaMOG_WLAN-CN]

### 11.32	CN aspects of Service Identification for RRC Improvements in GERAN [SIRIG]

### 11.33	CT aspect on Network Provided Location Information for IMS [NWK-PL2IMS-CT]

C3-121820	Access network information via Rx
					29.214	  CR-0252  (Rel-11) v11.6.0
					Source: Nokia Siemens Networks

Decision: 		The document was Withdrawn.

C3-121821	Access network information via Rx
					29.213	  CR-0441  (Rel-11) v11.4.0
					Source: Nokia Siemens Networks

Decision: 		The document was Withdrawn.

C3-121879	Revised WID on CT aspect on Network Provided Location Information for IMS
					Source: Huawei

Decision: 		The document was Revised to C3-121965.

C3-121965	Revised WID on CT aspect on Network Provided Location Information for IMS
					Source: Huawei

(Replaces C3-121879)

Decision: 		The document was Agreed.

### 11.34	II-NNI enhancements: SIP timers applicability [NNI_timers]

### 11.35	Roaming Architecture for Voice over IMS with Local Breakout – CT aspects [RAVEL-CT]

C3-121822	Updating loopback example
					29.079	  CR-0015  (Rel-11) v11.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122032.

C3-121823	Identifying an RAVEL session
					29.079	  CR-0016  (Rel-11) v11.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122033.

C3-121836	Feature capability g.3gpp.trf error corrections
					29.165	  CR-0483  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122034.

C3-121923	Ravel-related minor corrections
					29.165	  CR-0501  (Rel-11) v11.4.0
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-122035.

C3-122032	Updating loopback example
					29.079	  CR-0015  rev 1 (Rel-11) v11.1.0
					Source: Ericsson

(Replaces C3-121822)

Decision: 		The document was Agreed.

C3-122033	Identifying an RAVEL session
					29.079	  CR-0016  rev 1 (Rel-11) v11.1.0
					Source: Ericsson

(Replaces C3-121823)

Decision: 		The document was Revised to C3-122112.

C3-122035	Ravel-related minor corrections
					29.165	  CR-0501  rev 1 (Rel-11) v11.4.0
					Source: Nokia Siemens Networks

(Replaces C3-121923)

Decision: 		The document was Agreed.

C3-122066	GTPv2 supported in S2a and S2b (R11 29.061)
					29.061	  CR-0391  rev 1 (Rel-12) v11.2.0
					Source: Ericsson

(Replaces C3-121822)

Decision: 		The document was Revised to C3-122088.

C3-122088	GTPv2 supported in S2a and S2b (R11 29.061)
					29.061	  CR-0391  rev 2 (Rel-12) v11.2.0
					Source: Ericsson

(Replaces C3-122066)

Decision: 		The document was Agreed.

C3-122112	Identifying an RAVEL session
					29.079	  CR-0016  rev 2 (Rel-11) v11.1.0
					Source: Ericsson

(Replaces C3-122033)

Decision: 		The document was Revised to C3-122123.

C3-122123	Identifying an RAVEL session
					29.079	  CR-0016  rev 3 (Rel-11) v11.1.0
					Source: Ericsson

(Replaces C3-122112)

Discussion:

It was postponed till the next meeting.

Decision: 		The document was Postponed.

### 11.36	Inclusion of Media Resource Broker [MRB]

### 11.37	Enhanced T.38 FAX support [MMTel_T.38_FAX]

C3-121922	T.38 default version
					29.163	  CR-0693  (Rel-11) v11.4.0
					Source: Nokia Siemens Networks

Decision: 		The document was Agreed.

### 11.38	Enhanced Nodes Restoration for EPC [eNR_EPC]

C3-121815	PCC Impacts due to SGW Restoration procedures
					29.212	  CR-0918  (Rel-11) v11.6.0
					Source: Ericsson

Decision: 		The document was Merged with C3-121880 and C3-121919 into C3-122064.

C3-121880	BBERF (SGW) restoration (R11 29 212)
					29.212	  CR-0931  (Rel-11) v11.6.0
					Source: Huawei

Decision: 		The document was Merged with C3-121815 and C3-121919 into C3-122064.

C3-121919	PCC impacts of the S-GW restoration
					29.212	  CR-0943  (Rel-11) v11.6.0
					Source: ZTE

Decision: 		The document was Merged with C3-121815 and C3-121880 into C3-122064.

C3-121925	LS on Charging impacts for ePS restoration
					Source: Juniper Networks

Discussion:

There were no delegates from Juniper Networks, so it was postponed till the next meeting.

Decision: 		The document was Postponed.

C3-122064	PCC Impacts due to SGW Restoration procedures
					29.212	  CR-0918  rev 1 (Rel-11) v11.6.0
					Source: Ericsson

(Replaces C3-121815)

Discussion:

Huawei and ZTE were added to source companies.

Decision: 		The document was Agreed.

### 11.39	IMS overload control [IOC]

C3-121839	Event based load control
					29.165	  CR-0486  (Rel-11) v11.4.0
					Source: Ericsson

Decision: 		The document was Revised to C3-122036.

C3-122036	Event based load control
					29.165	  CR-0486  rev 1 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-121839)

Decision: 		The document was Revised to C3-122072.

C3-122072	Event based load control
					29.165	  CR-0486  rev 2 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-122036)

Decision: 		The document was Revised to C3-122121.

C3-122121	Event based load control
					29.165	  CR-0486  rev 3 (Rel-11) v11.4.0
					Source: Ericsson

(Replaces C3-122072)

Decision: 		The document was Agreed.

### 11.40	Technical Enhancements and Improvements [TEI11]

C3-121948	Inconsistency with TS 29.163 - 29.292r11
					29.292	  CR-0061  (Rel-11) v11.3.0
					Source: Orange

Discussion:

WI should be changed to "ICSRA".

Decision: 		The document was Revised to C3-122039.

### 11.41	Rel-11 contributions on other Work Items

C3-121826	Interface between the ISC gateway and an AS in an enterprise network
					29.165	  CR-0475  (Rel-11) v11.4.0
					Source: Ericsson

Discussion:

WI should be changed to "IMSProtoc5".

Decision: 		The document was Revised to C3-122037.

C3-121931	100 Trying not interworked between IMS and SIP-I based CS CN
					29.235	  CR-0092  (Rel-11) v11.0.0
					Source: Nokia Siemens Networks

Decision: 		The document was Revised to C3-122038.

C3-122038	100 Trying not interworked between IMS and SIP-I based CS CN
					29.235	  CR-0092  rev 1 (Rel-11) v11.0.0
					Source: Nokia Siemens Networks

(Replaces C3-121931)

Decision: 		The document was Agreed.

#### 11.41.1	Stage 3 for Support for 3GPP Voice Interworking with Enterprise IP-PBX [VINE-CT1]

#### 11.41.2	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

#### 11.41.3	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]

C3-122039	Inconsistency with TS 29.163 - 29.292r11
					29.292	  CR-0061  rev 1 (Rel-11) v11.3.0
					Source: Orange

(Replaces C3-121948)

Discussion:

WI was changed to "ICSRA" and it was postponed till the next meeting.

Decision: 		The document was Postponed.

## 12	Release 12

### 12.1	Interworking between a PLMN with WLAN to access the EPC and a PDN [SAES_WLAN_EPC_intwk]

C3-121881	APCO used in IP-CAN session establishment procedure (R11 29.061)
					29.061	  CR-0390  (Rel-12) v11.2.0
					Source: Huawei

Decision: 		The document was Revised to C3-122065.

C3-121882	GTPv2 supported in S2a and S2b (R11 29.061)
					29.061	  CR-0391  (Rel-12) v11.2.0
					Source: Huawei

Decision: 		The document was Revised to C3-122066.

C3-122065	APCO used in IP-CAN session establishment procedure (R11 29.061)
					29.061	  CR-0390  rev 1 (Rel-12) v11.2.0
					Source: Huawei

(Replaces C3-121881)

Decision: 		The document was Agreed.

### 12.2	Technical Enhancements and Improvements [TEI12]

### 12.3	Rel-12 contributions on other Work Items

#### 12.3.1	CT aspects of Extended IMS media plane security [eMEDIASEC_CT]

C3-121768	CT aspects of Extended IMS media plane security
					Source: Alcatel-Lucent

Decision: 		The document was Revised to C3-122073.

C3-122073	CT aspects of Extended IMS media plane security
					Source: Alcatel-Lucent

(Replaces C3-121768)

Decision: 		The document was Revised to C3-122103.

C3-122103	CT aspects of Extended IMS media plane security
					Source: Alcatel-Lucent

(Replaces C3-122073)

Decision: 		The document was Endorsed.

#### 12.3.2	Indicating Use Case [IUC-CT]

C3-121831	New WID Indicating Use Case
					Source: Ericsson

Decision: 		The document was Noted.

#### 12.3.3	DRVCC enhancements [eDRVCC]

C3-121832	New WID on DRVCC enhancements
					Source: Ericsson

Decision: 		The document was Revised to C3-121968.

C3-121968	New WID on DRVCC enhancements
					Source: Ericsson

(Replaces C3-121832)

Decision: 		The document was Revised to C3-122125.

C3-122125	New WID on DRVCC enhancements
					Source: Ericsson

(Replaces C3-121968)

Decision: 		The document was Endorsed.

#### 12.3.4	IMS based Telepresence (Stage 3) [IMS_TELEP]

C3-121885	WID on IMS based Telepresence (Stage 3)
					Source: Huawei

Discussion:

Needing explanation for blank of Stage 2 and adding new bullet for II-NNI in Objective section. The revision was produced.

Decision: 		The document was Revised to C3-121966.

C3-121966	WID on IMS based Telepresence (Stage 3)
					Source: Huawei

(Replaces C3-121885)

Decision: 		The document was Endorsed.

#### 12.3.5	IMS Stage-3 IETF Protocol Alignment  [IMSProtoc6]

C3-121926	Proposed WID for IMS Stage-3 IETF Protocol Alignment
					Source: Alcatel-Lucent / Keith Drage

Discussion:

Small editorial improvement was suggested.

Decision: 		The document was Revised to C3-121967.

C3-121967	Proposed WID for IMS Stage-3 IETF Protocol Alignment
					Source: Alcatel-Lucent / Keith Drage

(Replaces C3-121926)

Decision: 		The document was Endorsed.

#### 12.3.6	Synchronization between A Pair of  DRAs for PCRF addressing  [DRAs_Sync]

C3-121942	Synchronization between A Pair of  DRAs for PCRF addressing
					Source: ChinaTelecom, Huawei, ZTE, CATT

Discussion:

Presented by Mr.Qiao Weihua (from Huawei), Telecom Italia and Ericsson, NSN had the comment on the related load balance. Regarding discussion about the number and function of DRA, ZTE suggested to send LS to SA2.

Decision: 		The document was Noted.

C3-121943	Discussion on PCRF addressing in a pair of DRAs deployment scenario
					Source: China Telecom

Decision: 		The document was Noted.

#### 12.3.7	Other documents

C3-121959	Discussion on Interactions between Application Functions and PCC architecture
					Source: Orange

Decision: 		The document was Postponed.

## 13	Joint sessions

## 14	Work Organisation

### 14.1	Work Plan Review

C3-121777	Lastest Version of 3GPP Workplan
					Source: MCC

Decision: 		The document was Noted.

C3-121795	Status of CT3 Work Items
					Source: CT3 Chairman

Decision: 		The document was Revised to C3-122124.

C3-122124	Status of CT3 Work Items
					Source: CT3 Chairman

(Replaces C3-121795)

Decision: 		The document was Noted.

### 14.2	Specification Review

C3-121778	Status of CT3 Specifications following CT#57 meeting
					Source: MCC

Decision: 		The document was Revised to C3-121962.

C3-121962	Status of CT3 Specifications following CT#57 meeting
					Source: MCC

(Replaces C3-121778)

Discussion:

it is revision for fixing the rapportuer of 29.235. And the rapporteurs who needs to be changed was dicsussed. The rapporteurs will be updated accordingly in the 3GPP website.

Decision: 		The document was Revised to C3-122126.

C3-122126	Status of CT3 Specifications following CT#57 meeting
					Source: MCC

(Replaces C3-121962)

Decision: 		The document was Noted.

### 14.3	Next meetings, allocation of hosts

C3-121779	Meeting Calendar for 2013
					Source: MCC

Discussion:

The October 2013 meeting has to be decided till April 2013.

Decision: 		The document was Noted.

## 15	Summary of results

## 16	Any other business

## 17	Closing of the meeting

Dr. Ragnar Huslende gladly expressed his gratitude to the delegates for hard working and excellent progress during the meeting. Meeting was closed on Friday 16th  November 2012.

## Annex A. TS/TR

none

## Annex B. Work Item

| Tdoc | Agenda | Type | Title | Source | Decision |
| --- | --- | --- | --- | --- | --- |
| C3-121768 | 12.3 | WID | CT aspects of Extended IMS media plane security | Alcatel-Lucent | Revised |
| C3-121831 | 12.3 | WID | New WID Indicating Use Case | Ericsson | Noted |
| C3-121832 | 12.3 | WID | New WID on DRVCC enhancements | Ericsson | Revised |
| C3-121879 | 11.33 | WID | Revised WID on CT aspect on Network Provided Location Information for IMS | Huawei | Revised |
| C3-121885 | 12.3 | WID | WID on IMS based Telepresence (Stage 3) | Huawei | Revised |
| C3-121926 | 12.3 | WID | Proposed WID for IMS Stage-3 IETF Protocol Alignment | Alcatel-Lucent / Keith Drage | Revised |
| C3-121942 | 14.1 | WID | Synchronization between A Pair of DRAs for PCRF addressing | ChinaTelecom, Huawei, ZTE, CATT | Noted |
| C3-121965 | 11.33 | WID | Revised WID on CT aspect on Network Provided Location Information for IMS | Huawei | Agreed |
| C3-121966 | 12.3 | WID | WID on IMS based Telepresence (Stage 3) | Huawei | Endorsed |
| C3-121967 | 12.3 | WID | Proposed WID for IMS Stage-3 IETF Protocol Alignment | Alcatel-Lucent / Keith Drage | Endorsed |
| C3-121968 | 12.3 | WID | New WID on DRVCC enhancements | Ericsson | Revised |
| C3-122073 | 12.3 | WID | CT aspects of Extended IMS media plane security | Alcatel-Lucent | Revised |
| C3-122103 | 12.3 | WID | CT aspects of Extended IMS media plane security | Alcatel-Lucent | Endorsed |
| C3-122125 | 12.3 | WID | New WID on DRVCC enhancements | Ericsson | Endorsed |

## Annex C. Liaison Statements

### Annex C.1 Incoming Liaison Statements

| Tdoc | Title | Source | Source File | Response | Decision |
| --- | --- | --- | --- | --- | --- |
| C3-121780 | Reply LS on GSMA Application Network Efficiency Task Force "whitepaper and actions" | TSG CT WG4 | C4-121612 |  | Noted |
| C3-121781 | LS on GSMA Application Network Efficiency Task Force “whitepaper and actions” | TSG RAN WG2 | R2-124349 |  | Noted |
| C3-121782 | LS on GSMA Application Network Efficiency Task Force “whitepaper and actions” | TSG SA WG4 | S4-121237 |  | Noted |
| C3-121783 | Reply LS on T.38 related work in CT WGs | TSG SA WG4 | S4-121116 |  | Noted |
| C3-121784 | LS on GSMA Application Network Efficiency Task Force “whitepaper and actions” | TSG SA WG5 | S5-122172 |  | Noted |
| C3-121785 | LS on TS 32.299 AVPs for update in TS 29.230 | TSG SA WG5 | S5-122051 |  | Noted |
| C3-121786 | LS on GSMA Application Network Efficiency Task Force "whitepaper and actions" | TSG CT | CP-120668 |  | Noted |
| C3-121787 | LS on GSMA Application Network Efficiency Task Force “whitepaper and actions” | TSG RAN | RP-121454 |  | Noted |
| C3-121788 | Reply to 3GPP Liaison Statement on RC Mapping | i3 Forum WG "Technical Aspects" | i3 WS Tech - Reply to 3GPP LS on RC Mapping |  | Noted |
| C3-121789 | LS on Charging issue regarding PCC and ADC Rules | TSG SA WG2 | S2-124110 |  | Noted |
| C3-121790 | Reply LS on QoS parameters that can be upgraded and downgraded | TSG SA WG2 | S2-124143 |  | Noted |
| C3-121791 | Reply LS on PCC support for rSRVCC | TSG SA WG2 | S2-124168 |  | Noted |
| C3-121792 | LS on Device Triggering Identification | TSG SA WG2 | S2-124190 |  | Noted |
| C3-121963 | Reply LS on Device Triggering Identification | TSG SA WG3 | S3-121174 |  | Noted |
| C3-121964 | LS on SDP offer-answer negotiation of AVPF and CCM feedback messages | TSG SA WG4 | S4-121491 |  | Postponed |
| C3-122106 | Reply LS on TFT usage for the primary PDP context when access to the PGW | TSG SA WG2 | S2-124825 |  | Noted |

### Annex C.2 Outgoing Liaison Statements

| Tdoc | Title | LS To | LS Cc | Attachment |
| --- | --- | --- | --- | --- |
| C3-121991 | LS on Diameter AVP code value allocation in TS 29.368 | CT4 |  |  |
| C3-122063 | LS on Diameter code allocation for TS 29.219 | CT4 |  |  |
| C3-122107 | Reply LS on Device Triggering Identification | SA2 | CT1, SA3, CT4 |  |

## Annex D. Agreed Change Requests

| Tdoc | Agenda | Type | Title | Source | Spec | CR_number | CR_revision | Release | Decision | Version_old | Work_item | Category | Available | Meeting |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C3-121812 | 10.6 | CR | Correction on sponsored connectivity procedures | Ericsson | 29.213 | 0439 | 0 | Rel-10 | Agreed | 10.7.0 | PCC-Enh | F |  | 71 |
| C3-121813 | 10.6 | CR | Correction on sponsored connectivity procedures | Ericsson | 29.213 | 0440 | 0 | Rel-11 | Agreed | 11.4.0 | PCC-Enh | A |  | 71 |
| C3-121824 | 10.17 | CR | Reference update of draft-ietf-mediactrl-mixer-control-package | Ericsson | 29.079 | 0017 | 0 | Rel-10 | Agreed | 10.3.0 | OMR | F |  | 71 |
| C3-121825 | 10.17 | CR | Reference update of draft-ietf-mediactrl-mixer-control-package | Ericsson | 29.079 | 0018 | 0 | Rel-11 | Agreed | 11.1.0 | OMR | A |  | 71 |
| C3-121838 | 11.20 | CR | Bulk registration option item | Ericsson | 29.165 | 0485 | 0 | Rel-11 | Agreed | 11.4.0 | NNI_OI, GINI | F |  | 71 |
| C3-121845 | 10.18 | CR | Reference update: draft-ietf-sipcore-proxy-feature | Ericsson | 29.165 | 0488 | 0 | Rel-10 | Agreed | 10.9.0 | II-NNI2 | F |  | 71 |
| C3-121846 | 10.18 | CR | Reference update: draft-ietf-sipcore-proxy-feature | Ericsson | 29.165 | 0489 | 0 | Rel-11 | Agreed | 11.4.0 | II-NNI2 | A |  | 71 |
| C3-121850 | 10.21.2 | CR | Reference update: RFC 6679 | Ericsson | 29.163 | 0688 | 0 | Rel-10 | Agreed | 10.7.0 | ECSRA_LAA-CN | F |  | 71 |
| C3-121851 | 10.21.2 | CR | Reference update: RFC 6679 | Ericsson | 29.163 | 0689 | 0 | Rel-11 | Agreed | 11.4.0 | ECSRA_LAA-CN | A |  | 71 |
| C3-121852 | 10.21.2 | CR | Reference update: RFC 6679 | Ericsson | 29.292 | 0059 | 0 | Rel-10 | Agreed | 10.3.0 | ECSRA_LAA-CN | F |  | 71 |
| C3-121853 | 10.21.2 | CR | Reference update: RFC 6679 | Ericsson | 29.292 | 0060 | 0 | Rel-11 | Agreed | 11.3.0 | ECSRA_LAA-CN | A |  | 71 |
| C3-121862 | 8.15 | CR | Preconfigured packet filters and PCC rules for dedicated signalling bearer (R8 29.061) | Huawei | 29.061 | 0386 | 0 | Rel-8 | Agreed | 8.10.0 | SAES-St3-intwk | F |  | 71 |
| C3-121863 | 8.15 | CR | Preconfigured packet filters and PCC rules for dedicated signalling bearer (R9 29.061) | Huawei | 29.061 | 0387 | 0 | Rel-9 | Agreed | 9.10.0 | SAES-St3-intwk | A |  | 71 |
| C3-121864 | 8.15 | CR | Preconfigured packet filters and PCC rules for dedicated signalling bearer (R10 29.061) | Huawei | 29.061 | 0388 | 0 | Rel-10 | Agreed | 10.7.0 | SAES-St3-intwk | A |  | 71 |
| C3-121865 | 8.15 | CR | Preconfigured packet filters and PCC rules for dedicated signalling bearer (R11 29.061) | Huawei | 29.061 | 0389 | 0 | Rel-11 | Agreed | 11.2.0 | SAES-St3-intwk | A |  | 71 |
| C3-121892 | 11.21 | CR | Correcting minor errors | Ericsson | 29.165 | 0500 | 0 | Rel-11 | Agreed | 11.4.0 | IMSprotoc5 | F |  | 71 |
| C3-121916 | 11.25 | CR | Corrections to the call flows for NSWO | ZTE | 29.213 | 0449 | 0 | Rel-11 | Agreed | 11.4.0 | BBAI_BBII-CT | F |  | 71 |
| C3-121917 | 11.25 | CR | Editorial corrections to the BBAI BB2 architecture | ZTE, Ericsson | 29.215 | 0277 | 0 | Rel-11 | Agreed | 11.6.0 | BBAI_BBII-CT | F |  | 71 |
| C3-121922 | 11.37 | CR | T.38 default version | Nokia Siemens Networks | 29.163 | 0693 | 0 | Rel-11 | Agreed | 11.4.0 | MMTel_T.38_FAX | F |  | 71 |
| C3-121969 | 11.3 | CR | PCC CPE traversal support | Nokia Siemens Networks | 29.213 | 0450 | 1 | Rel-11 | Agreed | 11.4.0 | PCC | F |  | 71 |
| C3-121970 | 9.19 | CR | Removal of draft-dawes-dispatch-mediasec-parameter draft | Ericsson | 29.165 | 0476 | 1 | Rel-9 | Agreed | 9.12.0 | II-NNI | F |  | 71 |
| C3-121972 | 9.19 | CR | Removal of draft-dawes-dispatch-mediasec-parameter draft | Ericsson | 29.165 | 0478 | 1 | Rel-11 | Agreed | 11.4.0 | II-NNI | A |  | 71 |
| C3-121973 | 9.19 | CR | Trust domain error corrections | Ericsson | 29.165 | 0480 | 1 | Rel-9 | Agreed | 9.12.0 | II-NNI | F |  | 71 |
| C3-121974 | 9.19 | CR | Trust domain error corrections | Ericsson | 29.165 | 0481 | 1 | Rel-10 | Agreed | 10.9.0 | II-NNI | A |  | 71 |
| C3-121975 | 9.19 | CR | Trust domain error corrections | Ericsson | 29.165 | 0482 | 1 | Rel-11 | Agreed | 11.4.0 | II-NNI | A |  | 71 |
| C3-121976 | 9.23 | CR | Updating IMEI URN draft reference | Research in Motion | 29.163 | 0690 | 1 | Rel-9 | Agreed | 9.11.0 | IMS-EMER_GPRS_EPS_SRVCC | F |  | 71 |
| C3-121977 | 9.23 | CR | Updating IMEI URN draft reference | Research in Motion | 29.163 | 0691 | 1 | Rel-10 | Agreed | 10.7.0 | IMS-EMER_GPRS_EPS_SRVCC | A |  | 71 |
| C3-121978 | 9.23 | CR | Updating IMEI URN draft reference | Research in Motion | 29.163 | 0692 | 1 | Rel-11 | Agreed | 11.4.0 | IMS-EMER_GPRS_EPS_SRVCC | A |  | 71 |
| C3-121981 | 11.9 | CR | The deletion of Security-Server header from dynamic view tables | OKI, NTT | 29.165 | 0493 | 1 | Rel-11 | Agreed | 11.4.0 | NNI_DV | A |  | 71 |
| C3-121982 | 11.9 | CR | The deletion of Security-Server header from dynamic view tables | OKI, NTT | 29.165 | 0504 | 0 | Rel-10 | Agreed | 10.9.0 | NNI_DV | F |  | 71 |
| C3-121984 | 11.21 | CR | S-CSCF restoration procedures | Ericsson | 29.165 | 0479 | 1 | Rel-11 | Agreed | 11.4.0 | IMSprotoc5 | F |  | 71 |
| C3-121985 | 11.21 | CR | Reference column in MIME body table | Ericsson | 29.165 | 0490 | 1 | Rel-11 | Agreed | 11.4.0 | IMSProtoc5 | F |  | 71 |
| C3-121989 | 11.16 | CR | Correction on ADC functionality description (R11 29.212) | Huawei, Hisilicon, Allot Communications | 29.212 | 0927 | 1 | Rel-11 | Agreed | 11.6.0 | SAPP-CT3 | F |  | 71 |
| C3-121990 | 11.23 | CR | Assignment of allocated Diameter code values | Ericsson, Juniper | 29.368 | 0001 | 1 | Rel-11 | Agreed | 11.0.0 | SIMTC-Reach | F |  | 71 |
| C3-121992 | 11.16 | CR | Correction on ADC functionality description (R11 29.213) | Huawei, Hisilicon, Allot Communications | 29.213 | 0443 | 1 | Rel-11 | Agreed | 11.4.0 | SAPP-CT3 | F |  | 71 |
| C3-121993 | 11.16 | CR | Enforcement order of PCC and ADC rules for PCEF enhanced with ADC (R11 29.212) | Huawei, Deutsche Telekom, Allot Communications | 29.212 | 0928 | 1 | Rel-11 | Agreed | 11.6.0 | SAPP-CT3 | F |  | 71 |
| C3-121995 | 11.24 | CR | AVP of PCRF address in session establishment trigger | ZTE | 29.213 | 0444 | 1 | Rel-11 | Agreed | 11.4.0 | BBAI_BBI-CT | F |  | 71 |
| C3-121996 | 11.24 | CR | Correction to the BPCF Addressing | ZTE | 29.213 | 0445 | 1 | Rel-11 | Agreed | 11.4.0 | BBAI_BBI-CT | F |  | 71 |
| C3-121998 | 11.24 | CR | AN-GW-Address over Gx for EPC-routed | ZTE, CATT | 29.212 | 0942 | 1 | Rel-11 | Agreed | 11.6.0 | BBAI_BBI-CT | F |  | 71 |
| C3-122000 | 11.24 | CR | AVP for S9 session termination notification | ZTE, Ericsson, Huawei | 29.215 | 0275 | 1 | Rel-11 | Agreed | 11.6.0 | BBAI_BBI-CT | F |  | 71 |
| C3-122006 | 8.5 | CR | Bearer binding mechenism for GPRS | ZTE | 29.212 | 0937 | 1 | Rel-8 | Agreed | 8.16.0 | PCC | A |  | 71 |
| C3-122007 | 8.5 | CR | Bearer binding mechenism for GPRS | ZTE | 29.212 | 0938 | 1 | Rel-9 | Agreed | 9.11.0 | PCC | A |  | 71 |
| C3-122008 | 8.5 | CR | Bearer binding mechenism for GPRS | ZTE | 29.212 | 0939 | 1 | Rel-10 | Agreed | 10.8.0 | PCC | A |  | 71 |
| C3-122009 | 8.5 | CR | Bearer binding mechenism for GPRS | ZTE | 29.212 | 0940 | 1 | Rel-11 | Agreed | 11.6.0 | PCC | A |  | 71 |
| C3-122010 | 8.14.2 | CR | QCI and ARP handling, Gn connected P-GW | Ericsson | 29.212 | 0913 | 1 | Rel-8 | Agreed | 8.16.0 | SAES-St3-PCC | F |  | 71 |
| C3-122011 | 8.14.2 | CR | QCI and ARP handling, Gn connected P-GW | Ericsson | 29.212 | 0914 | 1 | Rel-9 | Agreed | 9.11.0 | SAES-St3-PCC | A |  | 71 |
| C3-122012 | 8.14.2 | CR | QCI and ARP handling, Gn connected P-GW | Ericsson | 29.212 | 0915 | 1 | Rel-10 | Agreed | 10.8.0 | SAES-St3-PCC | A |  | 71 |
| C3-122013 | 8.14.2 | CR | QCI and ARP handling, Gn connected P-GW | Ericsson | 29.212 | 0916 | 1 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | A |  | 71 |
| C3-122018 | 11.5 | CR | Clean up of Editor's Notes (R11 29.214) | Huawei | 29.214 | 0253 | 1 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | F |  | 71 |
| C3-122019 | 11.5 | CR | Clean up of Editor's Notes (R11 29.215) | Huawei | 29.215 | 0273 | 1 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | F |  | 71 |
| C3-122021 | 11.5 | CR | Clean up of Editor's Notes (R11 29.212) | Huawei | 29.212 | 0925 | 1 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | F |  | 71 |
| C3-122023 | 10.17 | CR | OMR Signalling Flows | Huawei | 29.079 | 0019 | 2 | Rel-10 | Agreed | 10.3.0 | OMR | F |  | 71 |
| C3-122024 | 10.17 | CR | OMR Signalling Flows | Huawei | 29.079 | 0020 | 2 | Rel-11 | Agreed | 11.1.0 | OMR | A |  | 71 |
| C3-122026 | 10.18 | CR | Clarification of SDP setting condition over the II-NNI | Fujitsu, NTT | 29.165 | 0473 | 2 | Rel-10 | Agreed | 10.9.0 | II-NNI2 | F |  | 71 |
| C3-122027 | 10.18 | CR | Clarification of SDP setting condition over the II-NNI | Fujitsu, NTT | 29.165 | 0474 | 2 | Rel-11 | Agreed | 11.4.0 | II-NNI2 | A |  | 71 |
| C3-122032 | 11.35 | CR | Updating loopback example | Ericsson | 29.079 | 0015 | 1 | Rel-11 | Agreed | 11.1.0 | RAVEL-CT | F |  | 71 |
| C3-122034 | 11.20 | CR | Feature capability g.3gpp.trf error corrections | Ericsson | 29.165 | 0483 | 1 | Rel-11 | Agreed | 11.4.0 | NNI_OI | F |  | 71 |
| C3-122035 | 11.35 | CR | Ravel-related minor corrections | Nokia Siemens Networks | 29.165 | 0501 | 1 | Rel-11 | Agreed | 11.4.0 | RAVEL-CT | F |  | 71 |
| C3-122037 | 11.21 | CR | Interface between the ISC gateway and an AS in an enterprise network | Ericsson | 29.165 | 0475 | 1 | Rel-11 | Agreed | 11.4.0 | IMSProtoc5 | B |  | 71 |
| C3-122038 | 11.41 | CR | 100 Trying not interworked between IMS and SIP-I based CS CN | Nokia Siemens Networks | 29.235 | 0092 | 1 | Rel-11 | Agreed | 11.0.0 | SIP-Nc | F |  | 71 |
| C3-122051 | 10.21.2 | CR | Reference update: RFC 6679 | Ericsson | 29.162 | 0113 | 1 | Rel-10 | Agreed | 10.6.0 | ECSRA_LAA-CN | F |  | 71 |
| C3-122052 | 10.21.2 | CR | Reference update: RFC 6679 | Ericsson | 29.162 | 0114 | 1 | Rel-11 | Agreed | 11.0.0 | ECSRA_LAA-CN | A |  | 71 |
| C3-122054 | 8.24 | CR | IMSI detach in MSC Server | Ericsson | 29.292 | 0058 | 1 | Rel-11 | Agreed | 11.3.0 | ICSRA | F |  | 71 |
| C3-122058 | 11.23 | CR | Removal of empty clauses | Nokia Siemens Networks | 29.368 | 0004 | 0 | Rel-11 | Agreed | 11.0.0 | SIMTC-Reach | F |  | 71 |
| C3-122060 | 11.24 | CR | Correction to the DRA functionality for NSWO Addressing | ZTE | 29.213 | 0448 | 1 | Rel-11 | Agreed | 11.4.0 | BBAI_BBII-CT | F |  | 71 |
| C3-122061 | 11.25 | CR | Clarification of S9 session procedure for NSWO traffic | ZTE | 29.215 | 0278 | 1 | Rel-11 | Agreed | 11.6.0 | BBAI_BBII-CT | F |  | 71 |
| C3-122062 | 11.17 | CR | Clarification of Supported-Features AVP (29.219 R11) | Ericsson | 29.219 | 0008 | 1 | Rel-11 | Agreed | 11.2.0 | QoS_SSL-CT3 | F |  | 71 |
| C3-122064 | 11.38 | CR | PCC Impacts due to SGW Restoration procedures | Ericsson | 29.212 | 0918 | 1 | Rel-11 | Agreed | 11.6.0 | eNR_EPC | B |  | 71 |
| C3-122065 | 12.1 | CR | APCO used in IP-CAN session establishment procedure (R11 29.061) | Huawei | 29.061 | 0390 | 1 | Rel-12 | Agreed | 11.2.0 | SAES_WLAN_EPC_intwk | B |  | 71 |
| C3-122068 | 11.24 | CR | Corrections to the call flows for EPC-routed | ZTE | 29.213 | 0446 | 1 | Rel-11 | Agreed | 11.4.0 | BBAI_BBI-CT | F |  | 71 |
| C3-122070 | 8.14.3 | CR | PCC procedures for Rx sessions with no service information | Ericsson | 29.214 | 0248 | 1 | Rel-8 | Agreed | 8.13.0 | SAES-St3-PCC | F |  | 71 |
| C3-122071 | 10.18 | CR | Policy-Contact in OMA 29.165r11 | Orange | 29.165 | 0503 | 2 | Rel-11 | Agreed | 11.4.0 | II-NNI2 | A |  | 71 |
| C3-122074 | 7.5 | CR | QoS parameters which can be upgraded or downgraded (R7 29.212) | Huawei | 29.212 | 0920 | 2 | Rel-7 | Agreed | 7.14.0 | PCC | F |  | 71 |
| C3-122076 | 7.5 | CR | QoS parameters which can be upgraded or downgraded (R9 29.212) | Huawei | 29.212 | 0922 | 2 | Rel-9 | Agreed | 9.11.0 | PCC | A |  | 71 |
| C3-122077 | 7.5 | CR | QoS parameters which can be upgraded or downgraded (R10 29.212) | Huawei | 29.212 | 0923 | 2 | Rel-10 | Agreed | 10.8.0 | PCC | A |  | 71 |
| C3-122078 | 7.5 | CR | QoS parameters which can be upgraded or downgraded (R11 29.212) | Huawei | 29.212 | 0924 | 2 | Rel-11 | Agreed | 11.6.0 | PCC | A |  | 71 |
| C3-122084 | 11.5 | CR | Clean up of Editor's Notes (R11 29.213) | Huawei | 29.213 | 0442 | 2 | Rel-11 | Agreed | 11.4.0 | SAES-St3-PCC | F |  | 71 |
| C3-122085 | 11.16 | CR | Redirect address for ADC rule (R11 29.212) | Huawei, Ericsson | 29.212 | 0929 | 2 | Rel-11 | Agreed | 11.6.0 | SAPP-CT3 | F |  | 71 |
| C3-122087 | 11.17 | CR | Addition of values to the Experimental-Result-Code AVP | Tekelec, Verizon, Alcatel-Lucent, Huawei | 29.219 | 0010 | 4 | Rel-11 | Agreed | 11.2.0 | QoS_SSL-CT3 | F |  | 71 |
| C3-122088 | 11.35 | CR | GTPv2 supported in S2a and S2b (R11 29.061) | Ericsson | 29.061 | 0391 | 2 | Rel-12 | Agreed | 11.2.0 | SAES_WLAN_EPC_intwk | B |  | 71 |
| C3-122089 | 11.24 | CR | Clarification of the S9 session procedure for EPC-routed traffic | ZTE | 29.215 | 0276 | 3 | Rel-11 | Agreed | 11.6.0 | BBAI_BBI-CT | F |  | 71 |
| C3-122091 | 11.30 | CR | Additional Text for Support of Multimedia Priority Service (MPS) in over Mn Interface | Applied Communication Sciences, NCS, AT&T, Alcatel-Lucent | 29.163 | 0694 | 2 | Rel-11 | Agreed | 11.4.0 | eMPS_Gateway | F |  | 71 |
| C3-122092 | 8.14.3 | CR | PCC procedures for Rx sessions with no service information | Ericsson | 29.214 | 0249 | 1 | Rel-9 | Agreed | 9.10.0 | SAES-St3-PCC | A |  | 71 |
| C3-122093 | 8.14.3 | CR | PCC procedures for Rx sessions with no service information | Ericsson | 29.214 | 0250 | 1 | Rel-10 | Agreed | 10.7.0 | SAES-St3-PCC | A |  | 71 |
| C3-122094 | 8.14.3 | CR | PCC procedures for Rx sessions with no service information | Ericsson | 29.214 | 0251 | 1 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | A |  | 71 |
| C3-122095 | 11.5 | CR | Clarification of Supported-Features AVP (29.212 R11) | Ericsson | 29.212 | 0912 | 2 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | F |  | 71 |
| C3-122096 | 11.5 | CR | Clarification of Supported-Features AVP (29.214 R11) | Ericsson | 29.214 | 0247 | 2 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | F |  | 71 |
| C3-122097 | 11.5 | CR | Clarification of Supported-Features AVP (29.215 R11) | Ericsson | 29.215 | 0272 | 2 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | F |  | 71 |
| C3-122098 | 11.22 | CR | End of CS to PS handover procedure | Ericsson | 29.212 | 0919 | 2 | Rel-11 | Agreed | 11.6.0 | rSRVCC-CT | F |  | 71 |
| C3-122100 | 11.24 | CR | AVP for S9 session termination notification | ZTE, Ericsson | 29.213 | 0447 | 2 | Rel-11 | Agreed | 11.4.0 | BBAI_BBI-CT | F |  | 71 |
| C3-122101 | 9.19 | CR | Removal of draft-dawes-dispatch-mediasec-parameter draft | Ericsson | 29.165 | 0477 | 4 | Rel-10 | Agreed | 10.9.0 | II-NNI | A |  | 71 |
| C3-122102 | 10.18 | CR | Policy-Contact in OMA 29.165r10 | Orange | 29.165 | 0502 | 3 | Rel-10 | Agreed | 10.9.0 | II-NNI2 | F |  | 71 |
| C3-122104 | 11.3 | CR | Correction of PCRF addressing in the presence of NAT devices and overlapping address space | China Mobile, Huawei, ZTE | 29.213 | 0451 | 2 | Rel-11 | Agreed | 11.4.0 | PCC | F |  | 71 |
| C3-122105 | 11.3 | CR | Correction of Rx reference point for PCRF addressing | China Mobile, Huawei, ZTE | 29.214 | 0255 | 2 | Rel-11 | Agreed | 11.6.0 | PCC | F |  | 71 |
| C3-122110 | 11.23 | CR | Correction of MTC-IWF checks on quota and rate of device triggers from SCS | Intel, Chen-Ho | 29.368 | 0003 | 3 | Rel-11 | Agreed | 11.0.0 | SIMTC-Reach | F |  | 71 |
| C3-122113 | 7.5 | CR | QoS parameters which can be upgraded or downgraded (R8 29.212) | Huawei, ZTE | 29.212 | 0921 | 3 | Rel-8 | Agreed | 8.16.0 | PCC | A |  | 71 |
| C3-122114 | 8.14.2 | CR | TFT usage for the primary PDP context when using PGW (R8 29.212) | Huawei | 29.212 | 0945 | 3 | Rel-8 | Agreed | 8.16.0 | SAES-St3-PCC | F |  | 71 |
| C3-122115 | 8.14.2 | CR | TFT usage for the primary PDP context when using PGW (R9 29.212) | Huawei | 29.212 | 0946 | 2 | Rel-9 | Agreed | 9.11.0 | SAES-St3-PCC | A |  | 71 |
| C3-122116 | 8.14.2 | CR | TFT usage for the primary PDP context when using PGW (R10 29.212) | Huawei | 29.212 | 0947 | 2 | Rel-10 | Agreed | 10.8.0 | SAES-St3-PCC | A |  | 71 |
| C3-122117 | 8.14.2 | CR | TFT usage for the primary PDP context when using PGW (R11 29.212) | Huawei | 29.212 | 0948 | 2 | Rel-11 | Agreed | 11.6.0 | SAES-St3-PCC | A |  | 71 |
| C3-122118 | 10.18 | CR | Description of charging correlation over II-NNI | NTT | 29.165 | 0498 | 3 | Rel-10 | Agreed | 10.9.0 | II-NNI2 | F |  | 71 |
| C3-122120 | 11.24 | CR | AVP of PCRF address in session establishment trigger | ZTE | 29.215 | 0274 | 3 | Rel-11 | Agreed | 11.6.0 | BBAI_BBI-CT | F |  | 71 |
| C3-122121 | 11.39 | CR | Event based load control | Ericsson | 29.165 | 0486 | 3 | Rel-11 | Agreed | 11.4.0 | IOC | B |  | 71 |
| C3-122122 | 10.18 | CR | Description of charging correlation over II-NNI | NTT | 29.165 | 0499 | 4 | Rel-11 | Agreed | 11.4.0 | II-NNI2 | A |  | 71 |
| C3-122128 | 11.30 | CR | Support of Multimedia Priority Service (MPS) in Modify over Ix Interface | Applied Communication Sciences, National Communica | 29.162 | 0115 | 4 | Rel-11 | Agreed | 11.0.0 | eMPS_Gateway | F |  | 71 |

## Annex E. List of Participants

| Name | Representing | Status-Partner | Ctry | Ph | Mob Ph | Email |
| --- | --- | --- | --- | --- | --- | --- |
| Allen, Andrew (Mr.) | Research in Motion Japan Ltd. | 3GPPMEMBER (ARIB) | US | +18478098636 |  | aallen@rim.com |
| Arai, Kenjiro (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81422593518 |  | arai.kenjiro@lab.ntt.co.jp |
| Ascolese, Antonio (Ing.) | TELECOM ITALIA S.p.A. | 3GPPMEMBER (ETSI) | IT | +390112285392 |  | antonio.ascolese@telecomitalia.it |
| Axell, Jorgen (Dr.) | Nanjing Ericsson Panda Com Ltd | 3GPPMEMBER (CCSA) | SE | +46 10 719 4450 | +46 70 519 4450 | Jorgen.Axell@ericsson.com |
| Bakker, John-Luc (Mr.) | Research in Motion UK Limited | 3GPPMEMBER (ETSI) | GB | +1-972-373-1761 | +1-908-463-7321 | jbakker@rim.com |
| Belling, Thomas (Dr.) | Nokia Siemens Networks GmbH | 3GPPMEMBER (ETSI) | DE | +49 89 5159 75207 | +49 172 2974678 | Thomas.Belling@nsn.com |
| Berionne, Michele (Mr.) | Qualcomm Incorporated | 3GPPMEMBER (ATIS) | US | +18585983642 |  | micheleb@qti.qualcomm.com |
| BERTRAND, Simon (Mr.) | ORANGE SA | 3GPPMEMBER (ETSI) | FR | +33145294200 |  | simon.bertrand@orange.com |
| Biondic, Nevenka (Mrs.) | Ericsson Inc. | 3GPPMEMBER (ATIS) | HR | +385 1 365 3824 |  | nevenka.biondic@ericsson.com |
| Brinkmann, Horst (Mr.) | Alcatel-Lucent Deutschland AG | 3GPPMEMBER (ETSI) | DE | +49 711 821 37207 |  | horst.brinkmann@alcatel-lucent.com |
| Chin, Chen-ho (Mr.) | Intel China Ltd. | 3GPPMEMBER (CCSA) |  |  | +32477413371 | chen-hox.chin@intel.com |
| Chowdhury, Sayan (Mr.) | Tekelec | 3GPPMEMBER (ATIS) | US | +1-508-804-7078 |  | sayan.chowdhury@tekelec.com |
| Dobrowolska, Beata (Ms.) | France Telecom | 3GPPMEMBER (ETSI) | FR | +33145295759 |  | beata.dobrowolska@orange.com |
| Emanuelsson, Sven-ove (Mr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | SE | +46107121548 |  | sven-ove.emanuelsson@ericsson.com |
| Fernandez, Susana (Miss) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | ES | +34646006865 |  | susana.fernandez@ericsson.com |
| Gebler, Erik (Mr.) | Acision UK Ltd | 3GPPMEMBER (ETSI) | NL | +31 30 210 3173 | +31 624 241 655 | erik.gebler@acision.com |
| Goldner, Alla (Mrs.) | Allot Communications Ltd. | 3GPPMEMBER (ETSI) | IL | +97297619251 |  | agoldner@allot.com |
| Han, Jiwan (Mr.) | ETSI | 3GPPORG_REP (ETSI) | FR | +33 (4) 92 94 42 31 | +33 (0)6 74 40 83 69 | jiwan.han@etsi.org |
| Herrero-Veron, Christian (Mr.) | Huawei Technologies Japan Co., | 3GPPMEMBER (ARIB) | SE | +46739200806 |  | christian.herrero@huawei.com |
| Hodges, Phil (Mr.) | Ericsson Japan K.K. | 3GPPMEMBER (ARIB) | AU | +61 404069546 |  | philip.hodges@ericsson.com |
| Holm, Jan (Mr.) | Ericsson Japan K.K. | 3GPPMEMBER (ARIB) | SE | +46 8 719 7378 | + 46705197378 | Jan.Holm@ericsson.com |
| Huslende, Ragnar (Dr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | NO | +47 911 10828 | +47 911 10828 | ragnar.huslende@ericsson.com |
| Inoue, Yoshihiro (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81 422 36 7502 |  | yoshihiro.inoue@ntt-at.co.jp |
| Jesske, Roland (Mr.) | Deutsche Telekom AG | 3GPPMEMBER (ETSI) | DE | +49 6151 5812766 | +49 171 861 8445 | r.jesske@telekom.de |
| Landais, Bruno (Mr.) | Alcatel-Lucent | 3GPPMEMBER (ETSI) | FR | +33 2 96 04 82 61 |  | bruno.landais@alcatel-lucent.com |
| Lavasani, Shahab (Mr.) | Huawei Technologies Sweden AB | 3GPPMEMBER (ETSI) | SE | +46 70 6360204 | +46 70 6360204 | shahab.lavasani@huawei.com |
| Li, Zhijun (Mr.) | ZTE Corporation | 3GPPMEMBER (ETSI) | CN | +86 25 52877867 |  | li.zhijun3@zte.com.cn |
| Lu, Fei (Mr.) | ZTE Corporation | 3GPPMEMBER (CCSA) | CN | +86-25-88014634 | +86-13951628123 | lu.fei1@zte.com.cn |
| Lukacs, Donald (Mr.) | Applied Communication Sciences | 3GPPMEMBER (ATIS) |  | +17327585293 |  | dlukacs@appcomsci.com |
| Mase, Asami (Miss) | Oki Electric Industry Co. Ltd. | 3GPPMEMBER (TTC) | JP | + |  | mase622@oki.com |
| Meredith, John M (Mr.) | ETSI | 3GPPORG_REP (ETSI) | FR | +33 4 92 94 42 37 | +33 (0)6 10 42 03 76 | john.meredith@etsi.org |
| Monrad, Atle (Mr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | NO | +47 45410665 | +47 454 10 665 | atle.monrad@ericsson.com |
| Muto, Yuta (Mr.) | Hitachi Ltd. | 3GPPMEMBER (ARIB) | JP | +81-42-323-1111 |  | yuta.muto.nc@hitachi.com |
| Okada, Yuki (Mr.) | Fujitsu Limited | 3GPPMEMBER (ARIB) | JP | +81-44-754-4146 |  | okada.yuki@jp.fujitsu.com |
| Pham, Quang truong (Mr.) | NEC Corporation | 3GPPMEMBER (ARIB) | JP | +81 3 3798 9259 |  | q-pham@az.jp.nec.com |
| Ping, Lin () | China Mobile Com. Corporation | 3GPPMEMBER (CCSA) | CN | +86 10 63604880 |  | linping@chinamobile.com |
| Punz, Gottfried (Mr.) | NEC EUROPE LTD | 3GPPMEMBER (ETSI) |  | +4962214342119 | +491776968288 | gottfried.punz@neclab.eu |
| Qiao, Weihua (Mr.) | HuaWei Technologies Co., Ltd | 3GPPMEMBER (CCSA) | CN | +86 10 82882310 |  | qiaoweihua@huawei.com |
| Räsänen, Juha (Mr.) | Nokia Siemens Networks Oy | 3GPPMEMBER (ETSI) | FI | +358 7180 08000 | +358 40 543 9058 | juha.rasanen@nsn.com |
| Shi, Susan (Ms.) | Huawei Technologies (UK) | 3GPPMEMBER (ETSI) | CN | +86 02987607582 |  | shishf@huawei.com |
| Shu, Lin (Mr.) | HiSilicon Technologies Co., Lt | 3GPPMEMBER (CCSA) | CN | +86-15216618582 |  | shulin@huawei.com |
| Subramanian, Ramachandran (Mr.) | QUALCOMM UK Ltd | 3GPPMEMBER (ETSI) | US | +1 858 651 2350 |  | rsubrama@qti.qualcomm.com |
| Suzuki, Naoaki (Mr.) | NEC Corporation | 3GPPMEMBER (TTC) | JP | +81-4-7185-6722 |  | n-suzuki@en.jp.nec.com |
| Wang, Jianrong (Ms.) | AT&T GNS Belgium SPRL | 3GPPMEMBER (ETSI) | US | +14255807701 | +1 4255807701 | jianrong.wang@att.com |
| YANG, Weiwei (Mr.) | HuaWei Technologies Co., Ltd | 3GPPMEMBER (ATIS) | GB |  |  | tommy@huawei.com |
| Yi Feng, Bi (Mr.) | ZTE Corporation | 3GPPMEMBER (CCSA) | CN | +86 755 5739300 |  | bi.yifeng@zte.com.cn |
| Zhou, Xiaoyun (Mr.) | ZTE Corporation | 3GPPMEMBER (CCSA) | CN | +8613813823840 |  | zhou.xiaoyun@zte.com.cn |

Report prepared by: Jiwan HAN