Third Generation Partnership Project (3GPP™)

DRAFT Meeting Report
for
TSG CT WG3
meeting: 74bis

Porto, Portugal, 07/10/2013 to 11/10/2013

1	Opening of the meeting	6

2	Agenda/schedule	6

2.1	Approval of the agenda.	6

2.2	Proposed schedule	6

3	Registration of documents	6

4	Reports	7

4.1	Report from previous CT3 meeting	7

4.2	Report from previous CT plenary	7

4.3	Reports from other groups	8

5	Items for immediate consideration	8

5.1	IPR disclosures	8

5.2	Other items for immediate consideration	8

6	Received Liaison Statements	8

7	Release 7 and earlier releases	11

7.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	11

7.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	11

7.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]	11

7.4	Multimedia Broadcast and Multicast Service  [MBMS]	11

7.5	Policy and Charging Control [PCC]	11

7.6	Diameter for Gi interface [DIAMGi]	12

7.7	Diameter for Wi interface [DIAMWi]	12

7.8	Multimedia interworking between IMS and CS networks [MIW-IMS]	12

7.9	Protocol impact from providing IMS services via fixed broadband [FBI]	12

7.10	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	12

7.11	Technical Enhancements and Improvements [TEIx]	12

7.12	Other Work Items	12

8	Release 8	12

8.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	12

8.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	12

8.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]	14

8.4	Multimedia Broadcast and Multicast Service  [MBMS]	14

8.5	Policy and Charging Control (non-SAE) [PCC]	14

8.6	Void	16

8.7	Diameter for Gi interface [DIAMGi]	16

8.8	Diameter for Wi interface [DIAMWi]	16

8.9	Void	16

8.10	Protocol impact from providing IMS services via fixed broadband [FBI]	16

8.11	IMS Interworking Protocol Aspects in Support of Cable Rebulatory Requirements [PktCbl-Intw]	16

8.12	Void	16

8.13	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	16

8.14	PCC aspects of SAE [SAES-St3-PCC]	16

8.14.1	- Signalling flows (29.213)	17

8.14.2	- Gx and Gxx interfaces (29.212)	17

8.14.3	- Rx interface (29.214)	18

8.14.4	- S9 interface (29.215)	19

8.15	Interworking between EPC and external PDNs [SAES-St3-intwk]	19

8.16	IMS inter-operator service interconnection interface [FBI2-IOPSI]	19

8.17	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	19

8.18	Interworking between User-to-User Signaling (UUS) and SIP [UUSIW]	19

8.19	Work Items related to TISPAN transfer	19

8.19.1	- Maintenance of TISPAN R1 [MAINT_R1]	19

8.19.2	- Maintenance of TISPAN R2 [MAINT_R2]	19

8.19.3	- Documentation of TISPAN R1 and R2  in CT3 [REDOC_TIS-C3]	19

8.19.4	- Support of Overlap signalling [Overlap]	19

8.19.5	- Stage 3 (CT3) of CWonIMS [CW_IMS]	19

8.19.6	- Stage 3 (CT3) of [CCBS_CCNR]	19

8.20	Contributions on Common IMS related to 3GPP2 [REDOC_3GPP2]	19

8.21	Support of Service-Level Interworking for Messaging Services [MESSIW]	19

8.22	Enhancement of interworking between MTSI and Circuit Switched networks  [MTSI_eMHI]	19

8.23	Core Network Impacts for A-Interface Over IP [AoIP-CN]	19

8.24	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]	19

8.25	CAT solution for voice and video call in CS domain [CAT_SS]	19

8.26	Technical Enhancements and Improvements [TEI8]	19

8.27	Rel-8 contributions on other Work Items	19

9	Release 9	19

9.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	20

9.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	20

9.3	Protocol impact from providing IMS services via fixed broadband [FBI]	20

9.4	MBMS [MBMS]	20

9.5	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]	20

9.6	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]	20

9.7	PCC aspects of SAE [SAES-St3-PCC]	20

9.8	Reserved	20

9.9	Reserved	20

9.10	Reserved	20

9.11	Reserved	20

9.12	Reserved	20

9.13	Reserved	20

9.14	Reserved	20

9.15	Reserved	20

9.16	CS-IBCF and CS-TrGW definition in 3GPP specifications           [CS-IBCF]	20

9.17	Interconnection Border Control Function (IBCF) – Transition Gateway (TrGW); Ix interface, Stage 3 [IMS_IBCF]	20

9.18	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	20

9.19	Operational Description of the Inter-IMS NNI   [II-NNI]	20

9.20	Support for IMS Emergency Calls over GPRS and EPS [IMS_EMER_GPRS_EPS]	23

9.21	PCC Enhancements [PCC-Enh]	23

9.22	Completion of IMS Restoration Procedures [eIMS_RP]	23

9.23	CT1 aspects of SRVCC support for IMS Emergency Calls [IMS_EMER_GPRS_EPS-SRVCC]	23

9.24	IMS Media Plane Security [MEDIASEC_CORE]	23

9.25	Technical Enhancements and Improvements [TEI9]	23

9.26	Rel-9 contributions on other work items	23

10	Release 10	23

10.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	23

10.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	23

10.3	PCC aspects of SAE [SAES-St3-PCC]	23

10.4	Interworking between EPC and external PDNs [SAES-St3-intwk]	23

10.5	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	23

10.6	PCC Enhancements [PCC-Enh]	23

10.7	Reserved	23

10.8	Reserved	23

10.9	Reserved	23

10.10	Reserved	23

10.11	Reserved	23

10.12	Reserved	23

10.13	Reserved	23

10.14	Reserved	23

10.15	Reserved	24

10.16	CPM-SMS Interworking [CPM-SMS]	24

10.17	Optimal Media Routeing [OMR]	24

10.18	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]	24

10.19	Call Completion Not Logged in [CCNL]	26

10.20	IP Flow Mobility and WLAN offload (Stage 3) [IFOM-CT]	26

10.21	Enabling Coder Selection and Rate Adaption for UTRAN and E-UTRAN for Load Adaptive Applications, CN impacts [ECSRA_LAA-CN]	26

10.21.1	-  Packet Core impacts	26

10.21.2	-  IMS/CS impacts	26

10.22	S2b Mobility based on GTP [SMOG-St3]	26

10.23	CT aspects of Enhancements for Multimedia Priority Service [eMPS-CN]	26

10.24	PCRF failure and restoration [PCRF-FR]	26

10.25	CT aspects of Multi Access PDN Connectivity  [MAPCON-St3]	26

10.26	CT3 Aspects of Policy Enhancements for Sponsored Connectivity and Coherent Access to Policy related Data Bases [PEST-CT3]	26

10.27	Dynamic View of Headers in Messages for II-NNI [NNI_DV]	26

10.28	CS and IMS Interworking for CAT early session model [CIIC_ES]	26

10.29	Stage 3 for Network Improvements for Machine Type Communications [NIMTC]	26

10.30	Technical Enhancements and Improvements [TEI10]	26

10.31	Rel-10 contributions on other Work Items	26

11	Release 11	26

11.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	26

11.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	26

11.3	Policy Control and Charging [PCC]	27

11.4	Interworking between EPC and external PDNs [SAES-St3-intwk]	27

11.5	PCC aspects of SAE [SAES-St3-PCC]	27

11.6	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]	29

11.7	PCC Enhancements [PCC-Enh]	29

11.8	Optimal Media Routeing [OMR]	29

11.9	Dynamic View of Headers in Messages for II-NNI [NNI_DV]	29

11.10	Reserved	29

11.11	Reserved	29

11.12	Reserved	29

11.13	Reserved	29

11.14	Reserved	29

11.15	Reserved	29

11.16	CT3 aspects of Service Awareness and Privacy Policies [SAPP-CT3]	29

11.17	CT3 aspects of QoS Control Based on Subscriber Spending Limits  [QoS_SSL-CT3]	30

11.18	USSD Simulation Service in IMS-stage 3 [USSI]	31

11.19	Single Radio Video Call Continuity       [vSRVCC-CT]	31

11.19.1	- IMS-related	31

11.19.2	- PCC-related	31

11.20	Further improvement of usability of II-NNI specification for inter-connection [NNI_OI]	31

11.21	IMS Stage-3 IETF Protocol Alignment          [IMSProtoc5]	31

11.22	CT aspects of Single Radio Voice Call Continuity from UTRAN/GERAN to E-UTRAN/HSPA [rSRVCC-CT]	31

11.22.1	- IMS/CS related	31

11.22.2	- Packet Core related	31

11.23	Stage 3 for System Improvements to Machine-Type Communications [SIMTC-Reach]	31

11.24	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block I [BBAI_BBI-CT]	31

11.25	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block II [BBAI_BBII-CT]	32

11.26	CN aspects of Anonymous Call Rejection in the CS domain [ACR_CS-CN]	32

11.27	Advanced Interconnection of Services [IPXS]	32

11.28	Enhancements for Multimedia Priority Service (MPS)  Gateway Control Priority [eMPS_Gateway]	32

11.29	CN aspects of Mobility based On GTP & PMIPv6 for WLAN access to EPC [SaMOG_WLAN-CN]	32

11.30	CT aspect on Network Provided Location Information for IMS [NWK-PL2IMS-CT]	32

11.31	II-NNI enhancements: SIP timers applicability [NNI_timers]	34

11.32	Roaming Architecture for Voice over IMS with Local Breakout – CT aspects [RAVEL-CT]	34

11.33	Inclusion of Media Resource Broker [MRB]	35

11.34	Enhanced T.38 FAX support [MMTel_T.38_FAX]	35

11.35	Enhanced Nodes Restoration for EPC [eNR_EPC]	35

11.36	IMS overload control [IOC]	38

11.37	Technical Enhancements and Improvements [TEI11]	39

11.38	Rel-11 contributions on other Work Items	39

11.39	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]	40

12	Release 12	40

12.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]	40

12.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]	40

12.3	Policy Control and Charging [PCC]	40

12.4	PCC aspects of SAE [SAES-St3-PCC]	40

12.5	Reserved	41

12.6	Reserved	41

12.7	Reserved	41

12.8	Reserved	41

12.9	Reserved	41

12.10	Reserved	41

12.11	Interworking between a PLMN with WLAN to access the EPC and a PDN [SAES_WLAN_EPC_intwk]	41

12.12	CT aspects of Extended IMS media plane security features [eMEDIASEC-CT]	41

12.13	IMS-based Telepresence (Stage 3) [IMS_TELEP]	41

12.14	IMS Stage-3 IETF Protocol Alignment  [IMSProtoc6]	41

12.15	IMS Emergency PSAP Callback [EMC_PC]	41

12.16	Diameter Overload Control [FS_DOCME]	41

12.17	Study on  Indication of NNI Routeing scenarios in SIP requests [FS_NNI_RS]	41

12.18	Study on XML based access of AF to the PCRF [FS_XML_AF_PCRF]	46

12.24	CT3 Aspect of Usage Monitoring Control PCC Enhancement [UMONC-CT3]	49

12.25	CT Aspects of Signalling of Image Size [SIS-CT]	49

12.26	CT Aspects of End-to-End MTSI Extensions [E2EMTSI-CT]	50

12.27	Policy and Charging Control for supporting traffic from fixed terminals and NSWO traffic from 3GPP UEs in fixed broadband access networks [P4C-F-CT3]	50

12.28	Study on Technical aspects on Roaming End-to-end scenarios with VoLTE IMS and other networks [FS_REVOLTE_IMS]	55

12.29	CT Aspects of IMS Business Trunking for IP-PBX in Static Mode of operation [BusTI-CT]	58

12.30	Updating IMS to conform to RFC 6665 [UP6665]	58

12.31	eMBMS restoration procedures [eMBMS_Rest]	58

12.32	CT3 part of Support of RTP / RTCP multiplexing (signalling) in IMS [RTCP_MUX]	58

12.33	Technical Enhancements and Improvements [TEI12]	59

12.34	Rel-12 contributions on other Work Items	59

12.34.1	UE Power Consumption Optimizations, stage 3 [MTCe-UEPCOP-CT]	60

12.34.2	Enhancements to IMS Operator Determined Barring [eIODB]	60

13	Joint sessions	60

14	Work Organisation	60

14.1	Work Plan Review	60

14.2	Specification Review	61

14.3	Next meetings, allocation of hosts	61

14.4	Calendar	61

14.5	Other issues	61

15	Summary of results	61

16	Any other business	61

17	Closing of the meeting	63

Annex A. TS/TR	63

Annex B. Work Item	63

Annex C. Liaison Statements	63

Annex C.1 Incoming Liaison Statements	63

Annex C.2 Outgoing Liaison Statements	64

Annex D. Agreed Change Requests	64

Annex E. List of Participants	67

this draft:  Thursday, (2013-10-24) 12:23  [date/time according to secretary's PC time zone setting]

Note: Hyperlinks to tdocs will work only if the present report is in a subdirectory named "report" and the tdocs themselves are in a parallel subdirectory names "docs".

## 1	Opening of the meeting

The CT3 Chairman, Mr. Weihua Qiao (from Huawei) openned the meeting CT3#74 in Tiara Atlantic Park Hotel, Porto on 9h00, 7th October 2013.

Mr. Antonio Asccolesse (from TELECOM ITALIA S.p.A) gave a welcome speech on the behalf of EF3.

CT3 Chairman reminded the delegates the register

## 2	Agenda/schedule

### 2.1	Approval of the agenda.

C3-131323	Draft Agenda for the CT3#74bis Meeting
					Source: CT3 Chairman

Discussion:

This Draft Agenda was revised before the meeting.

Decision: 		The document was Revised to C3-131336.

C3-131326	INFO    Proposed Schedule for CT3#74bis
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-131336	Draft Agenda for the CT3#74bis Meeting
					Source: CT3 Chairman

(Replaces C3-131323)

Decision: 		The document was Approved.

### 2.2	Proposed schedule

## 3	Registration of documents

C3-131327	Allocation of documents to agenda items (at Deadline)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-131328	Allocation of documents to agenda items (Start of Day 1)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-131329	Allocation of documents to agenda items (Start of Day 2)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-131330	Allocation of documents to agenda items (Start of Day 3)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-131331	Allocation of documents to agenda items (Start of Day 4)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-131332	Allocation of documents to agenda items (Start of Day 5)
					Source: CT3 Chairman

Decision: 		The document was Noted.

C3-131333	Allocation of documents to agenda items (End of Day 5)
					Source: CT3 Chairman

Decision: 		The document was Noted.

## 4	Reports

### 4.1	Report from previous CT3 meeting

C3-131482	Approved Meeting Report from CT3#74
					Source: MCC

Decision: 		The document was Approved.

### 4.2	Report from previous CT plenary

C3-131334	Brief Notes from CT#61 relevant to CT3
					Source: CT3 Chairman

Decision: 		The document was Noted.

### 4.3	Reports from other groups

## 5	Items for immediate consideration

### 5.1	IPR disclosures

### 5.2	Other items for immediate consideration

## 6	Received Liaison Statements

C3-131486	LS on updating 3GPP IMS to support RFC 6665
					Source: TSG CT WG1

Discussion:

CT3 have the related CRs in this meeting.

Decision: 		The document was Noted.

C3-131487	Reply LS on uplink packet filters
					Source: TSG CT WG1

Discussion:

No impact on CT3's PCC aspacts is foreseen for the time being.

Decision: 		The document was Noted.

C3-131488	LS on eMBMS service restoration 
					Source: TSG CT WG4

Decision: 		The document was Noted.

C3-131489	LS OUT on Rollback Behaviour in EPC during TAU/RAU rejection
					Source: TSG CT WG4

Discussion:

CT3 have noticed the impact on CT3 PCC aspects from this LS.

Decision: 		The document was Noted.

C3-131490	Reply LS on End-to-end QoS handling of MTSI
					Source: TSG CT WG4

Decision: 		The document was Noted.

C3-131491	LS on Parameter Format of AgeOfLocationInformation
					Source: TSG CT WG4

Decision: 		The document was Noted.

C3-131492	LS on new work item on "IMS support for RTP / RTCP transport multiplexing"
					Source: TSG CT WG4

Decision: 		The document was Noted.

C3-131493	Reply LS on Indication of NNI Routeing scenarios in SIP requests
					Source: GSMA

Discussion:

This LS is postponed. Mr. Jan Holm (from Ericsson) will have a research on this subject till the next meeting.

Decision: 		The document was Postponed.

C3-131494	LS on SMSC Usage Restriction 
					Source: TSG SA WG1

Decision: 		The document was Noted.

C3-131495	Reply to CT3 on Indication of NNI Routing scenarios in SIP requests
					Source: GSMA

Discussion:

This subject will be handled in the next week SA5 meeting. Mr. Jan Holm (from Ericsson)  and Mr. Roland Jesske (from Deutsche Telekom) will follow the progress of the subject. LS is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131496	LS on Normative work on overload handling for device triggering
					Source: TSG SA WG2

Decision: 		The document was Noted.

C3-131497	Reply LS to CT WG4 LS on new work item on "IMS support for RTP / RTCP transport multiplexing"
					Source: TSG SA WG2

Decision: 		The document was Noted.

C3-131498	Reply to LS from CT WG1 on uplink packet filters
					Source: TSG SA WG2

Discussion:

The decision which will decided in the upcoming SA2 is needed.

Decision: 		The document was Noted.

C3-131499	LS on End-to-end fixed-mobile interworking
					Source: TSG SA WG4

Discussion:

CT3 will study on the impact from this LS during this meeting or the upcomimg meeting.

Decision: 		The document was Noted.

C3-131500	Reply LS on End-to-end QoS handling of MTSI
					Source: TSG SA WG4

Discussion:

Replay LS on this LS is produced (C3-131501).

Decision: 		The document was Noted.

C3-131501	Reply LS on End-to-end QoS handling of MTSI
					Source: Ericsson

Decision: 		The document was Revised to C3-131594.

C3-131594	Reply LS on End-to-end QoS handling of MTSI
					Source: Ericsson

(Replaces C3-131501)

Decision: 		The document was Approved.

C3-131622	Reply LS on Reply LS on support for user location age or timestamp
					Source: TSG CT WG4

Discussion:

It is postponed till the next meeting.

Decision: 		The document was Postponed.

## 7	Release 7 and earlier releases

### 7.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 7.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 7.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]

### 7.4	Multimedia Broadcast and Multicast Service  [MBMS]

### 7.5	Policy and Charging Control [PCC]

C3-131459	Session binding clarification in relation to IPv6 prefix
					29.213	  CR-0515  (Rel-7) v7.12.0
					Source: Alcatel-Lucent

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131460	Session binding clarification in relation to IPv6 prefix
					29.213	  CR-0516  (Rel-8) v8.16.0
					Source: Alcatel-Lucent

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131461	Session binding clarification in relation to IPv6 prefix
					29.213	  CR-0517  (Rel-9) v9.11.0
					Source: Alcatel-Lucent

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131462	Session binding clarification in relation to IPv6 prefix
					29.213	  CR-0518  (Rel-10) v10.9.0
					Source: Alcatel-Lucent

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131463	Session binding clarification in relation to IPv6 prefix
					29.213	  CR-0519  (Rel-11) v11.8.0
					Source: Alcatel-Lucent

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131464	Session binding clarification in relation to IPv6 prefix
					29.213	  CR-0520  (Rel-12) v12.1.0
					Source: Alcatel-Lucent

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

### 7.6	Diameter for Gi interface [DIAMGi]

### 7.7	Diameter for Wi interface [DIAMWi]

### 7.8	Multimedia interworking between IMS and CS networks [MIW-IMS]

### 7.9	Protocol impact from providing IMS services via fixed broadband [FBI]

### 7.10	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 7.11	Technical Enhancements and Improvements [TEIx]

### 7.12	Other Work Items

## 8	Release 8

### 8.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 8.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-131411	Adding CS connected UEs
					29.162	  CR-0123  (Rel-8) v8.5.0
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-131412	Adding CS connected UEs
					29.162	  CR-0124  (Rel-9) v9.7.0
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-131413	Adding CS connected UEs
					29.162	  CR-0125  (Rel-10) v10.7.0
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-131414	Adding CS connected UEs
					29.162	  CR-0126  (Rel-11) v11.1.0
					Source: Ericsson

Decision: 		The document was Withdrawn.

C3-131415	Adding CS connected UEs
					29.162	  CR-0127  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131530.

C3-131530	Adding CS connected UEs
					29.162	  CR-0127  rev 1 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131415)

Discussion:

Category is changed to "F".

Decision: 		The document was Revised to C3-131574.

C3-131574	Adding CS connected UEs
					29.162	  CR-0127  rev 2 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131530)

Discussion:

WI code should be "IMS-CCR-IWCS" in the coverpage.

Decision: 		The document was Agreed.

### 8.3	Media Gateway Control Function (MGCF) – IM Media Gateway (IMS-MGW) Mn Interface [IMS-CCR-Mn]

### 8.4	Multimedia Broadcast and Multicast Service  [MBMS]

### 8.5	Policy and Charging Control (non-SAE) [PCC]

C3-131424	IP-CAN type notification correction
					29.214	  CR-0299  (Rel-8) v8.17.0
					Source: ZTE

Decision: 		The document was Revised to C3-131538.

C3-131425	IP-CAN type notification correction
					29.214	  CR-0300  (Rel-9) v9.14.0
					Source: ZTE

Decision: 		The document was Revised to C3-131539.

C3-131426	IP-CAN type notification correction
					29.214	  CR-0301  (Rel-10) v10.11.0
					Source: ZTE

Decision: 		The document was Revised to C3-131540.

C3-131427	IP-CAN type notification correction
					29.214	  CR-0302  (Rel-11) v11.10.0
					Source: ZTE

Decision: 		The document was Revised to C3-131541.

C3-131428	IP-CAN type notification correction
					29.214	  CR-0303  (Rel-12) v12.1.0
					Source: ZTE

Decision: 		The document was Revised to C3-131542.

C3-131538	IP-CAN type notification correction
					29.214	  CR-0299  rev 1 (Rel-8) v8.17.0
					Source: ZTE

(Replaces C3-131424)

Decision: 		The document was Revised to C3-131595.

C3-131539	IP-CAN type notification correction
					29.214	  CR-0300  rev 1 (Rel-9) v9.14.0
					Source: ZTE

(Replaces C3-131425)

Decision: 		The document was Revised to C3-131596.

C3-131540	IP-CAN type notification correction
					29.214	  CR-0301  rev 1 (Rel-10) v10.11.0
					Source: ZTE

(Replaces C3-131426)

Decision: 		The document was Revised to C3-131597.

C3-131541	IP-CAN type notification correction
					29.214	  CR-0302  rev 1 (Rel-11) v11.10.0
					Source: ZTE

(Replaces C3-131427)

Decision: 		The document was Revised to C3-131598.

C3-131542	IP-CAN type notification correction
					29.214	  CR-0303  rev 1 (Rel-12) v12.1.0
					Source: ZTE

(Replaces C3-131428)

Decision: 		The document was Revised to C3-131599.

C3-131595	IP-CAN type notification correction
					29.214	  CR-0299  rev 2 (Rel-8) v8.17.0
					Source: ZTE

(Replaces C3-131538)

Decision: 		The document was Agreed.

C3-131596	IP-CAN type notification correction
					29.214	  CR-0300  rev 2 (Rel-9) v9.14.0
					Source: ZTE

(Replaces C3-131539)

Decision: 		The document was Revised to C3-131638.

C3-131597	IP-CAN type notification correction
					29.214	  CR-0301  rev 2 (Rel-10) v10.11.0
					Source: ZTE

(Replaces C3-131540)

Decision: 		The document was Agreed.

C3-131598	IP-CAN type notification correction
					29.214	  CR-0302  rev 2 (Rel-11) v11.10.0
					Source: ZTE

(Replaces C3-131541)

Decision: 		The document was Agreed.

C3-131599	IP-CAN type notification correction
					29.214	  CR-0303  rev 2 (Rel-12) v12.1.0
					Source: ZTE

(Replaces C3-131542)

Decision: 		The document was Agreed.

C3-131638	IP-CAN type notification correction
					29.214	  CR-0300  rev 3 (Rel-9) v9.14.0
					Source: ZTE

(Replaces C3-131596)

Decision: 		The document was Agreed.

### 8.6	Void

### 8.7	Diameter for Gi interface [DIAMGi]

### 8.8	Diameter for Wi interface [DIAMWi]

### 8.9	Void

### 8.10	Protocol impact from providing IMS services via fixed broadband [FBI]

### 8.11	IMS Interworking Protocol Aspects in Support of Cable Rebulatory Requirements [PktCbl-Intw]

### 8.12	Void

### 8.13	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 8.14	PCC aspects of SAE [SAES-St3-PCC]

C3-131391	Correction in QoS derivation table in the AF
					29.213	  CR-0510  (Rel-8) v8.16.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131392	Correction in QoS derivation table in the AF
					29.213	  CR-0511  (Rel-9) v9.11.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131393	Correction in QoS derivation table in the AF
					29.213	  CR-0512  (Rel-10) v10.9.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131394	Correction in QoS derivation table in the AF
					29.213	  CR-0513  (Rel-11) v11.8.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131395	Correction in QoS derivation table in the AF
					29.213	  CR-0514  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Agreed.

#### 8.14.1	- Signalling flows (29.213)

#### 8.14.2	- Gx and Gxx interfaces (29.212)

C3-131338	Correction to QoS handling for interoperation with Gn/Gp SGSN
					29.212	  CR-1056  (Rel-8) v8.20.0
					Source: Huawei, China Telecom

Decision: 		The document was Withdrawn.

C3-131339	Correction to QoS handling for interoperation with Gn/Gp SGSN
					29.212	  CR-1057  (Rel-9) v9.15.0
					Source: Huawei, China Telecom

Decision: 		The document was Withdrawn.

C3-131340	Correction to QoS handling for interoperation with Gn/Gp SGSN
					29.212	  CR-1058  (Rel-10) v10.12.0
					Source: Huawei, China Telecom

Decision: 		The document was Withdrawn.

C3-131341	Correction to QoS handling for interoperation with Gn/Gp SGSN
					29.212	  CR-1059  (Rel-11) v11.10.0
					Source: Huawei, China Telecom

Decision: 		The document was Withdrawn.

C3-131342	Correction to QoS handling for interoperation with Gn/Gp SGSN
					29.212	  CR-1060  (Rel-12) v12.2.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131543.

C3-131543	Correction to QoS handling for interoperation with Gn/Gp SGSN
					29.212	  CR-1060  rev 1 (Rel-12) v12.2.0
					Source: Huawei, China Telecom

(Replaces C3-131342)

Discussion:

Category is changed to "F".

Decision: 		The document was Agreed.

#### 8.14.3	- Rx interface (29.214)

C3-131343	Corrections for PCC/QoS rule establishment failure
					29.214	  CR-0296  (Rel-8) v8.17.0
					Source: Huawei, China Telecom

Decision: 		The document was Agreed.

#### 8.14.4	- S9 interface (29.215)

### 8.15	Interworking between EPC and external PDNs [SAES-St3-intwk]

### 8.16	IMS inter-operator service interconnection interface [FBI2-IOPSI]

### 8.17	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

### 8.18	Interworking between User-to-User Signaling (UUS) and SIP [UUSIW]

### 8.19	Work Items related to TISPAN transfer

#### 8.19.1	- Maintenance of TISPAN R1 [MAINT_R1]

#### 8.19.2	- Maintenance of TISPAN R2 [MAINT_R2]

#### 8.19.3	- Documentation of TISPAN R1 and R2  in CT3 [REDOC_TIS-C3]

#### 8.19.4	- Support of Overlap signalling [Overlap]

#### 8.19.5	- Stage 3 (CT3) of CWonIMS [CW_IMS]

#### 8.19.6	- Stage 3 (CT3) of [CCBS_CCNR]

### 8.20	Contributions on Common IMS related to 3GPP2 [REDOC_3GPP2]

### 8.21	Support of Service-Level Interworking for Messaging Services [MESSIW]

### 8.22	Enhancement of interworking between MTSI and Circuit Switched networks  [MTSI_eMHI]

### 8.23	Core Network Impacts for A-Interface Over IP [AoIP-CN]

### 8.24	IMS Centralized Service Control Protocol, Addressing, Subscriber Data [ICSRA]

### 8.25	CAT solution for voice and video call in CS domain [CAT_SS]

### 8.26	Technical Enhancements and Improvements [TEI8]

### 8.27	Rel-8 contributions on other Work Items

## 9	Release 9

### 9.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 9.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 9.3	Protocol impact from providing IMS services via fixed broadband [FBI]

### 9.4	MBMS [MBMS]

### 9.5	Interworking between the 3GPP CS domain with BICC or ISUP as signalling protocol and external SIP-I networks [ExtSIPI]

### 9.6	Interworking between the 3GPP CS domain with SIP-I as signalling protocol and other networks [SIP_Nc]

### 9.7	PCC aspects of SAE [SAES-St3-PCC]

### 9.8	Reserved

### 9.9	Reserved

### 9.10	Reserved

### 9.11	Reserved

### 9.12	Reserved

### 9.13	Reserved

### 9.14	Reserved

### 9.15	Reserved

### 9.16	CS-IBCF and CS-TrGW definition in 3GPP specifications           [CS-IBCF]

### 9.17	Interconnection Border Control Function (IBCF) – Transition Gateway (TrGW); Ix interface, Stage 3 [IMS_IBCF]

### 9.18	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 9.19	Operational Description of the Inter-IMS NNI   [II-NNI]

C3-131369	Reference update of draft-vanelburg-dispatch-private-network-ind
					29.165	  CR-0593  (Rel-9) v9.15.0
					Source: NTT

Decision: 		The document was Agreed.

C3-131370	Reference update of draft-vanelburg-dispatch-private-network-ind
					29.165	  CR-0594  (Rel-10) v10.13.0
					Source: NTT

Decision: 		The document was Agreed.

C3-131371	Reference update of draft-vanelburg-dispatch-private-network-ind
					29.165	  CR-0595  (Rel-11) v11.8.0
					Source: NTT

Decision: 		The document was Agreed.

C3-131372	Reference update of draft-vanelburg-dispatch-private-network-ind
					29.165	  CR-0596  (Rel-12) v12.1.0
					Source: NTT

Decision: 		The document was Agreed.

C3-131376	Reference update: draft-kaplan-insipid-session-id
					29.165	  CR-0597  (Rel-9) v9.15.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131377	Reference update: draft-kaplan-insipid-session-id
					29.165	  CR-0598  (Rel-10) v10.13.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131378	Reference update: draft-kaplan-insipid-session-id
					29.165	  CR-0599  (Rel-11) v11.8.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131379	Reference update: draft-kaplan-insipid-session-id
					29.165	  CR-0600  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131473	Major capabilities of NOTIFY
					29.165	  CR-0571  rev 1 (Rel-9) v9.15.0
					Source: Fujitsu, NTT

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131474	Major capabilities of NOTIFY
					29.165	  CR-0572  rev 1 (Rel-10) v10.13.0
					Source: Fujitsu, NTT

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131475	Major capabilities of NOTIFY
					29.165	  CR-0573  rev 1 (Rel-11) v11.8.0
					Source: Fujitsu, NTT

Discussion:

This CR is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131476	Major capabilities of NOTIFY
					29.165	  CR-0574  rev 1 (Rel-12) v..
					Source: Fujitsu, NTT

Decision: 		The document was Revised to C3-131531.

C3-131531	Major capabilities of NOTIFY
					29.165	  CR-0574  rev 2 (Rel-12) v..
					Source: Fujitsu, NTT

(Replaces C3-131476)

Decision: 		The document was Agreed.

### 9.20	Support for IMS Emergency Calls over GPRS and EPS [IMS_EMER_GPRS_EPS]

### 9.21	PCC Enhancements [PCC-Enh]

### 9.22	Completion of IMS Restoration Procedures [eIMS_RP]

### 9.23	CT1 aspects of SRVCC support for IMS Emergency Calls [IMS_EMER_GPRS_EPS-SRVCC]

### 9.24	IMS Media Plane Security [MEDIASEC_CORE]

### 9.25	Technical Enhancements and Improvements [TEI9]

### 9.26	Rel-9 contributions on other work items

## 10	Release 10

### 10.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 10.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

### 10.3	PCC aspects of SAE [SAES-St3-PCC]

### 10.4	Interworking between EPC and external PDNs [SAES-St3-intwk]

### 10.5	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 10.6	PCC Enhancements [PCC-Enh]

### 10.7	Reserved

### 10.8	Reserved

### 10.9	Reserved

### 10.10	Reserved

### 10.11	Reserved

### 10.12	Reserved

### 10.13	Reserved

### 10.14	Reserved

### 10.15	Reserved

### 10.16	CPM-SMS Interworking [CPM-SMS]

### 10.17	Optimal Media Routeing [OMR]

### 10.18	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]

C3-131402	Correcting table number
					29.165	  CR-0603  (Rel-11) v11.8.0
					Source: Ericsson

Discussion:

WI is changed to "II-NNI2".

Decision: 		The document was Agreed.

C3-131403	Correcting table number
					29.165	  CR-0604  (Rel-12) v12.1.0
					Source: Ericsson

Discussion:

WI is changed to "II-NNI2".

Decision: 		The document was Agreed.

C3-131418	Removal of debug feature
					29.165	  CR-0607  (Rel-10) v10.13.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131532.

C3-131419	Removal of debug feature
					29.165	  CR-0608  (Rel-11) v11.8.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131533.

C3-131532	Removal of debug feature
					29.165	  CR-0607  rev 1 (Rel-10) v10.13.0
					Source: Ericsson

(Replaces C3-131418)

Decision: 		The document was Agreed.

C3-131533	Removal of debug feature
					29.165	  CR-0608  rev 1 (Rel-11) v11.8.0
					Source: Ericsson, Vodafone

(Replaces C3-131419)

Discussion:

This CR is the merger of C3-131419 and C3-1337. The category is changed to "F". Vodafone is added to the source company. WI is worng in the coverpage, should be corrected as "II-NNI2". So the revision is produced.

Decision: 		The document was Revised to C3-131575.

C3-131575	Removal of debug feature
					29.165	  CR-0608  rev 2 (Rel-11) v11.8.0
					Source: Ericsson, Vodafone

(Replaces C3-131533)

Decision: 		The document was Agreed.

### 10.19	Call Completion Not Logged in [CCNL]

### 10.20	IP Flow Mobility and WLAN offload (Stage 3) [IFOM-CT]

### 10.21	Enabling Coder Selection and Rate Adaption for UTRAN and E-UTRAN for Load Adaptive Applications, CN impacts [ECSRA_LAA-CN]

#### 10.21.1	-  Packet Core impacts

#### 10.21.2	-  IMS/CS impacts

### 10.22	S2b Mobility based on GTP [SMOG-St3]

### 10.23	CT aspects of Enhancements for Multimedia Priority Service [eMPS-CN]

### 10.24	PCRF failure and restoration [PCRF-FR]

### 10.25	CT aspects of Multi Access PDN Connectivity  [MAPCON-St3]

### 10.26	CT3 Aspects of Policy Enhancements for Sponsored Connectivity and Coherent Access to Policy related Data Bases [PEST-CT3]

### 10.27	Dynamic View of Headers in Messages for II-NNI [NNI_DV]

### 10.28	CS and IMS Interworking for CAT early session model [CIIC_ES]

### 10.29	Stage 3 for Network Improvements for Machine Type Communications [NIMTC]

### 10.30	Technical Enhancements and Improvements [TEI10]

### 10.31	Rel-10 contributions on other Work Items

## 11	Release 11

### 11.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 11.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-131409	Architecture update
					29.162	  CR-0121  (Rel-11) v11.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131534.

C3-131410	Architecture update
					29.162	  CR-0122  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131535.

C3-131534	Architecture update
					29.162	  CR-0121  rev 1 (Rel-11) v11.1.0
					Source: Ericsson

(Replaces C3-131409)

Decision: 		The document was Revised to C3-131576.

C3-131535	Architecture update
					29.162	  CR-0122  rev 1 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131410)

Decision: 		The document was Revised to C3-131577.

C3-131576	Architecture update
					29.162	  CR-0121  rev 2 (Rel-11) v11.1.0
					Source: Ericsson

(Replaces C3-131534)

Decision: 		The document was Agreed.

C3-131577	Architecture update
					29.162	  CR-0122  rev 2 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131535)

Decision: 		The document was Agreed.

### 11.3	Policy Control and Charging [PCC]

### 11.4	Interworking between EPC and external PDNs [SAES-St3-intwk]

### 11.5	PCC aspects of SAE [SAES-St3-PCC]

C3-131344	Corrections to CCA in Sd messages
					29.212	  CR-1061  (Rel-11) v11.10.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131544.

C3-131345	Corrections to CCA in Sd messages
					29.212	  CR-1062  (Rel-12) v12.2.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131545.

C3-131544	Corrections to CCA in Sd messages
					29.212	  CR-1061  rev 1 (Rel-11) v11.10.0
					Source: Huawei, China Telecom

(Replaces C3-131344)

Decision: 		The document was Agreed.

C3-131545	Corrections to CCA in Sd messages
					29.212	  CR-1062  rev 1 (Rel-12) v12.2.0
					Source: Huawei, China Telecom

(Replaces C3-131345)

Decision: 		The document was Agreed.

### 11.6	CT3 Aspects of MBMS Support in EPS [MBMS_EPS]

### 11.7	PCC Enhancements [PCC-Enh]

### 11.8	Optimal Media Routeing [OMR]

### 11.9	Dynamic View of Headers in Messages for II-NNI [NNI_DV]

### 11.10	Reserved

### 11.11	Reserved

### 11.12	Reserved

### 11.13	Reserved

### 11.14	Reserved

### 11.15	Reserved

### 11.16	CT3 aspects of Service Awareness and Privacy Policies [SAPP-CT3]

C3-131346	Correction to USAGE_REPORT value in Sd re-used AVPs
					29.212	  CR-1063  (Rel-11) v11.10.0
					Source: Huawei

Decision: 		The document was Agreed.

C3-131347	Correction to USAGE_REPORT value in Sd re-used AVPs
					29.212	  CR-1064  (Rel-12) v12.2.0
					Source: Huawei

Decision: 		The document was Revised to C3-131546.

C3-131546	Correction to USAGE_REPORT value in Sd re-used AVPs
					29.212	  CR-1064  rev 1 (Rel-12) v12.2.0
					Source: Huawei

(Replaces C3-131347)

Decision: 		The document was Agreed.

### 11.17	CT3 aspects of QoS Control Based on Subscriber Spending Limits  [QoS_SSL-CT3]

C3-131384	IE name mapping to Diameter AVP missing
					29.219	  CR-0017  (Rel-11) v11.5.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131547.

C3-131385	IE name mapping to Diameter AVP missing
					29.219	  CR-0018  (Rel-12) v12.0.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131548.

C3-131547	IE name mapping to Diameter AVP missing
					29.219	  CR-0017  rev 1 (Rel-11) v11.5.0
					Source: Ericsson

(Replaces C3-131384)

Decision: 		The document was Agreed.

C3-131548	IE name mapping to Diameter AVP missing
					29.219	  CR-0018  rev 1 (Rel-12) v12.0.0
					Source: Ericsson

(Replaces C3-131385)

Decision: 		The document was Agreed.

### 11.18	USSD Simulation Service in IMS-stage 3 [USSI]

### 11.19	Single Radio Video Call Continuity       [vSRVCC-CT]

#### 11.19.1	- IMS-related

#### 11.19.2	- PCC-related

### 11.20	Further improvement of usability of II-NNI specification for inter-connection [NNI_OI]

### 11.21	IMS Stage-3 IETF Protocol Alignment          [IMSProtoc5]

### 11.22	CT aspects of Single Radio Voice Call Continuity from UTRAN/GERAN to E-UTRAN/HSPA [rSRVCC-CT]

#### 11.22.1	- IMS/CS related

#### 11.22.2	- Packet Core related

### 11.23	Stage 3 for System Improvements to Machine-Type Communications [SIMTC-Reach]

### 11.24	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block I [BBAI_BBI-CT]

C3-131429	Clarification of the ePD/GP-GW IP address
					29.212	  CR-1071  (Rel-11) v11.10.0
					Source: ZTE

Decision: 		The document was Revised to C3-131549.

C3-131430	Clarification of the ePDG/P-GW IP address
					29.212	  CR-1072  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Revised to C3-131550.

C3-131549	Clarification of the ePD/GP-GW IP address
					29.212	  CR-1071  rev 1 (Rel-11) v11.10.0
					Source: ZTE

(Replaces C3-131429)

Decision: 		The document was Revised to C3-131600.

C3-131550	Clarification of the ePDG/P-GW IP address
					29.212	  CR-1072  rev 1 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131430)

Decision: 		The document was Revised to C3-131601.

C3-131600	Clarification of the ePD/GP-GW IP address
					29.212	  CR-1071  rev 2 (Rel-11) v11.10.0
					Source: ZTE

(Replaces C3-131549)

Decision: 		The document was Agreed.

C3-131601	Clarification of the ePDG/P-GW IP address
					29.212	  CR-1072  rev 2 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131550)

Decision: 		The document was Agreed.

### 11.25	Support for BroadBand Forum Accesses Interworking, Core Network Impacts, Building Block II [BBAI_BBII-CT]

### 11.26	CN aspects of Anonymous Call Rejection in the CS domain [ACR_CS-CN]

### 11.27	Advanced Interconnection of Services [IPXS]

### 11.28	Enhancements for Multimedia Priority Service (MPS)  Gateway Control Priority [eMPS_Gateway]

### 11.29	CN aspects of Mobility based On GTP & PMIPv6 for WLAN access to EPC [SaMOG_WLAN-CN]

### 11.30	CT aspect on Network Provided Location Information for IMS [NWK-PL2IMS-CT]

C3-131396	Correction of AVP name for location age
					29.212	  CR-1070  (Rel-12) v12.2.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131431	Correction to access network information for EPS
					29.212	  CR-1073  (Rel-11) v11.10.0
					Source: ZTE

Decision: 		The document was Agreed.

C3-131432	Correction to access network information for EPS
					29.212	  CR-1074  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Agreed.

C3-131433	Access Network Information Reporting Capability
					29.212	  CR-1075  (Rel-11) v11.10.0
					Source: ZTE

Decision: 		The document was Revised to C3-131630.

C3-131434	Access Network Information Reporting Capability
					29.212	  CR-1076  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Revised to C3-131631.

C3-131435	Access Network Information Reporting Capability
					29.214	  CR-0304  (Rel-11) v11.10.0
					Source: ZTE

Discussion:

It is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131436	Access Network Information Reporting Capability
					29.214	  CR-0305  (Rel-12) v12.1.0
					Source: ZTE

Discussion:

It is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131630	Access Network Information Reporting Correction
					29.212	  CR-1075  rev 1 (Rel-11) v11.10.0
					Source: ZTE

(Replaces C3-131433)

Discussion:

Title is changed.

Decision: 		The document was Agreed.

C3-131631	Access Network Information Reporting Correction
					29.212	  CR-1076  rev 1 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131434)

Discussion:

Title is changed.

Decision: 		The document was Agreed.

### 11.31	II-NNI enhancements: SIP timers applicability [NNI_timers]

### 11.32	Roaming Architecture for Voice over IMS with Local Breakout – CT aspects [RAVEL-CT]

C3-131416	tel URI support in the loopback scenario
					29.165	  CR-0605  (Rel-11) v11.8.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131578.

C3-131417	tel URI support in the loopback scenario
					29.165	  CR-0606  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131579.

C3-131578	tel URI support in the loopback scenario
					29.165	  CR-0605  rev 1 (Rel-11) v11.8.0
					Source: Ericsson

(Replaces C3-131416)

Decision: 		The document was Revised to C3-131613.

C3-131579	tel URI support in the loopback scenario
					29.165	  CR-0606  rev 1 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131417)

Decision: 		The document was Revised to C3-131614.

C3-131613	tel URI support in the loopback scenario
					29.165	  CR-0605  rev 2 (Rel-11) v11.8.0
					Source: Ericsson

(Replaces C3-131578)

Decision: 		The document was Agreed.

C3-131614	tel URI support in the loopback scenario
					29.165	  CR-0606  rev 2 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131579)

Decision: 		The document was Agreed.

### 11.33	Inclusion of Media Resource Broker [MRB]

### 11.34	Enhanced T.38 FAX support [MMTel_T.38_FAX]

### 11.35	Enhanced Nodes Restoration for EPC [eNR_EPC]

C3-131348	Correction to the applicability of Specific-Action AVP value in temporary network failure handling
					29.214	  CR-0297  (Rel-11) v11.10.0
					Source: Huawei

Decision: 		The document was Revised to C3-131505.

C3-131349	Correction to the applicability of Specific-Action AVP value in temporary network failure handling
					29.214	  CR-0298  (Rel-12) v12.1.0
					Source: Huawei

Decision: 		The document was Revised to C3-131506.

C3-131386	SGW Restoration impacts in S9 reference point
					29.215	  CR-0305  (Rel-11) v11.10.0
					Source: Ericsson, ZTE

Decision: 		The document was Revised to C3-131507.

C3-131387	SGW Restoration impacts in S9 reference point
					29.215	  CR-0306  (Rel-12) v12.1.0
					Source: Ericsson, ZTE

Decision: 		The document was Revised to C3-131508.

C3-131437	Temporary network failure handling when the PCCQoS rule is removed
					29.214	  CR-0306  (Rel-11) v11.10.0
					Source: ZTE

Decision: 		The document was Merged into C3-131505.

C3-131438	Temporary network failure handling when the PCCQoS rule is removed
					29.214	  CR-0307  (Rel-12) v12.1.0
					Source: ZTE

Decision: 		The document was Merged into C3-131506.

C3-131439	Discussion on error handling when the PCC rule is removed due to the S-GW restoration support
					Source: ZTE

Decision: 		The document was Noted.

C3-131440	Error handling when the PCC rule is removed due to the S-GW restoration support
					29.212	  CR-1077  (Rel-11) v11.10.0
					Source: ZTE

Decision: 		The document was Revised to C3-131509.

C3-131441	Error handling when the PCC rule is removed due to the S-GW restoration support
					29.212	  CR-1078  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Revised to C3-131510.

C3-131442	Error handling when the PCC rule is removed due to the S-GW restoration support
					Source: ZTE

Discussion:

Offline discussion is offered for the rewording.

Decision: 		The document was Revised to C3-131511.

C3-131470	SGW Restoration impacts in S9 reference point
					29.215	  CR-0307  (Rel-12) v12.1.0
					Source: China Mobile, Huawei

Decision: 		The document was Merged into C3-131508.

C3-131471	SGW Restoration impacts in S9 reference point
					29.215	  CR-0308  (Rel-11) v11.10.0
					Source: China Mobile, Huawei

Decision: 		The document was Merged into C3-131507.

C3-131505	Correction to the applicability of Specific-Action AVP value in temporary network failure handling
					29.214	  CR-0297  rev 1 (Rel-11) v11.10.0
					Source: Huawei, ZTE

(Replaces C3-131348)

Discussion:

This CR is merger of C3-131348 and C3-131437.

Decision: 		The document was Agreed.

C3-131506	Correction to the applicability of Specific-Action AVP value in temporary network failure handling
					29.214	  CR-0298  rev 1 (Rel-12) v12.1.0
					Source: Huawei, ZTE

(Replaces C3-131349)

Discussion:

This CR is merger of C3-131349 and C3-131438.

Decision: 		The document was Agreed.

C3-131507	SGW Restoration impacts in S9 reference point
					29.215	  CR-0305  rev 1 (Rel-11) v11.10.0
					Source: Ericsson, ZTE, China Mobile, Huawei

(Replaces C3-131386)

Discussion:

This CR is the merger of C3-131386 and C3-131471.

Decision: 		The document was Agreed.

C3-131508	SGW Restoration impacts in S9 reference point
					29.215	  CR-0306  rev 1 (Rel-12) v12.1.0
					Source: Ericsson, ZTE, China Mobile, Huawei

(Replaces C3-131387)

Discussion:

This CR is merger of C3-131387 and C3-131470.

Decision: 		The document was Agreed.

C3-131509	Error handling when the PCC rule is removed due to the S-GW restoration support
					29.212	  CR-1077  rev 1 (Rel-11) v11.10.0
					Source: ZTE

(Replaces C3-131440)

Decision: 		The document was Revised to C3-131606.

C3-131510	Error handling when the PCC rule is removed due to the S-GW restoration support
					29.212	  CR-1078  rev 1 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131441)

Decision: 		The document was Revised to C3-131607.

C3-131511	Error handling when the PCC rule is removed due to the S-GW restoration support
					Source: ZTE

(Replaces C3-131442)

Decision: 		The document was Revised to C3-131608.

C3-131606	Error handling when the PCC rule is removed due to the S-GW restoration support
					29.212	  CR-1077  rev 2 (Rel-11) v11.10.0
					Source: ZTE

(Replaces C3-131509)

Decision: 		The document was Agreed.

C3-131607	Error handling when the PCC rule is removed due to the S-GW restoration support
					29.212	  CR-1078  rev 2 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131510)

Decision: 		The document was Agreed.

C3-131608	Error handling when the PCC rule is removed due to the S-GW restoration support
					Source: ZTE

(Replaces C3-131511)

Decision: 		The document was Approved.

### 11.36	IMS overload control [IOC]

C3-131380	Reference update: draft-ietf-soc-overload-control, draft-ietf-soc-overload-rate-control and draft-ietf-soc-load-control-event-package
					29.165	  CR-0601  (Rel-11) v11.8.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131536.

C3-131381	Reference update: draft-ietf-soc-overload-control, draft-ietf-soc-overload-rate-control and draft-ietf-soc-load-control-event-package
					29.165	  CR-0602  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131537.

C3-131536	Reference update: draft-ietf-soc-overload-control, draft-ietf-soc-overload-rate-control and draft-ietf-soc-load-control-event-package
					29.165	  CR-0601  rev 1 (Rel-11) v11.8.0
					Source: Ericsson

(Replaces C3-131380)

Decision: 		The document was Revised to C3-131581.

C3-131537	Reference update: draft-ietf-soc-overload-control, draft-ietf-soc-overload-rate-control and draft-ietf-soc-load-control-event-package
					29.165	  CR-0602  rev 1 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131381)

Decision: 		The document was Revised to C3-131582.

C3-131581	Reference update: draft-ietf-soc-overload-control, draft-ietf-soc-overload-rate-control and draft-ietf-soc-load-control-event-package
					29.165	  CR-0601  rev 2 (Rel-11) v11.8.0
					Source: Ericsson

(Replaces C3-131536)

Decision: 		The document was Agreed.

C3-131582	Reference update: draft-ietf-soc-overload-control, draft-ietf-soc-overload-rate-control and draft-ietf-soc-load-control-event-package
					29.165	  CR-0602  rev 2 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131537)

Decision: 		The document was Agreed.

### 11.37	Technical Enhancements and Improvements [TEI11]

### 11.38	Rel-11 contributions on other Work Items

C3-131337	IMS debug removal of feature
					29.165	  CR-0592  (Rel-11) v11.8.0
					Source: Vodafone

Decision: 		The document was Merged into C3-131533.

### 11.39	Further Improvements of II-NNI specification based on Operational Feedback and Evolution of Other Specifications [II-NNI2]

## 12	Release 12

### 12.1	Interworking between IM subsystem and IP [IMS-CCR-IWIP]

### 12.2	Interworking between IM Subsystem with CS  [IMS-CCR-IWCS]

C3-131469	Support for both-way early media for UID
					29.163	  CR-0791  (Rel-12) v12.1.0
					Source: ALU

Decision: 		The document was Revised to C3-131573.

C3-131573	Support for both-way early media for UID
					29.163	  CR-0791  rev 1 (Rel-12) v12.1.0
					Source: ALU

(Replaces C3-131469)

Discussion:

WI is changed to "TEI12" and category is "B". It is postponed till the next meeting.

Decision: 		The document was Postponed.

### 12.3	Policy Control and Charging [PCC]

### 12.4	PCC aspects of SAE [SAES-St3-PCC]

C3-131443	Clarification of PVI and PCI handling for interoperation with GnGp SGSN
					29.212	  CR-1079  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Revised to C3-131584.

C3-131584	Clarification of PVI and PCI handling for interoperation with GnGp SGSN
					29.212	  CR-1079  rev 1 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131443)

Decision: 		The document was Revised to C3-131620.

C3-131620	Clarification of PVI and PCI handling for interoperation with GnGp SGSN
					29.212	  CR-1079  rev 2 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131584)

Decision: 		The document was Agreed.

### 12.5	Reserved

### 12.6	Reserved

### 12.7	Reserved

### 12.8	Reserved

### 12.9	Reserved

### 12.10	Reserved

### 12.11	Interworking between a PLMN with WLAN to access the EPC and a PDN [SAES_WLAN_EPC_intwk]

### 12.12	CT aspects of Extended IMS media plane security features [eMEDIASEC-CT]

C3-131458	CT aspects of Extended IMS media plane security features
					Source: Alcatel-Lucent

Decision: 		The document was Endorsed.

### 12.13	IMS-based Telepresence (Stage 3) [IMS_TELEP]

### 12.14	IMS Stage-3 IETF Protocol Alignment  [IMSProtoc6]

### 12.15	IMS Emergency PSAP Callback [EMC_PC]

### 12.16	Diameter Overload Control [FS_DOCME]

### 12.17	Study on  Indication of NNI Routeing scenarios in SIP requests [FS_NNI_RS]

C3-131397	Clarifying figure with reference points within the scope of this study in subclause 4.1
					Source: Ericsson

Decision: 		The document was Revised to C3-131519.

C3-131398	Removal of EN in clause 7
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131399	Requirements reference for encoding options
					Source: Ericsson

Decision: 		The document was Revised to C3-131520.

C3-131400	URI parameter solution
					Source: Ericsson

Decision: 		The document was Revised to C3-131513.

C3-131401	Compliance with the requirements in annex B
					Source: Ericsson

Decision: 		The document was Revised to C3-131517.

C3-131404	Feature-Caps solution
					Source: Ericsson

Decision: 		The document was Revised to C3-131514.

C3-131405	New header solution
					Source: Ericsson

Decision: 		The document was Revised to C3-131515.

C3-131406	II-NNI type used on other interfaces
					Source: Ericsson

Decision: 		The document was Revised to C3-131521.

C3-131407	P-Charging-Vector solution
					Source: Ericsson

Decision: 		The document was Revised to C3-131516.

C3-131408	Removal of the EN regarding reg-event
					Source: Ericsson

Decision: 		The document was Revised to C3-131522.

C3-131421	Clarifying the figure "Originating side II-NNI traversal scenarios" in 4.2.1
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131422	DISC draft-holmberg-dispatch-nni-reqs-00
					Source: Ericsson

Decision: 		The document was Noted.

C3-131423	Clarification of use cases in Annex B
					Source: OKI, NTT

Decision: 		The document was Agreed.

C3-131477	Summary of identified issues
					Source: NSN

Decision: 		The document was Agreed.

C3-131478	Interconnection requirements
					Source: NSN

Decision: 		The document was Agreed.

C3-131479	Implicit detection of II-NNI traversal scenario type
					Source: NSN

Decision: 		The document was Revised to C3-131518.

C3-131480	Requirement for an explicit indication of the II-NNI traversal scenario type
					Source: NSN

Decision: 		The document was Revised to C3-131523.

C3-131513	URI parameter solution
					Source: Ericsson

(Replaces C3-131400)

Decision: 		The document was Agreed.

C3-131514	Feature-Caps solution
					Source: Ericsson

(Replaces C3-131404)

Decision: 		The document was Revised to C3-131609.

C3-131515	New header solution
					Source: Ericsson

(Replaces C3-131405)

Decision: 		The document was Revised to C3-131610.

C3-131516	P-Charging-Vector solution
					Source: Ericsson

(Replaces C3-131407)

Decision: 		The document was Revised to C3-131611.

C3-131517	Compliance with the requirements in annex B
					Source: Ericsson

(Replaces C3-131401)

Decision: 		The document was Agreed.

C3-131518	Implicit detection of II-NNI traversal scenario type
					Source: NSN

(Replaces C3-131479)

Decision: 		The document was Agreed.

C3-131519	Clarifying figure with reference points within the scope of this study in subclause 4.1
					Source: Ericsson

(Replaces C3-131397)

Decision: 		The document was Agreed.

C3-131520	Requirements reference for encoding options
					Source: Ericsson

(Replaces C3-131399)

Decision: 		The document was Agreed.

C3-131521	II-NNI type used on other interfaces
					Source: Ericsson

(Replaces C3-131406)

Discussion:

It is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131522	Removal of the EN regarding reg-event
					Source: Ericsson

(Replaces C3-131408)

Decision: 		The document was Agreed.

C3-131523	Requirement for an explicit indication of the II-NNI traversal scenario type
					Source: NSN

(Replaces C3-131480)

Decision: 		The document was Agreed.

C3-131609	Feature-Caps solution
					Source: Ericsson

(Replaces C3-131514)

Decision: 		The document was Agreed.

C3-131610	New header solution
					Source: Ericsson

(Replaces C3-131515)

Decision: 		The document was Agreed.

C3-131611	P-Charging-Vector solution
					Source: Ericsson

(Replaces C3-131516)

Decision: 		The document was Agreed.

C3-131612	TR 24.802 v 0.4.0
					Source: Ericsson

Discussion:

Mr. Jan Holm (from Ericsson) will provide it till the 18th October 2013.

Decision: 		The document was n/a.

### 12.18	Study on XML based access of AF to the PCRF [FS_XML_AF_PCRF]

C3-131352	Comparison among candidate session management solutions
					Source: Huawei, Verizon, Alcatel-Lucent

Decision: 		The document was Revised to C3-131512.

C3-131353	Discussion on PCRF addressing in PCRF web server architecture
					Source: Huawei, Verizon, Alcatel-Lucent

Decision: 		The document was Noted.

C3-131354	PCRF addressing in PCRF web server architecture
					Source: Huawei, Verizon, Alcatel-Lucent

Decision: 		The document was Revised to C3-131559.

C3-131355	IP-CAN session procedures for PCRF web server
					Source: Huawei

Decision: 		The document was Revised to C3-131560.

C3-131356	Traffic plane events notification procedures for PCRF web server 
					Source: Huawei

Decision: 		The document was Revised to C3-131561.

C3-131357	Charging consideration for XML based Rx
					Source: Huawei, Verizon

Decision: 		The document was Revised to C3-131562.

C3-131358	Some corrections of roaming architecture of Protocol Converter
					Source: Huawei, Verizon, Alcatel-Lucent

Decision: 		The document was Revised to C3-131563.

C3-131444	Evaluation and conclusion of session management for XML based Rx interface
					Source: ZTE

Decision: 		The document was Merged into C3-131512.

C3-131457	Introduction of explicit references in the annex
					Source: Alcatel-Lucent, Intel Corporation, Verizon

Decision: 		The document was Agreed.

C3-131465	DISC: Analysis of addressing of PCRF by AF under Option A
					Source: Intel

Decision: 		The document was Noted.

C3-131466	PCR: Addressing Protocol Converters in a PLMN from Application Function
					Source: Intel

Decision: 		The document was Revised to C3-131583.

C3-131467	DISC: Pooling of Protocol Converters and load balancing
					Source: Intel

Discussion:

CT3 Chairman suggested two options after long discussion regarding C3-131465 and C3-131467.

Option 1 : putting every potential solutions in the TR and mention that stage 2 is not confirmed in the conclusion section.

Option 2 : considering these possible solutions as information with offline discussion before CT3#75 in San Francisco.

The related PCR, C3-131468 is withdrawn to collect more informtions for the next meeting.

Orange will follow this subject before the upcoming Sand Francisco meeting.

Decision: 		The document was Noted.

C3-131468	PCR: Load control mechanism for pool of PCs in a PLMN
					Source: Intel

Decision: 		The document was Withdrawn.

C3-131512	Comparison among candidate session management solutions
					Source: Huawei, Verizon, Alcatel-Lucent, ZTE

(Replaces C3-131352)

Discussion:

This PCR is the merger of C3-131352 and C3-131444.

Decision: 		The document was Revised to C3-131628.

C3-131559	PCRF addressing in PCRF web server architecture
					Source: Huawei, Verizon, Alcatel-Lucent

(Replaces C3-131354)

Decision: 		The document was Revised to C3-131623.

C3-131560	IP-CAN session procedures for PCRF web server
					Source: Huawei, Verizon

(Replaces C3-131355)

Decision: 		The document was Revised to C3-131603.

C3-131561	Traffic plane events notification procedures for PCRF web server 
					Source: Huawei, Verizon

(Replaces C3-131356)

Decision: 		The document was Agreed.

C3-131562	Charging consideration for XML based Rx
					Source: Huawei, Verizon

(Replaces C3-131357)

Decision: 		The document was Agreed.

C3-131563	Some corrections of roaming architecture of Protocol Converter
					Source: Huawei, Verizon, Alcatel-Lucent

(Replaces C3-131358)

Decision: 		The document was Agreed.

C3-131583	PCR: Addressing Protocol Converters in a PLMN from Application Function
					Source: Intel

(Replaces C3-131466)

Discussion:

It is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131603	IP-CAN session procedures for PCRF web server
					Source: Huawei, Verizon

(Replaces C3-131560)

Decision: 		The document was Agreed.

C3-131623	PCRF addressing in PCRF web server architecture
					Source: Huawei, Verizon, Alcatel-Lucent

(Replaces C3-131559)

Decision: 		The document was Agreed.

C3-131628	Comparison among candidate session management solutions
					Source: Huawei, Verizon, Alcatel-Lucent, ZTE

(Replaces C3-131512)

Discussion:

It is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131641	TR 29.817 v 0.3.0
					Source: Horst Brinkmann

Discussion:

Mr. Horst Brinkmann (from Alcatel-Lucent) will provide it until 18th October 2013.

Decision: 		The document was n/a.

### 12.24	CT3 Aspect of Usage Monitoring Control PCC Enhancement [UMONC-CT3]

### 12.25	CT Aspects of Signalling of Image Size [SIS-CT]

C3-131456	Handling procedures of generic image attributes
					29.162	  CR-0128  (Rel-12) v12.1.0
					Source: Huawei

Decision: 		The document was Revised to C3-131529.

C3-131529	Handling procedures of generic image attributes
					29.162	  CR-0128  rev 1 (Rel-12) v12.1.0
					Source: Huawei

(Replaces C3-131456)

Decision: 		The document was Agreed.

### 12.26	CT Aspects of End-to-End MTSI Extensions [E2EMTSI-CT]

### 12.27	Policy and Charging Control for supporting traffic from fixed terminals and NSWO traffic from 3GPP UEs in fixed broadband access networks [P4C-F-CT3]

C3-131359	Revised WID proposal for Policy and Charging Control for supporting Fixed Broadband Access network convergence
					Source: Huawei, China Telecom

Discussion:

Alcatel-Lucent wondered whether there is the impact on CT4, and no impact on CT4 from this WID is the anwer backed to Alcatel-Lucent.

Decision: 		The document was Agreed.

C3-131360	Adding the reference architecture to support fixed broadband access network convergence
					29.212	  CR-1067  (Rel-12) v12.2.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131568.

C3-131361	Input for general part in PCC procedures
					29.212	  CR-1068  (Rel-12) v12.2.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131569.

C3-131362	Adding IP-CAN session establishment to support fixed broadband access network convergence
					29.212	  CR-1069  (Rel-12) v12.2.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131570.

C3-131363	Adding the binding mechanism for NSWO traffic
					29.213	  CR-0503  (Rel-12) v12.1.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131571.

C3-131364	Adding the binding mechanism for traffic from fixed devices
					29.213	  CR-0504  (Rel-12) v12.1.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131572.

C3-131365	Input for introduction part in PCC procedures
					29.213	  CR-0505  (Rel-12) v12.1.0
					Source: Huawei, China Telecom

Decision: 		The document was Agreed.

C3-131366	Adding IP-CAN session establishment to support fixed broadband access network convergence
					29.213	  CR-0506  (Rel-12) v12.1.0
					Source: Huawei, China Telecom

Decision: 		The document was Revised to C3-131585.

C3-131367	Adding the scope of Fixed Broadband Access network convergence
					29.215	  CR-0303  (Rel-12) v12.1.0
					Source: Huawei, China Telecom

Decision: 		The document was Agreed.

C3-131368	Adding New Annex to support Fixed Broadband Access network convergence
					29.215	  CR-0304  (Rel-12) v12.1.0
					Source: Huawei, China Telecom

Discussion:

It is the skeleton of Annex.

Decision: 		The document was Agreed.

C3-131388	Definitions and abbreviations in Fixed Broadband Access network convergence
					29.213	  CR-0507  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131586.

C3-131389	IP-CAN session Termination for Fixed Broadband Access network convergence
					29.213	  CR-0508  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Agreed.

C3-131390	IP-CAN session Modification to support Fixed Broadband Access network convergence
					29.213	  CR-0509  (Rel-12) v12.1.0
					Source: Ericsson

Decision: 		The document was Revised to C3-131588.

C3-131446	Definition and abbreviationto support Fixed Broadband Access network convergence
					29.212	  CR-1081  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Revised to C3-131587.

C3-131447	Functional elements to support Fixed Broadband Access network convergence
					29.212	  CR-1082  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Revised to C3-131589.

C3-131448	IP-CAN session Modification to support Fixed Broadband Access network convergence
					29.212	  CR-1083  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Revised to C3-131590.

C3-131449	IP-CAN session termination to support Fixed Broadband Access network convergence
					29.212	  CR-1084  (Rel-12) v12.2.0
					Source: ZTE

Decision: 		The document was Revised to C3-131591.

C3-131568	Adding the reference architecture to support fixed broadband access network convergence
					29.212	  CR-1067  rev 1 (Rel-12) v12.2.0
					Source: Huawei, China Telecom

(Replaces C3-131360)

Decision: 		The document was Agreed.

C3-131569	Input for general part in PCC procedures
					29.212	  CR-1068  rev 1 (Rel-12) v12.2.0
					Source: Huawei, China Telecom

(Replaces C3-131361)

Decision: 		The document was Agreed.

C3-131570	Adding IP-CAN session establishment to support fixed broadband access network convergence
					29.212	  CR-1069  rev 1 (Rel-12) v12.2.0
					Source: Huawei, China Telecom

(Replaces C3-131362)

Decision: 		The document was Agreed.

C3-131571	Adding the binding mechanism for NSWO traffic
					29.213	  CR-0503  rev 1 (Rel-12) v12.1.0
					Source: Huawei, China Telecom

(Replaces C3-131363)

Decision: 		The document was Agreed.

C3-131572	Adding the binding mechanism for traffic from fixed devices
					29.213	  CR-0504  rev 1 (Rel-12) v12.1.0
					Source: Huawei, China Telecom

(Replaces C3-131364)

Decision: 		The document was Revised to C3-131625.

C3-131585	Adding IP-CAN session establishment to support fixed broadband access network convergence
					29.213	  CR-0506  rev 1 (Rel-12) v12.1.0
					Source: Huawei, China Telecom

(Replaces C3-131366)

Decision: 		The document was Revised to C3-131626.

C3-131586	Definitions and abbreviations in Fixed Broadband Access network convergence
					29.213	  CR-0507  rev 1 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131388)

Decision: 		The document was Revised to C3-131592.

C3-131587	Definition and abbreviationto support Fixed Broadband Access network convergence
					29.212	  CR-1081  rev 1 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131446)

Decision: 		The document was Agreed.

C3-131588	IP-CAN session Modification to support Fixed Broadband Access network convergence
					29.213	  CR-0509  rev 1 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131390)

Decision: 		The document was Revised to C3-131593.

C3-131589	Functional elements to support Fixed Broadband Access network convergence
					29.212	  CR-1082  rev 1 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131447)

Decision: 		The document was Revised to C3-131639.

C3-131590	IP-CAN session Modification to support Fixed Broadband Access network convergence
					29.212	  CR-1083  rev 1 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131448)

Decision: 		The document was Agreed.

C3-131591	IP-CAN session termination to support Fixed Broadband Access network convergence
					29.212	  CR-1084  rev 1 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131449)

Discussion:

It is postponed till the next meeting.

Decision: 		The document was Postponed.

C3-131592	Definitions and abbreviations in Fixed Broadband Access network convergence
					29.213	  CR-0507  rev 2 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131586)

Decision: 		The document was Revised to C3-131619.

C3-131593	IP-CAN session Modification to support Fixed Broadband Access network convergence
					29.213	  CR-0509  rev 2 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131588)

Decision: 		The document was Agreed.

C3-131619	Definitions and abbreviations in Fixed Broadband Access network convergence
					29.213	  CR-0507  rev 3 (Rel-12) v12.1.0
					Source: Ericsson

(Replaces C3-131592)

Decision: 		The document was Agreed.

C3-131625	Adding the binding mechanism for traffic from fixed devices
					29.213	  CR-0504  rev 2 (Rel-12) v12.1.0
					Source: Huawei, China Telecom

(Replaces C3-131572)

Decision: 		The document was Revised to C3-131637.

C3-131626	Adding IP-CAN session establishment to support fixed broadband access network convergence
					29.213	  CR-0506  rev 2 (Rel-12) v12.1.0
					Source: Huawei, China Telecom

(Replaces C3-131585)

Decision: 		The document was Agreed.

C3-131637	Adding the binding mechanism for traffic from fixed devices
					29.213	  CR-0504  rev 3 (Rel-12) v12.1.0
					Source: Huawei, China Telecom

(Replaces C3-131625)

Decision: 		The document was Agreed.

C3-131639	Functional elements to support Fixed Broadband Access network convergence
					29.212	  CR-1082  rev 2 (Rel-12) v12.2.0
					Source: ZTE

(Replaces C3-131589)

Decision: 		The document was Agreed.

### 12.28	Study on Technical aspects on Roaming End-to-end scenarios with VoLTE IMS and other networks [FS_REVOLTE_IMS]

C3-131450	Draft Skelton TR 29.949
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Agreed.

C3-131451	Scope proposal for TS29.949
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-131524.

C3-131452	Abbreviations Section proposal for TR 29.949
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Agreed.

C3-131453	Section References proposal for TR 29.949
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-131525.

C3-131454	Proposal section description of scenarios for TR29.949
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-131526.

C3-131455	New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks
					Source: Deutsche Telekom (Roland)

Decision: 		The document was Revised to C3-131527.

C3-131524	Scope proposal for TS29.949
					Source: Deutsche Telekom (Roland)

(Replaces C3-131451)

Decision: 		The document was Revised to C3-131615.

C3-131525	Section References proposal for TR 29.949
					Source: Deutsche Telekom (Roland)

(Replaces C3-131453)

Decision: 		The document was Agreed.

C3-131526	Proposal section description of scenarios for TR29.949
					Source: Deutsche Telekom (Roland)

(Replaces C3-131454)

Decision: 		The document was Revised to C3-131616.

C3-131527	New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks
					Source: Deutsche Telekom (Roland)

(Replaces C3-131455)

Decision: 		The document was Revised to C3-131617.

C3-131615	Scope proposal for TS29.949
					Source: Deutsche Telekom (Roland)

(Replaces C3-131524)

Decision: 		The document was Agreed.

C3-131616	Proposal section description of scenarios for TR29.949
					Source: Deutsche Telekom (Roland)

(Replaces C3-131526)

Decision: 		The document was Agreed.

C3-131617	New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks
					Source: Deutsche Telekom (Roland)

(Replaces C3-131527)

Decision: 		The document was Revised to C3-131629.

C3-131629	New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks
					Source: Deutsche Telekom (Roland)

(Replaces C3-131617)

Decision: 		The document was Revised to C3-131632.

C3-131632	New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks
					Source: Deutsche Telekom (Roland)

(Replaces C3-131629)

Decision: 		The document was Revised to C3-131633.

C3-131633	New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks
					Source: Deutsche Telekom (Roland)

(Replaces C3-131632)

Decision: 		The document was Revised to C3-131635.

C3-131634	TR 29.2949 v 0.1.0
					Source: Roland Jesske

Discussion:

Mr. Roland Jesske (from Deutsche Telekom) will provide it till 18th October 2013.

Decision: 		The document was n/a.

C3-131635	New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks
					Source: Deutsche Telekom (Roland)

(Replaces C3-131633)

Decision: 		The document was Revised to C3-131640.

C3-131640	New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks
					Source: Deutsche Telekom (Roland)

(Replaces C3-131635)

Decision: 		The document was Agreed.

### 12.29	CT Aspects of IMS Business Trunking for IP-PBX in Static Mode of operation [BusTI-CT]

### 12.30	Updating IMS to conform to RFC 6665 [UP6665]

C3-131420	RFC 3265 to RFC 6665
					29.165	  CR-0609  (Rel-12) v12.1.0
					Source: Ericsson, Telecom Italia

Decision: 		The document was Revised to C3-131530.

C3-131558	RFC 3265 to RFC 6665
					29.165	  CR-0609  rev 1 (Rel-12) v12.1.0
					Source: Ericsson, Telecom Italia

(Replaces C3-131420)

Decision: 		The document was Revised to C3-131580.

C3-131580	RFC 3265 to RFC 6665
					29.165	  CR-0609  rev 2 (Rel-12) v12.1.0
					Source: Ericsson, Telecom Italia

(Replaces C3-131558)

Decision: 		The document was Agreed.

### 12.31	eMBMS restoration procedures [eMBMS_Rest]

C3-131373	DISC  MBMS restoration upon SGmb failures in presence of a Diameter Agent between the BM-SC and MBMS GW
					Source: Alcatel-Lucent, Verizon

Discussion:

It is discussed during joint session with CT4.

Decision: 		The document was Noted.

### 12.32	CT3 part of Support of RTP / RTCP multiplexing (signalling) in IMS [RTCP_MUX]

C3-131374	Discussion of "Possible impact of RTP transport multiplexing on PCC"
					Source: Alcatel-Lucent

Discussion:

Dr. Thomans Belling (from Nokia Solutions Networks) suggest that CT3 need to wait SA2's decision regarding stage 2 and minimal apporch for this subject.

Decision: 		The document was Noted.

C3-131375	Revised WID on "Support of RTP / RTCP transport multiplexing (signalling) in IMS"
					Source: Alcatel-Lucent

Discussion:

Out going LS to SA2 is produced. (C3-131502)

Decision: 		The document was Withdrawn.

C3-131503	LS out Relpy LS on new work item on "IMS support for RTP / RTCP transport multiplexing
					Source: NSN

Decision: 		The document was Revised to C3-131602.

C3-131602	LS out Relpy LS on new work item on "IMS support for RTP / RTCP transport multiplexing
					Source: NSN

(Replaces C3-131503)

Decision: 		The document was Revised to C3-131621.

C3-131621	LS out Relpy LS on new work item on "IMS support for RTP / RTCP transport multiplexing
					Source: NSN

(Replaces C3-131602)

Decision: 		The document was Revised to C3-131627.

C3-131627	LS out Relpy LS on new work item on "IMS support for RTP / RTCP transport multiplexing
					Source: NSN

(Replaces C3-131621)

Decision: 		The document was Approved.

### 12.33	Technical Enhancements and Improvements [TEI12]

### 12.34	Rel-12 contributions on other Work Items

C3-131383	new WID Enhancements to IMS Operator Determined Barring
					Source: Ericsson

Discussion:

Supporting individual memebers will be added and time scale need to be modified.

Decision: 		The document was Revised to C3-131504.

C3-131504	new WID Enhancements to IMS Operator Determined Barring
					Source: Ericsson

(Replaces C3-131383)

Decision: 		The document was Endorsed.

#### 12.34.1	UE Power Consumption Optimizations, stage 3 [MTCe-UEPCOP-CT]

C3-131481	WID for UE Power Consumption Optimizations, stage 3
					Source: Ericsson

Discussion:

Nokia Solutions Networks, Alcatel-Lucent suggest to remove CT3 impact in WID sheet. Ericsson need time for offline discussion for this subject. Finally, it is withdrawn.

Decision: 		The document was Withdrawn.

#### 12.34.2	Enhancements to IMS Operator Determined Barring [eIODB]

## 13	Joint sessions

## 14	Work Organisation

### 14.1	Work Plan Review

C3-131335	Status of CT3 Work Items
					Source: CT3 Chairman

Decision: 		The document was Revised to C3-131642.

C3-131483	Latest Version of 3GPP Workplan
					Source: MCC

Decision: 		The document was Noted.

C3-131642	Status of CT3 Work Items
					Source: CT3 Chairman

(Replaces C3-131335)

Decision: 		The document was Noted.

### 14.2	Specification Review

C3-131484	Status of CT3 Specifications following CT#61 meeting
					Source: MCC

Discussion:

The rappourteurs are need to be updated.

Decision: 		The document was Noted.

### 14.3	Next meetings, allocation of hosts

### 14.4	Calendar

C3-131485	Meeting Calendar for 2013-2014
					Source: MCC

Decision: 		The document was Revised to C3-131618.

C3-131618	Meeting Calendar for 2013-2014
					Source: MCC

(Replaces C3-131485)

Discussion:

October 2014 meeting in Sophia Antipolis is not needed for CT3.

Decision: 		The document was Noted.

### 14.5	Other issues

Dr.Thomas Belling (from NSN) proposed two questions for efficient working procedure in CT3.

1. whether the agreeded CRs in breakout session have to be discussed again in CT3 main-room.

2. whether we can have a fix meeting schedule.

## 15	Summary of results

## 16	Any other business

C3-131551	Void
					Source: nn

Discussion:

It is unused tdoc number during PCC breakout session.

Decision: 		The document was Noted.

C3-131552	Void
					Source: nn

Discussion:

It is unused tdoc number during PCC breakout session.

Decision: 		The document was Noted.

C3-131553	Void
					Source: nn

Discussion:

It is unused tdoc number during PCC breakout session.

Decision: 		The document was Noted.

C3-131554	Void
					Source: nn

Discussion:

It is unused tdoc number during PCC breakout session.

Decision: 		The document was Noted.

C3-131555	Void
					Source: nn

Discussion:

It is unused tdoc number during PCC breakout session.

Decision: 		The document was Noted.

C3-131556	Void
					Source: nn

Discussion:

It is unused tdoc number during PCC breakout session.

Decision: 		The document was Noted.

C3-131557	Void
					Source: nn

Discussion:

It is unused tdoc number during PCC breakout session.

Decision: 		The document was Noted.

## 17	Closing of the meeting

## Annex A. TS/TR

| Tdoc | Agenda | Type | Title | Source |
| --- | --- | --- | --- | --- |
| C3-131612 | 12.17 | 3GPP TR | TR 24.802 v 0.4.0 | Ericsson |
| C3-131634 | 12.28 | 3GPP TR | TR 29.2949 v 0.1.0 | Deutsche Telekom |
| C3-131641 | 12.18 | 3GPP TR | TR 29.817 v 0.3.0 | Alcatel-Lucent |

## Annex B. Work Item

| Tdoc | Agenda | Type | Title | Source | Decision |
| --- | --- | --- | --- | --- | --- |
| C3-131359 | 12.27 | WID | Revised WID proposal for Policy and Charging Control for supporting Fixed Broadband Access network convergence | Huawei, China Telecom | Agreed |
| C3-131640 | 12.28 | WID | New Acronym for WID Technical Aspects on Roaming End to End scenarios with VoLTE IMS and other networks | Deutsche Telekom (Roland) | Agreed |
| C3-131458 | 12.12 | WID | CT aspects of Extended IMS media plane security features | Alcatel-Lucent | Endorsed |
| C3-131504 | 12.34 | WID | new WID Enhancements to IMS Operator Determined Barring | Ericsson | Endorsed |

## Annex C. Liaison Statements

## Annex C.1 Incoming Liaison Statements

| Tdoc | Title | Source | Source File | Decision |
| --- | --- | --- | --- | --- |
| C3-131486 | LS on updating 3GPP IMS to support RFC 6665 | TSG CT WG1 | C1-133496 | Noted |
| C3-131487 | Reply LS on uplink packet filters | TSG CT WG1 | C1-133546 | Noted |
| C3-131488 | LS on eMBMS service restoration | TSG CT WG4 | C4-131415 | Noted |
| C3-131489 | LS OUT on Rollback Behaviour in EPC during TAU/RAU rejection | TSG CT WG4 | C4-131514 | Noted |
| C3-131490 | Reply LS on End-to-end QoS handling of MTSI | TSG CT WG4 | C4-131520 | Noted |
| C3-131491 | LS on Parameter Format of AgeOfLocationInformation | TSG CT WG4 | C4-131544 | Noted |
| C3-131492 | LS on new work item on "IMS support for RTP / RTCP transport multiplexing" | TSG CT WG4 | C4-131546 | Noted |
| C3-131493 | Reply LS on Indication of NNI Routeing scenarios in SIP requests | GSMA | RILTE_Doc_33_004.doc | Postponed |
| C3-131494 | LS on SMSC Usage Restriction | TSG SA WG1 | S1-134179 | Noted |
| C3-131495 | Reply to CT3 on Indication of NNI Routing scenarios in SIP requests | GSMA | SOLU Doc 62_004.doc | Postponed |
| C3-131496 | LS on Normative work on overload handling for device triggering | TSG SA WG2 | S2-133806 | Noted |
| C3-131497 | Reply LS to CT WG4 LS on new work item on "IMS support for RTP / RTCP transport multiplexing" | TSG SA WG2 | S2-133825 | Noted |
| C3-131498 | Reply to LS from CT WG1 on uplink packet filters | TSG SA WG2 | S2-133840 | Noted |
| C3-131499 | LS on End-to-end fixed-mobile interworking | TSG SA WG4 | S4-131100 | Noted |
| C3-131500 | Reply LS on End-to-end QoS handling of MTSI | TSG SA WG4 | S4-131105 | Noted |
| C3-131502 | LS on ULI reporting enhancements | TSG SA WG2 | S2-133865 | Noted |
| C3-131622 | Reply LS on Reply LS on support for user location age or timestamp | TSG CT WG4 | C4-131815 | Postponed |

## Annex C.2 Outgoing Liaison Statements

| Tdoc | Title | LS To | LS Cc | Attachment |
| --- | --- | --- | --- | --- |
| C3-131594 | Reply LS on End-to-end QoS handling of MTSI | SA4 | CT1, CT4, SA2, CT, SA |  |
| C3-131608 | Error handling when the PCC rule is removed due to the S-GW restoration support | CT4 |  |  |
| C3-131627 | LS out Relpy LS on new work item on "IMS support for RTP / RTCP transport multiplexing | SA2 | SA5, CT4, CT |  |

## Annex D. Agreed Change Requests

| Tdoc | Agenda | Type | Title | Source | Spec | CR_number | CR_revision | Category | Version_old | Work_item | Release | 'Decision' |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C3-131343 | 8.14.3 | CR | Corrections for PCC/QoS rule establishment failure | Huawei, China Telecom | 29.214 | 0296 | 0 | F | 8.17.0 | SAES-St3-PCC | Rel-8 | Agreed |
| C3-131346 | 11.16 | CR | Correction to USAGE_REPORT value in Sd re-used AVPs | Huawei | 29.212 | 1063 | 0 | F | 11.10.0 | SAPP-CT3 | Rel-11 | Agreed |
| C3-131365 | 12.27 | CR | Input for introduction part in PCC procedures | Huawei, China Telecom | 29.213 | 0505 | 0 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131367 | 12.27 | CR | Adding the scope of Fixed Broadband Access network convergence | Huawei, China Telecom | 29.215 | 0303 | 0 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131368 | 12.27 | CR | Adding New Annex to support Fixed Broadband Access network convergence | Huawei, China Telecom | 29.215 | 0304 | 0 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131369 | 9.19 | CR | Reference update of draft-vanelburg-dispatch-private-network-ind | NTT | 29.165 | 0593 | 0 | F | 9.15.0 | II-NNI | Rel-9 | Agreed |
| C3-131370 | 9.19 | CR | Reference update of draft-vanelburg-dispatch-private-network-ind | NTT | 29.165 | 0594 | 0 | A | 10.13.0 | II-NNI | Rel-10 | Agreed |
| C3-131371 | 9.19 | CR | Reference update of draft-vanelburg-dispatch-private-network-ind | NTT | 29.165 | 0595 | 0 | A | 11.8.0 | II-NNI | Rel-11 | Agreed |
| C3-131372 | 9.19 | CR | Reference update of draft-vanelburg-dispatch-private-network-ind | NTT | 29.165 | 0596 | 0 | A | 12.1.0 | II-NNI | Rel-12 | Agreed |
| C3-131376 | 9.19 | CR | Reference update: draft-kaplan-insipid-session-id | Ericsson | 29.165 | 0597 | 0 | F | 9.15.0 | II-NNI | Rel-9 | Agreed |
| C3-131377 | 9.19 | CR | Reference update: draft-kaplan-insipid-session-id | Ericsson | 29.165 | 0598 | 0 | A | 10.13.0 | II-NNI | Rel-10 | Agreed |
| C3-131378 | 9.19 | CR | Reference update: draft-kaplan-insipid-session-id | Ericsson | 29.165 | 0599 | 0 | A | 11.8.0 | II-NNI | Rel-11 | Agreed |
| C3-131379 | 9.19 | CR | Reference update: draft-kaplan-insipid-session-id | Ericsson | 29.165 | 0600 | 0 | A | 12.1.0 | II-NNI | Rel-12 | Agreed |
| C3-131389 | 12.27 | CR | IP-CAN session Termination for Fixed Broadband Access network convergence | Ericsson | 29.213 | 0508 | 0 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131391 | 8.14 | CR | Correction in QoS derivation table in the AF | Ericsson | 29.213 | 0510 | 0 | F | 8.16.0 | SAES-St3-PCC | Rel-8 | Agreed |
| C3-131392 | 8.14 | CR | Correction in QoS derivation table in the AF | Ericsson | 29.213 | 0511 | 0 | A | 9.11.0 | SAES-St3-PCC | Rel-9 | Agreed |
| C3-131393 | 8.14 | CR | Correction in QoS derivation table in the AF | Ericsson | 29.213 | 0512 | 0 | A | 10.9.0 | SAES-St3-PCC | Rel-10 | Agreed |
| C3-131394 | 8.14 | CR | Correction in QoS derivation table in the AF | Ericsson | 29.213 | 0513 | 0 | A | 11.8.0 | SAES-St3-PCC | Rel-11 | Agreed |
| C3-131395 | 8.14 | CR | Correction in QoS derivation table in the AF | Ericsson | 29.213 | 0514 | 0 | A | 12.1.0 | SAES-St3-PCC | Rel-12 | Agreed |
| C3-131396 | 11.30 | CR | Correction of AVP name for location age | Ericsson | 29.212 | 1070 | 0 | D | 12.2.0 | NWK-PL2IMS-CT | Rel-12 | Agreed |
| C3-131402 | 10.18 | CR | Correcting table number | Ericsson | 29.165 | 0603 | 0 | F | 11.8.0 | II-NNI2 | Rel-11 | Agreed |
| C3-131403 | 10.18 | CR | Correcting table number | Ericsson | 29.165 | 0604 | 0 | A | 12.1.0 | II-NNI2 | Rel-12 | Agreed |
| C3-131431 | 11.30 | CR | Correction to access network information for EPS | ZTE | 29.212 | 1073 | 0 | F | 11.10.0 | NWK-PL2IMS-CT | Rel-11 | Agreed |
| C3-131432 | 11.30 | CR | Correction to access network information for EPS | ZTE | 29.212 | 1074 | 0 | A | 12.2.0 | NWK-PL2IMS-CT | Rel-12 | Agreed |
| C3-131505 | 11.35 | CR | Correction to the applicability of Specific-Action AVP value in temporary network failure handling | Huawei, ZTE | 29.214 | 0297 | 1 | F | 11.10.0 | eNR_EPC | Rel-11 | Agreed |
| C3-131506 | 11.35 | CR | Correction to the applicability of Specific-Action AVP value in temporary network failure handling | Huawei, ZTE | 29.214 | 0298 | 1 | A | 12.1.0 | eNR_EPC | Rel-12 | Agreed |
| C3-131507 | 11.35 | CR | SGW Restoration impacts in S9 reference point | Ericsson, ZTE, China Mobile, Huawei | 29.215 | 0305 | 1 | F | 11.10.0 | eNR_EPC | Rel-11 | Agreed |
| C3-131508 | 11.35 | CR | SGW Restoration impacts in S9 reference point | Ericsson, ZTE, China Mobile, Huawei | 29.215 | 0306 | 1 | A | 12.1.0 | eNR_EPC | Rel-12 | Agreed |
| C3-131528 | 12.22 | CR | CVO related clarifications | Ericsson, NSN | 29.162 | 0120 | 1 | F | 12.1.0 | CVO-CT | Rel-12 | Agreed |
| C3-131529 | 12.25 | CR | Handling procedures of generic image attributes | Huawei | 29.162 | 0128 | 1 | F | 12.1.0 | SIS_CT | Rel-12 | Agreed |
| C3-131531 | 9.19 | CR | Major capabilities of NOTIFY | Fujitsu, NTT | 29.165 | 0574 | 2 | A |  | II-NNI | Rel-12 | Agreed |
| C3-131532 | 10.18 | CR | Removal of debug feature | Ericsson | 29.165 | 0607 | 1 | F | 10.13.0 | II-NNI2 | Rel-10 | Agreed |
| C3-131543 | 8.14.2 | CR | Correction to QoS handling for interoperation with Gn/Gp SGSN | Huawei, China Telecom | 29.212 | 1060 | 1 | F | 12.2.0 | SAES-St3-PCC | Rel-12 | Agreed |
| C3-131544 | 11.5 | CR | Corrections to CCA in Sd messages | Huawei, China Telecom | 29.212 | 1061 | 1 | F | 11.10.0 | SAES-St3-PCC | Rel-11 | Agreed |
| C3-131545 | 11.5 | CR | Corrections to CCA in Sd messages | Huawei, China Telecom | 29.212 | 1062 | 1 | A | 12.2.0 | SAES-St3-PCC | Rel-12 | Agreed |
| C3-131546 | 11.16 | CR | Correction to USAGE_REPORT value in Sd re-used AVPs | Huawei | 29.212 | 1064 | 1 | A | 12.2.0 | SAPP-CT3 | Rel-12 | Agreed |
| C3-131547 | 11.17 | CR | IE name mapping to Diameter AVP missing | Ericsson | 29.219 | 0017 | 1 | F | 11.5.0 | QoS_SSL-CT3 | Rel-11 | Agreed |
| C3-131548 | 11.17 | CR | IE name mapping to Diameter AVP missing | Ericsson | 29.219 | 0018 | 1 | A | 12.0.0 | QoS_SSL-CT3 | Rel-12 | Agreed |
| C3-131568 | 12.27 | CR | Adding the reference architecture to support fixed broadband access network convergence | Huawei, China Telecom | 29.212 | 1067 | 1 | B | 12.2.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131569 | 12.27 | CR | Input for general part in PCC procedures | Huawei, China Telecom | 29.212 | 1068 | 1 | B | 12.2.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131570 | 12.27 | CR | Adding IP-CAN session establishment to support fixed broadband access network convergence | Huawei, China Telecom | 29.212 | 1069 | 1 | B | 12.2.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131571 | 12.27 | CR | Adding the binding mechanism for NSWO traffic | Huawei, China Telecom | 29.213 | 0503 | 1 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131574 | 8.2 | CR | Adding CS connected UEs | Ericsson | 29.162 | 0127 | 2 | F | 12.1.0 | IMS-CCR-IWCS | Rel-12 | Agreed |
| C3-131575 | 10.18 | CR | Removal of debug feature | Ericsson, Vodafone | 29.165 | 0608 | 2 | F | 11.8.0 | II-NNI2 | Rel-11 | Agreed |
| C3-131576 | 11.2 | CR | Architecture update | Ericsson | 29.162 | 0121 | 2 | F | 11.1.0 | IMS-CCR-IWCS | Rel-11 | Agreed |
| C3-131577 | 11.2 | CR | Architecture update | Ericsson | 29.162 | 0122 | 2 | A | 12.1.0 | IMS-CCR-IWCS | Rel-12 | Agreed |
| C3-131580 | 12.30 | CR | RFC 3265 to RFC 6665 | Ericsson, Telecom Italia | 29.165 | 0609 | 2 | C | 12.1.0 | UP6665 | Rel-12 | Agreed |
| C3-131581 | 11.36 | CR | Reference update: draft-ietf-soc-overload-control, draft-ietf-soc-overload-rate-control and draft-ietf-soc-load-control-event-package | Ericsson | 29.165 | 0601 | 2 | F | 11.8.0 | IOC | Rel-11 | Agreed |
| C3-131582 | 11.36 | CR | Reference update: draft-ietf-soc-overload-control, draft-ietf-soc-overload-rate-control and draft-ietf-soc-load-control-event-package | Ericsson | 29.165 | 0602 | 2 | A | 12.1.0 | IOC | Rel-12 | Agreed |
| C3-131587 | 12.27 | CR | Definition and abbreviationto support Fixed Broadband Access network convergence | ZTE | 29.212 | 1081 | 1 | B | 12.2.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131590 | 12.27 | CR | IP-CAN session Modification to support Fixed Broadband Access network convergence | ZTE | 29.212 | 1083 | 1 | B | 12.2.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131593 | 12.27 | CR | IP-CAN session Modification to support Fixed Broadband Access network convergence | Ericsson | 29.213 | 0509 | 2 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131595 | 8.5 | CR | IP-CAN type notification correction | ZTE | 29.214 | 0299 | 2 | F | 8.17.0 | PCC | Rel-8 | Agreed |
| C3-131597 | 8.5 | CR | IP-CAN type notification correction | ZTE | 29.214 | 0301 | 2 | A | 10.11.0 | PCC | Rel-10 | Agreed |
| C3-131598 | 8.5 | CR | IP-CAN type notification correction | ZTE | 29.214 | 0302 | 2 | A | 11.10.0 | PCC | Rel-11 | Agreed |
| C3-131599 | 8.5 | CR | IP-CAN type notification correction | ZTE | 29.214 | 0303 | 2 | A | 12.1.0 | PCC | Rel-12 | Agreed |
| C3-131600 | 11.24 | CR | Clarification of the ePD/GP-GW IP address | ZTE | 29.212 | 1071 | 2 | F | 11.10.0 | BBAI_BBI-CT | Rel-11 | Agreed |
| C3-131601 | 11.24 | CR | Clarification of the ePDG/P-GW IP address | ZTE | 29.212 | 1072 | 2 | A | 12.2.0 | BBAI_BBI-CT | Rel-12 | Agreed |
| C3-131604 | 12.23 | CR | Addition of Sd related functionality over S9 interface | Allot Communications, Juniper Networks, Huawei | 29.215 | 0302 | 2 | B | 12.1.0 | ABC-CT3 | Rel-12 | Agreed |
| C3-131605 | 12.23 | CR | Alignment correction to application detection description in ADC rule definition | Huawei, China Mobile, Allot Communications, China Telecom | 29.212 | 1065 | 2 | F | 12.2.0 | ABC-CT3 | Rel-12 | Agreed |
| C3-131606 | 11.35 | CR | Error handling when the PCC rule is removed due to the S-GW restoration support | ZTE | 29.212 | 1077 | 2 | F | 11.10.0 | eNR_EPC | Rel-11 | Agreed |
| C3-131607 | 11.35 | CR | Error handling when the PCC rule is removed due to the S-GW restoration support | ZTE | 29.212 | 1078 | 2 | A | 12.2.0 | eNR_EPC | Rel-12 | Agreed |
| C3-131613 | 11.32 | CR | tel URI support in the loopback scenario | Ericsson | 29.165 | 0605 | 2 | F | 11.8.0 | RAVEL-CT | Rel-11 | Agreed |
| C3-131614 | 11.32 | CR | tel URI support in the loopback scenario | Ericsson | 29.165 | 0606 | 2 | A | 12.1.0 | RAVEL-CT | Rel-12 | Agreed |
| C3-131619 | 12.27 | CR | Definitions and abbreviations in Fixed Broadband Access network convergence | Ericsson | 29.213 | 0507 | 3 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131620 | 12.4 | CR | Clarification of PVI and PCI handling for interoperation with GnGp SGSN | ZTE | 29.212 | 1079 | 2 | F | 12.2.0 | SAES-St3-PCC | Rel-12 | Agreed |
| C3-131626 | 12.27 | CR | Adding IP-CAN session establishment to support fixed broadband access network convergence | Huawei, China Telecom | 29.213 | 0506 | 2 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131630 | 11.30 | CR | Access Network Information Reporting Correction | ZTE | 29.212 | 1075 | 1 | F | 11.10.0 | NWK-PL2IMS-CT | Rel-11 | Agreed |
| C3-131631 | 11.30 | CR | Access Network Information Reporting Correction | ZTE | 29.212 | 1076 | 1 | A | 12.2.0 | NWK-PL2IMS-CT | Rel-12 | Agreed |
| C3-131636 | 12.23 | CR | Credit management session failure reporting by the PCEF | Huawei, Allot Communications, China Mobile, China Telecom, Juniper Networks | 29.212 | 1066 | 3 | F | 12.2.0 | ABC-CT3 | Rel-12 | Agreed |
| C3-131637 | 12.27 | CR | Adding the binding mechanism for traffic from fixed devices | Huawei, China Telecom | 29.213 | 0504 | 3 | B | 12.1.0 | P4C-F-CT3 | Rel-12 | Agreed |
| C3-131638 | 8.5 | CR | IP-CAN type notification correction | ZTE | 29.214 | 0300 | 3 | A | 9.14.0 | PCC | Rel-9 | Agreed |
| C3-131639 | 12.27 | CR | Functional elements to support Fixed Broadband Access network convergence | ZTE | 29.212 | 1082 | 2 | B | 12.2.0 | P4C-F-CT3 | Rel-12 | Agreed |

## Annex E. List of Participants

| Name | Representing | Status-Partner | Ctry | Ph | Mob Ph | Email |
| --- | --- | --- | --- | --- | --- | --- |
| Abou-assali, Tarek (Mr.) | Oracle Corporation | 3GPPMEMBER (ETSI) |  |  |  | tarek.abou.assali@oracle.com |
| Arai, Kenjiro (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81422593518 |  | arai.kenjiro@lab.ntt.co.jp |
| Ascolese, Antonio (Ing.) | TELECOM ITALIA S.p.A. | 3GPPMEMBER (ETSI) | IT | +390112285392 |  | antonio.ascolese@telecomitalia.it |
| Axell, Jorgen (Dr.) | Ericsson Inc. | 3GPPMEMBER (ATIS) | SE | +46 10 719 4450 | +46 70 519 4450 | Jorgen.Axell@ericsson.com |
| Bakker, John-Luc (Mr.) | BlackBerry UK Limited | 3GPPMEMBER (ETSI) | GB | +1-972-373-1761 | +1-908-463-7321 | jbakker@blackberry.com |
| Belling, Thomas (Dr.) | NSN | 3GPPMEMBER (ETSI) | DE | +49 89 5159 75207 | +49 172 2974678 | Thomas.Belling@nsn.com |
| Berry, Nigel. H (Mr.) | Alcatel-Lucent Telecom Ltd | 3GPPMEMBER (ETSI) | GB | +44 1793775019 | +44 7880 786684 | nigel.berry@alcatel-lucent.com |
| BERTRAND, Simon (Mr.) | Orange Slovakia | 3GPPMEMBER (ETSI) | FR | +33145294200 |  | simon.bertrand@orange.com |
| Biondic, Nevenka (Mrs.) | Ericsson Inc. | 3GPPMEMBER (ATIS) | HR | +385 1 365 3824 |  | nevenka.biondic@ericsson.com |
| Brinkmann, Horst (Mr.) | Alcatel-Lucent Deutschland AG | 3GPPMEMBER (ETSI) | DE | +49 711 821 37207 |  | horst.brinkmann@alcatel-lucent.com |
| Catovic, Amer (Dr.) | QUALCOMM CDMA Technologies | 3GPPMEMBER (ETSI) | US | +1-858-651-1663 |  | amerc@qti.qualcomm.com |
| Chaponniere, Lena (Mrs.) | Qualcomm Japan Inc | 3GPPMEMBER (ARIB) | FR | +18586584607 |  | lguellec@qti.qualcomm.com |
| Chin, Chen-ho (Mr.) | Intel Korea, Ltd. | 3GPPMEMBER (TTA) | BE |  | +32477413371 | chen-hox.chin@intel.com |
| Dawes, Peter (Mr.) | VODAFONE Group Plc | 3GPPMEMBER (ETSI) | GB | +44 7717 275009 |  | peter.dawes@vodafone.com |
| Di, Zhiyu (Mr.) | China Mobile Com. Corporation | 3GPPMEMBER (CCSA) |  |  |  | dizhiyu@chinamobile.com |
| Dobrowolska, Beata (Ms.) | ORANGE | 3GPPMEMBER (ETSI) | FR | +33145295759 |  | beata.dobrowolska@orange.com |
| Dolly, Martin (Mr.) | AT&T | 3GPPMEMBER (ATIS) | US | +1 609 903 3360 |  | md3135@att.com |
| Drage, Keith (Mr.) | Alcatel-Lucent Telecom Ltd | 3GPPMEMBER (ETSI) | GB | +44 1793 897312 | +44 7799 658151 | Keith.Drage@alcatel-lucent.com |
| Emanuelsson, Sven-ove (Mr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | SE | +46107121548 |  | sven-ove.emanuelsson@ericsson.com |
| Fernandez, Susana (Miss) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | ES | +34646006865 |  | susana.fernandez@ericsson.com |
| Gupta, Vivek (Mr.) | Intel K.K. | 3GPPMEMBER (ARIB) | FR | +1 408 513 5716 |  | vivek.g.gupta@intel.com |
| Han, Jiwan (Mr.) | ETSI | 3GPPORG_REP (ETSI) | FR | +33 (4) 92 94 42 31 | +33 (0)6 74 40 83 69 | jiwan.han@etsi.org |
| Holm, Jan (Mr.) | Nanjing Ericsson Panda Com Ltd | 3GPPMEMBER (CCSA) | SE | +46 8 719 7378 | + 46705197378 | Jan.Holm@ericsson.com |
| Inoue, Yoshihiro (Mr.) | NTT | 3GPPMEMBER (TTC) | JP | +81 422 36 7502 |  | yoshihiro.inoue@ntt-at.co.jp |
| Jesske, Roland (Mr.) | Deutsche Telekom AG | 3GPPMEMBER (ETSI) | DE | +49 6151 5812766 | +49 171 861 8445 | r.jesske@telekom.de |
| Kåll, Jan (Mr.) | NSN Japan | 3GPPMEMBER (ARIB) | FI | +358 400 400056 | +358400 400056 | jan.kall@nsn.com |
| Kanegae, Shunsuke (Mr.) | NTT corporation | 3GPPMEMBER (ETSI) | JP | +81422596689 |  | kanegae.shunsuke@lab.ntt.co.jp |
| Kiss, Krisztian (Mr.) | Apple Portugal | 3GPPMEMBER (ETSI) | US |  | +16503915969 | kkiss@apple.com |
| Korinek, Frank (Mr.) | Motorola Solutions UK Ltd. | 3GPPMEMBER (ETSI) | GB | +44 1256 790 790 | +1 847 877-7179 | Frank.Korinek@motorolasolutions.com |
| Kowalewski, Frank (Dr.) | Intel China Ltd. | 3GPPMEMBER (CCSA) | DE | +49 8923443512 |  | frank.kowalewski@intel.com |
| Kreipl, Michael (Mr.) | Telekom Deutschland GmbH | 3GPPMEMBER (ETSI) | DE | +49 6151 58-12081 | +49 151 42330896 | michael.kreipl@telekom.de |
| Landais, Bruno (Mr.) | Alcatel-Lucent | 3GPPMEMBER (ETSI) | FR | +33 2 96 04 82 61 |  | bruno.landais@alcatel-lucent.com |
| Lavasani, Shahab (Mr.) | Huawei Technologies Sweden AB | 3GPPMEMBER (ETSI) | SE | +46 70 6360204 | +46 70 6360204 | shahab.lavasani@huawei.com |
| Lee, Jay (Mr.) | Verizon Communications, Inc. | 3GPPMEMBER (ATIS) | US | +1-925-952-6747 |  | jay.lee@verizon.com |
| Leis, Peter (Mr.) | NSN Oy | 3GPPMEMBER (ETSI) | DE | +49 89 515925208 |  | peter.leis@nsn.com |
| Liu, Jennifer (Ms.) | Alcatel-Lucent | 3GPPMEMBER (ATIS) | US | +1-972-477-8532 | +1-214-536-3185 | jennifer.liu@alcatel-lucent.com |
| Lu, Fei (Mr.) | ZTE Corporation | 3GPPMEMBER (ETSI) | CN | +86-25-88014634 | +86-18651682123 | lu.fei1@zte.com.cn |
| Lukacs, Donald (Mr.) | Applied Communication Sciences | 3GPPMEMBER (ATIS) |  | +17327585293 |  | dlukacs@appcomsci.com |
| Machimoto, Masaki (Mr.) | DOCOMO Communications Lab. | 3GPPMEMBER (ETSI) |  |  |  | machimoto@nttdocomo.co.jp |
| Mase, Asami (Miss) | Oki Electric Industry Co. Ltd. | 3GPPMEMBER (TTC) | JP | + |  | mase622@oki.com |
| Monrad, Atle (Mr.) | Telefon AB LM Ericsson | 3GPPMEMBER (ETSI) | NO |  | +47 454 10 665 | atle.monrad@ericsson.com |
| Muto, Yuta (Mr.) | Hitachi Ltd. | 3GPPMEMBER (ARIB) | JP | +81-42-323-1111 |  | yuta.muto.nc@hitachi.com |
| Nakamura, Kiwa (Miss) | NEC Telecom MODUS Ltd. | 3GPPMEMBER (ETSI) |  |  |  | k-nakamura@cj.jp.nec.com |
| Okada, Yuki (Mr.) | Fujitsu Limited | 3GPPMEMBER (TTC) | JP | +81-44-754-4146 |  | okada.yuki@jp.fujitsu.com |
| Qiao, Weihua (Mr.) | HuaWei Technologies Co., Ltd | 3GPPMEMBER (CCSA) | CN | +8613691091311 | +8613691091311 | qiaoweihua@huawei.com |
| Russell, Nick (Mr.) | Research in Motion Japan Ltd. | 3GPPMEMBER (ARIB) | GB | +44 7748 938929 | +44 7748 938 929 | nrussell@blackberry.com |
| Salot, Nirav (Mr.) | Cisco Systems Belgium | 3GPPMEMBER (ETSI) |  |  | +919326737733 | nsalot@cisco.com |
| Schmitt, Peter (Mr.) | Huawei Technologies France | 3GPPMEMBER (ETSI) | CN |  | +49 171 7450251 | peter.schmitt@huawei.com |
| Schwarz, Albrecht (Dr.) | Alcatel-Lucent | 3GPPMEMBER (ETSI) | DE | +49 711 821 41425 |  | Albrecht.Schwarz@alcatel-lucent.com |
| Shi, Shufeng (Mrs.) | Huawei Technologies (UK) | 3GPPMEMBER (ETSI) |  | +862981775094 | +8613571984613 | susan.shishufeng@huawei.com |
| Shu, Lin (Mr.) | HiSilicon Technologies Co., Lt | 3GPPMEMBER (CCSA) | CN | +86-15216618582 |  | shulin@huawei.com |
| Subramanian, Ramachandran (Mr.) | Qualcomm Incorporated | 3GPPMEMBER (ATIS) | US | +1 858 651 2350 |  | rsubrama@qti.qualcomm.com |
| Suzuki, Naoaki (Mr.) | NEC EUROPE LTD | 3GPPMEMBER (ETSI) | JP | +81-4-7185-6722 |  | n-suzuki@en.jp.nec.com |
| Takakura, Tsuyoshi (Mr.) | NTT DOCOMO INC. | 3GPPMEMBER (ARIB) |  | +81468403370 |  | tsuyoshi.takakura.ey@s1.nttdocomo.com |
| Takeda, Shinya (Mr.) | NTT DOCOMO INC. | 3GPPMEMBER (TTC) | JP | +046-840-3530 |  | takedash@nttdocomo.co.jp |
| Xia, Haitao (Mr.) | HUAWEI TECHNOLOGIES Co. Ltd. | 3GPPMEMBER (ETSI) | CN | +86 10 60611953 |  | xiahaitao@huawei.com |
| YANG, Weiwei(Tommy) (Mr.) | HuaWei Technologies Co., Ltd | 3GPPMEMBER (ATIS) | GB |  |  | tommy@huawei.com |
| Yokoyama, Shin (Dr.) | DOCOMO Communications Lab. | 3GPPMEMBER (ETSI) |  | +81449007540 | +818013284732 | shin.yokoyama.kc@s1.nttdocomo.com |
| Yu, Youyang (Miss) | HUAWEI Technologies Japan K.K. | 3GPPMEMBER (ARIB) | CN | +13661409703 |  | yuyouyang@huawei.com |

Report prepared by: Jiwan Han, CT3 MCC.