3GPP TS 29.333 V0.1.0 (2005-08)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Core Network and Terminals;

Multimedia Resource Function Controller (MRFC) – Multimedia

Resource Function Processor (MRFP) Mp Interface - Stage 3;

(Release 7)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

UMTS, IP, Multimedia

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2005, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TTA, TTC).

All rights reserved.

Contents

Foreword	5

1	Scope	5

2	References	5

3	Definitions, symbols and abbreviations	7

3.1	Definitions	7

3.3	Abbreviations	7

4	Applicability	7

4.1	Architecture	7

4.2	 Functional Requirements	8

5.	Profile Description	9

5.1	Profile Identification	9

5.2	Summary	9

5.3	Gateway Control Protocol Version	9

5.4	Connection Model	9

5.5	 Context Attributes	10

5.6	Terminations	10

5.6.1	Termination Names	10

5.6.2	 Multiplexed Terminations	10

5.7	Descriptors	10

5.7.1	Stream Descriptor	10

5.7.1.1	LocalControl Descriptor	11

5.7.2	Events Descriptor	12

5.7.3	EventBuffer Descriptor	12

5.7.4	Signals Descriptor	13

5.7.5	DigitMap Descriptor	14

5.7.6	Statistics Descriptor	14

5.7.7	ObservedEvents Descriptor	14

5.7.8	 Topology Descriptor	15

5.7.9	Error Descriptor	15

5.8 Command API	15

5.8.1	Add	15

5.8.2	Modify	15

5.8.3	Subtract	15

5.8.4	Move	16

5.8.5	AuditValue	16

5.8.6	AuditCapabilities	16

5.8.7	Notify	16

5.8.8	ServiceChange	16

5.8.9 	Manipulating and Auditing Context Attributes	17

5.9 	Generic Command Syntax and Encoding	17

5.10 	Transactions	17

5.11 	Messages	18

5.12 	Transport	19

5.13 	Security	19

5.14 	Packages	19

5.15 	Mandatory Support of SDP and Annex C Information Elements	22

5.16 	Procedures	24

6.	 Procedures	24

6.1	 General Procedures	24

6.2	Use of Voice Codecs	24

6.2.1	Comfort Noise Insertion and Silence Suppression for Voice Codecs	24

6.2.2	 DTMF Transmission	24

6.2.3	Support of G.711 variants	25

6.2.3..1	G.711 Encoding Law	25

6.2.3.2	G.711 Silence Suppression Mode	25

6.2.3.3	G.711 Packet Loss Concealment	25

6.3	Procedures for basic user interaction	25

6.4	Procedures for advanced user interaction	25

6.5	Procedures for conferencing	26

6.6.	Procedures for transcoding	26

7.	MRFP and MRFC Management	26

7.1	 Overload Control	26

7.2	  IP QoS Control and Monitoring	26

Annex <X> (informative):	Change history	27

# Foreword

This Technical Specification has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# 1	Scope

The present document describes the protocol to be used on the Multimedia Resource Function Controller (MRFC) – Multimedia Resource Function Processor (MRFP) interface (Mp interface). The IMS architecture is described in 23.228.

This specification defines a profile of the Gateway Control Protocol (H.248.1), for controlling Multimedia Resource Function Processor supporting in-band user interaction, conferencing and transcoding for voice-services.

The present document is valid for a 3rd generation PLMN (UMTS) complying with Release 7 and later.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.  In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 23.228: "IP Multimedia Subsystem (IMS); Stage 2".

[2]	3GPP TS 23.002: "Network architecture".

[3]	ITU-T Recommendation H.248.1 (05/2002), Gateway control protocol: Version 2 + Corrigendum 1 (03/2004).

[4]	ITU-T Recommendation H.248.4 (11/2000), Gateway control protocol: Transport over Stream Control Transmission Protocol (SCTP) + Corrigendum 1 (03/2004).

[5]	ITU-T Recommendation H.248.7 (03/2004), Gateway control protocol: Generic announcement package.

[6]	ITU-T Recommendation H.248.9 (03/2002), Gateway control protocol: Adavanced media server package.

[7]	ITU-T Recommendation H.248.11 (11/2002), Gateway control protocol: Media gateway overload control package.

[8]	ITU-T Recommendation H.248.13 (03/2002), Gateway control protocol: Quality Alert Ceasing package.

[9]	ITU-T Recommendation H.248.14 (03/2002), Gateway control protocol: Inactivity timer package.

[10]	ITU-T Recommendation H.248.16 (11/2002), Gateway control protocol: Enhanced digit collection packages and procedures + Corrigendum 1 (03/2004).

[11]	ITU-T Recommendation H.248.19 (03/2004) Gateway control protocol: Decomposed Multipoint Control Unit, Audio, Video and Data Conferencing package

[12]	ITU-T Recommendation H.248.27 (07/2003), Gateway control protocol: Supplemental Tones package

[13]	ITU-T Recommendation Q.1950 (12/2002), Bearer independent call bearer control protocol.

[14]	ITU-T Recommendation G.711 (11/1988), Pulse code modulation (PCM) of voice frequencies.

[15]	ITU-T Recommendation G.711 Appendix I (09/1999), A high quality low-complexity algorithm for packet loss concealment with G.711.

[16]	ITU-T Recommendation G.711 Appendix I (09/1999), A comfort noise payload definition for ITU-T G.711 use in packet-based multimedia communication systems.

[17]	ITU-T Recommendation E.180 (03/1998), Technical characteristics of tones for the telephone service.

[18]	TS 183 022: Telecommunication and Internet converged Services and Protocols for Advanced Networking (TISPAN); MGC Information Package.

[19]	ES 201 970 Access and Terminals (AT); Public Switched Telephone Networks (PSTN); Harmonized specification of physical and electrical characteristics at a 2-wire analogue presented Network Temination Point (NTP).

[20]	IETF RFC 2327 (1998), SDP: Session Description Protocol.

[21]	IETF RFC 3551(2003), RTP Profile for Audio and Video Conferences with Minimal Control.

[22]	IETF RFC 2833 (2000), RTP Payload for DTMF Digits, Telephony Tones and Telephony Signals.

[23]	IETF RFC 4040 (2005), RTP payload format for a 64 kbit/s transparent call.

[24]	IETF RFC 3555 (2003), MIME Type Registration of RTP Payload Formats.

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply.

Media Gateway: See Recommendation H.248.1 [3].

Media Gateway Controller: See Recommendation H.248.1 [3].

MultiMedia Resource Function Controller: See 3GPP TS 23.002 [2].

MultiMedia Resource Function Processor:  See 3GPP TS 23.002 [2].

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

CDR	Call Data Record

CN	Comfort Noise

CRC	Cyclic Redundancy Check

DNS	Domain Name System

DTMF	Dual Tone Multi Frequency

FEC	Forward Error Correction

IP	Internet Protocol

IPsec	IP Security

MRFP	Media Gateway

MRFC	Media Gateway Controller

MID	Message Identifier

MRFC 	Media Resource Function Controller

MRFP	Media Resource Function Processor

NAT		Network Address Translation

OAM	Operation, Administration and Maintenance

OoS	Out of Service

PLC	Packet Loss Concealment

PT	Payload Type

QoS	Quality of Service

SCTP	Stream Control Transmission Protocol

SDP	Session Description Protocol

SPNE	Signal Processing Network Equipment

SSRC	Synchronisation Source

TCP	Transmission Control Protocol

TLS	Transport Layer Security

TTL	Time To Live

UDP	User Datagram Protocol

VBD	Voiceband Data

# 4	Applicability

## 4.1	Architecture

The Mp reference point allows an MRFC to control media stream resources provided by an MRFP. The MRFC controls the MRFP, based on the information received from Application Servers, via the S-CSCF, at the Mr reference point. The MRFP sources and sinks media streams at the Mb reference point, which represent the interface to core network transport resources. Figure 1 show the of the functional entities and reference points involved in the control of multimedia resources.  This specification focuses on the Mp reference point.

Figure 1: MRF entities and interfaces in the IMS architecture

Three categories of MRFP functionalities are identified by the present document:

- Support of basic User Interaction (UI). This category is subdivided into two subcategories:

  - Basic User Interaction (BASIC_UI): This includes basic support for sending tones, fixed announcements and collecting DTMF.

  - Advanced User Interaction (ADVANCED_UI): This includes support of  IVR and messaging capabilities.

- Support for transcoding (TRANSCODING). This category is subdivided into two subcategories:

  - Basic Transcoding (BASIC_TRANSCODING): This includes support for transcoding between voice codecs.

  - Advanced Transcoding  (ADVANCED_TRANSCODING): This includes support for basic transcoding and multimedia transcoding.

- Support for conferencing (CONFERENCING). This category is subdivided into two subcategories:

  - Basic Conferencing (BASIC_CONFERENCING): This includes support for 3-party calls up to large voice conferences.

  - Advanced conferencing (ADVANCED_CONFERENCING): This includes support for floor control procedures and multimedia conferences.

Editor's note: The present version of the document does not specify multimedia capabilities. Should the TISPAN R1 or 3GGP version of this profile already provide support for minimal multimedia capabilities (e.g. voice + video conference, video transcoding, ….)?

## 4.2		Functional Requirements

Support of the packages identified in the profile definition implies support of the underlying functionalities. This section identifies additional functional requirements that media gateways conforming to this standard shall comply with.

Media Resource Function Processors shall support IPv4 and may support IPv6.

Media Resource Function Processors shall support for G.711 A-law voice codec and may support other codecs. Media Resource Function Processors supporting TRANSCODING are expected to support a wide range of well-known codecs. The list of codecs is outside the scope of this specification.

Editor's note: shall we mandate other codec e.g. UMTS AMR..?

Media Resource Function Processors supporting other codecs than G.711 shall also support the procedures defined in RFC 2833 [22] to generate, detect and forward DTMF digits. DTMF shall be identified by name (see mode “Named Telephone Events” in clause 3/RFC 2833 [22]), as opposed to their waveform properties.

All properties of tones requested by the MRFC shall be provisioned in the Media Gateway. The MRFC is not required to send the physical characteristics of tones to Media Resource Function Processors.

# 5.	Profile Description

## 5.1	Profile Identification

The name and version of the profile that is sent in the service change command are:

Table 5.1.1

| Profile name: | Xxxx <to be defined> |
| --- | --- |
| Version: | 1 |

## 5.2	Summary

The profile defined in the present document enables the control of media resource function processors (MRFP) supporting in-band user interaction, conferencing and transcoding for voice services.

NOTE: 	It is expected that future versions of this profile will support similar features in the context of multimedia communications.

## 5.3	Gateway Control Protocol Version

Version 2 shall be the minimum version supported. Support of this version implies conformance to ITU-T Recommendation H.248 Version 2 [3] and Corrigendum 1 to this Recommendation, and implementation of the corrections available in the latest version of the H.248 Implementors' Guide.

## 5.4	Connection Model

Media Resource Function Processors shall support ephemeral terminations that sink and source RTP traffic. This type of H.248 Termination is denoted RTP in the following clauses.

Table 5.4.1

| Maximum number of contexts: | Provisioned (NOTE 1) |
| --- | --- |
| Maximum number of terminations per context: | 1 (NOTE 2), 2 (NOTE 3) 32 (NOTE 4) |
| Allowed terminations type combinations in a context: | Not Applicable |
| NOTE 1: The actual number of supported contexts can be audited by the MRFC using the MaxNrOfContexts property defined in the Base Root Package. NOTE 2: Support of 1 termination in a context is the basic requirement for the MRFP. NOTE 3: Support of 2 terminations is required if TRANSCODING is supported. NOTE 4: Support of up to 32 terminations may be required if CONFERENCING is supported. The actual number of supported terminations can be audited by the MRFC using the maxTerminationsPerContext property defined in the Base Root Package. |

## 5.5		Context Attributes

Table 5.5.1

| Context Attribute | Supported | Values Supported |
| --- | --- | --- |
| Topology | Yes | See § 5.7.8 |
| Priority Indicator | No | 0-15 |
| Emergency Indicator | No | Not Applicable |

## 5.6	Terminations

### 5.6.1	Termination Names

The Termination ID structure is provisioned in the MRFC and MRFP and is known by the MRFP and the MRFC at or before start up.

The following naming convention is recommended:

"RTP" * 9 ("/" /  ALPHA / DIGIT)

### 5.6.2		Multiplexed Terminations

Table 5.6.2.1

| Multiplex Terminations Supported? | NO |
| --- | --- |

## 5.7	Descriptors

### 5.7.1	Stream Descriptor

Table 5.7.1.1

| Maximum number of streams per termination type | ALL | 1 |
| --- | --- | --- |

#### 5.7.1.1	LocalControl Descriptor

The following tables specify the level of support required with regard to the properties in the local control descriptor.

Table 5.7.1.1.1

|  | Termination Type | Stream Type |
| --- | --- | --- |
| Reserve group used: | NO (NOTE) | RTP | Not Applicable |
| Reserve value used: | YES | RTP | Audio, Video |
| NOTE: Support of Resevre Group in case of multiple p-time values requires further studies |

ReserveValue

The MRFC shall set the "ReserveValue" property to "true" when multiple codecs are specified within a single "m=" line of a session descriptor block and resources are required to be reserved in the MRFP for the multiple codecs. This situation occurs for example in case of user interaction procedures where the user is expected to either speaks or enter digits. The "ReserveValue" property shall be set to "true" in cases where a low bit rate codec is used for transporting voice and the special payload type defined in RFC 2833 [22] is used for transporting DTMF.

Alternatively, if the MRFC when it specifies multiple codecs requires the MRFP to select one of the codecs, then it shall set the "ReserveValue" property to "false".

In the situation where the MRFC specifies a single codec within a "m line", then the ReserveValue property shall be omitted or set to "false".

Stream Mode

Table 5.7.1.1.2

| Termination Type | Stream Type | Allowed StreamMode Values |
| --- | --- | --- |
| ALL except ROOT | Any | Send, Receive, Send and Receive, Inactive |

Table 5.7.1.1.3

| Properties associated with Local Control Descriptor supported: | Yes |
| --- | --- |
| If yes | Property IDs Reported | Termination Type | Stream Type |
|  | mGCinfo/db | RTP | Any |
|  | aassm/* | RTP | Audio |
|  | aasrec/* | RTP | Audio |
|  | vcp/level | RTP | Audio |
|  | vlmp/mixlevel | RTP | Audio |
|  | vlmp/nspeakmix | RTP | Audio |
|  | mvlcp/mixpartnum | RTP | Audio |
|  | mvlcp/vollevip | RTP | Audio |

### 5.7.2	Events Descriptor

Table 5.7.2.1

| Events settable on termination types and stream types: | Yes |
| --- | --- |
| If yes | Event ID | Termination Type | Stream Type |
|  | g/* | RTP | Any |
|  | nt/*l | RTP | Any |
|  | rtp/* | RTP | Any |
|  | aas/rec/* | RTP | Not Applicable |
|  | aas/dc/* | RTP | Any |
|  | aas/b/* | RTP | Any |
|  | qac/* | RTP | Any |
|  | it/* | ROOT | Not Applicable |
|  | vdp/* | RTP | Audio |

Table 5.7.2.2

| Event Buffer Control used: | No |
| --- | --- |

Table 5.7.2.3

| Keepactive used on events: | Yes |
| --- | --- |

Table 5.7.2.4

| Embedded events in an event descriptor: | Yes |
| --- | --- |
| Embedded signals in an event descriptor: | Yes |

Table 5.7.2.5

| NotifyBehaviour used on events: | NO |
| --- | --- |
| If yes, | Supported values | Not Applicable |

### 5.7.3	EventBuffer Descriptor

Table 5.7.3.1

| Event Buffer descriptor used: | No |
| --- | --- |
| If yes | Event IDs | Not Applicable |

### 5.7.4	Signals Descriptor

Table 5.7.4.1

| Signals settable dependant on termination or streams types: | Yes |
| --- | --- |
| If yes | Signal ID | Termination Type | Stream Type / ID |
|  | cg/* | RTP | Audio |
|  | srvtn/* | RTP | Audio |
|  | xcg/* | RTP | Audio |
|  | an/* | RTP | Audio |
|  | int/* | RTP | Audio |
|  | biztn/* | RTP | Audio |
|  | aasrec/* | RTP | Audio |
|  | aasdc/* | RTP | Audio |
|  | aasba/* | RTP | Audio |
|  | conftn/* | All except ROOT | Any |
|  | indview/* | All except ROOT | Any |

Table 5.7.4.2

| Signals Lists supported: | Yes |
| --- | --- |
| If yes | Termination Type Supporting Lists | ALL except ROOT |
|  | Stream Type Supporting lists | ALL except ROOT |
|  | Maximum number of signals per signal list | 5 |

Table 5.7.4.3

| Signal type and duration supported? | Yes |
| --- | --- |
| If yes | Signal ID | Type or duration override |
|  | ALL | Both |

Table 5.7.4.4

| Signal Direction supported: | No |
| --- | --- |

Table 5.7.4.5

| Notify completion supported: | Yes |
| --- | --- |
| If yes | Signal ID | Type of completion supported |
|  | xg/*, svrtn/*, xcg/*, an/*, int/*, biztn/*, conftn/*, indview/* | ALL |

Table 5.7.4.6

| RequestID Parameter Supported: | Yes |
| --- | --- |

Table 5.7.4.7

| Signals played simultaneously: | Yes |
| --- | --- |
| If yes | Signal Ids that can be played simultaneously: | ALL |

Table 5.7.4.8

| Keepactive used on signals: | Yes |
| --- | --- |

### 5.7.5	DigitMap Descriptor

Media Resource Function Processors conforming to this profile shall support at least one DigitMap.

Table 5.7.5.1

| DigitMaps supported: | NOTE |
| --- | --- |
| If yes | DigitMap Name | Structure | Timers |
|  | Provisioned | Network operator dependent. | Network operator dependent. |
| NOTE: if (ADVANCED_UI or BASIC_UI) then YES else NO. |

### 5.7.6	Statistics Descriptor

Table 5.7.6.1

| Statistics supported on: | Termination |
| --- | --- |

Table 5. 7.6.2

| Statistics reported on Subtract: | Yes |
| --- | --- |
| If yes | Statistic IDs Reported | Termination Type | Stream Type |
|  | nt/dur nt/os nt/or | ALL RTP RTP | Not Applicable |
|  | rtp/* | RTP |  |

### 5.7.7	ObservedEvents Descriptor

When the event is provisioned in the media gateway, the Request Id is set to FFFFFFFF'H.

Table 5.7.7.1

| Event detection time supported: | Yes |
| --- | --- |

### 5.7.8		Topology Descriptor

Table 5.7.8.1

| Allowed triples: | (T1,T2, isolate) (T1,T2, oneway) (T1,T2, bothway) |
| --- | --- |

### 5.7.9	Error Descriptor

Table 5.7.9.1: Error codes sent by the MRFC

| Supported H.248.8 Error Codes: | ALL |
| --- | --- |
| Supported Error Codes defined in packages: | 400-411,421,422, 430, 431,440,442—458, 505, 533 |

Table 5.7.9.2 Error codes sent by the MRFP

| Supported H.248.8 Error Codes: | ALL |
| --- | --- |
| Supported Error Codes defined in packages: | 400-411, 412, 421,422,430, 431, 432-435,440,441,442-458, 471, 500-540, 600-612 |

## 5.8 Command API

### 5.8.1	Add

Table 5.8.1.1

| Descriptors used by Add request: | ALL except Mux |
| --- | --- |

Table 5.8.1.2

| Descriptors used by Add reply: | ALL except Mux |
| --- | --- |

### 5.8.2	Modify

Table 5.8.2.1

| Descriptors used by Modify request: | ALL except Mux |
| --- | --- |

Table 5. 8.2.2

| Descriptors used by Modify reply: | ALL except Mux |
| --- | --- |

### 5.8.3	Subtract

Table 5.8.3.1

| Descriptors used by Subtract request: | Audit |
| --- | --- |

Table 5.8.3.2

| Descriptors used by Subtract reply: | Statistics |
| --- | --- |

### 5.8.4	Move

Table 5.8.4.1

| Move command used: | Yes |
| --- | --- |

Table 5.8.4.2

| Descriptors used by Move Request: | ALL except Mux |
| --- | --- |
| Descriptors used by Move Reply: | ALL except Mux |

### 5.8.5	AuditValue

Table 5.8.5.1

| Audited Properties: | ALL properties | in ALL descriptors |
| --- | --- | --- |
| Audited Statistics: | ALL |
| Audited Signals: | ALL |
| Audited Events: | ALL |

Table 5.8.5.2

| Package Audit possible? | YES |
| --- | --- |

### 5.8.6	AuditCapabilities

Table 5.8.6.1

| Audited Properties: | ALL properties | in ALL descriptors |
| --- | --- | --- |
| Audited Statistics: | ALL |
| Audited Signals: | ALL |
| Audited Events: | ALL |

### 5.8.7	Notify

| Descriptors used by Notify Request or Reply: | ObservedEvents, Error |
| --- | --- |

### 5.8.8	ServiceChange

:

Table 5.8.8.1: Initiated by MRFC

| Service Change Methods Supported: | ServiceChange Reasons supported: |
| --- | --- |
| Forced, Graceful, Restart, Handoff | 900 – 917 except 908 and 909 |

Table 5.8.8.2 Initiated by MRFP:

| Service Change Methods Supported: | ServiceChange Reasons supported: |
| --- | --- |
| Forced, Graceful, Restart, Handoff, Failover, Disconnected | 900-917 |

Table 5.8.8.3

| ServiceChangeAddress used: | No |
| --- | --- |

Table 5.8.8.4

| ServiceChangeDelay used: | Yes |
| --- | --- |
| If yes | Valid time period: | Provisioned |

Table 5.8.8.5

| ServiceChange Incomplete Flag used: | No |
| --- | --- |

Table 5.8.8.6

| Version used in ServiceChangeVersion: | Version 2 [3] shall be the minimum version used in ServiceChangeVersion. |
| --- | --- |

Table 5.8.8.7

| Profile negotiation as per H.248.18: | No |
| --- | --- |

### 5.8.9 	Manipulating and Auditing Context Attributes

Table 5.8.9.1

| Context Attributes Manipulated: | ALL supported attributes (See table x.x) |
| --- | --- |
| Context Attributes Audited: | ALL supported attributes (See table x.x) |

## 5.9 	Generic Command Syntax and Encoding

Table 5.9.1

| Supported Encodings: | Text encoding shall be supported by both the MRFP and the MRFC. Both the long and short form of text encoding shall be supported at the receiving side. |
| --- | --- |

## 5.10 	Transactions

Table 5.10.1

| Maximum number of Transaction Requests / Replies / TransResponseAcks / Segment Replies per message: | TBD |
| --- | --- |
| NOTE : When more than one element are conveyed in one message, it is recommended that this message comprises a Transaction Request / Transaction Reply / Transaction Pending plus a Transaction Response Ack. |

Table 5.10.2

| Segmentation Supported: | UDP : No SCTP : Inherent in transport |
| --- | --- |
| NOTE: The H.248 Segmentation Package according Annex E.14 of H.248.1 Version 3 is intended for H.248 transport technologies without the capability of automatic message segmentation. This method is not required for UDP- or SCTP-based H.248 signalling transport in this Profile. |

Table 5.10.3

| Maximum number of commands per Transaction request: | TBD |
| --- | --- |

Table 5.10.4

| Maximum number of commands per Transaction reply: | TBD |
| --- | --- |

.

Table 5.10.5

| Commands able to be marked “Optional”: | AUDITVALUE, AUDITCAPABILITY |
| --- | --- |
| NOTE: the meaning of this table is that if one of the listed commands failed then the possibly present subsequent command within the same transaction will be processed. |

Table 5.10.6

| Transaction Timer: | Value |
| --- | --- |
| NormalMGExecutionTime | Provisioned in the MRFP |
| NormalMGCExecutionTime | Provisioned in the MRFP |
| MGOriginatedPendingLimit | Provisioned in the MRFP |
| MGCOriginatedPendingLimit | Provisioned in the MRFP |
| MGProvisionalResponseTimerValue | Provisioned in the MRFP |
| MGCProvisionalResponseTimerValue | Provisioned in the MRFP |

Transaction timers (as defined in the properties of the Base Root package) shall be in a range between 100 milliseconds and 5 seconds. The MRFC may overwrite the provisioned values.

## 5.11 	Messages

It is recommended that MRFP and MRFC names are in the form of fully qualified domain name. For example the domain name of the MRFC may be of the form MRFC1.whatever.net and the name of the MRFP may be of the form mg1.whatever.net.

The fully qualified domain name will be used by the MRFP and MRFC as part of the “Message Identifier” in the H.248 messages which identifies the originator of the message.

The MRFC domain name is provisioned in the MRFP or retrieved from the DNS using SRV records.

The use of a domain name provides the following benefits:

- MGs and MRFCs are identified by their domain name, not their network addresses. Several addresses can be associated with a domain name. If a command cannot be forwarded to one of the network addresses, implementations shall retry the transmission using another address.

- MGs and MRFCs may move to another platform. The association between a logical name (domain name) and the actual platform are kept in the Domain Name Service (DNS). MRFP and MRFC shall keep track of the record's time-to-live read from the DNS. They shall query the DNS to refresh the information if the time-to-live has expired.

The domain name may be used by MRFC/MRFP for authentication purposes.

Can assist in trouble shooting.

## 5.12 	Transport

Table 5.12.1

| Supported Transports: | Transport over UDP shall be supported. Support of SCTP is optional and shall conform to Recommendation H.248.4 [4]. Choosing one option or the other is a network operator’s decision, based on the network configuration. |
| --- | --- |

For UDP transport the destination IP addresses to be used for delivering the H.248 messages are retrieved through the following means:

The MRFC will store the source IP address retrieved from the message carrying first ServiceChange command.  All subsequent messages delivered to the MRFP will use this IP address.

The MRFP will store the source IP address retrieved from the message carrying the reply to the ServiceChange command.  All subsequent messages delivered to the MRFC will use this IP address.

NOTE: 	The MRFP will use the DNS lookup in order to retrieve the initial IP address to send the first ServiceChange command.  This IP address may be different than the IP address returned in the reply to ServiceChange command.

Table 5.12.2

| Control Association Monitoring Supported: | UDP : AuditValue on Root and H.248.14 [9] SCTP : Inherent in Transport, |
| --- | --- |

## 5.13 	Security

Table 5.13.1

| Supported Security: | For the purpose of the present document the control protocols are considered to be inside the secured zone of a single operator as shown in Figure 1. The specified H.248 security options should not be used, as these interfaces are considered to be within a secured zone. |
| --- | --- |

## 5.14 	Packages

Table 5.14.1

| Mandatory Packages |
| --- |
| Package Name / Reference | Package ID | Version |
| Generic (H.248.1, [3]) | g | 1 |
| Base Root (H.248.1, [3]) | root | 2 |
| Overload Control Package (H.248.11, [6]) | ocp | 1 |
| Network (H.248.1, [3]) | nt | 1 |
| RTP Package (H.248.1, [3]) | ntp | 1 |

Table 5.14.2

| Optional Packages |
| --- |
| Package Name / Reference | Package ID | Version | Support dependent on: |
| Extended DTMF Detection (H.248.16, [10]) | xdd | 1 | Support is mandatory if BASIC_UI and the AAS Digit Collection package is not supported, optional otherwise |
| Call Progress Tones Generator (H.248.1,3]) | cg | 1 | Support is mandatory if BASIC_UI and the Advanced Audio Server Base and the Voice Variable Syntax packages are not supported, optional otherwise |
| Basic Services Tones Generator (Q.1950, [13]) | srvtn | 1 | Support is mandatory if BASIC_UI and the Advanced Audio Server Base and the Voice Variable Syntax packages are not supported, optional otherwise |
| Expanded Call Progress Tones Generator (Q.1950, [13]) | xcg | 1 | Support is mandatory if BASIC_UI and the Advanced Audio Server Base and the Voice Variable Syntax packages are not supported, optional otherwise |
| Basic Announcement Syntax (H.248.9, [6]) | bannsyx | 1 | Support is mandatory if ADVANCED_UI is supported, Support is mandatory if BASIC_UI is supported and the Generic Announcement package is not supported, optional otherwise. |
| Voice Variable Syntax (H.248.9, [6]) | vvsyx | 1 | Support is mandatory if ADVANCED_UI is supported, optional otherwise. |
| Announcement Set Syntax (H.248.9, [6]) | setsyx | 2 | Support is mandatory if ADVANCED_UI, optional otherwise. |
| General text Variable type (H.248.9, [6]) | phrsyx | 2 | Support is mandatory if ADVANCED_UI, optional otherwise. (required for TTS) |
| Advanced Audio Server Base (H.248.9, [6]) | aasb | 1 | Support is mandatory if ADVANCED_UI, Support is mandatory if BASIC_UI and the Generic Announcement package is not supported, optional otherwise. |
| AAS Digit collection (H.248.9, [6]) | aasdc | 2 | Support is mandatory if ADVANCED_UI, optional otherwise. |
| AAS Recording package (H.248.9, [6]) | aasrec | 1 | Support is mandatory if ADVANCED_UI, optional otherwise. |
| AAS segment management (H.248.9, [6]) | aassm | 1 | Optional |
| Generic Announcement (H.248.7, [5]) | an | 2 | Support is mandatory if BASIC_UI and the Advanced Audio Server Base package is not supported, optional otherwise. |
| Intrusion Tones Generation (Q.1950, [13]) | int | 1 | Support is mandatory if BASIC_UI and the Advanced Audio Server Base and the Voice Variable Syntax packages are not supported, optional otherwise |
| Business Tones Generation (Q.1950, [13]) | biztn | 1 | Support is mandatory if BASIC_UI and the Advanced Audio Server Base and the Voice Variable Syntax packages are not supported, optional otherwise |
| Conferencing Tones Generation (H.248.27, [12]) | conftn | 1 | Support is mandatory if ADVANCED_CONFERENCING is supported, not required otherwise. |
| View (H.248.19, [11]) | indview | 1 | Support is mandatory if ADVANCED_CONFERENCING is supported, not required otherwise. |
| Volume Control (H.248.19, [11]) | vcp | 1 | Support is mandatory if ADVANCED_CONFERENCING is supported, optional otherwise. |
| Volume Detection (H.248.19, [11]) | vdt | 1 | Support is mandatory if ADVANCED_CONFERENCING is supported, optional otherwise. |
| Volume Level Mixing (H.248.19, [11]) | vlm | 1 | Support is mandatory if ADVANCED_CONFERENCING is supported, not required otherwise. |
| Mixing Volume Level Control (H.248.19, [11]) | mvlc | 1 | Support is mandatory if ADVANCED_CONFERENCING is supported, not required otherwise. |
| Quality Alert Ceasing (H.248.13, [8]) | aac | 1 | Support is mandatory if Quality of Service Monitoring is enabled on the MRFP. |
| Inactivity Timer (H.248.14, [9]) | it | 1 | Support is mandatory if UDP transport is enabled for H.248 messages. |
| MGC Information (TS 183 022, [18]) | MGCCInfo | 1 | This package may be supported as an operator option. For this profile the information string shall be limited to 32 octets in length. |

Table 5.14.3: Package Usage Information

| Package Usage Information: |
| --- |
| Package Name | Support of Properties, Parameters, Signals, Events, Statistics, Error Codes | Package Usage/ Provisioned Value: |
| Generic | ALL |  |
| Base Root | ALL |  |
| Call Progress Tones Generator | ALL | If used, the release tone shall be identical to the congestion tone. Levels, cadences and frequencies of signals shall conform to national specifications. In the absence of such specification, the following rules shall be used. Levels, cadences and frequencies of the following signals shall conform to ES 201 970 [19]: - Dial Tone - Ringing Tone (also known as ringback tone) - Busy Tone - Call Waiting Tone The characteristics of other signals shall conform to ITU-T Recommendation E.180 [17]. |
| Basic Services Tones Generator | ALL | Unless specified otherwise in national specifications, the characteristics of the Message Waiting Tone signal shall be those defined in ES 201 970 for the Special Dial Tone. |
| Expanded Call Progress Tones Generator | ALL | Unless specified otherwise in national specifications, the characteristics of the Special Condition Dial Tone (spec) shall be those of the Special Dial Tone defined in ES 201 970 [19] |
| Extended DTMF Detection | ALL | DTMF detection shall conform to ES 201 253-3. Recommended default values of the timers defined in H.248.1 [3] for an initial digit map are: - T = 20 seconds - S = 5 seconds - L = 10 seconds |
| Overload Control | ALL |  |
| Network | ALL | The MRFC should not set the Maximum Jitter Buffer property. Media Resource Function Processors shall ignore this property if received from a MRFC. |
| RTP | ALL |  |
| Generic Announcement | ALL |  |
| Intrusion Tones Generator | ALL |  |
| Business Tones Generator | ALL |  |
| DiffServ | ALL |  |
| Quality Alert Ceasing | ALL |  |
| Inactivity Timer | ALL |  |
| MGC Information | ALL |  |
| Basic Announcement Syntax (H.248.9, [6]) | ALL |  |
| Voice Variable Syntax (H.248.9, [6]) | ALL |  |
| Announcement Set Syntax (H.248.9, [6]) | ALL |  |
| General text Variable type (H.248.9, [6]) | ALL |  |
| Advanced Audio Server Base (H.248.9, [6]) | ALL |  |
| Aas Digit collection (H.248.9, [6]) | ALL |  |
| AAS Recording package (H.248.9, [6]) | ALL |  |
| AAS segment management (H.248.9, [6]) | ALL |  |

## 5.15 	Mandatory Support of SDP and Annex C Information Elements

The v=, o=, s=, m=, c=, t=, a= and b= lines of the SDP [20] syntax shall be supported. All other lines should be ignored if received.

Table 5.15.1

| Supported Annex C and SDP information elements: |
| --- |
| Information Element | Annex C Support | SDP Support |
| Protocol version (v=) | Not Supported | The protocol version (v=) line contains a single field: v= <version> and shall be used in accordance with RFC 2327 [20] (i.e. v=0). |
| Origin (o=) | Not Supported | The origin line consists of 6 fields: o= <user name> <session ID> <version> <network type> <address type> <address>. The MRFC is not required to supply this line but shall accept it. The MRFP should populate this line as follows or use the value received from the MRFC: - <user name> should contain an hyphen - <session ID> and <version> should contain one or mode digits as described in RFC 2327 [20] - <network type> shall be set to IN - <address type> shall be set to IP4 or IP6 The Address Type shall be set to “IP4" or “IP6” depending on the addressing scheme used by the network to which the MRFP is connected. - <address> should contain the fully qualified domain name of the gateway. |
| Session Name (s=) | Not Supported | The session name (s=) line contains a single field: s= <session-name>. The MRFC is not required to supply a session name but shall accept one. This line may be used to convey correlation information for use in CDRs. The MRFP shall use an hyphen "-" as a session name or the value received from the MRFC. |
| Connection data (c=) | Not Supported | The connection data line consists of 3 fields: c= <network-type> <address-type> <connection-address> - The <network-type> shall be set to “IN”. - The <address-type> shall be set to “IP4" or “IP6” depending on the addressing scheme used by the network to which the MRFP is connected. - The <connection-address> sent by the MRFC in the remote descriptor is the address to which the MRFP shall send the media flows. - The <connection-address> sent by the MRFC in local descriptors may be a unicast IPv4 or IPv6 address or it may be wildcarded to allow the MRFP to choose an address. In the second case, MGs shall fill this field with a unicast IP address at which they will receive the media stream. Thus a TTL value shall not be present and a "number of addresses" value shall not be present. The field shall not be filled with a fully-qualified domain name instead of an IP address. When the <connection address> is wildcarded (i.e. choose wildcard) by the MRFC, the MRFP allocates an IP address based on the address type. The addressing space for which this address is taken may depend on the termination ID supplied by the MRFC. |
| Media announcements (m=) | Not Supported | Media Announcements (m=) lines consist of 3 fields: m= <media> <port> <transport> <format> - The <media> field shall be set to "audio" - The <port> field in remote descriptors is provided by the MRFC and represents the port to which the MRFP shall send the media flows. - The <port> field in local descriptors may be provided by the MRFC or wildcarded (i.e. choose wildcard) to allow the MRFP to choose a value for the port on which it wishes to receive the media stream - The <transport> field shall be set to "RTP/AVP". - The <format> field may be explicitly supplied by the MRFC, wildcarded or overspecified. If the MRFC wishes to request the MRFP to choose which media formats it wishes to use for the call then the MRFC shall provide a "$" wildcard. If the MRFC wishes to suggest that the MRFP selects a media format from a list of possible media formats then it shall provide a list of appropriate media types in accordance with SDP. All conforming gateways shall support at least format ”8” for RTP/AVP (i.e. G.711 A-Law). Dynamic payloads shall not be used when a static RTP/AVP payload value is defined in RFC 3551[21]. |
| Bandwidth (b=) | Not Supported | The Bandwitdh (b=) line consists of 2 fields: b= <modifier>: <bandwidth-value> Bandwidth information shall be supplied by the MRFC if the required bandwidth cannot be immediately derived from the information contained in the m= line. If absent, the MRFP shall assume a reasonable default bandwidth value for well-known codecs and shall provide this value in the response sent to the MRFC. The Modifier field shall be set to “AS”. The Bandwidth Value field shall be set to the maximum bandwidth requirement of the media stream in kbit/s. The bandwidth value shall take into account all headers down to the IP layer, including a 5% bandwidth for RTCP packets. |
| Time (t=) | Not Supported | The time (t=) line consists of two fields: t= <start-time> <stop-time>. This line is ignored by both the MRFC and the MRFP if received in local and remote descriptors. The MRFC is not required to supply a time description but shall accept one. When supplied, this line shall be set to 0 0. |
| Attributes (a=) | Not Supported | Attributes (a=) lines consist of two fields: a= <attribute>: <value> One or more of the "a" attribute lines specified below may be included, depending on the payload type. An attribute line not specified below should not be used. Only the following attributes are understood by the MRFP. Other attributes are ignored. a= rtpmap: <payload type> <encoding name>/<clock rate> [/<encoding parameters>] a= fmtp:<format> <format specific parameters> a= ptime: <time> |

## 5.16 	Procedures

Procedures for ephemeral H.248 Terminations (here IP only) are described in section 6.

# 6.		Procedures

## 6.1		General Procedures

Media Resource Function Processors shall discard packets with RTP payload types (PT) that do not match the Local Descriptor contents.

NOTE 1:	Besides an incorrect RTP PT field might be also other reasons for discarding packets (invalid SSRC field, invalid CRC …).

NOTE 2:	The MRFP has the option to collate statistics on discarded packets.

When sending packets from a termination, Media Resource Function Processors shall use the address and port in the Local Descriptor as a source address and port.

## 6.2	Use of Voice Codecs

### 6.2.1	Comfort Noise Insertion and Silence Suppression for Voice Codecs

If a codec has built-in support for silence suppression and comfort noise insertion, the activation or deactivation of these features shall be indicated using the a= line according to RFC 3551 [21] and RFC 3555 [24].

If the selected codec does not have built in support for silence suppression and comfort noise (CN) insertion, the CN payload code of RFC 4040 [23] may be included in the media description.

E.g (for G.711):

v= 0

c= IN <address type> <connection address>

m = audio <port number> RTP/AVP 0 13

a= ptime: 10

If the CN payload is included in the Local Descriptor, the MRFP shall be prepared to received CN packets during silence periods.

If the CN payload is included in the Remote Descriptor, the MRFP shall send CN packets during silence periods.

Comfort noise analysis, voice activity detection and discontinuous transmission algorithms are outside the scope of this specification.

### 6.2.2		DTMF Transmission

When a G.711 codec is used, Media Resource Function Processors shall be able to generate, detect and forward DTMF tones inband.

When other codecs are used, the MRFC should request the use of the procedures defined in RFC 2833 [22] to send and receive DTMF tones.

If the Local Descriptor sent by the MRFC includes the support for RFC 2833, Media Resource Function Processors shall be prepared to receive DTMF tones in the form of named events and relay the appropriate audio signal to the physical terminations.

If the Remote Descriptor indicates that RFC 2833 is supported, Media Resource Function Processors shall be prepared to relay in the form of named events, any DTMF tone received from the physical terminations.

A Dynamic Payload type shall be used to indicate support of RFC 2833 for DTMF relay.

Example

v= 0

c= IN <address type> <connection address>

m= audio <port number> RTP/AVP 18 110

a= ptime: 10

a= rtpmap: 110 telephone-event/8000

a= fmtp: 110 0-15

### 6.2.3	Support of G.711 variants

#### 6.2.3..1	G.711 Encoding Law

Media Resource Function Processors conforming to this specification are required to support G.711 A-Law and may also support μ-Law in order to avoid call failure or transcoding in case the remote entity supports μ-Law only.  How and where to perform transcoding in IP networks in case both terminals/gateways do not support the same variant is outside the scope of this profile.

#### 6.2.3.2	G.711 Silence Suppression Mode

G.711-over-IP may be operated with or without silence suppression. In case of silence suppression, comfort noise generation shall be based on ITU-T Recommendation G.711 Appendix II [16]. These features may be enabled/disabled on a per session basis, using the procedure described in section 6.4.

#### 6.2.3.3	G.711 Packet Loss Concealment

G.711-over-IP may be operated with or without error loss concealment. Typically is that decision dependent on the IP packet loss rate conditions. G.711 error loss concealment is based on RTP packet granularity, therefore called as packet loss concealment (PLC). ITU-T Recommendation G.711 Appendix I [15] provides a framework for G.711 PLC mode.

## 6.3	Procedures for basic user interaction

User Interaction procedures are implemented by creating a context with an ephemeral termination representing the media flow to/from the user involved in the interaction procedure.

Signals representing tones and announcements are applied to this termination and played towards the exterior of the context. Events representing DTMF digits are detected on this termination.

## 6.4	Procedures for advanced user interaction

User Interaction procedures are implemented by creating a context with a single ephemeral termination representing the media flow to/from the user involved in the interaction procedure.

Signals representing tones and announcements are applied to this termination and played towards the exterior of the context.

Events representing DTMF digits or recognised speeched segments are detected on this termination.

Voice-messaging services are implemented by applying the playrec signal from the AAS Recording package and detecting related event on this termination.

## 6.5	Procedures for conferencing

Conference services are implemented by creating H.248 contexts with the appropriate number of terminations using native H.248 mixing capabilities. Each conference participant is represented by an ephemeral termination.

Floor control procedures are implemented according to the procedures described in H.248.19 [11].

## 6.6.	Procedures for transcoding

On receipt of a transcoding request for a two-party session between A and B, the internal MRFC shall request the MRFP to create a context with one ephemeral termination representing the A party (Ta) and one ephemeral termination representing the B party (Tb).

Remote and Local Descriptors shall be populated as follows:

The Remote Descriptor for termination Ta shall be set according to the SDP Offer initially received from the A party.

The Remote Descriptor for termination Tb shall be set according to the SDP Answer received from the B party.

The media format in the Local Descriptor for termination Ta shall be set according to the SDP Offer initially received from the A party. The IP address and port shall be wildcarded.

The media format in the Local Descriptor for termination Tb shall be set according to the SDP Answer received from the B party. The IP address and port shall be wildcarded.

The value of the Local Descriptor returned by the MRFP for the termination Ta shall be sent as an SDP Answer to the A party (via the S-CSCF/AS).

The value of the Local Descriptor returned by the MRFP for the termination Tb shall be sent as a new SDP Offer to the B party (via the S-CSCF/AS).

The MRFC is responsible for sending the SDP information in SIP messages that are compatible with the state of the SIP dialogue.

# 7.	MRFP and MRFC Management

## 7.1		Overload Control

MRFP overload control procedures are supported using the Overload Control package (H.248.11).

Editor's note: Use of the Detailed Congestion Reporting  package (H.248.32) for reporting congestion of specific specialised resources requires further studies.

7.2			IP QoS Control and Monitoring

The quality of service (QoS) of network connections can be monitored using the quality alert event of the network package. It is up to the MRFC to set the threshold value that will trigger the notification of this event. The threshold value is expressed as a percentage of measured quality loss. The Media Gateway does this by taking into account packet loss, jitter and delay, according to a provisioned algorithm. The Quality Alert Ceasing event of the Quality Alert Ceasing package enables the Media Gateway to notify the MRFC when the network connections return to an acceptable quality.

Annex <X> (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| Aug 2005 | CT4#29 | C4-051081 |  |  | TS 29.333 v0.1.0 | 0.0.0 | 0.1.0 |

# Text boxes

Scope of this specification