Joint-Working-Group (Parlay, ETSI TISPAN Project OSA, 3GPP CT5)	(C5-070559

Meeting CT5#40, 6 - 8 August 2007, Trondheim, NORWAY

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 29.198-15 | CR | 0013 | ( rev | - | ( Current version: | 7.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Clarify address and address range descriptions to prevent portability issues for OSA/Parlay clients |
| --- | --- |
| Source to WG: ( | AePONA |
| Source to TSG: ( | C5 |
| Work item code: ( | OSA3 |  | Date: ( | 05/09/2007 |
| Category: ( | A |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | Provide a clear explanation for address and address range descriptions in order to prevent portability issues for OSA/Parlay clients. |
| Summary of change: ( | The current Multi-media Messaging (MM) API specification contains a number of sections describing an address and address range where it is unclear whether source or destination address is being described. It is also unclear for createNotification and event criteria description what is meant by source or destination address, as this depends on whether the perspective is network or application centric. This CR proposes to add clarity to descriptions of address and address range in order to promote portability for Parlay/OSA applications using the Multi Media Messaging SCF. |
| Consequences if ( not approved: | Different intrepretation of address description may cause portability issues for Parlay/OSA applications. |
| Clauses affected: ( | 10, 11.2.2, 11.2.5 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( | R7 Mirror CR of C5-070529 |

1st Modified Section

# Multi-Media Messaging Service Properties

The following table lists properties relevant for the Multi-Media Messaging API.

| Property | Type | Description |
| --- | --- | --- |
| P_MESSAGE_DELIVERY_TYPE | STRING_SET | Specifies the message delivery capabilities which the SCS supports. Values are defined by TpMessageDeliveryType. |
| P_PUT_MESSAGE_FOLDER_TO_SEND | STRING_SET | Identifies the folder in the mailbox into which messages should be placed in order to be sent. |

The previous table lists properties related to capabilities of the SCS itself. The following table lists properties that are used in the context of the Service Level Agreement, e.g. to restrict the access of applications to the capabilities of the SCS.

| Property | Type | Description |
| --- | --- | --- |
| P_NOTIFICATION_ADDRESS_RANGES | XML_ADDRESS_RANGE_SET | Indicates for which addresses notifications may be set. This applies a restriction to addresses the SCS can request notification from. More than one range may be present. |
| P SOURCE_ADDRESS_RANGES | XML_ADDRESS_RANGE_SET | Indicates which addresses a client application on the SCS is allowed to use for its own identity, as used when sending a message to a destination or in criteria for notification of new message arrived. |

Next Modified Section

### TpMessagingEventCriteria

Defines the Tagged Choice of Data Elements that specify the criteria for an event notification to be generated.

|  | Tag Element Type |  |
| --- | --- | --- |
|  | TpMessagingEventName |  |

| Tag Element Value | Choice Element Type | Choice Element Name |
| --- | --- | --- |
| P_EVENT_MSG_NAME_UNDEFINED | NULL | Undefined |
| P_EVENT_MSG_NEW_MAILBOX_MESSAGE_ARRIVED | TpNewMailboxMessageArrivedCriteria | EventNewMailboxMessageArrived |
| P_EVENT_MSG_NEW_MESSAGE_ARRIVED | TpNewMessageArrivedCriteria | EventNewMessageArrived |
| P_EVENT_MSG_STATUS_REPORT_ARRIVED | TpAddressRange | EventNewMessageStatusReportArrived |

The address range defined for EventNewMessageStatusReportArrived refers to the addresses of devices in the network to which the client application on the SCS has sent or intends to send a message.

Next Modified Section

### TpNewMessageArrivedCriteria

Defines the Sequence of Data Elements that specify the criteria for a New Message Arrived event, for messages which are received outside the context of a mailbox.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| SourceAddress | TpAddressRange | Defines the source address for which the notification is requested. The source is the originator of the message, and is a device in the network. |
| DestinationAddress | TpAddressRange | Defines the destination address or address range for which the notification is requested. The destination is the address identity for the client application on the SCS. |
| CreateMultiMediaMessagingSession | TpBoolean | Used by the application to indicate if the SCF should create an instance of IpMultiMediaMessaging upon receipt of an event which matches these criteria. |

End of modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.