Joint-Working-Group (Parlay, ETSI TISPAN Project OSA, 3GPP CT5)	(C5-070533

Meeting CT5#40, 6 - 8 August 2007, Trondheim, NORWAY

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 29.199-15 | CR | 0002 | ( rev | - | ( Current version: | 7.1.2 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correct in Message Broadcast the notification mechanism for Delivery Receipt to include a start and stop in the manager interface - Align with 29.199-04/5 Short / Multimedia messaging |
| --- | --- |
| Source to WG: ( | ETRI (JeongHwan Kim) |
| Source to TSG: ( | C5 |
| Work item code: ( | OSA7 |  | Date: ( | 05/09/2007 |
| Category: ( | F |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | Correct the notification mechanism for Delivery Receipting to include a start and stop in the manager interface. |
| Summary of change: ( | Align Message broadcast with the CT#36 approved 29.199-04 CR0015, 29.199-05 CR0013 applied to the Messaging APIs (Short messaging, Multimedia messaging), start and stop operations for delivery receipt notifications are added on the manager interface. |
| Consequences if ( not approved: | Inconsistency with other messaging API specifications |
| Clauses affected: ( | 4, 8.1.1, 8.1.1.1, 8.2.1, New 8.3 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( | Align with the CT#36 approved 29.199-04 CR0015, 29.199-05 CR0013 |

1st Modified Section

# 4	Detailed service description

Message broadcast is a functionality that allows an application to send messages to all the fixed or mobile terminals in a specified geographical area.

Message broadcast provides operations for sending a broadcast message to the network and a polling mechanism for monitoring the delivery status of a sent broadcast message. It also provides an asynchronous notification mechanism for broadcast delivery status. In addition, a mechanism is provided to start and stop the notification of delivery receipts.

There are various use cases of using Message Broadcast Web Service including the commercial application. This Web Service could be also used for non-commercial purpose as follows:

Next Modified Section

### 8.1.1	Operation: sendBroadcastMessage

The application invokes the sendBroadcastMessage operation to send a broadcast message into the designated area(s), respectively specified by the message and the broadcastArea.

If message is longer than the maximum supported length in the network, the message content will be sent as several concatenated messages. E.g. a CBS message consists of several CBS pages(up to 15 pages) which comprises of 82 octets, which, using the default character set, equates to 93 characters (3GPP TS 23.041 [7]).

broadcastArea is an area or a set of areas which are the representation of the geographical area(s) in which a message is to be delivered. Areas can be described as alias name or a graphical notation such as circle and polygon. The alias name shall be determined at the provisioning step and understood by both application and network. In case of using a graphical notation, maximum and minimum size of an area can be restricted by the network.

Areas shall be covered by the mobile or wireline network. A message cannot be delivered to the terminals which are out of network coverage even though the application has indicated the area(s) in the send operation. In this case, Message Broadcast Web Service will generate a ServiceException(SVC 0300).

The application can also indicate optional parameters as follows:

- senderName specifies the sender's name, i.e. the string that is displayed on the user's terminal as the originator of the message.

- charging specifies the charging information.

- priority specifies the priority of message.

- deliveryTime specifies the time at which message delivery should be initiated by the send operation. By using this parameter, the Web Services could achieve an overload safety through the scheduling of broadcasts at non-peak time.

- totalBroadcasts specifies how many times the message should be broadcasted to each of the designated area(s).

- interval specifies the time duration between the broadcasts. The minimum interval should be restricted by the network capabilities.

- receiptRequest is optional and is specified when the application requires to receive notification of the status of the broadcast message delivery. It is a SimpleReference structure that indicates the application endpoint, interface used for notification of delivery receipt and a correlator that uniquely identifies the sending request.

-	If the notification mechanism is not supported by a network, a ServiceException (SVC0283) will be returned to the application and the message will not be sent out to the area(s) specified.

-	The correlator provided in the receiptRequest must be unique for this Web Service and application at the time the notification is initiated, otherwise a ServiceException (SVC0005) will be returned to the application.

-	Notification to the application is done by invoking the notifyBroadcastDeliveryReceipt operation at the endpoint specified in receiptRequest.

-	This optional message part is not used (or will be overridden) in case the startDeliveryReceiptNotification operation is used when the application requires to receive delivery receipt notifications. This is to avoid overlapping criteria.

- requestIdentifier is specified in the response message associated with each send operation.  The application can use it to invoke the getBroadcastStatus operation to poll for the delivery status.

Next Modified Section

#### 8.1.1.1	Input message: sendBroadcastMessageRequest

| Part name | Part type | Optional | Description |
| --- | --- | --- | --- |
| broadcastArea | BroadcastArea[1..unbounded] | No | geographical area(s) to which a message is desired to be broadcasted |
| senderName | xsd:string | Yes | If present, it indicates the sender's name of broadcast message, i.e. the string that is displayed on the user's terminal as the originator of the message |
| charging | common:chargingInformation | Yes | Charge to apply to this message |
| message | xsd:string | No | Text to be sent in Message Broadcast |
| priority | MessagePriority | Yes | Priority of the message. If not present, the network will assign a priority based on an operator policy. |
| deliveryTime | xsd :dateTime | Yes | If present, it specifies the time to initiate message broadcast in the network. If not present, message is sent immediately |
| totalBroadcasts | xsd :int | Yes | The number of broadcasts. If not present, default value is 1. |
| interval | common:TimeMetric | Yes | The time difference between consecutive broadcasts. It presents only if totalBroadcasts > 1 |
| receiptRequest | common :SimpleReference | Yes | It defines the application endpoint, interfaceName and correlator that will be used to notify application when the message has been sent out to the designated area or if delivery is impossible. It is not used (or will be overridden) in case startDeliveryReceiptNotification operation is used. |

Next Modified Section

### 8.2.1	Operation: notifyBroadcastDeliveryReceipt

The notifyBroadcastDeliveryReceipt operation must be implemented by a Web Service at the application side if it requires notification of broadcast result receipt. It will be invoked by the Parlay X server to notify the application when a message sent by an application has been handed over to messaging center like CBC and subsequently sent out to designated area(s) or if delivery is impossible. The notification will occur if and only if the status value of the sent message is Broadcasted or BroadcastImpossible and the application has specified interest in notification when sending a broadcast message  using one of the following mutually exclusive mechanisms:

- by specifying the optional receiptRequest part.  The correlator returned corresponds to the identifier specified by the application in the receiptRequest of the original sendBroadcastMessage request.

- by invoking the startDeliveryReceiptNotification operation requesting to receive delivery receipt notifications. The correlator returned corresponds to the identifier specified by the application in the reference of the original startDeliveryReceiptNofitication request.

When a broadcast message is sent to multiple geographical areas, the notification from the server will send notification for each area as and when a broadcast message is successfully sent out to the area.

Next Modified Section

## 8.3	Interface: MessageBroadcastNotificationManager

The message broadcast notification manager enables applications to set up and tear down notifications for broadcast messages, online.

### 8.3.1	Operation: startDeliveryReceiptNotification

Start notifications to the application for delivery receipts. The reference will be where to sned the delivery receipts. The notifyBroadcastDeliveryReceipt method (see clause 8.2.1) must be implemented by a Web Service at the application side if it requires notification of broadcast message delivery receipt. When the startDeliveryReceiptNotification is supported by the Service Provider, its use overrides the delivery receipting mechanism supported in the SendBroadcastMessage API (see clause 8.1:  sendBroadcastMessage operation).

#### 8.3.1.1	Input message: startDeliveryReceiptNotificationRequest

| Part name | Part type | Optional | Description |
| --- | --- | --- | --- |
| reference | common:SimpleReference | No | Notification endpoint definition |
| filterCriteria | xsd:string | No | The filterCriteria will allow the service to filter flexibly. One example would be for service provider to filter only successful final status. This however is implementation specific and will be left to the Service Provider. |

#### 8.3.1.2	Output message: startDeliveryReceiptNotificationResponse

| Part name | Part type | Optional | Description |
| --- | --- | --- | --- |
| None |  |  |  |

#### 8.3.1.3	Referenced faults

ServiceException from [6]:

- SVC0001 - Service error.

- SVC0002 - Invalid input value.

- SVC0005 - Duplicate correlator

- SVC0008 - Overlapping Criteria

- SVC0283 – Delivery Status Notification not supported

PolicyException from [6]:

- POL0001 - Policy error.

### 8.3.2	Operation: stopDeliveryReceiptNotification

The application may end delivery receipt notification using this operation.

#### 8.3.2.1	Input message: stopDeliveryReceiptNotificationRequest

| Part name | Part type | Optional | Description |
| --- | --- | --- | --- |
| correlator | xsd:string | No | Correlator of request to end |

#### 8.3.2.2	Output message: stopDeliveryReceiptNotificationResponse

| Part name | Part type | Optional | Description |
| --- | --- | --- | --- |
| None |  |  |  |

#### 8.3.2.3	Referenced faults

ServiceException from [6]:

- SVC0001 - Service error.

- SVC0002 - Invalid input value.

PolicyException from [6]:

- POL0001 - Policy error.

End of modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.