3GPP TSG-CT WG6 Meeting #91	C6-180688

# West Palm Beach (USA), 27 - 30 November 2018

| CR-Form-v11.1 |
| --- |
| CHANGE REQUEST |
|  | 31.102 | CR | 0826 | rev | 2 | Current version: | 15.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps | X | ME | X | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | SUCI EF_CalcInfo access clarification |
| --- | --- |
| Source to WG: | Gemalto |
| Source to TSG: | C6 |
| Work item code: | 5GS_Ph1-CT |  | Date: | 2017-11-29 |
| Category: | F |  | Release: | Rel-15 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The requirement “If "SUCI calculation is to be performed by the USIM" (i.e. service n°124 is "available" in EFUST and service n°125 is "available" in EFUST), this file shall not be available to the ME.” is unclear on whether the file may be present or not. In some use cases, the file may be present but not available to the ME in the meaning that it is not readable by the ME: At early deployment stage, the operator decide to let the ME perform the SUCI calculation Later, the operator decides to activate the calculation in the USIM, by updating via OTA the UST file and the EF_SUCI_Calc_Info file so that it becomes readable by the ME. Thus from the operational point of view, it is more efficient to deploy the USIM with an EF_SUCI_Calc_Info fully personalized but not readable by the ME. |
| Summary of change: | -Change the location of a presentation sentence -Add a note clarifying the meaning of file “not available to the ME” |
| Consequences if not approved: | It is unclear whether the file can be present or not when the SUCI calculation is to be performed by the USIM. |
| Clauses affected: | 4.4.11.8 |
|  | Y | N |  |  |
| Other specs |  | x | Other core specifications | TS/TR ... CR ... |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

***** Begin change *****

### 4.4.11.8	EFSUCI_Calc_Info (Subscription Concealed Identifier Calculation Information EF)

If "SUCI calculation is to be performed by the ME" (i.e. service n°124 is "available" in EFUST and service n°125 is not "available" in EFUST), this file shall be present. This EF contains information needed by the ME for the support of subscription identifier privacy as defined in 3GPP TS 33.501[105].

If "SUCI calculation is to be performed by the USIM" (i.e. service n°124 is "available" in EFUST and service n°125 is "available" in EFUST), this file shall not be available to the ME.

If service n°124 is not "available" in EFUST, this file shall not be available to the ME.

Note:	How the file is made "not available to the ME" is implementation specific, e.g. the file may not be present, the file may be present but not readable by the ME, or the file may be present but deactivated.

| Identifier: '4F07' | Structure: transparent | Optional |
| --- | --- | --- |
| SFI: '07' |  |
| File size: X bytes (X ≥ 2) | Update activity: low |
| Access Conditions: READ PIN UPDATE ADM DEACTIVATE ADM ACTIVATE ADM |
| Bytes | Description | M/O | Length |
| 1 to Z | Protection Scheme Identifier List data object | M | Z bytes |
| Z+1 to Y+Z | Home Network Public Key List data object | C | Y bytes |
| X-W+1 to X | Routing Information TLV data object | C | W bytes |

Editor’s Note: The presence condition of Routing Information TLV data object is FFS.

-	Protection Scheme Identifier List data object.

Contents:

This data object shall always be present. If Protection Scheme Identifier List data object length is not zero, this data object contains a list of the Protection Scheme Identifier and the corresponding Key Index. The first Protection Scheme Identifier entry has the highest priority and the last Protection Scheme Identifier entry has the lowest priority. The Key Index value indicates the position of the Home Network Public Key in the Home Network Public Key List, that is applicable to the Protection Scheme.

Coding:

| Description | Value | M/O/C | Length (bytes) |
| --- | --- | --- | --- |
| Protection Scheme Identifier List data object tag | 'A0' | M | 1 |
| Protection Scheme Identifier List data object length | L1 | M | Note 1 |
| Protection Scheme Identifier 1 (Highest priority) | -- | O | 1 |
| Key Index 1 | -- | C (Note 2) | 1 |
| Protection Scheme Identifier 2 | -- | O | 1 |
| Key Index 2 | -- | C (Note 2) | 1 |
| … | … | … | … |
| Protection Scheme Identifier N (Lowest priority) | -- | O | 1 |
| Key Index N | -- | C (Note 2) | 1 |
| Note 1: The length is coded according to ISO/IEC 8825-1 [35] Note 2: This field is present only if the corresponding Protection Scheme Identifier field is present |

The Protection Scheme Identifier represents a protection scheme as described in 3GPP TS 33.501 [105] and it is coded in one byte as follows:

|  |  | b8 | b7 | b6 | b5 | b4 | b3 | b2 | b1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | Protection Scheme identifier coded as described in 3GPP TS 33.501 [105] |
|  |  |  |  |  |  |  |  |  |  | RFU, bit = 0 |

Editor’s Note: The format may need to be updated depending on the outcome of 3GPP TS 23.003.

The Key Index is coded in one byte such that its value indicates the position of the Home Network Public Key in the Home Network Public Key List data object, that is applicable to the Protection Scheme. A Key Index with a value of "1" refers to the first Network Public Key entry in the Home Network Public Key List, and so on. A Key Index with a value of "0" indicates that there is no Home Network Public Key associated with that Protection Scheme (e.g., in the case of null-scheme).

-	Home Network Public Key List data object.

Contents:

This data object contains a list of the Home Network Public Key and the corresponding Home Network Public Key Identifier that shall be used by the ME to calculate the SUCI.

This data object may not be present if none of the protection scheme profiles identified by the Protection Scheme Identifiers included in the Protection Scheme Identifier List data object use the Home Network Public Key (e.g. null-scheme). If this data object is present, it shall contain at least one Home Network Public Key and the corresponding Home Network Public Key Identifier.

Coding:

| Description | Value | M/O/C | Length (bytes) |
| --- | --- | --- | --- |
| Home Network Public Key List data object | 'A1' | C | 1 |
| Home Network Public Key List data object length | L1 | C | Note 1 |
| Home Network Public Key 1 Identifier tag | '80' | C | 1 |
| Home Network Public Key 1 Identifier length | L2 | C | Note 1 |
| Home Network Public Key 1 Identifier | -- | C | L2 |
| Home Network Public Key 1 tag | '81' | C | 1 |
| Home Network Public Key 1 length | L3 | C | Note 1 |
| Home Network Public Key 1 | -- | C | L3 |
| … | … | … | … |
| Home Network Public Key N Identifier tag | '80' | O | 1 |
| Home Network Public Key N Identifier length | L4 | O | Note 1 |
| Home Network Public Key N Identifier | -- | O | L4 |
| Home Network Public Key N tag | '81' | O | 1 |
| Home Network Public Key N length | L5 | O | Note 1 |
| Home Network Public Key N | -- | O | L5 |
| Note 1: The length is coded according to ISO/IEC 8825-1 [35] |

Editor’s Note: Coding of the Home Network Public Key Identifier and Home Network Public Key are FFS.

-	Routing Information TLV data object.

Contents:

his data object contains Routing Indicator that allows together with the MCC and MNC to route network signalling with SUCI to AUSF and UDM instances capable to serve the subscriber, as specified in 3GPP TS 23.003 [25]. This data object may not be present in the case of null-scheme. If this data object is present, it shall have a valid Routing Indicator.

Coding:

| Description | Value | M/O/C | Length (bytes) |
| --- | --- | --- | --- |
| Routing Information TLV data object tag | 'A2' | C | 1 |
| Routing Information TLV data object length | L1 | C | Note 1 |
| Routing Information TLV data object value | -- | C | L1 |
| Note 1: The length is coded according to ISO/IEC 8825-1 [35] |

Editor’s Note: Coding of the above data object TLV value is FFS.

***** End of change *****