3GPP TSG CT WG6 Meeting #91	C6-180614

# West Palm Beach, US, 27-30 November 2018

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 31.103 | CR | 0128 | rev | - | Current version: | 15.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps | X | ME | X | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Default QoS flow usage restriction policy |
| --- | --- |
| Source to WG: | China Mobile |
| Source to TSG: | CT6 |
| Work item code: | 5GS_Ph1-CT |  | Date: | 2018-11-26 |
| Category: | F |  | Release: | Rel-15 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The “Default_QoS_Flow_usage_restriction_policy” MO was introduced (see TS 24.167 CR 0202) to avoid undesired usage of default 5G QoS flow. The corresponding node stored in the UICC is still missing. |
| Summary of change: | Add a new node under EFIMSConfigData indicating the default QoS flow usage restriction policy. |
| Consequences if not approved: | Unpredictable UE behavior leading to unconsistent user experience. |
| Clauses affected: | 4.2.18 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS 24.229 CR 6263 |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

********* First Change *********

### 4.2.18	EFIMSConfigData (IMS Configuration Data)

If service n°18 is "available", this file shall be present.

This EF contains the IMS configuration data object as specified in 3GPP TS 24.167 [35].

| Identifier: '6FF8' | Structure: BER-TLV | Optional |
| --- | --- | --- |
| File size: X bytes | Update activity: low |
| Access Conditions: READ PIN UPDATE ADM DEACTIVATE ADM ACTIVATE ADM |
| Bytes | Description | M/O | Length |
| N/A | IMS configuration data encoding | M | 3 bytes |
| N/A | IMS configuration data | O | Y bytes |

IMS configuration data object tags:

| IMS configuration data objects | Tag Values |
| --- | --- |
| IMS configuration data encoding | '80' |
| IMS configuration data | '81' |

Coding of the IMS configuration data encoding object

Contents:

Indicates the coding used for all the IMS configuration management objects stored in the EFIMSConfigData.

Coding:

A value of '00' indicates the XML format described in 3GPP TS 24.167 [35]. All other values are reserved.

Unused bytes shall be set to 'FF'.

IMS configuration data object:

# Coding of the IMS Configuration data object

| Length | Description | Value | Status |
| --- | --- | --- | --- |
| 1 byte | IMS configuration data object Tag | '81' | M |
| X byte | IMS configuration data object Length | Y | M |
| Y bytes | IMS configuration data | - | M |

Contents:

The IMS configuration data can contain the following nodes and associated parent node from 3GPP TS 24.167 [35]:

1	Default_EPS_bearer_context_usage_restriction_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in 3GPP TS 24.229 [32] subclause L.2.2.5.1D.

2	Media_type_restriction_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in 3GPP TS 24.229 [32] subclause 6.1.1.

3	Reliable_18x_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.4.2.

4	EPS_initial_attach_ConRefs node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause L.2.2.1.

5	Precondition_disabling_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.5A.

6	Timer_Emerg-reg leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.6.1.

7	EPC_via_untrusted_WLAN_mean_rekeying_time leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] Annex R.2.2.1.

8	EPC_via_untrusted_WLAN_NAT_keep_alive_time leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32]  Annex R.2.2.1.

9	EPC_via_untrusted_WLAN_timeout_period_for_liveness_check leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32]  Annex R.2.2.1.

10	Policy_on_local_numbers node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.2A.1.5A.

11	SMSoIP_usage_policy leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.341 [36]  subclause 5.2.1.3.

12	Estimated_P-CSCF_Recover_Time leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32]  subclause 5.72

13	IMS_Registration_Policy node as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32]  Annex B.3.1.0a and TS 24.229 [32]  Annex L.3.1.0a.

xx	Default_QoS_Flow_usage_restriction_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in 3GPP TS 24.229 [32] subclause U.2.2.5.1D.

Other nodes from 3GPP TS 24.167 [35] can be present in the IMS configuration data, however the ME shall ignore them.

Coding:

As specified in 3GPP TS 24.167 [35].

********* End of Changes *********