3GPP TSG-CT WG6 Meeting #91 	C6-180680

# West Palm Beach (FL), USA, 26-30 november 2018

| CR-Form-v11.1 |
| --- |
| CHANGE REQUEST |
|  | 31.103 | CR | 0129 | rev | 2 | Current version: | 15.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps | X | ME | X | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | New Timer for emergency call attempt in non-3GPP access |
| --- | --- |
| Source to WG: | Orange |
| Source to TSG: | C6 |
| Work item code: | TEI15 |  | Date: | 2018-11-28 |
| Category: | F |  | Release: | Rel-15 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) |
| Reason for change: | In the current request procedure for emergency sessions, emergency call over a non-3GPP access is possible when a 3GPP access is not available but there is no limitation for the UE to scan the cellular access before establishing the emergency session via WLAN when voice is available in this access. In CT1 (CR#6233 to TS.24.229) a new timer is defined with configurable values. Respective CR#0210 is the CR regarding configuring the timer under TS 24.167 3GPP IMS Management Object. *****ADDITIONNAL CHANGE**** By working in this CR, it has been identified a mistake introduced by a previous agreed CR (#0123 for rel-15 only C6-180053) which has deleted the wrong bullet. This is corrected in this CR. |
| Summary of change: | Addition of a new node under EFIMSConfigData to indicate the time for searching a 3GPP access usable for establishing an emergency call before performing the emergency call over the available non-3GPP access. *****ADDITIONNAL CHANGE**** Timer_Emerg-request leaf deleted by mistake instead of the Estimated_P-CSCF_Recover_Time leaf is re-introduced. |
| Consequences if not approved: | Not able to configure the UE of the time for searching a 3GPP access usable for establishing an emergency call before performing the emergency call over the available non-3GPP access. |
| Clauses affected: | 4.2.18 |
|  | Y | N |  |  |
| Other specs |  | x | Other core specifications | TS/TR ... CR ... |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

***** Next change *****

### 4.2.18	EFIMSConfigData (IMS Configuration Data)

If service n°18 is "available", this file shall be present.

This EF contains the IMS configuration data object as specified in 3GPP TS 24.167 [35].

| Identifier: '6FF8' | Structure: BER-TLV | Optional |
| --- | --- | --- |
| File size: X bytes | Update activity: low |
| Access Conditions: READ PIN UPDATE ADM DEACTIVATE ADM ACTIVATE ADM |
| Bytes | Description | M/O | Length |
| N/A | IMS configuration data encoding | M | 3 bytes |
| N/A | IMS configuration data | O | Y bytes |

IMS configuration data object tags:

| IMS configuration data objects | Tag Values |
| --- | --- |
| IMS configuration data encoding | '80' |
| IMS configuration data | '81' |

Coding of the IMS configuration data encoding object

Contents:

Indicates the coding used for all the IMS configuration management objects stored in the EFIMSConfigData.

Coding:

A value of '00' indicates the XML format described in 3GPP TS 24.167 [35]. All other values are reserved.

Unused bytes shall be set to 'FF'.

IMS configuration data object:

# Coding of the IMS Configuration data object

| Length | Description | Value | Status |
| --- | --- | --- | --- |
| 1 byte | IMS configuration data object Tag | '81' | M |
| X byte | IMS configuration data object Length | Y | M |
| Y bytes | IMS configuration data | - | M |

Contents:

The IMS configuration data can contain the following nodes and associated parent node from 3GPP TS 24.167 [35]:

1	Default_EPS_bearer_context_usage_restriction_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in 3GPP TS 24.229 [32] subclause L.2.2.5.1D.

2	Media_type_restriction_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in 3GPP TS 24.229 [32] subclause 6.1.1.

3	Reliable_18x_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.4.2.

4	EPS_initial_attach_ConRefs node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause L.2.2.1.

5	Precondition_disabling_policy node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.5A.

6	Timer_Emerg-reg leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.6.1.

7	EPC_via_untrusted_WLAN_mean_rekeying_time leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] Annex R.2.2.1.

8	EPC_via_untrusted_WLAN_NAT_keep_alive_time leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32]  Annex R.2.2.1.

9	EPC_via_untrusted_WLAN_timeout_period_for_liveness_check leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32]  Annex R.2.2.1.

10	Policy_on_local_numbers node and its descendant nodes as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.2A.1.5A.

11	SMSoIP_usage_policy leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.341 [36]  subclause 5.2.1.3.

12	Timer_Emerg-request leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32] subclause 5.1.6.8.1.

13	IMS_Registration_Policy node as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in TS 24.229 [32]  Annex B.3.1.0a and TS 24.229 [32]  Annex L.3.1.0a.

xx	Timer_Emerg_non3gpp leaf as described in 3GPP TS 24.167 [35]. Procedures for use of this policy are described in 3GPP TS 24.229 [32] Annex R.2.2.6.1 and W.2.2.6.1.

Other nodes from 3GPP TS 24.167 [35] can be present in the IMS configuration data, however the ME shall ignore them.

Coding:

As specified in 3GPP TS 24.167 [35].

***** End *****