| ETSI TC SCP Meeting #76 La Ciotat, France, 15-16 December 2016 | SCP(16)000249r1 |
| --- | --- |
| TC SCP CR-Form-v1.8.0 |
| CHANGE REQUEST |
| ( | 102 695-2 | CR | 044 | ( rev |  | ( Current version: | 11.0.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | smart card | X | terminal |  | server / network entity |  |  |  |
| Title: ( | Correction of test procedure in 5.6.4.4.2.3. |
| Source: ( | SCP |
| Work item name: ( | TEI10 |  | Date: ( | 16/12/2016 |
| Category: ( | F |  | Release: ( | REL-10 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. |  |
| TC SCP use of the status "Accepted" for change requests: At the TC SCP working group level, the status "Accepted" means that a change request is accepted for presentation to TC SCP Plenary. At the TC SCP Plenary level, the status "Accepted" means that a change request is accepted for implementation in the targeted specification. |
| Reason for change: ( | There is a typo of the type F test command. |
| Summary of change: ( | Correction of the step 4 in the test procedure. |
| Consequences if ( not accepted: | The specification might be misunderstood. |
| New tag value defined within the CR? |  | If ticked, add document number of related CR to TS 101 220: |  |
| Clauses affected: ( | 5.6.4.4.2.3 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Test specifications |  |
| Other comments: ( |  |

##### 5.6.4.4.2	Test case 1: RF error indicator

5.6.4.4.2.1	Test execution

Void.

5.6.4.4.2.2	Initial conditions

The host controller simulator is configured to support only the Type F RF gate.‬

For full power mode execution: HCI session initialization has been performed, the HCI interface is idle and the SWP interface is not DEACTIVATED.

For low power mode execution: the Host is not powered up.

At the end of the previous activation, the state of the card emulation pipe was open, and the MODE parameter was '02' (as set by the UICC).

5.6.4.4.2.3	Test procedure

| Step | Direction | Description | RQ |
| --- | --- | --- | --- |
| 1 | HCS(HUT | For full power mode execution: send EVT_FIELD_ON event. For low power mode execution: power up Host, activate SWP interface and establish SHDLC link. |  |
| 2 | HCS(HUT | Send the ISO/IEC 18092 [3] 212 kbps/424 kbps frames, where LEN is set to '37', CMD0 to 'D8', CMD1 to '00', and Byte 0 to Byte 51 to '02FE000000000000060708090A0B0C0D0E0F101112131415 161718191A1B1C1D1E1F202122232425262728292A2B2C2D2E2F3031', with EVT_SEND_DATA event in which RF error indicator is set to '01'. |  |
| 3 | HCS | Wait 1 s from the end of sending EOF in SWP frame in step 2. During this time HUT shall not send any ISO/IEC 18092 [3] 212 kbps/424 kbps frames. | RQ6 |
| 4 | HCS(HUT | Send the ISO/IEC 18092 [3] 212 kbps/424 kbps frames, where LEN is set to '37', CMD0 to 'D8', CMD1 to '00', and Byte 0 to Byte 51 to '02FE000000000000060708090A0B0C0D0E0F101112131415 161718191A1B1C1D1E1F202122232425262728292A2B2C2D2E2F3031', with EVT_SEND_DATA event in which RF error indicator is set to '00'. |  |
| 5 | HUT(HCS | Send the ISO/IEC 18092 [3] 212 kbps/424 kbps frames, where LEN is set to '37', CMD0 to 'D9', CMD1 to '01', and Byte 0 to Byte 51 to '02FE000000000000060708090A0B0C0D0E0F101112131415 161718191A1B1C1D1E1F202122232425262728292A2B2C2D2E2F3031', with EVT_SEND_DATA event. | RQ2, RQ4 |
| 6 | HCS(HUT | Send EVT_FIELD_OFF event. |  |

# Comments

Enter the specification number in this box. For example, 101 220. Do not prefix the number with anything . i.e. do not use "TS".

Enter the CR number here. This number is allocated by the WG and the ETSI support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://docbox.etsi.org/scp/scp/specs/ .

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the title of the related work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.