| 3GPP TSG GERAN Adhoc | Document | GAHW-000005 |
| --- | --- | --- |
| Munich, Germany 09 – 13 October, 2000 |  | Agenda item 6.1.1 |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 03.64 | CR | A | Current Version: | 8.6.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval |  |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME | x | UTRAN / Radio | x | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Ericsson | Date: | 2000-09-27 |
| Subject: | Introduction of the Network Assisted Cell Change feature in the stage 2 description |
| Work item: | GERAN Improvements 2 |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature | X |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 |  |
|  |  |  |  | Release 00 | X |
| Reason for change: | To shorten the cell re-selection outage time in packet transfer mode and to introduce a possibility to terminate ongoing packet transfer before the cell change is performed |
| Clauses affected: | 3.1, 6.5.6, 6.5.6.4 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

# 3	Abbreviations, symbols and definitions

## 3.1	Abbreviations

In addition to abbreviations in GSM 01.04 [1] and GSM 02.60 [2] the following abbreviations apply:

ARQ	Automatic Repeat reQuest

BCS	Block Check Sequence

BEC	Backward Error Correction

BH	Block Header

CCN	Cell Change Notification

CFCCH	Compact Frequency Correction Channel

CPAGCH	Compact Packet Access Grant Channel

CPBCCH	Compact Packet Broadcast Control Channel

CPCCCH	Compact Packet Common Control Channel

CPNCH	Compact Packet Notification Channel (for PTM-M on CPCCCH)

CPPCH	Compact Packet Paging Channel

CPRACH	Compact Packet Random Access Channel

CSCH	Compact Synchronization Channel

CS	Coding Scheme

CU	Cell Update

DTM	Dual Transfer Mode

EGPRS	Enhanced GPRS

FBI	Final Block Indicator

FH	Frame Header

GGSN	Gateway GPRS Support Node

HCS	Header Check Sequence

IR	Incremental Redundancy

LLC	Logical Link Control

MAC	Medium Access Control

MCS	Modulation and Coding Scheme

NCH	Notification Channel (for PTM-M on CCCH)

NSS	Network and Switching Subsystem

PACCH	Packet Associate Control Channel

PAGCH	Packet Access Grant Channel

PBCCH	Packet Broadcast Control Channel

PC	Power Control

PCCCH	Packet Common Control Channel

PDCH	Packet Data Channel

PDTCH	Packet Data Traffic Channel

PDU	Protocol Data Unit

PL	Physical Link

PNCH	Packet Notification Channel (for PTM-M on PCCCH)

PPCH	Packet Paging Channel

PRACH	Packet Random Access Channel

PSI	Packet System Information

PTCCH	Packet Timing Advance Control Channel

RLC	Radio Link Control

SGSN	Serving GPRS Support Node

SNDC	Subnetwork Dependent Convergence

TA	Timing Advance

TBF	Temporary Block Flow

TFI	Temporary Frame Identity

USF	Uplink State Flag

### 6.5.6	Cell Re-selection

NOTE:	The text in this subclause is informative. The normative text is in GSM 03.22 and GSM 05.08 [15]. Where there is a conflict between these descriptions, the normative text has precedence.

In GPRS Packet Idle and Packet Transfer modes, cell re-selection is performed by the MS, except for

- a class A MS (see GSM 02.60 [2] ) while in dedicated mode  in which case the cell is determined by the network according to the handover procedures;

- when the MS has been set in Network Control 2 (NC2) mode of operation by the network or

- when the MS is in Cell Change Notification (CCN) mode (see subclause 6.5.6.4).

The new cell re-selection criteria C31 and C32 are provided as a complement to the current GSM cell re-selection criteria. This provides a more general tool to make cell planning for GPRS as similar to existing planning in GSM as possible.C31 is a signal strength criterion used to decide whether prioritised cell re-selection shall be used. For cells that fulfil the C31 criterion, the cell with highest priority class shall be selected. If more than one cell has the highest priority, the one of those with the highest C32 value shall be selected. If no cell fulfils the C31 criterion, the one among all cells with the highest C32 value shall be selected.

C32 is an improvement of C2. It applies an individual offset and hysteresis value to each pair of cells, as well as the same temporary offsets as for C2. Additional hysteresis values apply for a cell re-selection that requires cell or routing area update.

Cell re-selection procedure apply to the MSs attached to GPRS if a PBCCH exists in the serving cell. If the PBCCH is not allocated, then the MS shall perform cell re-selection according to the C2 criteria.

In addition, the network may control the cell re-selection as described in subclause 6.5.6.3 and/or assist the MS in the cell re-selection procedure as described in subclause 6.5.6.4.

#### 6.5.6.1	Measurements for Cell Re-selection

The MS shall measure the received RF signal strength on the BCCH frequencies of the serving cell and the neighbour cells as indicated in the BA-GPRS list, and calculate the received level average (RLA) for each frequency, as specified in GSM 05.08 [15]. In addition the MS shall verify the BSIC of the cells. Only channels with the same BSIC as broadcast together with BA-GPRS on PBCCH shall be considered for re-selection.

A COMPACT capable MS shall in addition perform the above tasks for any CPBCCH, either transmitted in the serving cell or indicated, by way of frequency and time group in the BA-GPRS list.

Any cell having a CPBCCH indicated in the BA-GPRS list shall be time synchronized to that cell, as specified in GSM 05.10 [16].

When the number of downlink PDCHs assigned to certain types of multislot  MS (see GSM 05.02 [11] , annex B) does not allow them to perform measurements within the TDMA frame, the network shall provide measurement windows to ensure that the MS can perform a required number of measurements. The network shall provide periods of inactivity during a fixed allocation to allow the MS to make adjacent cell power measurements and BSIC detection.

#### 6.5.6.2	Broadcast Information

The PBCCH broadcasts GPRS specific cell re-selection parameters for serving and neighbour cells, including the BA (GPRS) list. A BA (GPRS) identifies the neighbour cells, including BSIC, that shall be considered for GPRS cell (re-selection (not necessary the same as for GSM in Idle or circuit switched mode)).

#### 6.5.6.3	Optional measurement reports and network controlled cell re-selection

It shall be possible for the network to order the mobile stations to send measurement reports to the network and to suspend its normal cell re-selection, and instead to accept decisions from the network. This applies to both Packet idle mode and Packet transfer mode.

The degree to which the mobile station shall resign its radio network control shall be variable, and be ordered in detail by the parameter NETWORK_CONTROL_ORDER.

Two sets of parameters are broadcast on PBCCH and are valid in Packet transfer and Packet idle modes respectively. NETWORK_CONTROL_ORDER can also be sent individually to an MS on PACCH, in which case it overrides the broadcast parameter.

Additionally, the network may request extended measurement reports from the MS and the reporting shall be maintained in packet idle mode. The reports may include interference measurements (see subclause 6.5.8.3.2). Measurement reports shall be sent individually from each MS as RLC transmissions.  Situations may appear where the network controlled cell re-selection procedures (NC1 or NC2 modes of operation) should not be used:

-	When a class A mobile station is simultaneously involved in a circuit switched service and in a GPRS transfer. In this case, handover for the circuit switched service has precedence over GPRS network controlled cell re-selection. -	When an MS is performing Anonymous Access, cell re-selection implying a change of Routeing Area results in the MS returning to the GPRS MM IDLE state, see GSM 03.60 [3]. Therefore, there might be cases where the network controlled cell re-selection would result in the Anonymous Access failing.

In that case, the MS shall stop sending measurement reports and ignore cell change orders.

#### 6.5.6.4	Network Assisted Cell Change

The Network Assisted Cell Change option adds a possibility to

- minimize the service outage time for an MS in the cell re-selection process,

- delay the cell re-selection until complete RLC-SDUs have been transferred.

This is achieved without forcing the MS into either mode NC1 or NC2 and consequently eliminates the need to load the radio path with measurement reports (see subclause 6.5.6.3).

The procedures related to Network Assisted Cell Change are a complement to mode NC0 and NC1 and are optional for both the MS and the network. If both nodes support the procedures, it is mandatory for the MS to use.

Network Assisted Cell Change consists mainly of two parts

- One part which manages the Cell Change Notification (CCN) procedure,

- One part that can assist the MS with system information for the target cell during ongoing packet transfer in the serving cell and before the cell change is performed.

The network indicates support of CCN on BCCH and PBCCH. The MS indicates support for CCN in MS capability information. If indicated or ordered by the network and when the MS is in packet transfer mode and in NC0 or NC1 mode, the MS shall enable CCN. When enabled, and when the criteria for cell re-selection is fulfilled, the MS shall enter CCN mode and notify the network. While in CCN mode the MS shall not change cell.

In the notification to the network, the MS shall report target cell identity, neighbour cell measurement results and which target cell system information has been received.

During the time the MS is in CCN mode, the network may send to the MS required system information for the target cell. The network may also any time when the MS is in Packet Transfer mode send system information for the neighbour cells which may be stored in the MS and used at a coming cell change. This will imply that an MS can immediately initiate access in the new cell when the cell change has been performed.

The MS shall leave the CCN mode when either

- The network responds with a continue or a re-select message or

- A certain time has elapsed or

- The TBF is released.

If the MS is in NC2 mode or in dedicated mode, the MS shall ignore the CCN mode.