3GPP TSG GERAN Ad Hoc	GAHW-000011
on Release 2000 and Beyond #2	Agenda Item 6.1.1

Munich, Germany

9-13 October 2000

Source:  Nortel Networks

A Comparison Between

GERAN Packet-Switched Call Setup Using SIP

and GSM Circuit-Switched Call Setup Using RIL3-CC,

RIL3-MM, RIL3-RR, and DTAP

Rev. 0.3

1	Introduction	3

2	List of Acronyms	3

3	Typical GSM Circuit-Switched Call Setup Sequence	4

3.1	Message Size Estimation	5

3.2	Layer 3 Trace	6

4	RRC Connection Messages and Direct Transfer Messages	8

4.1	UE Modes and RRC States	8

4.2	GPRS Attach	8

4.3	Primary PDP Context Activation	10

5	RSVP Messages	10

5.1	RSVP PATH Message	11

5.2	RSVP RESV Message	11

6	Typical SIP Call Setup Sequence	11

6.1	Message Size Estimation	14

6.2	Layer 3 Trace	14

7	Conclusions and Recommendations	14

8	References	14

APPENDIX A	TYPICAL GSM CIRCUIT-SWITCHED CALL SETUP SEQUENCE

APPENDIX B	LAYER 3 CC, MM, AND RR GSM CIRCUIT-SWITCHED MESSAGES: CALL SETUP

APPENDIX C	LAYER 3 TRACE FOR TYPICAL GSM CIRCUIT-SWITCHED CALL SETUP SEQUENCE

# Introduction

Previous versions of this contribution [1] discussed in detail the differences between the message sizes for a typical GSM circuit-switched call setup sequence and a typical SIP call setup sequence (viz., SIP to SIP call via a SIP proxy server).  For various reasons, the typical SIP call setup sequence in [1] did not account for the following messages that need to be transmitted over the air interface:

- RRC Connection messages (e.g., RRC Connection Request, Radio Bearer Setup, etc.) [2].

- Direct Transfer messages (e.g., NAS message comprising Service Request, Authentication and Ciphering Request, Secondary PDP Context Request, etc.) [3].

- RSVP messages [4].

- New draft SIP request methods and response codes (e.g., COMET, PRACK, 183 SESSION PROGRESS, etc.) [5], [6], [7].

This contribution attempts to assess the impact of these additional air interface messages.  Specifically, regarding the new draft SIP request methods and response codes (e.g., COMET, PRACK, 183 SESSION PROGRESS, etc.), a new typical SIP call setup sequence (viz., SIP to gateway call via a SIP proxy server) is also presented.

The contribution is organized as follows.  Section 2 gives a list of acronyms.  Section 3 discusses a typical GSM circuit-switched call setup sequence.  Section 4 discusses the RRC Connection messages and Direct Transfer messages that need to be exchanged between a mobile station (MS) and the network (both GERAN and Core Network) before SIP can be used to setup a GERAN packet-switched speech call.  Section 5 discusses RSVP.  Section 6 discusses a typical SIP call setup sequence (revised from [1] to include new draft SIP request methods and response codes).  Section 7 presents conclusions and recommendations.  Section 8 includes a list of references.  Appendices A through F provide supporting material.

# List of Acronyms

3GPP			3rd Generation Partnership Program

AGCH			Access Grant Channel

BCCH			Broadcast Control Channel

BSC			Base Station Controller

BTS			Base Transceiver Station

C				Conditional

CC				Call Control

CN				Core Network

CR				Carriage Return

CRLF			Carriage Return Line Feed

CSCF			Call Server Control Function

DTAP			Direct Transfer Application Part

EDGE			Enhanced Data Rates for Global Evolution

EGPRS		Enhanced General Packet Radio Service

FFS			For Further Study

FN				Frame Number

GERAN		GSM/EDGE Radio Access Network

GGSN			Gateway GPRS Support Node

GPRS			General Packet Radio Service

GSM			Global System for Mobile Communications

HTTP			HyperText Transfer Protocol

IE				Information Element

IP				Internet Protocol

LAPD			Link Access Protocol Data

LF				Line Feed

M				Mandatory

MM			Mobility Management

MS			Mobile Station

MSC			Mobile Switching Center

NBAP			Node B Application Part

O				Optional

PD				Protocol Discriminator

PDD			Post Dial Delay

PRACK		Provisional Response Acknowledgement

RACH			Random Access Channel

RIL3			Radio Interface Layer 3

RR				Radio Resource Management

RRC			Radio Resource Control

RSM			Radio Subsystem Management

RSVP			Resource reSerVation Protocol

SDCCH		Standalone Dedicated Control Channel

SDP			Session Description Protocol

SIP			Session Initiation Protocol

SS7			Signaling System 7

TCP			Transmission Control Protocol

UCS			Universal Character Set

UDP			User Datagram Protocol

UE				User Equipment

UTF			UCS Transformation Format

# Typical GSM Circuit-Switched Call Setup Sequence

GSM uses the SS7 protocols for its signaling.  The SS7 application layer has several sublayers specific to the GSM system.  The Radio Interface Layer 3 (RIL3) Radio Resource Management (RR) protocols establish and release radio connections between an MSC and various BSCs for the duration of a call.  The Radio Subsystem Management (RSM) protocol provides RR functions between the BTS and BSC.  The Direct Transfer Application Part (DTAP) protocols provide RR messages between the MS and MSC.  The distinction between DTAP and BSSMAP is provided by a Distribution protocol below them.

The RIL3 Mobility Management (MM) protocols deal with MS location management and security aspects of the system.  Functions performed under location management include location updating, IMSI attach, and periodic updating.  Some security aspect functions performed are authentication, TMSI reallocation, and identification.  The RIL3 Call Control Management (CC) protocols deal with mobile originating and terminating call establishment, supplementary services, and short messages.  All MM and CC functions reside in the MSC.  Therefore, neither the BSC nor the BTS interprets MM and CC messages.  Before exchanging messages between MM entities of the MS and the MSC, an RR connection needs to be established.

See [8], [9], [10], [11] for detailed information on RIL3-CC, RIL3-MM, RIL3-RR, and DTAP protocols.

Figure A1 in Appendix A illustrates a typical GSM circuit-switched call setup sequence (mobile originated).

## Message Size Estimation

Tables B1 through B14 in Appendix B provide details regarding the RIL3-CC, RIL3-MM, RIL3-RR, and DTAP messages that are used in the typical GSM circuit-switched call setup sequence (mobile originated) that is depicted in Figure A1 in Appendix A.

Using the information provided therein, the message size (in bytes) for the typical GSM circuit-switched call setup sequence can be estimated.  Referring to Table 1 below, the maximum message size when only the Mandatory (M) Information Elements (IE) are considered is 116 bytes.  If the Conditional (C) and Optional (O) IEs are also considered, a worst-case estimate can be made regarding the maximum message size: 116 bytes (M) + 317 + ? bytes (C) + 617 + ? bytes (O) = 1050 + ? bytes.  Granted, this is only an approximation, since not all possible combinations of C and O IEs are valid.  However, for the purposes of this study, the approximation is reasonable.

| Message |  | Length (bytes) |  |
| --- | --- | --- | --- |
|  | M | C | O |
| Immediate Assignment | 8 + (1 to 9) = {9, 18} | 6 | 3 |
| CM Service Request | 7 + (2 to 9) = {9, 18} | 0 | 1 |
| Authentication Request | 19 | 0 | 14 to 19 = {14, 19} |
| Authentication Response | 6 | 0 | 14 |
| Ciphering Mode Command | 3 | 0 | 0 |
| Ciphering Mode Complete | 2 | 0 | 3 to 11 = {3, 11} |
| Setup | 4 + (3 to 16) + (3 to 43) = {10, 63} | 4 | 5 + (3 to 16) + (2 to ?) + (2 to 23) + (2 to 23) + (2 to 18) + (2 to 18) + (2 to 5) + (2 to 5) + (3 to 33) + (2 to 3) + (2 to ?) + (2 to ?) = {1, 157 + ?} |
| Call Proceeding | 2 | 1 | 5 + (3 to 16) + (3 to 16) + (2 to ?) = {1, 39 + ?} |
| Assignment Command | 6 | 10 + (4 to 132) + (3 to 12) + (3 to 10) + (4 to 132) + (3 to 10) = {3, 306} | 54 + (4 to 8) = {1, 62} |
| Assignment Complete | 3 | 0 | 0 |
| Alerting | 2 | 0 | 4 + (2 to ?) + (3 to 131) = {2, 137 + ?} |
| Connect | 2 | 0 | 4 + (2 to ?) + (3 to 14) + (2 to 23) + (3 to 131) = {2, 174 + ?} |
| Connect Acknowledge | 2 | 0 | 0 |
| Totals | {75, 116} | {1, 317} | {1, 617 + ?} |

Table 1.  Message size for typical GSM circuit-switched call establishment.  NOTE: {x, y} = {min., max.}.  NOTE:  M = Mandatory; C = Conditional; O = Optional.

## Layer 3 Trace

Table C1 in Appendix C illustrates a Layer 3 trace for the typical GSM circuit-switched call setup sequence (mobile originated) that is depicted in Figure A1 in Appendix A.

The duration of the typical GSM circuit-switched call setup sequence can be determined by looking at the TDMA frame numbers (FN) that are delineated by the Layer 3 trace as follows:

FN start (channel request):		4,610

FN connect:						5,386

_______________________________

Difference:						   776

Since the duration of one TDMA frame is 4.615 msec, the duration of the entire typical GSM circuit-switched call setup sequence is 4.615 msec/frame ( 776 frames = 3.58 sec (actually, 120/26 msec/frame ( 776 frames).

During a GSM circuit-switched call setup sequence, the majority of the signaling is carried on an SDCCH.  The signaling frame structure comprises a 51-multiframe.  Logical channel combinations V and VII support the mapping of SDCCHs onto basic physical channels as follows:

V		FCCH + SCH + BCCH + CCCH + SDCCH/4 (0…3) + SACCH/C4 (0…3)

VII		SDCCH/8 (0…7) + SACCH/C8 (0…7)

The expression SDCCH/4 + SACCH/C4 means that it is possible to assign up to four SDCCHs with their required SACCHs.  These are referred to as "subchannels".  The position of the SDCCH for corresponding subchannels is at a certain distance from each other: for the uplink, it is 15 frames; for the downlink it is 36 frames.  The intention behind this is to reduce the command response cycle to one multiframe.  If, for example, the base station commands the mobile station to authenticate itself, the response can be sent only 15 frames later.  The same applies for the other direction, with the only difference being that the network has more time allocated for a response.  This is mainly due to the fact that: (1) the distances within the network for the signals are much greater; and (2) sufficient time must be allocated for the network to perform signaling processing/management.  This also applies for logical channel combination VIII (i.e., SDCCH/8 + SACCH/C8).  Note that for both logical channel combinations V and VII, a subchannel is transmitted once per 51-multiframe (i.e., once per 235.38 msec).

Physical blocks of 184 bits (23 bytes) are generated by Layer 1 for SDCCH messages.  The Layer 2 GSM protocol used for signaling transfer between an MS and BTS is LAPDm.  When information (i.e., an I-frame) has to be transferred over an SDCCH, frame format B is used.  Frame format B consists of an Address Field (1 byte), a Control Field (1 byte), a Length Indicator Field (1 byte), and an Information Field (i.e., a Layer 3 CC, MM, or RR message).  Therefore, 23 bytes minus 3 bytes = 20 bytes are available for transferring Layer 3 CC, MM, or RR messages.  If only the Mandatory (M) IEs are considered, nearly all of the Layer 3 CC, MM, and RR messages that are part of the typical GSM circuit-switched call setup sequence that is depicted in Figure A1 in Appendix A can fit into a 4 burst SDCCH (the only exception being the Setup message, see Table B8 in Appendix B).

Using this information, it is possible to estimate how much of the 3.58 sec duration of the entire typical GSM circuit-switched call setup sequence is due to the SDCCH signaling over the Um interface.  Note that, since the Channel Request message (RACH), Immediate Assignment message (AGCH), Assignment Complete message (FACCH), Alerting message (FACCH), Connect message (FACCH), and Connect Acknowledgment message (FACCH), are not transmitted over the SDCCH, the estimation will not include them.  Most of the delay caused by these messages is due to the signaling processing/management that the network must perform.

The minimum amount of time required for the SDCCH signaling over the Um interface is (not including network delay):

MS transmits Connection Management Service Request message

36 ( (120/26) msec = 166.15 msec

Network transmits Authentication Request message

15 ( (120/26) msec = 69.23 msec

MS transmits Authentication Response message

36 ( (120/26) msec = 166.15 msec

Network transmits Ciphering Mode Command message

15 ( (120/26) msec = 69.23 msec

MS transmits Ciphering Mode Complete message

51 ( (120/26) msec = 235.38 msec

MS transmits Setup message (only one 4 burst SDCCH was used for the Layer 3 trace)

36 ( (120/26) msec = 166.15 msec

Network transmits Call Proceeding message

51 ( (120/26) msec = 235. 38 msec

Network transmits Assignment Command message

_________________________________________

TOTAL = 1107.67 sec

This is due strictly to the 15 frame/36 frame SDCCH downlink/uplink frame offset period (i.e., again, not including network delay).  Note that the total amount of time required for SDCCH signaling over the Um interface including network delay can be determined from the Layer 3 trace for the typical GSM circuit-switched call setup sequence illustrated in Table C1 in Appendix C.  Nevertheless, the total budget due to minimum amount of time required for the SDCCH signaling over the Um interface is approximately 1107.67 msec (or 1.11 sec).  This is about 31% of the 3.58 sec duration of the entire typical GSM circuit-switched call setup sequence.

# RRC Connection Messages and Direct Transfer Messages

## UE Modes and RRC States

Two basic operational modes of a UE are idle mode and connected mode.  The connected mode can be further divided into service states, which define what kind of physical channels a UE is using.  Figure 1 shows the main RRC service states in the connected mode.  It also shows the transitions between idle mode and connected mode and the possible transitions within the connected mode [2].

Figure 1. UE modes and RRC states in connected mode.

## GPRS Attach

In order to quantify the RRC Connection messages and Direct Transfer messages that must be accounted for when analyzing the Post Dial Delay (PDD) and throughput requirements of a typical SIP call setup sequence as it applies to a GERAN packet-switched speech call, a "GPRS attach" signaling procedure/message is presented below.  NOTE: For the purposes of brevity, it is assumed that the MS is assigned a dedicated traffic channel.  Also, NBAP messages are omitted.

- MS powers on.

- MS enters PMM state "PMM-Detached state" (TS 23.060).

- MS scans and camps on a control channel.

- MS needs to perform GPRS attach. But first, a signaling connection needs to be established (a signaling connection comprises an RRC connection and an Iu connection).

- MS transitions from PMM state "PMM-Detached state" to PMM state "PMM-Connected state" and RRC mode "Connected mode" as follows:

- MS transmits RRC Connection Request message (TS 25.331) to BSC (GERAN) (details regarding MS-to-GERAN access are FFS, see [12]). Value of IE Establishment Cause are FFS.  NOTE: For UTRAN, RRC Connection Request message is transmitted via logical channel CCCH (TM-SAP), transport channel RACH, physical channel PRACH.

- BSC (GERAN) transmits RRC Connection Setup message (TS 25.331) to MS.  RRC signaling radio bearers are established (e.g., RBs 0-4) (details regarding differences between GERAN and UTRAN physical channel assignment for signaling radio bearers is FFS). G-RNTI is assigned for MS MS if RRC mode. NOTE: For UTRAN, RRC Connection Setup message is transmitted via logical channel CCCH (UM-SAP), transport channel FACH, physical channel SCCPCH.

- MS transmits RRC Connection Setup Complete message (TS 25.331) to BSC (GERAN).  NOTE: For UTRAN, RRC Connection Setup Complete message is transmitted via logical channel DCCH (AM-SAP), transport channel RACH/CPCH/DCH, physical channel PRACH/PCPCH/DPDCH+DPCCH.

- MS enters PMM state "PMM-Connected state" and RRC mode "Connected mode" (although, strictly speaking, GPRS attach has not yet been performed by MS).  NOTE: Since the value of IE Establishment Cause is FFS, the RRC mode "Connected mode" state is FFS (e.g., it could be either "Cell_DCH state" or "Cell_FACH state").

- MS transmits Initial Direct Transfer message (TS 25.331) to BSC (GERAN) to establish Iu signaling connection, Iu signaling flow identifier (integer, 0 to 63), etc. and transmit NAS message comprising Service Request message (TS 24.008).  Since Iu signaling connection need to be established, value of IE Service Type is 000 (viz., signaling).  NOTE: For UTRAN, Initial Direct Transfer message is transmitted via logical channel DCCH (AM-SAP), transport channel RACH/CPCH/DCH, physical channel PRACH/PCPCH/DPDCH+DPCCH.

- Subsequently, BSC (GERAN) transmits Initial UE Message message (TS 25.413) to CN to establish Iu signaling connection, Iu signaling connection identifier, etc. and transmit NAS message comprising Service Request message (TS 24.008).  Since Iu signaling connection needs to be established, value of IE Service Type is 000 (viz., signaling).

- NOTE: CN may initiate authentication and ciphering procedures depending upon information in Service Request message (TS 24.008).  This will involve a series of Uplink Direct Transfer messages (TS 25.331) and Downlink Direct Transfer messages (TS 25.331) between the MS and BSC(GERAN).  This will also involve a series of Direct Transfer, RNC Originated messages (TS 25.413) and Direct Transfer, CN Originated messages (TS 25.413) between the BSC (GERAN) and CN.  The NAS messages will be Authentication and Ciphering Request message and Authentication and Ciphering Response.

- CN transmits Direct Transfer, CN Originated message (TS 25.413) to BSC (GERAN) to transmit NAS message comprising Service Accept message (TS 24.008).

- Subsequently, BSC (GERAN) transmits Downlink Direct Transfer message (TS 25.331) to MS to transmit NAS message comprising Service Accept message (TS 24.008).  NOTE: For UTRAN, Downlink Direct Transfer message is transmitted via logical channel DCCH (AM-SAP), transport channel FACH/DSCH/DCH, physical channel SCCPCH/PDSCH/DPDCH+DPCCH.

- MS transmits Uplink Direct Transfer message (TS 25.331) to BSC (GERAN) or RNC to transmit NAS message comprising Attach Request message (TS 24.008).  NOTE: For UTRAN, Uplink Direct Transfer message is transmitted via logical channel DCCH (AM-SAP), transport channel RACH/CPCH/DCH, physical channel PRACH/PCPCH/DPDCH+DPCCH.

- Subsequently, BSC (GERAN) transmits Direct Transfer, RNC Originated message (TS 25.413) to CN to transmit NAS message comprising Attach Request message (TS 24.008).

- CN transmits Direct Transfer, CN Originated message (TS 25.413) to BSC (GERAN) to transmit NAS message comprising Attach Accept message (TS 24.008).

- Subsequently, BSC (GERAN) transmits Downlink Direct Transfer message (TS 25.331) to MS to transmit NAS message comprising Attach Accept message (TS 24.008).  NOTE: For UTRAN, Downlink Direct Transfer message is transmitted via logical channel DCCH (AM-SAP), transport channel FACH/DSCH/DCH, physical channel SCCPCH/PDSCH/DPDCH+DPCCH.

- NOTE: MS has now successfully transitioned from PMM state "PMM-Detached state" to PMM state "PMM-Connected state" and RRC mode "Connected mode" (i.e., MS has successfully performed GPRS Attach).

Estimation of the size of these messages is FFS.

## Primary PDP Context Activation

A "primary PDP context activation" signaling procedure/message is presented below.  NOTE: For the purposes of brevity, it is assumed that the MS continues its use of the dedicated traffic channel assigned during the "GPRS attach" signaling procedure/message.  Also, NBAP messages are omitted.

- MS needs to perform primary PDP context activation.

- MS transmits Uplink Direct Transfer message (TS 25.331) to BSC (GERAN) or RNC to transmit NAS message comprising Activate PDP Context Request message (TS 24.008).  NOTE: For UTRAN, Uplink Direct Transfer message is transmitted via logical channel DCCH (AM-SAP), transport channel RACH/CPCH/DCH, physical channel PRACH/PCPCH/DPDCH+DPCCH.

- Subsequently, BSC (GERAN) transmits Direct Transfer, RNC Originated message (TS 25.413) to CN to transmit NAS message comprising Activate PDP Context Request message (TS 24.008).

- CN transmits Radio Access Bearer Assignment Request message (TS 25.413) to BSC (GERAN) to establish radio access bearer.

- Subsequently, BSC (GERAN) transmits Radio Access Bearer Assignment Response message (TS 25.413)

- Subsequently, BSC (GERAN) transmits Direct Transfer, RNC Originated message (TS 25.413) to CN to transmit NAS message comprising Activate PDP Context Request message (TS 24.008).

- MS transitions to Cell PCH state or GRA PCH state of RRC mode "Connected mode" or release its RRC connection and returns to RRC mode "Idle mode".

Estimation of the size of these messages is FFS.

# RSVP Messages

The Resource reSerVation Protocol (RSVP) [4] provides a general means for an application to communicate its QoS requirements to an Integrated Services Internet infrastructure.  RSVP is not a data transport protocol, but a control protocol that signals QoS requests on behalf of a data flow.  RSVP is sophisticated, in the sense that it allows reservations in both the one-to-one unicast and the many-to-many multicast data transport scenarios.

The two RSVP messages involved with path setup and resource reservation are the PATH and RESV messages respectively.  These are discussed below.

## RSVP PATH Message

Figure 2 illustrates the format of the PATH message.

Figure 2. RSVP PATH message format.

Estimation of the size of the PATH message is FFS.

## RSVP RESV Message

Figure 3 illustrates the format of the RESV message.

Figure 3. RSVP RESV message format.

Estimation of the size of the RESV message is FFS.

# Typical SIP Call Setup Sequence

The Session Initiation Protocol (SIP) is a client-server, text-based signaling protocol used for creating and controlling multimedia sessions with two or more participants [13].  SIP can be transported over either TCP or UDP, but the most common implementations use SIP over UDP for simplicity and speed.  SIP commonly employs the Session Description Protocol (SDP) for the specification of system parameters (although this is not a requirement) [14].  SIP messages are encoded using HTTP/1.1 message syntax [15].  The character set is ISO 10646 with UTF-8 encoding [16], [17].  Lines are terminated with CRLF (carriage return, line feed), but receivers should be able to handle CR or LF as well.  SIP defines two basic message types: request and response.  Request messages are used to initiate, confirm, modify, and terminate calls.  Response messages are used to convey either provisional information such as "ringing", or "moved temporarily" response, or final information such as "busy" or "does not exist".  Table 2 lists the SIP request methods.  Note that Table 2 has been updated to include the SIP request methods COMET and PRACK [5], [6], [7].  Table 3 presents a summary of SIP response message categories and their use.

| Request method | Function |
| --- | --- |
| INVITE | Initiate a session. |
| ACK | Confirm the final response to an INVITE. |
| BYE | Terminate a session. |
| CANCEL | Cancel searches and "ringing". |
| OPTIONS | Communicate features supported. |
| REGISTER | Register a client with a location service. |
| COMET | Confirm all session pre-conditions. |
| PRACK | Confirm reliable provisional response. |

Table 2.  SIP request methods.

| Status Code | Category | Example information |
| --- | --- | --- |
| 1xx | Informational | Trying, ringing, call is being forwarded, queued. |
| 2xx | Success | OK |
| 3xx | Redirection | Move permanently, moved temporarily, etc. |
| 4xx | Client error | Bad request, unauthorized, not found, busy, etc. |
| 5xx | Server error | Server error, not implemented, bad gateway, etc. |
| 6xx | Global failure | Busy everywhere, does not exist anywhere, etc. |

Table 3.  SIP response codes.

Figure 4 [18] illustrates a new "revised" typical SIP call setup sequence (no speech codec negotiation) to account for the new draft SIP request methods and response codes (e.g., COMET, PRACK, 183 SESSION PROGRESS, etc.).  Unlike the typical SIP call setup sequence that was discussed in [1] (which was a SIP to SIP call via a SIP proxy server), Figure 4 illustrates a SIP to gateway call via a SIP proxy server).  Figure 4 also includes a typical SIP call release sequence.

Figure 3.  Typical SIP call setup sequence

## Message Size Estimation

This is FFS.

## Layer 3 Trace

This is FFS.

# Conclusions and Recommendations

This contribution is being presented for review and discussion.  The plan is to update all of the sections marked "FFS" for the TSG 3GPP GERAN #2 meeting in Stockholm, Sweden (November 13-17, 2000).

# References

[1]	Tdoc GP-000036 "A Comparison Between GERAN Packet-Switched Call Setup Using SIP and GSM Circuit-Switched Call Setup Using RIL3-CC, RIL3-MM, RIL3-RR, and DTAP, Rev. 0.2", Source: Nortel Networks, 3GPP TSG GERAN #1, August 28-September 1, 2000.

[2]	3GPP, TS 25.331 "RRC Protocol Specification", Ver. 3.3.0, Release 1999.

[3]	3GPP, TS 24.008 "Mobile Radio Interface Layer 3 Specification, Core Network Protocols - Stage 3", Ver. 3.4.1, Release 1999.

[4]	RFC 2205, R. Braden, L. Zhang, S. Berson, S. Herzog, S. Jamin, "Resource ReSerVation Protocol (RSVP) - Version 1 Functional Specification", September 1997.

[5]	Internet draft-ietf-manyfolks-sip-resource-01.txt, W. Marshall, K. Ramakrishnan, E. Miller, G. Russell, B. Beser, M. Mannette, K. Steinbrenner, D. Oran, F. Andreasen, M. Ramalho, J. Pickens, P. Lalwaney, J. Fellows, D. Evans, K. Kelly, A. Roach, J. Rosenberg, H. Schulzrinne, S. Donovan, "Integration of Resource Management and SIP", June 2000.

[6]	Internet draft-ietf-sip-100rel-02.txt, J. Rosenberg, H. Schulzrinne, "Reliability of Provisional Responses in SIP", June 2000.

[7]	Internet draft-ietf-rfc2543bis-01.txt, M. Handley, H. Schulzrinne, E. Schooler, J. Rosenberg, "SIP: Session Initiation Protocol", August 2000.

[8]	ETSI, GSM 04.08 "Digital Cellular Telecommunication System (Phase 2+); Mobile Radio Interface Layer 3 Specification" (GSM 04.08).

[9]	ETSI, GSM 04.18 "Digital Cellular Telecommunication System (Phase 2+); Mobile Radio Interface Layer 3 Specification, Radio Resource Control Protocol" (GSM 04.18).

[10]	3GPP, TS 24.007 "Mobile Radio Interface Signaling Layer 3; General Aspects" (TS 24.007).

[11]	3GPP, TS 24.008 "Mobile Radio Interface Layer 3 Specification, Core Network Protocols - Stage 3" (TS 24.008).

[12]	GAHW-000010 "GERAN Release 2000 Packet Channel Request Mechanism and Contention Resolution Mechanism", Source: Nortel Networks, 3GPP TSG GERAN Ad Hoc on Release 2000 and Beyond #2, October 9-13, 2000.

[13]	RFC 2543, M. Handley, H. Schulzrinne, E. Schooler, J. Rosenberg, "SIP: Session Initiation Protocol", March 1999.

[14]	RFC 2327, M. Handley, V. Jacobson, "SDP: Session Description Protocol", April 1998.

[15]	RFC 2068, R. Fielding, J. Gettys, J. Mogul, H. Frystyk, T. Berners-Lee, "Hypertext Transfer Protocol - HTTP/1.1", January 1997.

[16]	RFC 2279, F. Yergeau, "UTF-8, A Transformation Format of ISO 10646", January 1998.

[17]	RFC 2044, F. Yergeau, "UTF-8, A Transformation Format of Unicode and ISO 10646", October 1996.

[18]	Tdoc S2-001504 "Call Flows: SIP + End-to-End RSVP", 3GPP TSG SA WG2, Bristol, United Kingdom, September 4-8, 2000, Nortel Networks.

[19]	Redl, S., Weber, M., Oliphant, M., An Introduction to GSM, Artech House: Norwood, MA, 1995.

APPENDIX A  Typical GSM Circuit-Switched Call Setup Sequence

Figure A1.  CC, MM, and RR Layer 3 messages for a typical GSM circuit-switched call setup sequence (mobile originated).  NOTE: PD = Protocol Discriminator; CC = Call Control; MM = Mobility Management; RR = Radio Resource Management.

Appendix B  Layer 3 CC, MM, and RR GSM Circuit-Switched Messages

Table B1: CHANNEL REQUEST message content (ref. GSM 04.18)

MS codes	According to Establishment cause:
	bits
	8 .... 1

101xxxxx	Emergency call

110xxxxx	Call re-establishment; TCH/F was in use, or
		TCH/H was in use but the network does not
		set NECI bit to 1

011010xx	Call re-establishment; TCH/H was in use and the
		network sets NECI bit to 1

011011xx	Call re-establishment; TCH/H + TCH/H was in use
		and the network sets NECI bit to 1

100xxxxx	Answer to paging
	0010xxxx	
	0011xxxx	See table 9.9a/GSM 04.18
	0001xxxx

111xxxxx	Originating call and TCH/F is needed, or originating call
		and the network does not set NECI bit to 1, or
		procedures that can be completed with a SDCCH and the
		network does not set NECI bit to 1.				note 1

0100xxxx	Originating speech call from dual-rate mobile station when TCH/H
		is sufficient and supported by the MS for speech calls and the network 			sets NECI bit to 1	note 5

0101xxxx	Originating data call from dual-rate mobile station when TCH/H
		is sufficient and supported by the MS for data calls and the network sets 			NECI bit to 1	note 5

000xxxxx	Location updating and the network does not set NECI bit to 1

0000xxxx	Location updating and the network sets NECI bit to 1

0001xxxx	Other procedures which can be completed with	note 1
		an SDCCH and the network sets NECI bit to 1

011110xx	One phase packet access with request for single timeslot uplink
	01111x0x	transmission; one PDCH is needed.
	01111xx0

01110xxx	Single block packet access; one block period on a PDCH is needed for
		two phase packet access or other RR signalling purpose.

01100111	LMU establishment	note 2

01100xx0	Reserved for future use
	01100x01	
	01100011		note 2a

01111111	Reserved for future use.	note 2b

NOTE 1:	Examples of these procedures are: IMSI detach, Short Message Service (SMS), Supplementary Service management, Location Services.

NOTE 2:	If such messages are received by a network, an SDCCH shall be allocated.

NOTE 2a:	If such messages are received by a network, an SDCCH may be allocated.

NOTE 2b:	This value shall not be used by the mobile station on RACH. If such message is received by the network, it may be ignored.

Table B2: IMMEDIATE ASSIGNMENT message content (ref. GSM 04.18)

| IEI | Information element | Type / Reference | Presence | Format | length |
| --- | --- | --- | --- | --- | --- |
|  | L2 Pseudo Length | L2 Pseudo Length | M | V | 1 |
|  |  | 10.5.2.19 |  |  |  |
|  | RR management | Protocol Discriminator | M | V | 1/2 |
|  | Protocol Discriminator | 10.2 |  |  |  |
|  | Skip Indicator | Skip Indicator | M | V | 1/2 |
|  |  | 10.3.1 |  |  |  |
|  | Immediate Assignment | Message Type | M | V | 1 |
|  | Message Type | 10.4 |  |  |  |
|  | Page Mode | Page Mode | M | V | 1/2 |
|  |  | 10.5.2.26 |  |  |  |
|  | Dedicated mode or TBF | Dedicated mode or TBF | M | V | 1/2 |
|  |  | 10.5.2.25b |  |  |  |
|  | Channel Description | Channel Description | C | V | 3 |
|  |  | 10.5.2.5 |  |  |  |
|  | Packet Channel Description | Packet Channel Description | C | V | 3 |
|  |  | 10.5.2.25a |  |  |  |
|  | Request Reference | Request Reference | M | V | 3 |
|  |  | 10.5.2.30 |  |  |  |
|  | Timing Advance | Timing Advance | M | V | 1 |
|  |  | 10.5.2.40 |  |  |  |
|  | Mobile Allocation | Mobile Allocation | M | LV | 1-9 |
|  |  | 10.5.2.21 |  |  |  |
| 7C | Starting Time | Starting Time | O | TV | 3 |
|  |  | 10.5.2.38 |  |  |  |
|  | IA Rest Octets | IA Rest Octets | M | V | 0-11 |
|  |  | 10.5.2.16 |  |  |  |

Table B3: CM SERVICE REQUEST message content (ref. TS 24.008)

| IEI | Information element | Type / Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Mobility management | Protocol discriminator | M | V | ½ |
|  | protocol discriminator | 10.2 |  |  |  |
|  | Skip Indicator | Skip Indicator | M | V | ½ |
|  |  | 10.3.1 |  |  |  |
|  | CM Service Request | Message type | M | V | 1 |
|  | message type | 10.4 |  |  |  |
|  | CM service type | CM service type | M | V | ½ |
|  |  | 10.5.3.3 |  |  |  |
|  | Ciphering key sequence | Ciphering key sequence | M | V | ½ |
|  | number | number |  |  |  |
|  |  | 10.5.1.2 |  |  |  |
|  | Mobile station | Mobile station | M | LV | 4 |
|  | classmark | classmark 2 |  |  |  |
|  |  | 10.5.1.6 |  |  |  |
|  | Mobile identity | Mobile identity | M | LV | 2-9 |
|  |  | 10.5.1.4 |  |  |  |
| 8- | Priority | Priority Level | O | TV | 1 |
|  |  | 10.5.1.11 |  |  |  |

Table B4: AUTHENTICATION REQUEST message content (ref. TS 24.008)

| IEI | Information element | Type / Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Mobility management | Protocol discriminator | M | V | 1/2 |
|  | protocol discriminator | 10.2 |  |  |  |
|  | Skip Indicator | Skip Indicator | M | V | 1/2 |
|  |  | 10.3.1 |  |  |  |
|  | Authentication Request | Message type | M | V | 1 |
|  | message type | 10.4 |  |  |  |
|  | Ciphering key sequence | Ciphering key sequence | M | V | 1/2 |
|  | number | number |  |  |  |
|  |  | 10.5.1.2 |  |  |  |
|  | Spare half octet | Spare half octet | M | V | 1/2 |
|  |  | 10.5.1.8 |  |  |  |
|  | Authentication | Auth. parameter RAND | M | V | 16 |
|  | parameter RAND (UMTS challenge or GSM challenge) | 10.5.3.1 |  |  |  |
| 20 | Authentication | Auth. parameter AUTN | O | TLV | 14-19 |
|  | Parameter AUTN | 10.5.3.1.2 |  |  |  |

Table B5: AUTHENTICATION RESPONSE message content (ref. TS 24.008)

| IEI | Information element | Type / Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Mobility management | Protocol discriminator | M | V | 1/2 |
|  | protocol discriminator | 10.2 |  |  |  |
|  | Skip Indicator | Skip Indicator | M | V | 1/2 |
|  |  | 10.3.1 |  |  |  |
|  | Authentication Response | Message type | M | V | 1 |
|  | message type | 10.4 |  |  |  |
|  | Authentication Response | Auth. Response parameter | M | V | 4 |
|  | parameter | 10.5.3.2 |  |  |  |
| 21 | Authenticatio Response | Auth. Response parameter | O | TLV | 14 |
|  | Parameter (extension) | 10.5.3.2.1 |  |  |  |

Table B6: CIPHERING MODE COMMAND message content (ref. GSM 04.18)

| IEI | Information element | Type / Reference | Presence | Format | length |
| --- | --- | --- | --- | --- | --- |
|  | RR management | Protocol Discriminator | M | V | 1/2 |
|  | Protocol Discriminator | 10.2 |  |  |  |
|  | Skip Indicator | Skip Indicator | M | V | 1/2 |
|  |  | 10.3.1 |  |  |  |
|  | Cipher Mode Command | Message Type | M | V | 1 |
|  | Message Type | 10.4 |  |  |  |
|  | Ciphering Mode Setting | Cipher Mode Setting | M | V | 1/2 |
|  |  | 10.5.2.9 |  |  |  |
|  | Cipher Response | Cipher Response | M | V | 1/2 |
|  |  | 10.5.2.10 |  |  |  |

Table B7: CIPHERING MODE COMPLETE message content (ref. GSM 04.18)

| IEI | Information element | Type / Reference | Presence | Format | length |
| --- | --- | --- | --- | --- | --- |
|  | RR management | Protocol Discriminator | M | V | 1/2 |
|  | Protocol Discriminator | 10.2 |  |  |  |
|  | Skip Indicator | Skip Indicator | M | V | 1/2 |
|  |  | 10.3.1 |  |  |  |
|  | Cipher Mode Complete | Message Type | M | V | 1 |
|  | Message Type | 10.4 |  |  |  |
| 17 | Mobile Equipment | Mobile Identity | O | TLV | 3-11 |
|  | Identity | 10.5.1.4 |  |  |  |

Table B8: SETUP message content (mobile station to network direction) (ref. GSM 04.18)

| IEI | Information element | Type / Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Call control | Protocol discriminator | M | V | 1/2 |
|  | protocol discriminator | 10.2 |  |  |  |
|  | Transaction identifier | Transaction identifier | M | V | 1/2 |
|  |  | 10.3.2 |  |  |  |
|  | Setup | Message type | M | V | 1 |
|  | message type | 10.4 |  |  |  |
| D- | BC repeat indicator | Repeat indicator | C | TV | 1 |
|  |  | 10.5.4.22 |  |  |  |
| 04 | Bearer capability 1 | Bearer capability | M | TLV | 3-16 |
|  |  | 10.5.4.5 |  |  |  |
| 04 | Bearer capability 2 | Bearer capability | O | TLV | 3-16 |
|  |  | 10.5.4.5 |  |  |  |
| 1C | Facility(simple recall alignment) | Facility | O | TLV | 2- |
|  |  | 10.5.4.15 |  |  |  |
| 5D | Calling party sub- | Calling party subaddr. | O | TLV | 2-23 |
|  | address | 10.5.4.10 |  |  |  |
| 5E | Called party BCD | Called party BCD num. | M | TLV | 3-43 |
|  | number | 10.5.4.7 |  |  |  |
| 6D | Called party sub- | Called party subaddr. | O | TLV | 2-23 |
|  | address | 10.5.4.8 |  |  |  |
| D- | LLC repeat indicator | Repeat indicator | O | TV | 1 |
|  |  | 10.5.4.22 |  |  |  |
| 7C | Low layer | Low layer comp. | O | TLV | 2-18 |
|  | compatibility I | 10.5.4.18 |  |  |  |
| 7C | Low layer | Low layer comp. | O | TLV | 2-18 |
|  | compatibility II | 10.5.4.18 |  |  |  |
| D- | HLC repeat indicator | Repeat indicator | O | TV | 1 |
|  |  | 10.5.4.22 |  |  |  |
| 7D | High layer | High layer comp. | O | TLV | 2-5 |
|  | compatibility i | 10.5.4.16 |  |  |  |
| 7D | High layer | High layer comp. | O | TLV | 2-5 |
|  | compatibility ii | 10.5.4.16 |  |  |  |
| 7E | User-user | User-user | O | TLV | 3-35 |
|  |  | 10.5.4.25 |  |  |  |
| 7F | SS version | SS version indicator | O | TLV | 2-3 |
|  |  | 10.5.4.24 |  |  |  |
| A1 | CLIR suppression | CLIR suppression | C | T | 1 |
|  |  | 10.5.4.11a |  |  |  |
| A2 | CLIR invocation | CLIR invocation | C | T | 1 |
|  |  | 10.5.4.11b |  |  |  |
| 15 | CC capabilities | Call Control Capabilities | O | TLV | 3 |
|  |  | 10.5.4.5a |  |  |  |
| 1D | Facility $(CCBS)$ | Facility | O | TLV | 2-? |
|  | (advanced recall alignment) | 10.5.4.15 |  |  |  |
| 1B | Facility (recall alignment | Facility | O | TLV | 2-? |
|  | Not essential) $(CCBS)$ | 10.5.4.15 |  |  |  |

Table B9: CALL PROCEEDING message content (ref. TS 24.008)

| IEI | Information element | Type / Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Call control | Protocol discriminator | M | V | 1/2 |
|  | protocol discriminator | 10.2 |  |  |  |
|  | Transaction identifier | Transaction identifier | M | V | 1/2 |
|  |  | 10.3.2 |  |  |  |
|  | Call proceeding | Message type | M | V | 1 |
|  | message type | 10.4 |  |  |  |
| D- | Repeat Indicator | Repeat Indicator | C | TV | 1 |
|  |  | 10.5.4.22 |  |  |  |
| 04 | Bearer capability 1 | Bearer capability | O | TLV | 3-16 |
|  |  | 10.5.4.5 |  |  |  |
| 04 | Bearer capability 2 | Bearer capability | O | TLV | 3-16 |
|  |  | 10.5.4.5 |  |  |  |
| 1C | Facility | Facility | O | TLV | 2-? |
|  |  | 10.5.4.15 |  |  |  |
| 1E | Progress indicator | Progress indicator | O | TLV | 4 |
|  |  | 10.5.4.21 |  |  |  |
| 8- | Priority granted | Priority Level | O | TV | 1 |
|  |  | 10.5.1.11 |  |  |  |

Table B10: ASSIGNMENT COMMAND message content (ref. GSM 04.18)

| IEI | Information element | Type / Reference | Presence | Format | length |
| --- | --- | --- | --- | --- | --- |
|  | RR management | Protocol Discriminator | M | V | ½ |
|  | Protocol Discriminator | 10.2 |  |  |  |
|  | Skip Indicator | Skip Indicator | M | V | ½ |
|  |  | 10.3.1 |  |  |  |
|  | Assignment command | Message Type | M | V | 1 |
|  | Message Type | 10.4 |  |  |  |
|  | Description of the | Channel Description 2 | M | V | 3 |
|  | First Channel, after time | 10.5.2.5a |  |  |  |
|  | Power Command | Power Command | M | V | 1 |
|  |  | 10.5.2.28 |  |  |  |
| 05 | Frequency List, after time | Frequency List | C | TLV | 4-132 |
|  |  | 10.5.2.13 |  |  |  |
| 62 | Cell Channel | Cell Channel Description | O | TV | 17 |
|  | Description | 10.5.2.1b |  |  |  |
| 10 | Description of the | Multislot Allocation | C | TLV | 3-12 |
|  | multislot configuration | 10.5.2.21b |  |  |  |
| 63 | Mode of the First | Channel Mode | O | TV | 2 |
|  | Channel (Channel Set 1) | 10.5.2.6 |  |  |  |
| 11 | Mode of Channel Set 2 | Channel Mode | O | TV | 2 |
|  |  | 10.5.2.6 |  |  |  |
| 13 | Mode of Channel Set 3 | Channel Mode | O | TV | 2 |
|  |  | 10.5.2.6 |  |  |  |
| 14 | Mode of Channel Set 4 | Channel Mode | O | TV | 2 |
|  |  | 10.5.2.6 |  |  |  |
| 15 | Mode of Channel Set 5 | Channel Mode | O | TV | 2 |
|  |  | 10.5.2.6 |  |  |  |
| 16 | Mode of Channel Set 6 | Channel Mode | O | TV | 2 |
|  |  | 10.5.2.6 |  |  |  |
| 17 | Mode of Channel Set 7 | Channel Mode | O | TV | 2 |
|  |  | 10.5.2.6 |  |  |  |
| 18 | Mode of Channel Set 8 | Channel Mode | O | TV | 2 |
|  |  | 10.5.2.6 |  |  |  |
| 64 | Description of the | Channel Description | O | TV | 4 |
|  | Second Channel, after time | 10.5.2.5 |  |  |  |
| 66 | Mode of the Second | Channel Mode 2 | O | TV | 2 |
|  | Channel | 10.5.2.7 |  |  |  |
| 72 | Mobile Allocation, | Mobile Allocation | C | TLV | 3-10 |
|  | after time | 10.5.2.21 |  |  |  |
| 7C | Starting Time | Starting Time | O | TV | 3 |
|  |  | 10.5.2.38 |  |  |  |
| 19 | Frequency List, before time | Frequency List | C | TLV | 4-132 |
|  |  | 10.5.2.13 |  |  |  |
| 1C | Description of the | Channel Description 2 | O | TV | 4 |
|  | First Channel, before time | 10.5.2.5a |  |  |  |
| 1D | Description of the | Channel Description | O | TV | 4 |
|  | Second Channel, before time | 10.5.2.5 |  |  |  |
| 1E | Frequency channel sequence | Frequency channel sequence | C | TV | 10 |
|  | before time | 10.5.2.12 |  |  |  |
| 21 | Mobile Allocation, | Mobile Allocation | C | TLV | 3-10 |
|  | before time | 10.5.2.21 |  |  |  |
| 9- | Cipher Mode Setting | Cipher Mode Setting | O | TV | 1 |
|  |  | 10.5.2.9 |  |  |  |
| 01 | VGCS target mode Indication | VGCS target mode Indication | O | TLV | 3 |
|  |  | 10.5.2.42a |  |  |  |
| 03 | Multi-Rate | MultiRate configuration | O | TLV | 4-8 |
|  | configuration | 10.5.2.21aa |  |  |  |

Table B11: ASSIGNMENT COMPLETE message content (ref. GSM 04.18)

| IEI | Information element | Type / Reference | Presence | Format | length |
| --- | --- | --- | --- | --- | --- |
|  | RR management | Protocol Discriminator | M | V | 1/2 |
|  | Protocol Discriminator | 10.2 |  |  |  |
|  | Skip Indicator | Skip Indicator | M | V | 1/2 |
|  |  | 10.3.1 |  |  |  |
|  | Assignment Complete | Message Type | M | V | 1 |
|  | Message Type | 10.4 |  |  |  |
|  | RR Cause | RR Cause | M | V | 1 |
|  |  | 10.5.2.31 |  |  |  |

Table B12: ALERTING message content (network to mobile station direction) (TS 24.008)

| IEI | Information element | Type / Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Call control | Protocol discriminator | M | V | 1/2 |
|  | protocol discriminator | 10.2 |  |  |  |
|  | Transaction identifier | Transaction identifier | M | V | 1/2 |
|  |  | 10.3.2 |  |  |  |
|  | Alerting | Message type | M | V | 1 |
|  | message type | 10.4 |  |  |  |
| 1C | Facility | Facility | O | TLV | 2-? |
|  |  | 10.5.4.15 |  |  |  |
| 1E | Progress indicator | Progress indicator | O | TLV | 4 |
|  |  | 10.5.4.21 |  |  |  |
| 7E | User-user | User-user | O | TLV | 3-131 |
|  |  | 10.5.4.25 |  |  |  |

Table B13: CONNECT message content(network to mobile station direction) (TS 24.008)

| IEI | Information element | Type / Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Call control | Protocol discriminator | M | V | 1/2 |
|  | protocol discriminator | 10.2 |  |  |  |
|  | Transaction identifier | Transaction identifier | M | V | 1/2 |
|  |  | 10.3.2 |  |  |  |
|  | Connect | Message type | M | V | 1 |
|  | message type | 10.4 |  |  |  |
| 1C | Facility | Facility | O | TLV | 2-? |
|  |  | 10.5.4.15 |  |  |  |
| 1E | Progress indicator | Progress indicator | O | TLV | 4 |
|  |  | 10.5.4.21 |  |  |  |
| 4C | Connected number | Connected number | O | TLV | 3-14 |
|  |  | 10.5.4.13 |  |  |  |
| 4D | Connected subaddress | Connected subaddress | O | TLV | 2-23 |
|  |  | 10.5.4.14 |  |  |  |
| 7E | User-user | User-user | O | TLV | 3-131 |
|  |  | 10.5.4.25 |  |  |  |

Table B14: CONNECT ACKNOWLEDGE message content (ref. TS 24.008)

| IEI | Information element | Type / Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Call control | Protocol discriminator | M | V | 1/2 |
|  | protocol discriminator | 10.2 |  |  |  |
|  | Transaction identifier | Transaction identifier | M | V | 1/2 |
|  |  | 10.3.2 |  |  |  |
|  | Connect acknowledge | Message type | M | V | 1 |
|  | message type | 10.4 |  |  |  |

Appendix C  Layer 3 Trace for Typical GSM Circuit-Switched Call Setup Sequence

Table C1 illustrates a Layer 3 trace for the typical GSM circuit-switched call setup sequence (mobile originated) that is depicted in Figure A1 of Appendix A.  The typical GSM circuit-switched call setup sequence was performed in a network simulated by a test system described in [19].

The Layer 3 trace includes the following information: frame numbers (FN), time stamps, direction of transmission (uplink - ul, downlink = dl), the logical channel (RACH/AGCH/SDCCH/FACCH), time slot number, TI (Transaction Identifier), PD (Protocol Discriminator), as well as MTs (Message Types), IE names (Information Element), and their contents.  The T1, T2, and T3 counters appear as T1:T2:T3 (T2 counts from 0 to 25 and T3 counts from 0 to 50).

The Layer trace used an SDCCH/8 signaling channel.  The duration of the typical GSM circuit-switched call setup sequence can be determined by looking at the TDMA frame numbers (FN) that are delineated by the Layer 3 trace as follows:

FN start (channel request):		4,610

FN connect:						5,386

_______________________________

Difference:						   776

Since the duration of one TDMA frame is 4.615 msec, the duration of the entire typical GSM circuit-switched call setup sequence is 4.615 msec/frame ( 776 frames = 3.58 sec.

| MS transmits (uplink) | BS transmits (downlink) |
| --- | --- |
| FN:0004610: Umul1 ,rach, TS(0), TI(0),pd(rr), 0003:08:20 chan_req, chan_req(= 7h,0Ah); |  |
|  | FN:0004622: Umdl1 ,agch, TS(0), TI(0),pd(rr), 0003:20:32 imm_ass, pag_mod(= 0h), chan_desc(= 8h,3h,0h,0i,0h,02h), req_ref(= EAh,03h,14h,08h), tim_adv(= 00h), mob_alloc(= ); |
| FN:0004656: Umul1 ,sdcch(O), TS(3),TI(0),pd(mm), 0003.02:15 cm_serv_req, cm_serv(= 1h), ciph_key_seq(= 0h), mob_class2(= 0h,0h,2h,0i,0h), mob_id(= 4h,0i,12345678h); |  |
|  | FN:0004743: Umdl1 ,sdcch(0), TS(3), TI(0),pd(mm), 0003:11 :00 auth_req, ciph_key_seq(= 0h), rand(= 0123456789ABCDEF 0123456789ABCDEFh); |
| FN:0004809: Umul1 ,sdcch(O), TS(3),TI(0),pd(mm), 0003:25:15 auth_res, sres(= 90DFD9F0h); |  |
|  | FN:0004845: Umdl1 ,sdcch(0), TS(3), TI(0),pd(rr), 0003:09:00 ciph_mode_cmd, ciph_mode_set(= 0i); |
| FN:0004911: Umul1,sdcch(0), TS(3), TI(0),pd(rr), 0003:23:15 ciph_mode_com; |  |
| FN:0004962: Umul1,sdcch(0), TS(3), TI(0),pd(cc), 0003:22: 15 setup, bear_cap(= 1i,1h,0i,0i,0h), cd_p_bcd(= 0h,1h,089996410h); |  |
|  | FN:0004998: Umdl1 ,sdcch(0), TS(3), TI(8),pd(cc), 0003:06:00 call_proc; |
|  | FN:0005100: Umdl1 ,sdcch(0), TS(3), TI(0),pd(rr), 0003:04:00 assign_cmd, chan_desc(=01h,4h,0h,1i,00h,00h), pow_cmd(= 0Fh), |
| FN:0005304: Umul1,facch, TS(4), TI(0),pd(rr), 0004.00:00 assign_com, rr_cause(= 00h); |  |
|  | FN:0005334. Umdl1,facch, TS(4), TI(8),pd(cc), 0004:04:30 alert; |
|  | FN:0005369: Umdl1,facch, TS(4), TI(8),pd(cc), 0004:13:14 conn; |
| FN:0005386: Umul1,facch, TS(4), TI(0),pd(cc), 0004:04:31 conn_ack; |  |

Table C1  Layer 3 trace for typical GSM circuit switched call setup sequence (mobile originated) that is depicted in Figure A1 in Appendix A.