3GPP TSG GERAN Ad Hoc	GAHW-000013
on Release 2000 and Beyond #2	Agenda Item 6.1.4

Munich, Germany

9-11 October 2000

Source:  Nortel Networks

Coding Scheme for AMR 8-PSK Half-Rate

(Optimized Voice Bearer)

1	Introduction	3

2	Channel coding	3

3	AMR Full Rate Speech (AFS)	3

4	Convolutional encoder	3

4.1	TCH/AFS12.2	4

4.1.1	TYPE-1: Recursive systematic convolutional code	4

4.1.2	TYPE-2: Nonsystematic convolutional code	4

4.1.3	Puncturing	4

4.2	TCH/AFS10.2	5

4.2.1	TYPE-1: Recursive systematic convolutional code	5

4.2.2	TYPE-2: Nonsystematic convolutional code	5

4.2.3	Puncturing	6

4.3	TCH/AFS7.95	6

4.3.1	TYPE-1: Recursive systematic convolutional code	6

4.3.2	TYPE-2: Nonsystematic convolutional code	6

4.3.3	Puncturing	7

4.4	TCH/AFS7.4	7

4.4.1	TYPE-1: Recursive systematic convolutional code	7

4.4.2	TYPE-2: Nonsystematic convolutional code	8

4.4.3	Puncturing	8

4.5	TCH/AFS6.7	9

4.5.1	TYPE-1: Recursive systematic convolutional code	9

4.5.2	TYPE-2: Nonsystematic convolutional code	9

4.5.3	Puncturing	10

4.6	TCH/AFS5.9	10

4.6.1	TYPE-1: Recursive systematic convolutional code	10

4.6.2	TYPE-2: Nonsystematic convolutional code	10

4.6.3	Puncturing	11

4.7	TCH/AFS5.15	11

4.7.1	TYPE-1: Recursive systematic convolutional code	11

4.7.2	TYPE-2: Nonsystematic convolutional code	12

4.7.3	Puncturing	13

4.8	TCH/AFS4.75	13

4.8.1	TYPE-1: Recursive systematic convolutional code	13

4.8.2	TYPE-2: Nonsystematic convolutional code	14

4.8.3	Puncturing	14

5	Interleaving	14

6	Symbol Mapping	15

7	Mapping on a Burst	15

8	Simulation Results	15

9	Conclusions and Recommendations	28

Appendix A	29

A.1	Parity for speech frames	29

A.2	CRC Computation	29

APPENDIX B	32

# Introduction

In this contribution, channel coding schemes for all the 8PSK AMR modes for Half rate optimized bearer are presented. Performance results for 8PSK AMR (FS) on a half rate channel (TCH-8PSK/AFS/HRC) are presented for two different coding schemes, one with recursive systematic code and the other with a nonsystematic code.  The performance is evaluated by FER, RBER and Class 1B BER as a function of the bit number.

# Channel coding

Channel coding for all the AMR eight modes is designed following the rules stated below:

- Uniform protection is provided to all the Class 1A bits

- Class 1B bits are protected based on the order of importance, i.e., the initial bits are given more protection than the last bits.

- Class 1A bits are placed in the first two bit positions in the 8PSK symbol

- Symbols consisting of the Class 1A bits are placed near to the TS, immediately after the SB

The 696 (116*3*2) payload bits (including SB) are segregated into SBs, Reserved bits, inband coding bits and speech bits. In the wake of inconclusive discussion on the SBs, we are not specific about the SB and RSVD fields. The inband bits coded into 12 bits.

Coded In-Band bits 		12

SBs + RSVD bits 		24

Coded Speech bits		660

Exact number of bits used for the Inband signalling SBs and RSVD bits are for FFS.

# AMR Full Rate Speech (AFS)

AMR Full Rate Speech (AFS) with 8PSK Half Rate Channel (TCH-8PSK/AFS/HRC) uses the same speech bit classification as defined in GSM 05.03 Section 3.9.4.2. Appendix A shows the bit classification and the CRC computation.

# Convolutional encoder

The speech bits, u(k), are encoded with the recursive systematic/ nonsystematic convolutional codes as summarized below. The number of output bits after puncturing is 672 for all codec modes.

| Codec mode | Rate | Number of input bits to conv. coder | Number of output bits from conv. coder | Number of punctured bits |
| --- | --- | --- | --- | --- |
| TCH/AFS12.2 | 1/3 | 250 | 750 | 108 |
| TCH/AFS10.2 | 1/4 | 210 | 840 | 204 |
| TCH/AFS7.95 | 1/4 | 165 | 660 | 24 |
| TCH/AFS7.4 | 1/5 | 154 | 770 | 140 |
| TCH/AFS6.7 | 1/5 | 140 | 700 | 70 |
| TCH/AFS5.9 | 1/6 | 124 | 744 | 120 |
| TCH/AFS5.15 | 1/6 | 109 | 654 | 30 |
| TCH/AFS4.75 | 1/7 | 101 | 707 | 89 |

Below the coding for each codec mode is specified in detail.

## TCH/AFS12.2

### TYPE-1: Recursive systematic convolutional code

The block of 250 bits {u(0)… u(249)} is encoded with the 1/3 rate convolutional code defined by the following polynomials:

G4/G6		 = 	1 + D2 + D3+ D5+ D6 / 1 + D + D2 + D3+ D4 + D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D + D2 + D3 + D4 + D6

G6/G6 	= 	1

resulting in 750 coded bits, {C(0)… C(749)} defined by:

r(k) 		= 	u(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(3k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(3k+1)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(3k+2) 	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

for k = 0, 1, ..., 249

and for the termination of the coder

r(k) 		= 	0

C(3k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(3k+1)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(3k+2) 	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

### TYPE-2: Nonsystematic convolutional code

The block of 250 bits {u(0)… u(249)} is encoded with the 1/2 rate convolutional code defined by the following polynomials:

G4 		=	 1 + D2 + D3+ D5+ D6

G5 		= 	1 + D + D4+ D6

G6		 = 	1 + D + D2 + D3+ D4+ D6

resulting in 750 coded bits, {C(0)… C(749)} defined by:

C(3k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(3k+1)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(3k+2) 	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

for k = 0, 1, ..., 249

and for the termination of the coder {u(251), u(251), u(252), u(253), u(254), u(255)} is set to {0, 0, 0, 0, 0, 0}.

### Puncturing

The 768 coded bits are punctured in such a way that the following 108 coded bits:

3(10i+5)+2 		for i = 0, 1, …, 15

3(164+i)+2 		for i=0, 1, …, 91

are not transmitted. The result is a block of 660 coded and punctured bits, P(0)...P(659) which 	are appended to the in-band bits in c as

c(k+12) 	= 	P(k)		for k = 0, 1, ..., 659.

## TCH/AFS10.2

### TYPE-1: Recursive systematic convolutional code

The block of 210 bits {u(0)... u(209)} is encoded with the 1/4 rate convolutional code defined by the following polynomials:

G4/G6		 = 	1 + D2 + D3+ D5+ D6 / 1 + D + D2 + D3 + D4+ D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D + D2 + D3 + D4+ D6

G6/G6		 = 	1

G7/G6 	= 	1 + D + D2 + D3 + D6 / 1 + D + D2 + D3 + D4+ D6

resulting in 840 coded bits, {C(0)... C(839)} defined by:

r(k)		= 	u(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(4k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(4k+1)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(4k+2)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(4k+3)	= 	r(k) + r(k-1) + r(k-2)  + r(k-3) + r(k-6)

for k = 0, 1, ..., 209

and (for termination of the coder):

r(k)		= 	0

C(4k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(4k+1)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(4k+2)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(4k+3)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 210, 211, ..., 215

### TYPE-2: Nonsystematic convolutional code

The block of 210 bits {u(0)... u(209)} is encoded with the 1/4 rate convolutional code defined by the following polynomials:

G4 		= 	1 + D2 + D3+ D5+ D6

G5 		= 	1 + D + D4+ D6

G6		= 	1 + D + D2 + D3 + D4+ D6

G7 		= 	1 + D + D2 + D3 + D6

resulting in 840 coded bits, {C(0)... C(839)} defined by:

C(4k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(4k+1)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(4k+2)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(4k+3)	= 	u(k) + u(k-1) + u(k-2)  + u(k-3) + u(k-6)

for k = 0, 1, ..., 209

and (for termination of the coder):

u(k)		= 	0

C(4k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(4k+1)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(4k+2)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(4k+3)	= 	u(k) + u(k-1) + u(k-2)  + u(k-3) + u(k-6)

for k = 210, 211, ..., 215

### Puncturing

The code is punctured in such a way that the following 204 bits:

4(2i+8)+3		 	for i = 0, 1, …, 31

4(5i+85)+2 		for i = 0, 1, …,26

4(i+75)+3 		for i=0, 1, …,144

are not transmitted. The result is a block of 660 coded and punctured bits, P(0)...P(659) which are appended to the in-band bits in c as:

c(k+12) = P(k)		for k = 0, 1, ..., 659.

## TCH/AFS7.95

### TYPE-1: Recursive systematic convolutional code

The block of 165 bits {u(0)… u(164)} is encoded with the 1/4 rate convolutional code defined by the following polynomials:

G4/G6		 = 	1 + D2 + D3+ D5+ D6 / 1 + D + D2 + D3 + D4+ D6

G5/G6		 = 	1 + D + D4+ D6 / 1 + D + D2 + D3 + D4+ D6

G6/G6 	= 	1

G7/G6		= 	1 + D + D2 + D3 + D6 / 1 + D + D2 + D3 + D4+ D6

resulting in 660 coded bits, {C(0)... C(659)} defined by:

r(k)		= 	u(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(4k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(4k+1)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(4k+2)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(4k+3)	= 	r(k) + r(k-1) + r(k-2)  + r(k-3) + r(k-6)

for k = 0, 1, ..., 164

and (for termination of the coder):

r(k)		= 	0

C(4k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(4k+1)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(4k+2)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(4k+3)	= 	r(k) + r(k-1)	 + r(k-2)  + r(k-3) + r(k-6)

for k = 165, 166, ..., 170

### TYPE-2: Nonsystematic convolutional code

The block of 165 bits {u(0)… u(164)} is encoded with the 1/4 rate convolutional code defined by the following polynomials:

G4 		= 	1 + D2 + D3+ D5+ D6

G5		 = 	1 + D + D4+ D6

G6		= 	1 + D + D2 + D3 + D4+ D6

G7 		= 	1 + D + D2 + D3 + D6

resulting in 660 coded bits, {C(0)... C(659)} defined by:

C(4k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(4k+1)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(4k+2)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(4k+3)	= 	u(k) + u(k-1) + u(k-2)  + u(k-3) + u(k-6)

for k = 0, 1, ..., 164

and (for termination of the coder):

u(k)		= 	0

C(4k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(4k+1)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(4k+2)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(4k+3)	= 	u(k) + u(k-1) + u(k-2)  + u(k-3) + u(k-6)

for k = 165, 166, ..., 170

### Puncturing

The code is punctured in such a way that the following 24 coded bits:

4(10i+10)+3 		for i=0,…,8

4(5i+100)+3 		for i=0,…,14

are not transmitted. The result is a block of 660 coded and punctured bits, P(0)...P(659) which are appended to the in-band bits in c as

c(k+12) = P(k)		for k = 0, 1, ..., 659.

## TCH/AFS7.4

### TYPE-1: Recursive systematic convolutional code

The block of 154 bits {u(0)... u(153)} is encoded with the 1/5 rate convolutional code defined by the following polynomials:

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D +D2 + D3 + D4+ D6

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D +D2 + D3 + D4+ D6

G5/G6		 = 	1 + D + D4+ D6 / 1 + D +D2 + D3 + D4+ D6

G6/G6 	= 	1

G7/G6 	= 	1 + D +D2 + D3 + D6 / 1 + D +D2 + D3 + D4+ D6

resulting in 474 coded bits, {C(0)... C(473)} defined by:

r(k)		= 	u(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(5k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(5k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(5k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(5k+3) 	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(5k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 0, 1, ..., 153

and (for termination of the coder):

r(k)		= 	0

C(5k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(5k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(5k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(5k+3) 	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(5k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 154, 155, ..., 159

### TYPE-2: Nonsystematic convolutional code

The block of 154 bits {u(0)... u(153)} is encoded with the 1/5 rate convolutional code defined by the following polynomials:

G4		= 	1 + D2 + D3+ D5+ D6

G4 		= 	1 + D2 + D3+ D5+ D6

G5 		= 	1 + D + D4+ D6

G6 		= 	1 + D +D2 + D3 + D4+ D6

G7 		= 	1 + D +D2 + D3 + D6

resulting in 474 coded bits, {C(0)... C(473)} defined by:

C(5k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(5k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(5k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(5k+3) 	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(5k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 0, 1, ..., 153

and (for termination of the coder):

u(k)		= 	0

C(5k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(5k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(5k+2)	=	 u(k) + u(k-1) + u(k-4) + u(k-6)

C(5k+3) 	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(5k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 154, 155, ..., 159

### Puncturing

The code is punctured in such a way that the following 140 bits:

5(2*i+4) 		for 		i=0,…,32

5(8i+71)+3 	for		i=0,…,13

5(i+67)+4 	for 		i=0,…,92

are not transmitted. The result is a block of 660 coded and punctured bits, P(0)...P(659) which 	are appended to the in-band bits in c as:

c(k+12) = P(k)		for 		k = 0, 1, ..., 659.

## TCH/AFS6.7

### TYPE-1: Recursive systematic convolutional code

The block of 140 bits {u(0)… u(139)} is encoded with the 1/5 rate convolutional code defined by 	the following polynomials:

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D +D2 + D3 + D4+ D6

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D +D2 + D3 + D4+ D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D +D2 + D3 + D4+ D6

G6/G6	 	= 	1

G7/G6 	= 	1 + D +D2 + D3 + D6 / 1 + D +D2 + D3 + D4+ D6

resulting in 700 coded bits, {C(0)... C(699)} defined by:

r(k)		= 	u(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(5k)		=	 r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(5k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(5k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(5k+3) 	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(5k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 0, 1, ..., 139

and (for termination of the coder):

r(k)		= 	0

C(5k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(5k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(5k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(5k+3) 	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(5k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 140, 141, ..., 145

### TYPE-2: Nonsystematic convolutional code

The block of 140 bits {u(0)... u(139)} is encoded with the 1/5 rate convolutional code defined by the following polynomials:

G4 		= 	1 + D2 + D3+ D5+ D6

G4 		= 	1 + D2 + D3+ D5+ D6

G5 		= 	1 + D + D4+ D6

G6 		= 	1 + D +D2 + D3 + D4+ D6

G7 		= 	1 + D +D2 + D3 + D6

resulting in 700 coded bits, {C(0)... C(699)} defined by:

C(5k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(5k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(5k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(5k+3) 	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(5k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 0, 1, ..., 139

and (for termination of the coder):

u(k)		= 	0

C(5k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(5k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(5k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(5k+3) 	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(5k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 140, 141, ..., 145

### Puncturing

The code is punctured in such a way that the following 70 coded bits:

5(15*i)+4 	for i=0,…,4

5(i+80)+4 	for i=0,…,64

are not transmitted. The result is a block of 660 coded bits, P(0)...P(659) which are appended to 	the in-band bits in c as

c(k+12) = P(k)		for k = 0, 1, ..., 659.

## TCH/AFS5.9

### TYPE-1: Recursive systematic convolutional code

The block of 124 bits {u(0)… u(123)} is encoded with the 1/6 rate convolutional code defined by the following polynomials:

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D+D2 + D3+ D4+ D6

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D+D2 + D3+ D4+ D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D+D2 + D3+ D4+ D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D+D2 + D3+ D4+ D6

G6/G6 	= 	1

G7/G6 	= 	1 + D+D2 + D3 + D6 / 1 + D+D2 + D3+ D4+ D6

resulting in 744 coded bits, {C(0)… C(743)} defined by:

r(k)		= 	u(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(6k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(6k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(6k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(6k+3)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(6k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(6k+5)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)for k = 0, 1, ..., 123; r(k) = 0 for k<0

and (for termination of the coder):

r(k)		= 	0

C(6k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(6k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(6k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(6k+3)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(6k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(6k+5)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 124, 125, ..., 129

### TYPE-2: Nonsystematic convolutional code

The block of 124 bits {u(0)… u(123)} is encoded with the 1/6 rate convolutional code defined by the following polynomials:

G4		= 	1 + D2 + D3+ D5+ D6

G4 		= 	1 + D2 + D3+ D5+ D6

G5 		= 	1 + D + D4+ D6

G5 		= 	1 + D + D4+ D6

G6 		= 	1 + D+D2 + D3+ D4+ D6

G7 		= 	1 + D+D2 + D3 + D6

resulting in 744 coded bits, {C(0)… C(743)} defined by:

C(6k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(6k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(6k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(6k+3)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(6k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(6k+5)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 0, 1, ..., 123;

and (for termination of the coder):

u(k)		=	0

C(6k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(6k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(6k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(6k+3)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(6k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(6k+5)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 124, 125, ..., 129

### Puncturing

The code is punctured in such a way that the following 120 coded bits:

6(2I)+5 			for 		i=0,…,25

6(4i+65)+4 		for		i=0,…,16

6(i+53)+5 		for		i=0,…,76

are not transmitted. The result is a block of 660 coded and punctured bits, P(0)...P(659) which are appended to the in-band bits in c as

c(12+k) = P(k)		for k = 0, 1, ..., 659.

## TCH/AFS5.15

### TYPE-1: Recursive systematic convolutional code

The block of 109 bits {u(0)… u(108)} is encoded with the 1/6 rate convolutional code defined by 	the following polynomials:

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D+D2 + D3+ D4+ D6

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D+D2 + D3+ D4+ D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D+D2 + D3+ D4+ D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D+D2 + D3+ D4+ D6

G6/G6	 	= 	1

G7/G6 	= 	1 + D+D2 + D3 + D6 / 1 + D+D2 + D3+ D4+ D6

resulting in 654 coded bits, {C(0)… C(653)} defined by:

r(k)		= 	u(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(6k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(6k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(6k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(6k+3)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(6k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(6k+5)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 0, 1, ..., 108; r(k) = 0 for k<0

and (for termination of the coder):

r(k)		= 	0

C(6k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(6k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(6k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(6k+3)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(6k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(6k+5)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)	for k = 109, 110, ..., 114

### TYPE-2: Nonsystematic convolutional code

The block of 109 bits {u(0)… u(108)} is encoded with the 1/6 rate convolutional code defined by the following polynomials:

G4 		=	1 + D2 + D3+ D5+ D6

G4		 = 	1 + D2 + D3+ D5+ D6

G5 		= 	1 + D + D4+ D6

G5 		= 	1 + D + D4+ D6

G6 		= 	1 + D+D2 + D3+ D4+ D6

G7 		=	1 + D+D2 + D3 + D6

resulting in 654 coded bits, {C(0)… C(653)} defined by:

C(6k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(6k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(6k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(6k+3)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(6k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(6k+5)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 0, 1, ..., 108;

and (for termination of the coder):

u(k)		= 	0

C(6k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(6k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(6k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(6k+3)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(6k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(6k+5)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)		for k = 109, 110, ..., 114

### Puncturing

The code is punctured in such a way that the following 30 coded bits:

6(4i+2)+5 			for		 i= 0, …, 13

6(4i+57)+5 			for		i=0, …, 14

and 5(4*15+58)+5

are not transmitted. The result is a block of 660 coded and punctured bits, P(0)...P(659) which 	are appended to the in-band bits in c as

c(12+k) = P(k)		for k = 0, 1, ..., 659.

## TCH/AFS4.75

### TYPE-1: Recursive systematic convolutional code

The block of 101 bits {u(0)... u(100)} is encoded with the 1/7 rate convolutional code defined by the following polynomials:

G4/G6 	= 	1 + D2 + D3+ D5+ D6 / 1 + D+D2 + D3+ D4+ D6

G4/G6		 = 	1 + D2 + D3+ D5+ D6 / 1 + D+D2 + D3+ D4+ D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D+D2 + D3+ D4+ D6

G5/G6 	= 	1 + D + D4+ D6 / 1 + D+D2 + D3+ D4+ D6

G6/G6 	= 	1

G6/G6 	= 	1

G7/G6 	= 	1 + D+D2 + D3 + D6 / 1 + D+D2 + D3+ D4+ D6

resulting in 707 coded bits, {C(0)… C(706)} defined by:

r(k)		=	u(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(7k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(7k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(7k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(7k+3)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(7k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(7k+5)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(7k+6)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 0, 1, ..., 100; r(k) = 0 for k<0

and (for termination of the coder):

r(k)		= 	0

C(7k)		= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(7k+1)	= 	r(k) + r(k-2) + r(k-3) + r(k-5) + r(k-6)

C(7k+2)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(7k+3)	= 	r(k) + r(k-1) + r(k-4) + r(k-6)

C(7k+4)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(7k+5)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-4) + r(k-6)

C(7k+6)	= 	r(k) + r(k-1) + r(k-2) + r(k-3) + r(k-6)

for k = 101, 102, ..., 106

### TYPE-2: Nonsystematic convolutional code

The block of 101 bits {u(0)... u(100)} is encoded with the 1/7 rate convolutional code defined by the following polynomials:

G4 		= 	1 + D2 + D3+ D5+ D6

G4 		= 	1 + D2 + D3+ D5+ D6

G5 		= 	1 + D + D4+ D6

G5		= 	1 + D + D4+ D6

G6 		=	1 + D+D2 + D3+ D4+ D6

G6 		= 	1 + D+D2 + D3+ D4+ D6

G7 		= 	1 + D+D2 + D3 + D6

resulting in 707 coded bits, {C(0)… C(706)} defined by:

C(7k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(7k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(7k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(7k+3)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(7k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(7k+5)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(7k+6)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 0, 1, ..., 100;

and (for termination of the coder):

u(k)		= 	0

C(7k)		= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(7k+1)	= 	u(k) + u(k-2) + u(k-3) + u(k-5) + u(k-6)

C(7k+2)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(7k+3)	= 	u(k) + u(k-1) + u(k-4) + u(k-6)

C(7k+4)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(7k+5)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-4) + u(k-6)

C(7k+6)	= 	u(k) + u(k-1) + u(k-2) + u(k-3) + u(k-6)

for k = 101, 102, ..., 106

### Puncturing

The code is punctured in such a way that the following 89 coded bits:

7(3i+2)+6 	for		i=0, .., 14

7(5i+51)+5 	for		i=0, …, 11

7(i+45)+6 	for		i=0, …, 61

are not transmitted. The result is a block of 660 coded and punctured bits, P(0)...P(659) which are appended to the inband bits in c as

c(12+k) = P(k)		for k = 0, 1, ..., 659.

# Interleaving

The coded bits c(k) are divided into two parts c1(k) and c2(k) as follows:

C1(k) 		= 	c(k)	for k=0, 1, …, 343

C2(k)	=	c(k+344)	for k=0, 1, …, 327

The first 344 bits, C1(k), are interleaved using the following formula:

I1(B,j) = C1(n,k) for k=0, 1, …, 343

b = 2 mod(k,2) + mod(k,4) / 2

j = 2 mod(39k, 43) + mod(k,8) / 4

n = 0,1,...,N,N+1,...

B = B0 + 2n + b

The next 328 bits, C2(k), are interleaved using the following formula:

I2(B,j) = c2(n,k) for k = 0, 1, …, 327;

b = 2 mod(k,2) + mod(k,4) / 2

j = 2 mod(37k, 41) + mod(k,8) / 4

n = 0,1,...,N,N+1,...

B = B0 + 2n + b

The values of b and j in dependence of k are given by Appendix B.

# Symbol Mapping

The interleaved bit streams are rearranged in following order to always keep the Class 1A bits in the first two bit positions of the 8PSK symbol. Always the third bit carries class1B bit.

S1(B,3j) 		=	I1(B,2j)

S1(B,3j+1) 	=	I1(B,2j+1)

S1(B,3j+2)	=	I2(B,j)							for 		j=0, 1, …, 42

S2(B,j)		=	I2(B,j+43)					for 		j=0, 1, …, 38

The resulting bit streams are combined into S in the following way:

S(B,j)			= 	S2(B,j)			for 	j=0, 1, …, 20

S(B,j+7)		=	S1(B,j)			for	j=0, 1, …, 42

S(B,j+50)		=	S2(B,j+21)		for	j=0, 1, …, 17

S is mapped into 8PSK symbols by pairing 3 bits at a time as follows:

Sm(B,j) 		= 	{S(B,3*j), S(B,3*j+1), S(B,3*j+2)}   		for  	j = 0, 1, …, 55

# Mapping on a Burst

The result of the interleaving and symbol mapping is a distribution of the reordered 224 symbols of a given data block, n = N, over 4 blocks using the even numbered symbols of the first 2 blocks (B = B0+2N+0,1) and the odd numbered symbols of the last 2 blocks (B = B0+2N+2,3). The reordered symbols of the following data block, n = N + 1, use the even numbered symbols of the blocks B = B0 + 2N + 2,3 (B = B0+2(N+1)+0,1) and the odd numbered symbols of the blocks B = B0 + 2(N+1) + 2,3. Continuing with the next data blocks shows that one block always carries 56 symbols of data from one data block (n = N) and 57 symbols from the next block (n = N+1), where the symbols from the data block with the higher number always are the even numbered data symbols, and those of the data block with the lower number are the odd numbered symbols.

# Simulation Results

All the simulation results are for TU3, ideal frequency hopping case. We used 1000 speech frames in the simulations. Fig. 1(a) – Fig. 1(h) show the Class 1A FER for 8PSK TCH/AFS/HRC for all the AMR modes. All these results indicate that the performance with a nonsystematic convolutional code is better than that with a recursive systematic code. Fig. 2(a) – Fig. 2(h) show the Class 1B RBER performance for all the modes. Fig. 3(a) – Fig. 3(h) show the Class 1B RBER performance as a function of bit position for non-systematic convolutional coding scenarios. These results show that the BER performance progressively degrades as a function of the bit index.

FIG. 1(a)

FIG. 1(b)

FIG. 1(c)

FIG. 1(d)

FIG. 1(e)

FIG. 1(f)

FIG. 1(g)

FIG. 1(h)

FIG. 2(a)

FIG. 2(b)

FIG. 2(c)

FIG. 2(d)

FIG. 2(e)

FIG. 2(f)

FIG. 2(g)

FIG. 2(h)

FIG. 3(a)

FIG. 3(b)

FIG. 3(c)

FIG. 3(d)

FIG. 3(e)

FIG. 3(f)

FIG. 3(g)

FIG. 3(h)

# Conclusions and Recommendations

Simulation results show that the non-systematic codes proposed in this contribution are superior to recursive systematic convolutional codes.  A complete coding, puncturing, interleaving, bit to symbol mapping, and burst mapping scheme has been proposed for all of the 8-PSK half-rate AMR speech codec modes.  The recommendation is to review and reach a consensus regarding the choice of non-systematic codes for 8-PSK AMR half-rate optimized voice bearers vs. recursive systematic convolutional codes.

# Appendix A

The protection classes are:

1a	-	Data protected with the CRC and the convolution code.
1b 	-	Data protected with the convolution code.
No unprotected bits are used.

The number of class 1 (sum of class 1a and 1b), class 1a and class 1b bits for each codec mode is shown below:

| Codec Mode | Number of speech bits delivered per block | Number of class 1 bits per block | Number of class 1a bits per block | Number of class 1b bits per block |
| --- | --- | --- | --- | --- |
| TCH/AFS12.2 | 244 | 244 | 81 | 163 |
| TCH/AFS10.2 | 204 | 204 | 65 | 139 |
| TCH/AFS7.95 | 159 | 159 | 75 | 84 |
| TCH/AFS7.4 | 148 | 148 | 61 | 87 |
| TCH/AFS6.7 | 134 | 134 | 55 | 79 |
| TCH/AFS5.9 | 118 | 118 | 55 | 63 |
| TCH/AFS5.15 | 103 | 103 | 49 | 54 |
| TCH/AFS4.75 | 95 | 95 | 39 | 56 |

## A.1	Parity for speech frames

The basic parameters for each codec mode for the first encoding step are shown below:

| Codec mode | Speech encoded bits (Kd) | CRC protected bits (Kd1a) | Number of bits after first encoding step (Ku = Kd + 6) |
| --- | --- | --- | --- |
| TCH/AFS12.2 | 244 | 81 | 250 |
| TCH/AFS10.2 | 204 | 65 | 210 |
| TCH/AFS7.95 | 159 | 75 | 165 |
| TCH/AFS7.4 | 148 | 61 | 154 |
| TCH/AFS6.7 | 134 | 55 | 140 |
| TCH/AFS5.9 | 118 | 55 | 124 |
| TCH/AFS5.15 | 103 | 49 | 109 |
| TCH/AFS4.75 | 95 | 39 | 101 |

## A.2	CRC Computation

A 6-bit CRC is used for error-detection. These 6 parity bits are generated by the cyclic generator polynomial: g(D) = D6 + D5 + D3 + D2 + D1 + 1 from the first Kd1a bits of class 1, where Kd1a refers to number of bits in protection class 1a as shown above for each codec mode. The encoding of the cyclic code is performed in a systematic form, which means that, in GF(2), the polynomial:

d(0)D(Kd1a+5) + d(1)D(Kd1a+4) +... + d(Kd1a-1)D(6) + p(0)D(5) +…+ p(4)D+ p(5)

where p(0), p(1) … p(5) are the parity bits, when divided by g(D), yields a remainder equal to:

1+ D + D2 + D3 + D4 + D5.

The information and parity bits are merged:

u(k) = d(k)				for k = 0, 1, …, Kd1a-1

u(k) = p(k-Kd1a) 			for k = Kd1a, Kd1a+1, …, Kd1a+5

u(k) = d(k-6)				for k = Kd1a+6, Kd1a+7, …, Ku-1

Thus, after the first encoding step u(k) will be defined by the following contents for each codec mode:

TCH/AFS12.2:

u(k) = d(k)				for k = 0, 1, …, 80

u(k) = p(k-81)			for k = 81, 82, …, 86

u(k) = d(k-6)				for k = 87, 88, …, 249

TCH/AFS10.2:

u(k) = d(k)				for k = 0, 1, ..., 64

u(k) = p(k-65)			for k = 65, 66, ..., 70

u(k) = d(k-6)				for k = 71, 72, ..., 209

TCH/AFS7.95:

u(k) = d(k)				for k = 0, 1, …, 74

u(k) = p(k-75)			for k = 75, 76, …, 80

u(k) = d(k-6)				for k = 81, 82, …, 164

TCH/AFS7.4:

u(k) = d(k)				for k = 0, 1, …, 60

u(k) = p(k-61)			for k = 61, 62, …, 66

u(k) = d(k-6)				for k = 67, 68, …, 153

TCH/AFS6.7:

u(k) = d(k)				for k = 0, 1, …, 54

u(k) = p(k-55)			for k = 55, 56, …, 60

u(k) = d(k-6)				for k = 61, 62, …, 139

TCH/AFS5.9:

u(k) = d(k)				for k = 0, 1, …, 54

u(k) = p(k-55)			for k = 55, 56, …, 60

u(k) = d(k-6)				for k = 61, 62, …, 123

TCH/AFS5.15:

u(k) = d(k)				for k = 0, 1, …, 48

u(k) = p(k-49)			for k = 49, 50, …, 54

u(k) = d(k-6)				for k = 55, 56, …, 108

TCH/AFS4.75:

u(k) = d(k)				for k = 0, 1, ..., 38

u(k) = p(k-39)			for k = 39, 40, ..., 44

u(k) = d(k-6)				for k = 45, 46, ..., 100

# APPENDIX B

Table B1. Interleaving matrix for the first 344 speech bits

for 8-PSK TCH/AFR/HRC.

| b= | 0 | 1 | 2 | 3 |  |
| --- | --- | --- | --- | --- | --- |
| j=0 | k=0 | 258 | 129 | 43 |  |
| 1 | 172 | 86 | 301 | 215 |  |
| 2 | 32 | 290 | 161 | 75 |  |
| 3 | 204 | 118 | 333 | 247 |  |
| 4 | 64 | 322 | 193 | 107 |  |
| 5 | 236 | 150 | 21 | 279 |  |
| 6 | 96 | 10 | 225 | 139 |  |
| 7 | 268 | 182 | 53 | 311 |  |
| 8 | 128 | 42 | 257 | 171 |  |
| 9 | 300 | 214 | 85 | 343 |  |
| 10 | 160 | 74 | 289 | 203 |  |
| 11 | 332 | 246 | 117 | 31 |  |
| 12 | 192 | 106 | 321 | 235 |  |
| 13 | 20 | 278 | 149 | 63 |  |
| 14 | 224 | 138 | 9 | 267 |  |
| 15 | 52 | 310 | 181 | 95 |  |
| 16 | 256 | 170 | 41 | 299 |  |
| 17 | 84 | 342 | 213 | 127 |  |
| 18 | 288 | 202 | 73 | 331 |  |
| 19 | 116 | 30 | 245 | 159 |  |
| 20 | 320 | 234 | 105 | 19 |  |
| 21 | 148 | 62 | 277 | 191 |  |
| 22 | 8 | 266 | 137 | 51 |  |
| 23 | 180 | 94 | 309 | 223 |  |
| 24 | 40 | 298 | 169 | 83 |  |
| 25 | 212 | 126 | 341 | 255 |  |
| 26 | 72 | 330 | 201 | 115 |  |
| 27 | 244 | 158 | 29 | 287 |  |
| 28 | 104 | 18 | 233 | 147 |  |
| 29 | 276 | 190 | 61 | 319 |  |
| 30 | 136 | 50 | 265 | 179 |  |
| 31 | 308 | 222 | 93 | 7 |  |
| 32 | 168 | 82 | 297 | 211 |  |
| 33 | 340 | 254 | 125 | 39 |  |
| 34 | 200 | 114 | 329 | 243 |  |
| 35 | 28 | 286 | 157 | 71 |  |
| 36 | 232 | 146 | 17 | 275 |  |
| 37 | 60 | 318 | 189 | 103 |  |
| 38 | 264 | 178 | 49 | 307 |  |
| 39 | 92 | 6 | 221 | 135 |  |
| 40 | 296 | 210 | 81 | 339 |  |
| 41 | 124 | 38 | 253 | 167 |  |
| 42 | 328 | 242 | 113 | 27 |  |
| 43 | 156 | 70 | 285 | 199 |  |
| 44 | 16 | 274 | 145 | 59 |  |
| 45 | 188 | 102 | 317 | 231 |  |
| 46 | 48 | 306 | 177 | 91 |  |
| 47 | 220 | 134 | 5 | 263 |  |
| 48 | 80 | 338 | 209 | 123 |  |
| 49 | 252 | 166 | 37 | 295 |  |
| 50 | 112 | 26 | 241 | 155 |  |
| 51 | 284 | 198 | 69 | 327 |  |
| 52 | 144 | 58 | 273 | 187 |  |
| 53 | 316 | 230 | 101 | 15 |  |
| 54 | 176 | 90 | 305 | 219 |  |
| 55 | 4 | 262 | 133 | 47 |  |
| 56 | 208 | 122 | 337 | 251 |  |
| 57 | 36 | 294 | 165 | 79 |  |
| 58 | 240 | 154 | 25 | 283 |  |
| 59 | 68 | 326 | 197 | 111 |  |
| 60 | 272 | 186 | 57 | 315 |  |
| 61 | 100 | 14 | 229 | 143 |  |
| 62 | 304 | 218 | 89 | 3 |  |
| 63 | 132 | 46 | 261 | 175 |  |
| 64 | 336 | 250 | 121 | 35 |  |
| 65 | 164 | 78 | 293 | 207 |  |
| 66 | 24 | 282 | 153 | 67 |  |
| 67 | 196 | 110 | 325 | 239 |  |
| 68 | 56 | 314 | 185 | 99 |  |
| 69 | 228 | 142 | 13 | 271 |  |
| 70 | 88 | 2 | 217 | 131 |  |
| 71 | 260 | 174 | 45 | 303 |  |
| 72 | 120 | 34 | 249 | 163 |  |
| 73 | 292 | 206 | 77 | 335 |  |
| 74 | 152 | 66 | 281 | 195 |  |
| 75 | 324 | 238 | 109 | 23 |  |
| 76 | 184 | 98 | 313 | 227 |  |
| 77 | 12 | 270 | 141 | 55 |  |
| 78 | 216 | 130 | 1 | 259 |  |
| 79 | 44 | 302 | 173 | 87 |  |
| 80 | 248 | 162 | 33 | 291 |  |
| 81 | 76 | 334 | 205 | 119 |  |
| 82 | 280 | 194 | 65 | 323 |  |
| 83 | 108 | 22 | 237 | 151 |  |
| 84 | 312 | 226 | 97 | 11 |  |
| 85 | 140 | 54 | 269 | 183 |  |
| Table B2. Interleaving matrix for the second 324 speech bits for 8-PSK TCH/AFR/HRC. |  |
| b= | 0 | 1 | 2 | 3 |  |
| j=0 | k=0 | 82 | 41 | 123 |  |
| 1 | 164 | 246 | 205 | 287 |  |
| 2 | 256 | 10 | 297 | 51 |  |
| 3 | 92 | 174 | 133 | 215 |  |
| 4 | 184 | 266 | 225 | 307 |  |
| 5 | 20 | 102 | 61 | 143 |  |
| 6 | 112 | 194 | 153 | 235 |  |
| 7 | 276 | 30 | 317 | 71 |  |
| 8 | 40 | 122 | 81 | 163 |  |
| 9 | 204 | 286 | 245 | 327 |  |
| 10 | 296 | 50 | 9 | 91 |  |
| 11 | 132 | 214 | 173 | 255 |  |
| 12 | 224 | 306 | 265 | 19 |  |
| 13 | 60 | 142 | 101 | 183 |  |
| 14 | 152 | 234 | 193 | 275 |  |
| 15 | 316 | 70 | 29 | 111 |  |
| 16 | 80 | 162 | 121 | 203 |  |
| 17 | 244 | 326 | 285 | 39 |  |
| 18 | 8 | 90 | 49 | 131 |  |
| 19 | 172 | 254 | 213 | 295 |  |
| 20 | 264 | 18 | 305 | 59 |  |
| 21 | 100 | 182 | 141 | 223 |  |
| 22 | 192 | 274 | 233 | 315 |  |
| 23 | 28 | 110 | 69 | 151 |  |
| 24 | 120 | 202 | 161 | 243 |  |
| 25 | 284 | 38 | 325 | 79 |  |
| 26 | 48 | 130 | 89 | 171 |  |
| 27 | 212 | 294 | 253 | 7 |  |
| 28 | 304 | 58 | 17 | 99 |  |
| 29 | 140 | 222 | 181 | 263 |  |
| 30 | 232 | 314 | 273 | 27 |  |
| 31 | 68 | 150 | 109 | 191 |  |
| 32 | 160 | 242 | 201 | 283 |  |
| 33 | 324 | 78 | 37 | 119 |  |
| 34 | 88 | 170 | 129 | 211 |  |
| 35 | 252 | 6 | 293 | 47 |  |
| 36 | 16 | 98 | 57 | 139 |  |
| 37 | 180 | 262 | 221 | 303 |  |
| 38 | 272 | 26 | 313 | 67 |  |
| 39 | 108 | 190 | 149 | 231 |  |
| 40 | 200 | 282 | 241 | 323 |  |
| 41 | 36 | 118 | 77 | 159 |  |
| 42 | 128 | 210 | 169 | 251 |  |
| 43 | 292 | 46 | 5 | 87 |  |
| 44 | 56 | 138 | 97 | 179 |  |
| 45 | 220 | 302 | 261 | 15 |  |
| 46 | 312 | 66 | 25 | 107 |  |
| 47 | 148 | 230 | 189 | 271 |  |
| 48 | 240 | 322 | 281 | 35 |  |
| 49 | 76 | 158 | 117 | 199 |  |
| 50 | 168 | 250 | 209 | 291 |  |
| 51 | 4 | 86 | 45 | 127 |  |
| 52 | 96 | 178 | 137 | 219 |  |
| 53 | 260 | 14 | 301 | 55 |  |
| 54 | 24 | 106 | 65 | 147 |  |
| 55 | 188 | 270 | 229 | 311 |  |
| 56 | 280 | 34 | 321 | 75 |  |
| 57 | 116 | 198 | 157 | 239 |  |
| 58 | 208 | 290 | 249 | 3 |  |
| 59 | 44 | 126 | 85 | 167 |  |
| 60 | 136 | 218 | 177 | 259 |  |
| 61 | 300 | 54 | 13 | 95 |  |
| 62 | 64 | 146 | 105 | 187 |  |
| 63 | 228 | 310 | 269 | 23 |  |
| 64 | 320 | 74 | 33 | 115 |  |
| 65 | 156 | 238 | 197 | 279 |  |
| 66 | 248 | 2 | 289 | 43 |  |
| 67 | 84 | 166 | 125 | 207 |  |
| 68 | 176 | 258 | 217 | 299 |  |
| 69 | 12 | 94 | 53 | 135 |  |
| 70 | 104 | 186 | 145 | 227 |  |
| 71 | 268 | 22 | 309 | 63 |  |
| 72 | 32 | 114 | 73 | 155 |  |
| 73 | 196 | 278 | 237 | 319 |  |
| 74 | 288 | 42 | 1 | 83 |  |
| 75 | 124 | 206 | 165 | 247 |  |
| 76 | 216 | 298 | 257 | 11 |  |
| 77 | 52 | 134 | 93 | 175 |  |
| 78 | 144 | 226 | 185 | 267 |  |
| 79 | 308 | 62 | 21 | 103 |  |
| 80 | 72 | 154 | 113 | 195 |  |
| 81 | 236 | 318 | 277 | 31 |  |

# Footnotes

This expression is equivalent to writing as C(3k+2) 	= 	u(k)