3GPP TSG GERAN Ad Hoc	GAHW-000017
on Release 2000 and Beyond #2	Agenda Item 6.1.3

Munich, Germany

9-13 October 2000

Source:  Nortel Networks

Relationship Between GERAN UE RRC Modes and RRC States

1	Introduction	3

2	List of Acronyms	3

3	GPRS/EGPRS and GERAN Mobility Management States and Radio Resource Modes	4

3.1	GPRS/EGPRS Release 1999	4

3.2	GERAN Release 2000	5

4	GPRS/EGPRS, UTRAN, and GERAN User and Control Planes	6

4.1	GPRS/EGPRS, UTRAN and GERAN User Planes	6

4.2	GPRS/EGPRS, UTRAN, and GERAN Control Planes	7

5	UTRAN and GERAN RRC Connection Establishment Procedure	8

6	UTRAN and GERAN Signaling Radio Bearers	8

6.1	UTRAN Signaling Radio Bearers	8

6.2	GERAN Signaling Radio Bearers	10

7	Mapping Radio Bearer Identities to Temporary Block Flows	10

8	Conclusions and Recommendations	10

9	References	11

# Introduction

This contribution discusses the relationship between GERAN UE RRC modes and RRC states and the implications that this relationship has on the mapping of Signaling Radio Bearers (SRBs) and Radio Bearers (RBs) identities onto Temporary Block Flows (TBFs).  The contribution is also intended to open up a dialogue regarding the GERAN control plane.

# List of Acronyms

3GPP			3rd Generation Partnership Program

AAL5			ATM Adaptation Layer type 5

ATM			Asynchronous Transfer Mode

BN				Bit Number

BSC			Base Station Controller

BSS			Base Station System

BSSGP		Base Station System GPRS Protocol

BTS			Base Transceiver Station

DTM			Dual Transfer Mode

EDGE			Enhanced Data Rates for Global Evolution

EGPRS		Enhanced General Packet Radio Service

FFS			For Further Study

GCRI			GERAN Contention Resolution Identity

GERAN		GSM/EDGE Radio Access Network

GGSN			Gateway GPRS Support Node

GMM			GPRS Mobility Management

GPRS			General Packet Radio Service

G-RNTI		GERAN-RNTI

GSM			Global System for Mobile Communications

GTP			GPRS Tunneling Protocol

IE				Information Element

IMSI			International Mobile Subscriber Identity

IP				Internet Protocol

LLC			Logical Link Control

MAC			Medium Access Control

MM			Mobility Management

MS			Mobile Station

NAS			Non-Access Stratum

PDCH			Packet Data Channel

PDCP			Packet Data Convergence Protocol

PDP			Packet Data Protocol

PDU			Protocol Data Unit

PS				Packet Switched

PTMSI		Packet-Temporary Mobile Subscriber Identity

RAB			Radio Access Bearer

RANAP		Radio Access Network Application Protocol

RB				Radio Bearer

RLC			Radio Link Control

RNTI			Radio Network Temporary Identifier

RR				Radio Resource

RRC			Radio Resource Control

RT				Real-Time

SCCP			Signaling Connection Control Part

SGSN			Serving GPRS Support Node

SM			Session Management

SMS			Short Message Service

SNDCP		SubNetwork Dependent Convergence Protocol

SRB			Signaling Radio Bearer

TBF			Temporary Block Flow

TFI			Temporary Flow Identifier

TLLI			Temporary Logical Link Identifier

TS				Training Sequence

UDP			User Datagram Protocol

UE				User Equipment

UMTS			Universal Mobile Telecommunications Services

U-RNTI		UTRAN-RNTI

UTRAN		UMTS Terrestrial Radio Access Network

# GPRS/EGPRS and GERAN Mobility Management States and Radio Resource Modes

## GPRS/EGPRS Release 1999

GPRS/EGPRS Release 1999 is, in a sense, a connectionless service (i.e., a permanent MS-to-BSS/network Radio Resource (RR) connection is not required over the air interface in order to transfer data).  Uplink and downlink data transfer is done via a Temporary Block Flow (TBF) establishment.

A TBF is a physical connection used by two RR entities to support the unidirectional transfer of LLC PDUs on packet data physical channels.  The TBF is allocated radio resources on one or more PDCHs and comprises a number of RLC/MAC blocks carrying one or more LLC PDUs.  A TBF is temporary and is maintained only for the duration of the data transfer (i.e., until there are no more RLC/MAC blocks to be transmitted and, in RLC acknowledged mode, until all of the transmitted RLC/MAC blocks have been successfully acknowledged by the receiving entity).

Therefore, once a GPRS/EGPRS Release 1999 mobile station is GPRS attached and once a PDP context has been activated, uplink and downlink data transfer can occur without any need for a permanent MS-to-BSS/network RR connection.

Table 1 illustrates a correspondence between GPRS/EGPRS RR operating modes and GPRS/EGPRS MM states (non-DTM capable MS) [1].

| RR BSS | Packet transfer mode | Measurement report reception | No state | No state | No state |
| --- | --- | --- | --- | --- | --- |
| RR MS | Packet transfer mode | Packet idle mode | Packet idle mode | No state |
| GMM (NSS and MS) | Ready state | Standby state | Idle state |

Table 1. Correspondence between GPRS/EGPRS RR operating modes and GPRS/EGPRS MM states (non-DTM mode).

## GERAN Release 2000

Since GERAN Release 2000 will reuse (as much as possible), the UTRAN user plane protocols (and most likely, the UTRAN control plane protocols, although this is FFS), GERAN Release 2000 mobile stations will require a permanent MS-to-BSS/network Radio Resource Control (RRC) connection before uplink and downlink data transfer can occur.  This will require a separate user plane protocol stack (above the RLC/MAC/PHY layer level) and most likely a separate control plane protocol stack (also above the RLC/MAC/PHY layer level).  The consequences of this are different messages, different protocol discriminators, different procedures, etc. (e.g., radio bearers (RBs) in additional to TBFs).  For GERAN Release 2000, this means that the RBs must be mapped to the TBFs.

Table 2 illustrates a correspondence between GERAN RRC operating modes and GERAN MM states.

| RRC GERAN | Connected mode (Cell_DCH, Cell_FACH, Cell_PCH, GRA_PCH states) | Measurement report reception: Connected mode (Cell_DCH, Cell_FACH states) | Idle mode | No state |
| --- | --- | --- | --- | --- |
| RRC MS | Connected mode (Cell_DCH, Cell_FACH, Cell_PCH, GRA_PCH states) | Connected mode (Cell_DCH, Cell_FACH states) | Idle mode | No state |
| PMM ( CN and MS) | Connected state | Idle state | Detached state |

Table 2. Correspondence between GERAN RRC operating modes and GERAN MM states.

As shown in Table 2, the two basic operational RRC modes of a GERAN UE are idle mode and connected mode.  The connected mode can be further divided into service states, which define what kind of physical channels a UE is using.  Figure 1 shows the main RRC service states in the connected mode.  It also shows the transitions between idle mode and connected mode and the possible transitions within the connected mode [2].

Figure 1. GERAN UE RRC modes and RRC states in connected mode.

# GPRS/EGPRS, UTRAN, and GERAN User and Control Planes

## GPRS/EGPRS, UTRAN and GERAN User Planes

Figures 2 and 3 illustrate the GPRS/EGPRS and UTRAN user plane (MS-GGSN), respectively [3].  Figure 4 shows the user plane for GPRS/EGPRS and GERAN (MS-SGSN) that is included in the GERAN Stage 2 description [4].

Figure 2. User plane for GPRS/EGPRS (MS-GGSN).

Figure 3. User plane for UTRAN (MS-GGSN).

Figure 4. User plane for GPRS/EGPRS and GERAN (MS-SGSN) [5].

## GPRS/EGPRS, UTRAN, and GERAN Control Planes

Figures 5 and 6 illustrate the GPRS/EGPRS and UTRAN control plane (MS-SGSN), respectively [3].  The control plane for GPRS/EGPRS and GERAN (MS-SGSN) is not included in the GERAN Stage 2 description.  It is FFS [4].

Figure 5. Control plane for GPRS/EGPRS (MS-SGSN).

Figure 6. Control plane for UTRAN (MS-SGSN).

# UTRAN and GERAN RRC Connection Establishment Procedure

The UTRAN and GERAN RRC connection establishment procedure is illustrated in Figure 7.

Figure 7. UTRAN and GERAN RRC connection establishment procedure.

# UTRAN and GERAN Signaling Radio Bearers

## UTRAN Signaling Radio Bearers

For UTRAN, Signaling Radio Bearers (SRBs) are assigned to the UE during the RRC connection establishment procedure (via the RRC Connection Setup message).  The SRBs are identified by a RB identity as follows [2]:

| Information Element/Group name | Need | Multi | Type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| RB identity | MP |  | Integer (0 … 31) | Values 0-4 shall only be used for signaling radio bearers |

Table 3. RB identity.

For UTRAN, the RRC connection establishment procedure creates three (optionally four) Signaling Radio Bearers (SRBs) designated by the RB identities 0, 1, 2, and 3.  The SRBs can later be created, reconfigured, or even deleted with the normal RB control procedures.  The SRBs are used for RRC signaling according to the following rules:

- RB 0 is used for all messages sent on the DCCH and RLC-UM.

- RB 1 is used for all message sent on the DCCH and RLC-AM, except Direct Transfer messages.

- RB 2 is used for Direct Transfer messages (using DCCH and RLC-AM), which carry higher layer signaling.  The reason for reserving a dedicated signaling radio bearer for the Direct Transfer messages is to enable prioritization of UE-UTRAN signaling over UE-CN signaling by using the RLC services (there is no need for extra RRC functionality).

- RB 3 is optional and, if it exists, is also used for the Direct Transfer messages (using DCCH and RLC-AM).  With two SRBs carrying higher layer signaling, UTRAN can handle prioritization on signaling, RB 3 being used for "low priority" and RB 2 for "high priority" NAS signaling.  The priority level is indicated in RRC with the actual NAS message to be carried over the radio.  An example of low priority signaling might be SMS.

- For RRC messages utilizing transparent mode RLC (e.g., Cell Update, RRC Connection Re-establishment Request), [2] says only that any RB number above 3 can be used.

GSMA ISG has created a typical parameters set document for layer 1 and 2 configurations preferred by operators to ensure interoperability [5].  For heuristic purposes, Table 4 illustrates transport channel parameters for uplink 1.7 kbps SRBs for logical channel DCCH [5].

| Higher layer | RAB/signaling RB | SRB#0 | SRB#1 | SRB#2 | SRB#3 |
| --- | --- | --- | --- | --- | --- |
|  | User of Radio Bearer | RRC | RRC | NAS_DT High prio | NAS_DT Low prio |
| RLC | Logical channel type | DCCH | DCCH | DCCH | DCCH |
|  | RLC mode | UM | AM | AM | AM |
|  | Payload sizes, bit | 136 | 128 | 128 | 128 |
|  | Max data rate, bps | 1700 | 1600 | 1600 | 1600 |
|  | RLC header, bit | 8 | 16 | 16 | 16 |
| MAC | MAC header, bit | 4 | 4 | 4 | 4 |
|  | MAC multiplexing | 4 logical channel multiplexing |
| Layer 1 | TrCH type | DCH |
|  | TB sizes, bit | 148 |
|  | TFS | TF0, bits | 0x148 |
|  |  | TF1, bits | 1x148 |
|  | TTI, ms | 80 |
|  | Coding type | CC 1/3 |
|  | CRC, bit | 16 |
|  | Max number of bits/TTI before rate matching | 516 |
|  | Uplink: Max number of bits/radio frame before rate matching | 65 |

Table 4. Transports channel parameters for uplink 1.7 kbps SRBs for DCCH.

## GERAN Signaling Radio Bearers

GERAN SRBs are FFS.

# Mapping Radio Bearer Identities to Temporary Block Flows

For many services, a primary PDP context and a secondary PDP context will be activated, each having at least one Radio Access Bearer (RAB) and one RB.  If four SRBs are also required, a total of 6 RB identities would need to be mapped to a TBF if maximum service flexibility and efficiency are desired.  As shown in Table 3, an RB identity comprises 5 bits.  How and where to map the RB identities onto the TBF is FFS.

# Conclusions and Recommendations

This contribution discussed the relationship between GERAN UE RRC modes and RRC states and the implications that this relationship has on mapping Radio Bearer (RB) identities to Temporary Block Flows (TBFs).  Two basic problems were identified:

- How many SRBs and RBs should be mapped to a single TBF for maximum service flexibility and efficiency?

- Where should the multiplexing be done (e.g., at the PDCP or the RLC/MAC layer)?

The recommendation is to review and discuss.

# References

[1]	ETSI, GSM 03.64 "Digital Cellular Telecommunications System (Phase 2+); General Packet Radio Service (GPRS); Stage 2", Ver, 8.5.0, Release 1999.

[2]	3GPP, TS 25.331 "RRC Protocol Specification", Ver. 3.3.0, Release 1999.

[3]	3GPP, TS 23.060 "General Packet Radio Service (GPRS); Service Description; Stage 2", Ver. 3.4.0, Release 1999.

[4]	Tdoc GP-000471 "GERAN Overall Description, Stage 2", 3GPP TSG GERAN #1, Seattle,  WA, August 28-September 1, 2000.

[5]	Tdoc RP-000447 "Typical Radio Interface Parameter Sets, Ver. 1.3", Source: GSMA ISG, 3GPP TSG RAN #9, Hawaii, September 20-22, 2000.