# Source: Ericsson

##### Signalling for Header Removal in GERAN

# Introduction

In GERAN, removal of IP/UDP/RTP headers will be introduced to provide a spectrum efficient means of transporting the voice packets over the air interface.

In header removal, the transport and network protocol layers are terminated at the network side (in the downlink), and the payload only is transported to the mobile station. It is then up to the MS if the headers are regenerated or not. In the uplink, the IP/UDP/RTP headers are generated at the BSC, and then transported through the network.

Over the air interface, a dedicated channel optimised for speech is used.

This paper analyses the need of signalling prior to deploying header removal over the air interface, and proposes a way of carrying out the necessary signalling.

# Signalling needs

In the scenario envisioned, a call is initiated by a PDP context activation and a RAB is set up for control signalling. Control messages (e.g. SIP) are exchanged over the associated RAB.

Following the call control, a secondary PDP context will be activated for the user plane data (the RTP stream). In this secondary PDP context, the source IP address and source and destination UDP port numbers are transported from the MS transparently through the SGSN to the GGSN in a Traffic Flow Template (TFT). The SGSN will initiate the establishment of a new real time RAB to be used for the RTP flow.

In a header removal scheme, one removal/regeneration entity is located in the MS and the other in the BSC. In uplink packet transfer, the regenerator (in the BSC) will use a table lookup method to map the incoming packets from a specific RAB onto IP/UDP/RTP packets to be transported through the CN.

## RTP Header Removal and Regeneration

When regenerating RTP-packets at the network side, the BSC can base the time stamp on the time elapsed since the start of the call. The sequence numbers can also be generated correctly if there is no packet loss. How the packet loss situation is handled is FFS.

If RTP packet regeneration is needed by the VoIP application in the MS, the MS will have to generate RTP Sequence Numbers and Time Stamps.

## UDP/IP Header Removal and Regeneration

The following information needs to be known at the BSC in order for it to regenerate the network and transport headers:

- Source and destination IP address

- Source and destination UDP port number

# Proposed solution

It is assumed that the MS has already been assigned an IP address by the GGSN in the PDP context procedure. The Secondary PDP context procedure is carried out in conjunction with the setup of a new RAB for the user plane. This signalling is terminated in the SGSN.

Following the initial PDP Context Activation Procedure, the following flow would take place:

# Figure 1. Proposed Secondary PDP Context Activation and RAB Assignment Procedure

The Secondary PDP Context Activation Request sent by the MS contains a TFT specifying the Source IP address as well as the Source and Destination UDP Ports. The Destination IP address is known from the PDP context activation procedure. A message will have to be introduced over the Iu interface, communicating the information contained in the TFT to the BSC. This is sent in the RAB establishment procedure as depicted in Message 4 of Figure 1.

The inclusion of the TFT in this field is the only modification to the existing flow in current standards. Furthermore, no extra delays are introduced, and no extra bits need to be transmitted over the air interface.

# Conclusion

In the solution described in Section 3, the necessary information is transmitted in the RAB Assignment Procedure.

It is proposed to use this signalling solution for header removal in GERAN.