Source: Lucent Technologies

Proposed Changes to the GERAN Stage-2 Description: Physical Layer

Introduction

This contribution proposes following changes to section 6.8 (Physical Layer) of the GERAN stage-2 description.

- Removal of the reference of multiplexing of PDTCH and PACCH only within the silent periods of TCH over DPSCH (section 6.8.5.1 and 6.8.5.2). This reference is not consistant with the GERAN R00 multiplexing requirements.

- Clarification of channel coding options for PDTCH (section 6.8.7).

Proposed Stage-2 Changes

### Mapping of logical channels onto physical subchannels

#### DPSCH full rate

Excluding CBCH, broadcast channels and common control type channels, the following channel combinations are possible for a DPSCH full rate:

- TCH/F + FACCH/F + SACCH/TF

- TCH/F + FACCH/F + SACCH/TF  + PDTCH/F + PACCH/F

- PDTCH/F + PACCH/F + SACCH/TF

##### Multiframe mapping of logical channels onto DPSCH/F

Figure 1 shows the multiframe mapping of the logical channels for DPSCH/F.

| frame number |
| --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 |
| D | D | D | D | D | D | D | D | D | D | D | D | S | D | D | D | D | D | D | D | D | D | D | D | D | i |
| D | User Traffic | S | SACCH | i | Idle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Figure 1. DPSCH/F – Multiframe mapping of logical channels

#### DPSCH half rate

The following channel combinations are possible for a DPSCH half rate:

- TCH/H + FACCH/H + SACCH/TH

- TCH/H + FACCH/H + SACCH/TH  + PDTCH/H + PACCH/H

- PDTCH/H + PACCH/H + SACCH/TH

##### Multiframe mapping of logical channels onto DPSCH/H

Figure 3 shows the multiframe mapping of the logical channels for DPSCH/H.

| frame number - subchannel 0 |
| --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 |
| D | i | D | i | D | i | D | i | D | i | D | i | S | D | i | D | i | D | i | D | i | D | i | D | I | i |
| frame number - subchannel 1 |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 |
| i | D | i | D | i | D | i | D | i | D | i | D | i | i | D | i | D | i | D | i | D | i | D | i | D | S |
| D | User Traffic | S | SACCH | i | Idle |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Figure 3. DPSCH/H – Multiframe mapping of logical channels

### Channel Coding

Table 2: Channel Coding

| Logical Channel | Mod. | Radio Block / Frame Size (Bits) | SB (1) | Channel Coding | Interleaving |  |  | Physical Subchannel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Type | Rate | Type | Depth (bursts) |  |  |  |
| TCH/AFS | GMSK | 464 | 8 | CC | See GSM 05.03 | diag | 8 |  |  | DPSCH/F |
|  | 8PSK | 1392 | 24 | CC |  |  |  |  |  |  |
| TCH/AHS | GMSK | 232 | 4 | CC |  |  | 4 |  |  | DPSCH/H |
|  | 8PSK | 696 | 12 | CC |  |  |  |  |  |  |
| TCH/AQS | 8PSK | 348 | 6 | CC |  |  | 2 |  |  | DPSCH/Q |
| TCH/F | GMSK | 464 | 8 | CC |  | diag | 19 |  |  | DPSCH/F (2) |
|  | 8PSK | 1392 | 24 | RS+CC |  |  |  |  |  |  |
| TCH/H | GMSK | 464 | 8 | CC |  |  |  |  |  | DPSCH/H (2) |
|  | 8PSK | 1392 | 12 | RS+CC |  |  |  |  |  |  |
| PDTCH/F | GMSK | 464 | 12 | CC | See GSM 03.64 | rect | 4 |  |  | SPSCH/F |
|  |  |  |  |  |  |  |  |  |  | DPSCH/F |
|  |  |  | 12 |  |  |  |  |  |  |  |
|  | 8PSK | 1392 | 8 |  |  | rect | 4 |  |  | SPSCH/F |
|  |  |  |  |  |  |  |  |  |  | DPSCH/F |
|  |  |  | 8 |  |  |  |  |  |  |  |
| PDTCH/H | GMSK | 464 | 12 | CC | See GSM 03.64 | rect | 4 |  |  | SPSCH/H |
|  |  |  |  |  |  |  |  |  |  | DPSCH/H |
|  |  |  | 12 |  |  |  |  |  |  |  |
|  | 8PSK | 1392 | 8 |  |  | rect | 4 |  |  | SPSCH/H |
|  |  |  |  |  |  |  |  |  |  | DPSCH/H |
|  |  |  | 8 |  |  |  |  |  |  |  |
| The number of Stealing Bits (SB) is ffs For DPSCH, whether TCH or PDTCH or both may be used is ffs. CC: Convolutional Code RS: Reed Solomon code |

Editor's Note: the table above remains to be completed.