3GPP TSG GERAN Adhoc #2	Tdoc GAHW-000039

Munich, Germany	Agenda Items 6.1.3

October 9-13, 2000

Source: Lucent Technologies

GERAN RRC States

Introduction

This contribution is an updated version of [10]. This contribution introduces a Release 2000 RRC State model to support the proposed GERAN design as described in Refs. [1-5]. A companion contribution [11] shows samples of information flow diagram for RRC state transitions.

The RRC states are proposed based on the following considerations:

- The need to support of new services for R2000 as defined in the current stage 2 text.   In particular, the requirements to support dedicated MAC mode of operation.

- The desire for R2000 RRC to support PMM, given that GERAN will communicate with a UMTS packet core network and will use an Iu-ps interface.

- The desire for maximum reuse of existing packet RR procedures as defined in 04.60.

- The desire to have a single RRC state model that supports both shared and dedicated MAC modes of operation.

RRC States and State Transitions

Figure 1 shows the proposed R2000 GERAN RRC state model. For reference, GSM RR and GPRS packet modes of operations are also shown in Figure 1 (in green).

General assumptions:

- The RRC state model for R00 (Figure 1) supports only Iu based procedures. Currently only Iu-ps based procedures are included in the model. Should Iu-cs interface be supported in R00, this model needs to be extended to support Iu-cs.

- Specifically, A/Gb based procedures will still be supported by GERAN, but are not included in the RRC model.

Three of the GERAN Connected States, Cell_Shared (transfer) state, Cell_Idle state, and GRA_Idle state (in gray-shaded boxes) map to the existing RLC/MAC Packet Idle and Packet Transfer modes (see section 3). Consequently procedures defined in 04.60 apply with minimum change for these proposed states.

To support RT services on dedicated MAC, a new GERAN Connected State, Cell_Dedicated (transfer) state, and associated state transitions/procedures are introduced, as shown in blue in Figure 1.

This model is analogous to the UTRAN RRC State model as described in Ref. [9] and shown in Appendix A.

## Idle State

In the Idle state, there is no RRC connection established between the MS and GERAN. The MS has no relationship to GERAN, i.e. GERAN has no RRC context for the MS and has not assigned a G-RNTI to the MS. The MS is identified by non-access stratum identities such as IMSI and P-TMSI.

The MS monitors (P)BCCH for system broadcast information and (P)PCH for paging information.

### Transition from Idle State to GERAN Connected State

Upon receiving a paging request from the network or a request from upper layer in the MS (e.g. Attach Request), the MS leaves the Idle State in order to establish the first (and only) RRC connection. When the MS receives the confirmation of successful RRC Connection establishment from the network with assigned G-RNTI, the MS enters GERAN Connected State.

- Transition from Idle State to Cell_Shared State

Following successful RRC connection establishment, a TBF is established over shared physical sub-channel to transmit non-access stratum (NAS) message and MS enters Cell_Shared state.

- Transition from Idle State to Cell_Dedicated State

Following successful RRC connection establishment is established and dedicated physical sub-channel allocated for NAS and/or user data transfer, the MS enters Cell_Dedicated State. It is ffs if this transition is necessary.

Figure 1:  GERAN RRC States and State Transition

## GERAN Connected States

In the GERAN connected states, the MS has RRC connection established with the GERAN and the MS is known in the GERAN.  This means that the RRC context is setup at the GERAN and the MS is assigned a G-RNTI.

GERAN Connected States are aggregated states of all RBs (both user data and signaling) established for an MS. Each RB can be in one of the two states, namely idle state and transfer state, as described in Ref. [3] and summarized in Appendix B.

### Cell_Shared (Transfer) State

The Cell_Shared state is characterized by the following:

- No dedicated physical sub-channel is allocated to the MS.

- One or more shared physical sub-channels are allocated to the MS, i.e. one or more TBFs established.

- User data and/or NAS signaling data transfer on PDTCH in the direction of an established TBF.

- The MS location is known at the cell level.

In the Cell_Shared State, one or more RBs are in transfer state with TBF(s) established on a shared physical sub-channel(s) for the MS.

RRC procedures to be performed in Cell_Shared (Transfer) State include:

- TBF procedures initiated by the MS or by the network on PACCH using TBF procedures currently defined for Packet Transfer mode [7].

- RB Setup/Release procedure initiated by the network triggered by RAB assignment request.

- Re-configuration of shared physical sub-channel(s) for established TBFs.

- RRC release procedures.

- Cell re-selection procedure.

- Measurements report procedures.

#### State Transitions in Cell_Shared (Transfer) State

- Transition from Cell_Shared to Idle State

Transition to Idle State occurs when the RRC connection is released.

- Transition from Cell_Shared to Cell_Dedicated State

Cell_Dedicated State is entered when dedicated physical sub-channel(s) is allocated for a RB, which is triggered by RAB Assignment request from the CN. When a dedicated radio resource is allocated to the MS, it is optional to re-configure existing RBs (in both idle and transfer state) onto the dedicated physical sub-channel and continue the TBF (for RB in transfer state) on the dedicated physical sub-channel without TBF restart. Alternatively, the established RB over the shared physical sub-channel may remain on the shared radio resource.

- Transition from Cell_Shared to Cell_Idle State

Cell_Idle state is entered upon release of all TBFs, i.e. release of all shared physical sub-channels.

### Cell_Dedicated (Transfer) State

This state is introduced to support the new dedicated MAC mode. New RRC procedures are to be defined for this state.

The Cell_Dedicated state is characterized by the following:

- One or more dedicated physical sub-channels are allocated to the MS.

- Zero or more shared physical sub-channels are allocated to the MS.

- Data transfer on TCH/PDTCH in both uplink and downlink direction.

- The MS location is known to the cell level.

RRC procedures to be performed in Cell_Dedicated (Transfer) State include:

- RB Setup/Release procedure initiated by the network using PACCH.

- Re-configuration of dedicated physical sub-channel(s) for RBs in transfer mode.

- Radio resource re-configuration procedures.

- Handover procedures.

- Measurement Report procedure on SACCH.

#### State Transitions in Cell_Dedicated (Transfer) State

- Transition from Cell_Dedicated to Cell_Shared State

Cell_Shared state is entered when all dedicated radio resource is released, e.g. when an optimized speech RB is released. Upon release of dedicated radio resource, RBs with TBFs established on the dedicated radio resource are reassigned to shared physical sub-channel(s).

- Transition from Cell_Dedicated to Cell_Idle State

Cell_Idle state is entered upon release of dedicated physical sub-channels and release of all TBFs for the MS, the MS transitions into Cell_Idle state.

- Transition from Cell_Dedicated to Idle State

Transition to Idle State occurs when the RRC connection is released.

### Cell_Idle State

The Cell_Idle state is characterized by

- MS camps on (P)CCCH.

- No user data transfer in this state. To start data transfer, the MS must first transition into Cell_Shared or Cell_Dedicated state.

- MS position is known on the cell level.

In Cell_Idle state, all RBs for the MS are in idle state.

RRC procedures to be performed in Cell_Idle State include:

- TBF establishment procedures initiated by the MS using access procedures on (P)RACH, or initiated by the network by paging through (P)CCCH. Existing TBF establishment procedures for Packet Idle mode [7] apply.

- RB setup/release procedures and RB re-configuration procedures.

- Paging procedure initiated by the network. MS is paged in the cell known when MS last performed cell update in Cell_Shared state.

- Non-DRX and DRX procedures.

- Cell update procedure upon cell change.

#### State Transitions in Cell_Idle State

- Transition from Cell_Idle State to Cell_Shared State

Cell_Shared state is entered upon successful TBF establishment in order to transfer user data and/or NAS messages. This is triggered by paging from network or data transfer request from MS.

- Transition from Cell_Idle State to GRA_Idle State

This transition occurs when the associated timer expires, or by explicit signaling, or some other mechanism, e.g. using counter that tracks the number of Cell Update performed.

- Transition from Cell_Idle State to Cell_Dedicated State

Cell_Dedicated state is entered when a RB is established with dedicated physical sub-channel allocation. This is triggered, e.g. by the RAB assignment request from network.

- Transition from Cell_Idle State to Cell_Idle State

This transition occurs when RRC procedure is performed without TBF establishment nor dedicated channel allocation, e.g. Cell Update, RB Setup without physical resource allocated to the RB, etc.

- Transition from Cell_Idle State to Idle State

Idle state is entered upon release of RRC connection.

### GRA_Idle State (GERAN Registration Area Idle State)

The GRA_Idle state is characterized by

- MS camps on (P)CCCH.

- No dedicated nor shared physical sub-channel is allocated to the MS.

- No user data transfer in this state. To start data transfer, the MS must first transition into Cell_Shared or Cell_Dedicated state.

- MS location is known on the GERAN Registration Area level.

In GRA_Idle state, all RBs for the MS are in idle state.

RRC procedures to be performed in GRA_Idle State include:

- TBF establishment procedures initiated by the MS using access procedures on (P)RACH, or initiated by the network by paging through PPCH. Existing TBF establishment procedures for Packet Idle mode [7] apply.

- RB setup/release procedures.

- Paging procedures initiated by the network. MS is paged in the all cells belonging to the last known GRA.

- The MS performs Registration  area update when GRA changes or when the routing area timer expires.

- Non-DRX and DRX procedures.

#### State Transition from GRA_Idle State

- Transition from GRA_Idle to Cell_Dedicated State

Cell_Dedicated state is entered when a RB is established with dedicated physical sub-channel allocation. This is triggered by, e.g. RAB assignment request from network.

- Transition from GRA_Idle to Cell_Shared State

Cell_Shared state is entered upon successful TBF establishment with shared physical sub-channel allocation. This is triggered by paging from network or MS initiated data transfer request.

- Transition from GRA_Idle to GRA_Idle State

This transition occurs when RRC procedures are performed without TBF establishment nor dedicated resource allocation, e.g. GRA Update, RB setup without physical resource allocated to the RB, etc.

- Transition from GRA_Idle to Idle State

GRA_Idle state is entered upon the release of RRC connection.

RRC State Mapping to R99 GERAN Concepts

Table 1 shows the relationship between the RRC states, the GPRS Mobility Management States from 23.060, and the RLC/MAC modes from 04.60.

| R00 RRC State | R99 GPRS MM State | R99 RLC/MAC Mode |
| --- | --- | --- |
| Idle | Idle | Packet Idle |
| GRA_Idle | Standby | Packet Idle |
| Cell_Idle | Ready | Packet Idle |
| Cell_Shared | Ready | Packet Transfer |
| Cell_Dedicated | Not Applicable | New (Packet transfer) |

Table 1  RRC State Mapping to R99 GERAN Concepts

As highlighted in the table, the concept of a cell-dedicated RRC state does not yet exist for RLC/MAC and will have to be introduced into 04.60 or the equivalent new specification of 04.60.

Table 1 also relates the new RRC states to existing GPRS mobility management states.  The implication here is that procedures for transferring among these states may be reused, and that these states correlate to the proposed new RRC states.

Relationships between RRC States and PMM States

Table 2 shows the correspondence between the RRC States and PMM States described in 23.060 in the absence of Iu-cs connection from GERAN to the core network.

| RRC States | Idle | GRA_Idle | Cell_Idle | Cell_Shared | Cell_Dedicated |
| --- | --- | --- | --- | --- | --- |
| PMM States | PMM-Detached | PMM-Idle | PMM-Connected |

Table 2. Relationship between R00 GERAN RRC States and PMM States in the absence of Iu-cs.

The definitions of the UMTS Mobility Management states (PMM states) are provided in Appendix C.

Recommendations

It is recommended that the proposed RRC States as described in section 2 be adopted

for GERAN R2000 and be placed in stage 2 text.

Further, it would be beneficial to discuss and reach consensus on whether RRC procedures currently specified in 04.60 and 04.18 should be consolidated in a common place for R2000.

References

- GERAN Design, 3GPP TSG GERAN Adhoc#1, Tdoc 2g00-77, Lucent Technologies

- GERAN Design, 3GPP TSG GERAN#1, Tdoc GP-000112, Lucent Technologies

- RRC Radio Bearer Control Functions in GERAN, 3GPP TSG GERAN Adhoc#1, Tdoc 2g00-79, Lucent Technologies

- GERAN Sample Scenarios, 3GPP TSG GERAN Adhoc#1, Tdoc 2g00-081, Lucent Technologies

- New RLC/MAC Functions for R2000, 3GPP TSG GERAN Adhoc#1, Tdoc 2g00-082, Lucent Technologies

- GERAN Overall Description, Stage 2, GSM 03.51, V0.0.1, R2000

- GPRS MS-BSS Interface, Radio Link Control/Medium Access Control protocol, GSM 04.60, version 8.3.0 R1999

- GPRS Service Description, Stage 2, 3G TS 23.060, V3.3.0, R1999

- Radio Resource Control (RRC) Protocol Specification, 3G TS 25.331, V3.3.0, R1999

- GERAN RRC States, 3GPP TSG GERAN #1, Tdoc GP-000113, Lucent Technologies

- GERAN RRC State Transition Scenarios, 3GPP TSG GERAN Adhoc#2, Tdoc GAHW-000040, Lucent Technologies

Appendix A	RRC States and State Transitions in UMTS

Figure 2 is reproduced from 3G TS 25.331 (Figure 55) for information. Detailed description can be found in Ref. [9].

Figure 2. RRC States and State Transitions including GSM.

[1: The indicated division within idle mode is only included for clarification and shall not be interpreted as states.]

Appendix B	Radio Bearer States

An established RB may be in one of two states depending on whether the RB has radio resources assigned to it:

- Transfer state.  A RB in transfer state has radio resources allocated and it is ready to transfer data. For instance, a RB using shared MAC has TBF established when the RB is in transfer state.

- Idle state. A RB in idle state has an RLC instance configured at its local RLC entity, but has no TBF assigned (i.e. no radio resources). When there is data to send, the RRC establishes a TBF to support the RB.

Figure 3 shows the RB state transition diagram. Detailed discussion on RRC Radio bearer control functions are provided in Ref. [3].

Figure 3:  RB state transition diagram

Appendix C	Mobility Management States in UMTS (PMM State)

The text contained herein is reproduced from 23.060 [8].

PMM-DETACHED State In the PMM-DETACHED state there is no communication between the MS and the 3G-SGSN. The MS and SGSN contexts hold no valid location or routeing information for the MS. The MS MM state machine does not react on system information related to the 3G-SGSN. The MS is not reachable by a 3G-SGSN, as the MS location is not known.

In order to establish MM contexts in the MS and the SGSN, the MS shall perform the GPRS Attach procedure. When the PS signalling connection is established between the MS and the 3G-SGSN for performing the GPRS attach, the state changes to PMM-CONNECTED in the 3G-SGSN and in the MS. The PS signalling connection is made up of two parts; an RRC connection and an Iu connection.

PMM-IDLE State The MS location is known in the 3G-SGSN with an accuracy of a routeing area. Paging is needed in order to reach the MS, e.g., for signalling. The MS and SGSN have established MM contexts as described in clause "Information Storage".

The MS shall perform a routeing area update if the RA changes. Signalling towards the HLR is needed if the 3G-SGSN does not have an MM context for this MS.

The MS and 3G-SGSN shall enter the PMM-CONNECTED state when the PS signalling connection is established between the MS and the 3G-SGSN.

GPRS detach changes the state to PMM-DETACHED. The 3G-SGSN may perform an implicit GPRS detach any time after the MS reachable timer expiry. The MS's MM context is deleted, preferably after a certain (implementation dependent) time. The HLR may be informed about the deletion (see subclause "Purge Function").

PMM-CONNECTED State The MS location is known in the 3G-SGSN with an accuracy of a serving RNC. In the PMM-CONNECTED state, the location of the MS is tracked by the serving RNC. The MS performs the routeing area update procedure when RAI in the MM system information changes.

When an MS and a 3G-SGSN are in the PMM-CONNECTED state, a PS signalling connection is established between the MS and the 3G-SGSN.

In the 3G-SGSN, PS signalling connection release or failed downlink transfer with cause "IMSI unknown in RNC" changes the state to PMM-IDLE.

The MS shall enter the PMM-IDLE state when its PS signalling connection to the 3G-SGSN has been released or broken. This release or failure is explicitly indicated by the RNC to the MS or detected by the MS (RRC connection failure). The radio connection shall also be released if a URA update fails because of "RRC connection not established", or if the URA update timer expires while the MS is out of coverage.

After a signalling procedure (e.g., routeing area update), the 3G-SGSN may decide to release the PS signalling connection, after which the state is changed to PMM-IDLE.

GPRS detach changes the state to PMM-DETACHED.

State Transitions and Functions Figure 4 introduces the MM states for a GPRS subscriber (PMM). The states and activations are further described below the figure.

Figure 4. PMM State Model

# Footnotes

As currently defined, non-DRX mode is entered: a) upon TBF release, or b) when MS initiates MM non-DRX mode. In case a) , the non-DRX period is controlled by timers. In case b), the non-DRX period ends when the MM procedure is completed. It seems desirable to support the non-DRX mode in the similar situations, such as TBF release and RRC MM procedures  (Cell Update and GRA Update).

See footnote 1 on page 4.