3GPP TSG GERAN Adhoc#2				           Tdoc GAHW-000041

Oct 9-13, 2000	Agenda item 6.1.3
Munich, Germany

Source: Lucent Technologies

Title: On GERAN Data Link Control Signaling for a Dedicated Channel

# Abstract:  By comparing the PDU formats of DLC and RLC/MAC with regard to the overhead information required by dedicated link control signalling, the conclusion can be drawn that LAPDm can and should be used for data link control by the GERAN.  As a result, a DLC/MAC PDU format is proposed as a special case of RLC/MAC format for the dedicated MAC-mode. Correspondingly, the protocol architecture is refined.

# 1. Introduction

To support the dedicated channel in GERAN, particularly for provisioning of dedicated optimized voice service, there is a need for the data link control signaling, which should be designed under the following constraints:

- It should easily fit into GERAN protocol architecture.

- It should be developed within the GERAN specification time schedule.

- Its spectrum efficiency and performance should not be worse than existing DLC.

For dedicated control, the GERAN physical layer provides logical channels FACCH and SACCH.  On the next higher layer (L2), the link control for dedicated MAC-channel can be designed based on different principles, e.g. based on the existing RLC/MAC protocol [3] or on DLC protocol [2].  The feasibility of the design should be assessed by the above constraints.  This paper focuses on an approach that takes advantage of both RLC/MAC and DLC protocols.  It uses logical FACCH and SACCH to carry LAPDm protocol on dedicated physical sub-channels, assuming no support of SMSCB service on DLC is required.  Support of BCCH/CCCH is ffs.

2. Existing DLC PDU Format

In physical layer (L1) the channel block for SACCH, FACCH, PACCH and PDTCH (CS-1) all have the same size: 23 octets. FACCH/PACCH/PDTCH (CS-1) have no L1 header, while SACCH has 2 octets of header for power control and timing advance information.  In the data link layer (L2) the LAPDm uses 5 different channel block formats, where only 4 are relevant for our discussion.  Figure 1 shows a L2 format used by SACCH (L1  header not shown) and FACCH  [1][2].

| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Spare | LPD | SAPI | C/R | EA |
| Control Field |
| Length Indicator |
| Format A: Fill bits (N201 [=18 octets for SACCH ; =20 octets for FACCH/SDCCH ]) Format B: Information fields + Fill bits (N201[=18 octets for SACCH; =20 octets for FACCH/SDCCH]) |

Figure.1: L2 format for SACCH and FACCH in up-link (down -link), where EA= address field extension bit, C/R= command/response bit, LPD = link protocol discriminator, SAPI = service access point identifier. Only format A and B are shown, which are also representative for L2 Format B4 (applies to UI on SACCH) and Bter (applies to UI for SAPI 0).

3. Existing RLC/MAC PDU Format

For GPRS layer L2, the link control is accomplished by the RLC/MAC protocol using the following formats:

| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Payload Type | spare | R | MAC header |
| Control Message Contents (22 octets) | . Up-link |

| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Payload Type | RRBP | S/P |  | USF |  | MAC header |
| RBSN | RTI | FS | AC | Octet 1 (optional) |
| PR | TFI | D | Octet 2 (optional) |
| Control Message Contents (=20-22 octets) | . Down-link |

Figure 2: PACCH up-link format (above) and PACCH down-link format (lower)

For the transportation of the upper layer data, PDTCH (CS-1) uses the following formats:

| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Payload Type | Countdown Value | SI | R | MAC header |
| Spare | PI | TFI | TI | Octet 1 |
| BSN | E | Octet 2 |
| Length Indicator | M | E | Octet 3… M(optional) |
| TLLI | Octet M+1…4(optional) |
| PFI | E | Octet M+5 |
| RLC data | Up-link |

| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Payload Type | RRBP | S/P |  | USF |  | MAC header |
| PR | TFI | FBI | Octet 1 |
| BSN |  | Octet 2 |
| Length Indicator | M | E | Octet 2 –M(optional) |
| RLC data | . Down-link |

Figure 3: PDTCH(CS-1) up-link format (upper) , PDTCH(CS-1) down-link format(lower).

4. Discussion

RLC/MAC protocol is designed for packet switched radio interface and, as such, requires much more header information than for a circuit switched radio interface. By providing dedicated link control via logical FACCH and SACCH, GERAN may not need all the overheads of RLC/MAC control block. For instance, in case of PACCH in down-link, RRBP (relative reserved block period), S/P (supplementary/ polling), RBSN (block sequence number), RTI (radio transaction identifier), FS (final segment), AC (address control), PR (power reduction), TFI (temporal flow identifier), D (direction bit), R (retry) are redundant or useless for dedicated data link control.  Thus, a redesign of the RLC/MAC seems necessary in order to meet the spectrum efficiency and performance requirements for the dedicated link control.  Fortunately, we don’t have to start such a redesign of RLC/MAC, if we can reuse the LAPDm protocol. LAPDm is a protocol designed for dedicated link control and can be regarded as designed specifically for the dedicated MAC mode. If LAPDm can be embedded into the protocol architecture without compromising the performance, it will be an optimised design for data link control signalling for a dedicated channel.

5. Proposed DLC/MAC PDU Format

In the following we will use the example of format B of LAPDm.  Application of the results to other LAPDm formats mentioned above is trivial.  According to 04.06, the header information LPD can only take value LPD=0(data link control) or 1(SMSCB).  Under the assumption that SMSCB will not be supported by data link control in GERAN, MAC can use the LPD field to transport DLC messages by means of the following procedure:

- The transmitting DLC will set  bits  (8, 7, 6)  to value  [0, 0, 0], before delivering the PDU to MAC

- The transmitting MAC will set bits  (8, 7, 6) to value  [1, 1, 0], where the spare bit is coded 0, and send the PDU to the lower layer PHY for transmission.

- The receiving MAC recognises by the value of bits (8, 7, 6) that the PDU has a DLC payload and replaces the values of bits (8, 7, 6) with [0, 0, 0], and deliver the payload to the upper layer DLC.

The clear benefit here is that 04.06 does not need to be modified. In addition, the MAC can handle the multiplexing of both RLC and DLC: If the value of bit (8, 7) in the first received MAC octet is others than [1, 1], the MAC will proceed according to 04.60 and deliver the payload to RLC.  This approach is feasible, because the current valid values for the parameter “Payload Type ” are 00, 01, 10, while the value 11 is reserved. According to 04.60, whenever Payload Type=11 is received, the legacy receiver will ignore all fields except the USF.  Since USF is useless for a dedicated channel such as SACCH and FACCH, the field can be reused for other purposes, e.g. for C/R and EA of LAPDm. To summarise our proposal, the dedicated data link control in GERAN can be accomplished by using a DLC/MAC format as shown in Fig. 4.:

| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Payload Type | Spare | SAPI | C/R | EA |
| control field |
| Length Indicator |
| Information fields + Fill bits (N201[=18 octets for SACCH; =20 octets for FACCH]) |

Figure 4: DLC/MAC block format. The black printed parts are for MAC, the red for DLC.

The DLC/MAC format can be viewed as a special RLC/MAC format as well as a special DLC format. (Wave-Matter Duality!)

6. Proposed Change to GERAN Protocol Architecture

Since the “Payload Type” parameter is common to both PACCH and PDTCH (CS-1), in up-link as well as in down -link, the proposal applies to all GPRS RLC/MAC blocks. Thus, it requires a GERAN receiver

- To treat all data  from SACCH and FACCH as GPRS RLC/MAC  block

- If the value of parameter  “Payload Type” is 11, it will interpret the rest of the block according to 04.06 except the bits (8, 7, 6) of the first octet.

- Otherwise, it will interpret the rest of the block according to 04.60

This approach leads to the following change to the GERAN protocol architecture (Fig 5):

Figure 5: Proposed Change to GERAN Protocol Architecture

7.  Conclusion

LAPDm is a proven reliable protocol for supporting data link control signalling in GSM. By embedding LAPDm protocol into GERAN protocol architecture, a RLC/MAC design can be achieved with minimum development efforts.  The proposed approach merges RLC/MAC block and LAPDm block to minimise redundant header information, while enabling the transportation of both RLC PDU and DLC PDU via logical FACCH/SACCH.  It satisfies all the constraints listed in the introduction of this paper and provides a viable solution to the problem of data link control design.

Recommendation:    Adopt the proposed procedures (Section 5) and the protocol architecture change (Fig.5), which places DLC (LAPDm) above the MAC so that the MAC can multiplex DLC (LAPDm) and RLC. If this proposal is adopted, Lucent is willing to propose detailed CRs to the Stage 2 document.

REFERENCES

[1] GSM 04.04

[2] GSM 04.06

[3] GSM 04.60

[4] GSM 04.51

# Text boxes

RLC

DLC (LAPDm)

Shared - MAC

Dedicated - MAC