3GPP TSG GERAN adhoc                                                     Tdoc GAHW-000047
Munich, Germany                                       Agenda item 6.1.2.1 
October 9th – 13th 2000

Source: Ericsson

Migration scenarios for GERAN CS domain

# Introduction

GERAN R00/01 is adopting Iu-ps for the connection to UMTS CN (Core Network). A and Gb interfaces are necessary to support legacy terminals. A CS (Circuit Switched) option for R00 (and beyond) mobiles is requested. This document discusses some alternative approaches and makes high-level cost comparisons.

The document is for discussion.

The outline is:

Chapter 2 discusses a possible migration method, two different migration scenarios (based on A or Iu-cs interface) and the high-level operator requirements.

Chapter 3 discusses how well the two migration scenarios meet the high-level requirements.

Chapter 5 summarizes

# Requirements

This chapter discusses a possible migration method for current GSM operators and the resulting high-level operator requirements.

We assume that the service evolution method for current GSM operators requesting an “intermediate” CS mode is based on service continuity and (close to) 100% coverage before the next evolution step starts:

The figure above does not assume CS-PS handover for service continuity, but relies on 100% DTM coverage followed by 100% 3G PS coverage, which supports “all essential” services.

Two different scenarios have been envisaged for the intermediate step (which will be detailed in chapter 3):

- Use the 3G CN also for GERAN CS services. Full alignment with UMTS is desirable. Iu-cs is the choice.

- Use the 2G CN over a modified A interface for all GERAN CS services. This has been claimed to minimize the changes for existing GSM operators. A+Iu-ps in “Simple Class A” mode is required.

Both cases must support “single-radio” terminals and the evolution of Multi-media (simultaneous sessions with different QoS), which starts with DTM and continues into full 3G PS Multi-media functionality. This implies, among other things, coordination of radio resources, similar to the R99 DTM mechanism or the R99 UTRAN mechanisms.

“Alignment with UMTS” is detailed in Ref. 1 and will not be discussed here.

“Minimized changes” is a vague description, but it is believed to include:

- Trunking efficiency. Will CS traffic be segmented into smaller groups? Will traffic on old equipment decrease faster than what is economically planned?

- Transport technology (need to invest in new)

- Compatibility and upgrading of existing equipment.

- No “extra” capacity expansions, e.g. due to additional signalling load between 2G & 3G parts

- Quality of Service. No significant deterioration allowed, e.g. longer handoff muting or transport delay.

Operators are encouraged to provide more detail on requirements.

# Discussion of Migration Scenarios

This document limits the discussion to the following two scenarios:

- Scenario 1: Existing GSM operator also deploying UMTS. Uses (evolved) A for R00 CS support in GERAN

- Scenario 2: Existing GSM operator also deploying UMTS. Uses Iu-cs for R00 CS support in GERAN.

Scenario 1:

Note: lines mean capacity expansion, not operational life span.

Scenario 2:

In Scenario 2 the existing mechanisms for CC/MM/RR in UMTS can be re-used in GERAN.

The high-level differences between the scenarios are:

- Scenario 1 will carry out the migration effort later and with a larger installed base.

- Scenario 1 requires an added operational mode

A high-level comparison of how the two scenarios fulfill the Requirements:

| Cost Item | Scenario 1 | Scenario 2 |
| --- | --- | --- |
| CS trunking efficiency. Will CS traffic be segmented into smaller groups? Will traffic on old equipment drop faster than what is economically planned? | Full CS trunking efficiency within GERAN. | Pre-R00 and post-R00 MS may operate on different trunks. However, this is offset by increased use of UMTS CN and possible load sharing mechanism (for services, which are equal 2G/3G) |
| Transport technology (need to invest in new or re-configure) | Existing STM transport network can be used for A interface. BTS transport upgrading to efficiently support variable BW services is desired. | Existing transport technology will probably be used for Iu-cs, since Iu will be modified to use IP and probably several L1/L2. The use of routers with inherent traffic concentration allows using fewer and larger CN nodes. BTS transport: same as alternative 1. |
| Compatibility of TRAU | Upgrade of BSS TRAU pool for AMR optional (but desired from quality perspective) | Capacity expansion of CN TRAU pool for AMR needed. |
| No “extra” capacity expansion needed to support potential added CS signalling load between 2G & 3G parts | The volume of 2G-3G interaction is postponed. All GERAN-internal CS traffic is carried in 2G CN. Traffic UTRAN-GERAN involves 2G-3G CN signalling. | More initial 2G-3G CN load, due to increased frequency of 2G-3G LA Updates & Handovers. Similar to dual-mode UMTS/GSM. Reduces as traffic migrates to 3G. |
| Quality of Service. No significant deterioration allowed, e.g. longer handoff muting or transport delay. | Unchanged for CS part. | Unchanged for CS part |
| New functional development, TimeToMarket | New GERAN-unique RR/MM mode must be developed, impacting at least BSS and MS (Ref. 2) | UMTS modes are re-used, both in MS, BSS and CN. |

Scenario 2 also has the benefits and drawbacks:

- + Shorter time to maintain 2G and 3G CN nodes for operators having both GSM and UMTS

- + Some operators only need to invest in a 3G CN.

- + No new GERAN-unique MM/RR operational modes in MS or BSS.

- - Iu must offer alternatives to ATM, for operators unwilling to invest in ATM (similar to the GSM-UMTS case)

- - Higher CN load (similar to the GSM-UMTS case)

See Ref. 1 for an extensive list.

# Conclusion

This document has discussed some GERAN CS migration options, for existing GSM operators also deploying UMTS, from a cost perspective.

Two CS alternatives were analyzed: based on an upgraded A interface and based on Iu-cs.

The differences are mainly:

- a new operational mode must be designed for the upgraded A interface, causing delayed deployment, particularly of MS.

- the A interface alternative postpones the added CN load, due to MS moving between 2G-3G, but it will occur later and from a larger 2G base.

The alternative based on the Iu-cs interface allows faster R00 MS deployment and saves overall long-term cost. It is therefore the preferred choice.

# References

[1]	Inclusion of Iu-cs into GERAN architecture, Tdoc GAHW-000046

[2]	Comments on A/Iu-cs, Tdoc GAHW-000070