Source:	BellSouth

Title:	Support of Legacy Transceivers

Document for:	Discussion and Approval

Agenda Item:	6.1.1.2

The GERAN compatibility with operational Infrastructure Equipment was discussed during the Joint SMG2/S2 workshop held in Uppsala, Sweden on February 21-22, 2000. The outcome of this discussion is contained in Tdoc 2g00-021.

The GERAN compatibility with Legacy Transceivers was discussed again during TSG-GERAN#1 and it was confirmed at that time that the agreement reached in Uppsala should stand unless it was demonstrated that the related requirements were significantly increasing the overall GERAN complexity.

The same outcome document (Tdoc 2g00-021) was also recommending that “when defining bearers, reuse of existing physical layer definitions should be given preference”.

Based on this statement and the current status of the discussions in GERAN, we believe that there is no evidence that the requirements agreed in Uppsala would indeed increase the GERAN complexity.

Consequently, it is proposed:

Recommendation 1: To attach Tdoc 2g00-021 as Annex 3 of the GERAN Project Document (TS 50.099) since this document (Tdoc 2g00-021) has the value of System Requirements for the compatibility of GERAN with Existing Networks.

Recommendation 2: To modify the GERAN Stage 2 Specification section 6.8.7 (Channel Coding) and Annex A as proposed in Annex 1 of this document. Specifically, the modifications consist in listing all Speech Logical Channels to be supported by GERAN including:

The existing Logical Channels: TCH/FS, TCH/EFS, TCH/HS, TCH/AFS and TCH/AHS

The new R00 Logical Channels:	TCH/WFS (Wideband Speech Codec in GMSK FR Channel)
E-TCH/WFS (Wideband Speech Codec in 8-PSK FR Channel)
E-TCH/WHS (Wideband Speech Codec in 8-PSK HR Channel)
E-TCH/AHS (AMR in 8-PSK HR Channel)
E-TCH/AQS (AMR in 8-PSK QR Channel)

Note that it is necessary to differentiate the GMSK and 8-PSK Logical Channels because of the difference in Channel Coding and because of the potential difference in supported Codec Modes. For example, AMR-HR GMSK (noted TCH/AFS) supports only 6 Codec Modes while AMR-HR 8-PSK (noted E-TCH/AHS) will likely support all 8 AMR Codec Modes. It is proposed to add an ‘E-‘ before the Logical Channels name when it is using the 8-PSK modulation.

Recommendation 3: To confirm that all PDTCH Channel Coding schemes defined in GPRS/EGPRS Release 99 (CS1-4 and MC1-9) will also be supported for all classes of services in GERAN Release 00.

Although this was not discussed during the Architecture Workshop in Uppsala, it should also be recognized that it was never agreed either to restrict GERAN R00 to the EGPRS Coding Schemes (MCS1-9). It is expected that a lot of GPRS compatible transceivers will only be capable of supporting the GPRS Coding schemes and associated protocols for quite some time. Consequently, GERAN should not be restricted to the EGPRS Channel Coding schemes.

#### Annex A: Proposed Changes to the GERAN Stage 2 Specifications

### 6.8.7	Channel Coding

Table 2: Channel Coding

| Logical Channel | Mod. | Radio Block / Frame Size (Bits) | SB (1) | Channel Coding | Interleaving |  |  | Physical Subchannel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Type | Rate | Type | Depth (bursts) |  |  |  |
| TCH/FS TCH/EFS TCH/AFS TCH/WFS | GMSK | 464 | 8 | CC | See GSM 05.03 | diag | 8 |  |  | DPSCH/F |
| E-TCH/WFS | 8PSK | 1392 | 24 | CC |  |  |  |  |  |  |
| TCH/HS TCH/AHS | GMSK | 232 | 4 | CC |  |  | 4 |  |  | DPSCH/H |
| E-TCH/AHS | 8PSK | 696 | 12 | CC |  |  |  |  |  |  |
| E-TCH/AQS | 8PSK | 348 | 6 | CC |  |  | 2 |  |  | DPSCH/Q |
| TCH/F | GMSK | 464 | 8 | CC |  | diag | 19 |  |  | DPSCH/F (2) |
|  | 8PSK | 1392 | 24 | RS+CC |  |  |  |  |  |  |
| TCH/H | GMSK | 464 | 8 | CC |  |  |  |  |  | DPSCH/H (2) |
|  | 8PSK | 1392 | 12 | RS+CC |  |  |  |  |  |  |
| PDTCH/F | GMSK | 464 | 12 | CC | See GSM 03.64 | rect | 4 |  |  | SPSCH/F |
|  |  |  |  |  |  |  |  |  |  | DPSCH/F |
|  |  |  | 12 |  |  | ffs | ffs |  |  | SPSCH/F |
|  |  |  |  |  |  |  |  |  |  | DPSCH/F (2) |
|  | 8PSK | 1392 | 8 |  |  | rect | 4 |  |  | SPSCH/F |
|  |  |  |  |  |  |  |  |  |  | DPSCH/F |
|  |  |  | 8 |  |  | ffs | ffs |  |  | SPSCH/F |
|  |  |  |  |  |  |  |  |  |  | DPSCH/F (2) |
| PDTCH/H | GMSK | 464 | 12 | CC | See GSM 03.64 | rect | 4 |  |  | SPSCH/H |
|  |  |  |  |  |  |  |  |  |  | DPSCH/H |
|  |  |  | 12 |  |  | ffs | ffs |  |  | SPSCH/H |
|  |  |  |  |  |  |  |  |  |  | DPSCH/H (2) |
|  | 8PSK | 1392 | 8 |  |  | rect | 4 |  |  | SPSCH/H |
|  |  |  |  |  |  |  |  |  |  | DPSCH/H |
|  |  |  | 8 |  |  | ffs | ffs |  |  | SPSCH/H |
|  |  |  |  |  |  |  |  |  |  | DPSCH/H (2) |
| The number of Stealing Bits (SB) is ffs For DPSCH, whether TCH or PDTCH or both may be used is ffs. CC: Convolutional Code RS: Reed Solomon code |

Editor's Note: the table above remains to be completed.

Annex A (informative):
Radio Access Bearer Realization

This annex describes how the different protocols of the GERAN User Plane protocol stack are configured to provide the desired radio access bearer classes (conversational, streaming, interactive and background). Only the traffic over Iu-ps interface is considered.

# A.1	Conversational Radio Access Bearer

In the table below, case A represents optimized conversational RAB further described in section A.1.2. Case B represents the generic conversational RAB.

Table 2: Conversational RAB

| PDCP | RLC | MAC | Physical Layer | OS |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Physical SubChannel | Traffic Channel | Dedicated Control Channel |  |  |
|  |  |  |  | Type | Interleav. | Mod. | Coding |  |  |  |
| Non Transparent Header Removal | Transp. | Dedicated | DPSCH/F | TCH/F | 8 diag | GMSK | UEP | Based on TCH/FS TCH/EFS TCH/AFS TCH/WFS | FACCH/F (2) SACCH/TF | 1 - 2 | A |
|  |  |  |  |  |  | 8PSK (1) | UEP | Based on E-TCH/WFS | FACCH/F (2) SACCH/TF | 1 - 2 |  |
|  |  |  | DPSCH/H | TCH/H | 4 diag | GMSK | UEP | Based on TCH/HS TCH/AHS | FACCH/H (2) SACCH/TH | 1 - 2 |  |
|  |  |  |  |  |  | 8PSK | UEP | Based on E-TCH/AHS E-TCH/WFS | FACCH/H (2) SACCH/TH | 1 - 2 |  |
|  |  |  | DPSCH/Q | TCH/Q | 2 diag | 8PSK | UEP | Based on E-TCH/AQS | FACCH/Q SACCH/TQ | 1 |  |
| Non Transparent Header Compression or No Adaptation Transparent | Unack | Dedicated | DPSCH/F | PDTCH/F | 4 rect | GMSK | EEP | SACCH/TF PACCH/F | 1 - 2 | B |
|  |  |  |  |  |  | 8PSK | EEP | SACCH/TF PACCH/F | 1 - 2 |  |
|  |  |  |  | TCH/F (2) | ffs | GMSK | EEP | FACCH/F (2) SACCH/TF | 1 - 2 |  |
|  |  |  |  |  |  | 8PSK | EEP | FACCH/F (2) SACCH/TF | 1 - 2 |  |
|  |  |  | DPSCH/H | PDTCH/H | 4 rect | GMSK | EEP | SACCH/TH PACCH/H | 1 - 2 |  |
|  |  |  |  |  |  | 8PSK | EEP | SACCH/TH PACCH/H | 1 - 2 |  |
|  |  |  |  | TCH/H | ffs | GMSK | EEP | FACCH/H SACCH/TH | 1 - 2 |  |
| UEP Unequal Error Protection - EEP Equal Error Protection - OS Operational Scenario Supported This row is intended for the realization of wide-band speech codec and is ffs Whether FACCH and PACCH are both needed for OS 2 multiplexing is ffs |