# Proposal for RRC description to GERAN Stage 2

# 1. INTRODUCTION

In this contribution is proposed additional text related to RRC to GERAN Stage 2: definitions for RRC Connection mobility and RRC connection modes. The baseline for this contribution has been UTRAN Radio Interface Protocol Architecture specification (3G TS 25.301 version 3.3.0).

# 2. PROPOSED ADDED TEXT

Following new sections are proposed to be added:

# 6.3.1b	RRC Connection Mobility

The different levels of RRC connection between MS and  GERAN are listed below:

-	No signalling connection exists
The MS has no relation to GERAN, only to CN. For data transfer, a signalling connection has to be established.

-	Signalling connection exists
There is a RRC connection between MS and GERAN. The MS position can be known on different levels:

-	GERAN Registration Area (GRA) level 
The MS position is known on GERAN registration area level. GRA is a specified set of cell, which can be identified on the BCCH.

-	Cell level
The MS position is known on cell level.

# 6.3.1c	RRC connection modes

Two modes of operation are currently defined for the MS, idle mode and connected mode.

After power on, the MS stays in idle mode until it transmits a request to establish an RRC connection. In idle mode the MS is identified by non-access stratum identities such as IMSI, TMSI and P-TMSI. In addition, the GERAN has no own information about the individual idle mode MSs, and can only address e.g. all MSs in a cell or all MSs monitoring a specific paging occasion.

The connected mode is entered when the RRC connection is established. A RRC connection is established between the MS and GERAN. The MS is assigned a radio network temporary identity (G-RNTI) to be used as MS identity. MS is identified within a GERAN with the G-RNTI.

The MS leaves the connected mode and returns to idle mode when the RRC connection is released or at RRC connection failure.