3G TS 25.323 V3.2.0 (2000-06)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Radio Access Network;

Packet Data Convergence Protocol (PDCP) Specification

(Release 1999)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organisational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organisational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organisational Partners' Publications Offices.

Keywords

PDCP

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2000, 3GPP Organizational Partners (ARIB, CWTS, ETSI, T1, TTA,TTC).

All rights reserved.

Contents

Foreword	4

1	Scope	5

2	References	5

3	Abbreviations	5

4	General	6

4.1	Objective	6

4.2	Overview on sublayer architecture	6

5	Functions	7

5.1	Header Compression	7

5.1.1	Assignment of PID values	8

5.1.2	TCP/IP and UDP/IP header compression (RFC 2507)	9

5.1.2.1	Assignment of PID values for RFC2507	9

5.2	Multiplexing	9

5.3	Data Transfer	9

5.3.1	Data transfer over acknowledged mode RLC	9

5.3.2	Data transfer over unacknowledged and transparent mode RLC	10

5.4	SRNS Relocation	10

5.4.1	PDCP Sequence Numbering	11

6	Services	11

6.1	Services provided to upper layers	11

6.2	Services expected from RLC layer	11

7	Elements for layer-to-layer communication	12

7.1	Primitives between PDCP and upper layers	12

8	Elements for peer-to-peer communication	12

8.1	Protocol data units	12

8.2	Formats	13

8.2.1	PDCP-No-Header PDU	13

8.2.2	PDCP Data PDU	13

8.2.3	PDCP SeqNum PDU	13

8.3	Parameters	13

8.3.1	PDU Type	14

8.3.2	PID	14

8.3.3	Data	14

8.3.4	Sequence number	14

9	Handling of unknown, unforeseen and erroneous protocol data	14

Annex A (informative): Change history	15

# Foreword

This Technical Specification (TS) has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# 1	Scope

The present document provides the description of the user plane Packet Data Convergence Protocol (PDCP).

PDCP provides its services to the NAS at the UE or the relay at the RAN.

PDCP uses the services provided by the Radio Link Control (RLC) sublayer.

The main functions of PDCP are:

-	compression of redundant Network PDU control information (header compression);

-	transfer of packet data protocol user data using services provided by RLC protocol.

The following functions are not part of release 1999 but will be included in Release 2000:

-	multiplexing of different RBs onto the same RLC-entity;

-	transfer of states and header compression context information to target SRNC/BSS during SRNS/BSS relocation.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.

[1]	3G TS 25.401: "UTRAN Overall Description".

[2]	3G TR 25.990: "Vocabulary for the UTRAN".

[3]	3G TS 25.301: "Radio Interface Protocol Architecture".

[4]	3G TS 25.303: "Interlayer Procedures in Connected Mode".

[5]	3G TS 25.322: "RLC Protocol Specification".

[6]	3G TS 25.331: "RRC Protocol Specification".

[7]	3G TS 23.121: "Architectural Requirements for Release 1999".

[8]	IETF RFC 2507: "IP Header Compression".

[9]	3G TS 23.060: "General Packet Radio Service (GPRS); Service description; Stage 2".

[10]	3G TS XX.XXX: “GERAN Overall Description – Stage 1”

[11]	3G TS 03.51: “GERAN Overall Description – Stage 2”

# 3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

AS	Access Stratum

AM	Acknowledged Mode

BSC	Base Station Controller

BSS	Base Station Sub-system

C-SAP	Control Service Access Point

IETF	Internet Engineering Task Force

IP	Internet Protocol

L2	Layer 2 (data link layer)

L3	Layer 3 (network layer)

NAS	Non Access Stratum

NTr	Non Transparent

PDCP	Packet Data Convergence Protocol

PDU	Protocol Data Unit

PID	Packet Identifier

RB	Radio Bearer

RFC	Request For Comments

RLC	Radio Link Control

RRC	Radio Resource Control

RTP	Real Time Protocol

SAP	Service Access Point

SDU	Service Data Unit

TCP	Transmission Control Protocol

Tr	Transparent

UDP	User Datagram Protocol

UE	User Equipment

UM	Un-acknowledged Mode

UMTS	Universal Mobile Telecommunications System

UTRA	UMTS Terrestrial Radio Access

UTRAN	UMTS Terrestrial Radio Access Network

# 4	General

## 4.1	Objective

The present document describes the functionality of PDCP. The overall UTRAN and GERAN logical architectures are defined in 3GPP TS 25.301 [3], and 3GPP TS 03.51 [11] respectively.

Network layer protocols are intended to be capable of operating over services derived from a wide variety of sub-networks and data links. The Core Network and RANs support several network layer protocols providing protocol transparency for the users of the service where required..

The introduction of new network layer protocols to be transferred over the RAN shall be possible without any changes to RAN protocols. PDCP shall provide optimisation functions aiding channel efficiency via transparent and non-transparent modes of operation. The supported optimisation methods are standardised IETF header compression algorithms, and header removal. The multiplexing of RBs onto the same RLC entity shall be supported in R00.

Multiplexing of RBs onto the same RLC entity will be included in Release 2000 but is not available in Release 1999. Therefore, in Release 1999 every RB, is connected to one PDCP entity and one PDCP entity is connected to one RLC entity. The PDCP entities are located in the PDCP sublayer.

Every PDCP entity uses zero, one or several header compression algorithm types with certain parameters. Several PDCP entities may use the same algorithm type. The algorithm types and their parameters are negotiated by RRC and indicated to PDCP through the PDCP Control Service Access Point (PDCP-C-SAP).

Since the adaptation of different network layer protocols to PDCP is implementation dependent, it is not defined in the present document.

## 4.2	Overview on sublayer architecture

Figure 1 shows the model of the PDCP within the UTRAN and GERAN protocol architectures. Every PDCP-SAP uses exactly one PDCP entity. Each PDCP entity uses none, one or several header compression algorithm types.

Figure 1: PDCP structure

Figure 1 represents only one possible structure for PDCP and this should not restrict implementation. However, subclauses 5.1 and 5.2 shall be adhered to.

# 5	Functions

Packet Data Convergence Protocol shall perform the following functions:

- header compression and decompression of IP data streams (e.g., TCP/IP and RTP/UDP/IP headers)at the transmitting and receiving entity, respectively. The header compression method is specific to the particular network layer, transport layer or upper layer protocol combinations e.g. TCP/IP and RTP/UDP/IP;

- header removal for IP data streams (e.g., TCP/IP and RTP/UDP/IP headers) at the transmitting entity, with optional header generation at the receiving entity (e.g. for PC-based voice applications)

-	transfer of user data. Transmission of user data means that PDCP receives PDCP SDU from the NAS and forwards it to the RLC layer and vice versa;

-	forwarding of PDCP SDUs and associated PDCP sequence numbering only when lossless SRNS/BSS relocation is to be supported;

-	multiplexing of different RBs onto the same RLC entity. Multiplexing is not part of Release 1999 but will be included in Release 2000.

## 5.1	Header Compression

The header compression method is specific for each network layer protocol type. The network layer protocol type is indicated during PDP context activation as defined in 23.060 [9]. The header compression algorithms and their parameters are negotiated by RRC for each PDCP entity and indicated to PDCP through the PDCP-C-SAP. Compressor and decompressor initiated signalling between peer PDCP entities, during operation, is carried out in the user plane.

The PDCP layer shall be able to support several header compression algorithms and it shall always be possible to extend the list of supported algorithms in the future.

The PDCP layer can have one or several PDCP entities. Each PDCP entity may use zero, one, or several header compression algorithms. It shall be possible to establish several header compression algorithms of different types related to one PDCP entity. Different PDCP entities may include header compression algorithms of the same type.

Figure 1 shows an example how PDCP may be configured.

### 5.1.1	Assignment of PID values

PDCP shall be able to distinguish different types of header compression packets to handle them with a correct header compression algorithm and furthermore to indicate the type of the packet within a certain algorithm. This is realised by utilising the PID field in the PDU structure. The table is reconfigured every time the PDCP entity is reconfigured.

The following table illustrates an example of the PID value allocation table when three arbitrary header compression methods (RFC 2507 [8], Methods A and B) are configured for one PDCP entity.

Table 1: Example of the PID value allocation table

| PID Value | Optimisation method | Packet type |
| --- | --- | --- |
| 0 | No header compression | - |
| 1 | RFC2507 | Full header |
| 2 | RFC2507 | Compressed TCP |
| 3 | RFC2507 | Compressed TCP nondelta |
| 4 | RFC2507 | Compressed non TCP |
| 5 | RFC2507 | Context state |
| 6 | Method A | Uncompressed TCP/IP |
| 7 | Method A | Compressed TCP/IP |
| 8 | Method B | Uncompressed IP/UDP/RTP |
| 9 | Method B | Compressed IP/UDP/RTP |
| ... | Unassigned value | - |

The assignment of the PID values follow the general rules listed below:

-	PID value 0 is reserved permanently for no compression;

-	PID values are assigned in ascending order, starting from 1;

-	PID values are assigned independently to each PDCP entity;

-	PID values are reassigned for the PDCP entity after renegotiation of the header compression algorithms;

-	the list of negotiated (or re-negotiated) header compression entities shall be examined, starting from the first one in the list. The number of PID values to be assigned is specified in the subclause for this algorithm;

-	if there are not enough unused PID values to be assigned to a header compression algorithm, the negotiated header compression entities using this algorithm shall be ignored without error notification;

-	PID values that are used and are not defined invalidate the PDCP PDU;

-	for a certain algorithm in a PDCP entity the assignment of PID values starts from (n+1) where n is the number of PID values already assigned to other algorithms. The assignment is done in the order the algorithms are negotiated by RRC. In the example given in table 1 RFC 2507 was the first, Method A was the second and Method B was the third algorithm in the PDCP Info information element exchanged between peer RRC entities. The PID follows this order.

The used header compression algorithm and the packet type are unambiguously known by the basis of the PID value and shall apply to peer PDCP entities. While transferring data, the PID values are conveyed in the field of the PDCP header belonging to the PDCP PDU. Any successfully negotiated algorithm may be used for header compression of a PDCP SDU.

### 5.1.2	TCP/IP and UDP/IP header compression (RFC 2507)

Detailed operation of the RFC 2507 header compression is described in clause 3 of the IETF specification RFC 2507 [8]. Furthermore the mechanisms related to error recovery and packet reordering are described in clauses 10 and 11 of the RFC 2507. These mechanisms shall be included in the functionality of the header compression supported by PDCP.

#### 5.1.2.1	Assignment of PID values for RFC2507

The following PID values shall be assigned to the RFC 2507 header compression in the order presented in the table where n is the number of PID values already assigned to other algorithms.

Table 2: PID values assigned to RFC 2507 header compression algorithm

| PID value | Optimisation method | Packet type |
| --- | --- | --- |
| n+1 | RFC 2507 | Full header |
| n+2 | RFC 2507 | Compressed TCP |
| n+3 | RFC 2507 | Compressed TCP non-delta |
| n+4 | RFC 2507 | Compressed non-TCP |
| n+5 | RFC 2507 | Context state |

## 5.2	Header Removal

Packets arriving with IPv6 base and extension headers, TCP, UDP or RTP headers are modified to remove all the header information. The remaining packet body is sent to the RLC via the appropriate SAP.

#### 5.2.1	Assignment of PID values for header removal

The following PID values shall be assigned to the header removal algorithm used by PDCP, where n is the number of PID values already assigned to other algorithms.

Table 4: PID values assigned to header removal

| PID value | Optimisation method | Packet type |
| --- | --- | --- |
| n+1 | N/A | IP/UDP/RTP Headers Removed |

## 5.3	Multiplexing

Multiplexing of different RBs onto the same RLC entity is not part of Release 1999 but will be included in Release 2000.

## 5.4	Data Transfer

### 5.4.1	Data transfer over acknowledged mode RLC

If header compression is negotiated the PDCP entity shall perform header compression upon reception of a PDCP-DATA.Req. The PDCP-PDU is then delivered in RLC-AM-DATA.Req to RLC.

During operation, when the peer PDCP entity receives the PDCP-PDU in an RLC-AM-DATA.Ind primitive, the PDCP entity shall perform the header decompression (if negotiated) of the PDCP-PDU to obtain the PDCP SDU and deliver the PDCP SDU to the PDCP user with the PDCP-DATA.Ind. The following figure illustrates data transfer over acknowledged mode RLC.

Figure 2: PDCP data transfer over acknowledged mode RLC

### 5.4.2	Data transfer over unacknowledged and transparent mode RLC

PDCP shall perform any negotiated header adaptation upon reception of a PDCP-DATA.Req. The PDCP-PDU is then delivered in RLC-UM-DATA.Req or RLC-Tr-DATA.Req to RLC.

When the peer PDCP entity receives the PDCP-PDU in the RLC-UM-DATA.Ind or RLC-Tr-DATA.Ind primitive, the PDCP entity shall perform the negotiated header re-adaptation of the PDCP-PDU to obtain the PDCP SDU and deliver the PDCP SDU to the PDCP user with the PDCP-DATA.Ind. The following figure illustrates data transfer over unacknowledged and transparent mode RLC.

Figure 3: PDCP data transfer over unacknowledged or transparent mode RLC

## 5.5	SRNS/BSS Relocation

Lossless SRNS/BSS relocation is only applicable when RLC is in in-sequence delivery and acknowledged mode RLC. PDCP will only support lossless SRNS/BSS relocation if it is 'capable' of doing so. This is indicated by RRC in the information element "Support for lossless SRNS/BSS relocation" in PDCP Capability and PDCP info.

The PDCP layer shall carry out the following functions during lossless SRNS/BSS relocation:

-	forwarding of PDCP SDUs and associated sequence numbering;

-	transfer of the next expected PDCP SDU sequence number from UE to target SRNC/BSS and vice versa (by RRC); and

-	reset of PDCP entities.

For each radio bearer, the Receive PDCP Sequence Number of the next PDCP SDU expected to be received is transferred from the source to target SRNC/BSS. For each radio bearer the source SRNC/BSS forwards to the target SRNC/BSS the downlink PDCP-SDUs. Source SRNC/BSS provides the Send PDCP SDU sequence number of the first PDCP SDU to be forwarded to the target SRNC/BSS.

The target SRNC/BSS shall send to the UE the next expected UL Receive PDCP Sequence Number. The UE shall send to the target SRNC/BSS the DL Receive PDCP Sequence Number of the next expected PDCP SDU. The successfully transmitted PDCP SDUs are thus confirmed.

The reset of all compression entities, for an RB, shall be made during SRNS/BSS relocation. Header compression is still possible during relocation Negotiated compression parameters remain valid during reset, but all state information is initialised, e.g. header compression contexts. The PDCP sequence numbers are reset to zero after relocation, if lossless SRNS/BSS relocation is supported. Therefore, in header compression case, the first 'compressed' packet is a full header. For Release 2000, it may be considered not to reset the PDCP entity, internal protocol information, i.e. states and header compression contexts, but to forward these from the source SRNC/BSS to target SRNC/BSS. Header compression for a PDCP entity can then continue from the state that it had directly before SRNS/BSS relocation.

In the case where lossless SRNS/BSS relocation is not supported, the PDCP layer shall carry out following functions:

-	reset of PDCP entities.

### 5.5.1	PDCP Sequence Numbering

PDCP sequence numbering is only applicable when lossless SRNS/BSS relocation is to be supported. The value of the PDCP sequence number ranges from 0 to 65535. The PDCP SN window size indicates the maximum number of PDCP PDUs that can be numbered at any given time. The PDCP SN window size is negotiated by RRC. When the PDCP entity is setup for the first time for the PDCP user the PDCP sequence numbers are initialised to zero.

For each radio bearer:

-	an UL_Send PDCP sequence number is associated with each sent PDCP-PDU in the UE and is incremented by one when a PDCP PDU is delivered to RLC;

-	a DL_Send PDCP sequence number is associated with each sent PDCP-PDU in the NW and is incremented by one when a PDCP PDU is delivered to RLC;

-	an UL_Receive PDCP sequence number is associated with each received PDCP-PDU in the NW and is incremented by one when a PDCP PDU is received from RLC or is incremented by one for each discarded RLC SDU, as indicated by the RLC SDU Discard function [5];

-	a DL_Receive PDCP sequence number is associated with each received PDCP-PDU in the UE and is incremented by one when a PDCP PDU is received from RLC or is incremented by one for each discarded RLC SDU, as indicated by the RLC SDU Discard function [5].

PDCP sequence numbers are never decremented in the PDCP Tx.

The PDCP SeqNum PDU shall be sent once by the peer PDCP entities when synchronisation of the PDCP SN is required. It shall only be used for radio bearers that support or are configured (by a radio bearer reconfiguration) to support lossless SRNS relocation. Synchronisation of PDCP SN is required after RLC reset or RB reconfiguration.

If RLC discards a RLC SDU which contains a PDCP SeqNum PDU, the next PDCP PDU delivered to RLC shall be a PDCP SeqNum PDU. When a PDCP entity receives a PDCP SeqNum PDU, the receive PDCP sequence number shall be set to the value indicated in the PDCP SeqNum PDU.

# 6	Services

## 6.1	Services provided to upper layers

The following services are provided by PDCP to upper layers:

-	PDCP SDU delivery.

## 6.2	Services available from RLC layer

For a detailed description of the following functions see [5].

-	Data transfer in acknowledged mode.

-	Data transfer in unacknowledged mode.

-	Data transfer in transparent mode.

-	Segmentation and reassembly.

-	In-Sequence delivery.

# 7	Elements for layer-to-layer communication

The interaction between the PDCP layer and other layers are described in terms of primitives where the primitives represent the logical exchange of information and control between the PDCP layer and other layers. The primitives shall not specify or constrain implementations.

## 7.1	Primitives between PDCP and upper layers

The primitives between PDCP and upper layers are shown in table 3.

Table 3: Primitives between PDCP and upper layers

| Generic Name | Parameter |
| --- | --- |
|  | Req. | Ind. | Resp. | Conf. |
| PDCP-DATA | Data | Data | Not Defined | Not Defined |
| CPDCP-CONFIG | PDCP-Info, RLC-SAP | Not Defined | Not Defined | Not Defined |
| CPDCP-RELEASE | RLC-SAP | Not Defined | Not Defined | Not Defined |
| CPDCP-RELOC | No Parameter | Not Defined | Not Defined | Not Defined |

Each Primitive is defined as follows:

a)	PDCP-DATA-Req./Ind.

-	PDCP-DATA-Req is used by higher user-plane protocol layers to request a transmission of higher layer PDU. PDCP-DATA-Ind is used to deliver PDCP SDU that has been received to upper user plane protocol layers.

b)	CPDCP-CONFIG-Req.

-	CPDCP-CONFIG Req is used to configure and – in case of already existing PDCP entity – to reconfigure a PDCP entity and to assign it to the radio bearer associated with that entity.

c)	PDCP-RELEASE-Req.

-	CPDCP-RELEASE-Req is used by RRC to release a PDCP entity.

d)	CPDCP- RELOC-Req.

-	CPDCP-RELOC-Req initiates the SRNS relocation procedure in PDCP.

The following parameters are used in the primitives:

1)	PDCP info:

-	contains the parameters for each of the header adaptation algorithms configured to be used by one PDCP entity.

2)	RLC-SAP:

-	the RLC-SAP (Tr/UM/AM) used by PDCP entity when communicating with RLC sublayer.

# 8	Elements for peer-to-peer communication

## 8.1	Protocol data units

Two different protocol data unit formats are defined in PDCP for Release 1999. This is configured for the PDCP entity by RRC with the information element, "PDCP PDU header" in PDCP info.

## 8.2	Formats

A PDCP PDU is byte-aligned, if the RLC is run on unacknowledged or acknowledged mode. Otherwise, in transparent mode, it is bit-aligned. In the drawings in subclause 8.2, bit strings are represented by tables in which the first bit is the leftmost one on the first line of the table, the last bit is the rightmost on the last line of the table, and more generally the bit string is to be read from left to right and then in the reading order of the lines.

SDUs are bit strings, with any nonnull length. If not compressed within PDCP an SDU is included from first bit onward.

### 8.2.1	PDCP-No-Header PDU

The PDCP-No-Header PDU does not introduce any overhead to the PDCP SDU.

The format of the PDCP-No-Header-PDU is shown in table 4.

Table 4: PDCP-No-Header PDU

Data

### 8.2.2	PDCP Data PDU

The data PDU is used to convey a payload unit containing a PDCP SDU, header compression related control signalling or data that has been obtained from PDCP SDU after header compression.

The format of the PDCP-Data-PDU is shown in table 5.

Table 5: PDCP-Data-PDU format

| PDU type | PID |
| --- | --- |
| Data |

### 8.2.3	PDCP SeqNum PDU

The sequence number PDU is used to convey a payload unit containing a PDCP PDU sequence number and PDCP SDU, header compression related control signalling or data that has been obtained from PDCP SDU after header compression.

The format of the PDCP-SeqNum-PDU is shown in table 6.

Table 6: PDCP-SeqNum-PDU format

| PDU type | PID |
| --- | --- |
| Sequence number |
| Data |

## 8.3	Parameters

If not otherwise mentioned in the definition of each field then the bits in the parameters shall be interpreted as follows: the left most bit string is the first and most significant and the right most bit is the last and least significant bit.

Unless otherwise mentioned, integers are encoded in standard binary encoding for unsigned integers. In all cases the bits appear ordered from MSB to LSB when read in the PDU.

### 8.3.1	PDU Type

# Length: 3 bits.

# The PDU type field indicates the PDCP-data-PDU type.

| Bit | PDU Type |
| --- | --- |
| 000 | PID field used for header compression information (PDCP-PDU format described in table 5) |
| 001 | PID field used for header compression information and the PDCP PDU sequence number included (PDCP-PDU format described in table 6) |
| 010-111 | Reserved (PDUs with this encoding are invalid for this version of the protocol) |

### 8.3.2	PID

# Length: 5 bits.

# The PID type field indicates the used header compression and packet type.

| Bit | Description |
| --- | --- |
| 00000 | No header compression |
| 00001-11111 | Dynamically negotiated header compression identifier, as described in subclause 5.1.1 |

PID field value defines used header compression type and packet type. One compression algorithm may reserve a certain amount of values from PID field value space for different packet types. Receiving PDCP makes reverse operation (e.g. header decompression) according to PID field value. There is not fixed relation between PID field value and used optimisation / packet type, but PID field values are defined dynamically at the PDCP parameter negotiation.

### 8.3.3	Data

PDCP SDUs that have been header compressed, as described in RFC 2507 for 1999, are mapped to this field if header compression is negotiated. Otherwise, PDCP SDUs are mapped to this field.

### 8.3.4	Sequence number

Length: 16 bits

PDCP PDU sequence number.

# 9	Handling of unknown, unforeseen and erroneous protocol data

## 9.1 Invalid PID Received

## 9.2 In-Sequence Mode Delivery Failure

Annex A (informative):
Change history

| Change history |
| --- |
| TSG-RAN# | Version | CR | Tdoc RAN | New Version | Subject/Comment |
| RAN_06 | - | - | RP-99645 | 3.0.0 | (12/99) Approved at TSG-RAN #6 and placed under Change Control |
| RAN_07 | 3.0.0 | 004 | RP-000041 | 3.1.0 | (03/00) Bit order of PDCP PDUs |
| RAN_07 | 3.0.0 | 005 | RP-000041 | 3.1.0 | Changes to PDCP |
| RAN_08 | 3.1.0 | 006 | RP-000221 | 3.2.0 | (06/00) Changes in PDCP PDU format due to PDCP sequence numbering |

Martin Hans

Siemens AG

Tel.: +49 5341 28 5851

e-mail: Martin.Hans@de.bosch.com

# Comments

Need to check what the spec number of this is, and whether it is still planned to create it

Check what the spec number of this is

I assume that header removal will never be used if acknowledgements are required since the correct packet  sequence  number cannot be guaranteed (if re-generated at the receiver) in this case.

PDCP may assume that these services are available

This section is required for the case a PID is received which does not have a corresponding table entry. The action to be performed in this case is FFS.

This section is required for the case where PDCP receives a message from RLC indicating that a packet cannot be delivery while PDCP is operating in ‘In-sequence delivery’ mode. The action to be performed is FFS.