# Drafting session outcome for Channel Coding proposal to GERAN Stage 2

# Introduction

This document proposes changes and additions (as agreed during the discussion session) to the current channel coding table in the GERAN Stage 2 description, ref [1]. In section 3 the new channel coding table is included with revision marks.

Proposed changes and additions.

TCH/FS, TCH/EFS and TCH/HS, with GMSK modulation, are added with a [tbd]. Decision will be taken after response from 3GPP SA2.

TCH/WFS GMSK, TCH/WFS 8-PSK and TCH/WHS 8-PSK are  added for AMR-WB.

The different AMR-NB codec modes are added for TCH/AFS, TCH/AHS and TCH/AQS.

TCH/F is updated with the applicable coding schemes for GMSK and 8-PSK.

TCH/H is removed. The use of the TCH/H channel for GMSK is considered to be very limited and it does not exist for 8-PSK today and is therefore not proposed to be part of this release.

CS1-4 and MCS1-9 are included for the PDTCH channels and the Stealing Bits are 8 for CS1-4 and MCS5-9. The 12 Stealing bits for the MCS1-4 are described as 8+4. The number of Stealing Bits is added for PDTCH Dedicated Physical Subchannel the same way as for Shared Physical Subchannel.

It was decided, at the drafting meeting during TSG GERAN #1, that TCH channels should be possible to be used for DPSCH. Since the PDTCH could also be used for DPSCH note 2 is removed.

Channel Coding

# Channel Coding

# Table 2 gives an overview of the logical traffic channels with the corresponding type of channel and their mapping to physical subchannel. The list shall be considered as the possible, but not mandatory, channels.

Table 2: Channel Coding

| Logical Channel | Mod. | Radio Block / Frame Size (Bits) | SB (1) | Channel Coding | Interleaving |  |  | Physical Subchannel |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Type | Rate |  | Type | Depth (bursts) |  |  |  |
| TCH/FS [tbd] | GMSK | 464 | 8 | CC | TCH/FS13 kbps |  | diag | 8 |  |  | DPSCH/F |
| TCH/EFS [tbd] | GMSK | 464 | 8 | CC | TCH/EFS12.2 kbps |  | diag | 8 |  |  | DPSCH/F |
| TCH/WFS [tbd] | GMSK | 464 | 8 | CC | [tbc] |  | diag | 8 |  |  | DPSCH/F |
| TCH/WFS [tbd] | 8PSK | 1392 | 24 | CC | [tbc] |  | diag | 8 |  |  | DPSCH/F |
| TCH/WHS [tbd] | 8PSK | 696 | 12 | CC | [tbc] |  | diag | 4 |  |  | DPSCH/H |
| TCH/HS [tbd] | GMSK | 232 | 4 | CC | TCH/HS5.6 kbps |  | diag | 4 |  |  | DPSCH/H |
| TCH/AFS | GMSK | 464 | 8 | CC | AMR4.75 AMR5.15 AMR5.90 AMR6.70 AMR7.40 AMR7.95 AMR10.2 AMR12.2 |  | diag | 8 |  |  | DPSCH/F |
| TCH/AHS | GMSK | 232 | 4 | CC | AMR4.75 AMR5.15 AMR5.90 AMR6.70 AMR7.40 AMR7.95 |  |  | 4 |  |  | DPSCH/H |
|  | 8PSK | 696 | 12 | CC | AMR4.75 AMR5.15 AMR5.90 AMR6.70 AMR7.40 AMR7.95 AMR10.2 AMR12.2 |  |  |  |  |  |  |
| TCH/AQS | 8PSK | 348 | 6 | CC | AMR4.75 AMR5.15 AMR5.90 AMR6.70 AMR7.40 AMR7.95 AMR10.2 AMR12.2 |  |  | 2 |  |  | DPSCH/Q |
| TCH/F | GMSK | 464 | 8 | CC | TCH/F9.6 TCH/F14.4 |  | diag | 2219 |  |  | DPSCH/F |
|  | 8PSK | 1392 | 24 | RS+CC | E-TCH/F28.8 E-TCH/F32.0 E-TCH/F43.2 |  |  |  |  |  |  |
| PDTCH/F | GMSK | 464 | 8+4 | CC | MCS1-4 |  | rect | 4 |  |  | SPSCH/F |
|  |  |  | 8 |  | CS1-4 |  |  |  |  |  |  |
|  |  |  | 8+4 |  | MCS1-4 |  |  |  |  |  | DPSCH/F |
|  |  |  | 8 |  | CS1-4 |  |  |  |  |  |  |
|  | 8PSK | 1392 | 8 |  | MCS5-9 |  | rect | 4 |  |  | SPSCH/F |
|  |  |  | 8 |  | MCS5-9 |  |  |  |  |  | DPSCH/F |
| PDTCH/H | GMSK | 464 | 8+4 | CC | MCS1-4 |  | rect | 4 |  |  | SPSCH/H |
|  |  |  | 8 |  | CS1-4 |  |  |  |  |  |  |
|  |  |  | 8+4 |  | MCS1-4 |  |  |  |  |  | DPSCH/H |
|  |  |  | 8 |  | CS1-4 |  |  |  |  |  |  |
|  | 8PSK | 1392 | 8 |  | MCS5-9 |  | rect | 4 |  |  | SPSCH/H |
|  |  |  | 8 |  | MCS5-9 |  |  |  |  |  | DPSCH/H |
| The number of Stealing Bits (SB) is ffs CC: Convolutional Code RS: Reed Solomon code |  |

# Editor's Note: the table above remains to be completed.

# References

# [1] “GERAN Overall Description, Stage 2”, Tdoc 3GPP TSG GERAN 200-471, Seattle, WA, USA, August 25 – September 1, 2000, source Rapporteur.