GPP TSG GERAN Adhoc #2	Tdoc GAHW-000090

Munich, Germany	Agenda Item 6.1.4.

9th-13th October 2000

Title: 	Comparison of AMR Speech Transmission over 8-PSK Quarterrate and GMSK Halfrate Voice Bearers

Source : 	Siemens

1. Introduction

8-PSK modulation allows the usage of quarterrate voice bearers for AMR speech transmission. This document compares the AMR speech transmission over 8-PSK quarterrate bearers with the AMR speech transmission over GMSK halfrate bearers (AHS).

2. Proposed Channel Coding for 8-PSK QR

We propose to use only the 6 AMR modes with the lowest data rates, which provide acceptable speech quality under realistic channel conditions.

2.1. Ordering according to subjective importance

The source encoded frames of speech data are reordered by using the reordering tables already applied for GSMK fullrate and halfrate voice bearers [1].

2.2. Protection classes

The bits of a speech frame are divided into two classes.

1a - Data protected with the CRC and the convolutional code.
1b - Data protected with the convolutional code.

No bits are transmitted unprotected.

2.3. Parity for speech frames

The class 1a bits are protected by a 6-bit CRC using the generator polynomial

g(D) = 1+D+D2+D3+D5+D6 as defined in [1] for AFS and AHS.

2.4. Convolutional Encoder

The class 1a bits, the 6 CRC bits and the class 1b bits then are encoded by a recursive systematic convolutional code using sets of the polynomials as defined in [1].

G4 = 1+D2+D3+D5+D6

G5 = 1+D+D4+D6

G6 = 1+D+D2+D3+D4+D6

G7 = 1+D+D2+D3+D6.

2.4. Puncturing

The output bits from the convolutional encoder are punctured properly to obtain 336 channel bits per frame

2.5. Inband data

The 2 bits of inband data are protected by a rate 1/3 blockcode using an appropriate coding scheme.

The resulting 6 inband bits are mapped on the strong bits of the 8-PSK symbol.

2.6. Stealing flags

In every block of 8-PSK symbols two symbols are reserved for stealing flags [4].

2.7. Interleaving

The bits are interleaved diagonally over two bursts.

3. Simulation results

The following figures compare the performance of AMR speech transmission using the channel coding scheme described above with the AMR speech transmission over GMSK halfrate bearers based on analysis of frame erasure rate (FER) and the residual bit error rate (RBER) of the class 1b bits.

The error patterns for the simulations are generated with internal simulation chains for TU03 channel profiles with ideal frequency hopping at a carrier frequency of 900 MHz.

3.1. AMR mode with 4.75 kbps

3.2. AMR mode with 5.15 kbps

3.3. AMR mode with 5.90 kbps

3.4. AMR mode with 6.70 kbps

3.5. AMR mode with 7.40 kbps

3.6. AMR mode with 7.95 kbps

4. Conclusion

This document provides a performance overview of AMR speech transmission over 8-PSK quarterrate voice bearers by evaluation of the 6 lowest AMR modes. Using the proposed channel coding scheme results in a average FER loss of about 3 dB to 4 dB but some gain in RBER 1b in channel C/I in comparision with transmission over GMSK HR bearers. Our analysis shows that optimization of the channel coding scheme to decrease the FER by allowing higher RBER in class 1b is possible.

4. References

[1] Digital Cellular Telecommunications System (Phase 2+), Channel Coding, GSM 05.03 version 8.5.0. Release 1999, june 2000

[2] SMG2 WS GERAN/EDGE, T-doc 2e00-135 “Performance Analysis of Quarter Rate Speech Channels”, Nokia, 8-12 may 2000, Seattle, Washington, USA

[3] 3GPP TSG GERAN Adhoc #1, T-doc 2g00-076, “Performance Analysis of Quarter Rate Speech Channels”, Nokia, 7-11 august 2000, Helsinki, Finland

[4] 3GPP TSG GERAN Adhoc #1, T-doc 2g00-055, “Stealing Bits Aspects for GERAN”, Ericsson, 7-11 august 2000, Helsinki, Finland

[5] 3GPP TSG GERAN Adhoc #2, GAHW-000028, “Performance Analysis for 8-PSK Half Rate and Quarter Rate Voice Bearers”, Motorola, 9-13 october 2000, Munich, Germany