3GPP TSG GERAN Adhoc #2	Tdoc GERAN Adhoc 0093/00
October 9 – October 13, 2000	Agenda item 6.1.4 
Munich, Germany

Source: Ericsson

8PSK HR Voice Bearer performance

# Background

An 8-PSK HR optimized AMR voice bearer may have some interesting features compared to the already standardized TCH/AHS GMSK HR bearer. One is the possibility to use all eight AMR modes thus making the clean channel speech quality of the HR bearer equal to that of the FR (TCH/AFS) bearer and possibly simplify tandem free connection between half rate and full rate.

Another interesting property of an 8-PSK HR bearer would be increased channel robustness compared to GMSK HR. Such improvements in robustness has already been reported in several earlier contributions [1], [2]. There is also a requirement document [3], which reflects the desire to have an 8-PSK HR bearer with increased robustness to improve system capacity.

In this contribution a comparison is made between the performance of the TCH/AFS, TCH/AHS and an 8-PSK HR bearer. The comparison is based both on channel coding statistics and also a formal listening test. This document is an update of [9], where the channel coding statistics chapter has been updated with results for TU3 noFH and HT100 iFH in addition to the previous Tu3 iFH results.

# 8-PSK HR channel coding

Channel coding schemes for all eight AMR modes have been designed for 8-PSK HR. The coding scheme follows the “guidelines” in [8] which means that it is based on existing polynomials and TCH/AFS class allocation.

During the design, the performance has been assessed by statistical measures like FER and RBER as well as informal expert listening in a similar way as when the channel coding for TCH/AFS and TCH/AHS was developed.

The total number of available bits on the 8-PSK HR air interface is 696 bits per 20 ms speech frame. No extra overhead, i.e. no compressed IP/UDP/RTP header or RLC/MAC header is assumed for the 8-PSK HR bearer.

## Interleaving

The same type of diagonal interleaving as for TCH/AHS has been used for 8-PSK HR.

## Stealing bits

Eight of the least sensitive bits in the 8-PSK mapping have been set aside per burst for stealing bits. This means that for each 20 ms speech frame 16 of the available 696 bits are not used for the speech payload. Note that this is not necessarily a proposal from Ericsson, it is only to have a reasonable assumption of the number of speech payload bits.

## Inband coding

The same link adaption and inband channel as for TCH/AFS and TCH/AHS is assumed. The protection of the inband channel is however different compared to TCH/AFS and TCH/AHS. Two information bits are sent every frame thus allowing a mode set of maximum four modes. Mode indication and mode command/request alternates allowing modes changes every 40 ms.

The two information bits are encoded with a block code to a total of 27 air interface bits. These bits are mapped on the most sensitive bits of the 8-PSK symbols.

## CRC encoding

All schemes uses the same polynomial, g(D) = D6 + D5 + D3 + D2 + D + 1, to generate the 6 CRC parity for the class 1A bits. This is the same polynomial as used in TCH/AFS and TCH/AHS.

The same allocation of bits into classes as in TCH/AFS is used. Table 1 shows this allocation.

| AMR mode | Total number of bits | Number of class 1A bits | Number of class 1B bits | Number of class 2 bits |
| --- | --- | --- | --- | --- |
| MR475 | 95 | 39 | 56 | 0 |
| MR515 | 103 | 49 | 54 | 0 |
| MR59 | 118 | 55 | 63 | 0 |
| MR67 | 134 | 55 | 79 | 0 |
| MR74 | 148 | 61 | 87 | 0 |
| MR795 | 159 | 75 | 84 | 0 |
| MR102 | 204 | 65 | 139 | 0 |
| MR122 | 244 | 81 | 163 | 0 |

Table 1.  8-PSK HR class allocation

## Convolutional encoding

The following four polynomial from the GSM 05.03 [4] specification are used for the convolutional encoding.

G4 = D6 + D5 + D3 + D2 + 1		G5 = D6 + D4 + D + 1

G6 = D6 + D4 + D3 + D2 + D + 1		G7 = D6 + D3 + D2 + D + 1

The channel coding schemes for all 8-PSK HR modes uses a RSC, recursive systematic code. Table 2 shows an overview of how the 653 (=696-16-27) bit code words are generated.

| AMR mode | Feed forward polynomials | Feedback polynomial | Code rate for class 1A and CRC | Average code rate for class 1B | Number of bits punctured |
| --- | --- | --- | --- | --- | --- |
| MR475 | G4 G4 G5 G5 G6 G6 G7 | G6 | 3/19 | 3/17 | 96 |
| MR515 | G4 G4 G5 G6 G6 G7 | G6 | 3/18 | 3/16 | 37 |
| MR59 | G4 G4 G5 G6 G6 G7 | G6 | 3/16 | 3/14 | 127 |
| MR67 | G4 G4 G5 G6 G7 | G6 | 6/28 | 6/26 | 77 |
| MR74 | G4 G4 G5 G6 G7 | G6 | 4/17 | 4/16 | 147 |
| MR795 | G4 G5 G6 G7 | G6 | 9/36 | 9/32 | 31 |
| MR102 | G4 G5 G6 G7 | G6 | 4/13 | 4/11 | 211 |
| MR122 | G4 G5 G6 | G5 | 5/14 | 5/11 | 115 |

Table 2. 8-PSK HR Channel Coding

The puncturing is designed to give an even protection of the class 1A bits while the protection within class 1B is not equal to reflect the individual error sensitivity of the class 1B bits. The property of the 8-PSK symbol mapping with one bit more sensitive than the other two is exploited when the coded bits are mapped to symbols similar to the TDMA-HR channel coding for AMR under development in TIA TR45.3.5.

# Statistical Results

The curves in figure 1 - 22 show the frame erasure rate (FER) for GMSK FR (TCH/AFS), GMSK HR (TCH/AHS) and 8-PSK HR. Three channel cases have been simulated, TU3 with ideal frequency hopping (IFH), TU3 with no frequency hopping (NFH) and HT100 with ideal frequency hopping. All simulations are without receiver impairments. The length of the simulations is 10000 speech frames. For AMR the ideal mode switching threshold is below 1% FER which means that FER comparisons are not so relevant for higher FER with the exception of the most robust mode in a mode set, normally the MR475 mode. The results are summarised in table .

| Channel | Modulation and rate | AMR mode |
| --- | --- | --- |
|  |  | MR475 | MR515 | MR59 | MR67 | MR74 | MR795 | MR102 | MR122 |
| TU3 IFH | GMSK FR |  |  |  |  |  |  |  |  |
|  | GMSK HR |  |  |  |  |  |  | - | - |
|  | 8PSK HR |  |  |  |  |  |  |  |  |
| HT100 IFH | GMSK FR |  |  |  |  |  |  |  |  |
|  | GMSK HR |  |  |  |  |  |  | - | - |
|  | 8PSK HR |  |  |  |  |  |  |  |  |
| TU3 NFH | GMSK FR |  |  |  |  |  |  |  |  |
|  | GMSK HR |  |  |  |  |  |  | - | - |
|  | 8PSK HR |  |  |  |  |  |  |  |  |

Table 1. Required C/I for a class 1a FER of 1% for different AMR codecs under different channel conditions.

Figure 1. FER MR122 TU3 IFH

Figure 2. FER MR102 TU3 IFH

Figure 3. FER MR795 TU3 IFH

Figure 4. FER MR74 TU3 IFH

Figure 5. FER MR67 TU3 IFH

Figure 6. FER MR59 TU3 IFH

Figure 7. FER MR515 TU3 IFH

Figure 8. FER MR475 TU3 IFH

Figure 9. FER MR122 HT100 IFH

Figure 10. FER MR102 HT100 IFH

Figure 11. FER MR795 HT100 IFH

Figure 12. FER MR74 HT100 IFH

Figure 13. FER MR67 HT100 IFH

Figure 14. FER MR59 HT100 IFH

Figure 15. FER MR515 HT100 IFH

Figure 16. FER MR475 HT100 IFH

Figure 17. FER MR122 TU3 NFH

Figure 18. FER MR102 TU3 NFH

Figure 19. FER MR795 TU3 NFH

Figure 20. FER MR74 TU3 NFH

Figure 21. FER MR67 TU3 NFH

Figure 22. FER MR59 TU3 NFH

Figure 23. FER MR515 TU3 NFH

Figure 24 FER MR475 TU3 NFH

# Listening test

In addition to the simulations described in section 3 a formal listening test has been done. The ETSI fixed point c-code [5] was used to simulate the AMR speech coder. The test was done at static C/I conditions (TU3, ideal frequency hopping). The AMR adaption was turned off but the decoded inband bits was used by the channel decoder to select decoding mode, i.e. an error in the decoded inband bits may result in an erased frame. To limit the listening test to a feasible size not all modes where tested for all C/I points.

The same radio channel simulator that was used for the statistical results in section 3 was used to create the speech samples for the listening test. Some additional data about the test:

- ACR test according to ITU P.800 methodology ("MOS-test")

- 30 non-expert listeners

- 6 randomization groups with presentation order and source sample randomization

- Monaural listening in headphones 79 dB SPL

- Hooth noise 25 dBA in listening room

- High quality recorded Swedish speech source material -26 dBOV

- 2 male and 2 female talkers per condition

- 8 seconds long sentence pair per talker and condition

- Source material mod-IRS send filtered

- Processed material mod-IRS receive filtered

- Same 32 s fading channel realization used for all GSM/EDGE degraded channel conditions

- Original, G.726 32 kb/s ADPCM, GSM-EFR, TDMA-EFR  and 5 MNRU references

- Total 48 conditions

Table 3 shows the results for all conditions. The curve in figure 9 shows the MOS score for GMSK-FR, GMSK HR and 8-PSK HR with "ideal adaption" where the mode with the highest score is picked for each condition.

| Condition | MOS | CI 95% |
| --- | --- | --- |
| Original | 4,17 | 0,14 |
| G.726 | 3,69 | 0,16 |
| GSM EFR 10 dB C/I | 3,61 | 0,16 |
| IS-641 17 dB C/I 7 Hz | 2,89 | 0,17 |
| IS-641 17 dB C/I 77 Hz | 3,36 | 0,17 |
| MNRU 6 dB | 1,25 | 0,08 |
| MNRU 12 dB | 1,97 | 0,12 |
| MNRU 18 dB | 3,13 | 0,15 |
| MNRU 24 dB | 3,79 | 0,16 |
| MNRU 30 dB | 4,11 | 0,15 |
| MR122 Clean | 3,98 | 0,14 |
| MR102 Clean | 3,83 | 0,15 |
| MR795 Clean | 3,68 | 0,15 |
| MR74 Clean | 3,70 | 0,15 |
| MR67 Clean | 3,64 | 0,15 |
| MR59 Clean | 3,56 | 0,16 |
| MR515 Clean | 3,31 | 0,15 |
| MR475 Clean | 2,95 | 0,14 |
| MR122 GMSK-FR 16 dB | 3,95 | 0,14 |
| MR122 GMSK-FR 13 dB | 3,87 | 0,15 |
| MR102 GMSK-FR 13 dB | 3,86 | 0,14 |
| MR102 GMSK-FR 10 dB | 3,79 | 0,13 |
| MR795 GMSK-FR 10 dB | 3,55 | 0,15 |
| MR795 GMSK-FR 7 dB | 3,77 | 0,15 |
| MR74 GMSK-FR 7 dB | 3,78 | 0,14 |
| MR59 GMSK-FR 4 dB | 3,26 | 0,18 |
| MR515 GMSK-FR 4 dB | 3,02 | 0,16 |
| MR475 GMSK-FR 1 dB | 2,32 | 0,15 |
| MR795 GMSK-HR 16 dB | 3,82 | 0,15 |
| MR59 GMSK-HR 13 dB | 3,40 | 0,16 |
| MR59 GMSK-HR 10 dB | 3,17 | 0,16 |
| MR475 GMSK-HR 10 dB | 2,95 | 0,15 |
| MR475 GMSK-HR 7 dB | 2,68 | 0,14 |
| MR475 GMSK-HR 4 dB | 1,64 | 0,12 |
| MR122 8-PSK-HR 16 dB | 3,98 | 0,16 |
| MR102 8-PSK-HR 16 dB | 3,80 | 0,15 |
| MR102 8-PSK-HR 13 dB | 3,73 | 0,13 |
| MR795 8-PSK-HR 13 dB | 3,62 | 0,15 |
| MR67 8-PSK-HR 13 dB | 3,67 | 0,14 |
| MR795 8-PSK-HR 10 dB | 3,24 | 0,16 |
| MR67 8-PSK-HR 10 dB | 3,34 | 0,14 |
| MR59 8-PSK-HR 10 dB | 3,43 | 0,16 |
| MR67 8-PSK-HR 9 dB | 3,26 | 0,15 |
| MR59 8-PSK-HR 9 dB | 3,28 | 0,16 |
| MR475 8-PSK-HR 9 dB | 3,03 | 0,14 |
| MR515 8-PSK-HR 7 dB | 2,79 | 0,14 |
| MR475 8-PSK-HR 7 dB | 2,59 | 0,14 |
| MR475 8-PSK-HR 4 dB | 1,49 | 0,11 |

Table 3. MOS scores

Figure 24. MOS scores

The resulting MOS curves for GMSK FR and GMSK HR are similar to the GSM 06.75 characterization test [6] although it is important to note that results from different listening tests can not be directly compared with each other. In this case the radio simulator for GMSK is not the same as the ETSI AMR radio simulator that was used in the GSM AMR characterization which means that a direct comparison of the degraded channel conditions can not be done.

| Condition | MOS | GMSK FR | GMSK HR | 8-PSK HR |
| --- | --- | --- | --- | --- |
| GSM EFR 10 dB C/I | 3,61 | 5.5 dB | 14.5 dB | 11.5 dB |
| TDMA-EFR 17 dB C/N 7 Hz | 2,89 | 2.5 dB | 8 dB | 7.5 dB |
| TDMA EFR 17 dB C/N 77 Hz | 3,36 | 4.5 dB | 13 dB | 9.5 dB |

Table 4.  Reference conditions

Table 4 shows the scores of the GSM-EFR and TDMA references and the C/I level for the corresponding quality for the AMR cases. The GSM-EFR reference was simulated with the same radio simulator as the AMR cases. The TDMA reference was simulated using software distributed in TR 45.3.5 during the TDMA-EFR standardization.

# Summary

The listening test results for TU3 iFH confirms what can be seen in the FER curves for TU3 iFH: 8-PSK HR gives a speech quality improvements for medium to high C/I but it does not improve the robustness at low C/I compared to TCH/AHS. The target requirement in [3] of a 3-4 dB delta from TCH/AFS is not met. At the suggested point, MR74 1% FER, the FER curves show a 5.5 dB delta and approximately the same difference can be seen in the listening test results.

In the FER curves it can be seen that  8PSK HR has a relative gain going from TU3 iFH to HT100 iFH, but a loss going to TU3 noFH. The reason for that ….??

# References

[1] Lucent, Tdoc SMG2 575/00, “Physical layer design studies for speech in RT-EGPRS”

[2] Nokia, Tdoc SMG2 2-00-745, “8PSK Half Rate Voice Bearer”

[3] AT&T, Tdoc SMG2 EDGE 2e00-113, “Target Requirements for 8PSK HR Voice Bearers”

[4] ETSI, GSM 05.03, “Digital cellular telecommunications system Channel coding”

[5] ETSI, GSM 06.73, “Digital cellular telecommunications system ANSI-C code for the GSM Adaptive Multi-Rate speech codec”

[6] ETSI, GSM 06.75, “Digital cellular telecommunications system Performance Characterization of the GSM Adaptive Multi-Rate (AMR) speech codec”

[7] Ericsson/Nokia/Siemens, Tdoc SMG11 329/98, “Objective test results for alternative AMR channel coding schemes”

[8] Nokia, Tdoc 2g00-101, “Realisation and channel coding of new AMR bearers”

[9] Ericsson, Tdoc TSG GERAN 161/00, “8PSK HR Voice Bearer performance”