Source: Ericsson

Changes to stage 2 descriptions: RLC/MAC PDU formats

# 1.	Introduction

It has been agreed to include a section about RLC/MAC PDU formats in the stage 2 description [1]. This document proposes some changes to that text and to include it in the Stage 2 description [1].

# 2.	Proposed changes to stage 2 description

## RLC/MAC PDU formats for different protocol modes

### Acknowledged RLC mode

#### Shared MAC mode

In shared MAC mode one or more radio bearers of one or more mobile stations can be multiplexed to the same physical subchannel.

The RLC/MAC header is already defined in 04.60 and depicted in Figure 1 to  Figure 5 for downlink and in Figure 7 to Figure 11 for uplink. EGPRS coding schemes (MCS-1, … , MCS-9) and GPRS coding schemes CS-1, … ,CS-4 are used (the exact use of some fields in the EGPRS header, such as the current RRBP bits, may change).

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Payload Type | RRBP | S/P |  | USF |  |
| PR | TFI | FBI |
|  |  |  | BSN |  |  |  | E |
| Length indicator | M | E |
| . . . |
| Length indicator | M | E |

Figure 1: Downlink RLC data block header for CS-1, CS-2, CS-3 and CS-4.

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| TFI | RRBP | ES/P | USF |
| BSN1 | PR | TFI |
| BSN1 |
| BSN2 | BSN1 |
| CPS | BSN2 |

Figure 2: Downlink RLC data block header for MCS-7, MCS-8 and MCS-9

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| TFI | RRBP | ES/P | USF |
| BSN1 | PR | TFI |
| BSN1 |
|  | CPS | BSN1 |

Figure 3: Downlink RLC data block header for MCS-5 and MCS-6

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| TFI | RRBP | ES/P | USF |
| BSN1 | PR | TFI |
| BSN1 |
|  | SPB | CPS | BSN1 |

Figure 5: Downlink RLC data block header for MCS-1, MCS-2, MCS-3  and MCS-4

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Payload Type | Countdown Value | SI | R |
| spare | TFI | TI |
|  |  |  | BSN |  |  |  | E |
| Length indicator | M | E |
| . . . |
| Length indicator | M | E |
|  |  |  | TLLI |  |  |  |

Figure 7: Uplink RLC data block header for CS-1, CS-2, CS-3 and CS-4.

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| TFI | Countdown Value | SI | R |
| BSN1 | TFI |
| BSN2 | BSN1 |
| BSN2 |
| Spare | RSB | CPS |
|  |  | Spare |

Figure 6: Uplink RLC data block header for MCS-7, MCS-8 and MCS-9

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| TFI | Countdown Value | SI | R |
| BSN1 | TFI |
| CPS | BSN1 |
| Spare | CPS |
|  | Spare |

Figure 7: Uplink RLC data block header for MCS-5 and MCS-6

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| TFI | Countdown Value | SI | R |
| BSN1 | TFI |
| CPS | BSN1 |
|  | Spare | RSB | SPB | CPS |

Figure 11: Uplink RLC data block header for MCS-1, MCS-2, MCS-3  and MCS-4

#### Dedicated MAC mode

### To avoid cumbersome re-design of the GPRS/EGPRS channel codes RLC/MAC header and coding schemes (CS-1, … ,CS-4 and MCS-1, … , MCS-9) as defined in 6.7.1.1 are used without any modifications. Unacknowledged RLC mode

#### Shared MAC mode

#### To avoid cumbersome re-design of the GPRS/EGPRS channel codes RLC/MAC header and coding schemes (CS-1, … ,CS-4 and MCS-1, … , MCS-9) as defined in 6.7.1.1 are used without any modifications. Dedicated MAC mode using PDTCH.

To avoid cumbersome re-design of the GPRS/EGPRS channel codes RLC/MAC header and coding schemes (CS-1, … ,CS-4 and MCS-1, … , MCS-9) as defined in 6.7.1.1 are used without any modifications.

#### Dedicated MAC mode using TCH

GERAN R’00 will provide a dedicated unacknowledged radio bearer towards the Iu-ps interface. This bearer could be used by services having a fairly constant bit rate, e.g. streaming.

The RLC header defined below is concatenated with the data part of the payload and fitted into the radio block, the payload bit stream can if necessary be truncated to fit both data and header into the block to be encoded.

The purpose of not reusing the RLC/MAC-header in EGPRS is to avoid protocol-overhead since the EGPRS-header offers several fields that are redundant in unacknowledged operation. Thus, the reduced RLC header only consists of the following fields:

- Block Sequence Number (BSN),

- Length Indicator (LI),

- Extension bit (E), and

- Block Check Sequence (BCS 8) (a 16 bit BCS for the payload is optional)

The RLC-PDU header is assembled as depicted in Figure 1.

| Bit |
| --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| BSN | E |
| LI | E |
| … | … |
| LI | E |
| BCS 8 |

Figure 9: Uplink/Downlink RLC data block header for dedicated MAC mode on TCH

### Transparent RLC mode

#### Dedicated MAC mode

The transparent mode is used for example to transmit voice in GERAN. The different channel coding schemes used for voice in GSM are used. New coding schemes for 8-PSK quarter rate, half rate and possibly full rate speech are also required. Other coding schemes like e.g. CSD/ECSD is FFS.

Since RLC is used in transparent mode and MAC in dedicated mode, no RLC/MAC header has to be added.

# Refrences

[1]	43.051, “GERAN Overall Description, Stage 2”