# Channel Coding proposal to GERAN Stage 2

# Introduction

This document proposes changes and additions (as agreed during the discussion) to the current channel coding table in the GERAN Stage 2 description, ref [1]. In section 3 the new channel coding table is included with revision marks.

# References

# [1] “GERAN Overall Description, Stage 2”, Tdoc 3GPP TSG GERAN 200-471, Seattle, WA, USA, August 25 – September 1, 2000, source Rapporteur.

Modification to stage 2

Note: revision marks have been removed for readability purposes.

----------------------------------------------------------------------------------------------------------------

# Channel Coding

# Table 2 gives an overview of the logical traffic channels with the corresponding type of channel and their mapping to physical subchannel. The list shall be considered as the possible, but not mandatory, channels.

Table 2: Channel Coding

| Logical Channel | Mod. | Radio Block / Frame Size (Bits) | SB (1) | Channel Coding | Interleaving | Physical Subchannel |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Type | Rate | Type | Depth (bursts) |  |
| TCH/FS [tbd] (2) | GMSK | 464 | 8 | CC | 13 kbps | diag | 8 | DPSCH/F |
| TCH/EFS [tbd] (2) | GMSK | 464 | 8 | CC | 12.2 kbps | diag | 8 | DPSCH/F |
| TCH/WFS [tbd] (3) | GMSK | 464 | 8 | CC | [tbc] | diag | 8 | DPSCH/F |
| O-TCH/WFS[tbd] (3) | 8PSK | 1392 | 24 | CC | [tbc] | diag | 8 | DPSCH/F |
| O-TCH/WHS [tbd] (3) | 8PSK | 696 | 12 | CC | [tbc] | diag | 4 | DPSCH/H |
| TCH/HS [tbd] (2) | GMSK | 232 | 4 | CC | 5.6 kbps | diag | 4 | DPSCH/H |
| TCH/AFS | GMSK | 464 | 8 | CC | TCH/AFS4.75 TCH/AFS5.15 TCH/AFS5.90 TCH/AFS6.70 TCH/AFS7.40 TCH/AFS7.95 TCH/AFS10.2 TCH/AFS12.2 | diag | 8 | DPSCH/F |
| TCH/AHS | GMSK | 232 | 4 | CC | TCH/AHS4.75 TCH/AHS5.15 TCH/AHS5.90 TCH/AHS6.70 TCH/AHS7.40 TCH/AHS7.95 | diag | 4 | DPSCH/H |
| O-TCH/AHS | 8PSK | 696 | 12 | CC | O-TCH/AHS4.75 O-TCH/AHS5.15 O-TCH/AHS5.90 O-TCH/AHS6.70 O-TCH/AHS7.40 O-TCH/AHS7.95 O-TCH/AHS10.2 O-TCH/AHS12.2 | diag | 4 | DPSCH/H |
| O-TCH/AQS | 8PSK | 348 | 6 | CC | O-TCH/AQS4.75 O-TCH/AQS5.15 O-TCH/AQS5.90 O-TCH/AQS6.70 O-TCH/AQS7.40 O-TCH/AQS7.95 O-TCH/AQS10.2 O-TCH/AQS12.2 | diag | 2 | DPSCH/Q |
| TCH/F | GMSK | 464 | 8 | CC | TCH/F9.6 TCH/F14.4 | diag | 22 | DPSCH/F |
| E-TCH/F | 8PSK | 1392 | 24 | RS+CC | E-TCH/F28.8 E-TCH/F32.0 E-TCH/F43.2 | diag | 22 | DPSCH/F |
| PDTCH/F | GMSK | 464 | 8+4 | CC | MCS1-4 | rect | 4 | SPSCH/F |
|  |  |  | 8 |  | CS1-4 |  |  |  |
|  |  |  | 8+4 |  | MCS1-4 |  |  | DPSCH/F |
|  |  |  | 8 |  | CS1-4 |  |  |  |
|  |  |  | 8+4 |  | MCS1-4 | ffs | ffs | DPSCH/F |
|  |  |  | 8 |  | CS1-4 |  |  |  |
|  | 8PSK | 1392 | 8 |  | MCS5-9 | rect | 4 | SPSCH/F |
|  |  |  | 8 |  | MCS5-9 |  |  | DPSCH/F |
|  |  |  | 8 |  | MCS5-9 | ffs | ffs | DPSCH/F |
| PDTCH/H | GMSK | 464 | 8+4 | CC | MCS1-4 | rect | 4 | SPSCH/H |
|  |  |  | 8 |  | CS1-4 |  |  |  |
|  |  |  | 8+4 |  | MCS1-4 |  |  | DPSCH/H |
|  |  |  | 8 |  | CS1-4 |  |  |  |
|  |  |  | 8+4 |  | MCS1-4 | ffs | ffs | DPSCH/H |
|  |  |  | 8 |  | CS1-4 |  |  |  |
|  | 8PSK | 1392 | 8 |  | MCS5-9 | rect | 4 | SPSCH/H |
|  |  |  | 8 |  | MCS5-9 |  |  | DPSCH/H |
|  |  |  | 8 |  | MCS5-9 | ffs | ffs | DPSCH/H |
| The number of Stealing Bits (SB) is ffs The possibility to establish TCH/EFS, TCH/FS, TCH/HS speech channels is to be decided by 3GPP SA2 Wideband AMR speech service over TCH/WFS, O-TCH/WHS and O-TCH/WHS is still under study within 3GPP SA4. CC: Convolutional Code RS: Reed Solomon code |

# Editor's Notes:

# The table above remains to be completed.

# Except for the already existing logical channels, the 8PSK modulated logical channel are indicated by an "O-" prefix (as in Octal PSK).

# ----------------------------------------------------------------------------------------------------------------