3GPP TSG GERAN Adhoc #2	Tdoc GAHW-000102
October 9-13, 2000	
Munich, Germany

Notes from drafting session on bearers, identifiers, TBFs etc

Source:	AT&T

# Reminder of the agreed baseline (TBF/RLC)

The following was agreed to be a baseline assumption for the relation between TBFs and RLC flows etc, to be used as a starting point for discussion (assuming shared MAC mode).

- One ‘RLC flow’ per TBF

- One TFI per TBF

- Allow multiple TBFs per MS

- One USF addresses one TBF*

- TBF established only when there is traffic to send

- RB lifetime can be longer than TBF lifetime

*FFS

# Common view on potential problems with baseline solution

Proponents of enhancement proposals stressed the following problems with the baseline scheme.

Ericsson:

- 8 addressable uplink TBFs per physical subchannel not sufficient

- TBF establishment signalling

(GAHW-000072)

Nokia:

- TBF establishment signalling

- The network must schedule data flows of one MS in the uplink, rather than the MS itself

(GAHW-000056)

# Analysis of enhancement proposals

Solutions described in the following contributions for enhancing the baseline scheme were discussed.

GAHW-000091 (Nokia)

GAHW-000072 (Ericsson)

GAHW-000054 (Nokia)

In addition, the proposal to keep a TBF alive for some time even without traffic in the transmitter buffer was briefly discussed (proponents: Vodafone, Nokia, Ericsson, Siemens). One example of usage is given by Tdoc GAHW-000061.

# Adopting a working assumption on TBF/RLC entity relation functionality for R4

## Agreements

The following was agreed as additions/modifications of the baseline assumptions.

Shared physical subchannel:

Dynamic allocation:

-One or more USFs may be allocated to a single MS

-One or more TBFs of one MS may be associated with one USF

Fixed allocation:

- One or more TBFs of one MS may be associated with one ‘fixed allocation’

Dedicated physical subchannel:

- No TBF is associated with a data flow on a TCH logical channel

Lucent accepted the task to draft a change proposal to 43.051 (Tdoc GAHW-000098), incorporating agreements made.

## Outstanding issues

The baseline functionality may be increased by additional functionality, as a consequence of consensus on the following issues.

Shared physical subchannel:

Baseline: One ‘RLC flow’ maps to exactly one TBF (Lucent, Nokia)

- Multiple ‘RLC flows’ on one TBF possible through MAC multiplexing (Ericsson)

Baseline: TBF is always released when no traffic in transmitter buffer (Lucent)

- TBF may stay alive without traffic in transmitter buffer (Nokia, Vodafone, Ericsson, Siemens)

Baseline: One TFI is unique on one uplink physical subchannel (Ericsson, Lucent)

- One TFI can be used by multiple MSs on one uplink physical subchannel (Nokia)

Dedicated physical subchannel:

- No TBF/TFI is associated with a data flow on a PDTCH logical channel (Nokia)

- TBF/TFI is associated with a data flow on a PDTCH logical channel (Ericsson, Lucent)

(This issue relates to the unresolved RRC issue and could not be resolved separately.)

# Discussion and adoption of an R4 working assumption on RLC multiplexing

GAHW-000054 (Nokia)

It was agreed that RLC multiplexing will not be supported for R4.