Source: AT&T, Ericsson, Lucent,  Nokia, Nortel Networks

Working assumption on OS2 concept

# Introduction

This document contains some pieces of solutions for an OS2 concept that could be agreed on between the companies above.

## During speech transmission

- Speech and FACCH are diagonally interleaved.

- In this transmitter state, only speech and FACCH are possible. Only 2 stealing bit combinations are necessary in order to distinguish between speech and FACCH.

- The all zeros is used for speech.

- The actual content of the data using FACCH channel coding is FFS.

## End of speech

- The end of speech is indicated by the SID_FIRST identification marker.

## During silent periods indicated by the SID_FIRST identification marker

- During silent periods, SID_UPDATE are sent on a regular basis following existing AMR procedures.

- Best effort data packets may also be sent (block interleaved over four bursts).

- SID_UPDATE should be transmitted using existing AMR procedures.

- Modulation and stealing bits indicates the coding scheme of the best effort data packets.

- The all zeros stealing bit combination shall be reserved to allow the receiver to detect the start of speech.

## At start of speech

- The start of speech is indicated by the all zeros stealing bits combination. ONSET shall be transmitted according to present AMR procedures.

# Summary

The agreed behavior of the transmitter when multiplexing speech and data has been shown above.

The following items are identified as FFS:

- What happens if a FACCH is sent at the beginning of a talk-spurt?

- What are the important error cases/recovery scenarios?

- How is FACCH (e.g. handover commands) sent during silent periods?

- Exact definition and interleaving of the stealing bits.

- Receiver behavior (i.e., decoding rules/guidelines to ensure quick recovery on errors).

- Any different solutions for 8-PSK FR, 8PSK HR, GMSK HR?