Source: Lucent Technologies

Proposed Changes to the GERAN Stage-2 Description: Physical Layer

Introduction

This contribution proposes following changes to section 6.8 (Physical Layer) of the GERAN stage-2 description.

- Removal of the reference of multiplexing of PDTCH and PACCH only within the silent periods of TCH over DPSCH (only to sections 6.8.5.1 and 6.8.5.2, not to subsequent subsections). This reference is not consistant with the GERAN R00 multiplexing requirements.

Proposed Stage-2 Changes

### Mapping of logical channels onto physical subchannels

#### DPSCH full rate

Excluding CBCH, broadcast channels and common control type channels, the following channel combinations are possible for a DPSCH full rate:

- TCH/F + FACCH/F + SACCH/TF

- TCH/F + FACCH/F + SACCH/TF  + PDTCH/F + PACCH/F

- PDTCH/F + PACCH/F + SACCH/TF

#### DPSCH half rate

The following channel combinations are possible for a DPSCH half rate:

- TCH/H + FACCH/H + SACCH/TH

- TCH/H + FACCH/H + SACCH/TH  + PDTCH/H + PACCH/H

- PDTCH/H + PACCH/H + SACCH/TH