3GPP TSG GERAN Adhoc #2	Tdoc GAHW-000109
October 9-13, 2000	Agenda item 6.1.3
Munich, Germany

Clarification of physical layer multiplexing in GERAN stage 2 specification

Source:	AT&T

# Introduction

This is a proposal to clarify the description of the physical layer multiplexing the GERAN stage 2 specification [43.051, Tdoc GAHW-000045] to cover the cases under discussion and partly found in Tables 2-5 of 43.051. This contribution is based on the paper and GAHW-000078 resulting discussion.

# Proposed changes to 43.051

## Multiplexing Principles

### Multiplexing of different types of radio access bearers for one MS

Different types of Radio Access Bearer Services can be multiplexed for one MS using functionality of MAC and/or physical layers.

RABs carried on PDTCH logical channels can be multiplexed for one MS on one or more shared and/or dedicated physical subchannels.

A Conversational or Streaming RAB carried on a TCH logical channel can be multiplexed with one or more Interactive and/or Background RABs for one MS on one dedicated physical subchannel. Cases supported by GERAN are:

- Conversational RAB + Background RABs and/or Interactive RABs with low traffic handling priority (Editor’s note: formerly referred to as Operational Scenario 2)

- Optimised voice Radio Bearer is used to realise the Conversational RAB

- Generic Conversational Radio Bearer is used to realise the Conversational RAB

- Conversational RAB + Interactive RABs with high traffic handling priority

- Optimised voice Radio Bearer is used to realise the Conversational RAB

- Generic Conversational Radio Bearer is used to realise the Conversational RAB

3	Conversational RAB + Interactive RABs with high traffic handling priority + Background RABs and/or Interactive RABs with low traffic handling priority

- a)	Optimised voice Radio Bearer is used to realise the Conversational RAB

- b)	Generic Conversational Radio Bearer is used to realise the Conversational RAB

4	Streaming RAB + Background RABs and/or Interactive RAB with low traffic handling priority

- Streaming RAB + Interactive RABs with high traffic handling priority

- Streaming RAB + Interactive RABs with high traffic handling priority + Background RABs and/or Interactive RAB with low traffic handling priority

(In the list above, the term ‘Background RAB or Interactive RAB with low traffic handling priority’ is used for the case where the conversational/streaming flow always has precedence over this data flow. The term ‘Interactive RAB with high traffic handling priority’ is used for the case where the data flow may have precedence over the conversational/streaming flow.)

#### Dedicated Mode

In dedicated mode, the MS is allocated a dedicated physical subchannel for exclusive use of the bearers it supports.

- Priority handling between data flows of one mobile station. Priorities are e.g. given by attributes of Radio Bearer services.

- Multiplexing/demultiplexing of higher layer PDUs delivered to/from the physical layer on dedicated physical subchannels. This function can be utilised when several upper layer services (e.g. RLC instances) can be mapped efficiently on the same physical subchannel.

#### Dedicated MAC mode

The current working assumption is to use the RLC/MAC protocol of GSM 04.60 as a basis. The channel coding for this protocol mode combination is for further study. Potential channel coding schemes to be used are GPRS/EGPRS and CSD/ECSD coding schemes.

Annex A (informative):
Radio Access Bearer Realization

This annex describes how the different protocols of the GERAN User Plane protocol stack are configured to provide the desired radio access bearer classes (conversational, streaming, interactive and background). Only the traffic over Iu-ps interface is considered.

# A.1	Conversational Radio Access Bearer

In the table below, case A represents optimized conversational RAB further described in section A.1.2. Case B represents the generic conversational RAB.

Table 2: Conversational RAB

| PDCP | RLC | MAC | Physical Layer | TCHmultiplexing case (section 5.1.1) |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Physical SubChannel | Traffic Channel | Dedicated Control Channel |  |  |
|  |  |  |  | Type | Interleav. | Mod. | Coding |  |  |  |
| Non Transparent Header Removal | Transp. | Dedicated | DPSCH/F | TCH/F | 8 diag | GMSK | UEP | As TCH/AFS | FACCH/F (2) SACCH/TF | 1a, 2a, 3a | A |
|  |  |  |  |  |  | 8PSK (1) | UEP | ffs | FACCH/F (2) SACCH/TF | 1a, 2a, 3a |  |
|  |  |  | DPSCH/H | TCH/H | 4 diag | GMSK | UEP | As TCH/AHS | FACCH/H (2) SACCH/TH | 1a, 2a, 3a |  |
|  |  |  |  |  |  | 8PSK | UEP | As TCH/AHS | FACCH/H (2) SACCH/TH | 1a, 2a, 3a |  |
|  |  |  | DPSCH/Q | TCH/Q | 2 diag | 8PSK | UEP | TCH/QS | FACCH/Q SACCH/TQ | 2a |  |
| Non Transparent Header Compression or No Adaptation Transparent | Unack | Dedicated | DPSCH/F | PDTCH/F | 4 rect | GMSK | EEP | SACCH/TF PACCH/F | NA | B |
|  |  |  |  |  |  | 8PSK | EEP | SACCH/TF PACCH/F | NA– |  |
|  |  |  |  | TCH/F (2) | ffs | GMSK | EEP | FACCH/F (2) SACCH/TF | 1b, 2b, 3b |  |
|  |  |  |  |  |  | 8PSK | EEP | FACCH/F (2) SACCH/TF | 1b, 2b, 3b |  |
|  |  |  | DPSCH/H | PDTCH/H | 4 rect | GMSK | EEP | SACCH/TH PACCH/H | NA– |  |
|  |  |  |  |  |  | 8PSK | EEP | SACCH/TH PACCH/H | NA |  |
|  |  |  |  | TCH/H | ffs | GMSK | EEP | FACCH/H SACCH/TH | 1b, 2b, 3b |  |
| UEP Unequal Error Protection - EEP Equal Error Protection This row is intended for the realization of wide-band speech codec and is ffs Whether FACCH and PACCH are both needed is ffs |

# A.2	Streaming, Interactive, Background Radio Access Bearers

## A.2.1	Streaming

Table 3: Streaming RAB

| PDCP | RLC | MAC | Physical Layer | TCH multiplexing case (section 5.1.1) |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Physical SubChannel | Traffic Channel | Dedicated Control Channel |  |  |
|  |  |  |  | Type | Interleav. | Mod. | Coding |  |  |  |
| Non Transparent Header Compression or No Adaptation Transparent | Unack | Dedicated | DPSCH/F | PDTCH/F | 4 rect | GMSK | EEP | SACCH/TF PACCH/F | NA | A |
|  |  |  |  |  |  | 8PSK | EEP | SACCH/TF PACCH/F | NA |  |
|  |  |  |  | TCH/F | ffs | GMSK | EEP | FACCH/F (1) SACCH/TF | 4-6 |  |
|  |  |  |  |  |  | 8PSK | EEP | FACCH/F (1) SACCH/TF | 4-6 |  |
|  |  |  | DPSCH/H | PDTCH/H | 4 rect | GMSK | EEP | SACCH/TH PACCH/H | NA |  |
|  |  |  |  |  |  | 8PSK | EEP | SACCH/TH PACCH/H | NA |  |
|  |  |  |  | TCH/H | ffs | GMSK | EEP | FACCH/H (1) SACCH/TH | 4-6 |  |
| Non Transparent Header Compression or No Adaptation Transparent | Ack | Dedicated | DPSCH/F | PDTCH/F | 4 rect | GMSK | EEP | SACCH/TF PACCH/F | NA | B |
|  |  |  |  |  |  | 8PSK | EEP | SACCH/TF PACCH/F | NA |  |
|  |  |  | DPSCH/H | PDTCH/H | 4 rect | GMSK | EEP | SACCH/TH PACCH/H | NA |  |
|  |  |  |  |  |  | 8PSK | EEP | SACCH/TH PACCH/H | NA |  |
| Non Transparent Header Compression or No Adaptation Transparent | Unack | Shared | SPSCH/F | PDTCH/F | 4 rect | GMSK | EEP | PACCH/F PTCCH/F | NA | C |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/F PTCCH/F | NA |  |
|  |  |  | SPSCH/H | PDTCH/H | 4 rect | GMSK | EEP | PACCH/H PTCCH/H | NA |  |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/H PTCCH/H | NA |  |
| Non Transparent Header Compression or No Adaptation Transparent | Ack | Shared | SPSCH/F | PDTCH/F | 4 rect | GMSK | EEP | PACCH/F PTCCH/F | NA | D |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/F PTCCH/F | NA |  |
|  |  |  | SPSCH/H | PDTCH/H | 4 rect | GMSK | EEP | PACCH/H PTCCH/H | NA |  |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/H PTCCH/H | NA |  |
| UEP Unequal Error Protection - EEP Equal Error Protection - OS Operational Scenario Supported (1) Whether FACCH and PACCH are both needed when multiplexing PDTCH and TCH is FFS |

## A.2.2	Interactive

Table 4: Interactive RAB

| PDCP | RLC | MAC | Physical Layer | TCH multiplexing case (section 5.1.1) |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Physical SubChannel | Traffic Channel | Dedicated Control Channel |  |  |
|  |  |  |  | Type | Interleav. | Mod. | Coding |  |  |  |
| Non Transparent Header Compression No Adaptation Transparent | Ack | Dedicated | DPSCH/F | PDTCH/F | 4 rect. | GMSK | EEP | PACCH/F SACCH/TF | 1-6 | A |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/F SACCH/TF | 1-6 |  |
|  |  |  | DPSCH/H | PDTCH/H | 4 rect. | GMSK | EEP | PACCH/FH SACCH/TH | 1-6 |  |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/H SACCH/TH | 1-6 |  |
| Non Transparent Header Compression No Adaptation Transparent | Ack | Shared | SPSCH/F | PDTCH/F | 4 rect. | GMSK | EEP | PACCH/F PTCCH/F | NA | B |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/F PTCCH/F | NA |  |
|  |  |  | SPSCH/H | PDTCH/H | 4 rect. | GMSK | EEP | PACCH/H PTCCH/H | NA |  |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/H PTCCH/H | NA |  |
| UEP Unequal Error Protection - EEP Equal Error Protection |

## A.2.3	Background

Table 5: Background RAB

| PDCP | RLC | MAC | Physical Layer | TCH multiplexing case (section 5.1.1) |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Physical SubChannel | Traffic Channel | Dedicated Control Channel |  |  |
|  |  |  |  | Type | Interleav. | Mod. | Coding |  |  |  |
| Non Transparent Header Compression No Adaptation Transparent | Ack | Dedicated | DPSCH/F | PDTCH/F | 4 rect. | GMSK | EEP | PACCH/F SACCH/TF | 1, 3, 4, 6 | A |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/F SACCH/TF | 1, 3, 4, 6 |  |
|  |  |  | DPSCH/H | PDTCH/H | 4 rect. | GMSK | EEP | PACCH/FH SACCH/TH | 1, 3, 4, 6 |  |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/H SACCH/TH | 1, 3, 4, 6 |  |
| Non Transparent Header Compression No Adaptation Transparent | Ack | Shared | SPSCH/F | PDTCH/F | 4 rect. | GMSK | EEP | PACCH/F PTCCH/F | NA | B |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/F PTCCH/F | NA |  |
|  |  |  | SPSCH/H | PDTCH/H | 4 rect. | GMSK | EEP | PACCH/H PTCCH/H | NA |  |
|  |  |  |  |  |  | 8PSK | EEP | PACCH/H PTCCH/H | NA |  |
| UEP Unequal Error Protection - EEP Equal Error Protection |