Title:	DRAFT LS on GERAN architectural working assumptions

Source:	GERAN ad hoc #2( TSG GERAN

To:	3GPP TSG SA WG 2	Contact:	José Luis Carrizo

Cc:	3GPP TSG RAN WG 3	Tel:	+44 1635 676093

Date:	13th October 2000	E-mail:	jose-luis.carrizo@vodafone.co.uk

TSG GERAN thanks TSG SA WG2 for their attention and support with GERAN architectural issues. TSG GERAN would also like to inform TSG SA WG2 of the latest decisions regarding the connectivity of the GERAN to the Core Network.

TSG GERAN have agreed:

- To adopt the Iu-CS interface as the means to connect the GERAN BSC to the 3G MSC from Release 4 onwards. TSG GERAN believe that this decision increases the synergies between GERAN and UTRAN, making it easier for manufacturers to develop new services over a single interface. Note that TSG GERAN make no assumption about whether 2G and 3G MSCs are combined or separate physical nodes.

- To encourage the enhancement of the Iu-CS interface to support the services that the A interface currently supports and for which operators express interest. This is necessary so that there is no loss of service capabilities in the transition form Release 99 to Release 4. TSG GERAN would appreciate TSG RAN WG3’s views on this.

- To work on a new option for the transport network layer for the A interface in R4 and beyond, looking for harmonisation with the transport network layer on the Iu-CS interface. For instance, use of ATM (as in Release 99 of the Iu interface), use of IP (as, possibly, in Release 4 of the Iu interface) or further enhancements that may be defined in the future. TSG GERAN believe that this decision helps operators with the maintenance of both the A and the Iu-CS interfaces towards the Core Network.

- That the mobile station shall operate using only the following modes:

- A / Gb mode

- for pre-Release 4 terminals

- for Release 4 terminals when connected to a GERAN with no Iu interface towards the Core Network

- Iu mode (i.e. Iu-CS and Iu-PS)

- for Release 4 terminals when connected to a GERAN with Iu interfaces towards the Core Network

Both modes must be supported by the standard and no other modes (e.g. A / Iu-PS or Iu-CS / Gb) shall be allowed. Since both modes are already used in Release 99 (the first one for the GSM/GPRS mobile station and the second for the UMTS user equipments), TSG GERAN believe that this decision simplifies the development and testing of R4 GERAN terminals, resulting in a reduced cost and earlier availability.

TSG GERAN would kindly ask TSG SA2 to update the TSs and TRs under its responsibility to reflect this decision.

# Footnotes

Alcatel, AT&T, BellSouth Cellular, Comsys Ltd, Ericsson, Flayers AG, InterDigital Cummunications Corporation, Lucent Technologies, Motorola, Nokia, Nortel Networks, Northstream, SBC, Sharp Labs of Europe, Siemens, Telia AB, Vodafone.

Terminology recently approved in 3GPP.