## Slide 1
Latest Status of the Clean Slate
Track of Activities
Chris Pudney
Vodafone Group plc (Rapporteur: FS_IoT_LC)
GP-150666
Rev of GP-150550 which is Rev of GP-150400

## Slide 2: Outline
Introduction to Cellular IoT (FS_IoT_LC)
  Objectives
  Timeline
Clean slate solutions
  Narrow Band M2M (NB M2M)
  Narrow Band OFDMA (NB OFDMA)
  Cooperative Ultra Narrow Band (C-UNB)
  Combined Narrow Band and Chirp Spread Spectrum
  Converged (NB M2M and NB OFDMA) solution
Potential Work Item phase
  Planned meeting schedule

## Slide 3: Introduction to FS_IoT_LC
In GERAN#62 (May 2014), a study item on “Cellular System Support for Ultra Low Complexity and Low Throughput Internet of Things” was approved.
Objectives of the Study:
  The main objective of the study is to evaluate how to support low throughput and low complexity Machine Type Communications.
  Different solutions can be investigated, e.g. a non-legacy based design, and/or a backward compatible evolution of GSM/EDGE.

## Slide 4: Objectives of FS_IoT_LC
  Provide a data rate of at least 160 bps1 (on both the uplink and downlink) at the (equivalent of) the SAP to the SNDCP layer with the aim of achieving an extended coverage of 20 dB compared to legacy GPRS (Non EGPRS).
  Scale to support a massive number of MTC Mobile Stations
  Reduce power consumption of MTC Mobile Stations compared with legacy GPRS (non EGPRS) so that they can have up to ten years battery life with battery capacity of 5 Watt-hours
  Maximise the reduction in complexity of the Mobile Termination compared to that of a legacy GPRS (non EGPRS) MT
1 The minimum SNDCP SDU of 80 octets, with 4 sec latency (excluding synchronization time) for ‘alarms’ giving a requirement of at least 160 bps at SNDCP SAP.

## Slide 5: Objectives of FS_IoT_LC (contd…)
  Avoid negative impacts to legacy GSM/WCDMA/LTE system(s) deployed in the same frequency band and adhere to the regulatory requirements applying to the spectrum bands in which the system operates.
  Minimise impacts to the GPRS/EDGE base station hardware.
  Identify Core Network Architecture, security framework and Radio Access Network-Core Network interface (e.g. S1 or Gb), and associated protocol stacks, suitable for the M2M market in the 2017 and onwards timeframe.
  For both options:
    There is no requirement for inter-RAT mobility.
    Intra-RAT mobility is assumed to be based on cell reselection.

## Slide 6: Timeline of Study Item
GERAN#62 (May 2014) – SID approved
GERAN#63 (Aug 2014 ) – v0.2.0
GERAN#64 (Nov 2014 ) – v0.3.0
GERAN#65 (March 2015) – v1.0.0
GERAN#66 (May 2015) – v1.3.0
Future meeting calendar
GERAN 1/2 CIoT ad hoc#3, 29 June – 2 July 2015
GERAN#67 (August 2015) – Conclude the study (exp)

## Slide 7: Clean Slate Solutions
As of GERAN#66 (May 2015), the candidate clean slate solutions are:
  Narrow Band M2M (NB M2M)
  Narrow Band OFDMA (NB-OFDMA)
  Cooperative Ultra Narrow Band (C-UNB)
  Combined Narrowband and Chirp Spread Spectrum
  Converged (NB M2M and NB OFDMA) solution
Proposals only – content not yet available in TR

## Slide 8: 1: Narrow Band M2M (NB M2M)
Downlink physical layer design
  FDMA, 12 sub-channels (2 broadcast + 10 data) over 200 kHz, 15 kHz channel spacing, 10 kHz guard at each edge.
  Variable-length burst (one or more 10-ms slot), Rate ½ and ¾ convolutional coding, π/2-BPSK, π/4-QPSK and 16-QAM
Uplink physical layer design
  FDMA, 36 sub-channels (random access + data) over 200 kHz, 5 kHz channel spacing, 10 kHz guard at each edge.
  Variable-length burst (one or more 10-ms slot), 1/3 and 2/3 Turbo coding, GMSK, π/2-BPSK, π/4-QPSK and π/8-8PSK, single carrier, sub-channel bonding

## Slide 9: 1: Narrow Band M2M (NB M2M)
Concept evaluations captured in the TR
  Coverage achieves 20 dB extension objective for synchronization, random access, data and control channels.
  Capacity achieves 50k devices per cell sector objective with the agreed traffic model, using a single 200 kHz channel.
  Battery life achieves 10 years from 5 Wh battery capacity for most evaluated scenarios (exceptions are for higher reporting frequencies with high coverage extension).
  Latency achieves 10 second objective for exception reports for all coverage extensions.
  Coexistence with GSM/UMTS/LTE is partially captured in the TR.

## Slide 10: 2. Narrow Band OFDMA (NB-OFDMA)
NB-OFDMA Physical layer design
  Narrow Band OFDMA (NB-OFDMA) on the downlink
  Single Carrier FDMA (SC-FDMA) on the uplink
  72 sub-channels over 200 kHz, 2.5 kHz channel spacing, 10 kHz guard at each edge.
  Concept evaluations captured in the TR
  Coverage achieves 20 dB extension objective for synchronization, random access, data and control channels
  Capacity achieves 50k devices per cell sector objective with the agreed traffic model, using a single 200 kHz channel.
  Battery life achieves 10 years from 5 Wh battery capacity for most evaluated scenarios (exceptions are for higher reporting frequencies with high coverage extension).
  Latency achieves 10 second objective for exception reports for all coverage extensions.

## Slide 11: 2. Narrow Band OFDMA (NB-OFDMA)
NB-OFDMA MAC
  Broadcast information defined
  Procedure for paging and data transfer defined
  Key MAC control messages defined

## Slide 12: 3. Cooperative Ultra Narrow Band (C-UNB) (Proposals only, not yet in TR)
C-UNB Physical layer design
  Mono frequency block network
  Ultra narrow band modulation
  No time or frequency synchronisation
C-UNB link layer aspect
  Segmentation/reassembly specific to C-UNB
C-UNB architecture
  Dedicated server added in the core network
  Can connect to Gb interface

## Slide 13: 4. Combined Narrow Band and Chirp Spread Spectrum (Proposals only, not yet in TR)
No contributions presented in GERAN#66, May 2015

## Slide 14: 5. Converged (NB M2M and NB OFDMA) solution (Proposals only, not yet in TR)
Only an initial overview presented in GERAN#66
Indicative parameters for converged solution
 | Downlink | Uplink
Multiple access | OFDMA | FDMA
Sub-channel symbol rate | 3.75 kHz | 3.75 kHz
Sub-channel spacing | 3.75 kHz | 5 kHz
Number of sub-channels | 48 | 36
Maximum transmit power | 43 dBm | 23 dBm
Modulation mandatory | BPSK, QPSK | GMSK
Modulation optional | 16QAM | BPSK, QPSK, 8PSK
Pulse shaping | Wideband spectral shaping | Symbol rate shaping GMSK: BT=0.3 PSK: root-raised cosine
FFT size | 64 | -
Cyclic prefix | 6 samples | -
Sub-channel bonding | - | x2, x4, x8
FEC | Tail biting convolutional | Turbo

## Slide 15: Candidate independent issues
No decision yet on Gb based architecture vs S1 based architecture - but current analysis favours Gb based
Preferred coding for RRC messages: CSN.1

## Slide 16: Potential Work Item phase
Specification completion aimed for end Feb 2016
Proposed Meeting Schedule
  RAN 1/2: 5 – 9 October 2015, Malmo, Sweden
  RAN 3: 5 – 9 October 2015, Sophia Antipolis, France
  RAN 4: 12 – 16 October 2015, Sophia Antipolis, France
  RAN 1/2/3/4: 16 – 20 November 2015, Anaheim, USA
  RAN 1/2 ad hoc: 14 – 18 December 2015, TBD
  RAN 1/2/4(ad hoc): 11 – 15 January 2016 TBD
  RAN 1/2/3/4: 15 – 19 February 2016, Malta
Additional meetings

## Slide 17: Meeting organization suggestion
Parallel streams in RAN 1 and RAN 2
Some parallel sessions in RAN 4
RAN 3 work (if any) in main session (common with LTE-EC)
Organise GERAN WG1 / WG2 and RAN WG1/WG2 (CIoT ad hoc) sessions in time-division/parallel manner. E.g:
  - GERAN 1 “evolved GSM” morning - RAN 1 “clean slate” afternoon - GERAN 2 “evolved GSM” afternoon - RAN 2 “clean slate” morning

## Slide 18: Thank You