3GPP TSG-GERAN WG4 Meeting #2 	Tdoc-G4000228

Sophia Antipolis, France, 20-24 November 2000

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
|  | 51.010 | CR | CR-Num | rev | - | ( Current version: | 4.1.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE | X | Radio Access Network |  | Core Network |  |
| Title: ( | GPRS RLC Test Cases section 43 |
| Source: ( | Motorola, Setcom |
| Work item code: ( | GPRS |  | Date: ( | 20 November 2000 |
| Category: ( | F |  | Release: ( | REL-4 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | Minor corrections |
| Summary of change: ( | 43.1.1.3 - Clarification of comments related to retransmission of unacknowledged and acknowledged blocks in step 15. 43.1.1.4 - Unnecessary steps in expected sequence deleted. There is no reason to wait BS_CV_MAX block periods. Also, reference in step 14 (old numbering) was referring to the wrong step numbers. 43.1.2.1 – Steps 2 and 3 are repeated (added new step 4 to do this), until BSN = N. For each received Packet Downlink Ack/Nack, SS verifies that SSN = [BSN + 1] modulo 128. 43.1.2.4 - Correction of comments for SS message comments. 43.2.1 – Missing message step assigning USF. |
| Consequences if ( not approved: | Incorrect test implementation |
| Clauses affected: ( | 43.1.1.3, 43.1.1.4, 43.1.2.1, 43.1.2.4, 43.2.1 |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://www.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2000-09 contains the specifications resulting from the September 2000 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

# 43	RLC Test Cases

#### 43.1.1.3	Acknowledged mode / Uplink TBF / Acknowledge state variable V(A)

43.1.1.3.1	Conformance requirements

1.	The Acknowledge state variable V(A) contains the BSN value of the oldest RLC data block that has not been  positively acknowledged by its peer. V(A) can take on the values 0 through 127.

2.	V(A) shall be set to the value 0 at the beginning of each TBF in which the RLC endpoint is the transmitter.

3.	The value of V(A) shall be updated from the values received from its peer in the received block bitmap (RBB) of the Packet Ack/Nack message (see subclause 9.1.8).

References

GSM 04.60, sections 9.1.2 and 9.1.8.

43.1.2.3.2	Test purpose

1.	To verify that the mobile station correctly decodes the RBB and updates the values of V(A).

43.1.2.3.3	Method of test

Initial Conditions

System Simulator:

1 cell, default setting, PBCCH not present

Mobile Station:

The MS is GPRS updated with a P-TMSI allocated, SPLIT PG CYCLE negotiated and the test PDP Context2 activated.

Related PICS/PIXIT Statement(s)

The way to initiate an acknowledged uplink transfer.

Test Procedure

1.	The mobile station transmits k (window size) blocks without acknowledgment from SS. SS then acknowledges the first n blocks. The mobile station then shall transmit n more data blocks.

2.	The test is performed for the values of N = 10,15 and 20.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 |  | { Uplink dynamic allocation two phase access} | n = 3000 octets USF_GRANULARITY = 1 block CHANNEL_CODING_COMMAND: cs1 |
| 2 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH, containing USF assigned to the MS. |
| 3 | MS -> SS | UPLINK RLC DATA BLOCK | Received on the assigned PDTCH |
| 4 |  |  | Repeat steps 2 and 3 until the stall indication bit is set in the data block received in step 3. SS doesn’t acknowledge any of the data blocks with BSN from 0 to 63 |
| 5 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH assigned, USF assigned to the MS. |
| 6 | MS -> SS | UPLINK RLC DATA BLOCK | Received on the assigned PDTCH |
| 7 |  |  | Repeat steps 5 and 6 until unacknowledged data blocks (BSN = 0 to 30) are retransmitted with SI field set to 1 |
| 8 |  |  | Wait BS_CV_MAX periods without granting USF. |
| 9 | SS -> MS | PACKET UPLINK ACK/NACK | SS acknowledges first N (=10) RLC data blocks, RBB set to 1 and negatively acknowledges the rest with RBB set to 0 USF not assigned to the MS |
| 10 |  |  | Wait for 6 blocks with no USF |
| 11 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH assigned, USF assigned to the MS. |
| 12 | MS -> SS | UPLINK RLC DATA BLOCK | Received on the assigned PDTCH BSN = N & SI = 0 |
| 13 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH assigned, USF assigned to the MS. |
| 14 | MS -> SS | UPLINK RLC DATA BLOCK | Received on the assigned PDTCH BSN = N + 1 & SI = 0 |
| 15 | SS |  | Repeat steps 13 and 14 until all negatively acknowledged data blocks are retransmitted followed by new data blocks SS verifies that the negatively acknowledged data blocks are retransmitted before new data blocks are sent, by verifying that RLC data blocks with BSN from N to 63 are received first, then RLC data blocks with BSN from 64 to 63+N are received. |
| 16 |  | { Completion of uplink RLC data block transfer} |  |
| 17 | - | - | The procedure is repeated for different values of N |

#### 43.1.1.4	Acknowledged mode / Uplink TBF / Negatively acknowledged RLC data blocks

43.1.1.4.1	Conformance requirements

1.	The transmitter shall transmit the oldest RLC data block whose corresponding element in V(B) indexed relative to V(A) has the value NACKED.

2.	If [ V(S) < V(A) + k ] modulo 128 and no RLC data blocks have a corresponding element in V(B) with the value NACKED, the RLC data block with BSN = V(S) shall be transmitted.

3.	As each RLC data block is transmitted the corresponding element in V(B) shall be set to the value PENDING_ACK.

References

GSM 04.60, section 9.1.3.

43.1.1.4.2	Test purpose

1.	To verify that the mobile station retransmits Nacked data blocks before transmission of new information.

2.	To verify that the mobile station retransmits Nacked blocks in order of age, older first.

3.	To verify that the mobile station only retransmit  Nacked blocks once per negative acknowledgment.

43.1.1.4.3	Method of test

Initial Conditions

System Simulator:

1 cell, default setting, , PBCCH not present, BS_CV_MAX = 0

Mobile Station:

The MS is GPRS updated with a P-TMSI allocated, SPLIT PG CYCLE negotiated and the test PDP Context2 activated.

Related PICS/PIXIT Statement(s)

The way to initiate an acknowledged uplink transfer.

Test Procedure

The MS is made to transmit RLC data blocks. The SS randomly negatively acknowledges RLC data blocks. The MS retransmits the negatively acknowledged RLC data blocks, oldest first before transmitting new RLC data blocks.

The SS does not send further acknowledgements. The MS does not retransmit the previously negatively acknowledged RLC data blocks.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 |  | { Uplink dynamic allocation two phase access} | n = 1500 octets USF_GRANULARITY = 1 block CHANNEL_CODING_COMMAND: cs1 |
| 2 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH assigned, USF assigned to the MS. |
| 3 | MS -> SS | UPLINK RLC DATA BLOCK | Received on the assigned PDTCH |
| 4 |  |  | Repeat steps 2 and 3 until received data block BSN = 30 |
| 5 | SS -> MS | PACKET UPLINK ACK/NACK | SS acknowledges RLC data blocks with BSN 10 to 30, RBB set to 1 and negatively acknowledges the rest with RBB set to 0 USF not assigned to the MS |
| 6 |  |  | Wait for 6 blocks with no USF |
| 7 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH assigned, USF assigned to the MS. |
| 8 | MS -> SS | UPLINK RLC DATA BLOCK | Received on the assigned PDTCH BSN = 0..9 |
| 9 | SS |  | Repeat steps 7 & 8 ten times SS verifies that the Nacked data blocks are received before new data block once per negative acknowledgment. After these data blocks new data block BSN=31 should be received |
| 10 | SS -> MS | PACKET UPLINK ACK/NACK | SS acknowledges retransmitted (BSN 0..9) RLC data blocks, RBB set to 1 |
| 11 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH, containing USF assigned to the MS. |
| 12 | MS -> SS | UPLINK RLC DATA BLOCK | Received on the assigned PDTCH |
| 13 | SS |  | Repeat steps 11 and 12 until the stall indication bit is set in the data block received in step 12. SS verifies that acknowledged blocks are not retransmitted |
| 14 | SS -> MS | PACKET UPLINK ACK/NACK | SS negatively acknowledges RLC data blocks with BSN 55 to 60, RBB set to 0 and acknowledges the rest with RBB set to 1 USF not assigned to the MS |
| 15 |  |  | Wait for 6 blocks with no USF. |
| 16 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH assigned, USF assigned to the MS. |
| 17 | MS -> SS | UPLINK RLC DATA BLOCK | Received on the assigned PDTCH BSN = 55..60 |
| 18 | SS |  | Repeat steps 16 & 17 until all Nacked blocks are received SS verifies that the Nacked data blocks are received before new data blocks once per negative acknowledgment. |
| 19 |  | { Completion of uplink RLC data block transfer} |  |

### Acknowledged mode / Downlink TBF

#### 43.1.2.1	Acknowledged mode / Downlink TBF / Receive state variable V(R)

43.1.2.1.1	Conformance requirements

1.	In RLC acknowledged mode, each RLC endpoint receiver shall have an associated receive state variable V(R). The receive state variable denotes the BSN of the next in-sequence RLC data block expected to be received.

2.	The mobile station shall set V(R) to the value 0 at the beginning of each TBF in which the RLC endpoint is the receiver.

References

GSM 04.60, section 9.1.5.

43.1.3.1.2	Test purpose

1.	To verify correct initialisation of the receive state variable, V(R).

2.	To verify the receive state variable, V(R) is set to the next in sequence RLC data block expected to be received.

43.1.3.1.3	Method of test

Initial Conditions

System Simulator:

1 cell, default setting, PBCCH not present

Mobile Station:

The MS is GPRS updated with a P-TMSI allocated, SPLIT PG CYCLE negotiated and the test PDP Context2 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service.

Test Procedure

SS establishes a downlink TBF and sends RLC data blocks with BSN values between 0 to N in sequence. The MS is polled in each RLC data block by setting the S/P bit. SS verifies that the SSN in the Packet Downlink Ack/Nack messages sent by the MS are set to [BSN+1] modulo 128. SS then sends  RLC data block with random BSN N1 that holds a value between [N+1] modulo 128 and [N+64] modulo 128. The MS is polled in the last RLC data block by setting the S/P bit. SS verifies that the SSN in the Packet Downlink Ack/Nack message sent by the MS is set to [N1+1] modulo 128.

The test is performed for the values of N = 1,10,63,64,126,127.

Maximum Duration of Test

5 min.

Expected Sequence

| 1 |  | {Downlink TBF establishment} | Macro parameters: Acknowledged mode |
| --- | --- | --- | --- |
| 2 | SS -> MS | DOWNLINK RLC DATA BLOCK | MS is polled S/P bit ‘1’ RRBP 00 |
| 3 | MS -> SS | Packet Downlink Ack/ Nack | SS verifies that SSN = [BSN + 1] modulo 128 |
| 4 |  |  | Repeat steps 2 and 3 until BSN = N |
| 5 | SS -> MS | DOWNLINK RLC DATA BLOCK | BSN = N1 a random number between [N+1] mod 128 and [N+64] modulo 128 MS is polled S/P bit ‘1’ RRBP 00 |
| 6 | MS -> SS | Packet Downlink Ack/ Nack | SS verifies that SSN = [N1+1] modulo 128. |

#### 43.1.2.4	Acknowledged mode / Downlink TBF / Re-assembly / Length Indicator

43.1.2.4.1	Conformance requirements

1.	The Extension (E) bit is used to indicate the presence of an optional extension octet in the RLC data block header. The More (M) bit is used to indicate the presence of an LLC frame following the current LLC frame. The M bit, the E bit, and the Length Indicator, are used to delimit LLC frames within a TBF.

2.	The Length Indicator (LI) field is six bits in length and shall be encoded as a binary number. The value 0 shall indicate that no LLC frame boundary does exist, that the M bit shall be ignored and that the E bit shall be interpreted as having the value 1.

3	A singular case occurs when the end of the LLC PDU would fit within the RLC data block but the addition of the Length Indicator octet (to indicate the LLC PDU boundary) causes the LLC PDU to extend into the next RLC data block. In this case, this additional LI field shall take the value 0 whatever is the length of the last but one LLC PDU segment.

References

GSM 04.60, section 9.1.11, Annexure B 2.

43.1.2.4.2	Test purpose

To verify the correct decoding of RLC data block length indication, more(M) and extension(E) bit fields during re-assembly of LLC frames into RLC data blocks.

43.1.3.4.3	Method of test

Initial Conditions

System Simulator:

1 cell, default setting.

Mobile Station:

The MS is GPRS updated with a P-TMSI allocated, SPLIT PG CYCLE negotiated and PDPContext7 activated.

Related PICS/PIXIT Statement(s)

None

Test Procedure

SS establishes a downlink TBF and sends data blocks containing two LLC frames (A bit set) with length indicator encoded. The MS is expected to decode these fields and re-assemble LLC frames correctly.

The size of the first LLC frame  is 15 octets and second is 24 octets .

Maximum Duration of Test

5 min.

Expected Sequence

| 1 |  | {Downlink TBF establishment} | Macro parameters: Acknowledged mode |
| --- | --- | --- | --- |
| 2 | SS -> MS | DOWNLINK RLC DATA BLOCK | 15 octets of first LLC frame and 4 octets of second LLC frame Length Indicator = 15,M =1, E = 1 A bit set (A = 1 ) in both LLC frames |
| 3 |  | { Uplink dynamic allocation two phase access} | USF_GRANULARITY = 1 block |
| 4 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH assigned, USF assigned to the MS. |
| 5 | MS -> SS | UPLINK RLC DATA BLOCK | LLC Supervisory frame (RR) acknowledging first LLC frame |
| 6 |  | { Completion of uplink RLC data block transfer} |  |
| 7 | SS -> MS | DOWNLINK RLC DATA BLOCK | 19 octets from second LLC frame Length indicator = 0, M = 0, E = 1 |
| 8 | SS -> MS | DOWNLINK RLC DATA BLOCK | 1 octet from second LLC frame Length indicator = 1, M = 0, E = 1, FBI=1 |
| 9 |  | { Uplink dynamic allocation two phase access} | USF_GRANULARITY = 1 block |
| 10 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | Sent on the PACCH of the PDCH assigned, USF assigned to the MS. |
| 11 | MS -> SS | UPLINK RLC DATA BLOCK | LLC Supervisory frame (RR) acknowledging second LLC frame |
| 12 |  | { Completion of uplink RLC data block transfer} |  |

## 43.2	Control Blocks

### 43.2.1	Control Blocks Re-assembly

43.2.1.1	Conformance requirements

The network may segment RLC/MAC control messages into one or two RLC/MAC control blocks depending on the length of the RLC/MAC control message.

RLC/MAC control blocks shall be collected at the receiver until all RLC/MAC control blocks comprising a RLC/MAC control message have been received. The receiving side shall determine the length of the RLC/MAC control message contents by interpreting the RLC/MAC control block contents.

References

GSM 04.60, sections 9.1.11a, 9.1.11b and 9.1.2.

43.2.1.2	Test purpose

To verify that the MS re-assembles a RLC control message If it spans across more than one RLC control block.

43.2.1.3	Method of test

Initial Conditions

System Simulator:

1 cell, default setting, PBCCH not present

Mobile Station:

The MS is switched off.

Related PICS/PIXIT Statement(s)

Method of trigger GPRS attach at power on.

Test Procedure

The MS is switched on and triggered to perform a GPRS attach. The SS sends a PACKET UPLINK ASSIGNMENT message that spans more than one RLC control block. The PACKET UPLINK ASSIGNMENT message contains Dynamic Allocation struct (Timeslot allocation with power control parameters included) and frequency parameters with direct encoding 2 struct information fields. The SS verifies that RLC data blocks containing Attach Request message are received from the MS.. Switch off the MS.

Maximum Duration of Test

5 min.

Expected sequence

| 1 | MS |  | The MS is switched on and triggered to perform a GPRS attach. |
| --- | --- | --- | --- |
| 2 | MS -> SS | CHANNEL REQUEST |  |
| 3 | SS -> MS | IMMEDIATE ASSIGNMENT | Indicating two phase access |
| 4 | MS -> SS | PACKET RESOURCE REQUEST |  |
| 5 | SS -> MS | PACKET UPLINK ASSIGNMENT | Frequency Parameter direct encoding 2 information element. Dynamic Allocation struct information element (Timeslot allocation and Power Control parameters included) Payload type = 10, Sent on PACCH. |
| 6 | SS -> MS | PACKET DOWNLINK DUMMY CONTROL BLOCK | USF assigned to the MS |
| 7 | MS -> SS | UPLINK RLC DATA BLOCKS | Attach Request received on PDTCH assigned in step 5 |

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the lastest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.