3GPP TSG-GERAN WG4 #2 	G4-000284

# Sophia-Antipolis, France, 20-24 Nov. 2000

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | 51.010-1 | CR | CR-Num | ( rev | - | ( Current version: | 4.1.0 | ( |
| Proposed change affects: ( | (U)SIM |  | ME/UE | x | Radio Access Network |  | Core Network |  |
| Title: ( | Wrong reference to table 42.2.1.1 |
| Source: ( | Setcom GmbH |
| Work item code: ( | GPRS |  | Date: ( | 9.Nov.2000 |
| Category: ( | D |  | Release: ( | REL-4 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | Wrong reference to table 42.2.1.1/1b in step 2 of some test cases, in which the Specific Message Contents refer to PACKET UPLINK ASSIGNMENT in step2, so that table 42.2.1.2/1b must be used. Access procedure in TC 42.2.2.6.1 step 8 unnecessary. |
| Summary of change: ( | Replace by correct reference. In step 8 of TC 42.2.2.6.1 the SS verifies that the MS sends Random Access. |
| Consequences if ( not approved: | Test will be confusing |
| Clauses affected: ( | 42.2.2.6.1, 42.2.2.6.2, 42.2.2.6.3, 42.2.2.6.4, 42.2.2.6.5, 42.2.2.7.1, 42.2.2.7.2, 42.2.2.7.3, 42.2.2.7.4, , 42.2.2.7.5, 42.2.2.8.1, 42.2.2.8.2, 42.2.2.9.1, 42.2.2.10.1, 42.2.2.10.2, 42.2.2.10.3 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

##### 42.2.2.6.1	Fixed Allocation / Uplink Transfer / MS requests new resources/ T3168/Expiry

42.2.2.6.1.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.6.1.2	Conformance requirements

At sending of the PACKET RESOURCE REQUEST message, the mobile station shall start timer T3168.

On receipt of a PACKET UPLINK ASSIGNMENT or PACKET TIMESLOT RECONFIGURE message the mobile station shall stop timer T3168 and switch to the assigned PDCHs.

On expiry of timer T3168, the mobile station shall retransmit the PACKET RESOURCE REQUEST message unless the PACKET RESOURCE REQUEST message has already been  transmitted four times in which case the mobile station shall perform an abnormal release with random access.

If no PACKET UPLINK ASSIGNMENT or PACKET TIMESLOT RECONFIGURE message is received before the mobile station has completed its currently assigned TBFs the mobile station shall stop timer T3168 and return to packet idle mode (listening to its paging channel).

On receipt of a PACKET ACCESS REJECT message , the mobile station shall stop timer T3168 if running and return to packet idle mode. Before initiating a new packet access procedure the mobile station shall decode the PRACH Control Parameters if they are broadcast.

References

GSM 04.60, subclause 7.1.3.1, 8.1.1.3.2, 8.7.2, 12.24

42.2.2.6.1.3	Test purpose

Verify that when T3168 expires, the MS retransmits the PACKET RESOURCE REQUEST again (up to four times total).  Verify that when T3168 expires after the fourth transmission of the PACKET RESOURCE REQUEST, that the MS performs abnormal release with random access.

42.2.2.6.1.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before the current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	When T3168 expires, MS resends PACKET RESOURCE REQUEST (up to 4 times)

4.	When T3168 expires the fourth time, MS performs abnormal release with random access.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources - MS starts timer T3168 |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources - This is sent T3168 seconds after previous PRR. - MS re-starts timer T3168 |
| 7 |  |  | Steps 5 and 6 are repeated 2 more times such that a total of 4 PRRs are sent. |
| 8 | MS -> SS | CHANNEL REQUEST | Verify MS sends Random Access |

Specific Message Contents

PACKET SYSTEM INFORMATION MESSAGE 1 (throughout):

| T3168 | 0 (.5 second) |
| --- | --- |

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

##### 42.2.2.6.2	Fixed Allocation / Uplink Transfer / MS requests new resources/ T3168/Stop with Packet Uplink Assignment

42.2.2.6.2.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.6.2.2	Conformance requirements

At sending of the PACKET RESOURCE REQUEST message, the mobile station shall start timer T3168.

On receipt of a PACKET UPLINK ASSIGNMENT or PACKET TIMESLOT RECONFIGURE message the mobile station shall stop timer T3168 and switch to the assigned PDCHs.

References

GSM 04.60, subclause 7.1.3.1, 8.1.1.3.2, 12.24

42.2.2.6.2.3	Test purpose

Verify that when PACKET UPLINK ASSIGNMENT is received, MS stops T3168.

42.2.2.6.2.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before the current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	Prior to T3168 expiring, MS receives a new allocation.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources - MS starts timer T3168 |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET UPLINK ASSIGNMENT | Sent (.8*T3168) seconds after step 4. - MS stops timer T3168 |
| 7 | MS |  | Step 5 is repeated until current allocation is exhausted. |
| 8 | MS |  | MS starts to use the new allocation from step 6 at the next allocation boundary. |

Specific Message Contents

PACKET SYSTEM INFORMATION MESSAGE 1 (throughout):

| T3168 | 4 (2.5 seconds) |
| --- | --- |

PACKET UPLINK ASSIGNMENT message in step 2 and step 6.

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

##### 42.2.2.6.3	Fixed Allocation / Uplink Transfer / MS requests new resources/ T3168/Stop with Packet Uplink Ack/Nack with REPEAT_ALLOCATION

42.2.2.6.3.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.6.3.2	Conformance requirements

At sending of the PACKET RESOURCE REQUEST message, the mobile station shall start timer T3168.

References

GSM 04.60, subclause 7.1.3.1, 12.24

42.2.2.6.3.3	Test purpose

Verify that when PACKET UPLINK ACK/NACK is received, the MS stops T3168.

42.2.2.6.3.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before the current allocation expires, MS sends PACKET RESOURCE REQUEST.

3	Prior to T3168 expiring, MS receives a REPEAT_ALLOCATION.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources - MS starts timer T3168 |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET UPLINK ACK/NACK | Sent (.8*T3168) seconds after step 4. - MS stops timer T3168 |
| 7 | MS |  | Step 5 is repeated until current allocation is exhausted. |
| 8 | MS |  | MS starts to use the new allocation from step 6 at the next allocation boundary. |

Specific Message Contents

PACKET SYSTEM INFORMATION MESSAGE 1 (throughout):

| T3168 | 6 (3.5 seconds) |
| --- | --- |

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1 |

PACKET UPLINK ACK/NACK message in step 6:

| REPEAT_ALLOCATION | 1 |
| --- | --- |

##### 42.2.2.6.4	Fixed Allocation / Uplink Transfer / MS requests new resources/ T3168/Stop with Packet Access Reject

42.2.2.6.4.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.6.4.2	Conformance requirements

At sending of the PACKET RESOURCE REQUEST message, the mobile station shall start timer T3168.

On receipt of a PACKET ACCESS REJECT message , the mobile station shall stop timer T3168 if running and return to packet idle mode. Before initiating a new packet access procedure the mobile station shall decode the PRACH Control Parameters if they are broadcast.

References

GSM 04.60, subclause 7.1.3.1, 12.24

42.2.2.6.4.3	Test purpose

Verify that when PACKET ACCESS REJECT is received, the MS does not complete the current allocation.

42.2.2.6.4.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before the current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	Prior to T3168 expiring, MS receives a PACKET ACCESS REJECT.

4.	MS returns to packet idle mode without finishing the current allocation.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources - MS starts timer T3168 |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET ACCESS REJECT | Sent (.8*T3168) seconds after step 4 on PACCH. - No waiting time - MS stops timer T3168 |
| 7 | SS |  | Verify MS does not continue to use the assigned PDCH or finish the current allocation. (MS may choose to initiate access again.) |

Specific Message Contents

PACKET SYSTEM INFORMATION MESSAGE 1 (throughout):

| T3168 | 7 (4.0 seconds) |
| --- | --- |

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

##### 42.2.2.6.5	Fixed Allocation / Uplink Transfer / MS requests new resources/ T3168/Continue with Packet Uplink Ack/Nack without REPEAT_ALLOCATION and without ALLOCATION_BITMAP

42.2.2.6.5.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.6.5.2	Conformance requirements

At sending of the PACKET RESOURCE REQUEST message, the mobile station shall start timer T3168.

On expiry of timer T3168, the mobile station shall retransmit the PACKET RESOURCE REQUEST message unless the PACKET RESOURCE REQUEST message has already been  transmitted four times in which case the mobile station shall perform an abnormal release with random access.

References

GSM 04.60, subclause  8.1.1.3.2, 12.24

42.2.2.6.5.3	Test purpose

Verify that when MS receives a PACKET UPLINK ACK/NACK without an allocation, T3168 continues to run, and then expires, causing the MS to transmit the PACKET RESOURCE REQUEST again.

42.2.2.6.5.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before the current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	MS receives a PACKET UPLINK ACK/NACK with no REPEAT_ALLOCATION and no ALLOCATION_BITMAP.  When T3168 expires, MS resends PACKET RESOURCE REQUEST.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources - MS starts timer T3168 |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET UPLINK ACK/NACK | No resources assigned - This is sent within (.2*T3168) after previous PRR. |
| 7 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources - This is sent T3168 +/- (.1*T3168) after previous PRR. - MS re-starts timer T3168 |

Specific Message Contents

PACKET SYSTEM INFORMATION MESSAGE 1 (throughout):

| T3168 | 1 (1 second) |
| --- | --- |

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

#### 42.2.2.7	Fixed Allocation / Uplink Transfer / MS requests new resources/ Successful

##### 42.2.2.7.1	Fixed Allocation / Uplink Transfer / MS requests new resources/ Successful/Packet Uplink Assignment with ALLOCATION_BITMAP

42.2.2.7.1.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.7.1.2	Conformance requirements

At sending of the PACKET RESOURCE REQUEST message, the mobile station shall start timer T3168.

On receipt of a PACKET UPLINK ASSIGNMENT or PACKET TIMESLOT RECONFIGURE message the mobile station shall stop timer T3168 and switch to the assigned PDCHs.

References

GSM 04.60, subclause 8.1.1.3.2

42.2.2.7.1.3	Test purpose

Verify that when PACKET UPLINK ASSIGNMENT is received, MS switches to new resources after current allocation is exhausted.

42.2.2.7.1.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before the current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	Prior to T3168 expiring, MS receives a PACKET UPLINK ASSIGNMENT (with ALLOCATION_BITMAP).

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET UPLINK ASSIGNMENT | Sent (.5*T3168) after step 4. |
| 7 | MS |  | Step 5 is repeated until current allocation is exhausted. |
| 8 | MS |  | MS uses allocation from step 6. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2 and  step 6:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

##### 42.2.2.7.2	Fixed Allocation / Uplink Transfer / MS requests new resources/ Successful/Multiple Packet Uplink Assignments

42.2.2.7.2.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.7.2.2	Conformance requirements

Upon receipt of a complete uplink assignment containing an ALLOCATION_BITMAP, the mobile station shall begin transmitting on the new resources at the indicated TBF Starting Time. If there is a conflict between a previous allocation and the new allocation, the new allocation shall take precedence.

References

GSM 04.60, subclause 8.1.1.3.2.2

42.2.2.7.2.3	Test purpose

Verify that when the new PACKET UPLINK ASSIGNMENT is received, MS switches to new resources at the starting time if there is a conflict with the current assignment.

42.2.2.7.2.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before the current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	MS receives a PACKET UPLINK ASSIGNMENT with starting time prior to the end of the current allocation.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET UPLINK ASSIGNMENT | Sent .5 second after step 4. - Starting time conflicts with current allocation. |
| 7 | MS -> SS | RLC_DATA_BLOCKS | Verify MS sends no more than 6 data blocks after step 6 using the allocation from step 2. |
| 8 | MS -> SS | RLC DATA BLOCKS | MS uses new allocation from step 6 at the starting time specified in step 6. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

PACKET UPLINK ASSIGNMENT message in step 6:

| Starting_time | <26 frames after current frame> |
| --- | --- |
| Fixed allocation |  |
| - TIMESLOT ALLOCATION | One timeslot assigned <different from previous> |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

##### 42.2.2.7.3	Fixed Allocation / Uplink Transfer / MS requests new resources/ Successful/Packet Uplink Ack/Nack with ALLOCATION_BITMAP

42.2.2.7.3.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.7.3.2	Conformance requirements

Upon receipt of a PACKET UPLINK ACK/NACK with a REPEAT_ALLOCATION, the mobile station shall start a new allocation when the current allocation ends. This new allocation shall begin immediately after the current allocation ends and shall use the most recently received ALLOCATION_BITMAP. If the mobile station receives multiple PACKET UPLINK ACK/NACK messages with REPEAT_ALLOCATION during an allocation, the mobile shall repeat the ALLOCATION_BITMAP only once.

References

GSM 04.60, subclause 8.1.1.3.2.2

42.2.2.7.3.3	Test purpose

Verify that the MS uses the new ALLOCATION_BITMAP from the PACKET UPLINK ACK/NACK message.

42.2.2.7.3.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before the current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	After the current allocation expires, MS receives a new allocation in a PACKET UPLINK ACK/NACK.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2, until current allocation is exhausted. |
| 6 | SS -> MS | PACKET UPLINK ACK/NACK | Sent 1 second after step 4, with new ALLOCATION_BITMAP. |
| 7 | MS |  | MS starts to use the new allocation from step 6 at the next allocation boundary. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 5 bits are set to 1. |

PACKET UPLINK ACK/NACK message in step 6:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned <different from previous> |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

##### 42.2.2.7.4	Fixed Allocation / Uplink Transfer / MS requests new resources/ Successful/Multiple Packet Uplink Ack/Nack with ALLOCATION_BITMAP

42.2.2.7.4.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.7.4.2	Conformance requirements

Upon receipt of a PACKET UPLINK ACK/NACK with a REPEAT_ALLOCATION, the mobile station shall start a new allocation when the current allocation ends. This new allocation shall begin immediately after the current allocation ends and shall use the most recently received ALLOCATION_BITMAP. If the mobile station receives multiple PACKET UPLINK ACK/NACK messages with REPEAT_ALLOCATION during an allocation, the mobile shall repeat the ALLOCATION_BITMAP only once.

References

GSM 04.60, subclause 8.1.1.3.2.2

42.2.2.7.4.3	Test purpose

Verify that the MS uses the ALLOCATION_BITMAP currently being used as the allocation bitmap that applies to the REPEAT_ALLOCATION.

42.2.2.7.4.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	MS receives a series of PACKET UPLINK ACK/NACK messages before the current allocation expires, containing a new allocation, followed by a repeat allocation, followed by a different new allocation, followed by a repeat allocation.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources (can come any time during the allocation) |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET UPLINK ACK/NACK | Sent 1 second after step 4, with new ALLOCATION_BITMAP. |
| 7 | SS -> MS | PACKET UPLINK ACK/NACK | REPEAT_ALLOCATION |
| 8 | SS -> MS | PACKET UPLINK ACK/NACK | Different ALLOCATION_BITMAP than step 6. |
| 9 | SS -> MS | PACKET UPLINK ACK/NACK | REPEAT_ALLOCATION (This repeat only applies to the allocation in progress.) |
| 10 | MS |  | Step 5 is repeated until current allocation is exhausted. |
| 11 | MS |  | MS starts to repeat the allocation from step 2 at the next allocation boundary. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

PACKET UPLINK ACK/NACK message in step 6:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned <different from previous> |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. <different from previous> |

PACKET UPLINK ACK/NACK message in step 7 and 9:

| REPEAT_ALLOCATION | 1 |
| --- | --- |

PACKET UPLINK ACK/NACK message in step 8:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned <different from steps 2 and 6> |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. <different from previous> |

##### 42.2.2.7.5	Fixed Allocation / Uplink Transfer / MS requests new resources/ Successful/Multiple Packet Uplink Ack/Nack with REPEAT_ALLOCATION

42.2.2.7.5.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.7.5.2	Conformance requirements

Upon receipt of a PACKET UPLINK ACK/NACK with a REPEAT_ALLOCATION, the mobile station shall start a new allocation when the current allocation ends. This new allocation shall begin immediately after the current allocation ends and shall use the most recently received ALLOCATION_BITMAP. If the mobile station receives multiple PACKET UPLINK ACK/NACK messages with REPEAT_ALLOCATION during an allocation, the mobile shall repeat the ALLOCATION_BITMAP only once.

References

GSM 04.60, subclause 8.1.1.3.2.2

42.2.2.7.5.3	Test purpose

Verify that the MS repeats the current allocation only once.

42.2.2.7.5.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

- MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

- Before current allocation expires, MS sends PACKET RESOURCE REQUEST.

- MS receives a series of PACKET UPLINK ACK/NACK messages before the current allocation expires, each containing a repeat allocation.

- MS responds at the next allocation boundary by using the previous allocation but only once.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources (sent sometime during current allocation) |
| 5 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET UPLINK ACK/NACK | Sent (.5*T3168) after step 4, with REPEAT_ALLOCATION. |
| 7 | SS -> MS | PACKET UPLINK ACK/NACK | REPEAT_ALLOCATION |
| 8 | SS -> MS | PACKET UPLINK ACK/NACK | REPEAT_ALLOCATION |
| 9 | MS |  | Step 5 is repeated until current allocation is exhausted. |
| 10 | MS |  | MS starts to repeat the allocation from step 2 at the next allocation boundary. |
|  |  |  | If MS sends PACKET_RESOURCE_REQUEST anytime during step 10, SS sends a different PACKET_UPLINK_ASSIGNMENT than sent previously. |
| 11 | SS |  | Verify MS does not use the allocation from step 2 after step 10. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

PACKET UPLINK ACK/NACK message in step 10:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned <different from previous> |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. <different from previous> |

PACKET UPLINK ACK/NACK message in step 6,7 and 8:

| REPEAT_ALLOCATION | 1 |
| --- | --- |

#### 42.2.2.8	Fixed Allocation / Uplink Transfer / MS requests new resources/ Failure

##### 42.2.2.8.1	Fixed Allocation / Uplink Transfer / MS requests new resources/ Failure/Packet Access Reject

42.2.2.8.1.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.8.1.2	Conformance requirements

On receipt of a PACKET ACCESS REJECT message , the mobile station shall stop timer T3168 if running and indicate a packet access failure to upper layer.

References

GSM 04.60, subclause 8.1.1.3.2

42.2.2.8.1.3	Test purpose

Verify that the MS returns to packet idle mode when PACKET ACCESS REJECT is received.

42.2.2.8.1.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	After the current allocation expires, MS receives a PACKET ACCESS REJECT message.

4.	MS returns to packet idle mode.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources |
| 5 | SS -> MS | PACKET ACCESS REJECT |  |
| 6 | MS -> SS | RLC DATA BLOCKS | MS sends no more than 6 RLC data blocks after step 5. |
| 7 | SS |  | Verify that MS is not transmitting on the previous PDCH. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | 48 |
| - ALLOCATION_BITMAP | Exactly 10 bits are set to 1. |

##### 42.2.2.8.2	Fixed Allocation / Uplink Transfer / MS requests new resources/ Failure/Packet Access Reject with WAIT_INDICATION during allocation in progress

42.2.2.8.2.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.8.2.2	Conformance requirements

If the PACKET ACCESS REJECT message contains a WAIT_INDICATION field in a Reject structure addressed to the mobile station, the mobile station shall

-	start timer T3172 and if the mobile station has additional RLC data blocks to transmit, it shall initiate a new TBF establishment procedure on the RACH or PRACH, but the mobile station is not allowed to make a new attempt for packet access in the same cell until timer T3172 expires, it may, however, attempt packet access in an other cell after successful cell reselection. A mobile station in GPRS MS class A or B mode of operation may attempt to enter the dedicated mode in the same cell before timer T3172 has expired. During the time T3172 is running, the mobile station shall ignore all received PACKET PAGING REQUEST messages except paging request to trigger RR connection establishment.

The value of the WAIT_INDICATION field (i.e. timer T3172) relates to the cell from which it was received.

References

GSM 04.60, subclause 8.1.1.3.2

42.2.2.8.2.3	Test purpose

Verify that the MS waits T3172 before sending additional PACKET RESOURCE REQUEST messages, when PACKET ACCESS REJECT is received with a WAIT_INDICATION.

42.2.2.8.2.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH  present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before current allocation expires, MS sends PACKET RESOURCE REQUEST.

3.	Before the current allocation expires, MS receives a PACKET ACCESS REJECT message.

4.	MS waits T3172 before sending additional PACKET RESOURCE REQUEST messages.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCKS | MS transmits RLC blocks only when TBF starting time occurs |
| 4 | MS -> SS | PACKET RESOURCE REQUEST | MS requests additional resources |
| 5 | MS -> SS | RLC DATA BLOCK | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 6 | SS -> MS | PACKET ACCESS REJECT | Sent (.5*T3168) after step 4. - MS starts T3172 |
| 7 | MS -> SS | RLC DATA BLOCK | MS sends no more than 6 RLC data blocks after step 6. |
| 8 | MS -> SS | PACKET CHANNEL REQUEST | Sent more than 2 seconds after step 6. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | <any suitable value > |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

PACKET ACCESS REJECT message in step 6:

| WAIT_INDICATION | 2 |
| --- | --- |
| WAIT_INDICATION_SIZE | 0 – WAIT_INDICATION in units of seconds |

#### 42.2.2.9	Fixed Allocation / Uplink Transfer / Network initiates new resources

42.2.2.9.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.2.2.9.2	Conformance requirements

The network may at any time during the uplink TBF initiate a change of resources by sending on the downlink PACCH monitored by the MS, an unsolicited PACKET UPLINK ASSIGNMENT or PACKET TIMESLOT RECONFIGURE, or an uplink resource reassignment in a PACKET UPLINK ACK/NACK message to the mobile station.

References

GSM 04.60, subclause 8.1.1.3.2

42.2.2.9.3	Test purpose

Verify that the MS obeys unsolicited PACKET UPLINK ASSIGNMENT message during an uplink TBF.

42.2.2.9.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF.

2.	Before current allocation expires, SS sends unsolicited PACKET UPLINK ASSIGNMENT.

3.	After the current allocation expires, MS uses the newly assigned resources.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCK | MS transmits RLC block only when TBF starting time occurs |
| 4 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 4A | MS -> SS | PACKET RESOURCE REQUEST | Optional: MS may request new resources. If this occurs, SS proceeds with step 4B. |
| 4B | SS -> MS | PACKET UPLINK ASSIGNMENT | Assign uplink resources in response to MS request. |
| 5 | SS -> MS | PACKET UPLINK ASSIGNMENT | Unsolicited – sent on PACCH. Different from step 4B. |
| 6 | MS -> SS | RLC DATA BLOCK | MS continues to transmit RLC data blocks according to allocation from step 2, until the allocation is exhausted. |
| 7 | MS -> SS | RLC DATA BLOCK | MS starts to use the new allocation from step 5 at the given starting time. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | <any suitable value > |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |

PACKET UPLINK ASSIGNMENT message in step 5:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | One timeslot assigned <different than previous> |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | <any suitable value > |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |
| Starting Time | 100 frames after current allocation expires |

#### 42.2.2.10	Fixed Allocation / Uplink Transfer / PACCH operation

##### 42.2.2.10.1	Fixed Allocation / Uplink Transfer / PACCH operation/ Normal Operation

42.2.2.10.1.1	Definition and applicability

This test case applies to all MSs supporting GPRS multi-slot class 3 and higher.

          - Conformance requirements

A mobile station shall monitor one PDCH in the allocation for downlink PACCH except during the measurement gap. The network shall indicate that PDCH on uplink resource assignment (DOWNLINK_CONTROL_TIMESLOT parameter) according to MS multislot class.

References

GSM 04.60, subclause 8.1.1.3.4, Annex D

GSM 5.02, Annex B.1

42.2.2.10.1.3	Test purpose

Verify that the MS monitors the correct PDCH for PACCH during an uplink TBF.

42.2.2.10.1.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF on 2 timeslots.

2.	MS receives PACKET POLLING REQUEST on the PDCH corresponding to its downlink PACCH.

3.	MS responds to the poll by sending PACKET CONTROL ACKNOWLEDGEMENT.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCK | MS transmits RLC block only when TBF starting time occurs |
| 4 | MS -> SS | RLC DATA BLOCK | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 5 | SS -> MS | PACKET POLLING REQUEST | Sent on PACCH, PDCH 0. |
| 6 | MS -> SS | PACKET CONTROL ACKNOWLEDGEMENT | Sent in next but one block after step 5, on PDCH 0. |
| 7 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2, until the allocation is exhausted. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | Two timeslot assigned (0 and 1) |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | <any suitable value > |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |
| - DOWNLINK_CONTROL_TIMESLOT | 000 |

PACKET POLLING REQUEST message in step 5:

| TYPE_OF_ACK | 1 (Respond with RLC/MAC control block) |
| --- | --- |
| TFI | Addressing this MS |

##### 42.2.2.10.2	Fixed Allocation / Uplink Transfer / PACCH operation/ PACCH message addressed to another MS

42.2.2.10.2.1	Definition and applicability

This test case applies to all MSs supporting GPRS multi-slot class 3 and higher.

42.2.2.10.2.2	Conformance Requirements

A mobile station shall monitor one PDCH in the allocation for downlink PACCH except during the measurement gap. The network shall indicate that PDCH on uplink resource assignment (DOWNLINK_CONTROL_TIMESLOT parameter) according to MS multislot class.

References

GSM 04.60, subclause 8.1.1.3.4, Annex D

GSM 5.02, Annex B.1

42.2.2.10.2.3	Test purpose

Verify that the MS ignores the PACCH message if addressed to another MS.

42.2.2.10.2.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer and enters a open-ended TBF on 2 timeslots.

2.	MS receives PACKET POLLING REQUEST on the PDCH corresponding to its downlink PACCH, addressed to another MS.

3.	MS does not respond to the poll.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCK | MS transmits RLC block only when TBF starting time occurs |
| 4 | MS -> SS | RLC DATA BLOCK | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 5 | SS -> MS | PACKET POLLING REQUEST | Sent on PACCH, PDCH 0. |
| 6 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2, until the allocation is exhausted. - Verify no PACKET CONTROL ACKNOWLEDGEMENT is sent by MS. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | Two timeslots assigned (0 and 1) |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | <any suitable value > |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |
| - DOWNLINK_CONTROL_TIMESLOT | 000 |

PACKET POLLING REQUEST message in step 5:

| TYPE_OF_ACK | 1 (Respond with RLC/MAC control block) |
| --- | --- |
| TFI | Not matching this MS. |

##### 42.2.2.10.3	Fixed Allocation/ Uplink Transfer / Abnormal cases / PACCH timeslot removed

42.2.2.10.3.1	Definition and applicability

This test case applies to all MSs supporting GPRS multi-slot class 3 and higher.

42.2.2.10.3.2	Conformance requirements

If an uplink TBF in fixed allocation mode was in progress and if one of timeslots that are being released is its downlink PACCH timeslot, the mobile station shall temporarily read all downlink blocks that it is able to decode according to its multislot capability, on all of its remaining assigned PDCHs, and act upon any RLC/MAC control message that is addressed to it, until another downlink PACCH timeslot is assigned. If the mobile station's multislot capability does not allow it to monitor the downlink of any of its assigned PDCHs, it shall perform an abnormal release with random access.

References

GSM 04.60, subclause 8.2

GSM 5.02, Annex B.1

42.2.2.10.3.3	Test purpose

Verify that the MS monitors the correct PDCH for PACCH during an uplink TBF after the previously assigned downlink PACCH timeslot is released.

42.2.2.10.3.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH not present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service,

The way to initiate an uplink transfer,

Test Procedure

1.	MS is triggered to begin an uplink data transfer (via CCCH) and enters a open-ended TBF on 2 timeslots, with one timeslot assigned for its downlink PACCH.

2.	MS receives PACKET PDCH RELEASE message on its assigned PACCH.

3.	MS receives PACKET POLLING REQUEST on the PDCH that was just released, corresponding to its downlink PACCH.

4.	MS does not respond to the poll.

5.	MS receives PACKET POLLING REQUEST on another downlink PDCH to which it is assigned.

6.	MS responds to the poll.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS |  | Trigger the MS to initiate an uplink packet transfer containing 1000 octets. |
| 2 |  |  | Bring the MS into packet uplink transfer mode by the generic procedure defined in the table 42.2.1.2/1b. |
| 3 | MS -> SS | RLC DATA BLOCK | MS transmits RLC block only when TBF starting time occurs |
| 4 | MS -> SS | RLC DATA BLOCK | MS continues to transmit RLC data blocks according to allocation from step 2. |
| 5 | SS -> MS | PACKET PDCH RELEASE | Sent on PACCH, PDCH 0. |
| 6 | SS -> MS | PACKET POLLING REQUEST | Sent on PACCH, PDCH 0. |
| 7 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2, but without any transmission on PDCH 0. - Verify no PACKET CONTROL ACKNOWLEDGEMENT is sent by MS onPDCH0. |
| 8 | SS -> MS | PACKET POLLING REQUEST | Sent on PACCH, PDCH 1. |
| 9 | MS -> SS | PACKET CONTROL ACKNOWLEDGEMENT | Sent in next but one block after step 8, on PDCH 1. |
| 10 | MS -> SS | RLC DATA BLOCKS | MS continues to transmit RLC data blocks according to allocation from step 2, until the allocation is exhausted. |

Specific Message Contents

PACKET UPLINK ASSIGNMENT message in step 2:

| Fixed allocation |  |
| --- | --- |
| - TIMESLOT ALLOCATION | Two timeslots assigned (0 and 1) |
| - BLOCKS_OR_BLOCK_PERIODS | 0 – blocks |
| - ALLOCATION_BITMAP_LENGTH | <any suitable value > |
| - ALLOCATION_BITMAP | Exactly 40 bits are set to 1. |
| - DOWNLINK_CONTROL_TIMESLOT | 000 |

PACKET POLLING REQUEST message in step 6 and 8:

| TYPE_OF_ACK | 1 (Respond with RLC/MAC control block) |
| --- | --- |
| TFI | matching this MS |

PACKET PDCH RELEASE message in step 5:

| PAGE_MODE | 00 – Normal Paging |
| --- | --- |
| TIMESLOTS_AVAILABLE | <not present> |

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the lastest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.