3GPP TSG-GERAN WG4 Meeting #6 	TDoc G4-010637

Sophia Antipolis, rance, 8 - 10 October 2001

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | 51.010-1 | CR | 424 | ( rev | - | ( Current version: | 4.5.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE | x | Radio Access Network |  | Core Network |  |
| Title: ( | TIMING ADVANCE value in PACKET DOWNLINK ASSIGNMENT |
| Source: ( | Setcom |
| Work item code: ( | GPRS |  | Date: ( | 2001-08-28 |
| Category: ( | F |  | Release: ( | REL-4 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | The Timing Advance value in the PACKET DOWNLINK ASSIGNMENT message in step 1 should be the same as the default value specified in section 40. |
| Summary of change: ( | Use default timing advance value. |
| Consequences if ( not approved: | Not only the conformance requirement specified in the test case are tested. |
| Clauses affected: ( | 42.5.2.1 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( | This CR applies to R97 and later releases |

#### 42.5.2.1	Downlink Transfer/ Polling/ Normal operation/RLC data block

42.5.2.1.1	Definition and applicability

This test case applies to all MSs supporting GPRS.

42.5.2.1.2	Conformance Requirement

Whenever the mobile station receives an RLC data block addressed to itself and with a valid RRBP field in the RLC data block header (i.e., is polled), the mobile station shall transmit a Packet Downlink ACK/NACK message in the uplink radio block specified by the RRBP field whatever the BSN value of the received RLC data block, unless another RLC/MAC control message is waiting to be transmitted, in which case the other RLC/MAC control message shall be sent.

The RRBP value specifies a single uplink block in which the mobile station shall transmit either a PACKET CONTROL ACKNOWLEDGEMENT message or a PACCH block to the network. If the RRBP field is received as part of an RLC/MAC block containing an RLC/MAC control block containing any message except Packet Paging Request, Packet Access Reject, and Packet Queueing Notification, the mobile station shall transmit a PACKET CONTROL ACKNOWLEDGEMENT message in the uplink radio block specified. If the RRBP field is received as part of an RLC/MAC block containing an RLC/MAC control block containing a Packet Paging Request, Packet Access Reject, or Packet Queueing Notification message, the mobile station shall ignore this RRBP field. The mobile station shall only react on RLC/MAC control blocks containing a valid RRBP field if the mobile station is unambiguously addressed eitherin the downlink RLC/MAC control block header or in the control message itself.

References

GSM 04.60, subclause 8.1.2.2, 10.4.5

42.5.2.1.3	Test purpose

Verify that an MS responds to a poll with a PACKET DOWNLINK ACK/NACK message in the block specified by the RRBP field.

42.5.2.1.4	Method of test

Initial Conditions

System Simulator:

1 cell, GPRS supported, PCCCH present

Mobile Station:

The MS is in the state "idle, GMM-registered" with a P-TMSI allocated, SPLIT PG CYCLE negotiated, and PDP context 3 activated.

Related PICS/PIXIT Statement(s)

Support GPRS service

Test Procedure

1.	MS receives a PACKET DOWNLINK ASSIGNMENT message on its assigned PCCCH, containing no starting time.

2.	SS transmits a downlink RLC data block.

3.	MS responds by sending a PACKET DOWNLINK ACK/NACK in the block specified by the RRBP field of the RLC data block.

Maximum Duration of Test

5 min.

Expected Sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | SS -> MS | PACKET DOWNLINK ASSIGNMENT | Triggers the MS to switch to assigned PDCH. |
| 2 | SS -> MS | RLC DATA BLOCK | 3 blocks after the previous message, with valid RRBP field, on assigned PDCH, addressed to MS. |
| 3 | MS -> SS | PACKET DOWNLINK ACK/NACK | MS acknowledges the RLC DATA BLOCK 26 frames after step 2. |
| 4 |  | {Completition of downlink data transfer} | Macro |

Specific Message Contents

PACKET DOWNLINK ASSIGNMENT message in step 1:

| TIMESLOT_ALLOCATION | <one timeslot assigned> |
| --- | --- |
| PACKET TIMING ADVANCE | Timing Advance Value = as default |
| TBF STARTING TIME | <IE not present> |

DOWNLINK RLC DATA BLOCK in step 2:

| RRBP | 11 – Response shall be sent by MS in N+26 frames. |
| --- | --- |
| S/P | 1 – RRBP field is valid |

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the lastest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.